## Slide 1
Title
ATD User Guide
System
CS1000
Abstract
User Guide
Revision History
LG PBX System
Software Technical Information
STI-0008
Jan. 31, 2001
Revision
Date
By
History
1.0
01.31.2001
C.K Ahn
First Issue
1.1
04.16.2001
Y.K.Song
LCD Display changed

## Slide 2
Contents
Answer of Extension Call ---------------------------------------------------------------------------------- 3
Answer of Trunk Incoming Call --------------------------------------------------------------------------- 4
Attendant to Station Calling ------------------------------------------------------------------------------- 5
Attendant to Trunk Calling --------------------------------------------------------------------------------- 6
Answering Selection ----------------------------------------------------------------------------------------- 7
Attendant to Extension Call Transfer -------------------------------------------------------------------- 8
Incoming Trunk Call Transfer ----------------------------------------------------------------------------- 9
Attendant Consultation Transfer ------------------------------------------------------------------------- 10
Call Hold (Europe Version) -------------------------------------------------------------------------------- 11
Extensions Busy Status ------------------------------------------------------------------------------------ 12
Attendant to Attendant Calling ---------------------------------------------------------------------------- 13
Attendant Redialing ------------------------------------------------------------------------------------------ 14
Attendant to Attendant Transfer -------------------------------------------------------------------------- 15
Busy Lamp Field Status ------------------------------------------------------------------------------------ 16
Last Transferred Call Cancellation ----------------------------------------------------------------------- 17
Collect Call ----------------------------------------------------------------------------------------------------- 18
Forced Release ----------------------------------------------------------------------------------------------- 19
Night Transfer (PNA) ---------------------------------------------------------------------------------------- 20
Overflow -------------------------------------------------------------------------------------------------------- 21
Through Dialing ----------------------------------------------------------------------------------------------- 22
Trunk Selection ----------------------------------------------------------------------------------------------- 23
Automatic Recall --------------------------------------------------------------------------------------------- 24
ATD Break In ------------------------------------------------------------------------------------------------- 25
Call Waiting Number Display ------------------------------------------------------------------------------ 26
ATD Camp On ------------------------------------------------------------------------------------------------ 27
ATD Conference --------------------------------------------------------------------------------------------- 28
ATD Lamp Test ---------------------------------------------------------------------------------------------- 29
Operator Alarm ---------------------------------------------------------------------------------------------- 30
ATD System Speed Dialing ------------------------------------------------------------------------------- 31
Trunk Call Supervision ------------------------------------------------------------------------------------ 32
Verify Busy Line Status ------------------------------------------------------------------------------------ 33
ATD Group Hunting ----------------------------------------------------------------------------------------- 34
ATD MUTE ---------------------------------------------------------------------------------------------------- 35
Contents

## Slide 3
Answer of Extension Call
1. If a extension dials the attendant calling code, "STA ANS“
LED flashes.
2. Upon pressing the "STA ANS" or "ANSWER" Key, Tenant
Group Number, Extension Number and Class of Service are
displayed on the LCD, and then an operator and a calling
extension can talk each other. If there is no more connected
incoming call, the number of waiting call on the LCD is
changed into 00.
3. After talking, if an operator presses the "RLS" Key or
extension goes on hook, the corresponding line is released
from connection.
Button
Procedures
Display
This feature allows an operator to answer the extension call.
STA
ANS
ANSWER
RLS
ATN:0000 09 : 00 : 00
00 00 00 BUSY:
00 2002 I IC-STA

## Slide 4
Answer of Trunk Incoming Call
1. When a trunk call is incoming to Attendant Console,
“TRK ANS“ LED flashes.
2. Upon pressing the “TRK ANS" or "ANSWER" Key, Tenant
Group Number and Trunk Serial Number of the incoming
trunk are displayed on the LCD, and then an operator and a
calling trunk incoming call can talk each other. If there is no
more connected incoming call, the number of waiting call on
the LCD is changed into 00.
3. After talking, if an operator presses the "RLS" Key or
outside subscriber goes on hook, the corresponding line is
released from connection.
Button
Procedures
Display
This feature allows an operator to answer the incoming trunk call.
TRK
ANS
ANSWER
RLS
ATN:0000 09 : 00 : 00
00 00 00 BUSY:
00 0001 BW IC-TRK

## Slide 5
Attendant to Station Calling
1. Dial the desired extension number.
2. The LCD will show Tenant Group Number, Extension
Number, Class of Service and status of extension.
3. If the called extension is idle, an operator presses
the "CONNECT" key, then the operator will hear RBT and
the called extension will ring.
4. When the called extension goes off-hook, the connect
message is displayed on the LCD, then they can talk with
each other.
Button
Procedures
Display
This service feature permits an operator to directly dial any extension.
CONNECT
ATN:0000 09 : 00 : 00
00 00 00 BUSY:
00 2002 I IDLE
ATN:0000 09 : 30 : 55
00 00 00 BUSY:
00 2002 I CONNECT

## Slide 6
Attendant to Trunk Calling
1. Dial the trunk access code or trunk serial number after
pressing “TRK SEL” key, and then the LCD will show Tenant
Group Number, trunk serial number of the available trunk line.
An operator receives dial tone of trunk line. If the all trunk
lines are busy, the LCD shows all "ALL- BUSY" message.
2. Dial the desired outside number.
3. When the called part answers, the call is established.
4. After talking, an operator may release the line by pressing
the "RLS" key.
Button
Procedures
Display
This service feature allows an operator to dial the outgoing trunk line
RLS
TRK
SEL
ATN:0000 09 : 00 : 00
00 00 00 BUSY:
00 0008 BW
ATN:0000 09 : 00 : 00
00 00 00 BUSY:
00 0008 BW
8182002

## Slide 7
Answering Selection
1) Trunk Call Answer
"TRK ANS" Key or "ANSWER" Key
2) Extension Call Answer
"STA ANS" Key or "ANSWER" Key
3) Recall Answer
"RCL ANS" Key or "ANSWER" Key
Note)
When an operator answers the incoming call using
the "ANSWER" Key, the incoming call is connected by turns of
trunk call, recall, extension call.
Button
Procedures
Display
This feature allows an operator to select the answer of the various incoming call (Trunk call, Extension call and Recall).
ANSWER
TRK
ANS
STA
ANS
RCL
ANS
ATN:0000 09 : 00 : 00
00 00 00 BUSY:
00 2002 I IC-STA
ATN:0000 09 : 00 : 00
00 00 00 BUSY:
00 0062 BW IC-TRK
ATN:0000 09 : 00 : 00
00 00 00 BUSY:
00 2002 I
00 0061 BW RC-XFR

## Slide 8
Attendant to Extension Call Transfer
Korea Version
1. While talking with extension "A", operator dials extension "B".
2. The LCD will show Tenant Group Number and Extension
Number and Class of Service of extension "B".
3. Press the "CONNECT" Key for the connection of talking path
between extension "A" and "B".
Europe Version
1. While talking with extension "A", operator dials extension "B".
2. The LCD will show Tenant Group Number and Extension
Number and Class of Service of extension "B“ and
Extension B will ring
3. Extension B answers.
4. Press the "CONNECT" Key for the connection of talking path
between extension "A" and "B".
Button
Procedures
Display
This feature allows an operator while engaged in an extension call, to transfer the call to other extension.
CONNECT
CONNECT
ATN:0000 09 : 00 : 00
00 00 00 BUSY:
00 2002 I IDLE
00 2100 I IC-STA
ATN:0000 09 : 00 : 00
00 00 00 BUSY:
00 2002 I IDLE
00 2100 I IC-STA

## Slide 9
Incoming Trunk Call Transfer
Korea Version
1. During the talking with trunk line, the operator dials the
extension number. When an operator dials the extension
number, the status of the extension is displayed on the LCD.
2. When the called part is idle, an operator presses
the "CONNECT" key; outside subscriber hears RBT and
extension is ringing.
3. If the called extension goes off-hook, incoming trunk line to
extension is established.
Europe Version
1. During the talking with trunk line, the operator dials the
extension number.
2. The status of the extension is displayed on the LCD and
Extension will ring
3. Extension answers.
4. Press the "CONNECT" Key for the connection of talking path
between outside subscriber and extension.
Button
Procedures
Display
This feature allows an operator while engaged in an trunk incoming call, to transfer the call to other extension.
CONNECT
CONNECT
ATN:0000 09 : 00 : 00
00 00 00 BUSY:
00 2002 I IDLE
00 0002 BW IC-TRK
ATN:0000 09 : 00 : 00
00 00 00 BUSY:
00 2002 I IDLE
00 0002 BW IC-TRK

## Slide 10
Attendant Consultation Transfer
Button
Procedures
Display
This service feature allows an operator to transfer the trunk line or extension to other extension after conversation with the desired extension instead of direct transferring.
CONNECT
CLR
RLS
ATN:0000 09 : 00 : 00
00 00 00 BUSY:
00 2002 I IDLE
00 2002 I
ATN:0000 09 : 00 : 00
00 00 00 BUSY:
00 2002 I
00 0062 I
1. If extension "A" requests the connection with an extension "B“
during the conversation with Attendant, the operator dials the
extension number of an extension "B".
2. The LCD shows Tenant Group Number, Extension Number,
Class of Service and status of extension "B“, and extension “B”
will ring directly.
3. At this time, an extension "A“ hears MOH under the held state.
4. Extension B answers.
5. If an operator presses the “CLR” key, an operator can consult
conversation between extension A and B.
6. If an operator presses the “CONNECT” key, extension “A” and
“B” will connect.
7. If operator presses the “CONF” key, extension “A”, “B” and
Attendant.(3-way conferences)

## Slide 11
Call Hold (Europe Version)
Call Hold
1. The operator presses "HOLD" key while talking to the
extension.
2. The LCD of the attendant becomes cleared off and one of
the "Hold Indicator" LED turns on and the extension in
conversation hears the MOH. In this case, the attendant
becomes in idle state.
Answer held call
1. The operator presses just “HOLD VERIFY” key to pick up
the calls that were held in order
Button
Procedures
Display
This function enables the operator to hold an outside subscriber or an extension that is in conversation with attendant. Through this function, the operator can answer and verify the held extension/outside subscriber, and also he can connect with the extension/outside subscriber that is in conversation with the held extension/outside subscriber.
HOLD
HOLD
VERIFY
ATN:0000 09 : 30 : 55
00 00 00 BUSY:
00 2002 I
00 2003 I

## Slide 12
10 Extensions Busy Status
Registration to 10EXT Busy lamp field
1. The operator presses "FUNC" key.
2. The "FUNC" LED turns on.
3. Dial the Index Number (0~9).
4.The registered extension number is displayed when the
extension is registered to the 10EXT Busy Lamp Field. If
there is no registered extension, "NO:######" is displayed
on the LCD of attendant.
5. Enter the extension number to be registered.
6. The operator enters "ENT" key.
7. Attendant is in idle state if the registration is completed
normally. If an error occurs, Error Message is displayed on
the LCD of attendant.
Deleting registered extension number in 10EXT Busy lamp
field
1. The operator presses "FUNC" key.
2. The "FUNC" LED turns on.
3. Dial the Index Number (0~9).
4. It the extension is registered in the 10EXT Busy Lamp Field
the registered extension number is displayed, and if
not, "NO:######” is displayed on the LCD of attendant.
5. When pressing "FORC RLS" key after the registered
extension is displayed, the displayed extension will be
deleted in 10EXT Busy Field
6. If the deletion is completed normally, the attendant is in idle
state.
Deletion of all the extension registered in 10EXT Busy lamp
field
1. The operator presses "FUNC" key.
2. The "FUNC" LED turns on.
3. Dial the 'delete all' ("*") code.
4. Dial 1 (Are you sure? - 1:YES / 0:NO)
5. The following message is displayed
All ATD 10 EXT Info Cancellation!!!
6. If all the extension registered in the 10EXT Busy Lamp Field
is deleted completely, the attendant is in idle state.
Button
Procedures
Display
The function enables the attendant to perform the real-time monitoring on the status of 10 extensions that are registered to the 10EXT Busy Field of the Busy Field Lamp on ATD panel.
FUNC
FUNC
FORC
RLC
FUNC
ATN:0000 09 : 00 : 00
00 00 00 BUSY:
10EXT Index / Redial
( 0-9 * / # )
ATN:0000 09 : 00 : 00
00 00 00 BUSY:
NO : ######
ATN:0000 09 : 00 : 00
00 00 00 BUSY:
TNO: 2002
ATN:0000 09 : 00 : 00
00 00 00 BUSY:
ARE YOU SURE ?
( 1 : YES / 0 : NO )

## Slide 13
Attendant to Attendant Calling
Attendant to attendant calling
1. An operator dials other operator's own extension number to
call.
2. The calling operator hears the ring back tone and the "STA
ANS" lamp of the called attendant will be flashed.
3. The called operator answers.
4. An attendant-to-attendant call is set up.
Button
Procedures
Display
This function allows the operator to call other attendant by dialing operator's own extension number .
STA
ANS
ATN:0000 09 : 00 : 00
00 00 00 BUSY:
00 2002 I IC-STA

## Slide 14
Attendant Redialing
1. Press the "FUNC" Key and ‘#’ code
2. Last dialed digits are displayed at LCD.
3. The outside subscriber answers.
4. The call between ATD and outside subscriber is established.
Button
Procedures
Display
If an operator wants to call again the last dialed subscriber or outgoing telephone number, this feature allows an operator to call the last dialed number using the "FUNC" Key and then, press ‘#’ instead of dialing the number.
FUNC
ATN:0000 09 : 00 : 00
00 00 00 BUSY:
10EXT Index / Redial
( 0-9 * / # )
ATN:0000 09 : 00 : 00
00 00 00 BUSY:
00 2002 BW
028182003

## Slide 15
Attendant to Attendant Transfer
Transfer from attendant to attendant
1. If an attendant tries to transfer the extension to another
attendant during a call, the operator presses the “ATD XFR"
key and enters the serial number of the attendant (00~07) to
transfer the call.
2. The calling attendant is released, extension hears MOH, and
the “ATD XFR" LED of the called attendant flashes.
3. The called attendant answers the call.
4. Then, a call between the held extension and the called
operator is established.
Button
Procedures
Display
The function enables an attendant to transfer the extension on line with the attendant to another attendant.
ATD
XFR
ATD
XFR
ATN:0000 09 : 00 : 00
00 00 00 BUSY:
01
00 2002 I IC-STA

## Slide 16
Busy Lamp Field Status
How to use
1. The operator presses "BUSY GRP" key.
2. The "BUSY GRP" LED turns on.
3. The operator dials the number of trunk or extension group to
be verified.
4. The dialing group number is displayed on “BUSY” of the LCD
of the attendant.
5. The operator enters "ENT" key.
6. The availability of the registered trunk or subscribers of the
extension group is successively displayed on the LED.
7. The operator presses "BUSY GRP" key while
the "BUSY GRP" LED is on.
8. Then, the registered availability status is canceled as the
number of the group displayed on the attendant LCD is
cleared off.
Note) Input Range for extension or trunk group
Group numbers inputted when using the busy indication
function are station Subscriber numbers without the last two
digits.
For example, the group Number of station number 2XX is 2 and
the group number of station numbers less than 100 is 0. Also,
the group number of station number 21XX becomes 21 and for
the trunk serial number 0000 ~ 0099 , the group number
becomes 00. For 0100 ~ 0199, it becomes 01.
Button
Procedures
Display
The function assigns the trunk or extension group as busy group to verify the status of the subscriber in the group.
BUSY GRP
ENT
BUSY GRP
ATN: 0000 09 : 00 : 00
00 00 00 BUSY :
S:DAY A:DAY
ATN: 0000 09 : 00 : 00
00 00 00 BUSY : 21
S;DAY A:DAY

## Slide 17
Last Transferred Call Cancellation
1. An operator dials an extension number that the operator
transferred wrongly to or that is ringing.
2. The extension status is displayed on the LCD of the
attendant.
3. If the operator presses “CLR" key, it will cancel the last
transferred call. Then, the conversation between the
extension and the operator is resumed.
Button
Procedures
Display
If an operator transfers an extension that is in conversation with him or her to a wrong number, this function allows the operator to cancel the wrong call transfer and to reestablish the conversation with the transferred subscriber.
CLR
ATN: 0000 09 : 00 : 00
00 00 00 BUSY:
00 2002 I
ATN: 0000 09 : 00 : 00
00 00 00 BUSY:
00 2003 I IDLE
00 2002 I
ATN: 0000 09 : 00 : 00
00 00 00 BUSY:
00 2002 I

## Slide 18
Collect Call
Collect call information registration in attendant.
1. Attendant is conversation with outside subscriber.
2. Attendant enters the extension number.
3. The outside subscriber is held and hears MOH, the
attendant hears RBT, and the extension is ringing.
4. If the extension answers, the attendant asks whether to
receive the collect call. If the extension wants to receive, the
attendant presses "CHRG" key.
5. The attendant dials “3” and enters the caller information.
6. The attendant presses “ENT” key.
6. The attendant enters the information of the collect call.
7. The attendant enters the number of outside subscriber.
8. The attendant enters “ENT" key.
9. The attendant is released with its LCD cleared, and the call is
made between the outside subscriber and the extension.
When the extension refuses to receive the collect call.
1. The extension refuses to receive the collect call.
2. The attendant presses "CLR" key to talk with the outside
subscriber.
3. In case of mistype, the operator presses "CLR" key and
starts entering again.
Button
Procedures
Display
When the call incoming to attendant requests collect call, this function enables attendant to register the related information.
CHRG
ENT
CLR
CLR
ATN:0000 09 : 30 : 55
00 00 00 BUSY:
028182003
00 0008 BW IC-TRK
ATN:0000 09 : 30 : 55
00 00 00 BUSY:
3028182003

## Slide 19
Forced Release
Forced release of the extension line
1. An attendant dials an extension number.
2. The status of the selected extension is displayed.
3. If the selected extension line is not idle, the attendant
presses the "FORC RLS" key.
4. The extension and the attendant are released.
Forced release of the trunk line
1. The attendant presses the "TRK SEL" key.
2. The attendant dials the serial number of the trunk line
(4 digits).
3. The status of the selected trunk line is displayed.
4. If the selected trunk line is not idle, the attendant presses the
"FORC RLS" key.
5. The trunk line and the attendant are released.
Note: It is required the option of “Use ATD Force Release”
(Yes) – 5.6 ATD Service Option.
Button
Procedures
Display
This function enables attendant to select a specific extension/trunk and to release the extension/trunk compulsorily.
FORC
RLS
TRK
SEL
FORC
RLS
ATN: 0000 09 : 00 : 00
00 00 00 BUSY:
00 2002 I ECONV
00 2102 I
ATN: 0000 09 : 00 : 00
00 00 00 BUSY:
00 0016 BW ECONV
00 2002 I

## Slide 20
Night Transfer(PNA)
Attendant night transfer
1. If the system is set up in day mode, an operator pushes the
"NIGHT" button on the left side of the attendant.
2. Then, the “NITE" LED of the attendant turns on.
3. An incoming call to the attendant is terminated.
4. All incoming calls to the individual number of each attendant
in the night mode are automatically transferred to night
extension (PNA Extension).
5. When an outside subscriber calls the attendant
representative number or when an extension enters the
attendant calling code, normally the attendant is called.
However, if the attendant of the tenant is operated in the
night mode, the incoming call is automatically forwarded to a
night extension (PNA Extension).
6. The operator pushes the "NIGHT" (Night Mode) button on
the left side of the attendant again for changing night mode
to day mode.
7. Then, the “NITE" LED of the attendant turns off.
Button
Procedures
Display
This function enables an operator to change the day mode to the night mode so that an incoming call can be connected to the extension registered as night extension automatically.
NITE
NIGHT
NITE
NIGHT
ATN: 0000 09 : 00 : 00
00 00 00 BUSY:
S: NIGHT A: NIGHT
ATN: 0000 09 : 00 : 00
00 00 00 BUSY:
S: DAY A: DAY

## Slide 21
Overflow
Attendant overflow
1. When judging that there are too many incoming calls waiting
at an attendant, the operator presses the "OVF" key.
2. Then, the "OVF" LED of the attendant turns on.
3. Incoming calls over a certain number are forwarded to the
attendant so that call waiting happens.
4. Then, the calls waiting at the attendant are transferred to the
attendant overflow subscriber.
5. The operator presses the "OVF" key again in order to cancel
the overflow function.
6. Then, all incoming calls received after then are transferred to
the attendant.
Button
Procedures
Display
If the number of calls incoming to attendants increases and consequently the number of waiting calls exceeds certain number, this function enables an operator to assign substitute attendant overflow extension to an extension so that the waiting calls are forwarded to the substitute attendant overflow extension.
OVF
OVF
ATN:0000 09 : 30 : 55
00 00 00 BUSY:
S: DAY A: DAY

## Slide 22
Through Dialing
When the attendant provides the trunk only.
1. The operator is in conversation with an extension.
2. The operator dials the trunk access code if the extension
desires to make the trunk call.
3. The serial number of the available trunk is displayed on the
attendant LCD and the extension will hear the hold tone as
he becomes automatically held.
4. The operator presses "CONNECT" key.
5. The attendant LCD is cleared off, the extension hears the
trunk dial tone and the attendant is released.
6. The extension dials the outside subscriber number.
When the attendant dials all the outside subscriber
numbers while the attendant is in conversation with the
extension.
1. The operator is in conversation with the extension.
2. The operator dials both the trunk calling code and the
outside subscriber number.
3. The extension hears the hold tone as he becomes
automatically held and the operator hears the trunk ring back
tone.
4. The operator presses "CONNECT" key.
5. The attendant is released and the held call between
extension and outside subscriber is performed.
Button
Procedures
Display
This function allows the operator to seize a trunk instead of an extension whose trunk outgoing was restricted, and then send the call instead of the related extension.
CONNECT
CONNECT
ATN: 0000 09 : 00 : 00
00 00 00 BUSY:
00 0026 BW
ATN: 0000 09 : 00 : 00
00 00 00 BUSY:
S: DAY A: DAY
ATN: 0000 09 : 00 : 00
00 00 00 BUSY:
00 0030 BW
8182000

## Slide 23
Trunk Selection
Trunk selection
1. The attendant presses the "TRK SEL" key
at the attendant.
2. The attendant dials the trunk serial number (four digits).
3. The selected trunk is occupied.
Note)
Trunk Serial Number starts “0000”
Button
Procedures
Display
This function enables the attendant to select and occupy the trunk by dialing its serial number.
TRK
SEL
ATN: 0000 09 : 00 : 00
00 00 00 BUSY:
00 0000 BW IDLE

## Slide 24
Automatic Recall
1. When the recall signal arrives at the attendant console, "RCL
ANS" lamp blinks.
2. Press the "RCL ANS" or "ANSWER" key, then the operator
can talk with the held trunk line; The LCD shows information
of the recalled trunk line
3. If the trunk line wants to talk with the same extension that
he/she wanted to talk, press the "CONNECT" key.
4. If the trunk line wants to talk with other extension, dial the
extension number, then press the "CONNECT" key.
Note) Recall Case
RC-NOANS : Attendant recall message, when the outside extension does not answer the transferred
incoming trunk call for a fixed time.
RC-CAMP : Attendant recall message, when the incoming
Trunk call is held over a fixed time under the camp-
on state.
RC-XFR : When the extension does not answer the transferred incoming trunk call for a fixed time.
RC-WAKE : Attendant recall message, when the Wake-up
registered extension does not answer the wake-up
call or the line is busy at the wake-up time.
3. When a call is received to the attendant console,
the "RCL ANS", "TRK ANS“ or "STA ANS" lamp will blink
according to the incoming call status.
Button
Procedures
Display
When an operator transfers a trunk call to an extension, if the extension does not answer within a assigned time, the transferred line automatically recall the attendant console; So, this feature allows an operator to answer the recall.
CONNECT
RCL
ANS
ANSWER
CONNECT
ATN:0000 09 : 30 : 55
00 00 00 BUSY:
00 2002 I IDLE
00 0008 BW RC-XFR
ATN:0000 09 : 30 : 55
00 00 00 BUSY:
28182003
2002 BW RC-CAMP
ATN:0000 09 : 30 : 55
00 00 00 BUSY:
28182003
2002 I BW RC-XFR
ATN:0000 09 : 30 : 55
00 00 00 BUSY:
WK_NO_ANS
2002 I RC_WAKE
ATN:0000 09 : 30 : 55
00 00 00 BUSY:
WK_BUSY
2002 I RC_WAKE
ATN:0000 09 : 30 : 55
00 00 00 BUSY:
WK_REGIST
2002 I RC_WAKE
ATN:0000 09 : 30 : 55
00 00 00 BUSY:
WK_ANSWER
2002 I RC_WAKE
ATN:0000 09 : 30 : 55
00 00 00 BUSY:
WK_CANCEL
2002 I RC_WAKE

## Slide 25
Attendant Break-in
1. When a called extension is busy, an operator presses
the "BRK IN" Key, then the Break-in Tone will be heard by
the connected parts (by option). After the fixed Break-in Tone
time, an operator can talk with the connected parts in the 3-
way conference mode.
2. After talking with the connected parts, if an operator presses
the "RLS" Key, the attendant console comes out from the
attendant override mode.
Button
Procedures
Display
This feature allows an operator to enter a busy extension within a system and talk with the connected parts like as the 3-Way Conference mode.
BRK IN
RLS
ATN: 0000 09 : 00 : 00
00 00 00 BUSY:
00 2002 I ECONV
00 2102 I
ATN: 0000 09 : 00 : 00
00 00 00 BUSY:
00 2002 I BRK-IN
00 2102 I

## Slide 26
Call Waiting Number Display
1. The call waiting number is displayed on the second line of
LCD with the order of trunk call, recall and extension call.
2. The connected call status is displayed on the fourth line of
the right side of LCD as below:
IC-STA : Incoming extension call message, when an operator answers the incoming call using the "STA ANS" key.
IC-TRK : Incoming trunk call message, when an operator answers the incoming call using the "TRK ANS" key.
RC-NOANS : Attendant recall message, when the outside
extension does not answer the transferred
incoming trunk call for a fixed time.
RC-CAMP : Attendant recall message, when the incoming
Trunk call is held over a fixed time under the camp-
on state.
RC-XFR : When the extension does not answer the transferred incoming trunk call for a fixed time.
RC-WAKE : Attendant recall message, when the Wake-up
registered extension does not answer the wake-up
call or the line is busy at the wake-up time.
3. When a call is received to the attendant console,
the "RCL ANS", "TRK ANS“ or "STA ANS" lamp will blink
according to the incoming call status.
Button
Procedures
Display
When a recall signal or extension/trunk line incoming signal is received to the attendant console, the LCD shows the call waiting number and the incoming call status with the visual indicating lamps.
STA
ANS
TRK
ANS
RCL
ANS
STA
ANS
TRK
ANS
RCL
ANS
ATN: 0000 09 : 00 : 00
00 00 01 BUSY:
ATN: 0000 09 : 00 : 00
01 00 00 BUSY:
ATN: 0000 09 : 00 : 00
00 01 00 BUSY:

## Slide 27
Attendant Camp-on
1. During talking with Trunk line, operator dials the extension
number. If the extension is busy, press the "CAMP ON" Key.
At this time, trunk line is automatically held.
2. When the extension becomes idle, ring signal is sent to the
extension and the ring back tone is sent to the trunk part.
3. ATD presses "CONNECT" key.
3. If the extension does not answer the call within a fixed time,
this call is recalled to the attendant console.
(Refer to "Automatic Recall" feature.)
Button
Procedures
Display
This feature allows an operator to hold an incoming trunk call when a called extension is busy and after the extension becomes idle, it is automatically rung and connected to the waiting trunk party upon answering.
CAMP
ON
ATN: 0000 09 : 00 : 00
00 00 00 BUSY:
00 2002 I ECONV
00 2032 BW IC-TRK

## Slide 28
Attendant Conference
Korea Version
1. During the talk with extension or trunk line subscriber, the
operator dials the extension number (A) for the conference.
2. Extension A answers
3. ATD presses “CONF” key for conference.
4. By the answer of extension (A), a 3-way conference mode is
established.
5. If an operator presses the "RLS" Key, the attendant console
comes out from the 3-way conference mode, and then the
rest, two subscribers can talk with each other.
Button
Procedures
Display
This feature allows an operator to enter the 3-way conference mode including the attendant console.
CONF
RLS
CONF
ATN: 0000 09 : 00 : 00
00 00 00 BUSY:
00 2002 I IDLE
00 0002 BW IC-TRK
ATN: 0000 09 : 00 : 00
00 00 00 BUSY:
00 2002 I CONF
00 0002 BW IC-TRK

## Slide 29
Attendant Lamp Test
Press the "LAMP CHECK" Key, all lamps and LEDs light. If any
lamp or LED does not light, it should be replaced with new ones.
Button
Procedures
Display
This feature allows an operator to check the status of all lamps, LEDs and display panel.
LAMP
CHECK
ATN:0000 09 : 30 : 55
00 00 00 BUSY:
S: DAY A: DAY

## Slide 30
Operator Alarm
1. If an operator presses the "BELL ON/OFF" key located at the
left side of attendant console, the "BELL ON" lamp lights;
On/Off state of the "BELL ON" lamp is alternately changed
by the "BELL On/Off" key.
When the following incidents are happened to an attendant
console under the "BELL ON" lamp-on state, an operator
alarm bell beeps.
a) Key operation error
b) Call waiting indication in attendant console.
When the lamp of STA ANS or TRK ANS or RCL ANS is
blinking.
c) Attendant recall
d) Monitoring call time out
e) Holding call time out
2. “ERR-XX” and “ ERROR” indicate system warning.
3. “ERROR” indicates operator error.
Button
Procedures
Display
When an operator takes a key-operation error or an important job is happened to the attendant console, this feature allows an operator to know various alarms through the visual lamps and audible alarm indicator.
BELL
ON
BELL
ON/OFF
STA
ANS
TRK
ANS
RCL
ANS
ATN: 0000 09 : 00 : 00
00 00 00 BUSY:
ERROR A:DAY

## Slide 31
Attendant System Speed Dialing
1. Dial the speed dialing number (System Speed Dial Code).
2. If all trunk lines are busy, the busy message is displayed on
the LCD.
3. According to the predetermined code, the programmed
telephone number is automatically transmitted by the system.
After the telephone number transmission, the operator
receives the ring back tone from the trunk line. At this time, if
all trunk lines are busy, the operator receives the busy tone.
4. By the answer of trunk line subscriber, the call is
established.
Button
Procedures
Display
This feature allows an operator to use the system speed dialing feature.
ATN: 0000 09 : 00 : 00
00 00 00 BUSY:
600
ATN: 0000 09 : 00 : 00
00 00 00 BUSY:
00 0019 BW
8182100

## Slide 32
Verify Busy Line Status
Extension status display
1. The attendant dials extension number.
2. The LCD of the attendant displays such information on the
extension as the telephone number, class, tenant number
and current state.
Outside subscriber status display
1. The attendant dials the trunk serial number after pressing
the “TRK SEL” key.
2. The tenant number, trunk serial number and the status of
incoming or outgoing trunk call is displayed on the LCD of
the attendant.
Incoming call display
1. The attendant presses the “ANSWER” key.
2. Type of incoming call is displayed.
Forwarding information display
1. A transfer call is generated at the attendant.
2. The call forwarding information is displayed on the LCD of
the attendant.
Call processing status display
1. The call status that the attendant processes currently is
displayed on the LCD of the attendant.
Button
Procedures
Display
This function allows the attendant to display extension numbers, trunk numbers, thee types of incoming calls, extension numbers incoming from trunks and the status of call process on the LCD when the attendant calls other extension, or an extension calls the attendant, or the attendant is on line with an extension.
TRK
SEL
ANSWER
ATN: 0000 09 : 00 : 00
00 00 00 BUSY:
00 2002 I ECONV
00 2102 I
ATN: 0000 09 : 00 : 00
00 00 00 BUSY:
00 0009 BW ECONV
00 2002 I
ATN: 0000 09 : 00 : 00
00 00 00 BUSY:
00 0002 BW IC-TRK
ATN: 0000 09 : 00 : 00
00 00 00 BUSY:
00 2002 I CONNECT
ATN:0000 09 : 00 : 00
00 00 00 00 : 00
00 2002 I IDLE
712004 AFWD

## Slide 33
ATD Group Hunting
1. An operator calls extension A.
2. Extension A is busy, and then operator will hear busy tone.
3. An operator press “GRP CALL” key for calling extension B
registered in same hunting group.
4. If extension B is idle, extension B will ring.
5. Extension B answers.
6. The call between ATD and extension B is established.
Note)
Extension 2002 and 2100 is in the same hunting group.
Button
Procedures
Display
This function allows to call extension registered in same hunting group, when called extension is busy
GRP
CALL
ATN: 0000 09 : 00 : 00
00 00 00 BUSY:
00 2002 I ECONV
00 2102 I
ATN: 0000 09 : 00 : 00
00 00 00 BUSY:
00 2100 I CONNECT

## Slide 34
ATD Mute
1. ATD presses the “Mute” button during in conversation.
2. The Mute Lamp is turned on and the ATD voice is not sent,
but the ATD can hear the voice of the opposite extension.
3. The ATD presses the Mute button again.
4. The Mute LED is turned off and the function is cancelled.
Button
Procedures
Display
The function allows ATD to receive the voice of the opposite extension without sending the ATD voice during a call.
MUTE
ATN:0000 09 : 30 : 55
00 00 00 BUSY:
S: DAY A: DAY