## Slide 1
Title
Digital Key Telephone User’s Guide
System
CS1000
Abstract
User Guide
LG PBX System
Software Technical Information
STI-0009
Jan. 31, 2001
Revision
Date
By
History
1.0
01.31.2001
C.K Ahn
First Issue
1.1
04.16.2001
Y.K.Song
LCD Display changed

## Slide 2
Contents …………………………………………………2
Digital Key Telephone Family ……………………….. 4
Button Arrangement for ……………………………… 5
Digital Key Telephone Family
Absence Information 1……………………………….. 7
Absence Information 2 ………………………………. 8
ATD Calling Code ……………………………………. 9
Background Music Code ……………………………. 9
Break-in (Override) ………………………………….. 9
Call Back… ………………………………….……….. 10
Call Forward – Busy ………………………….…….. 11
Call Forward – Busy/No Answer ……….………….. 12
Call Forward – Follow Me ………………………….. 13
Call Forward – No Answer ……………………….... 14
Call Forward – Unconditional ……………….……… 15
Call Forward – All Trunk Incoming ……………….. 16
Call Forward –VPM All CFWD ……………………... 17
Call Forward –VPM Busy CFWD………………….. 18
Call Forward –VPM No Answer CFWD…………… 19
Call Forward –VPM Busy/No Answer CFWD …... 20
Call Forward – Cancel ……………………………… 20
Call Hold - Individual(Exclusive) ………………….. 21
Call Hold - System …………………………………. 21
Call Park - Individual(Exclusive) ………………….. 22
Call Park - System …………………………………. 23
Call Transfer ………………………………………... 24
Call Waiting …………………………………………. 25
Camp-On ……………………………………………. 25
Conference …………………………………………. 26
Consultation Transfer …………………...………… 26
Consultation Transfer to Conference ………….… 27
Do Not Disturb (DND) ……………………………… 27
DKTU - Dial Memo …………………………….… 28
DKTU - Flexible Button ……….…….…. 39
DKTU - Ring Selection …………………. 30
DKTU Name Registration ………….…… 31
Last Number Redial …………………..……. 31
Manager/Secretary Calling ………………... 32
Message Waiting 1 …………………………. 33
Message Waiting 2 …………………………. 34
Message Waiting 3 …………………………. 35
Mute …………………………………….……. 36
Name Display ………………………….……. 36
Outgoing Restriction …………………..……. 37
Outside Call …………………………………. 38
Other Group Call Pick-Up …………………. 39
Password Change …………………….……. 39
Privacy ……………………………………….. 40
Revertible Ring ……………………………… 40
Same Group Call Pick-Up …………………. 41
Save and Repeat …………………………… 41
Selective DND ………………………………. 42
Service Class to Day Change Code ………. 42
Service Class to Night Change Code ……... 42
Speed Dial - Individual(Exclusive) ………… 43
Station to Station Call ………………………. 44
Transfer to Attendant ………………………. 44
Timed Reminder (Wake-Up) ………………. 45
Walking COS (Remote DOD) ……………… 46
Speakerphone……………….. ……………… 47
Speaker Volume Control ……….…………… 47
Ring Volume Control ………...……………… 47
Contents

## Slide 3
KD Series
● KD-36D ● KD-24N
KD-36D : LCD Display, 24 Flexible Buttons
KD-36N : No LCD Display, 24 Flexible Buttons
KD-24D : LCD Display, 12 Flexible Buttons
KD-24N : No LCD Display, 24 Flexible Buttons
Large Digital Key Telephone (You cannot use Large LCD keyset with GDK-16/20W system.)
● KD-33LD ● KD/E-36LD
KD/E Series
● KD/E-36EXE ● KD/E-24ENH ● KD/E-8BTN
KD/E-36EXE : LCD Display, 24 Flexible Buttons
KD/E-36ENH : No LCD Display, 24 Flexible Buttons
KD/E-24EXE : LCD Display, 12 Flexible Buttons
KD/E-24ENH : No LCD Display, 24 Flexible Buttons
KD/E-8 BTN : No LCD Display, 8 Flexible Buttons
Digital Key Telephone Family

## Slide 4
LKD Series (You cannot use LKD-30LD with GDK-16/20W system.)
● LKD-2N/S ● LKD-8D/S ● LKD-30LD
LKD-2N/S: No LCD Display, 2 Flexible Buttons
LKD-8D/S: LCD Display, 8 Flexible Buttons
LKD-30D: LCD Display, 30 Flexible Buttons (Dual LED with Flex. BTN 01~24 & Single LED with 25~30)
LKD-30LD: Large LCD Display, 30 Flexible Buttons (Dual LED with Flex. BTN 01~24 & Single LED with 25~30)
LKD-DSS: 48 Flexible Buttons
Digital Key Telephone Family

## Slide 5
Button Arrangement for Digital Key Telephone Family
Large Digital Key Telephone (You cannot use large LCD keyset with GDK-16/20W system.)
● KD-33LD ● KD/E-36LD
KD Series
● KD-36D ● KD-36N ● KD-24D ● KD-24N

## Slide 6
Button Arrangement for Digital Key Telephone Family
KD/E Series
● KD/E-36EXE ● KD/E-24ENH ● KD/E-8BTN
LKD Series
● LKD-8D/S ● LKD-30D

## Slide 7
Absence Information 1
Lunch return at HH : MM (Registration)
This is a feature to inform the other of having lunch when one is called by the other extension.
TRANS/PGM + DND/FWD + 01 + Hour (HH) + Minute (MM) + HOLD/SAVE
On vacation return at date MM – DD (Registration)
This is a feature to inform the other of having a Vacation when one is called by the other extension.
TRANS/PGM + DND/FWD + 02 + Month (MM) + Day (DD) + HOLD/SAVE
Out of office return in AM (Registration)
This is a feature to inform the other of being out of the office and return to the office in AM, when one is called by the other extension.
TRANS/PGM + DND/FWD + 03 + HOLD/SAVE
Out of office return in PM (Registration)
This is a feature to inform the other of being out of the office and return to the office in PM, when one is called by the other extension.
TRANS/PGM + DND/FWD + 04 + HOLD/SAVE
Out of office return tomorrow (Registration)
This is a feature to inform the other of being out of the office and return to office tomorrow, when one is called by the other extension.
TRANS/PGM + DND/FWD + 05 + HOLD/SAVE
Out of office return unknown (Registration)
This is a feature to inform the other of being out of the office without a schedule when one is called by the other extension.
TRANS/PGM + DND/FWD + 06 + HOLD/SAVE
Button
Procedures
Range
This feature allows user to select an absence information to be displayed on the LCD of DKTU calling the station.

## Slide 8
Absence Information 2
Out of town (Registration)
This is a feature to inform the other of having left the office and not being this town, when one is called by the other extension.
TRANS/PGM + DND/FWD + 07 + HOLD/SAVE
In a Meeting return at time HH: MM (Registration)
This is a feature to inform the other of having a conference and the time of ending a conference when one is called by the other extension.
TRANS/PGM + DND/FWD + 08 + Hour (HH) + Minute (MM)
+ HOLD/SAVE
At home (Registration)
This is a feature to inform the other of having left the office when one is called by the other extension.
TRANS/PGM + DND/FWD + 09 + HOLD/SAVE
At branch office (Registration)
This is a feature to inform the other of having a business trip to branch office when one is called by the other extension.
TRANS/PGM + DND/FWD + 10+ HOLD/SAVE
Call : XXX – XXXX (Registration)
This is a feature to inform the other of the place where one is when one is called by the other extension.
TRANS/PGM + DND/FWD + 11 + Telephone Number + HOLD/SAVE
In office : STA XXXX (Registration)
This is a feature to inform the other of stand-by in the office when one is called by the other extension.
TRANS/PGM + DND/FWD + 12 + Extension Number + HOLD/SAVE
Absence Information Cancel
This is a feature to cancel the absent announcement.
TRANS/PGM + DND/FWD + 00 + HOLD/SAVE
Button
Procedures
Range
This feature allows user to select an absence information to be displayed on the LCD of DKTU calling the station.

## Slide 9
ATD Calling Code
1. Extension dials one of “Attendant Calling Code”,
“Attendant Telephone Number” or “Attendant Representative
Number”,
2. If the attendant answers, a call between extension and
attendant is performed.
Button
Procedures
Range
This function allows extension to call ATD.
Background Music Code
Registration
1. Off Hook
2. Press background music registration code (#2) + ID(0~9)
Cancel
1. Off Hook
2. Press background music cancel code (#2) + *
Button
Procedures
Range
This feature allows user to listen to background music during idle time by registering this feature.
Break-in (Override)
1. An extension hooks off the handset.
2. The extension dials another extension number whose line is
busy.
3. The extension hears the busy tone because the subscriber’s
line is busy.
4. The calling extension enters the override code (Default: 3).
5. The break-in tone is sent to inform the called extension of the
override.
6. The called extension hears the break-in tone and a 3-PTY
conference call is set up.
Button
Procedures
Range
The function allows an extension or operator to break in another extension call. First, the system sends the break-in tone to the extension whose line is busy to inform the extension of the override. And then, it changes the mode to 3-way conference mode. In this case, a conference call alarm tone is provided as an option.

## Slide 10
Call Back
1. An extension dials another extension.
2. The calling extension hears the busy tone.
3. The calling extension dials “4” or “CALL BK” button.
4. The reserving extension hears the service set tone as the
sign of the call completion.
5. The following message is displayed on the LCD.
PLACED IN QUEUE FOR
STAXXXX 09:00 am
6. The reserving extension hooks on the handset and waits.
7. The call in the reserved extension has been completed.
8. The ringing is sent to the reserving extension.
9. The reserving extension hooks off the handset.
10. The ring back tone is sent to the reserving extension and
the ringing to the reserved extension.
11. The reserved extension answers.
12. A call is performed.
call back cancel
1. The reserving extension hooks off the handset.
2. The reserving extension presses the “CALL BK” button or the
extension call back cancel code (Default: *55).
3. The reserving extension hears the service set tone as the
sign of extension call back cancel.
Button
Procedures
Range
This function reserves a call when the called extension is busy and then let the call be made after the previous call of the called extension is completed, by giving the ringing to the reserving extension as soon as the previous call is completed and then automatically transmitting the ringing to the reserved extension when the reserving extension hooks off the handset.

## Slide 11
Call Forward – Busy
1. An extension hooks off the handset or presses “MON”
button.
2. The extension presses “DND/FWD” button. In this case, the
following message is displayed on the LCD.
ENTER CALL FORWARD TYPE
3. The extension enters “2”. In this case, the following message
is displayed on the LCD.
ENTER A DIAL DIGIT
4. The extension dials an extension number or outside number
with trunk access code.
5. If the number is valid and the registration is successfully
completed, the extension hears the service set tone, the
“DND/FWD” LED turns on and flashes, and the following
message is displayed on the LCD.
(Call forward to extension number)
FORWARD – BUSY
XXXX 09:00 am
(Call forward to outside number)
FORWARD – BUSY
XXXXXXXXX 09:00am
Button
Procedures
Range
When an extension that is registered with this function is busy, this function lets the incoming calls to be forwarded to other pre-determined extension/outside subscriber.

## Slide 12
Call Forward – Busy/No Answer
1. An extension presses “MON” button.
2. The extension presses “DND/FWD” button. In this case, the
following message is displayed on the LCD.
ENTER CALL FORWARD TYPE
3. The extension enters “4”. In this case, the following message
is displayed on the LCD.
ENTER A DIAL DIGIT
4. The extension dials an extension number or outside number
with trunk access code.
5. If the number is valid and the registration is successfully
completed, the extension hears the service set tone, the
“DND/FWD” LED turns on and flashes, and the following
message is displayed on the LCD.
(Call forward to extension number)
FORWARD – BUSY/NO ANS
XXXX 09:00 am
(Call forward to outside number)
FORWARD – BUSY/NO ANS
XXXXXXXXX 09:00am
Button
Procedures
Range
When an extension that is registered with this function is busy or does not answer, this function lets the incoming calls to be forwarded to other pre-determined extension/outside subscriber.

## Slide 13
Call Forward – Follow Me
1. An extension presses “MON” button.
2. The extension presses “DND/FWD” button. In this case, the
following message is displayed on the LCD.
ENTER CALL FORWARD TYPE
3. The extension dials “#”. In this case, the following message
is displayed on the LCD.
ENTER A DIAL DIGIT
4. The extension dials an extension number where to register
with the call forward – follow me. In this case, the following
message is displayed on the LCD.
ENTER CURRENT PASSWORD
5. The extension dials the password of above extension
number. In this case, the following message is displayed in
LCD.
ENTER A STATION NUMBER
6. The extension dials the extension number where the call
forward – follow me will be registered.
7. If the registration is successfully completed, the confirm tone
is sent out.
8. In a terminal where the call forward – follow me is registered,
the “DND/FWD” button LED turns on and flashes, and the
following message is displayed on the LCD.
FORWARD – ALL
XXXX 09:am
Button
Procedures
Range
When an extension that does not register with the call forward moves, this function allows the extension to register with the unconditional call forward from the original call forwarded phone to a specific phone remotely.

## Slide 14
Call Forward – No Answer
1. An extension hooks off the handset or presses “MON”
button.
2. The extension presses “DND/FWD” button. In this case, the
following message is displayed on the LCD.
ENTER CALL FORWARD TYPE
3. The extension enters “3”. In this case, the following message
is displayed on the LCD.
ENTER A DIAL DIGIT
4. The extension dials an extension number or outside number
with trunk access code.
5. If the number is valid and the registration is successfully
completed, the extension hears the service set tone, the
“DND/FWD” LED turns on and flashes, and the following
message is displayed on the LCD.
(Call forward to extension number)
FORWARD – NO ANSWER
XXXX 09:00 am
(Call forward to outside number)
FORWARD – NO ANSWER
XXXXXXXXX 09:00am
Button
Procedures
Range
When an extension that registered to this function does not answer, the function lets the incoming calls to be terminated at the assigned extension/outside subscriber.

## Slide 15
Call Forward – Unconditional
1. An extension hooks off the handset or presses “MON”
button.
2. The extension presses “DND/FWD” button. In this case, the
following message is displayed on the LCD.
ENTER CALL FORWARD TYPE
3. The extension enters “1”. In this case, the following message
is displayed on the LCD.
ENTER A DIAL DIGIT
4. The extension dials an extension number or outside number
with trunk access code.
5. If the number is valid and the registration is successfully
completed, the extension hears the service set tone, the
“DND/FWD” LED turns on and flashes.
6. If the extension hooks on the handset or presses “MON
” button, the following message is displayed on the LED.
(Call forward to extension number)
FORWARD – ALL
XXXX 09:00 am
(Call forward to outside number)
FORWARD – ALL
XXXXXXXXX 09:00am
Button
Procedures
Range
If an extension registers with the call forward - unconditional, all calls incoming to the extension are unconditionally forwarded to other extensions or outside subscribers assigned, regardless of the extension status (busy, idle or DND).

## Slide 16
Call Forward – All Trunk Incoming Call
1. An extension hooks off the handset or presses “MON”
button.
2. The extension presses “DND/FWD” button. In this case, the
following message is displayed on the LCD.
ENTER CALL FORWARD TYPE
3. The extension enters “6”. In this case, the following message
is displayed on the LCD.
ENTER A DIAL DIGIT
4. The extension dials an extension number or outside number
with trunk access code.
5. If the number is valid and the registration is successfully
completed, the extension hears the service set tone, the
“DND/FWD” LED turns on and flashes.
6. If the extension hooks on the handset or presses “MON”
button, the following message is displayed on the LED.
FORWARD – ALL (E)
XXXX 09:00 am
Button
Procedures
Range
If an extension registers with the call forward, only extension incoming are unconditionally forwarded to other extensions, regardless of the extension status (busy, idle or DND).

## Slide 17
Call Forward – VPM All CFWD
1. An extension hooks off the handset or presses “MON”
button.
2. The extension presses “DND/FWD” button. In this case, the
following message is displayed on the LCD.
ENTER CALL FORWARD TYPE
3. The extension enters “7”. If the registeration is successfully
completed, the extension hears the service set tone and
‘DND/FWD’ LED turns on and flashes.
4. If the extension hooks on the handset or presses “MON”
button, the following message is displayed on the LED.
FORWARD – ALL
VOICE MAIL 09:00 am
Button
Procedures
Range
If an extension registers with the call forward, all incoming calls to the extension are unconditionally forwarded to VMS, regardless of the extension status (busy, idle or DND).

## Slide 18
Call Forward –VPM Busy CFWD
1. An extension hooks off the handset or presses “MON”
button.
2. The extension presses “DND/FWD” button. In this case, the
following message is displayed on the LCD.
ENTER CALL FORWARD TYPE
3. The extension enters “8”. If the registeration is successfully
completed, the extension hears the service set tone and
‘DND/FWD’ LED turns on and flashes.
4. If the extension hooks on the handset or presses “MON”
button, the following message is displayed on the LED.
FORWARD – BUSY
VOICE MAIL 09:00 am
Button
Procedures
Range
When an extension that is registered with this function is busy, this function lets the incoming calls to be forwarded to VMS.

## Slide 19
Call Forward –VPM No Answer CFWD
1. An extension hooks off the handset or presses “MON”
button.
2. The extension presses “DND/FWD” button. In this case, the
following message is displayed on the LCD.
ENTER CALL FORWARD TYPE
3. The extension enters “9”. If the registeration is successfully
completed, the extension hears the service set tone and
‘DND/FWD’ LED turns on and flashes.
4. If the extension hooks on the handset or presses “MON”
button, the following message is displayed on the LED.
FORWARD – NO ANSWER
VOICE MAIL 09:00 am
Button
Procedures
Range
When an extension that registered to this function does not answer, the function lets the incoming calls to be terminated to VMS.

## Slide 20
Call Forward –VPM Busy/No Answer CFWD
1. An extension hooks off the handset or presses “MON”
button.
2. The extension presses “DND/FWD” button. In this case, the
following message is displayed on the LCD.
ENTER CALL FORWARD TYPE
3. The extension enters “*”. If the registeration is successfully
completed, the extension hears the service set tone and
‘DND/FWD’ LED turns on and flashes.
4. If the extension hooks on the handset or presses “MON”
button, the following message is displayed on the LED.
FORWARD – BUSY/NO ANS
VOICE MAIL 09:00 am
Button
Procedures
Range
When an extension that registered to this function is busy or does not answer, the function lets the incoming calls to be terminated to VMS.
Call Forward – Cancel
1. An extension picks up the handset or presses “MON”
button.
2. The extension presses “DND/FWD” button.
3. If the call forwarded is registered in the terminal, the
registration information is deleted and if the deletion is
successfully completed, the extension hears the confirm tone
and the flashing “DND/FWD” button LED turns off.
4. If the extension hooks on the handset or presses “MON
” button, the call forward registration information is not
displayed anymore.
Button
Procedures
Range
This function allows the extension to cancel the call forward information that is registered.

## Slide 21
Call Hold – Individual (Exclusive)
1. An extension is in conversation with an extension/outside
subscriber.
2. If the [2.6 System option-Hold Preference] item is set to
“EXC-HOLD”, press the “HOLD SAVE” once. Otherwise,
if it is “SYS-HOLD”, press the “HOLD SAVE” twice to
perform this function.
3. If the Individual Hold is successfully performed, one of the
held flexible buttons on the DKTU flashes.
4. If the DKTU extension that performed the hold desires to
resume the call with the held extension/outside subscriber,
he can do it by pressing the flashing flexible button.
Button
Procedures
Range
This function allows the extension to hold an extension/outside subscriber that is in conversation with him or her. The opposite extension/outside subscriber becomes held hearing the hold tone, and only the extension that performs the hold can resume the call with him or her again.
Call Hold - System
1. An extension is in conversation with other extension/outside
subscriber.
2. if the [2.6 System option-Hold Preference] item is set to
“SYS-HOLD”, press “HOLD/SAVE” button once. Otherwise, if
it is “EXC-HOLD”, press “HOLD/SAVE” button twice.
3. If the system hold is successfully performed, the flexible
buttons of all DKTUs where some extensions/outside
subscribers are held will blink.
4. The DKTU extension that desires to call the held extension /
outside subscriber can resume the call by pressing the
related flexible button.
Button
Procedures
Range
This function holds the extension/outside subscriber that is busy, within the system. The opposite extension waits while hearing the hold tone and then the call held within the system will be connected later.

## Slide 22
Call Park - Individual(Exclusive)
1. An extension presses the “TRANS/PGM Button while on
line.
2. The extension presses the registration code for an individual
call park (Default: #8).
3. The extension registering the individual call park hears
confirm tone when the performance is successful, and the
following message is displayed on the LCD of the extension.
LINE HOLDING
LINE 10603 11:04 AM
4. When function is successfully registered, the held extension
hears hold tone, and the following message is displayed on
the LCD screen.
HELD BY XXXX
JUL 01 93 09:00:am
Answer to the individual call park.
1. The extension parking the call presses the answering code
for an individual call park (Default: #8).
2. A call is connected to the extension being in an individual call
park.
Button
Procedures
Range
This function enables an extension on line to park the call individually and to resume the call with the parked extension when the calling extension wants to make a call again.

## Slide 23
Call Park - System
System call park registration
1. An extension presses “TRANS/PGM” button during the
call.
2. The extension presses the system call park code
(Default: #7).
3. The extension hears the service set tone when if the function
is successfully registered. Then, the following message is
displayed on the LCD.
LINE HOLDING
LINE 10101 09:00 am
4. When the function is successfully registered, the extension
hears the hold tone.
System call park
1. Press the system call park answer code (Default: #7).
2. Press the system call parked extension number.
3. A call is performed with the parked extension/outside
subscriber.
Button
Procedures
Range
This function holds other extension/outside subscriber that is in conversation with him or her, within the system and then lets this held extension/outside subscriber to call with other extension.

## Slide 24
Call Transfer
Unscreened Transfer on extension.
1. Extension (A) is in conversation with other extension (B).
2. Extension (A) presses “TRANS/PGM” button.
3. Extension (B) hears the hold tone.
4. Extension (A) dials the number of extension (C).
5. Extension (A) hears the ring back tone and extension (C)
hears the ringing.
6. Extension (A) hooks on the handset.
7. The extension (B) hears the ring back tone and the extension
(C) hears the ringing.
8. The extension (C) answers.
9. A call is performed between extension (B) and (C).
Screened Transfer on extension.
1. Extension (A) is in conversation with other extension (B).
2. Extension (A) presses “TRANS/PGM” button.
3. Extension (B) is in hold and hears the hold tone.
4. Extension (A) dials the phone number of extension (C).
5. Extension (A) hears the ring back tone and extension (C)
hears the ringing.
6. Extension (C) answers.
7. Call is performed between extensions (B) and (C).
8. Extension (A) hooks on the handset.
9. A call is performed between extensions (B) and (C).
Button
Procedures
Range
This function enables the extension or attendant to be transferred to other extension during the call with opposite extension/subscriber.

## Slide 25
Call Waiting
1. DKTU (A) hooks off the handset.
2. DKTU (A) dials the phone number of extension (B) that is
busy.
3. DKTU (A) hears the busy tone.
4. DKTU (A) dials the call waiting code (Default 5).
5. DKTU (A) is held and hears the hold tone, and the opposite
extension (B) hears the warning tone during the call with
other.
6. DKTU (B) presses “TRANS/PGM” or “HOLD/SAVE”
button.
7. Extension (C) that is on line with DKTU (B) is automatically
held and hears the hold tone. A call is performed between
DKTU (A) that is held hearing the hold tone and Extension (C).
8. DKTU (B) presses “TRANS/PGM” or “HOLD/SAVE button
again.
9. A call is performed again with extension (C), and DKTU (A)
becomes held again.
Button
Procedures
Range
When an extension needs to call another extension urgently, the extension can dial the call waiting code to notify the opposite party of that the extension has an emergency call at the moment. The extension that is called by the call waiting hears the warning tone and then it can let the opposite party in conversation with himself to be held and then to perform a call with the emergency calling extension.
Camp-On
1. DKTU (A) calls another DKTU (B) whose line is busy.
2. The busy tone is heard as DKTU (B) is on line.
3. The DKTU (A) presses Camp-On Registration Feature Code
(Default: 6).
4. The hold tone is transmitted to DKTU (A), and the warning
tone to DKTU (B).
5. DKTU (B) hooks on the handset.
6. Ring back tone is transmitted to DKTU (A), and ring current is
transmitted to DKTU (B).
7. DKTU (B) hooks off the handset.
8. The call is performed between DKTU (A) and (B).
Button
Procedures
Range
The function allows a subscriber to inform a waiting call to an extension on line with other extension, and to wait for the answer from the extension.

## Slide 26
Conference
1. DKTU (A) on line with DKTU (B) presses “CONF”(Conference)
button.
2. Extension (B) becomes held and hears a hold tone, and
DKTU (A) hears a dial tone.
3. DKTU (A) enters the telephone number of extension (C) to
have conference with.
4. DKTU (A) hears ring back tone, and extension (C) hears ring
current.
5. Extension (C) answers.
6. Conference call is performed among DKTU (A), (B), and (C).
Button
Procedures
Range
This function enables an extension or an outside subscriber on line to call the other extension to have conference call.
Consultation Transfer
1. Extension (A) is on line with other extension or outside
subscriber (B).
2. Extension (A) presses “TRANS/PGM” button.
3. Extension/outside subscriber (B) becomes held and hears
hold tone, and extension (A) hears 2nd dial tone.
4. Extension (A) dials the number of extension (C).
5. Extension (A) receives ring back tone, and extension (C)
receives ring current.
6. Extension (C) hooks off the handset.
7. Consultation call is made between extension (A) and
subscriber (C), and they decide whether to perform transfer.
8. Extension (A) hooks on the handset.
9. A call is made between extension/outside subscriber (B) and
extension (C).
Button
Procedures
Range
This function enables an extension or an attendant to hold the opposite extension on line, call other extension to perform consultation call, and transfer the call after determining whether to transfer call.

## Slide 27
Consultation Transfer to Conference
1. Extension (A) is on line with other extension or outside
subscriber (B).
2. Extension (A) presses “TRANS/PGM” for transfer.
3. Outside subscriber (B) becomes held and hears hold tone,
and extension (A) hears 2nd dial tone.
4. Extension (A) dials the telephone number of
extension/outside subscriber (C).
5. Extension (A) and (C) receives ringing, respectively.
6. Extension/outside subscriber (C) hooks off the handset.
7. Extension (A) and extension/outside subscriber (C) perform a
consultation call and determine whether to perform a
conference call.
8. Extension (A) presses “TRANS/PGM” button two times.
9. Three way conference call is performed among extension (A),
(B), and (C).
Button
Procedures
Range
This function enables an extension to hold an opposite extension on line, and call other extension for consultation transfer to perform three-way conference call.
Do Not Disturb (DND)
DND registration
1. A DKTU extension presses the “DND/FWD” button while he
is idle.
2. The DND is displayed on the DKTU terminal and the service
is registered.
3. The “DND/FWD” LED turned on.
DND cancel
1. An DKTU extension presses “DND/FWD” button while the
DND is registered to the DKTU.
2. The idle state is displayed on the DKTU terminal and the
service is cancelled.
3. The “DND/FWD” button LED turned off.
Button
Procedures
Range
This function allows the extension to deny all incoming calls by registering the DND (Do Not Disturb) function. It is also possible to cancel the function.

## Slide 28
DKTU - Dial Memo
Register the dial memo on DKTU
1. A DKTU extension is on line with an outside subscriber.
2. The DKTU extension presses “SPEED” button.
3. The DKTU extension presses “TRANS/PGM” button.
4. The DKTU extension dials the trunk code.
5. The DKTU extension dials the phone number of an outside
subscriber.
6. The DKTU extension presses “HOLD/SAVE” button.
7. If above procedure is successfully completed, the following
message is displayed on the LCD.
** COMPLETED **
REDIAL IS REGISTERED
8. The DKTU extension keeps the call with the outside
subscriber who was on line.
Use the registered dial memo on the DKTU
1. A The DKTU extension presses “SPEED” button.
2. The following message is displayed on the LCD.
STATION XXX
MEMORY 09:00 am
3. The DKTU extension dials “#”.
4. Automatic dial to the assigned outside number.
5. The ring back tone is sent out and the called party hears
ringing.
6. When the called party answers the phone, a call is performed.
Button
Procedures
Range
This allows the extension to record the outside subscriber number on its own DKTU while maintaining the call with opposite party.

## Slide 29
DKTU - Flexible Button
Registration
1. Assign trunk button:
TRANS/PGM Button + Flexible Button + 1 + Shelf No (1~3) +
LB No (01~12) + Line No (01~32) + Service set tone + [Flexible
Button + Shelf No (1~3) + LB No (01~12) + Line No (01~32) +
Service set tone] + .. + [.. ]
2. Assign of internal line button:
TRANS/PGM BTN + Flexible Button + 2 + Internal Number +
Service set tone + [Flexible Button + Internal Number + Service
set tone] + .. + [.. ]
3. Assign feature button:
TRANS/PGM Button + Flexible Button + 3 + Function No
(00~14) + Service set tone + [Flexible Button + Function Code
(00~14) + Service set tone] + .. + [ ..]
4. Assign Outside Telephone Number:
TRANS/PGM Button + Flexible Button + 4 + Trunk Access
Code or Outgoing Number including Extension Call Code +
[Flexible Button + Extension Call Code or Outgoing Number
including Extension Call Code] + .. + [ ..]
5. Assign pool/loop button
TRANS/PGM Button + Flexible Button + 5 + Service set tone
6. Assign digit save button
TRANS/PGM Button + Flexible Button + 6 + Digits + [Flexible
Button + Digits] + .. + [ ..]
Verification
1. Press the [TRANS/PGM] button.
2. Press a flexible button to be verified.
3. Then, the property of the flexible button is displayed.
Delete
1. Press the [TRANS/PGM] button.
2. Press a flexible button to be verified.
3. Then, the property of the flexible button is displayed.
4, Dial the number “0”.
5, The service set tone is heard.
Function No.
00 : Delete
01 : Group
Hunting
02 : Call Pick Up
03 : Manager
/ Secretary
Calling &
Transfer
04 : UNAAnswer
05 : Busy Override
06 : Night Class
of SVC
07 : Day Class of SVC
08 : Password Change
09 : Absence Status
Registration &
Cancel
10 : Call Back
11 : Timed Reminder
12 : Call I/C Mode
Change
13 : Call Waiting
14 : Other Group
Pick Up
Button
Procedures
Range
This function allows the extension to utilize flexible buttons for special purposes, changing the features of the flexible buttons in the DKTU or DSS in various ways.

## Slide 30
DKTU - Ring Selection
Ring type selection at DKTU
1. An extension hooks off the handset.
2. The extension dials the LDK Ring Selection code
(Default: #1). The following message is displayed on the LCD.
RING TYPE (0-2) : [X]
MAR 01 2000 09:00 am
“X” indicates the current ring type.
3. The extension dials one of the ring types (0~2).
4. The ring of the selected ring type sounds out. The following
message is displayed on the LCD.
[RING1] Ringing Test
MAR 01 2000 09:00 am
5. The extension hooks on the handset.
Button
Procedures
Range
The function allows the extension using the DKTU to select the ring type.

## Slide 31
Last Number Redial
Last number redial on DKTU
1. An extension hooks off the handset.
2. The extension presses the redial code (Default: ##).
or presses the “SPEED” button + “*”.
or press “REDIAL” button
3. The number of the last extension/trunk dialed by the
extension is redialed.
4. The called extension answers.
5. The call is established.
Button
Procedures
Range
This function automatically stores the last number of outside subscriber dialed by extension/attendant and redials the number when the extension presses the redial code. The new one updates the previously stored number whenever the extension hooks off the handset and dials a new number. Note that special service codes are not redialed.
Name Registration
TRANS/PGM + SPEED + *0 + English Name + HOLD/SAVE
Note) English Name Definition
A = 21, B = 22, C = 23
D = 31, E = 32, F = 33
G = 41, H = 42, I = 43
J = 51, K = 52, L = 53
M = 61, N = 62, O = 63
P = 71, Q = 11, R = 72
S = 73, T = 81, U = 82, V = 83
W = 91, X = 92, Y = 93
Z = 12, . = 13, , = *3, ; = *2, Blank = *1
0 = 00, 1 = 10, 2 = 20, 3 = 30, 4 = 40
5 = 50, 6 = 60, 7 = 70, 8 = 80, 9 = 90
DKTU Name Registration
Button
Procedures
Range
This is a feature to indicate a name on the other’s LCD at the time of paging or incoming by inputting his name instead of his telephone number.

## Slide 32
Manager/Secretary Calling
Calling from the secretary to the manager
1. A secretary hooks off the handset.
2. The secretary dials manager’s number.
3. If the manager is in idle state, the secretary and the manager
hear the ring back tone and ringing, respectively. If the
manager answers the ringing, a call is established.
4. If the manager is not in idle state, the secretary hears the
busy tone.
Calling from one manager to the other manager
1. The manager hooks off the handset.
2. If the option of manager’s calling is unconditional call, the call
is performed. If the option is the calling by class, the call is
performed only in case that the calling manager class is
higher than or equal to the called manager class, and
otherwise, the calling manager hears the busy tone.
Calling from the extension to the manager
1. An extension hooks off the handset.
2. The extension calls the manager.
3. If the option of manager call from extension is assigned as
auto-transfer to secretary ,the extension call is transferred to
secretary, otherwise, the call is connected to the manager.
4. The manager or secretary answers the call.
5. The call is established.
Calling from the trunk to the manager
1. Outside subscriber dials manager’s extension number.
2. If the option of manager call from trunk is assigned as
auto-transfer to secretary ,the trunk incoming call is
transferred to secretary, otherwise, the call is connected to
the manager.
4. The manager or secretary answers the call.
5. The call is established.
Button
Procedures
Range
In general, an extension cannot make a direct call to a manager, but should go through the secretary. However, Managers and secretaries can call each other directly. They can call each other by dialing the extension number or the manager/secretary calling code.

## Slide 33
Message Waiting 1
Message waiting registration on DKTU
1. An extension dials another extension number.
2. The extension does not answer the call since the extension
is absent.
3. The calling presses the “CALL BK” button.
4. The calling extension hears the service set tone.
5. If the terminal to which the message waiting is registered is
DKTU, the following message is displayed.
MSG EXT(1)TRK(0) VM(0)
2000-03-01 09:00 am
Message waiting answer on DKTU
1. The message waiting is displayed on the LCD of the extension.
2. The extension presses the “MON” button.
3. The extension presses the “CALL BK” button.
4. The extension receiving the message hears ring back tone while
the extension that registered the message hears the ringing.
5. The extension that registered the message answers the ring.
6. A call between the two extensions is established.
Message waiting Cancel on DKTU
1. An extension hooks off the handset.
2. The extension enters the message Cancel code (Default:
*700). At this time, the following message is displayed on the
LCD of DKTU.
ENTER A STATION NUMBER
3. The extension presses the number of another extension that
received the message.
4. The extension hears the service set tone.
Message waiting answer rejection on DKTU
1. The extension presses “CALL BK” button.
2. The extension presses the “DND/FWD” button.
3. The extension hears the service set tone.
4. At this time, the deleted message is not displayed on the LCD
screen any more.
Button
Procedures
Range
When the called extension is absent, this function enables the calling extension to leave a message and notifies the called extension of the message when the called extension comes back.

## Slide 34
Message Waiting 2
Message waiting registration by the outside subscriber
1. An outside subscriber calls an extension.
2. The called extension does not answer the call.
3. The outside subscriber is released.
4. The message waiting is automatically registered to the
extension according to the message waiting registration option.
MSG EXT(0)TRK(1) VM(0)
MAR 01 2000 09:00 am
Deletion of all message waiting information registered to
DKTU
1. An extension dials the deletion code (Default: *70*) of all
message waiting information.
2. All information is deleted and the result is displayed on the LCD
of DKTU.
Deletion of all message waiting information registered to
DKTU by the request from the extension
1. An extension dials the deletion code (Default: *701) of all
message waiting information registered by the request from the
extension.
2. All information is deleted and the result is displayed on the LCD
screen of DKTU.
Deletion of all message waiting information registered to
DKTU by the request from the outside subscriber
1. An extension dials the deletion code (Default: *702) of all
message waiting information registered by the request from the
outside subscriber.
2. All information is deleted and the result is displayed on the LCD
screen of DKTU.
Button
Procedures
Range
When the called extension is absent, this function enables the calling extension to leave a message and notifies the called extension of the message when the called extension comes back.

## Slide 35
Message Waiting 3
Deletion of all message waiting information registered to
DKTU by the request from the VPM
1. An extension dials the deletion code (Default: *703) of all
message waiting information registered by the request from
the VPM.
2. All information is deleted and the result is displayed on the
LCD screen of DKTU.
One by one deletion of the message waiting information
registered to DKTU
1. The LED of the reserve button flashes if there is any
registered message.
2. The extension presses the Waiting button while the handset
is in position.
3. If there are more than two registered messages, they are
displayed on the LCD of the DKTU in the order that they were
received.
MESSAGE:XXXX 18:50
2000-03-01 09:00 am
4. To delete any registered message, the extension should
press the “DND/FWD” button while the message to delete is
displayed on the LCD.
Button
Procedures
Range
When the called extension is absent, this function enables the calling extension to leave a message and notifies the called extension of the message when the called extension comes back.
Mute
1. A DKTU presses the “Mute” button during in conversation.
2. The Mute LED is turned on and the DKTU voice is not sent,
but the DKTU can hear the voice of the opposite extension.
3. The DKTU presses the Mute button again.
4. The Mute LED is turned off and the call is restored.
Button
Procedures
Range
The function enables a DKTU to receive the voice of the opposite extension without sending the DKTU voice during a call.

## Slide 36
Name Display
Call received directly from the terminal of which the name
Is “CS1000”
CALL FROM CS1000
2000-03-01 09:00 am
Call incoming to the terminal of which the name is “CS1000”
CALL TO CS1000
2000-03-01 09:00 am
Call received by the call pick up from the terminal of which
the name is “CS1000”
PICK UP CS1000
CONNECT XXXX 09:00 am
XXXX: Extension that is actually in a call
Call picked up by extension C (CS1000 is registered as
the name) while extension A calls extension B
PICKED BY CS1000
CALL TO XXXX
XXXX: Extension number of extension B
Button
Procedures
Range
If an extension registers his or her name as well as the phone number, the function displays extension’s name and his or her number when calling/in a call/picking up.

## Slide 37
Outgoing Restriction
Outgoing restriction registration
1. An extension hooks off the handset.
2. The extension enters the outgoing restriction registration
code (Default: *45).
3. The extension enters the extension own 4-digit password.
4. The extension assigns the outgoing restriction type (0~3).
5. The extension hears the service set tone indicating that the
registration is completed.
Outgoing restriction Cancel on SLT/DKTU
1. An extension hooks off the handset.
2. The extension enters the outgoing restriction Cancel
code (Default: *44).
3. The extension enters the extension own 4-digit password.
4. The extension hears the service set tone indicating that the
registration is completed.
Outgoing restriction type
0=Cancel, 1=LOCAL, 2=DDD, 3=ISD
Note) Type
0=Cancel
1=Local/DDD/ISD Call restriction
2=DDD/ISD Call restriction
3= ISD Call restriction
Button
Procedures
Range
The function enables extensions to restrict outgoing calls by setting their own password to their terminals so that other extension cannot attempt outgoing calls with the terminals.

## Slide 38
Outside Call
Trunk call with trunk access code
1. Extension goes to off hook.
2. Extension hears extension dial tone.
3. Extension press trunk access code.
4. Extension hears trunk dial tone.
5. Extension dials outside number.
6. Extension hears ring back tone.
7. Outside subscriber answers the call.
8. The call between extension and outside subscriber is
established.
Trunk call with flexible button.
1. Extension goes to off hook.
2. Extension hears extension dial tone.
3. Extension press flexible button assigned as trunk port.
4. Extension hears trunk dial tone
5. Extension dials outside number.
6. Extension hears ring back tone.
7. Outside subscriber answers the call.
8. The call between extension and outside subscriber is
established.
Button
Procedures
Range
Used for an outgoing trunk call. With this function, it is possible to make a group call or an individual call of an outgoing trunk call.

## Slide 39
Password Change
1. A DKTU dials the password change code (Default: *43).
2. The DKTU enters the current 4-digit password.
3. The DKTU enters the new 4-digit password.
4. The DKTU presses the “HOLD/SAVE” button.
Note)
The default password of all extension is “0000”.
Button
Procedures
Range
The function enables the extensions to set and change their passwords.
Other Group Call Pick-Up
How to use the feature code
1. An extension in another pickup group rings.
2. The proxy extension presses the other group call pick-up
code (Default: *2).
3. The proxy extension enters the phone number of an
extension that is ringing.
4. The call with the calling extension is established and the
extension that is ringing is released.
How to use the other group call pickup button
1. An extension in another pickup group rings.
2. The proxy extension presses the flexible button of DKTU that
is assigned as other group call pick-up button.
3. The proxy extension enters the phone number of the
extension that is ringing.
4. The call with the calling extension is established and the
extension that is ringing is released.
Button
Procedures
Range
The function enables an extension to answer a call ring incoming to an extension in another pickup group.

## Slide 40
Privacy
Privacy assignment on DKTU
1. A DKTU in a call presses the “TRANS/PGM” button.
2. The opposite extension hears the music on hold.
3. The extension that pressed the “TRANS/PGM” button enters
the privacy code (Default: *461).
4. The call between the two extensions is resumed.
Button
Procedures
Range
This function protects important calls or data calls from interruption of other extensions.
Revertible Ring
1. An extension hooks off the handset.
2. The extension dials his or her number.
3. The extension hears the service set tone.
4. The extension hooks on the handset.
5. The extension hears the ringing.
6. The extension hooks off the handset.
7. The extension hears the service set tone.
Button
Procedures
Range
The function enables extensions to check their own numbers or verify whether the ringing signal normally works.

## Slide 41
Same Group Call Pick-Up
How to use the feature code
1. Ringing is sent to an extension in the same pickup group.
2. Another extension that intends to answer the ringing presses
the same group call pick-up code (Default: **).
3. The call with the calling extension is established and the
extension whose telephone rang first is released.
How to use the same group call pickup button
1. Ringing is sent to an extension in the same pickup group.
2. Another extension that intends to answer the ringing presses
the flexible button in DKTU that is assigned as same group
call pick-up button.
3. The call with the calling extension is established and the
extension whose telephone rang first is released.
Button
Procedures
Range
The function enables an extension to answer a call incoming to another extension in the same pickup group instead of another extension.
Save and Repeat
Number saving on DKTU
1. An extension presses the “SPEED” button while being
connected to another extension or a trunk.
2. If the extension presses the “SPEED” button, the number of
another extension currently on line is saved and the following
message is displayed on the LCD screen.
3. The extension is maintained without disconnection.
Redial of saved number on DKTU
1. If an extension presses the “#9” button. the
2. Another extension’s or outside subscriber’s number that the
calling extension has saved is redialed.
3. Another extension/the outside subscriber answers it.
4. The call is established.
Button
Procedures
Range
The function enables the extension to temporarily save numbers dialed and reuse them.

## Slide 42
Selective DND
Selective DND Registration
1. Only extension incoming call denial
*59 + *
2. Only trunk incoming call denial
*59 + #
3. Trunk/extension incoming call denied
*59 + 0
DND cancel
1. An DKTU extension presses “DND/FWD” button while the
DND is registered to the DKTU.
2. The idle state is displayed on the DKTU terminal and the
service is cancelled.
3. The “DND/FWD” button LED turned off.
Button
Procedures
Range
The subscriber can deny the termination to itself by selecting the internal call or the office call.
Service Class to Day Change Code
Registration
1. Extension press *42
2. Extension press own password (4 digits)
3. Extension hears service set tone.
Button
Procedures
Range
This feature allows extension to change to day class of service.
Service Class to Night Change Code
Registration
1. Extension press *41
2. Extension press own password (4 digits)
3. Extension hears service set tone.
Button
Procedures
Range
This feature allows extension to change to night class of service.

## Slide 43
Speed Dial - Individual(Exclusive)
Registration of individual speed dial on DKTU
1. An extension presses the “TRANS/PGM” button.
2. The extension presses the “SPEED” button.
3. The extension dials a speed dial code (00 ~ 09). At this time,
if the information already registered exists, the information is
displayed on the LCD.
XXXXXXXXXX
MEMORY REG. 00
XXXXXXXXXX : Outside subscriber’s number registered
00 : Speed Dial Code
4. The extension dials the trunk access code and the outside
subscriber’s number.
5. The extension presses the “HOLD/SAVE” button.
6. The extension hears the service set tone indicating that the
registration is completed. At this time, the following message
is displayed on the LCD.
** COMPLETED **
MEMORY REG. 0000
0000 : Speed Dial Code (00 ~ 09)
Verification/usage of individual speed dial on DKTU
1. An extension presses the “TRANS/PGM” button.
2. The extension presses the “SPEED” button.
3. The extension dials a speed dial code (00 ~ 09). At this time,
if the information already registered exists, the information is
displayed on the LCD.
4. The extension presses the “Volume” button to search the
desired information.
5. If the extension finds the number desired to call, the
extension presses the “HOLD/SAVE” button.
6. The outside subscriber is called and answers the call, and
the call between the two is established.
Cancellation of individual speed dial on DKTU
1. An extension presses the “TRANS/PGM” button.
2. The extension presses the “SPEED” button.
3. The extension presses the “Volume” button to search the
desired information.
4. The extension dials 0 to cancel the desired information.
Individual
Speed Dial Code
(00 ~ 09)
Button
Procedures
Range
The function enables an extension to register frequently called numbers of outside subscribers on the list of the speed dial.

## Slide 44
Station to Station Call
Extension call with extension number
1. Extension A goes to off hook.
2. Extension A hears extension dial tone.
3. Extension B press extension B number.
6. Extension hears ring back tone.
7. Extension B answers the call.
8. The call between extension A and extension B is
established.
Extension call with flexible button.
1. Extension A goes to off hook.
2. Extension A hears extension dial tone.
3. Extension A press flexible button assigned as extension B
number.
6. Extension A hears ring back tone.
7. Extension B answers the call.
8. The call between extension A and extension B is
established.
Button
Procedures
Range
Pick up the handset or press the HFREE button, dial and call an extension number.
Transfer to Attendant
Transfer extension to attendant
1. An extension while he is on line presses “TRANS/PGM”
button.
2. The opposite extension that is in conversation at that
moment will hear the hold tone and the extension will hear
the second dial tone.
3. If the extension dials one of “Attendant Calling Code”,
“Attendant Telephone Number” or “Attendant Representative
Number”, the held extension is transferred to the attendant
and hears the ring back tone, and the transferring extension
hears the service set tone.
4. If the attendant answers, a call between transferred
extension and attendant is performed.
Button
Procedures
Range
This function transfers the on line call of an extension to the attendant.

## Slide 45
Timed Reminder (Wake-Up)
Wake up registration on DKTU
1. If a DKTU extension dials the wake up code (Default: *3), the
current registration information is displayed as below.
HH:MM:T (0/1/2)
ENTER YOU WAKE UP TIME
2. The extension sets up the hour (two digits).
3. The extension sets up the minute (two digits).
4. The extension sets up the wake up type
(one digit: 0 = today, 1 = tomorrow, 2 = everyday).
5. The extension presses “HOLD/SAVE” button.
6. The extension hears the service set tone.
Wake up cancel on DKTU
1. A DKTU extension hooks off the handset and hears the dial
tone.
2. The extension dials the wake up cancel code (Default: #3).
3. The extension hears the service set tone. In this case, the
following is displayed to show the wake up function is
deleted.
ERASED WAKE UP TIME
HH:MM
HH:MM : Registration delete Time: Minute.
Button
Procedures
Range
This function allows the extension to setup a specific time and when the time arrives the ringing is sent out to the extension to remind the time.

## Slide 46
Walking COS (Remote DOD)
When not using the Account Code on SLT/DKTU.
1. An extension hooks off the handset.
2. The extension dials the Walking COS code (Default: *78). In
case of the DKTU, the following message is displayed on the
LCD.
ENTER A STATION NUMBER
3. The extension dials the extension number of the telephone to
use. In case of the DKTU, the following message is displayed
on the LCD.
ENTER CURRENT PASSWORD
4. The extension dials the four-digit password of the telephone
to use. In case of the DKTU, the following message is
displayed on the LCD.
More Fet.Code/Acc. Code
5. When the trunk access code is dialed, the idle trunk is
occupied.
6. The extension dials the telephone number of the outside
subscriber.
7. When the outside subscriber answers, a call is established.
(Note)
When the extension password is wrong or set to default
password (0000), the feature is not available.
Button
Procedures
Range
This function enables the extension to use the low class telephone as if using his/her own high-class telephone.
Flash
Button
Procedures
While connected to an outside line, press “FLASH” button.
Range
Disconnects outside line and reseizes dial tone. It can be used to send a timed break recall when
the system is connected with a PBX.

## Slide 47
Button
Procedures
In speakerphone mode, press “VOLUME” button to control the speakerphone volume.
Button
Procedures
When bell rings, press “VOLUME” button to control ring volume.
Ring Volume Control
To activate speakerphone,
1. Press “MON” button.
2. Dial outside line number or intercom number to talk.
Button
Procedures
Pressing an outside line button, a speed button, a station button or dialing a station number will
automatically activate the speakerphone.
Speaker Volume Control
Speakerphone
Range
Range