## Slide 1
Title
SLT User Guide
System
CS1000
Abstract
User Guide
Revision History
LG PBX System
Software Technical Information
STI-0018
Mar. 13, 2001
Revision
Date
By
History
1.0
13.03.2001
C.K Ahn
First Issue
1
1.1
16.04.2001
Y.K Song
Feature code change

## Slide 2
Contents ………………………………………… 2
Attendant calling………………………………… 3
Absence information……………………………. 3
Break in (Override) …………………………….. 3
Call back…………………………………………. 3
Call forwarding…. ………………………………. 3
Call pickup……………………………………….. 3
Call transfer……………………………………… 3
Call waiting………….…………………………… 3
Camp on…………………………..…….……….. 3
Conference………………..…………………….. 3
Consultation transfer……. …………………….. 3
Consultation transfer to attendant…………….. 4
Do Not Disturb (DND)…………………………... 4
Group hunting…………………………………… 4
Individual call park………………………………. 4
Individual speed dial……………………………. 4
Last number redial……………………………… 4
Message waiting…….. ………………………… 4
Outgoing call restriction………. ………………. 4
Password change……………………………….. 4
Privacy……………………………………………. 4
Remote DOD (Walking COS)………………….. 4
Revertible ring…………………………………… 4
Save and repeat………………………………….4
Selective Do Not Disturb……………………….. 5
System call park………………………………….5
Time reminder (Wake up)……………...………. 5
Baby listening………………………….………… 5
Maid state…………………………….………….. 5
Contents
2

## Slide 3
529 – VPM No Answer
52 – VPM Busy/No Answer
● Hang up.
To cancel Call Forwarding
● Lift handset.
● Dial 520.
● Hang up.
Call Pickup
When hearing an unattended phone ringing in your ear.
Same Group Call Pickup
● Lift handset.
● Dial .
● You can be connected to an incoming extension or
outside line call.
Other Group Call Pickup
● Lift handset.
● Dial 2 and Extension no. which is ringing.
● You can be connected to an incoming extension or
outside line call.
Call Transfer
● While connected to an outside line, press
hook switch.
● Dial the desired extension number or external number.
● Hang up to complete call transfer.
Call Waiting
● After receiving intercom busy tone, dial 5.
● Hold tone is heard and wait to be answer.
Answering a Call Waiting
● You will receive warning tone in handset.
● Press hook switch to take a new one.
Camp On
● After receiving intercom busy ton, dial 6.
● Hold tone is heard in calling station and warning
tone is heard in called station.
● When called station answers, talk or hang up to
transfer the call.
Answering a Camp On
● You will receive warning tone in handset.
● Press hook switch to take a new one.
Conference
The system allows fifty six (56) internal extensions and/or external extensions participating in a conference call.
● During conversation, press hook switch and dial # 5.
● Dial the desired extension number or external number.
● Repeat the above steps to participate the extension
in a conference call.
Consultation Transfer
● While connected to an outside line, press hook switch.
● Dial the desired extension number and wait to be
answered.
● Announce the call.
● Hang up to complete call transfer.
Attendant Calling
● Lift handset.
● Dial the following number to access the attendant.
Dial 9 (attendant access code)
Dial the attendant extension number.
Dial the attendant representative number.
Absence Information
You can choose a pre-selected message to be displayed on the LCD of DKTU calling your station.
● Lift handset.
● Dial 8.
● Dial the following number to leave your message.
(01~12)
Dial 01+(Time) LUNCH RETURN AT HH:MM
Dial 02+(Date) ON VACATION RETURN AT MM:DD
Dial 03 OUT OF OFFICE RETURN IN AM
Dial 04 OUT OF OFFICE RETURN IN PM
Dial 05 OUT OF OFFICE RETURN TOMORROW
Dial 06 OUT OF OFFICE RETURN UNKNOWN
Dial 07 OUT OF TOWN
Dial 08+(Time) IN A MEETING RETURN AT HH:MM
Dial 09 AT HOME
Dial 10 AT BRANCH OFFICE
Dial 11+(External no.) CALL XXX-XXXX
Dial 12+(Extension no.) IN OFFICE : STA XXXX
● Press hook switch.
● Hang up.
To erase a pre-selected message.
● Lift handset.
● Dial 8 +00.
● Hang up.
Break In (Override)
● After receiving intercom busy tone, dial 3.
Call Back
● After receiving intercom busy tone, dial 4.
● Hang up.
To cancel Call Back
● Lift handset.
● Dial 55.
● Hang up.
Call Forwarding
● Lift handset.
● Dial the desired call forwarding number
521+Extension no. or (Trunk Access Code+Outside
no.) – Unconditional (All)
522+Extension no. or (Trunk Access Code+Outside
no.) – Busy
523+Extension no. or (Trunk Access Code+Outside
no.) – No Answer
524+Extension no. or (Trunk Access Code+Outside
no.) – Busy/No Answer
52#+Extension no. to be registered + Password +
Extension no. – Follow Me
526+Extension no. – All Trunk Incoming
527 – VPM All Call Forwarding
528 – VPM Busy Call Forwarding
3

## Slide 4
To cancel Message Waiting
● Lift handset.
● Dial 700.
● Dial the desired extension number to be cancelled.
● You will hear the confirmation tone and hang up.
Outgoing Call Restriction
● Lift handset.
● Dial 45.
● Dial the password and restriction type (1~3).
1- Local/DDD/ISD
2- DDD/ISD
3- ISD
● You will hear the confirmation tone and hang up.
To cancel Outgoing Call Restriction
● Lift handset.
● Dial 45.
● Dial the password.
● Dial 0 or pres hook switch.
● Dial 44.
● Dial the password again.
● You will hear the confirmation tone and hang up.
Password Change
● Lift handset.
● Dial 43.
● Dial the current password.
(Note: The default password is “0000”.)
● Dial new password.
● You will hear the confirmation tone and hang up.
Privacy
● During conversation, press hook switch.
● Dial 461.
● Continue talking.
Remote DOD (Walking COS)
● Lift handset.
● Dial 78.
● Dial the desired extension number.
● Dial the password.
● Dial the trunk access code and outside number.
Revertible Ring
● Lift handset.
● Dial own extension number.
● You will hear the confirmation tone and hang up.
● After than, the ring will be sound.
● You will hear the confirmation tone if you answer the
call.
● Hang up.
Save and Repeat
● During conversation, press hook switch.
● Dial # 9.
To use Save and Repeat
● Lift handset.
● Dial # 9.
Consultation Transfer to Conference
● While connected to an outside line, press hook switch.
● Dial the desired extension number and wait to be
answered.
● Announce the call.
● When the other party answers, press hook switch twice.
(All three parties are now connected.)
Do Not Disturb (DND)
● Lift handset.
● Dial 51.
● Hang up.
To cancel Do Not Disturb
● Lift handset.
● Dial 50.
● Hang up.
Group Hunting
● After receiving intercom busy tone, dial 2.
● Wait to be answered by the idle extension in same group.
Individual Call Park
● While connected to an outside call, press hook switch.
● Dial # 8.
● Hang up.
● To retrieve a parked call, dial # 8.
Individual Speed Dial
To store Individual Speed Dial
● Lift handset.
● Dial #.
● Dial speed dial number (0~9).
● Dial the trunk access code and the desired external
number you wish to store.
● Press hook switch.
● You will hear confirmation tone and hang up.
To use Individual Speed Dial
● Lift handset.
● Dial # 6.
● Dial the desired speed dial number (0~9).
Last Number Redial
● Lift handset.
● Dial # #.
Message Waiting
● Lift handset.
● Dial the desired extension number.
● No reply or extension busy tone
from a extension.
● Press hook switch.
● Dial 71.
● Hang up.
To answer Message Waiting
● Lift handset.
● Dial 72.
● You will be connected to the extension which registers
the message waiting.
4

## Slide 5
Selective Do Not Disturb
● Lift handset.
● Dial 58.
● Dial the DND type.
0 - All Calls
- Only internal call
# - Only external call
● You will hear the confirmation tone and hang up.
To cancel Do Not Disturb
● Lift handset.
● Dial 50.
● You will hear the confirmation tone and hang up.
System Call Park
● During conversation, press hook switch.
● Dial # 7.
To retrieve a parked call
● Lift handset.
● Dial # 7.
● Dial the desired extension number to be retrieved.
Timed Reminder (Wake Up)
The system automatically send ring signal to the extension
which registers wake up time.
● Lift handset.
● Dial 3.
● Dial the desired time (HH:MM).
● Dial wake up type (0~2).
0- Today
1- Tomorrow
2- Every Day
● You will hear the confirmation tone and hang up.
To cancel Wake Up
● Lift handset.
● Dial # 3.
● You will hear the confirmation tone and hang up.
Following features are only available in hotel.
Baby Listening
This feature allows a guest to monitor his room from any other party of the hotel. You can hear the room which is set baby listening but the room will not be disturbed.
To activate Baby Listening at guest’s room;
● Lift handset.
● Dial 541.
● You will hear the confirmation ton.
To cancel Baby Listen at guest’s room;
● Lift handset.
● Dial 541.
● You will hear the confirmation tone.
To operate Baby Listening from any other extension in the system;
● Lift handset.
● Dial 542.
● Dial the guest’s own room number.
● Dial the password.
● After hearing the confirmation tone, baby listening is
operated.
Maid State
The maid can update the maid status of any room.
● Lift handset.
● Dial 56.
● Dial room status (1~8)
01- Cleaning Needed
02- Under Cleaning
03- Cleaned Up
04- Repair Needed
05- Under Repair
06- Repair Complete
07- Reserved
● Dial maid identification (4 digits).
● You will hear the confirmation ton.
5