## Slide 1
Important Safety Information

## Slide 2
Important Safety Information

## Slide 3
Important Safety Information

## Slide 4
Table of Contents
Putting into Operation
LDP-7024LD
ICON Description on LCD
Input / Output Devices and Button
Cable Connection
ADP (Additional Device Port)
Placing or answering an outside call
1. Placing an Outside Call
2. Answering an Outside Call
3 Soft & Navigation Button
Basic Function
1. Idle
1.1 Call
1.1.1 Call Log
1.1.2 Speed Dial
1.1.3 Call by Station Name
1.2 Pickup
1.3 Redial
2. Talk
2.1 Transfer
2.2 Conference
2.3 Mute
3. Flash Dial
4. Reject Ring
5. Busy
6. Absence or DND
Menu Button Function
1. Basic Program
1.1 Station Name Program
1.1.1 Name Register
1.1 2 Name Delete
1.2 Bell Program
1.2.1 Melody Register
1.2.2 Melody Delete
1.3 Receive Mode Program
1.4 Day/Night Mode Program
1.5 Speaker Mode Program
1.6 Language Program
1.7 Password Program
1.8 LCD Brightness Program
6
6
7
8
10
11
13
13
13
14
15
15
15
16
17
17
18
18
19
19
20
20
21
21
22
22
23
23
24
24
24
25
25
25
26
26
26
27
27
27

## Slide 5
Table of Contents
2. Advanced Program
2.1 Wakeup Program
2.1.1 Wakeup Register
2.1.2 Wakeup Delete
2.2 Absence Program
2.2.1 Absence Register
2.2.2 Absence Cancel
2.3 Call Forward Program
2.3.1 Call Forward Register
2.3.2 Call Forward Cancel
2.4. Speed Program
3. Bluetooth Program
3.1 Bluetooth Register
3.1.1 Pairing
3.1.2 Unpairing
3.1.3 Paired Information
3.2 Bluetooth Enable
4. Phone Book
5. Schedule
5.1 Schedule Add/Del/Edit
5.1.1 Schedule Add
5.1.2 Schedule Del/Edit
5.2 Find Schedule
5.3 Delete Past Schedule
5.4 View Alarm Schedule
5.5 Delete All Schedule
Phone Book Function
1. New Entry
2. Search By Name
3. Search By Number
4. Search By Group
5. Edit CO Access Code
6. Delete All Entry
Entering Characters
Glossary of Terms
28
28
28
28
29
29
29
30
30
30
31
31
31
32
33
34
34
35
35
36
36
37
38
38
39
39
40
40
42
42
43
44
44
45
46

## Slide 6
Putting into Operation
LDP-7024LD
LDP-7024LD is a user-friendly digital keyset, which offer convenience to user with 3 soft key and navigation key.
Features
-.Trendy and Stylish LDP Family design
-.Multi Level Graphic LCD (9 * 32)
-.Dual LED 24 Flexible buttons
-.Additional Device Port for SLT and FAX
-.Call Log Feature
-.Call Recording Feature (USB Module, Option)
-.Hands-Free Solution (Blue Tooth Module, Option)
-.Wall Mountable(Option)

## Slide 7
Putting into Operation
ICON Description on LCD
ICON
1. You have received message
Description
2. Call forward
3. DND mode
4. Earphone mode
5. Full Duplex Speaker Phone Mode
6. Mute mode
7. Setting melody
8. Setting alarm
9. Schedule
10. Phone book
11. ON : Already paired but linked-radio with headset
12. STADY ON : Ready to make and answer a call.
BLINK : Ongoing communication via Bluetooth headset.

## Slide 8
Putting into Operation
Input / Output Devices and Button
1
2
3
4
5
6
7
8
1
Handset
Earphone-Jack Socket
(Ear/Mic Mode)
Speaker
Speed Button
FWD/DND Button
Speaker Button
Hold/Save Button
Phonebook Button
9
10
11
12
13
14
15
16
17
LCD Display
Ring LED
3 Soft Button
Flexible Button
Trans/PGM Button
Call back Button
Volume Button
Menu Button
Handsfree Microphone
9
11
12
13
14
15
16
17
3
4
5
6
7
8
2
10

## Slide 9
Putting into Operation
17
Used for handset call.
The optional earphone into the handset to provide a handsfree phone conversation.
Outputs tones and voice at your extension.
Used to access speed dialing, speed programming, save number redial.
The DND (Do Not Disturb) feature lets you activate a ‘Do not ring this phone’ mode. When the DND is active, this button is red. It is also used to activate call forwards, to another station or voicemail for example.
Used to forward calls to another station or voice mail.
Speaker toggles the speakerphone state. The button is red when the speakerphone is active.
This button put a call on hold or save information when programming.
Save the telephone number and make a call use this button.
Display information about telephone status, dialing directories, and test message information.
Illuminates when the phone is ringing.
Used to work in conjunction with fixed and flexible feature.
The remaining Flex buttons can be assigned to a features.
This button is used to start a transfer (Trans) of a call or enter programming mode (PGM).
A station can initiate a call back request to another busy station. Once that station becomes idle, the station that left the call back request is signaled.
The volume button adjusts the audio levels follows.
Use this menu button to move to the desired option(Dial, MSG, Program) and use for arrows key.
Used to work in conjunction with fixed and flexible feature.
Handset
Earphone-Jack Socket
Speaker
Speed Button
FWD/DND
Speaker Button
Hold/Save Button
Phonebook Button
LCD Display
Ring LED
3 Soft Button
Flexible Button
Trans/PGM Button
Call Back Button
Volume Button
Menu Button
Handsfree Microphone
16
15
13
14
12
11
10
9
8
7
6
5
3
4
2
1

## Slide 10
Putting into Operation
Cable Connection
①
②
③
④
Cable connection
①, ② Connect the end of the telephone cord to the handset
and the other end to the handset jack at the bottom of the telephone.
③, ④ Connect the end of the cable to the port at the bottom of telephone and the other end to the switch port.
※ Connect the Earphone to the headphone jack at the left side of the telephone.
(In case front view of the base.)

## Slide 11
Putting into Operation
ADP (Additional Device Port)

## Slide 12
Putting into Operation
ADP (Additional Device Port)

## Slide 13
Placing or Answering an Outside Call
1. Placing an Outside Call
Lift handset
▶
Enter the extension number
Dial 9,0 or select CO line flexible button
talk
▶
or
CO Line
Lift handset
▶
Enter the desired phone number
talk
▶
or
▶
Extension
2. Answering an Outside Call
Lift handset
or
▶
talk
Extension and CO Line

## Slide 14
3 Soft & Navigation Button
“3 Soft Button” is located on the bottom of the LCD display and IP LDK systems provide some fitting message for each operation. It gives easy access to operations with a navigation key or volume up/down key. In IDLE state, some operations which becomes available will be displayed “MENU”, “PICKUP” and “REDIAL”. Then by pressing one of 3 soft button, a user can activate the desired feature.
3 Soft Button
31
30
29
28
27
26
25
24
23
22
21
20
19
18
17
16
15
14
13
12
11
10
9
8
7
6
5
4
3
2
1
SAT
FRI
THU
WED
THE
MON
SUN
2004
01/01
STATION 2000
2004-01-01 12:00 pm
CALL PICKUP REDIAL
Navigation Button
Sometimes a system does show all message for some operation, then the arrow key will be displayed the begin or end line. By pressing a navigation key of LDP-7000 series, others will be displayed.
1.BASIC PROGRAM
2.ADVANCED PROGRAM
3.BLUETOOTH PROGRAM
4.PHONE BOOK
5.SCHEDULE
1.BASIC PROGRAM
2.ADVANCED PROGRAM
3.BLUETOOTH PROGRAM
4.PHONE BOOK
5.SCHEDULE

## Slide 15
Basic Function
The 3 soft button enables you to select the various function. For instance, if you want to select the pickup, press the first button on the left as below shown. And if there are more than three functions and displays an arrow on LCD, use navigation key to move the next or previous function.
3 Soft Button is located on the bottom of the LCD display and systems provide.
1. Idle
CALL : Press the [CALL] button to call outgoing.
PICKUP : Press the [PICKUP] button to pickup the ring in the same pickup group.
REDIAL : Press the [REDIAL] button to make a last number redial.
31
30
29
28
27
26
25
24
23
22
21
20
19
18
17
16
15
14
13
12
11
10
9
8
7
6
5
4
3
2
1
SAT
FRI
THU
WED
THE
MON
SUN
2004
01/01
STATION 2000
2004-01-01 12:00 pm
CALL PICKUP REDIAL
1.1 Call
A station can make a call by several methods which are the call log list, the individual speed dial, and the call by extension name.
CALL LOG : Press the [LOG] button to look up the call log list and make the call.
INDSPEED : Press the [INDSPD] button to look up the individual speed dial and make the call.
EXTNAME : Press the [EXTNAME] button to search extension by name and make the call.
Press the [CALL] button to enter call menu.
STATION 2000
2004-01-01 12:00 pm
CALL PICKUP REDIAL
STATION 2000
2004-01-01 12:00 pm
CALL LOG INDSPEED EXTNAME

## Slide 16
Basic Function
1.1.1 Call Log
STATION 2000
2004-01-01 12:00 pm
CALL LOG INDSPEED EXTNAME
01:OG2001
02:OG2002
UPPER INFO CALL
>
[01] EXT O/G 01-01 12:00
2001
OK
01:OG2001
02:OG2002
UPPER INFO CALL
>
CALL TO 2001
2004-01-01 12:00 pm
FLASH CALLBACK
The station can call through call log which is logged incoming, outgoing call to other station or outside through the trunk line.
Press the [CALL LOG] button to display call log list.
Press the [OK] button to return log list.
Press the [CALL] button to call with log list.
Press the volume up/down button to search the list.
If you confirm more detail information that log then press the [INFO] button.

## Slide 17
1.1.2 Speed Dial
System support the individual speed dial. The station can call with this individual speed dial.
Press the [INDSPEED] button to query individual speed dial.
Basic Function
01: 90191234567
02: 9021234567
UPPER CALL
>
Press the volume up/down button to search the list.
Press the [CALL] button to call with selected speed dial.
90191234567
LINE 10101 12:00 pm
FLASH
1.1.3 Call by Station Name
System support the call by station name.
Press the [EXTNAME] button to call by station name.
JONE
ENTER NAME
Enter the station name and hold button to search name and call.
JONE 2001
2004-01-01 12:00 pm
FLASH CALLBACK
STATION 2000
2004-01-01 12:00 pm
CALL LOG INDSPEED EXTNAME
STATION 2000
2004-01-01 12:00 pm
CALL LOG INDSPEED EXTNAME

## Slide 18
A station can pickup a call ringing to an unattended station within the same pickup group by using the pickup procedure.
＊ Refer to system feature manual.
Basic Function
1.2 Pickup
TRANS : Press the [TRANS] button to transfer the call to another station.
CONF : Press the [CONF] button to make a conference.
MUTE : Press the [MUTE] button to mute the handset, speaker, or headset but does not affect the speech coming over the speaker or handset. Pressing the [MUTE] button again activates the microphone.
Press the [PICKUP] button to pickup the call.
1.3 Redial
A station can redial which the latest dialed number.
FLASH : Press the [FLASH] button to flash the station.
CALLBACK : Press the [CALLBACK] button to register call back information.
Press the [REDIAL] button to dial the latest dialed.
STATION 2000
2004-01-01 12:00 pm
CALL PICKUP REDIAL
PICK UP 2001
2002 12:00 pm
TRANS CONF MUTE
STATION 2000
2004-01-01 12:00 pm
CALL PICKUP REDIAL
CALL TO 2001
2004-01-01 12:00 pm
FLASH CALLBACK

## Slide 19
Basic Function
2. Talk
While a station talk to another, the station can redial which the latest dialed number.
TRANS : Press the [TRANS] button to transfer the call to another station.
CONF : Press the [CONF] button to make a conference.
MUTE : Press the [MUTE] button to mute the handset, speaker, or headset but does not affect the speech coming over the speaker or handset. Pressing the [MUTE] button again activates the microphone.
2.1 Transfer
While a station talk to another, the station can transfer the call to any others.
Press the [TRANS] button to transfer the call.
Dial the another extension.
CANCEL : Press the [CANCEL] button to cancel transfer.
CONNECT TO 2001
2004-01-01 12:00 pm
TRANS CONF MUTE
CONNECT TO 2001
2004-01-01 12:00 pm
TRANS CONF MUTE
2002
ENTER A STATION NUMBER
CANCEL
XFER TO 2002
2004-01-01 12:00 pm
CANCEL
CONNECT TO 2002
2004-01-01 12:00 pm
TRANS CONF MUTE

## Slide 20
While a station talk to another, the station can transfer the call to any others.
Basic Function
2.2 Conference
Press the [CONF] button to make conference call.
Dial the another extension.
CANCEL : Press the [CANCEL] button to cancel make conference call.
While a station talk to another, the station can enable to mute the handset, speaker or headset.
2.3 Mute
Press the [MUTE] button to mute or the call.
NOTE
If station has no MUTE button, then station display mute state by character “@”.
CONNECT TO 2001
2004-01-01 12:00 pm
TRANS CONF MUTE
2002
ENTER A STATION NUMBER
CANCEL
CALL TO 2002
2004-01-01 12:00 pm
CANCEL
CONFERENCE
2004-01-01 12:00 pm
TRANS CONF MUTE
CONNECT TO 2001
2004-01-01 12:00 pm
TRANS CONF MUTE

## Slide 21
Basic Function
3. Flash Dial
While a station dial the number, the station can flash the state.
Press the [FLASH] button to flash the state.
The station hears dial tone.
4. Reject Ring
While a station is ringing, the station can reject the call.
Press the [REJECT] button to reject the call.
The station go idle state.
9012345678
LINE 10101 12:00 pm
FLASH
STATION 2000
2004-01-01 12:00 pm
CALL PICKUP DEDIAL
CALL FROM 2001
2004-01-01 12:00 pm
REJECT
STATION 2000
2004-01-01 12:00 pm
CALL PICKUP DEDIAL

## Slide 22
Basic Function
5. Busy
If the called station is busy then the station can execute several function.
The station hears busy tone.
FLASH : Press the [FLASH] button to flash the station.
CALLBACK : Press the [CALLBACK] button to leave message.
CALLWAIT : Press the [CALLWAIT] button to wait relative station goes idle.
CAMP ON : Press the [CAMPON] button to camp on the relative station.
GRPHUNT : Press the [GRPHUNT] button to hunt nay other station in same group.
OVERRIDE : Press the [OVERRIDE] button to override the relative station call.
VOICE OVER : Press the [VOICE OVER] button to voice over the relative station.
6. Absence or DND
If the called station is absence or DND then the station can leave call back message.
FLASH : Press the [FLASH] button to flash the station.
CALLBACK : Press the [CALLBACK] button to leave message.
2001
2004-01-01 12:00 pm
FLASH CALLBACK CALLWAIT>
2001
2004-01-01 12:00 pm
<CAMPON GRPHUNT OVERRIDE>
2001
2004-01-01 12:00 pm
<VOICE OVER
STA IN DO NOT DISTURB
2004-01-01 12:00 pm
FLASH CALLBK

## Slide 23
Menu Button Function
Press the [Menu] button.
1.BASIC PROGRAM
2.ADVANCED PROGRAM
3.BLUETOOTH PROGRAM
4.PHONE BOOK
5.SCHEDULE
1. Basic Program
UPPER
1.STATION NAME PROGRAM
2.BELL PROGRAM
3.RECEIVE MODE PROGRAM
4.DAY/NIGHT MODE PROGRAM
5.SPEAKER MODE PROGRAM
UPPER : Return to upper main menu.
Select the sub menu by using navigation button and press OK button or press digit button which related submenu number.

## Slide 24
1.1.1 Name Register
1.NAME REGISTER
2.NAME DELETE
UPPER OK
>
Press the [OK] or button.
JUNE
ENTER NAME
OK
Enter the Name and press the [OK] or button.
JUNE
WAS REGISTERED
FLASH
Menu Button Function
1.1.2 Name Delete
2.NAME DELETE
UPPER OK
>
Press the [OK] or button.
NAME WAS DELETED !
FLASH
1.1 Station Name Program
1.NAME REGISTER
2.NAME DELETE
UPPER OK
>

## Slide 25
1.MELODY REGISTER
2.MELODY DELETE
UPPER OK
>
1.2 Bell Program
Menu Button Function
1.2.1 Melody Register
1.MELODY REGISTER
2.MELODY DELETE
UPPER OK
>
Press the [OK] or button.
Melody Bell can available set melody option board.
◀ Pleasure(10) ▶
[01] Cancan
[02] Trumpet Ensemble
[03] Pathetique
[04] Russian Dance
[05] Bohe Folk song
EXIT OK
Select the melody category and melody by using navigation button.
Press the [OK] or button.
REGISTYER COMPLETED
FLASH
1.2.2 Melody Delete
2.MELODY DELETE
UPPER OK
>
Press the [OK] or button.
Deleted !
FLASH

## Slide 26
Menu Button Function
1.3 Receive Mode Program
1.4 Day/Night Mode Program
TN MODE
TN / HF
UPPER NEXT CFRM
TN MODE
REGISTER COMPLETED
FLASH
UPPER : Press the [UPPER] button to return previous menu.
NEXT : Press the [NEXT] button to select receive mode.
CFRM : Press the [CFRM] button to register selected receive mode.
DAY MODE
DAY / NIGHT
UPPER NEXT CFRM
DAY MODE
REGISTER COMPLETED
FLASH
UPPER : Press the [UPPER] button to return previous menu.
NEXT : Press the [NEXT] button to select I/C mode.
CFRM : Press the [CFRM] button to register selected I/C mode.
----
Enter Password
Enter the password with four digit.
Initial password is “0000”.
1.5 Speaker Mode Program
SPEAKER MODE
SPK / EARMIC / HEADSET
UPPER NEXT CFRM
SPEAKER MODE
REGISTER COMPLETED
FLASH
UPPER : Press the [UPPER] button to return previous menu.
NEXT : Press the [NEXT] button to select speaker mode.
CFRM : Press the [CFRM] button to register selected speaker mode.

## Slide 27
1.6 Language Program
NATIVE
Select Display Language
UPPER NEXT CFRM
NATIVE
REGISTER COMPLETED
FLASH
UPPER : Press the [UPPER] button to return previous menu.
NEXT : Press the [NEXT] button to select language.
CFRM : Press the [CFRM] button to register selected language.
Menu Button Function
1.7 Password Program
----
Enter Password
Enter the current password with four digit.
Initial password is “0000”.
----
Enter New Password
Enter the new password with four digit.
****
REGISTER COMPLETED
1. BRIGHTEST
2. BRIGHT
3. DARK
4. DARKEST
1.8 LCD Brightness Program
ENTER BRIGHTNESS VALUE (1~4)
PRESS HOLD BUTTON TO SAVE
Select the brightness level by using navigation button or digit button and press hold or ok button to save.

## Slide 28
Menu Button Function
2. Advanced Program
UPPER
1.WAKEUP PROGRAM
2.ABSENCE PROGRAM
3.CALL FORWARD PROGRAM
4.SPEED PROGRAM
UPPER : Return to upper main menu.
Select the sub menu by using navigation button and press OK button or press digit button which related submenu number.
2.1 Wakeup Program
1.WAKEUP REGISTER
2.WAKEUP DELETE
UPPER OK
>
2.1.1 Wakeup Register
HH:MM:T (0/1/2)
ENTER YOUR WAKE UP TIME
FLASH
Enter wake up time with option.
0 : Today
1 : Tomorrow
2 : Everyday
** COMPLETED **
2004-01-01 12:00 pm
FLASH
2.1.2 Wakeup Delete
ERASED WAKE UP TIME
12:00
FLASH

## Slide 29
2.2 Absence Program
Menu Button Function
UPPER
1.LUNCH
2.MEETING
3.VACATION
4.OUT OF OFFICE…
5.ETC…
6.CANCEL ABSENCE
UPPER : Return to upper menu.
Select the sub menu by using navigation button and press OK button or press digit button which related submenu number.
2.2.1 Absence Register
HH:mm
ENTER RETURN TIME
UPPER OK
Enter return time or date.
LUNCH RETURN AT 12:00
2004-01-01 12:00 pm
FLASH
LUNCH RETURN AT XX:XX
IN A MEETING RETURN AT TIME XX:XX
ON VACATION RETURN AT DATE XX-XX
OUT OF OFFICE RETURN AT TIME XX:XX
OUT OF OFFICE RETURN AT DATE XX-XX
OUT OF OFFICE RETURN IN TOMORROW
OUT OF OFFICE RETURN UNKNOWN
OUT OF TOWN
IN OFFICE: STA XXXX
AT BRENCH OFFICE
CALL: XXXXXXXX
Available Absence State
2.2.2 Absence Cancel
Cancel Absence state
FLASH

## Slide 30
2.3 Call Forward Program
Menu Button Function
UPPER
1.ALL
2.BUSY
3.NO ANSWER
4.BUSY / NO ANSWER
5.CANCEL FORWARD
2.3.1 Call Forward Register
2000
ENTER A DIAL DIGIT
FORWARD - ALL
2004-01-01 12:00 pm
FLASH
Enter desired station or outside telephone number.
2.3.2 Call Forward Cancel
All
Busy
No Answer
Busy / No Answer
Call Forward Option
System supports more call forward types. For these type, refer to system feature manual.
NOTE
** Completed **
FLASH

## Slide 31
2.4 Speed Program
Menu Button Function
00
MEMORY REG. 12:00 pm
Enter speed dial number 00~09.
NOT REGISTERED
MEMORY REG. 12:00 pm
Enter outside telephone number include trunk access code.
9123456789
MEMORY REG. 12:00 pm
** COMPLETED **
MEMORY REG. 00
FLASH
Press hold button to save entered telephone number.
3. Bluetooth Program
1.REGISTER BLUETOOTH
2.BLUETOOTH ENABLE
UPPER OK
>
3.1 Register Bluetooth
B L U E T O O T H
1. PAIRING
2. UNPAIRING
3. PAIRED INFORMATION
EXIT NEXT OK

## Slide 32
B L U E T O O T H
EXIT
3.1.1 Pairing
Menu Button Function
SEARCHING FOR DEVICE
PLEASE WAITING ..
■ ■ ■ ■ ■ ■
Before pairing, prepare the bluetooth ear set by pairing mode.
B L U E T O O T H
EXIT OK
[1/1] JABRA 250 (HS)
00-07-A4-00-45-4D
Press OK button.
B L U E T O O T H
EXIT
CONNECTION DEVICE
PLEASE WAITING ..
■ ■ ■ ■ ■ ■

## Slide 33
B L U E T O O T H
EXIT DEL OK
ENTER PIN CODE
CODE : XXXX
Enter the bluetooth ear set pin code and press the OK button.
Menu Button Function
B L U E T O O T H
EXIT
PAIRING SUCCESS
JABRA 250 PAIRED
3.1.2 Unpairing
B L U E T O O T H
EXIT UPPER OK
INITIALIZE DEVICE
ARE YOU SURE?
Press the OK button.

## Slide 34
B L U E T O O T H
EXIT
INITIALIZE DEVICE
PLEASE WAITING ..
■ ■ ■ ■ ■ ■
3.1.3 Paired Information
B L U E T O O T H
EXIT UPPER
JABRA 250 (HS-C)
00-07-A4-00-45-4D
Display paired bluetooth ear set information.
3.2 Bluetooth Enable
BLUETOOTH ON
UPPER NEXT CFRM
Select bluetooth use by press [NEXT] button and save by press [OK] button.
BLUETOOTH ON
REGISTER COMPLETED
FLASH
If the LDP-7024LD set to use bluetooth on, then
NOTE
icon display.
Menu Button Function

## Slide 35
4. Phone Book
Menu Button Function
P H O N E B O O K
1. NEW ENTRY
2. SEARCH BY NAME
3. SEARCH BY NUMBER
EXIT SEL
4. SEARCH BY GROUP
5. EDIT CO ACCESS CODE
P H O N E B O O K
6. DELETE ALL ENTRY
EXIT SEL
Refer to Phone Book Function.
5. Schedule
S C H E D U L E
EXIT SEL
1. SCHEDULE ADD/DEL/EDIT
2. FIND SCHEDULE
3. DELETE PAST SCHEDULE
4. VIEW ALARM SCHEDULE
5. DELETE ALL SCHEDULE
S C H E D U L E
UPPER TODAY SEL
1. SCHEDULE ADD/DEL/EDIT
2. FIND SCHEDULE
3. DELETE PAST SCHEDULE
4. VIEW ALARM SCHEDULE
5. DELETE ALL SCHEDULE
31
30
29
28
27
26
25
24
23
22
21
20
19
18
17
16
15
14
13
12
11
10
9
8
7
6
5
4
3
2
1
SAT
FRI
THU
WED
THE
MON
SUN
CALENDAR
2004/01
The number of the schedule is added up to 50.
The calendar of schedule is from 1960 to 2040.
Select the date by using navigation button and press the OK button to save it.
To move date to current date press TODAY button or digit 5.
To move date to last year, press digit 1.
To move date to next year, press digit 3.
To move date to last month, press digit 7.
To move date to next month, press digit 9.

## Slide 36
SCHEDULE
UPPER ADD VIEW
[PM] 12:00 MEETING
DATE : 2004/01/01(THU) 1/1
5.1 Schedule Add/Del/Edit
Press ADD button to add new schedule.
SCHEDULE ADD
UPPER AM SAVE
DATE
TIME
REPEAT
ALARM
TEXT
: 2004/01/01(THU)
: [PM] 12 : 00
: NONE
: NONE
Use digit key to enter the time directly.
To change AM/PM, press AM or PM button.
SCHEDULE ADD
UPPER SAVE
DATE
TIME
REPEAT
ALARM
TEXT
: 2004/01/01(THU)
: [PM] 12 : 00
: NONE
: NONE
Select repeat option.
Select option is every DAY, WEEK, or MONTH.
Menu Button Function
5.1.1 Schedule Add

## Slide 37
SCHEDULE ADD
UPPER SET SAVE
DATE
TIME
REPEAT
ALARM
TEXT
: 2004/01/01(THU)
: [PM] 12 : 00
: NONE
: NONE
For to set inform alarm press SET button and enter alarm timing.
: 
SCHEDULE ADD
UPPER SET SAVE
DATE
TIME
REPEAT
ALARM
TEXT
: 2004/01/01(THU)
: [PM] 12 : 00
: NONE
: NONE
Enter the schedule name and press the SAVE button to save.
The alarm icon will be displayed on the top of LCD and it will ring for the time. After checking the schedule, the icon will be disappeared.
: CONFERENCE
Menu Button Function
5.1.2 Schedule Del/Edit
Press VIEW button to delete or edit exist schedule.
SCHEDULE ADD
UPPER DEL EDIT
DATE
TIME
REPEAT
ALARM
TEXT
: 2004/01/01(THU)
: [PM] 12 : 00
: NONE
: NONE
: CONFERENCE
To delete this schedule, press the DEL button.
To edit this schedule, press the EDIT button and edit same method.

## Slide 38
5.2 Find Schedule
Menu Button Function
FIND SCHEDULE
UPPER ALL FIND
SEARCH
YEAR
MONTH
TEXT
SCHEDULE
: 2004
: 01
:
Select Year, Month, and enter name of schedule.
RESULTS
UPPER VIEW
DATE : 20040101(THU) 1/1
[PM] 12 : 00 MEETING
Press the VIEW button to check the contents of schedule.
5.3 Delete Past Schedule
PAST SCHEDULE
UPPER SEL
PAST SCH. : 03
Press the DEL button to delete pasted schedule and conform select YES and press SEL Button.
ARE YOU SURE
TO DELETE DATA ?
NO
YES

## Slide 39
5.4 View Alarm Schedule
Menu Button Function
31
30
29
28
27
26
25
24
23
22
21
20
19
18
17
16
15
14
13
12
11
10
9
8
7
6
5
4
3
2
1
SAT
FRI
THU
WED
THE
MON
SUN
2004
01/01
WAKE UP RING
2004-01-01 12:00 pm
CALL PICKUP REDIAL
When the stored schedule comes, the schedule icon will be displayed on the top of LCD and the wakeup ring will ring to inform time.
ALARM SCHEDULE
UPPER
DATE
TIME
REPEAT
ALARM
TEXT
: 2004/01/01(THU)
: [PM] 12 : 00
: NONE
: 00 HOUR 01 MIN BEFORE
: MEETING
After check alarmed schedule, dismissed the alarm icon.
5.5 Delete All Schedule
S C H E D U L E
EXIT SEL
1. SCHEDULE ADD/DEL/EDIT
2. FIND SCHEDULE
3. DELETE PAST SCHEDULE
4. VIEW ALARM SCHEDULE
5. DELETE ALL SCHEDULE
ARE YOU SURE
TO DELETE DATA ?
NO
YES
Press the DEL button to delete pasted schedule and conform select YES and press SEL Button.

## Slide 40
Phone Book Function
P H O N E B O O K
1. NEW ENTRY
2. SEARCH BY NAME
3. SEARCH BY NUMBER
EXIT SEL
4. SEARCH BY GROUP
5. EDIT CO ACCESS CODE
P H O N E B O O K
6. DELETE ALL ENTRY
EXIT SEL
1. New Entry
NEW ENTRY
NAME
TYPE
CO CODE
UPPER ABC SAVE
NUMBER
GROUP
: JUNE
: MOBILE
: NOT USE
:
: NO GR.
Enter the name.
To move to the next step, press the navigation down button.
The number of the phone number registers up to 100.
Use the softkey button to enter the character such as English, Number and Symbol, press the softkey button to select the type ABC, abc, NUM and SYM.
NOTE
NEW ENTRY
NAME
TYPE
CO CODE
UPPER ABC SAVE
NUMBER
GROUP
: JUNE
: MOBILE
: NOT USE
:
: NO GR.
Enter the type, select the desired one among the MOBILE, OFFICE, HOME, FAX, E-MAIL, ADDRESS or MENO.

## Slide 41
NEW ENTRY
NAME
TYPE
CO CODE
UPPER ABC SAVE
NUMBER
GROUP
: JUNE
: MOBILE
: NOT USE
:
: NO GR.
Phone Book Function
Select the CO access code, use the navigation button to select the NOT USE or CODE-1, 2, 3, 4 or 5.
In case of selecting one of the e-mail or address or memo, NOT USE will be displayed and can’t select the CO access code.
NOTE
NEW ENTRY
NAME
TYPE
CO CODE
UPPER ABC SAVE
NUMBER
GROUP
: JUNE
: MOBILE
: NOT USE
: 0191234567
: NO GR.
Enter the phone number. In case of selecting e-mail or address or memo on type, the contents is available.
NEW ENTRY
NAME
TYPE
CO CODE
UPPER ABC SAVE
NUMBER
GROUP
: JUNE
: MOBILE
: NOT USE
:
: NO GR.
Select the group. Use the navigation button to select NO GR., FAMILY, FRIEND, OFFICE, SCHOOL, SENIOR or JUNIOR.
Press the SAVE button to save the new entry.

## Slide 42
2. Search By Name
P H O N E B O O K
1. NEW ENTRY
2. SEARCH BY NAME
3. SEARCH BY NUMBER
UPPER ABC FIND
4. SEARCH BY GROUP
5. EDIT CO ACCESS CODE
SEARCH BY NAME
INPUT NAME ?
JUNE
When entering the name, enter the full name or the part of the name(ex:JUNE) and press the FIND button.
Phone Book Function
For detailed information about entering name, see the Entering Character part of this document.
NOTE
RESULTS
001 : JUNE MARK
003 : ABRAHAM
007 : LUCKY
UPPER EDIT SEND
MOBILE 0191234567
The name will be displayed. Use the navigation button to select the desired name.
Press the EDIT button to correct the phone number.
Press the SEND to make a call.
Select type by using the navigation button.
3. Search By Number
P H O N E B O O K
1. NEW ENTRY
2. SEARCH BY NAME
3. SEARCH BY NUMBER
UPPER FIND
4. SEARCH BY GROUP
5. EDIT CO ACCESS CODE
SEARCH BY NUMBER
INPUT NUMBER ?
019
When entering the phone number, enter the part of the phone number or the full number and press the FIND button.

## Slide 43
RESULTS
001 : JUNE MARK
003 : ABRAHAM
007 : LUCKY
UPPER EDIT SEND
MOBILE 0191234567
The name will be displayed. Use the navigation button to select the desired name.
Press the EDIT button to correct the phone number.
Press the SEND button to make a call.
Phone Book Function
4. Search By Group
P H O N E B O O K
1. NEW ENTRY
2. SEARCH BY NAME
3. SEARCH BY NUMBER
UPPER FIND
4. SEARCH BY GROUP
5. EDIT CO ACCESS CODE
Use the navigation button to select the group and press the FIND button.
SEARCH BY GROUP
NO GR.
FAMILY
FRIEND
OFFICE
RESULTS
001 : JUNE MARK
003 : ABRAHAM
007 : LUCKY
UPPER EDIT SEND
MOBILE 0191234567
The name will be displayed. Use the navigation button to select the desired name.
Press the EDIT button to correct the phone number.
Press the SEND button to make a call.

## Slide 44
5. Edit CO Access Code
Phone Book Function
CO ACCESS CODE
CODE-1 : 9
CODE-2 :
CODE-3 :
UPPER SAVE
CODE-4 :
CODE-5 :
Use the navigation button to select the code and enter the CO access code.
Press the SAVE button to save. The entered CO access code is entered when the phone number registers or corrects.
6. Delete All Entry
Use the navigation button to select YES.
Press the OK or the SEL button to delete all the phone book.
P H O N E B O O K
6. DELETE ALL ENTRY
UPPER SEL
ARE YOU SURE
TO DELETE DATA ?
NO
YES

## Slide 45
Entering Characters
Enter the figure
ABC
abc
NUM
Enter the letters
ABC
abc
▶
▶
Enter the symbol
ABC
abc
NUM
SYMBL
▶
▶
▶
▶
Dial
▶
Dial
▲▼ Norm
1 / 4 ◀▶
① ② ③ ④ ⑤ ⑥ ⑦ ⑧ ⑨ 0
. ( ) - ! ? * _
※ Use the button and then select the symbol.
A
B
C
D
E
F
G
H
I
J
K
L
M
N
O
P
Q
R
S
T
U
V
W
X
Y
Z
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+

## Slide 46
Glossary of Terms
Intercom – describes internal calls within the telephone system
Central Office Line – also known as a trunk line or outside line
A commonly used number stored in a speed bin for easy access
Do Not Disturb – a telephone in DND will show as busy to callers
Forward – your calls can be sent to another location such a voicemail or another station
Direct Dial Inwards or Direct Inwards Dialing – ISDN lines can be provided with multiple telephone numbers which are each routed to individual extensions or Hunt Groups
Digital Key Telephone Unit – a LG digital telephone
Single Line Telephone – an analogue telephone
A type of CO line that comes in multiples of 2 or more
Conference – where you can talk to 2 or more internal or external parties
1
2
3
4
5
6
7
8
9
10
Extension
CO Line
Speed Dial
DND
FWD
DDI or DID
DKTU
SLT
CONF
ISDN