## Slide 1
Business Enabled Communications
V2.0 VM Features
iPECS-MG

## Slide 2
Contents
VMIB Access
Call Recording
Phontage Backup/Delete
Company Directory
Announce Only VM
VM Message Cascade
Voice Mail COS
Outbound Notification
E-mail Notification
Personal CCR (VM Reroute Dest.)
VM Message Playback Options
Message Type (Private / Urgent Message)
Mailbox Features (Send Message, Distribution List, Mailbox control, Broadcast)
VM Message Delivery Confirmation
VM Message Future Delivery
Temporary User Greeting
Delete Sent Message
Remote System Greeting Record
AME (Answering Machine Emulation)

## Slide 3
Voice Mail COS
Voice Mail COS
Attributes | Description | Remark
Greeting Length | This defines maximum user greeting length. | 0-99 Sec.
User Message Length | This defines maximum user message recording time. | 1-600 Sec.
Number of messages | This defines maximum number of voice mail message. | 1-250,
Retention Time | Voice mail messages will be automatically deleted after this amount of days. | 0-99 days
E-Mail Notification | E-mail notification can be enabled or disabled. | ON/OFF
Private Message Mark | Private message mark can be enabled or disabled | ON/OFF
Authority for Greeting & Password | Authority for Greeting & Password can be enabled or disabled | ON/OFF
Distribution List | Distribution List can be enabled or disabled | ON/OFF
Each voice mailbox can have its own class of service so that allows for different parameters for each voice mail such as greeting length, message length, number of messages and etc.
One of 5 COS can be assigned in each mailbox. (1~5).
Station VM COS - VMIB Attribute PGM145
VM COS Option - VM COS Attributes PGM243
Notes: 인사말
메시지 남기는 시간
메시지 개수
메시지 유지 날짜
이메일 송부 여부
PGM 243 Private Message Mark for Private Message
녹음후# 1. 일반, 2.응급, 3. 사설(전달불가) => page 24
3

## Slide 4
The reroute destination can be set as follows
1. From the station : [Tran/PGM] + ‘7’ + ‘7’
2. In Web Admin : [PGM 147] – Index 1
Calls to a voicemail-forwarded station can be rerouted
Personal CCR (VM Reroute Dest.)
1. Call comes in to a station forwarded to voicemail
2. Caller hears the greeting of the called party and dials ‘0’ to request call rerouting
Reroute Destination – Station – Station Group – ACD Group
– Attendant
– Networking Station
– Announcement Table
– Speed Dial

## Slide 5
VM Message Playback Options
VM Message Pause/Resume, Fast Forward and Rewind
“ Hello, this is MJ. I just called to remind you to attend the meeting on next Monday for our new products.
………………………………………………………………... ……………………………………………………………………………………………..“
Initial Position
End Position
Current Position
Voice Message left in the mail-box
PAUSE if user dials ‘8’
①
③ FAST FORWARD if user dials ‘#’
REWIND if user dials ‘*’ ②
④
RESUME if user dials ‘8’
Message RW/FF Time (PGM 147 – 5)
: 03 ~ 99 seconds
Message Playback Time-Line
Notes: 5

## Slide 6
When a caller leaves a message,
the following prompt will be provided.
For regular delivery, press 1.
To mark urgent, press 2.
To mark private, Press 3.
To mark urgent and private, Press 4.
To request delivery receipt of the message
for future, Press 5
VM Message Delivery Confirmation
VM Delivery Confirmation (Available only for internal stations)
① Calling party sends a message with delivery confirmation mark
② Called party checks the received voice message ③ System sends a delivery confirmation message to the calling party
④ Calling party hears the delivery confirmation message
Calling Party
Called Party
①
②
③
④
When the caller hears the message,
the following prompt will be provided.
“Message for XXX was listened to on HH:MM MM/DD”
XXX  mailbox number or recorded name
HH:MM  Time
MM/DD  Date
①
④
Notes: PGM 243 – F7 Confirm Message Receipt
6

## Slide 7
Caller dials ‘6’
User dials 4 digits MM/DD and 4 digits HH:MM.
(Month: 01 ~ 12, Day: 01 ~31, Hour: 00 ~ 11, Minute: 00 ~ 59)
User dials 1 digit for AM or PM should be dialed.
(Example) Dialing 0903 0830 1 means Sep 3rd 8:30 AM
When a caller leaves a message,
the following prompt will be provided.
For regular delivery, press 1.
To mark urgent, press 2.
To mark private, Press 3.
To mark urgent and private, Press 4.
To request delivery receipt of the message
for future, Press 5
For future delivery, press 6
VM Message Future Delivery
Future Delivery
Calling Party
Called Party
②
VMIB
①
System will prompt
“Enter date and time and
press one of the following options, 1 for AM, 2 for PM”
①
System checks the delivery time and sends the message
at the right reserved time.
②
Notes: PGM 243 F6 - Future Delivery Message
7

## Slide 8
Temporary User Greeting
Temporary User Greeting
Press 8 to access the greetings from the main menu.
A new prompt will state, “to listen to your current greeting press 5, to record a new greeting press 7, to access your temporary greeting press 8, to return to the main menu press 9”
Press 8 to record temporary greeting.
To listen, press 1
To record, press 2
To delete, press 3
Once the temporary greeting is recorded, when the user access their mailbox with a temporary greeting active, the prompt “your temporary greeting is recorded and active” will play prior to the main menu prompt.
The user is given an option to record a temporary greeting. Once recorded, the greeting is enabled and played when a caller goes to the mailbox.
Once the greeting is deleted, the standard greeting is resumed.
When the temporary greeting is active, a prompt plays temporary greeting active when a mailbox owner accesses the mailbox.
Notes: 8

## Slide 9
Delete Sent Messages
Delete Sent Messages
Step 1
From the main menu press [5]
The prompt will state “to edit distribution lists press 1, to delete sent message press 2, to access your VM name press 3”
Step 2
Press 2
The prompt will state “enter the mailbox number for the message to delete”
Enter the mailbox number
The prompt will state “mailbox XXX message will be deleted, press # to confirm, * to cancel”
This allows a mailbox owner to delete a sent message before the destination party has listened to it.
Notes: 9