## Slide 1
KEYSET ADMIN
Notes: PC admin is
PC admin can manage all LDK system series.(Move to next page)

## Slide 2
Layout of Keyset
Entering Keyset Admin
Menu Example
Button Usage
Programming Menus
Example
1. Contents
Pre-programmed Database
Station Base Program
CO Line Base Program
System Base Program
Station Group Program
Installation
Notes: PC admin is
PC admin can manage all LDK system series.(Move to next page)

## Slide 3
2. Layout of Keyset
Speaker Hold/Save
Trans / Pgm
Speed
Notes: The following PC Spec. is required to install PC admin.
Please just refer to the requirements.(Move to next page)

## Slide 4
3. Entering Keyset Admin (1/2)
+
+
▷ Press
LCD Display will show
▷ Then Press
LCD Display will show
▷ Enter program number (e.g.100)
Admin 100 started
Trans/Pgm
Trans/Pgm
ADMIN PROGRAM START
BACK DELETE SAVE
To enter Admin Programming
ENTER PGM NUMBER
BACK DELETE SAVE
LOCATION PROGRAM
PRESS FLEX_KEY (1-2)
BACK DELETE SAVE
With default values, station 100 can enter admin program.
Notes: Whilst the keyset is in programming mode
it will only operate as an Admin terminal.
Normal keyset operation is not available.
It will not be able to ring on incoming
calls, and will be busy for internal calls

## Slide 5
Press
Station will go to the idle state.
ON/OFF
=
3. Entering Keyset Admin (2/2)
To exit Admin Programming
STATION 100 (T)
28 AUG 06 02:01 pm
PICKUP CONF REDIAL

## Slide 6
4. Button Usages
Trans/Pgm
Speed
[TRANS/PGM] will move you to the start menu.
[HOLD/SAVE] will store the value.
Hold/Save
Volume
[Volume Up/Dn] is used to scroll the data up and down.
[SPEED] is used to delete current data.
Flexible buttons are used to select menus.
1
Soft menu is used to go back / delete / save.
[BACK] will move you back to the upper step.
Numeric data is entered from keypad.

## Slide 7
5. Program Menu (1/4)
: Needs to be Restart
Notes: If your system gives error tone when flexible button 10 ( LCR Program ) is pressed, then you do not have a MEMU installed.
All UK systems should have a MEMU installed.

## Slide 8
5. Program Menu (2/4)
Notes: If your system gives error tone when flexible button 10 ( LCR Program ) is pressed, then you do not have a MEMU installed.
All UK systems should have a MEMU installed.

## Slide 9
5. Program Menu (3/4)
Notes: If your system gives error tone when flexible button 10 ( LCR Program ) is pressed, then you do not have a MEMU installed.
All UK systems should have a MEMU installed.

## Slide 10
5. Program Menu (4/4)
Notes: If your system gives error tone when flexible button 10 ( LCR Program ) is pressed, then you do not have a MEMU installed.
All UK systems should have a MEMU installed.

## Slide 11
- Press Flex_1 to set Nation Code
To change Nation Code, DIP4 should be set to ON.
- Press Flex_2 to set Site Name
Enter Site Name from Keypad.
6. Example
PRE-PROGRAMMED DATABASE
LOCATION PROGRAM
PRESS FLEX_KEY (1-2)
BACK DELETE SAVE
▷ Location Program ( PGM 100 )
NATION CODE
PROTECTED DATABASE(DIP4)
BACK DELETE SAVE
SITE NAME
HEAD OFFICE
BACK DELETE SAVE
Notes: The flexible buttons available are ;
1. Station Database Initialisation
2. CO Line Database Initialisation
3. ISDN Database Initialisation
4. System Feature Database Initialisation
5. System Timer Database Initialisation
6. Toll Table Database Initialisation
7. Authorisation Code Table Initialisation
8. Flexible Station Number Initialisation
9. Flexible Button Program Initialisation
10. LCR Database Initialisation
11. All Database Initialisation
Press the Button relating to the section of programming required and the press [HOLD/SAVE] to enter.

## Slide 12
ADDITIONAL BOARD ASSIGNMENT
SLOT 06 (F1:ID F2:DEVS)
ID:UNKNOWN DEVS:0
BACK DELETE SAVE
6. Example
2. Enter 2 digits of Slot number you want to program. (e.g. slot 06)
BKSU
EKSU
VMIU, AAFU
VOIB
1
2
5
6
3
4
7
8
9
10
2. CO
3. Others
1. Extension
BOARD ASSIGNMENT
ENTER SLOT NUMBER
BACK DELETE SAVE
1. Enter PGM 101 by pressing [Trans/Pgm] + ‘*’ + ‘#’ + ‘101’ at Admin Keyset
▷ BOARD ASSIGNMENT(PGM101) & LOGICAL SLOT ASSIGN(PGM 103)

## Slide 13
6. Example
3. Press Flex_1 and enter 2 digits Board ID code (e.g. 41 for VOIB)
STA | CODE | COL | CODE | Etc | CODE
SLIB16 SLIB8 HYBRID | 13 14 17 | LCOB3 E1IB8 VOIB | 33 40 41 | VMIU AAFU | 64 65
SLOT 06 (F1:ID F2:DEVS)
ID:UNKNOWN DEVS:0
BACK DELETE SAVE
4. Press Flex_2 and enter device number and press [SAVE]. (e.g. 20 for E1HB8)
SLOT 10 (F1:ID F2:DEVS)
ID:DCOB DEVS:20
BACK DELETE SAVE

## Slide 14
LOGICAL SLOT ASSIGN
COL STA VMIB
BACK DELETE SAVE
6. Example
5. Enter PGM 103 by pressing [Trans/Pgm] + ‘*’ + ‘#’ + ‘103’ at Admin Keyset
05 07 . . . . . . . .
. . . . . . . . . . . .
BACK DELETE SAVE
6. Press Flex_1 for COL logical slot assignment
05 07 06 . . . . . .
. . . . . . . . . . . .
BACK DELETE SAVE
7. Enter new slot order including slot 06 and Press [SAVE]. (e.g. 050706)
8. Restart the system.

## Slide 15
- Enter Station range you want to select (e.g. 100110)
- Press Flex_1 to set Auto Speaker option
- Dial 1/0 and Press [Hold/Save] to save data
- If you exit without save, the data is not changed.
6. Example
STATION BASED PROGRAM
STATION ATT 1
ENTER STA RANGE
BACK DELETE SAVE
▷ Station Attribute 1 ( PGM 111 )
100-110 STATION ATT1
PRESS FLEX_KEY (01-24)
BACK DELETE SAVE
100-110 AUTO SPKR
(1:ON/0:OFF) : ON
BACK DELETE SAVE
Notes: The flexible buttons available are ;
1. Station Database Initialisation
2. CO Line Database Initialisation
3. ISDN Database Initialisation
4. System Feature Database Initialisation
5. System Timer Database Initialisation
6. Toll Table Database Initialisation
7. Authorisation Code Table Initialisation
8. Flexible Station Number Initialisation
9. Flexible Button Program Initialisation
10. LCR Database Initialisation
11. All Database Initialisation
Press the Button relating to the section of programming required and the press [HOLD/SAVE] to enter.

## Slide 16
6. Example
CO LINE BASED PROGRAM
- Enter CO line range you want to select (e.g. 0103)
- Press Flex_1 to set CO Line Group
- Enter desired CO Group number with 2 digits and press [Hold/Save] button.
- If you exit without save, the data is not changed.
CO LINE ATT 1
ENTER COL RANGE
BACK DELETE SAVE
▷ CO Line Attribute 1 ( PGM 141 )
01- 03 CO LINE ATT1
PRESS FLEX_KEY (01- 10)
BACK DELETE SAVE
01- 03 CO LINE GRP
(00 - 25) : 01
BACK DELETE SAVE
Notes: The flexible buttons available are ;
1. Station Database Initialisation
2. CO Line Database Initialisation
3. ISDN Database Initialisation
4. System Feature Database Initialisation
5. System Timer Database Initialisation
6. Toll Table Database Initialisation
7. Authorisation Code Table Initialisation
8. Flexible Station Number Initialisation
9. Flexible Button Program Initialisation
10. LCR Database Initialisation
11. All Database Initialisation
Press the Button relating to the section of programming required and the press [HOLD/SAVE] to enter.

## Slide 17
6. Example
SYSTEM BASED PROGRAM
- Press Flex_4 to set DISA Retry Count.
- Enter desired retry count number with 1 digits and press [Hold/Save] button.
- If you exit without save, the data is not changed.
SYSTEM ATT 1
PRESS FLEX_KEY (01 – 20)
BACK DELETE SAVE
▷ System Attribute 1 ( PGM 161 )
DISA RETRY CNT
(0 - 9) : 3
BACK DELETE SAVE
Notes: The menus available are ;
1. TEI type T
2. Calling Sub-Address T
3. Incoming Zero Insertion T
4. Outgoing Zero Insertion T
5. Outgoing Check Digit T
6. My Area Code T
7. My Nation Code T
8. COLP Table T
9. MSN Table T
10. DID Digit Conversion S
S = sub-menu
T = terminal menu

## Slide 18
6. Example
STATION GROUP PROGRAM
- Enter Station Group number(620).
- Press FLEX_1 to select Station Group type.
- After set station group type, press FLEX_3 to assign member.
- Enter station range.
- If you want to enter stations one by one, enter station number after press Flex key(1~4).
- You can scroll up/dn to see whole of the members if their are more than 4.
STATION GRP ASSIGN
ENTER HUNT NO(620-629)
BACK DELETE SAVE
▷ Station Group Assign ( PGM 190 )
STATION GRP 620
F1:TYPE F2:PKUP F3:MEM
BACK DELETE SAVE
STATION GRP 620
NOT ASSIGNED (0-6)
BACK DELETE SAVE
CIRCULAR GRP 620
. . . . . . . . . . . . . . . .
BACK DELETE SAVE

## Slide 19
7. Practice Exercise
Insert boards and units
Set Nationality
Initialize system as Nation Default
How to Install

## Slide 20
7. Practice Exercise
1) Insert all boards
2) Power on the system (All switches of MPB are set to ‘ON’)
3) Assign Nationality (PGM 100 - BTN 1) (After Assignment, please reset manually)
4) Set the DIP4 of BMBU to ‘OFF’ to preserve the programming data against reset
5) Change the numbering plan if needed (PGM 104 ~ 107)
NATION CODE
66
BACK DELETE SAVE
NUMBERING PLAN(1-8)
1
BACK DELETE SAVE
How to Install
When restart, initial values based on current nation code are set.