## Slide 1
BASIC FEATURES

## Slide 2
Contents
CO Line Access
  How to access CO Line?
  How to get incoming call
Rerouting Features
  Call Forward
  Call Forward to Off-net
  Call Forward to VMIB
  Preset Call Forward
  Direct Call Pick-up
  Group Call Pick-up
Call Handling
  Call Waiting(Camp on)
  Voice Over
  Music On Hold(MOH)
  Analog CO-to-CO Call Timer Extend
  Forced Hands-Free
  Dial by Name
Call Barring Features
  Authorization Code
  Station COS & Walking COS
Other Features
  Conference
  Paging
  Executive & Secretary Transfer
  SMDR
  Attendant Override & Intrusion
Notes: 본문(Description)
(Move to the next)
LDK have many feature. I will explain basic feature one by one as contents.

## Slide 3
User can access the CO line to make an outgoing call with several methods.
Description
How to access CO line? (1/4)
PSTN
4501234
9 4501234
801 4501234
8801 4501234
ipLDK-60 System
Notes: 본문(Description)
(Move to the next)

## Slide 4
 By pressing a flexible button that CO line is programmed.
 Individual CO Line, CO Line Group, Loop(1st CO Group)
 By dialing CO access code. There are three kinds of CO access code.
 Individual CO line access code : 88XX (PGM107-BTN8)
 CO Line Group access code : 8XX(PGM107-BTN11)
 Loop(1st CO Group) access code : 9 or 0(PGM107-BTN12)
※ Each access code can be changed in the system numbering plan.
 How to assign LOOP button in the flexible button at each station?
[TRANS/PGM] + [Flexible BTN] + [TRANS/PGM] + 84 + [HOLD/SAVE]
※ To assign LOOP button,
‘CO PGM’(PGM112-F6) feature of the station should be enabled.
How to access CO line? (2/4)
Operation
Notes: Let’s see how to access CO line in the IP LDK system.
First, we can access CO line by pressing a flexible button that CO line is programmed.
We can program an individual CO line, CO Group CO line and Loop in the flexible button
Second, we can access CO line by dialing CO access code. There are three kinds of CO access code.
1. Individual CO access code (default 88XX)
2. CO Group access code (default 8XX)
3. Loop code (9 or 0)
Each access code can be changed in the system numbering plan.
(Move to the next)

## Slide 5
 Each CO line can be a group
of similar type or accessibility.
; Program to assign CO line group
(PGM141-BTN1)
* The number of CO Groups
(ipLDK-60 : 24EA)
 Accessibility of each station can
be controlled by admin programming.
; Program for accessibility
of CO Group Access Station
(PGM117)
How to access CO line? (3/4)
Program
Group 1
- For international call
CO 1
CO 2
CO 3
Not allow
Group 2
- For national call
CO 4
CO 5
CO 6
Group 3
- E1 line
CO 7
CO 36
.
.
.
.
Station(A)
Notes: Each CO line can be grouping of similar type or accessibility by PGM141/BTN1.
Accessibility of each station can be controlled by admin programming. PGM117
For example station(A) can seize the CO4 to CO6 in CO group2 and CO7 to CO15 in CO Group3.
But Station(A) cannot seize the CO1 to CO3 because Station(A) has no accessibility.
LDK-300 has 72 CO group.
(Move to the next)

## Slide 6
● CO line of accessible CO group can
be selected by round-robin or last
choice.
; Program for CO Line Choice
(PGM160-BTN3)
● CO line of another accessible CO
group can be seized if all CO lines
of group are busy.
; Program for Override 1st CO Group
(PGM161-BTN3)
Round-robin
Last choice
CO 1
CO 2
CO 3
Group 1
CO 4
CO 5
CO 6
Group 2
Override 1st CO group to next CO group
How to access CO line? (4/4)
Program
Notes: CO line of accessible CO group can be selected by round-robin or last choice.
Round robin mean the co line is seized alternately.
Last choice means the last co line is seized all the time.
It can be programmed in the PGM 160-3.
If 1st co group is all busy, and then the next co group will be seized. We call it override 1st CO group.
It can be programmed in the PGM 161-3.
(Move to the next page)

## Slide 7
Description
If there is an incoming call through CO Line which is ring assigned, the pre-assigned destination gets the call.
The destination can be Station, Hunt Group or VMIB announcement.
How to get incoming call (1/3)
 CO Line Ring Assignment : PGM144
VMIB announcement
Station A
Hunt Group
Station B
PSTN
ipLDK-60 System
Program
Notes: If LDK receives Ring from the outside caller, LDK can terminate the call to pre assigned a station or hunt group or VMIB.
We can program the destination in the PGM 144 ring assignment.

## Slide 8
CO line ring assignment at the admin station :
- Assign procedure to each station
( [TRANS/PGM] + * # + [TRANS/PGM] + ‘144’ ) + CO range + Ring type + ‘1’
+ STA range + Delay count + [HOLD/SAVE]
Ring type : F1-Day, F2-Night, F3-Weekend, F4-On-demand
Delay count : 0~9 (about 3 sec/count)
- Assign procedure to hunt group
( [TRANS/PGM] + * # + [TRANS/PGM] + ‘144’ ) + CO range + Ring type + ‘2’
+ Hunt Group No + [HOLD/SAVE]
Ring type : F1-Day, F2-Night, F3-Weekend, F4-On-demand
- Assign procedure to VMIB
( [TRANS/PGM] + * # + [TRANS/PGM] + ‘144’ ) + CO range + Ring type + ‘3’
+ VMIB Greeting Message No.(00:Cancel, 01~70:Assign) + [HOLD/SAVE]
Ring type : F1-Day, F2-Night, F3-Weekend, F4-On-demand
How to get incoming call (2/3)
Notes: This page shows the detail how to program the destination. Station, Hunt group, VMIB.

## Slide 9
ipLDK can assign a separate destination for system mode.
There are 4 kinds of mode : day, night, weekend and on-demand.
 Attendant can change the system mode.
1. Press the [DND/FWD] button.
2. Dial one digit
(1:Day / 2:Night / 3:Weekend / 4:On-demand / 5:Auto Ring Mode)
3. Press the [HOLD/SAVE] button.
※ If ATD is in Auto Ring Mode, Weekly Time Table(PGM233) is applied.
Multiple stations can be assigned as ring assignment destination.
In that case, ipLDK can give a delay to ring to each stations.
The ring can be delayed by 0 to 9 ring cycles.
How to get incoming call (3/3)
Others
Notes: 본문

## Slide 10
VMIB announcement 01
Station 100
Station 101
CO Line Access Practice
Test scenario
[CO Line Assigned & How to CO Seize]
1. Station 101 only access analog CO Line (assume CO 1, 2, 3 is analog)
2. Incoming CO 1 is connected Station 101
3. Incoming CO 2 is connected Station 102
4. Incoming CO 3 is connected VMIB Prompt 1
CO 1
CO 2
CO 3
PSTN
[ How to operate & Program ]
PGM 141 + 01 03 (select analog CO) + Flx1 : CO Group 2
PGM 117 + 101 101 (select station range) + turn off all co group except co group 2
PGM 144 + 01 01 (select CO range) + Flx1 + 1 (select station) + 100 100 (select station range) + 0 (set delay time)
PGM 144 + 02 02 (select CO range) + Flx1 + 1 (select station) + 101 101 (select station range) + 0 (set delay time)
PGM 144 + 02 02 (select CO range) + Flx1 + 3 (select VMIB) + 01 (select system greeting number)

## Slide 11
User can direct the system to re-route call to a station when the user’s station is unconditional / busy / no answer in other station.
Call Forward (1/6)
Unconditional
Busy
No Answer
Busy/No Answer
Follow me
 Call Forward Usage : PGM111-BTN2
Description
Program
Notes: 본문(Description)
We have 본문.
Unconditional
Busy
No Answer
Busy/No Answer
Follow me

## Slide 12
Call Forward - Unconditional
Call is forwarded immediately.
STA (B)
STA (A)
STA (C)
Call Forward (2/6)
Notes: This is an example of unconditional CFWD.

## Slide 13
Call Forward - Busy
In busy state
STA (A)
STA (B)
STA (C)
Call Forward (3/6)
Notes: This is a example of busy CFWD.
When the STA(B) is busy, STA(A) is calling to STA(B).
So the call is routed to STA(C)

## Slide 14
Call Forward - No Answer
Not answered within predefined ‘No Answer’ time
 Call Forward No Answer Timer : PGM181-BTN1
STA (B)
STA (A)
STA (C)
Program
Call Forward (4/6)
Notes: This is a example of no answer CFWD.

## Slide 15
Call Forward - Follow me
Authorization Code : PGM227
(Authorization code should be registered to use Follow-me Call Forward.)
When a user move to another station, a call can be forwarded to the moved station from the original station.
STA (B) is connected with
STA (A) in the seat of STA (C)
STA (A)
STA (B)
STA (C)
STA (A) moved to STA (C)
Program
Call Forward (5/6)
Notes: 본문
Authorization code should be registered to use Follow-me Call Forward.
We can program Authorization code in the PGM 227.

## Slide 16
Operation
Call Forward - Unconditional: Call is forwarded immediately.
(“[MON] + [FWD] + 1 + Sta No/ Group No/ # for VMIB”)
 Call Forward - Busy : When the user’s station is busy.
( “[MON] + [FWD] + 2 + Sta No, Group No, or # for VMIB”)
 Call Forward - No Answer : If not answered within predefined ‘No Answer’ time.
( “[MON] + [FWD] + 3 + Sta No, Group No, or # for VMIB”)
 Call Forward - Busy/No Answer : If not answered or busy.
( “[MON] + [FWD] + 4 + Sta No, Group No, or # for VMIB”)
 Call Forward - Follow me : When a user moved to another station, a call can
be forwarded to the moved station from the original station.
( “[MON] + [FWD] + 0 + Sta No + Auth Code”)
Call Forward (6/6)
Notes: We can program each call forwarding as follow.
Please refer to it when making a practice.

## Slide 17
Station can forward intercom or incoming CO line calls to external party.
Station Off-net Call Forward (1/3)
Unconditional
No Answer
Description
STA (C)
Assign Station Off-net Call Forward
at your station during out of office.
You can get a call with your cellular
phone or pager outside.
Notes: 본문(Description)
There are unconditional and no answer off-net call forwarding.

## Slide 18
1. Assign Call Forward;
Lift handset or press [MON] button.
Unconditional : [FWD] + “5” + Speed Bin(Pre-programmed)
or [FWD] + “8” + CO Button + Destination Number
(: Automatically stored to Last station Speed bin)
No Answer : [FWD] + “6” + Speed Bin(Pre-programmed)
or [FWD] + “9” + CO Button + Destination Number
(: Automatically stored to Last station Speed bin)
Press the [HOLD/SAVE] Button.
Confirmation tone will be heard and on-hook.
[DND/FOR] button is flashing and the following message is displayed on LCD.
2. Assign Speed Dial Number;
To assign(in each station):
[TRANS/PGM] + [SPEED] + Speed bin No. + Phone No. + [HOLD/SAVE] + Name + [HOLD/SAVE]
To assign System Speed Dial(by Attendant)
[TRANS/PGM] + [SPEED] + Speed bin No. + Phone No.+ [HOLD/SAVE]+ Name + [HOLD/SAVE]
FORWARDED TO SPEED XXXX
JAN 01 07 11:40 AM
PICKUP CONF REDIAL
Station Off-net Call Forward (2/3)
Notes: We can program each off-net call forwarding as follow.
Please refer to it when making a practice.
Button 5 and 6 will use pre-programmed Speed Bin
Button 8 and 9 will use station speed bin 099 and it is required to program the station speed bin every when registering CFWD.
We can program speed bin as follows.

## Slide 19
Call Forward Usage : PGM111-BTN2 (ON/OFF)
Off-net Call Forward : PGM111-BTN18(ON/OFF)
Off-net call mode : PGM112-BTN12 (EXT/ALL)
(All:External and Internal, EXT:External Only)
Program
Station Off-net Call Forward (3/3)
Notes: There are programs related to CFWD.

## Slide 20
The attendant can direct the system to re-route incoming CO line calls to a directory number outside the system.
Incoming CO Line Off-net Call Forward (1/3)
Description
CO Line Off-net Call Forward
is set for all incoming CO
line calls in your office.
CO LINE
You can get a call with you cellular phone.
Notes: 본문(Description)

## Slide 21
At attendant
Lift handset or press [MON] button.
[DND/FOR] + “7”
Select CO line(s) to be call forwarded
: Press CO or CO group button in the flexible button
or Dial CO or CO group access code
Speed bin no.
Confirmation tone will be heard and then on-hook.
The designated CO button is flashing.
Operation
CO PGM Usage : PGM112-BTN6
(To program a CO related button to a flexible button)
Program
Incoming CO Line Off-net Call Forward (2/3)
Notes: We can program incoming off-net CFWD at the attendant as follows.

## Slide 22
Features
 It is useful when a station in the system cannot answer a CO line call.
 It is possible to assign some CO lines to be forwarded in the system, so other
CO lines (not assigned) can be answered by available stations.
 It is only available to receive a call, not make a call.
 Call Forward Usage : PGM111-BTN2
 Unsupervised Conference Timer : PGM182-BTN6
Program
Incoming CO Line Off-net Call Forward (3/3)
Notes: 본문(Condition)

## Slide 23
Call Forward to VMIB (1/2)
Station can forward intercom or incoming CO line calls to VMIB.
Description
Call 100
VMIB announce of the STA 100 is heard
Dial ‘#’ during announcement or wait until
the greeting is finished.
Leave voice(VMIB) message to STA 100
STA 105
STA 100
Forward to VMIB
Notes: 본문(Description)
본문(Picture)

## Slide 24
Unconditional : [MON] + [FWD] + 1 + #
Busy : [MON] + [FWD] + 2 + #
No Answer : [MON] + [FWD] + 3 + #
Busy/No Answer : [MON] + [FWD] + 4 + #
※ User Greeting should be recorded in advance to use VMIB Call Forward.
How to record User Greeting in a DKTU;
[TRANS/PGM] + 6 + 1 + # + Recording + [HOLD/SAVE]
Call Forward to VMIB (2/2)
Operation
Program
 Call Forward Usage : PGM111-BTN2
 VMIB Access : PGM113-BTN2
Notes: We can forward a call to VMIB in case of the following cases;
Unconditional, busy, no answer, busy/no answer.
※ User Greeting should be recorded in advance to use VMIB CFWD.
We can record the user greeting as follow.
How to record User Greeting : [TRANS/PGM]+6+1+#+Recording+[HOLD/SAVE]
Also these programs are required before using VMIB service.

## Slide 25
Station 101
Station 102
Forward to Station 103
Call Forward Practice
Test scenario
[make Call forward with Station 102]
1. Make Unconditional Forward to Station 103.
2. Make Busy / No-Answer Forward to Station 103.
3. Make Unconditional Off-net Call Forward (Forward Type 8, with CO line 1) .
4. Make Busy Forward to VMIB.
Station 103
PSTN
Station 200
[ How to operate & Program ]
[MON] + [DND/FWD] + 1 + 103
[MON] + [DND/FWD] + 3 + 103
[MON] + [DND/FWD] + 1 (select CO number) + external station number
[MON] + [DND/FWD] + 2 + # (Select own VMIB)

## Slide 26
Incoming CO lines can be forwarded to an assigned station or hunt group
if the call is not answered within predefined time, Preset Forward Timer.
Preset Call Forward (1/2)
CO LINE
A
B
C
D
E
Call STA (A)
To make Preset Call Forward to STA (A)(B)(C)(D)(E)
Description
Notes: 본문(Description)
If extension A does not answer from the CO call, the call will be forwarded to B, C, D, E in order.

## Slide 27
Condition
 It is available for incoming CO lines (not for DID).
 It can be assigned regardless of the number of station. But, looping of Preset
Call Forward is not available.
Preset Call Forward : PGM121
Preset Call Forward Timer : PGM181-BTN12
Program
Preset Call Forward (2/2)
Notes: 본문(condition)

## Slide 28
A station can pick up a call ringing other station by pressing the pick up code (7)
and intercom number of ringing station.
Direct Call Pick-up
7 + dial the
intercom no.
Pick up the call of STA (A) in STA (B)
Description
STA(A)
STA(B)
Notes: Let’s see direct call pick up.
본문(description)

## Slide 29
A station in the same pick-up group can pick-up a call ringing the other station
in the group. Intercom calls, incoming CO calla, recalling CO calls and transferred
CO calls can be answered by a station instead of the ringing station if they are the
member of the same pick-up group.(PGM 190)
Group Call Pick-up (1/2)
Description
Pick-up Group
A
D
E
Dial Pick-up code (566).
Call STA (E)
CO LINE
Program
Group Call Pick-up Code : PGM107-F2
Notes: 본문(Description)

## Slide 30
To assign Call Pick-up Group,
1) [TRANS/PGM] + * + # + [TRANS/PGM] + 190
2) Dial the group number to be assigned.
3) [BTN 1] + ‘6’ + [HOLD/SAVE]
4) [BTN 3] + station range + [HOLD/SAVE]
or [BTN 3] + Flexible BTN + station number + [HOLD/SAVE]
To assign Auto Pick-up Group,
1) [TRANS/PGM] + * + # + [TRANS/PGM] + 191
2) Dial the group number to be assigned.
3) [BTN 1] + ‘1’ + [HOLD/SAVE]
Group Call Pick-up (2/2)
Program
Notes: We can program group call pick up in the PGM 190.

## Slide 31
Station 101
Call Pickup Practice
Test scenario
[make Call pickup]
1. Test direct call pickup.
2. Make Pickup Group 620 with station 101 and 102
Station 102
620 Group
[ How to operate & Program ]
PGM 190 + 620 (select group number) + Flx1 + 6 (select pickup group)
PGM 190 + 620 (select group number) + Flx3 + 101 102 (select station range)
PGM 191 + 620 (select group number) + Flx1 + yes

## Slide 32
When a user calls a busy station, busy tone is heard and the user can give a signal to the busy station. The busy station is notified of the call waiting by a camp-on tone and flashing LED of the [HOLD/SAVE] button.
The busy station can alternate conversation between the two parties by pressing
[HOLD/SAVE] button.
[In SLT : Hook Flash + SLT Hold Code “560”]
Call Waiting(Camp on)
Call 100
Busy Tone is heard
Dial ‘*’
Hears MOH
STA 105
STA 100
STA 102
Short Beep Tone is heard
Description
Notes: 본문(Description)

## Slide 33
This feature provides voice announcements for a busy station without
interrupting the existing conversation. The caller can talk to the busy station over
the existing conversation so that only the busy station hear both incoming parties.
The busy station can alternate conversation between the two parties by pressing
[HOLD/SAVE] button.
.
Voice Over for called extension : PGM113-BTN6
Caller Voice Over : PGM111-BTN22(From V3.6)
Voice Over
Call 100
Busy Tone is heard
Dial ‘*’
Can talk to STA 100
STA 105
Voice of STA 105 is heard
STA 102
STA 100
Description
Program
Notes: 본문(Description)

## Slide 34
When a call is placed in holding state system can provide music instead of tone.
Music On Hold(MOH) (1/3)
Network
When user (A) push the HOLD button,
caller hear the internal music.
Caller
Station 100
Station 101
USER (A)
USER (B)
1. Internal MOH
Description
Notes: 본문(Description)
LDK provides internal MOH and external MOH ports.
In this picture, the caller hears internal MOH.

## Slide 35
2. External MOH
When USER A presses the HOLD button,
caller hear the External music which is connected to external MOH port or SLT port
☞ Note : MOHU is needed(one MOHU supports 2 MOH channels)
Network
Caller
Music On Hold(MOH) (2/3)
Station 100
Station 101
USER (A)
USER (B)
Notes: In this picture, the caller hears external MOH from the external device connected to LDK system

## Slide 36
 It is operated automatically when programmed.
User select the Music source channel as follows;
- Channel 0 : None
- Channel 1 : Internal Music Channel
- Channel 2 : External Music Channel
- Channel 3 : Reserved
- Channel 4 ~ 8 : SLT MOH Channel (1 – 5)
- Channel 9 : Hold Tone
 Select the Music Source Channel : PGM142-BTN6 / PGM171-BTN2
Assign the SLT port with MOH channel : PGM171-BTN4
Operation
Music On Hold(MOH) (3/3)
Program
Notes: 본문(operation)

## Slide 37
The user can extend the “Unsupervised Conference Timer” during a CO-to-CO
connection by dialing a code (##)
Extension time is in multiples of the Supervised Conference Timer as determined by user.
Analogue CO-to-CO Call Timer Extend
PGM 160 – BTN 18 : Unsupervised Conference Timer Extend(Enable/Disable)
PGM 109 – BTN 6 : Unsupervised Conference Timer Code(##)
PGM 182 – BTN 6 : Unsupervised Conference Timer
Enter the command of DISA CO-to-CO Call Timer Extension Code – by CO Caller or Called User:
1. When the analog CO-to-CO lines are connected
2. Either the caller or called user dials the unsupervised conference timer extension code ‘##’
and the extension time multiple data 1 digit (1 ~ 9).
3. ipLDK re-assigns the unsupervised conference timer to multiple of entered digit.
4. Before 15 seconds of the unsupervised conference timer expired,
the warning tone is provided to indicate the disconnection.
For example,
The unsupervised conference timer is set to 10 minutes and the entered digit is 3,
and then the timer is extended to 30 minutes.
Description
Operation
Program

## Slide 38
A DKTU caller can temporarily change the answer mode of the called DKTU from “Tone” to “Hands Free”, by dialing a code (#).
If a called DKTU is changed to hands free mode, the connection tone is provided and
the voice path is opened.
The caller DKTU must have this feature enabled in Admin Programming
Forced Hands-Free
PGM 111 – BTN 19 : Forced Hands Free Mode(Enable/Disable)
To activate forced hands free mode
1. Call to DKT which is a tone mode.
2. When user hears a ring back tone, dial Forced hands free Code ( ‘#’ )
3. Called party DKT stops ringing and speaker/microphone are activated.
Description
Operation
Program

## Slide 39
User of DKTU with LCD can dial by registered name of ICM and Station & System Speed dial.
 Press [Speed] + [Speed]
DIGITAL
DIAL BY NAME
ICM:1 U_SPD:2 S_SPD:3
DIGITAL
1: CH KIM ( 131 )
2: KH LEE ( 166)
 Dial the desired directory number.
DIGITAL
1: WP KAL ( 167 )
2: YH LEE ( 118 )
 Press Volume or
Enter alphanumeric data with 2 digits.
DIGITAL
1: CH KIM ( 131 )
2: KH LEE ( 166)
 Dial 1 or 2 which is desired name,
and Press [HOLD/SAVE]
Dial by Name
Description
Operation
Notes: 본문(Description)

## Slide 40
Call Handling Practice
Test scenario
[make Voice Over situation]
1. Station 100 & Station 101 is connected.
2. Station 102 make a call to Station 101 and hear busy tone, then Station 102 try to Camp-On
3. Station 101 can move from existing call to new call but existing call is not released.
[make Forced Hands Free]
1. Station 101 make a call to Station 102 but Station 102 is No-Answer.
2. Station 101 want to make a forced hands free mode.
[Change MOH]
1. Change default Internal MOH Romance to Walts & test.
[ How to operate & Program ]
PGM 113 + 101 101 (select station range) + Flx 6 + Enable
PGM 111 + 101 101 (select station range) + Flx 19 + On
PGM 171 + Flx 8 + 05 (Walts)
Station 100
Station 101
Station 102
1. Existing Call
2. New Call
3. Can move from E-call to N-call

## Slide 41
The authorization code(Password) is used for giving limitation to some cases
- CO Group Account / DISA Account code
- COS Down / COS Restore
- Walking COS
- Loop LCR Account
Authorization Code (Password) (1/3)
Authorization Code Table : PGM227
DISA Account Code : PGM141-BTN3
CO Group Account Code : PGM141-BTN9
Loop LCR Account Code : PGM111-BTN16
Description
Program
Notes: 본문(description)
We can apply the authorization to the following features.
CO Group Account / DISA Account code
COS Down / COS Restore
Walking COS
Loop LCR ACNT

## Slide 42
To register the authorization code in a station.
[TRANS/PGM] + 3 1 + authorization code + [HOLD/SAVE]
To change the authorization code in a station,
[TRANS/PGM] + 3 2 + current authorization code + ‘#’
+ new authorization code + [HOLD/SAVE]
COS Down : TRANS/PGM + 21
1. Authorization Code should be assigned in advance.
2. [MUTE] button is flashing.
COS Restore : TRANS/PGM + 22 + Authorization Code
To access a CO line when authorization codes are required,
1. Attempt a CO line access, and DND warning tone is heard.
2. Enter the authorization code and ‘#’ (end mark of authorization code).
3. If valid, the CO line is connected and if not valid, you will hear error tone.
Operation
Authorization Code (Password) (2/3)
Notes: 본문(operation)

## Slide 43
Condition
The authorization code(Password) is used for giving limitation to some cases
To limit access to specified CO lines by stations and DISA users
(DISA Account/CO Group Account)
To put station’s class of service to COS 7 for preventing unauthorized
toll dialing (COS Down/COS Restore)
To override toll restriction and make a toll call from toll restricted phone
(Walking COS)
If Loop LCR ACNT is set about a station, the authorization code is required.
The total number of authorization codes in system is 200.
An authorization code can be used for SMDR, a DISA account code.
An authorization code is assigned from 3 digits to 11 digits flexibly.
Or, 5 digits fixed codes system can be used. (PGM 161 – F21).
An authorization code can not be duplicated.
Authorization Code (Password) (3/3)
Notes: 본문(condition)
When using flexible length authorization code system, press # after dial auth code to notify last digit.

## Slide 44
Station COS (1/2)
Description
Each station and CO line can be assigned to have a different class to allow or deny call service.
* Note) 1 : Canned Restriction 1,
2 : Canned Restriction 2
Notes: 본문(Description)
LDK system has 9 classes for station and 5 classes for CO line.
And there are 4 allow and deny tables and 2 Canned toll tables.
Each allow/deny table has 30 entries and 20 entries for the Canned toll tables.
For example, in case of a station has COS2.
If this station seizes CO COS1, it is restricted by allow/deny table A.
If this station seizes CO COS3, it is restricted by allow/deny table B.
If this station seizes CO COS4, it is restricted by the Canned Toll allow/deny table.
The Canned Toll allow/deny table will be explained next page.
And COS7 station can only use intercom call. CO call is not available.

## Slide 45
Station COS (2/2)
 Station COS : PGM116
CO Line COS : PGM141-Btn2
CO-to-CO COS : PGM166
Toll Exception Table : PGM224
Canned Toll Table(Allow/Deny) : PGM225
Emergency Code Table : PGM226
Program
STA COS 6  Canned Toll Table : Long distance call is not allowed.
(The dialed digits : 8 digits maximum)
STA COS 5  Canned Toll Table : Long distance call is not allowed.
(The dialed digits : more than 8 digits)
STA COS 7 : Intercom Only, but Paging and Emergency Call are available.
The attributes of CO-to-CO COS are the same as the STA COS.
Condition
Canned Restriction 1
Canned Restriction 2
Notes: 본문(Description)
If COS6 station seizes CO COS4, it is restricted by the Canned Toll allow/deny table and maximum 7 dialed digits are available.
If COS5 station seizes CO COS4, it is restricted by the Canned Toll allow/deny table and more than 7 dialed digits are available.
The following programs are related to COS.

## Slide 46
It allows to temporarily override toll restriction and makes a CO call from
toll restricted phone.
Walking COS (1/2)
The fee for the call with Walking COS will be charged to the station which is accorded to the
used password, not actual using station.
STA COS 1
STA COS 6
Description
Notes: 본문(Description)

## Slide 47
 It is available for keyset and SLT.
 For SLT: “563”(program code) + “23”
 To program walking COS button at Flex. BTN:
[TRANS/PGM] + [Flex. BTN] + [TRANS/PGM] + “23”+ [HOLD/SAVE]
 Authorization Code : PGM227
Walking COS (2/2)
1. Press the [TRANS/PGM] button.
2. Dial 2 3.
3. Confirmation tone will be heard and enter the authorization code.
4. If the authorization code is matched, intercom dial tone will be heard.
(At this time, the used extension COS is changed to the station’s COS temporarily.)
5. You can place a CO line call only one time.
Program
Operation
Notes: We can activate this feature like this.
본문(Operation & Program)
Authorization code should be registered to use walking COS.
We can program Authorization code in the PGM 227.

## Slide 48
Authorization Code Practice
Test scenario
[make Co Group account]
1. Make authorization Code of Station 101
2. When CO line 3 is CO Group 3, Make account of CO group 3 is enable
& test outgoing call with station 101.
[ How to operate & Program ]
PGM 227 + 002 (select Port of Station 101) + Flx1 + 111111# (press Autho Code of station 101)
PGM 141 + 03 03 (select co range) + Flx1 + 03 (select co group of co line 3)
PGM 141 + 03 03 (select co range) + Flx9 + On
Station 101
PSTN
CO Group 3 : CO line 3

## Slide 49
A station user(Supervisor) can make a call with intercom stations and CO Lines. Supervisor invite station user or CO Line user one by one with [CONF] button. Connected users can speak and hear with each other at the same time.
Conference (1/3)
CO Line 2
[CONF] + CALL CO LINE 2
[CONF] + [CONF]
STA (A)
CO Line 1
DURING CONVERSATION
Description
In SLT : Hook Flash + Hook Flash within 2 seconds to establish a conference.
Notes: 본문(Description)

## Slide 50
Condition
To establish an Add-on Conference,
1. Press the [CONF] button and make a call to internal party.
2. When answered, press the [CONF] button.
3. When all parties have been called, press the [CONF] button again.
To make a Multi-line Conference,
1. Press the [CONF] button and place a call to an external party.
2. When answered, press the [CONF] button.
3. When all parties have been called, press the [CONF] button again.
To make Unsupervised Conference,
1. During a conference, press the [CONF] button in supervisor and go to ON HOOK.
2. The conference is not disconnected and the [CONF] button LED of supervisor is flashing.
To re-enter the conference, go to OFF HOOK and press [CONF] button in supervisor.
To release the conference forcibly, press [CONF] button without OFF HOOK.
Conference (2/3)
Notes: 본문(Condition)

## Slide 51
Condition
 Max. 15 users can enter a conference including supervisor.
 In unsupervised conference, it is restricted by Unsupervised Conference Timer
if there is no internal station in the conference.
 The supervisor may exit the conference though the conference is still connected.
 Unsupervised Conference Timer : PGM182-BTM6
Program
Conference (3/3)
Notes: 본문(Condition)

## Slide 52
A station, which is allowed to access page facilities, can connect and transmit
voice announcements to any or all the systems external/internal page zones.
Paging (1/5)
Description
Notes: 본문(Description)

## Slide 53
 Page zone can be assigned to control internal page in the system.
 The paging codes are as follows;
 Page Access : PGM111-BTN 8
Internal Page Zone Access : PGM118
Conference Page Zone Access : PGM119
Page Warning Tone : PGM161-BTN4
 Page Timeout Timer : PGM181-BTN10
501-505
Int. Zone
Ext. Zone
Internal All
All Call
Meet-me
506-510
545
543
549
544
Conf. Zone
 External Zone Paging (545: BKSU 1)
 Meet-me for Paging (In SLT:544, In DKTU:HOLD/SAVE Button)
Features
Program
Paging (2/5)
Notes: 본문(Feature)

## Slide 54
The pre-recorded message with VMIB can be paged.
 Press [TRANS/PGM] + “65” to record page message at a station
having access privilege of VMIB.
 Press [TRANS/PGM] + “67” to delete the recorded message.
 Dial paging code then the recorded message will be played.
 VMIB Access Privilege : PGM113-BTN 2
Paging with VMIB (3/5)
Description
Operation
Program
Notes: We can also page a VMIB announcement instead of a caller
And we can record the paging VMIB announcement as follows.

## Slide 55
In the paging conference group, a station can join the page during another station is being paged.
Paging Conference Group (4/5)
The conversation
will be heard to
other stations in the
group with paging.
Description
Notes: 본문(description)
The conversation will be heard to other stations in the group with paging

## Slide 56
 The second originator should have [CONF] button to join the page.
 It is possible for any paged station user to be the second originator by off-hook
and pressing the [CONF] button. At that time, the previous second originator
will go to idle state, and the new second originator can make a page with the
first originator.
 In SLT : Hook Flash + SLT Conference Page Join Code (58)
 In DKTU : Lift the handset(Off Hook) + [CONF] button
 Conference Page Zone : PGM119
 Page Access : PGM111-BTN2
Page Warning Tone : PGM161-BTN4
SLT Conference Page Join Code : PGM109-BTN5
Paging Conference Group (5/5)
Operation
Program
Notes: 본문(operation)

## Slide 57
Stations can be assigned as Executive and Secretary pairs. ICM or CO Call to Executive station can be routed automatically to the paired secretary.
CO / ICM
Calls Exec STA 110
Executive STA
110
Secretary STA
111
Executive & Secretary Transfer (1/3)
Description
Notes: 본문(Description)

## Slide 58
1. When the Executive presses the [DND] button, all calls are routed
to a Secretary.
2. If ‘CO Call To SEC’ feature is set to ON, CO incoming call is automatically
forwarded to the Secretary .
3. If ‘CO Call To SEC’ feature is set to ON and ‘Call EXEC If SEC DND’ feature
is set to ON and the secretary is in DND state, the incoming call is not forwarded
to Secretary but to Executive.
Executive/Secretary Pair : PGM229
CO Call To SEC : PGM229-BTN2
Call EXEC If SEC DND : PGM229-BTN3
EXEC grade : PGM229-BTN4 (Only for Korea, India)
Operation
Program
Executive & Secretary Transfer (2/3)
Notes: 본문(Description)

## Slide 59
One Executive can have more than
two Secretary.
 Looping is not allowed
in Executive and Secretary pair.
Executive 120
Executive 121
Secretary 120
Pair #1
Pair #2
 One station can be assigned more
than two Executive as Secretary.
Secretary #1
Executive & Secretary Transfer (3/3)
Secretary 121
Executive #1
Executive #2
Secretary
Secretary #2
Executive
Notes: 본문(Picture)

## Slide 60
The ipLDK System SMDR(station message detail recording) provides details information about both incoming calls and outgoing calls.
The number of SMDR per systems
 ipLDK-60 : 2000
SMDR (station message detail recording)
Description
Attendant
RS-232C
Or
Ethernet
Notes: 본문(Description)

## Slide 61
SMDR - Overall Format
NO STA CO TIME START DIALED ACT CNT COST ACCOUNT CODE
NNNN AAAA BB HH:MM:SS YY/MM/DD HH:MM TDD…D GG KKKKK CCCCCCCCCC VVVVVVVVVVVV
NO : 4 digits Sequential number(Range 0000~9999)
STA : 4 digits Station number
CO : 2 digits CO line number(Range 01~36)
TIME : 8 digits Call duration field(HH:MM:SS)
START : 14 digits Call start time(YY/MM/DD HH:MM)
T : 1 digit Call type indicator(I=incoming, O=outgoing, T=Transferred call)
DIALED : 18 digits Dialed telephone number field
ACT GRP. : 2 digits Account group number field
CNT : 5 digits Metering count field
COST : 10 digits Call cost field
ACNT CODE : 11 digits authorization code field
 SDMR Account Group : PGM 124
 Select the Metering type : PGM 142-BTN 3
SMDR Attribute : PGM 177
Print Serial Port Selection : PGM 175 (Offline SMDR, Online SMDR)
Select the AOC type : PGM 200-BTN 1
Format
Program
Notes: SMDR information includes station number, outgoing CO Line,
time, date, duration of call, call type, dialed number and so on.
Authorization codes may also be entered and recorded.
If you want to use a billing server, the billing software should be
developed according to our SMDR format.

## Slide 62
 SMDR Start Timer : PGM177-BTN12
Analog Line without Metering signal
Seize CO
Dialing
Last Digit
SMDR Time
Call Duration
On-hook
Analog Line with Metering signal (SPR)
Seize CO
Dialing
Last Digit
Detect 1st metering
Call Duration
On-hook
SMDR - Call Duration Time 1
Program
Notes: In the analog line, the call duration can be defined as follows.
In a case there is no metering signal, the call charging starts after the last dialed digit
In case there is a metering signal such as Polarity reverse or metering tone,
the call charging is defined according to the signal.

## Slide 63
 AOC type : PGM200-BTN1
ISDN Line without AOC information
 From receiving the CONNECT message to end of the call
ISDN Line with AOC information
Analyze the charging information in Facility Message according to
the ETSI specification
 Support AOC-S, AOC-D, AOC-E
SMDR - Call Duration Time 2
Program
Notes: In the ISDN line, AOC information is provided from ISDN network.
There are AOC-S, AOC-D and AOC-E in the AOC information.

## Slide 64
Station can be assigned as member of call account group on SMDR
The number of Account Group per system
ipLDK-60 : 23
 If programmed, Account Group is displayed in the SMDR automatically
 A station belongs to only one call account group
 All stations are not assigned as member of any call Account Group by default.
 SMDR Account Group : PGM124
SMDR - Account Group
Description
Operation
Program
Notes: 본문(Description)
본문(Operation)

## Slide 65
While on an outside call, users can enter a series of digits that will be included in the SMDR.
The series of digits, ‘Account Code’, can be used to allocate cost or time for the call.
 Account Code should be entered during a conversion
 In a Keyset  In a SLT
① Press {Account Code} flexible button ① Off Hook and intercom dial tone heard
② Dial the Account Code(Max. 12digits) ② Dial feature code 550
③ Press {Account Code} flexible button ③ Dial the Account Code(Max. 12digits)
④ Hook flash
 In a Keyset, to access the account code feature, {Account Code} flexible button
should be assigned.
[TRANS/PGM] + Flexible button + [TRANS/PGM] + 8 0 + [HOLD/SAVE]
SMDR - Account Code
Description
Operation
Program
Notes: 본문(Description)
본문(Operation)

## Slide 66
Attendant print and delete the SMDR.
 [PGM] + 0111 : Print SMDR(Station Base)
 [PGM] + 0112 : Delete SMDR(Station Base)
 [PGM] + 0113 : Print SMDR(Account Group Base)
 [PGM] + 0114 : Delete SMDR(Account Group Base)
 [PGM] + 0115 : Display call charge on LCD (Station Base)
 [PGM] + 0116 : Aborting SMDR Printing
 Numbering plan : PGM106-BTN10
 SMDR Attribute : PGM177
SMDR - Print By Attendant
Description
Operation
Program
Notes: Attendant print and delete the SMDR based on station or account group.

## Slide 67
OVERRIDE : Only ATTD can send a ring signal to a station which is in DND mode.
INTRUSION : ATTD or Station can make a conversation
even a station or CO line is busy.
ATTD Override
Dial “120”
Receive DND tone
Attendant
DND Station 120
Dial * or Intrusion BTN
ICM ring to STA 120
 How to assign Intrusion button
[TRANS/PGM] + Flexible BTN + [TRANS/PGM] + 86 + [HOLD/SAVE]
Attendant Override & Intrusion (1/2)
Description
Notes: 본문(Description)
본문(picture)
We can assign intrusion button in the flexible button like this.

## Slide 68
ATD/Station Intrusion - CO Line or STA
Notice : AUTO PRIVACY(PGM161-BTN5) should be disabled and
Station 100 should have the OVERRIDE PRIVILEGE(PGM113-BTN 4).
Station 100
How to use 1
Press BTN for CO 1 which is busy.
How to use 2
1) Call STA 120 which is busy.
2) Press Intrusion BTN during hearing busy tone.
Station 120
CO 1 or STA
● Provide warning tone or Not : PGM161-BTN 6
Attendant Override & Intrusion (2/2)
Notes: There are two ways to intrude the conversation.
After hearing the busy tone, Press BTN for CO 1 which is busy.
After hearing the busy tone, Press the intrusion button.
AUTO PRIVACY (PGM 161/BTN5) should be disabled and
The caller station 100 should have the OVERRIDE PRIVILEGE (PGM 113/BTN 4).