## Slide 1
PSTN Caller ID

## Slide 2
ipLDK-60 supports FSK Caller ID for CO and SLT
ipLDK-60 supports DTMF Caller ID for CO and SLT
Related Specifications
- FSK Caller ID : ETSI EN 300 659-1 (Only Type 1 Supported)
- DTMF Caller ID : TDK-TS 900 216(Denmark),
TELEBRAS 220-250-713(Brazil)
General

## Slide 3
SLT Caller ID Display
- ipLDK-60 system generates FSK signal or DTMF tone to make CLI display on SLTs
- Only Type 1 Supported (OnHook Data Transmission)
Program
Description
 Station ID Assign : PGM 110-BTN1 (12: SLT-CID(FSK), 13:SLT-CID(DTMF))

## Slide 4
- ipLDK-60 system can receive Caller ID information from outside CO lines.
- Detected CLI is displayed on the stations assigned in PGM144.
LCO Caller ID Display
Program
Description
 CID MODE SELECT : PGM 147-BTN1
 CID NAME DISPLAY : PGM 147-BTN2
 CLIP DISPLAY : PGM 114-BTN1

## Slide 5
SMS Service

## Slide 6
ipLDK-60 supports ETSI SMS protocol 1
Max. 4 channels are available for SMS in ipLDK-60
ipLDK-60 delivers SMS messages to SLT, DKTU, IP Phone, ez-Phone, ez-Attendant, Phontage
SMS messages received from PSTN are volatile
(If system is reset, SMS messages are erased)
General

## Slide 7
Terminal | RX | TX | Remark
SMS SLT | O | O | Transparent TX (only external TX)
DKTU, IP phone | O | X | Only DKTU character set
ez-Phone ez-Attendant Phontage | O | O | Internal and external TX
ipLDK-60 SMS service table

## Slide 8
SMS SLT
How to submit Short Message to SM-SC
PSTN
PC Applications
  In case of SMS SLT,
  1. Connect an SMS SLT to ipLDK-60 and enter the SM-SC number
  2. program PGM 291-BTN1, PGM 292-BTN3
  3. Edit a short message then send

## Slide 9
In case of ez-Phone,

## Slide 10
1. Run ez-phone application and log on ipLDK-60 system.
2. Select [Send SMS to PSTN] menu
3. Select [sending] tab, and fill each field
4. Press [send] button
Program
 SMS CENTER NUMBER : PGM 291-BTN1
 SMS OUTGOING CO : PGM 292-BTN3

## Slide 11
How to receive a Short Message from SM-SC
Description
  There are 4 types of terminal which can receive a short message
   DKTU, IP Phone : ipLDK-60 saves short messages for DKTU but it is volatile. that is, if system is reset, these short messages are erased.
   SMS SLT : ipLDK-60 delivers short messages received from SM-SC to an SMS SLT. In other words, ipLDK-60 system works as an SM-SC. After delivery, the short messages are deleted
   PC Applications : ipLDK-60 sends short messages received from SM-SC to PC applications(ez-Phone, ez-Attendant, Phontage). After sending, the short messages are deleted
Program
 PGM 147-BTN1 : CID MODE SELECT(FSK or DTMF)
 PGM 291-BTN2 : SMS CENTER CLI
 PGM 292-BTN1 : SMS RECEIVE STA

## Slide 12
Conditions
  Number of SMS messages : 100
  Number of SMS channels : 4