## Slide 1
Introduction to ETSI ES 201 912

## Slide 2
System Overview
SM-TE : Short Message Terminal Equipment
SM-SC : Short Message Service Centre
SM-TE
PSTN/ISDN
Gateway
SM-SC
Core
LAN connection or other
PSTN or ISDN
ISDN, SS7 or other
providing
Calling Line
Identity
information
providing
Calling Line
Identity
information
SM-SC

## Slide 3
SMS Protocol Stack : Consists of 3 layers
1. Transfer Layer : ETSI TS 100 901 (GSM 03.40), ETSI TS 100 942(GSM 04.11)
2. Data Link Layer : ETSI ES 201 912
3. Physical Layer : EN 300 659-2(FSK TX), ETS EN 300 778-2(FSK RX)
2. SMS PROTOCOL ARCHITECTURE
SM-TE
SM-SC
Physical Layer
Data Link Layer
Transfer Layer
Physical Layer
Data Link Layer
Transfer Layer
PSTN/ISDN
FSK signaling (voice band)

## Slide 4
Timing diagram for a SM-TE originated call
(SM submission :SM transfer from SM-TE to SM-SC)
Physical Layer :
- Bi-directional voice band signalling
- Half Duplex
- 1200baud FSK modulation
2. SMS PROTOCOL ARCHITECTURE (PHYSICAL LAYER)
First
FSK Frame
Second
FSK Frame
T10min
T11min
DLL-SMS-EST(…)
(generated by SM-TE)
DLL-SMS-DATA(…)
(generated by SM-SC)
T10min = n x 100 ms; n = 1..256
T11min = 100 ms (echo-suppressors or echo-cancellers)

## Slide 5
2. SMS PROTOCOL ARCHITECTURE (DATA LINK LAYER)
Mark signal :
- consists of a block of 80 mark bits  25 mark bits
- to synchronize the FSK receiver of the receiving entity.
2. Message Type (1 octet) :
- contains a binary encoded value to identify the message
- Most significant bit is used as extension bit
Mark
Signal
Message
Type
Message
Length
Payload (Transfer Layer Message)
Check-
sum
Data Link Layer Message structure
DATA LINK LAYER :
- SM-DLL provides a service to the Short Message Transfer Layer (SM-TL).
- Responsible for bit error detection, for prepending the Mark signal
- Controls the response time of peer entity

## Slide 6
Message Type | HEX | BIN | Description
DLL_SMS_DATA | 91/11h | X0010001b | Carries SM data
DLL_SMS_ERROR | 92/12h | X0010010b | Indicates that a DLL error has occurred. See Error Handling.
DLL_SMS_EST | 93/13h | X0010011b | Indicates that the DLL connection has been established.
DLL_SMS_REL | 94/14h | X0010100b | Indicates the release of the DLL connection.
DLL_SMS_ACK | 95/15h | X0010101b | Carries a positive SM acknowledgement.
DLL_SMS_NACK | 96/16h | X0010110b | Carries a negative SM acknowledgement.
Extension bit
“0” : Payload of Transfer
Layer Segmented
“1” : Non-segmentation
2. SMS PROTOCOL ARCHITECTURE (DATA LINK LAYER)
3. Message Length (1 octet) :
- the binary encoded number of octets (excluding the message type, message length and checksum octets)
- The maximum message length is 176 octets.
4. Checksum octet (1 octet) :
the two's complement of the modulo 256 sum of all the octets in the message
starting from the message type octet up to the end of the message (excluding the checksum itself).

## Slide 7
ERROR HANDLING
1. Error case : a wrong checksum, an unknown message type etc.
2. Message type : DLL_SMS_ERROR
3. The Data Link Layer of the sending entity has to repeat the last message.
If a message is confirmed negative for two times,
the connection shall be released by both entities.
2. SMS PROTOCOL ARCHITECTURE (DATA LINK LAYER)
Error Code(binary) | Description
0000 0001 b | Wrong checksum
0000 0010 b | Wrong message length
0000 0011 b | Unknown message type
0000 0100 b | Extension mechanism not supported
1111 1111 b | Unspecified error cause

## Slide 8
TRANSFER LAYER :
- SM-TL provides a service to the Short Message Application Layer (SM-AL)
- ETSI document TS 100 901 (GSM 03.40)
- The maximum message length of SM-TL is 176 octets
2. SMS PROTOCOL ARCHITECTURE (TRANSFER LAYER)
PDU Type of SM-TL
1. SMS-DELIVER : a SM(short message) from SC(service centre) to the MS(mobile station)
2. SMS-DELIVER-REPORT : a failure cause(if necessary), ACK or NACK to an SMS-DELIVER
3. SMS-SUBMIT : conveying a SM from MS to the SC
4. SMS-SUBMIT-REPORT : a failure cause(if necessary), ACK or NACK to an SMS-SUBMIT
5. SMS-STATUS-REPORT : conveying a status report from SC to the MS
6. SMS-COMMAND : conveying a command from the MS to the SC