## Slide 1
VMIU FEATURES

## Slide 2
VMIU General
System VMIU Announcement
Voice Mail Service
VMIU Capacity
Feature – Message Transfer
Feature – MSG Add, Rewind
Feature – Remote Control
How to get incoming call
DISA
CCR
Practice – DISA & VMIU
Practice – CCR & VMIU
Contents
Notes: I will start explaining the VMIU, DISA and CCR

## Slide 3
Features
Description
If VMIU board is installed on a system, voice announcement can be provided
to each station or CO line.
 Provides System Prompts/Greetings & User Greetings.
Provides Message Store and Retrieve Individual Message
Provides Message Transfer with or without appending additional comment
Provides Message Rewind during listening to the message
Provides Message Store with CLI and Call-Back
Provides VMIU Remote Control
Provides Voice Announcement to DID, DISA and Hunt Group
VMIU General
Notes: In this time, I will explain VMIU Service.
VMIU is voice mail service unit.

## Slide 4
System Prompt & System Greeting
System VMIU Announcement
Notes: This is the system prompt and system greeting list provided in the VMIU.
There are 100 message.
1 to 70 are used for system greeting and 71 to 100 are used for system prompt.
The system greetings and system prompt are used to play voice announcement for
DID, DISA and Hunt Group.
ATD can record them.(VMIB ACCESS should be ENABLEed, PGM113-BTN2)
71 to 100 are already recorded but ATD can change them according to the customer site.

## Slide 5
To record a system greeting from System Attendant
① [TRANS/PGM] + “06”
② Dial the announcement number (001~100).
→“Please press # button to leave a message” is heard.
If there is a recorded system greeting, it is heard.
③ “#” + recording + [HOLD/SAVE]
To record a system greeting with external music source at System Attendant
① [TRANS/PGM] + “06”
② Dial the announcement number (001~100).
→“Please press # button to leave a message” is heard.
If there is a recorded system greeting, it is heard.
③ Dial “*”.
④ Press # key to start recording.
⑤ Press [HOLD/SAVE] to stop recording.
Connect an external music source to the MOH port (red color) of the system
Note for Recording with External Music Source
System VMIU Announcement
Notes: In the ATD, the system prompt and system greeting can be recorded.

## Slide 6
Pre-Condition
Voice Mail Service
1. Extension should have an ability to access VMIU Mailbox
 PGM113-BTN2(VMIB Access) → Enable
2. Extension should record his user greeting message.
 [TRANS/PGM] + 6 + 1 + # + Recording + [HOLD/SAVE]
How to retrieve message
1. Press [Call Back] Button
2. Enter Password(Optional)
* Extension can assign a password to restrict the access to his mailbox.
 PGM113-BTN8 : VMIB MSG Password
 PGM227 : Authorization Code (Ex. STA107  BIN NO 008)
3. The message recorded time and date is played(Optional)
 PGM113-BTN9 : VMIB MSG Date and Time
Notes: Each station can use Voice Mail Service.
We need to program the follows to use it.
We can retrieve the recorded message.

## Slide 7
VMIU/AAFU System & User Greeting Recording Capacity
VMIU Capacity
 | VMIU | AAFU
Default Prompt | 495 sec | 495 sec
 | 8.25 min | 8.25 min
System Greeting/Prompt | 1481 sec | 1481 sec
 | 24.68 min | 24.68 min
User Greeting | 5940 sec | 594 sec
 | 99 min | 9 min
Notes: This is the VMIU capacity.
The user greeting includes the individual greeting message and recorded voice mail message.

## Slide 8
STA (B)
Message Transfer
User can transfer the recorded message to the other station while the message is being played;
Press the associated DSS button or dial the station number to transfer the message.
STA (A)
Dial station number of
STA (C)
Features – Message Transfer
STA (C)

## Slide 9
The user can append a voice message before transferring it to another station’s mailbox.
The user can rewind a retrieved message during listening mode.
VMIU messages will contain the CLI of caller, user can activate “Callback”.
[For example]
Add
Rewind
CALL BK
[Admin Programming]
PGM 181 – BTN 17
: VMIB Message Rewind Timer(1-99 sec)
[Operation]
MSG Add
1. To retrieve the message, Press the soft button [MSG].
2. To add the message, Press the soft button [ADD] .
3. Record to add the message.
4. To finish recording, press the soft button [SAVE].
5. To transfer the message, dial the station number.
MSG Rewind
1. To retrieve the message, Press the soft button [MSG].
2. To rewind the message, Press the soft button [REWIND]
Call back during listening to a message
1. Press the soft button [CALLBACK]
2. Then system dials the displayed CLI automatically.
Features – MSG Add, Rewind
Notes: The user can add or rewind the recorded voice mail message while listening to the message
The additional features can be used by using 3 soft button.

## Slide 10
Remote Control via DID/DISA
Make a call with DID/DISA line.
Dial “*” while the user greeting is played.
Dial the accorded password (max.11 digits).
The message can be
changed/heard/deleted by remote control.
- Listen the left voice messages : 1
- Listen or change user greeting : 2
- Release call forward to VMIU : 3
- Exit remote VMIU control menu : *
VMIU Call Forward is assigned
Features – Remote Control
Notes: The user can access the VMIU from the remote site to listen to a recorded
voice mail message when he is out of office.
The extension should be forwarded to VMIU in advance.
The operation is like this.

## Slide 11
How to get incoming call in analog CO line
DKTU
PSTN
Ring Signal
1. Ring Assignment :
 Station, Hunt Group, Voice Announcement can be assigned as a destination
 It can be programmed in the PGM144
2. DISA(Direct Inward System Access) :
 When the system receive the ring, system gives a dial tone and
outside caller can call extension or seize the CO line.
 It can be programmed in the PGM140-BTN2
Notes: We can get incoming call in analog CO line with 2 methods.
One is Ring Assignment, the other is DISA.
In the Ring Assignment,
When the system receives ring signal from PSTN, the system can assign Station,
Hunt Group, Voice Announcement as a destination.
It can be programmed in the PGM144
In the DISA,
When the system receives ring signal from PSTN,
the system gives a dial tone and outside caller can call extension or seize the CO line.
It can be programmed in the PGM140-Btn2

## Slide 12
Features
Description
When a call is received with DISA CO line,
① VMIU is not installed : intercom dial tone will be provided.
② VMIU is installed : assigned voice announcement will be provided.
At the tone or announcement, dial the desired station number or CO line access code.
If DISA attribute is assigned into NIGHT mode ON and VMIU announcement with
digit #, assigned voice announcement is provided and the call is disconnected
in NIGHT Mode.
 You can control the system with remote when the DISA/DID are operated in
the system. In this case, the authorization code should be assigned.
DISA(1/2)

## Slide 13
DISA Basic Admin Programming
1) [TRANS/PGM] + * # + [TRANS/PGM] + 140
2) Enter the Co line range to be assigned to DISA line.
3) [BTN 2] + Ring type + [BTN 1] + ‘1’ + [HOLD/SAVE] : DISA Activate
- Ring type : F1-Day, F2-Night, F3-Weekend, F4-On-demand
4) [BTN 2] + Ring type + [BTN 2] + ‘01~70’ + [HOLD/SAVE] : VMIU Greeting Assign
DISA(2/2)
 DISA Line Assignment + DISA Voice Announcement : PGM140-BTN2
 DISA Account Code : PGM141-BTN3
 DISA Retry Counter : PGM160-BTN4
 DISA/DID Destination : PGM167-BTN 1, 2, 3
Program
Notes: This is the DISA basic admin programming.
The DISA related admin programming is like this.

## Slide 14
Description
If external user call to the system through DISA or DID, the system give VMIU
announcement. A external caller can call a destination by pressing just one digit.
The destination can be a station, Hunt group, external number, and another VMIU
announcement of other department.
CCR (Customer Call Routing) (1/3)
0. Operator :Station 1001
1. Sales Dept. : Hunt 620
PSTN
“Hello, This is Technical Department ...“
Please dial desired station number.
Or, if you don’t know,
dial 1 for Chulho KIM
dial 2 for Thomas LEE
and dial 0 for operator. “
Thank you. : VMIU announcement 03
2. Technical Dept. : VMIU Announcement 03
“Hello, This is Sales Department ...“
Please dial desired station number.
Thank you. : VMIU announcement 02
“Hello, this is LG-Nortel. Please dial desired station number.
Or, if you don’t know,
dial 1 for Sales Department,
dial 2 for Technical Department
and dial 0 for operator. “
Thank you.
: VMIU announcement 01
Notes: If external user call to the system through DISA or DID, the system give VMIU announcement 1 like this.
Hello,~
A external caller can call a destination by pressing just one digit.
The destination can be a station, hunt group, external number and
another VMIU announcement of other department.

## Slide 15
3) Assign STA No./STA.Group No./Voice Announcement./Speed dial./Paging
4) Press [HOLD/SAVE] button to save.
2) Dial the number of announcement which
is heard after system greeting.
DIGITAL
CUSTOM CALL ROUTING:01
PRESS FLEX KEY (01-10)
Admin Programming
1) [TRANS/PGM] + *＃ + [TRANS/PGM] + 228
DIGITAL
CUSTOM CALL ROUTING
SELECT CCR TABLE (01-70)
LCD Display
CCR (Customer Call Routing) (2/3)
Notes: The CCR can be programmed in the PGM 228 like this.

## Slide 16
Operation
1) When a call comes into the system through DISA/DID line, the external user
can call to a station, hunt group, external number , another VMIU, paging
by pressing just one digit according to the predefined VMIU announcement
without assistant of a attendant.
2) Dialing one digit and wait for CCR Inter-digit timer (PGM 180-BTN 15) without
pressing any digits, the call will route to the ring assigned destination or drop the
line after error tone.
3) Pressing # button while CCR is operated, the first system greeting will be heard
again. Press * button to listen to the current system greeting .
4) If the first entered digit is not STA No./STA Grp No./Co Acc code/Atd Code ,
the call will be routed to a destination by CCR table directly.
5) The followings can be stored for a destination in CCR table.
Station Number, Station Group Number, VMIU Message No, VMIU & Drop,
System Speed, Internal/External/All Call Page.
CCR (Customer Call Routing) (3/3)
Notes: This is more detailed CCR operation. Just refer to it when you practice.

## Slide 17
Practice – DISA & VMIU Announcement
1000
PSTN
External Caller
1001
1002
1012
Hunt Group (620)
Cir, Ter, UCD, Ring, VM
Dial : 123-4567
(CO Type : Normal)
Procedure
Description
This feature allows CO incoming calls to access to specific destination without an attendant answering.
On seizing incoming an CO Line, the system gives either a VMIU announcement or a dial tone.
The caller than dials additional digit to access the desired destination.
1.Ext. party Dial : 123-4567
2.ipLDK-60 System answered
3.The ipLDK-60 system gives either a VMIU announcement or a dial tone.(PGM140-BTN2 : VMIU Greeting Assign)
4.Ext. party : dial the Number(Station No, Hunt group No, ATTD, CO Access No, CCR Code)
1) Station Number : ex) 1000  ringing station 1000 (DID/DISA Destination : PGM167)
2) Hunt Group No : ex) 620  ringing Hunt group member (Hunt Attributes : PGM191)
3) Attendant No : ex) 0 or 9  ringing Attendant
4) CO Access No : ex) 0 or 9(LOOP),88XXX,8XX
 The caller heard CO dial tone.(PGM141 : DISA Account code  off)
 The caller heard authorization code prompt.(PGM141 : DISA Account code  on)
5) CCR Code : Next page continue.(PGM228 : CCR Table)
Notes: This is an example of DISA service.
I will show you how it works and how to program it.

## Slide 18
1. CCR Table 01
Destination 1 : VMIU 02(CCR 02)
Destination 2 : VMIU 03(CCR 03)
2. CCR Table 02
Destination 1 : Station 101(Man(A))
Destination 2 : Station 102(Man(B))
2. CCR Table 03
Destination 1 : Station 103(Chulho KIM)
Destination 2 : Station 104(Thomas LEE)
[Admin]
“Hello, this is LG-Nortel. Please dial desired station number.
Or, if you don’t know,
dial 1 for Sales Department,
dial 2 for Technical Department
and dial 0 for operator. “
Thank you.
: VMIU announcement 01
0. Operator :Station 100
1. Sales Dept. : VMIU Announcement 02
PSTN
“Hello, This is Technical Department ...“
Please dial desired station number.
Or, if you don’t know,
dial 1 for Chulho KIM
dial 2 for Thomas LEE
and dial 0 for operator. “
Thank you. : VMIU announcement 03
2. Technical Dept. : VMIU Announcement 03
“Hello, This is Sales Department ...“
Please dial desired station number.
Thank you. : VMIU announcement 02
Practice – CCR & VMIU Announcement
Notes: This is an example of CCR service.
I will show you how it works and how to program it.

## Slide 19
Appendix. VMIU Voice Prompt programming by FTP

## Slide 20
1. Run FTP Client program.
Default Conditions
1. System IP (PGM 108)
2. Must be VMIU & Prompt file (ex. english.bin)
2. ftp command.
*.bin is prompt file name
Ex) korea.bin, russia.bin, english.bin
VMIB PROMPT PROGRAMMING by FTP
User : admin
Password: admin

## Slide 21
VMIB PROMPT PROGRAMMING by FTP
3. After File transferring.
4. Connect the System from telnet or serial port.
5. Enter maintenance mode. (password : brandy) & Confirm prompt file

## Slide 22
VMIB PROMPT PROGRAMMING by FTP
6. Programming Prompt
7. System rebooting
fp i (nation name)
russia : Russia prompt
english : English prompt
korea : Korean prompt