## Slide 1
MAINTENANCE

## Slide 2
System Monitoring
  Trace (Device, Board)
  Other (Memory Dump/Modification, STA/CO Status)
System Maintenance/Diagnostic
  Maintenance
  Diagnostic
1. Mode

## Slide 3
2. DIP Switch
DIP Switch Setting/Meaning
  SW1 on BMBU – DIP2 Trace Control
    ON - Trace Off (Default position)
    OFF - Trace On (To get trace information)
  SW1 on BMBU – DIP4 Database Initialize
    ON - Initialize Memory when system restarts (Default position)
    OFF - Save Database

## Slide 4
3. System Monitoring
To enter into system monitoring mode
  
  ENTER PASSWORD:jennie
  mon>
  Example:
  ipLDK-60 System
  Version GS88P-C.7Ak OCT/06
  Dsp Version: 3.0(06/06/29)
  DATE: 02/12/01
  TIME: 10:51:30
  SITE NAME :
  ENTER PASSWORD: ******
  mon>

## Slide 5
Board Trace (Max 6)
  mon> t b xx [n]
  xx: Slot number of board.
  Option ‘n’ is graphical CO simple display mode.
  Board : 1 ~ 10 (1 ~ 10 for Physical slot number)
  CPTU : 11 (Virtual slot number for CPT circuit)
  DTRU : 12 (Virtual slot number for DTMF receiver circuit)
  SMSB : 14 (Virtual slot number for SMS circuit)
  Example ) For setting trace for board in slot 1;
    mon> t b 1
mon> t d 
  Delete all current trace commands and revert to idle condition.
mon> x 
  Go to idle condition.
3. System Monitoring

## Slide 6
Device Trace
  mon t { [ [c|e|h|t] sxx ] | [ [c|e|h|t|n] cxx ] } [a]
  c : Device command tracing. (MP  PP)
  e : Event tracing. (PP, Internal, Timer Event)
  h : Highway tracing.
  t : CTI device command / event tracing.
  (Multi-options can be used; ceh, c, eh, ch, etc.)
  sxx : Trace of station xx
  (xxx: Physical station number, i.e., port number of station)
  cxx : Trace of CO line xx (xx: CO line number)
  a : Include LED/LCD data.
3. System Monitoring

## Slide 7
Device Trace (Max 15) - continued
  Example
  To get trace command(c) and event(e) of station 100 (physical port 1):
    mon> t ce s1
  To trace command and event of CO line 5 with LED/LCD data:
    mon> t ce c5 a
  For the command/event trace for CO line 6:
    mon> t ce c6
3. System Monitoring

## Slide 8
Other Commands
Dump memory
  mon> d xxxxxx yyyyyy
  Dump memory between address xxxxxx and yyyyyy
  (xxxxxx, yyyyyy: memory address in hexadecimal)
Modify memory content
  mon> m xxxxxx bb
  Modify memory of address xxxxxx to bb
  (xxxxxx: memory address in hexadecimal, bb: byte value in hexadecimal)
3. System Monitoring

## Slide 9
Other Commands - continued
Show station status
  mon> s xx
  Show station xx status,
  xx : Station port number
Show CO line status
  mon> c xx
  Show CO line xx status,
  xx : CO line number
3. System Monitoring

## Slide 10
Other Commands - continued
View/Set print port
  mon> p {v|s}
  v : View assigned print port
  s : Set print port
3. System Monitoring

## Slide 11
To enter into system maintenance and diagnostic mode
  
  ENTER PASSWORD:brandy
  maint>
  Example:
        ipLDK-60 System
        Version GS88P-C.7Ak OCT/06
        Dsp Version: 3.0(06/06/29)
        DATE: 02/12/01
        TIME: 10:55:40
        SITE NAME :
        ENTER PASSWORD: ******
        maint>
4. System Maintenance / Diagnostics

## Slide 12
Board configuration
  maint> bc
  Shows board configuration table.
B-channel listening
  maint> bl xx yyy {r|t}
  Listens to rx|tx channel of time-slot yyy at station xx (port number).
  xx : Station port number
  yyy : Time-slot number to be listened to
  r : rx channel
  t : tx channel
4. System Maintenance / Diagnostics

## Slide 13
Board status
  maint> bs [xx]
  Shows board status.
  xx : Slot number. 0 for MPB.
HDLC status
  maint> hd
  Shows HDLC status.
Reboot the system
  maint> reboot
  Reboots the system.
  Requires admin password.
4. System Maintenance / Diagnostics

## Slide 14
Traffic analysis
  maint> ta {all|period|period_abort|atd|callsum|callhour|hw|
  cosum|cohour} [hhmm] [timetype]
  all timetype : Print all traffic report
  period hhmm timetype : Print traffic report periodically
  period_abort : Cancel periodic print
  atd timetype : Print attendant traffic report
  callsum : Print call summary report
  callhour : Print call hourly report
  hw timetype : Print H/W usage summary report
  cosum timetype : Print CO traffic summary report
  cohour cogrp# : Print CO traffic hourly report
4. System Maintenance / Diagnostics

## Slide 15
Traffic analysis - continued
  hhmm : hour/minute
  timetype
    tt : Today total
    yt : Yesterday total
    lh : Last hour
    yp : Yesterday peak
    tp : Today peak
4. System Maintenance / Diagnostics