## Slide 1
MODEM CONNECTION
Notes: PC admin is
PC admin can manage all LDK system series.(Move to next page)

## Slide 2
Remote Access through Analog Modem
PSTN
For Modem connection, MODU must be installed in ipLDK-60
Recommended Speed: 9600 bps
Connection types
- Normal Dial-up connection / PPP (Point-to-Point Protocol) connection
Features
- Remote maintenance (Console commands available as with RS-232)
- Remote Admin Programming via PC-Admin
- Remote S/W Upgrade
- Remote Database Up/Download
MODU

## Slide 3
Modem Assignment : PGM 170
Station Number : PGM 170 – BTN 1  Call need to be transferred
CO line Number : PGM 170 – BTN 2  CO line is dedicated for modem
 You can assign either a station number or a CO line number for Modem.
But not both.
RS-232 PORT SETTING for COM 2 (MODU) : PGM 174 – BTN 2
Baud Rate : BTN 1
CTS/RTS : BTN 2
 These settings are between CPU and MODU
Actual modem speed is determined when the connection is established.
Connection speed is negotiated by the modems without any intervention
of ipLDK-60 system.
PPP Usage : PGM 108 – BTN 6 (ON/OFF)
Program for Modem
Admin Programming for Modem Connection

## Slide 4
Normal Dial-up Connection via PC Admin
1. Select Modem Connection in PC Admin
2. Press Setting to check if the modem is properly configure
3. Modem configuration is seen
4. Enter Admin Password if programmed

## Slide 5
Normal Dial-up Connection via PC Admin
5. Wait until connection is established
6. Connection set-up is finished

## Slide 6
PPP configuration (Windows 2000 case)
1. Make New Connection in
“Network and Dial-up Connections”

## Slide 7
PPP configuration (Windows 2000 case)

## Slide 8
2. Select your modem
PPP configuration (Windows 2000 case)

## Slide 9
3. Setting telephone number of ipLDK-60
Here in the example, it’s 16.
PPP configuration (Windows 2000 case)

## Slide 10
4. Windows 2000 specific setting
This is up to you.
PPP configuration (Windows 2000 case)

## Slide 11
5. New connection is made.
You can add a shortcut here.
PPP configuration (Windows 2000 case)

## Slide 12
6. Shortcut of New connection is displayed.
“Analog Modem Remote Access”
PPP configuration (Windows 2000 case)

## Slide 13
PPP connection establishment
1. Initial windows for new connection
Enter user ID and correct password.

## Slide 14
3. Once you click “Dial”, you will see the call is in progress.
2. Check the ID and password.
The password is encrypted so that it seems to be very long.
PPP connection establishment

## Slide 15
3. When the line is connected, user name and password is verified.
4. If the verification is successful, the PPP connection is available for data exchange.
PPP connection establishment

## Slide 16
5. Status of the connection can be checked with the right click of the icon.
PPP connection establishment

## Slide 17
PPP connected
ipLDK-60 IP : 10.0.0.3
PC IP : 10.0.0.2
1. Telnet connection to system (10.0.0.3)
2. PC Admin LAN connection to system (10.0.0.3)
3. DB Up/Download & S/W Upgrade

## Slide 18
PPP Disconnection