## Slide 1
E1HB8 Feature

## Slide 2
E1HB8 General
ADMIN setting
LED status
Dip Switch
How to get ‘MBU’ trace data for ‘E1HB8’
How to get ‘E1HB8’ trace data
How to upgrade software via WEB
Practice
1. Contents

## Slide 3
2. E1HB8 General
PSTN
PX
PX
1) E1HB8 has to be installed in only Basic Rack.
2) E1HB8 has E1R2 and SLU8. This document is for only E1R2.
3) There are 3 kinds of dialing ways. That’s, Dial pulse, DTMF and R2MFC.
It depends on PX’s condition.
4) E1R2 could receive CID(DNIS) and send CLI(ANI) via only R2MFC signaling.

## Slide 4
3. ADMIN setting
DESCRIPTION
PGM NUMBER
DEFAULT VALUE
E1 SETTING
Logical slot assign
CO type
ANI request
Incoming digit type
outgoing digit type
R2 out manage timer
R2 in manage timer
R2 disappear timer
R2 pulse timer
R2 ready timer
Line status
Calling category
CLIP table index
COLP table entry
EXT or ATD
Inter digit timer
Out digit timer
DID inter digit timer
PABX Dial tone
PABX Ringback tone
140 + Flex BTN 1
103
186 + Flex BTN 11
187 + Flex BTN 1
187 + Flex BTN 2
186 + Flex BTN 3
186 + Flex BTN 4
186 + Flex BTN 5
186 + Flex BTN 6
186 + Flex BTN 7
186 + Flex BTN 9
186 + Flex BTN 10
143 + Flex BTN 2
201
114 + Flex BTN 5
181 + Flex BTN 8
186 + Flex BTN 13
182 + Flex BTN 12
142 + Flex BTN 7
142 + Flex BTN 8
Normal CO (1)
2
0 (off)
R2MFC (2)
R2MFC (2)
14
14
14
07
07
6
1
Not assigned
Not assigned
EXT
05
05
05
YES (1)
NO (0)
DCO DID (5)
0 or 2
0 or 1
R2MFC (2)
second
second
second
* 20msec
* 20msec
Group B
Group II
CLI table Index of PGM 201 when calling
0 : DID & DOD / 2 : DID only
0 : not request / 1 : request if DID
0 : EXT / 1 : ATD
Inter digit time if I/C
Timer of last dial if O/G
Timer of DID conversion
0 : DIAL Tone is not provided from PABX.
Board assign
101
DCOB type
187 + Flex BTN 4
CLIP DISP
114 + Flex BTN 1
0 (off)
0 : Dial Pulse / 1 : DTMF / 2: R2MFC
REMARK
R2MFC (2)
CLI table Index of PGM 201 when called
0 : Ringback Tone is not provided from PABX.

## Slide 5
3. ADMIN setting
DID conversion
ERROR prompt usage
DCO Gain
R2 CRC check
DCO IP address
DCO Gateway address
DCO Subnet mask
Master Clock
PABX Busy tone
PABX ANNC tone
BUSY prompt usage
ANNC prompt usage
PABX Error tone
146 & 231
186 + Flex BTN 14
186 + Flex BTN 15
186 + Flex BTN 16
186 + Flex BTN 17
155 + Flex BTN 1
155 + Flex BTN 3
155 + Flex BTN 4
155 + Flex BTN 5
155 + Flex BTN 7
142 + Flex BTN 10
142 + Flex BTN 11
142 + Flex BTN 9
Off (0)
32
Off (0)
0 (Slave)
NO (0)
NO (0)
Off (0)
Off (0)
NO (0)
DESCRIPTION
PGM NUMBER
DEFAULT VALUE
E1 SETTING
REMARK
0 : Slave / 1 : Master
Used at WEB upgrade
0 : ERROR Tone is not provided from PABX.
0 : BUSY Tone is not provided from PABX.
0 : Annc Tone is not provided from PABX.
Used at WEB upgrade
Used at WEB upgrade
India Only
10
10
187 + Flex BTN3
NO of CLI Dgts

## Slide 6
4. LED status
1) In normal operation of slave clock, LED 8 is blinking and LED 9 is turned ON.
2) In normal operation of master clock, LED 8 is blinking and LED 7 is turned ON.
3) If the E1 line has no signal, LED 2,4,5 and 7 are turned ON.
4) If at least one of LED 2,3,4 and 5 is turned ON, it says the E1 line has faults physically.
So, it needs to contact PX’s engineer to check E1 line.
LED number
Meaning (in case of LED ON)
LED 1
LED 2
LED 3
LED 4
LED 5
LED 7
LED 8
LOS (Loss of Signal) error
Receive All-1 from PX
Receive MA (Multiframe Alignment) or RMA (Remote Multiframe Alignment)
Master clock enabled
when at least 1 of 30 CO lines is seized/seizing (incoming or outgoing)
LED 6
Enable to send CRC with frame
IN_USE
LOS
AIS
MA, RMA
FA, RFA
Tx CRC
CLOCK
ALIVE
Name
Receive FA (Frame Alignment) or RFA (Remote Frame Alignment)
If a E1HB8 is alive and is operating normally
LED 9
H/W
It’s turned ON automatically when the slave clock is operating correctly.
5. Dip Switch
1) In India, Dip Switches are not used.

## Slide 7
6. How to get ‘MBU’ trace data for ‘E1HB8’
* Setting environment
1) Bits per Second (bps) : 19200
2) Data bit : 8
3) Parity : none
4) Stop bit : 1
5) Flow Control : none
6) MBU Dip Switch 2 : Off (On : trace off, Off : trace on)
7) 9-pin serial cable is necessary
Enter moniter mode by password ‘jennie’
and type ‘t b 06’.
mon> t d
mon> t b 06
mon>x

## Slide 8
* Setting environment
1) Bits per Second (bps) : 19200
2) Data bit : 8
3) Parity : none
4) Stop bit : 1
5) Flow Control : none
6) MBU Dip Switch 2 : Off (On : trace off, Off : trace on)
7) It’s necessary to buy GDK-TRC box for 4-9-pin serial conversion.
7. How to get ‘E1HB8’ trace data

## Slide 9
* How to set Line signaling trace
1) ‘cmdevt’ operates line signaling trace ON/OFF.
2) It toggles whenever ‘cmdevt’ is entered.
* How to set R2MFC signaling trace
1) ‘r2trc’ operates R2MFC signaling trace ON/OFF.
2) It toggles whenever ‘r2trc’ command is entered.
3) ‘trcch’ decides which channel is selected among 30ch. It says hex-type.
example) ch1->trcch 00, ch2->trcch 01, ch3->trcch 02, ch4->trcch 03, ch5->trcch 04
ch6->trcch 05, ch7->trcch 06, ch8->trcch 07, ch9->trcch 08, ch10->trcch 09
ch11->trcch 0A, ch12->trcch 0B, ch13->trcch 0C, ch14->trcch 0D, ch15->trcch 0E
ch16->trcch 0F, ch17->trcch 10, ch18->trcch 11, ch19->trcch 12, ch20->trcch 13
ch21->trcch 14, ch22->trcch 15, ch23->trcch 16, ch24->trcch 17, ch25->trcch 18
ch26->trcch 19, ch27->trcch 1A, ch28->trcch 1B, ch29->trcch 1C, ch30->trcch 1D
7. How to get ‘E1HB8’ trace data

## Slide 10
* How to get the board information
1) ‘info’ displays the board’s information.
23/27
7. How to get ‘E1HB8’ trace data
nation code : 0x91ff
version : GS88f-A.0Ab
Dip SW3,2,1,0 : 0x08

## Slide 11
1) Equipments for E1HB8 Software Upgrade Process
-- LAN cable
-- PC/Notebook
-- E1HB8 Board
8. How to upgrade software via WEB
2) Please execute your web browser and type IP address of E1HB8 to access software upgrade main page.
[See Appendix 1 for more detailed information about IP related settings]
24/27

## Slide 12
3) Now click “Open Files” button and select a proper software image to update.
4) Please click ‘Upload’ button to execute software upgrade procedure.
25/27
8. How to upgrade software via WEB

## Slide 13
5) After finishing image file upload procedure, the web page will be changed like below figure.
Click ‘Proceed Flash Update’ button to upgrade new software.
6) The E1HB8 board will be reset automatically as soon as the software up- grade procedure ends.
8. How to upgrade software via WEB