## Slide 1
E1HB8 Feature

## Slide 2
E1HB8 General
E1 framer overview
Line signaling codes
R2 Register signaling
Line & R2 register signaling flow for call cases
Brazil Collect Call Blocking
ADMIN setting
LED status
Dip Switch
How to get ‘MBU’ trace data for ‘E1HB8’
How to get ‘E1HB8’ trace data
How to upgrade software via WEB
Practice
1. Contents

## Slide 3
PSTN
PX
PX
2. E1HB8 General
1) E1HB8 has to be installed in only Basic Rack.
2) E1HB8 has E1R2 and SLU8. This document is for only E1R2.
3) There are 3 kinds of dialing ways. That’s, Dial pulse, DTMF and R2MFC.
It depends on PX’s condition.
4) E1R2 could receive CID(DNIS) and send CLI(ANI) via only R2MFC signaling.

## Slide 4
TS0
TS1
TS15
TS16
TS17
TS31
…..
…..
: Frame Alignment Signal
X : default ‘1’
MA signal
remote MA signal (loss ’1’, normal ‘0’)
C1
0
0
1
1
0
1
1
0
0
0
0
X
Y
X
X
TS0
TS1
TS15
ch1
ch16
TS31
…..
…..
: remote FA Signal (loss ‘1’, normal ‘0’)
0
1
A
: Non Frame Alignment Signal
TS17
TS0
TS1
TS15
ch2
TS17
TS31
…..
…..
C2
0
0
1
1
0
1
1
TS0
TS1
TS15
ch3
ch18
TS31
…..
…..
0
1
A
TS17
ch17
TS0
TS1
TS15
ch4
TS17
TS31
…..
…..
C3
0
0
1
1
0
1
1
TS0
TS1
TS15
ch5
ch20
TS31
…..
…..
1
1
A
TS17
ch19
TS0
TS1
TS15
ch6
TS17
TS31
…..
…..
C4
0
0
1
1
0
1
1
TS0
TS1
TS15
ch7
ch22
TS31
…..
…..
0
1
A
TS17
ch21
TS0
TS1
TS15
ch8
TS17
TS31
…..
…..
C1
0
0
1
1
0
1
1
TS0
TS1
TS15
ch9
ch24
TS31
…..
…..
1
1
A
TS17
ch23
TS0
TS1
TS15
ch10
TS17
TS31
…..
…..
C2
0
0
1
1
0
1
1
TS0
TS1
TS15
ch11
ch26
TS31
…..
…..
1
1
A
TS17
ch25
TS0
TS1
TS15
ch12
TS17
TS31
…..
…..
C3
0
0
1
1
0
1
1
TS0
TS1
TS15
ch13
ch28
TS31
…..
…..
Si1
1
A
TS17
ch27
TS0
TS1
TS15
ch14
TS17
TS31
…..
…..
C4
0
0
1
1
0
1
1
TS0
TS1
TS15
ch15
ch30
TS31
…..
…..
Si2
1
A
TS17
ch29
FRAME0
FRAME1
FRAME2
FRAME3
FRAME4
FRAME5
FRAME6
FRAME7
FRAME8
FRAME9
FRAME10
FRAME11
FRAME12
FRAME13
FRAME14
FRAME15
Si1 : far end CRC reporting (error ‘0’, error free ‘1’)
Si2 : far end CRC reporting (error ‘0’, error free ‘1’)
Sub Multi frame II
Sub Multi frame I
A
C
D
B
: C & D is fixed into ’01’
3. E1 framer overview

## Slide 5
Call Phases
Signaling Channels
Forward
Backward
Af
Bf
Ab
Bb
Idle Trunk
1
0
1
0
Signal
Designation
Signal
Direction
Seizure
Seizure Signal
Seizure Acknowledge Signal
Note
Call in
Progress
Call Answer
Answering Signal
Conversation
Metering
Metering Signal
0
0
1
0
0
0
1
1
0
0
0
1
0
0
1
1
0
0
0
1
0
0
1
1
Clear Back Signal
Clear Forward Signal
Release Acknowledge Signal
Forced Release Signal
Forced Release Ack. Signal
Blocking Signal
Failure Signal
Call
Disconnection
Special
Situations
150ms in AB pulse
Going from ‘0’ to ‘1’
X = 0: A Hang Up 1st
X = 1: B Hang Up 1st
0
0
1
1
1
0
X
1
0
0
0
0
1
0
0
0
1
0
1
0
1
0
1
1
1
1
1
0
4. Line signaling Codes

## Slide 6
Sending
Receiving
Outgoing R2 register
Incoming R2 register
Forward Signal
Acknowledging
Backward Signal
Time
Acknowledging
Backward signal
Next Forward Signal
5. R2 Register signaling
1) Compelled Signaling cycle

## Slide 7
Combinations
Frequencies (Hz)
No.
Forward direction
(signals of Groups I and II)
Backward direction
(signals of Groups A and B)
Index (x)
Weight (y)
0 + 1
Numerical
Value
=
x + y
1380
1500
1620
1740
1860
1980
1140
1020
900
780
660
540
f0
f1
f2
f3
f4
f5
0
1
2
4
7
11
1
0 + 2
2
1 + 2
3
0 + 4
4
1 + 4
5
2 + 4
6
0 + 7
7
1 + 7
8
2 + 7
9
3 + 7
10
0 + 11
11
1 + 11
12
2 + 11
13
3 + 11
14
4 + 11
15
x
y
x
y
x
y
x
y
x
y
x
y
x
y
x
y
x
y
x
y
x
y
x
y
x
y
x
y
x
y
2) Multi frequency combinations
5. R2 Register signaling

## Slide 8
Signal
Signals in the Forward Direction
Group I
Group II
Digit 1
1
Digit 2
2
Digit 3
3
Digit 4
4
Digit 5
5
Digit 6
6
Digit 7
7
Digit 8
8
Digit 9
9
Digit 0
10
Half-echo suppressor at origination insertion
11
Request denied or indication of international transit
12
Access to testing equipment
13
Half-echo suppressor at destination insertion
or international traffic indication
14
End-of-number or indication that the call has
been routed via satellite
15
Ordinary subscriber
Subscriber with special rates
Maintenance equipment
Local payphone
Operator
Data communication equipment
Long Distance Payphone
Collect call
Space
Subscriber with forward transfer facility
Space
Space
Space
Space
3) Signals in the forward direction
5. R2 Register signaling

## Slide 9
4) Signals in the backward direction
Signal
Signals in the backward direction
Group A
Group B
Send next digit
Subscriber’s line free, charge
Need for echo half-suppressor at
destination or send the first digit sent
Subscriber’s line busy
Prepare for reception of Group B signals
Subscriber’s line with changed number
Congestion
Congestion
Send calling party’s category and
identification
Subscriber’s line free, no charge
Spare
Subscriber’s line free, charge,
place hold under called party control
Send N-2 digit
Unallocated number
Send N-3 digit
spare
Send N-1 digit
spare
Spare
spare
Send international transit indication
spare
Send language or discriminating digit
spare
Send information on international
origination register location
spare
Request information on the need for
destination echo half-suppressor insertion
spare
Congestion in international exchange
spare
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
National Service
International Service
5. R2 Register signaling

## Slide 10
5-1) While DID incoming call, a calling party sends all DID-digits and finishes R2 signaling first.
5) Line & R2 register signaling flow for call cases
Direction
Line signal
AB
Forward
10
Group
Group
Backward
AB
Line signal
PX
ipLDK-60
Idle
10
Idle
00
Seize
10
00
11
Seize Ack.
00
Called digit - 1
11
I-x1
A-1
Send next digit
00
Called digit - 2
11
I-x2
A-1
Send next digit
00
11
00
11
00
Called digit - n
11
I-xn
A-1
Send next digit
00
11
…
00
End of number
I-15
Complete addr
Pass to Grp. B
A-3
00
Calling party
category
11
II-x
B-x
Line status
00
11
11
11
00
ringing
01
Answer
TALK
00
00
00
01
10
Clear
Forward
01
10
Release Ack.
signal
10
Idle
10
Idle
00
11
10
5. R2 Register signaling

## Slide 11
5-2) When a Called Party sends ‘Address Complete pass to Group B signal pick up’ first.
Direction
Line signal
AB
Forward
10
Group
Group
Backward
AB
Line signal
PX
ipLDK-60
Idle
10
Idle
00
Seize
10
00
11
Seize Ack.
00
Called digit - 1
11
I-x1
A-1
Send next digit
00
Called digit - 2
11
I-x2
A-1
Send next digit
00
11
00
11
00
Called digit - n
11
I-xn
A-1
Send next digit
00
11
…
Complete addr
Pass to Grp. B
A-3
00
Calling party
category
11
II-x
B-x
Line status
00
11
11
00
ringing
01
Answer
TALK
00
00
00
01
10
Clear
Forward
11
10
Release Ack.
signal
10
Idle
10
Idle
11
Clear back
signal
00
11
00
10
5. R2 Register signaling

## Slide 12
5-3) When a Called Party requests a CID(ANI).
Direction
Line signal
AB
Forward
10
Group
Group
Backward
AB
Line signal
PX
ipLDK-60
Idle
10
Idle
00
Seize
10
00
11
Seize Ack.
00
Called digit - 1
11
I-x1
A-5
Calling part’s ID
00
Calling category
11
II-1
A-5
Calling part’s ID
00
11
00
11
00
CLI digit - 2
11
I-y2
A-1
Send next digit
00
11
Complete addr
Pass to Grp. B
A-3
00
Calling party
category
11
II-x
B-x
Line status
00
11
11
00
00
11
CLI digit - 1
I-y1
A-5
Calling part’s ID
11
A-5
Calling part’s ID
11
…
End of number
I-15
00
00
00
00
00
Called digit - 2
11
I-x2
A-1
Send next digit
00
11
11
11
…
00
Called digit - n
I-xn
00
11
11
5. R2 Register signaling

## Slide 13
5-4) When a Called Party requests CID, but a calling party rejects to send CID.
Direction
Line signal
AB
Forward
10
Group
Group
Backward
AB
Line signal
PX
ipLDK-60
Idle
10
Idle
00
Seize
10
00
11
Seize Ack.
00
Called digit - 1
11
I-x1
A-5
Calling part’s ID
00
Calling category
11
II-1
A-5
Calling part’s ID
00
11
00
11
A-1
Send next digit
00
11
Complete addr
Pass to Grp. B
A-3
00
Calling party
category
11
II-x
B-x
Line status
00
11
11
00
00
11
Request denied
I-12
00
Called digit - 2
11
I-x2
A-1
Send next digit
00
11
…
00
Called digit - n
I-xn
00
11
11
ringing
01
Answer
TALK
00
00
00
01
11
5. R2 Register signaling

## Slide 14
5-5) In abnormal case, when Calling Party doesn’t send Forward signal, Backward signal is disconnected.
Direction
Line signal
AB
Forward
10
Group
Group
Backward
AB
Line signal
PX
ipLDK-60
Idle
10
Idle
00
Seize
10
00
11
Seize Ack.
00
Called digit - 1
11
I-x1
A-1
Send next digit
00
Called digit - 2
11
I-x2
A-1
Send next digit
00
11
00
11
00
11
A-4
Congestion
00
11
00
Time-out
(15sec)
11
ringing
00
11
5. R2 Register signaling

## Slide 15
6. Brazil Collect Call Blocking
If an DID incoming call is received from PX, a called party could block that call
If a called party doesn’t want to receive and charge with collect call signaling.
There are two kinds of collect call blocking.
1) Collect call blocking with no indication
2) Collect call blocking with indication

## Slide 16
1) Collect call blocking with no indication
Direction
Line signal
AB
Forward
10
Group
Group
Backward
AB
Line signal
PX
ipLDK-60
Idle
10
Idle
00
Seize
10
00
11
Seize Ack.
00
Called digit - 1
11
I-x1
A-1
Send next digit
00
11
00
Called digit - n
11
I-xn
A-1
Send next digit
00
11
…
00
End of number
I-15
Complete addr
Pass to Grp. B
A-3
00
Calling party
category
11
II-x
B-x
Line status
00
11
11
11
00
ringing
01
Answer
TALK
00
00
00
01
10
Clear
Forward
01
10
Release Ack.
signal
10
Idle
10
Idle
00
11
11
Clear Back
01
Answer
00
00
1 sec
2 sec
continuously
10
6. Brazil Collect Call Blocking

## Slide 17
2) Collect call blocking with indication
Direction
Line signal
AB
Forward
10
Group
Group
Backward
AB
Line signal
PX
ipLDK-60
Idle
10
Idle
00
Seize
10
00
11
Seize Ack.
00
Called digit - 1
11
I-x1
A-1
Send next digit
00
11
00
Called digit - n
11
I-xn
A-1
Send next digit
00
11
…
00
End of number
I-15
Complete addr
Pass to Grp. B
A-3
00
Collect call l
11
II-8
B-7
Unallocated
number
00
11
11
11
00
00
11
6. Brazil Collect Call Blocking

## Slide 18
7. ADMIN setting
description
PGM number
Default value
E1R2 value
remarks
Logical slot assign
CO conversion type
ANI request
Incoming digit type
outgoing digit type
R2 out manage timer
R2 in manage timer
R2 disappear timer
R2 pulse timer
R2 ready timer
Line status
Calling category
CLIP table index
COLP table entry
EXT or ATD
Inter digit timer
Out digit timer
DID inter digit timer
PABX Dial tone
PABX Ringback tone
140 + Flex BTN 1
103
186 + Flex BTN 11
187 + Flex BTN 1
187 + Flex BTN 2
186 + Flex BTN 3
186 + Flex BTN 4
186 + Flex BTN 5
186 + Flex BTN 6
186 + Flex BTN 7
186 + Flex BTN 9
186 + Flex BTN 10
143 + Flex BTN 2
201
114 + Flex BTN 5
181 + Flex BTN 8
186 + Flex BTN 13
182 + Flex BTN 12
142 + Flex BTN 7
142 + Flex BTN 8
Normal CO (1)
2
0 (off)
R2MFC (2)
R2MFC (2)
14
14
14
07
07
6
1
Not assigned
Not assigned
EXT
05
05
05
YES (1)
NO (0)
DCO DID (5)
0 or 2
0 or 1
R2MFC (2)
R2MFC (2)
second
second
second
* 20msec
* 20msec
Group B
Group II
Index value
of PGM 201
2 : DID only
0 : DID & DOD
0 : not request
1 : request if DID
0 : EXT
1 : ATD
Index prefix of CLI
Inter digit time
if I/C
Timer of last dial
if O/G
Timer of
DID conversion
0 : PABX not send
1 : YES
0 : PABX not send
1 : YES
Board assign
101
DCOB type
187 + Flex BTN 4
CLIP DISP
114 + Flex BTN 1
0 (off)
0 : Dial Pulse
1 : DTMF
0 : Dial Pulse
1 : DTMF

## Slide 19
description
PGM number
Default value
E1R2 value
remarks
DID conversion
ERROR prompt usage
Block R2 Collect Call
Collect make timer
Collect break timer
DCO Gain
R2 CRC check
DCO IP address
DCO Gateway address
DCO Subnet mask
Master Clock
PABX Busy tone
146 & 231
186 + Flex BTN 14
186 + Flex BTN 15
186 + Flex BTN 16
146 + Flex BTN 7
146 + Flex BTN 8
146 + Flex BTN 9
186 + Flex BTN 17
155 + Flex BTN 1
155 + Flex BTN 3
155 + Flex BTN 4
155 + Flex BTN 5
155 + Flex BTN 7
142 + Flex BTN 10
Off (0)
0 (Off)
010 (1sec)
020 (2sec)
32
Off (0)
0 (Slave)
NO (0)
* 100msec
0 : Slave
1 : Master
0 : PABX not send
1 : YES
PABX ANNC tone
142 + Flex BTN 11
NO (0)
0 : PABX not send
1 : YES
Off (0)
Off (0)
BUSY prompt usage
ANNC prompt usage
1 : with no indication
2 : with indication
* 100msec
020
010
PABX Error tone
142 + Flex BTN 9
NO (0)
0 : PABX not send
1 : YES
If WEB upgrade
If WEB upgrade
If WEB upgrade
7. ADMIN setting

## Slide 20
8. LED status
1) In normal operation of slave clock, LED 8 is blinking and LED 9 is turned ON.
2) In normal operation of master clock, LED 8 is blinking and LED 7 is turned ON.
3) If the E1 line has no signal, LED 2,4,5 and 7 are turned ON.
4) If at least one of LED 2,3,4 and 5 is turned ON, it says the E1 line has faults physically.
So, it needs to contact PX’s engineer to check E1 line.
LED number
Meaning (in case of LED ON)
LED 1
LED 2
LED 3
LED 4
LED 5
LED 7
LED 8
LOS (Loss of Signal) error
Receive All-1 from PX
Receive MA (Multiframe Alignment) or RMA (Remote Multiframe Alignment)
Master clock enabled
when at least 1 of 30 CO lines is seized/seizing (incoming or outgoing)
LED 6
Enable to send CRC with frame
IN_USE
LOS
AIS
MA, RMA
FA, RFA
Tx CRC
CLOCK
ALIVE
Name
Receive FA (Frame Alignment) or RFA (Remote Frame Alignment)
If a E1HB8 is alive and is operating normally
LED 9
H/W
It’s turned ON automatically when the slave clock is operating correctly.
9. Dip Switch
1) In brazil, only Dip-switch 2 is used.
Off : default, clear back signal when going to IDLE of incoming talking call
On : forced release signal when going to IDLE of incoming talking call

## Slide 21
10. How to get ‘MBU’ trace data for ‘E1HB8’
* Setting environment
1) Bits per Second (bps) : 19200
2) Data bit : 8
3) Parity : none
4) Stop bit : 1
5) Flow Control : none
6) MBU Dip Switch 2 : Off (On : trace off, Off : trace on)
7) 9-pin serial cable necessary
* If entering the trace screen and do these.
mon> t d
mon> t b 06
mon> t x

## Slide 22
* Setting environment
1) Bits per Second (bps) : 19200
2) Data bit : 8
3) Parity : none
4) Stop bit : 1
5) Flow Control : none
6) MBU Dip Switch 2 : Off (On : trace off, Off : trace on)
7) It’s necessary to buy GDK-TRC box for 4-9-pin serial conversion.
11. How to get ‘E1HB8’ trace data

## Slide 23
* How to set Line signaling trace
1) ‘cmdevt’ operates line signaling trace ON/OFF.
2) It toggles whenever ‘cmdevt’ command is entered.
* How to set R2MFC signaling trace
1) ‘r2trc’ operates R2MFC signaling trace ON/OFF.
2) It toggles whenever ‘r2trc’ command is entered.
3) ‘trcch’ decides which channel is selected among 30ch. It says hex-type.
example)
ch1->trcch 00, ch2->trcch 01, ch3->trcch 02, ch4->trcch 03, ch5->trcch 04
ch6->trcch 05, ch7->trcch 06, ch8->trcch 07, ch9->trcch 08, ch10->trcch 09
ch11->trcch 0A, ch12->trcch 0B, ch13->trcch 0C, ch14->trcch 0D, ch15->trcch 0E
ch16->trcch 0F, ch17->trcch 10, ch18->trcch 11, ch19->trcch 12, ch20->trcch 13
ch21->trcch 14, ch22->trcch 15, ch23->trcch 16, ch24->trcch 17, ch25->trcch 18
ch26->trcch 19, ch27->trcch 1A, ch28->trcch 1B, ch29->trcch 1C, ch30->trcch 1D
11. How to get ‘E1HB8’ trace data

## Slide 24
* How to get the board information
1) ‘info’ displays the board’s information.
23/27
11. How to get ‘E1HB8’ trace data

## Slide 25
1) Equipments for E1HB8 Software Upgrade Process
- LAN cable
-- PC/Notebook
- E1HB8 Board
12. How to upgrade software via WEB
2) Please execute your web browser and type IP address of E1HB8 to access software upgrade main page.
[See Appendix 1 for more detailed information about IP related settings]
24/27

## Slide 26
3) Now click “Open Files” button and select a proper software image to update.
4) Please click ‘Upload’ button to execute software upgrade procedure.
25/27
12. How to upgrade software via WEB

## Slide 27
5) After finishing image file upload procedure, the web page will be changed like below figure.
Click ‘Proceed Flash Update’ button to upgrade new software.
6) The E1HB8 board will be reset automatically as soon as the software up- grade procedure ends.
12. How to upgrade software via WEB