## Slide 1
E1HB8 Feature
E1HB8 Feature

## Slide 2
E1HB8 General
E1 framer overview
Line signaling codes
R2 Register signaling
Line & R2 register signaling flow for call cases
India CLI
ADMIN setting
LED status
Dip Switch
How to get ‘MBU’ trace data for ‘E1HB8’
How to get ‘E1HB8’ trace data
How to upgrade software via WEB
Practice
Contents

## Slide 3
1. E1HB8 General
PSTN
PX
PX
1) E1HB8 has to be installed in only Basic Rack.
2) E1HB8 has E1R2 and SLU8. This document is for only E1R2.
3) There are 3 kinds of dialing ways. That’s, Dial pulse, DTMF and R2MFC.
It depends on PX’s condition.
4) E1R2 could receive CID(ANI request) and send CLI from calling party via only R2MFC signaling.

## Slide 4
Si2
1
A
Si2 : far end CRC reporting (error ‘0’, error free ‘1’)
TS0
TS1
TS15
TS16
TS17
TS31
…..
…..
: Frame Alignment Signal
X : default ‘1’
MA signal
remote MA signal (loss ’1’, normal ‘0’)
C1
0
0
1
1
0
1
1
0
0
0
0
X
Y
X
X
TS0
TS1
TS15
ch1
ch16
TS31
…..
…..
: remote FA Signal (loss ‘1’, normal ‘0’)
0
1
A
: Non Frame Alignment Signal
TS17
TS0
TS1
TS15
ch2
TS17
TS31
…..
…..
C2
0
0
1
1
0
1
1
TS0
TS1
TS15
ch3
ch18
TS31
…..
…..
0
1
A
TS17
ch17
TS0
TS1
TS15
ch4
TS17
TS31
…..
…..
C3
0
0
1
1
0
1
1
TS0
TS1
TS15
ch5
ch20
TS31
…..
…..
1
1
A
TS17
ch19
TS0
TS1
TS15
ch6
TS17
TS31
…..
…..
C4
0
0
1
1
0
1
1
TS0
TS1
TS15
ch7
ch22
TS31
…..
…..
0
1
A
TS17
ch21
TS0
TS1
TS15
ch8
TS17
TS31
…..
…..
C1
0
0
1
1
0
1
1
TS0
TS1
TS15
ch9
ch24
TS31
…..
…..
1
1
A
TS17
ch23
TS0
TS1
TS15
ch10
TS17
TS31
…..
…..
C2
0
0
1
1
0
1
1
TS0
TS1
TS15
ch11
ch26
TS31
…..
…..
1
1
A
TS17
ch25
TS0
TS1
TS15
ch12
TS17
TS31
…..
…..
C3
0
0
1
1
0
1
1
TS0
TS1
TS15
ch13
ch28
TS31
…..
…..
Si1
1
A
TS17
ch27
TS0
TS1
TS15
ch14
TS17
TS31
…..
…..
C4
0
0
1
1
0
1
1
TS0
TS1
TS15
ch15
ch30
TS31
…..
…..
TS17
ch29
FRAME0
FRAME1
FRAME2
FRAME3
FRAME4
FRAME5
FRAME6
FRAME7
FRAME8
FRAME9
FRAME10
FRAME11
FRAME12
FRAME13
FRAME14
FRAME15
Si1 : far end CRC reporting (error ‘0’, error free ‘1’)
Sub Multi frame II
Sub Multi frame I
A
C
D
B
: C & D is fixed into ’01’
2. E1 framer overview

## Slide 5
Call Phases
Signaling Channels
Forward
Backward
Af
Bf
Ab
Bb
Idle Trunk
1
0
1
0
Signal
Designation
Signal
Direction
Seizure
Seizure Signal
Seizure Acknowledge Signal
Note
Call in
Progress
Call Answer
Answering Signal
Conversation
0
0
1
0
0
0
1
1
0
0
0
1
0
0
1
1
0
0
0
1
Clear Back Signal
Clear Forward Signal
Release Acknowledge Signal
Forced Release Ack. Signal
Blocking Signal
Failure Signal
Call
Disconnection
Special
Situations
X = 0: A Hang Up 1st
X = 1: B Hang Up 1st
0
0
1
1
1
0
X
1
1
0
0
0
1
0
1
0
1
0
1
1
1
1
1
0
3. Line signaling Codes

## Slide 6
4. R2 Register signaling
Sending
Receiving
Outgoing R2 register
Incoming R2 register
Forward Signal
Acknowledging
Backward Signal
Time
Acknowledging
Backward signal
Next Forward Signal
1) Compelled Signaling cycle

## Slide 7
Combinations
Frequencies (Hz)
No.
Forward direction
(signals of Groups I and II)
Backward direction
(signals of Groups A and B)
Index (x)
Weight (y)
0 + 1
Numerical
Value
=
x + y
1380
1500
1620
1740
1860
1980
1140
1020
900
780
660
540
f0
f1
f2
f3
f4
f5
0
1
2
4
7
11
1
0 + 2
2
1 + 2
3
0 + 4
4
1 + 4
5
2 + 4
6
0 + 7
7
1 + 7
8
2 + 7
9
3 + 7
10
0 + 11
11
1 + 11
12
2 + 11
13
3 + 11
14
4 + 11
15
x
y
x
y
x
y
x
y
x
y
x
y
x
y
x
y
x
y
x
y
x
y
x
y
x
y
x
y
x
y
2) Multi frequency combinations
4. R2 Register signaling

## Slide 8
3) Signals in the forward direction
Signal
Signals in the Forward Direction
Group I
Group II
Digit 1 / CLI Enabled
1
Digit 2
2
Digit 3
3
Digit 4
4
Digit 5
5
Digit 6
6
Digit 7
7
Digit 8
8
Digit 9
9
Digit 0 / CLI Disabled
10
11
Space
12
13
14
15
Ordinary subscriber
Priority Subscriber
Spare at current
Spare at current
Operator
STD coin box
Space
Space
Space
Space
Space
Space
Space
Space
Space
Space
Space
Space
Space
4. R2 Register signaling

## Slide 9
4) Signals in the backward direction
Signal
Signals in the backward direction
Group A
Group B
Send next digit (n+1)
spare
Restart
Changed number
Change over to reception of Group B signals
Called line busy
Calling line identification
Congestion
Send category of the calling subscriber
Unallocated number
Switch-through the speech path
Normal subscriber, free, with metering
Send last but two digit (N-2)
– not available in local exchange
Called line free, but non-metered
spare; not available in local exchange
spare; not available in local exchange
Spare
spare; not available in local exchange
Send international transit indication
spare
Send language or discriminating digit
spare
Send information on international
origination register location
spare
Request information on the need for
destination echo half-suppressor insertion
spare
Congestion in international exchange
spare
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
National Service
International Service
Send last but two digit (N-3)
– not available in local exchange
Send last but two digit (N-1)
– not available in local exchange
4. R2 Register signaling

## Slide 10
5. Line & R2 register signaling flow for call cases
1) While DID incoming call, a calling party sends all DID-digits and finishes R2 signaling first.
Direction
Line signal
AB
Forward
10
Group
Group
Backward
AB
Line signal
PX
ipLDK-60
Idle
10
Idle
00
Seize
10
00
11
Seize Ack.
00
Called digit - 1
11
I-x1
A-5
Request Category
00
Calling category
11
II-x
A-1
Send next digit
00
11
00
11
00
Called digit - n
11
I-xn
00
11
…
Complete addr
Pass to Grp. B
A-3
00
Calling category
11
II-x
B-x
Line status
00
11
11
11
00
ringing
01
Answer
TALK
00
00
00
01
10
Clear
Forward
01
10
Release Ack.
signal
10
Idle
10
Idle
00
11
10
Called digit - 2
I-x2
A-1
Send next digit
00

## Slide 11
2) When a Called Party requests a CID(ANI request) and a Calling party permits sending CLI.
Direction
Line signal
AB
Forward
10
Group
Group
Backward
AB
Line signal
PX
ipLDK-60
Idle
10
Idle
00
Seize
10
00
11
Seize Ack.
00
Called digit - 1
11
I-x1
A-5
Request Category
00
Calling category
11
II-1
A-1
Send next digit
00
11
00
11
00
CLI Enabled
11
I-1
00
11
Complete addr
Pass to Grp. B
A-3
00
Calling party
category
11
II-x
B-x
Line status
00
11
11
00
00
11
I-xn
A-4
Request Calling ID
11
A-4
Request Calling ID
11
…
00
00
00
00
00
Called digit - 2
11
I-x2
A-1
Send next digit
00
11
11
11
…
00
CLI digit - n
I-yn
00
11
11
Called digit - 1
CLI digit - 1
I-y1
A-4
Request Calling ID
5. Line & R2 register signaling flow for call cases

## Slide 12
3) When a Called Party requests a CID(ANI request) and a Calling party rejects.
Direction
Line signal
AB
Forward
10
Group
Group
Backward
AB
Line signal
PX
ipLDK-60
Idle
10
Idle
00
Seize
10
00
11
Seize Ack.
00
Called digit - 1
11
I-x1
A-5
Request Category
00
Calling category
11
II-1
A-1
Send next digit
00
11
00
11
00
CLI Disabled
11
I-10
00
11
Complete addr
Pass to Grp. B
A-3
Calling party
category
II-x
B-x
Line status
00
11
I-xn
A-4
Request Calling ID
11
11
00
00
00
00
00
Called digit - 2
11
I-x2
A-1
Send next digit
00
11
11
11
…
00
11
Called digit - 1
ringing
5. Line & R2 register signaling flow for call cases

## Slide 13
4) In abnormal case, when Calling Party doesn’t send Forward signal, Backward signal is disconnected.
Direction
Line signal
AB
Forward
10
Group
Group
Backward
AB
Line signal
PX
ipLDK-60
Idle
10
Idle
00
Seize
10
00
11
Seize Ack.
00
Called digit - 1
11
I-x1
A-5
Send next digit
00
Calling category
11
II-x
A-1
Send next digit
00
11
00
11
00
11
A-4
Congestion
00
11
00
Time-out
(15sec)
11
ringing
00
11
5. Line & R2 register signaling flow for call cases

## Slide 14
Digit 1 (0)
A5
Group II (category)
A1
Digit 2 (2)
A1
Digit 3 (2)
A4
‘1’ – category
A4
‘3’
A4
‘3’
A4
‘2’
A4
‘5’
A4
‘6’
A4
‘7’
A4
‘8’
A5
Group II (category)
A1
Digit 4 (4)
A1
Digit 5 (1)
A1
Digit 6 (3)
A1
Digit 7 (4)
A1
Digit 8 (3)
A1
Digit 9 (2)
A1
Digit 10 (1)
A1
A6
…
Calling party : (022) 4134321, Called party : 3325678
6. India CLI

## Slide 15
7. ADMIN setting
description
PGM number
Default value
E1R2 value
remarks
Logical slot assign
CO conversion type
ANI request
Incoming digit type
outgoing digit type
R2 out manage timer
R2 in manage timer
R2 disappear timer
R2 pulse timer
R2 ready timer
Line status
Calling category
CLIP table index
COLP table entry
EXT or ATD
Inter digit timer
Out digit timer
DID inter digit timer
PABX Dial tone
PABX Ringback tone
140 + Flex BTN 1
103
186 + Flex BTN 11
187 + Flex BTN 1
187 + Flex BTN 2
186 + Flex BTN 3
186 + Flex BTN 4
186 + Flex BTN 5
186 + Flex BTN 6
186 + Flex BTN 7
186 + Flex BTN 9
186 + Flex BTN 10
143 + Flex BTN 2
201
114 + Flex BTN 5
181 + Flex BTN 8
186 + Flex BTN 13
182 + Flex BTN 12
142 + Flex BTN 7
142 + Flex BTN 8
Normal CO (1)
2
0 (off)
R2MFC (2)
R2MFC (2)
14
14
14
07
07
6
1
Not assigned
Not assigned
EXT
05
05
05
YES (1)
NO (0)
DCO DID (5)
0 or 2
0 or 1
R2MFC (2)
R2MFC (2)
second
second
second
* 20msec
* 20msec
Group B
Group II
Index value
of PGM 201
2 : DID only
0 : DID & DOD
0 : not request
1 : request if DID
0 : EXT
1 : ATD
Index prefix of CLI
Inter digit time
if I/C
Timer of last dial
if O/G
Timer of
DID conversion
0 : PABX not send
1 : YES
0 : PABX not send
1 : YES
Board assign
101
DCOB type
187 + Flex BTN 4
CLIP DISP
114 + Flex BTN 1
0 (off)
0 : Dial Pulse
1 : DTMF
0 : Dial Pulse
1 : DTMF

## Slide 16
description
PGM number
Default value
E1R2 value
remarks
DID conversion
ERROR prompt usage
DCO Gain
R2 CRC check
DCO IP address
DCO Gateway address
DCO Subnet mask
DCO server IP address
Master Clock
PABX Busy tone
146 & 231
186 + Flex BTN 14
186 + Flex BTN 15
186 + Flex BTN 16
186 + Flex BTN 17
155 + Flex BTN 1
155 + Flex BTN 3
155 + Flex BTN 4
155 + Flex BTN 5
155 + Flex BTN 6
155 + Flex BTN 7
142 + Flex BTN 10
Off (0)
32
Off (0)
0 (Slave)
NO (0)
0 : Slave
1 : Master
0 : PABX not send
1 : YES
PABX ANNC tone
142 + Flex BTN 11
NO (0)
0 : PABX not send
1 : YES
Off (0)
Off (0)
BUSY prompt usage
ANNC prompt usage
PABX Error tone
142 + Flex BTN 9
NO (0)
0 : PABX not send
1 : YES
If WEB upgrade
If WEB upgrade
If WEB upgrade
If WEB upgrade
NO OF CLI DGTS
187 + Flex BTN 3
10
10
India only
7. ADMIN setting

## Slide 17
8. LED status
LED number
Meaning (in case of LED ON)
LED 1
LED 2
LED 3
LED 4
LED 5
LED 7
LED 8
LOS (Loss of Signal) error
Receive All-1 from PX
Receive MA (Multiframe Alignment) or RMA (Remote Multiframe Alignment)
Master clock enabled
when at least 1 of 30 CO lines is seized/seizing (incoming or outgoing)
LED 6
Enable to send CRC with frame
IN_USE
LOS
AIS
MA, RMA
FA, RFA
Tx CRC
CLOCK
ALIVE
Name
Receive FA (Frame Alignment) or RFA (Remote Frame Alignment)
If a E1HB8 is alive and is operating normally
1) In normal operation of slave clock, LED 8 is blinking and LED 9 is turned ON.
2) In normal operation of master clock, LED 8 is blinking and LED 7 is turned ON.
3) If the E1 line has no signal, LED 2,4,5 and 7 are turned ON.
4) If at least one of LED 2,3,4 and 5 is turned ON, it says the E1 line has faults physically.
So, it needs to contact PX’s engineer to check E1 line.
LED 9
H/W
It’s turned ON automatically when the slave clock is operating correctly.
9. Dip Switch
In India, Dip-switches are not used

## Slide 18
10. How to get trace data for ‘E1HB8’
* Setting environment (COM port connection)
1) Bits per Second (bps) : 19200
2) Data bit : 8
3) Parity : none
4) Stop bit : 1
5) Flow Control : none
6) MBU Dip Switch 2 : Off (On : trace off, Off : trace on)
7) 9-pin serial cable necessary
* If entering the trace screen and do these.
mon> t d
mon> t b 06
mon> t x

## Slide 19
* Setting environment
1) Bits per Second (bps) : 19200
2) Data bit : 8
3) Parity : none
4) Stop bit : 1
5) Flow Control : none
6) MBU Dip Switch 2 : Off (On : trace off, Off : trace on)
7) It’s necessary to buy GDK-TRC box for 4-9-pin serial conversion.
11. How to get ‘E1HB8’ trace data

## Slide 20
* How to set Line signaling trace
1) ‘cmdevt’ operates line signaling trace ON/OFF.
2) It toggles whenever ‘cmdevt’ command is entered.
* How to set R2MFC signaling trace
1) ‘r2trc’ operates R2MFC signaling trace ON/OFF.
2) It toggles whenever ‘r2trc’ command is entered.
3) ‘trcch’ decides which channel is selected among 30ch. It says hex-type.
example)
ch1->trcch 00, ch2->trcch 01, ch3->trcch 02, ch4->trcch 03, ch5->trcch 04
ch6->trcch 05, ch7->trcch 06, ch8->trcch 07, ch9->trcch 08, ch10->trcch 09
ch11->trcch 0A, ch12->trcch 0B, ch13->trcch 0C, ch14->trcch 0D, ch15->trcch 0E
ch16->trcch 0F, ch17->trcch 10, ch18->trcch 11, ch19->trcch 12, ch20->trcch 13
ch21->trcch 14, ch22->trcch 15, ch23->trcch 16, ch24->trcch 17, ch25->trcch 18
ch26->trcch 19, ch27->trcch 1A, ch28->trcch 1B, ch29->trcch 1C, ch30->trcch 1D
11. How to get ‘E1HB8’ trace data

## Slide 21
* How to get the board information
1) ‘info’ displays the board’s information.
India : 91FF
11. How to get ‘E1HB8’ trace data
0x91ff
GS88F-A.0Aa
0x08

## Slide 22
1) Equipments for E1HB8 Software Upgrade Process
- LAN cable
-- PC/Notebook
- E1HB8 Board
12. How to upgrade software via WEB
2) Please execute your web browser and type IP address of E1HB8 to access software upgrade main page.
[See Appendix 1 for more detailed information about IP related settings]

## Slide 23
3) Now click “Open Files” button and select a proper software image to update.
4) Please click ‘Upload’ button to execute software upgrade procedure.
12. How to upgrade software via WEB

## Slide 24
5) After finishing image file upload procedure, the web page will be changed like below figure.
Click ‘Proceed Flash Update’ button to upgrade new software.
6) The E1HB8 board will be reset automatically as soon as the software up- grade procedure ends.
12. How to upgrade software via WEB