## Slide 1
VOICE NETWORKING

## Slide 2
Contents
Overview
Overall Networking Configuration
LG IP Networking Solution
Feature
VoIP Connection
Feature Operation
Practice
Notes: In this course, I will explain about Voice Networking feature with the following order.
First, we will review the overview of Voice Networking .
And then, I will introduce our networking configuration, feature, how to connection with PRI and VOIP.
And at last, we will review the feature operation with some simple examples that we can exercise together.

## Slide 3
Overview
ipLDK Voice networking provides a way of communication to inter-work
with networked system over Internet (VoIP).
ipLDK provides uniform numbering plan for all users in the network
The networked systems can be considered as one system.
Extension in any system can talk with other system like extension call
Up to 72 systems can be inter-working via public or private network
ipLDK supports the total solution from Home office to Headquarter office
with ipLDK-60 Systems
Notes: Ip LDK voice networking feature provides a way of communication to inter-work with networked system over VOIP or PRI.
Our voice networking feature is based on QSIG and H.450 protocol.
QSIG means Q signaling protocol and it is a series of international standards and based on Q.931
H.450 is standard created by International Telecommunications Union and it is based on H.323
But, Now, we supports this feature among LG-Nortel systems.
ipLDK provides uniform numbering plan for all users in the network
And the networked systems can be considered as one system. so, Extension in any system can talk with other system like extension call
IpLDK system has 72 networking numbering Table. So Up to 72 systems can be inter-working via public or private network
So, ipLDK supports the total solution from Home office to Headquarter office with LG Nortel Systems (ipLDK-20/100/300/300E, LDK-24 and iPECS, RSG )

## Slide 4
Overall Networking Configuration
Branch Office B
Router
BLF Manager
Headquarter Office
Router
Local Office
Router
ipLDK-60
Branch Office A
ipLDK-60
IP Network
Router
Local Office
ipLDK-60
IP Phone Users
Phontage Users
Notes: This is overall networking configuraion
As you see, ipLDK systems can be networked through the ISDN PRI or IP Network.

## Slide 5
Feature
Net Call (Basic Call)
Net Call Transfer (Screen / Unscreened)
Net Call Forward
 Unconditional / Busy / No Answer / Busy No Answer / Follow-Me
Name Display
Call Offer(Camp-On)
Message Waiting Indication (MWI by Request)
Call Completion (Call Back)
CO Transit-In/Out
Absent Text Message Service
Do Not Disturb (DND) Service
Busy Lamp Field (BLF) Service
Centralized SMDR
Centralized VMS
The Following QSIG Features are provided
Notes: ipLDK supports the Following QSIG Features
First, ipLDK system provides the basic net call. So you can dial the extension of other system as if you dials the internal extension
and ip LDK system provides screened or unscreened trasnfer
ip LDK system provides unconditional, busy, no answer, follow me call forward
ip LDK system provides name display service.
And station A net call to station b and station A has his name, station B can check station A’s name.
ip LDK system provides call offer .
It is similar to Camp-On feature.
And station A net call to station b and station B is busy state, station A can send the indication by dialing call offer code.
ip LDK system provides Message wait indication or call completion .
I

## Slide 6
VoIP Connection
VoIP Connection between Systems
Master
Slave
LAN
STA NO
100 ~ 147
STA NO
200 ~ 247
1. Station range : 100~147
2. MPB IP Address : 192.168.23.10
3. VOIB IP Address : 192.168.23.11
4. CO Line type :
(LCOB : Normal, VOIB : ISDN DID)  PGM140
5. DID Conversion Type : Type 1
6. CO Range :
(LCOB : 1~6, VOIB : 7~14)
7. Net CO Group :
(VOIB : Net CO Group 01)
(LCOB : Net CO Group 02)
1. Station range : 200~247
2. MPB IP Address : 192.168.23.20
3. VOIB IP Address : 192.168.23.21
4. CO Line type :
(VOIB : ISDN DID)  PGM140
5. DID Conversion Type : Type 1
6. CO Range :
(VOIB : 1~6)
7. Net CO Group :
(VOIB : Net CO Group 01)
Master System
Slave System
“9” : CO Access Code
IP Networking Lock Key(5) for each system is required to use
LANU
VOIB
PSTN
LCO
LANU
VOIB
Notes: This is an example of QSIG Connection via VoIP.
Normally we call it, IP Networking when configuring QSIG
through VoIP.
There is a CO line for call transit out In the master system,
so slave system can access the CO line through IP network.
Before programming it, IP Networking S/W Lock Key should
be applied in advance.
From now, we will show you how to program QSIG.

## Slide 7
VoIP Connection
8. Networking Table
PGM320
BTN 1 : Net Enable
PGM322 (Net CO)
BTN 1 : Net CO Group = 01
BTN 4 : Net CO Type = NET or PSTN
- VOIB : Net CO Group 01/NET
- LCOB : Net CO Group 02/PSTN
PGM324
BIN 00 (Master, itself)
BTN 1 (Usage) = NET
BTN 2 (STA Number) = 1#**
BTN 3 (Net CO Gr) = 00
BIN 01 (Slave system)
BTN 1 (Usage) = NET
BTN 2 (STA Number) = 2**
BTN 3 (Net CO Gr) = 01
BTN 4 (CPN) /BTN(1)
CPN IP Info 1= 192.168.23.21
BIN 02 (Master system) (*Note 2)
BTN 1 (Usage) = PSTN
BTN 2 (STA Number) = 9 (*Note 1)
BTN 3 (Net CO Gr) = 02
8. Networking Table
PGM320
BTN 1 : Net Enable
PGM322 (Net CO)
BTN 1 : Net CO Group = 01
BTN 4 : Net CO Type = NET or PSTN
- VOIB : Net CO Group 01/NET
PGM324
BIN 00 (Slave, itself)
BTN 1 (Usage) = NET
BTN 2 (STA Number) = 2#**
BTN 3 (Net CO Gr) = 00
BIN 01 (Master system)
BTN 1 (Usage) = NET
BTN 2 (STA Number) = 1**
BTN 3 (Net CO Gr) = 01
BTN 4 (CPN) /BTN(1)
CPN IP Info 1 = 192.168.23.11
BIN 02 (Master system) (*Note 2)
BTN 1 (Usage) = PSTN
BTN 2 (STA Number) = 9 (*Note 1)
BTN 3 (Net CO Gr) = 01
BTN 4 (CPN) /BTN(1)
CPN IP Info 1 = 192.168.23.11
BTN 7 (Digit Repeat) = Yes
Master System
Slave System
* Note 1 : Delete 1st CO Group Access Code (PGM107) in advance.
* Note 2 : A station in slave system can access the LCOB lines of master system by dialing “9”.
“9” should not be used in numbering plan.
Notes: PGM 320 : Networking Basic Attribute
Flex1: Net enable To change this field. You should have the networking lock key.
PGM 322: Net CO line Attribute
PGM 324 : networking numbering plan table.
Note 1: we use uniform numbering plan, so you can’t use the same code for the difference purpose.

## Slide 8
Station 101
Station 102
Networking Practice
Test scenario
[make Networking]
1. Make Networking System A and B with VOIB CO (CO 4~7).
[ How to operate & Program ]
Please Reference VOIP connection Page.
Station 201
Station 202
IP Network
System A
System B

## Slide 9
101
Networking Practice
Test scenario
[make Networking]
1. Make Networking System A and B.
IP Network
System A
System B
102
201
202
[ How to operate & Program System B]
1. PGM 105 + del + 200 247
2. PGM 140 + 04 07 + Flx1 + 3 (ISDN/DID Type)
3. PGM 143 + 04 07 + Flx4 + 1
4. PGM 340 + Flx1 + 10.10.20.1 (VOIB IP)
5. PGM 340 + Flx2 + 10.10.20.254 (VOIB Gateway)
6. PGM 320 + Flx1 + On
7. PGM 322 + 04 07 + Flx1 + 01
8. PGM 322 + 04 07 + Flx4 + NET
9. PGM 324 + 00 + Flx1 + NET
10. PGM 324 + 00 + Flx2 + 2#**
11. PGM 324 + 00 + Flx3 + 00
12. PGM 324 + 01 + Flx1 + NET
13. PGM 324 + 01 + Flx2 + 1**
14. PGM 324 + 01 + Flx3 + 01
15. PGM 324 + 01 + Flx4 + Flx1 + 10.10.10.1
[ How to operate & Program System A]
1. PGM 105 + del + 100 147
2. PGM 140 + 04 07 + Flx1 + 3 (ISDN/DID Type)
3. PGM 143 + 04 07 + Flx4 + 1
4. PGM 340 + Flx1 + 10.10.10.1 (VOIB IP)
5. PGM 340 + Flx2 + 10.10.10.254 (VOIB Gateway)
6. PGM 320 + Flx1 + On
7. PGM 322 + 04 07 + Flx1 + 01
8. PGM 322 + 04 07 + Flx4 + NET
9. PGM 324 + 00 + Flx1 + NET
10. PGM 324 + 00 + Flx2 + 1#**
11. PGM 324 + 00 + Flx3 + 00
12. PGM 324 + 01 + Flx1 + NET
13. PGM 324 + 01 + Flx2 + 2**
14. PGM 324 + 01 + Flx3 + 01
15. PGM 324 + 01 + Flx4 + Flx1 + 10.10.20.1

## Slide 10
[Admin Programming]
■ Networking Basic Attribute : PGM 320
■ Networking CO Line Attribute : PGM 322
■ Networking Routing Table : PGM 324
[Call Flow]
Note : During conversation, all telephony features are
available.(For example, call transfer, hold, conference and etc.)
Feature Operation (Net Call)
Step
Flow
1
Station 101 dials Station 202 in Slave System
2
System searches Networking Numbering Table.
3
2** matches 202, (2** means ‘200 ~ 299’)
4
System gets destination IP address
5
VoIP net call goes to destination IP
6
Ringing at the exact destination (202)
7
Destination (202) answers
8
Conversation is established
Notes: It shows how the net call is processing.
Call Flow
If destination 202 answers, the conversation is established.

## Slide 11
Internet
PSTN
Step 3
202
100
Step 1 ~ 2
Step 4
Step 5
Step 6
[Admin Programming]
■ Networking Basic Attribute : PGM 320
■ Networking Transfer Mode : PGM 321-FLEX1
■ Networking CO Line Attribute : PGM 322
■ Networking Routing Table : PGM 324
[Call Flow]
Feature Operation (Net Call Transfer)
Notes: It shows how the net call transfer is processing.
Call Flow
If destination 202 answers, the conversation is established.

## Slide 12
Internet
PSTN
Step 1
202
100
Step 2
Step 3
Step 4
Step 5
[Admin Programming]
■ Call Forward Attribute : PGM 111-FLEX2
■ Networking Basic Attribute : PGM 320
■ Networking Transfer Mode : PGM 321-FLEX1
■ Networking CO Line Attribute : PGM 322
■ Networking Routing Table : PGM 324
[Call Flow]
Feature Operation (Net Call Forward)
Notes: It shows how the net call forwarding is processing.
Call Flow
If destination 202 answers, the conversation is established.

## Slide 13
[Admin Programming]
■ Networking Basic Attribute : PGM 320
Internet
Step 1
202
100
Step 3
BUSY
Step 2
Step 4
Step 5
[Call Flow]
Feature Operation (Call Offer)
Notes: It shows how the net call offer is processing.
Call Flow
If destination 202 presses the [CO] button,
the conversation is established.

## Slide 14
[Admin Programming]
■ Networking Basic Attribute : PGM 320-FLEX8
Internet
Step 1
202
100
Step 3
BUSY
Step 2
Step 4
Step 5
[Call Flow]
Feature Operation (Call Completion)
Notes: It shows how the net call completion is processing.
Call Flow
If destination 202 answers, the conversation is established.

## Slide 15
[Admin Programming]
■ Networking CO Line Type : PGM 322
■ Networking Routing Table : PGM 324
■ CO to CO COS : PGM 166
Internet
PSTN
202
Step 4
Step 2
Step 1
Step 5
Step 3
Additional Programming
Master :
PGM 322 : CO 1
BTN 1 (Net Col Group) = 02 for PSTN Lines
BTN 4 (Net CO Type) = PSTN
PGM 324 BIN 02
-FLEX 1 (Usage) = PSTN
-FLEX 2 (Net Code) = 9 (transit code)
-FLEX 3 (Net CO Group) = 02
PGM 166 CO to CO COS
-FLEX 1 (Day) : 1, FLEX 2 (Night) : 1
Additional Programming
Slave :
PGM 324 BIN 10
-FLEX 1 (Usage) = PSTN
-FLEX 2 (Net Code) = 9 (transit code)
-FLEX 3 (Net CO Group) = 01
-FLEX 4 (CPN) = 10.10.10.1
-FLEX 7 (DGT Repeat) = YES
[Call Flow]
Feature Operation (CO Transit-Out)
Notes: It shows how the net CO Transit Out is processing.
Call Flow
If destination 202 answers, the conversation is established.

## Slide 16
[Admin Programming]
■ Networking Routing Table : PGM 324
Internet
PSTN
202
Step 1
Step 3
Step 4
Step 5
[Call Flow]
Feature Operation (CO Transit-In)
Step 2
Notes: It shows how the net CO Transit In is processing.
Call Flow
If destination 202 answers, the conversation is established.

## Slide 17
[Application]
■ BLF Manager Software(PC Application)
[Admin Programming]
■ Networking Supplementary Attribute : PGM 321
- TCP Port Assign(FLEX2)
- UDP Port Assign(FLEX3)
- BLF Manager IP Address Assign(FLEX4)
- Duration of BLF Status(FLEX5)
■ Networking Routing Table : PGM 324
Internet
Step 1
202
100
BUSY
BLF Manager
Step 2
[Call Flow]
Feature Operation (BLF Service)
Notes: It shows how the BLF is processing.
Station 100 assigns station 202 in a flexible button.
If station 202 is busy,
the BLF broadcasts the busy status to the networked system.
Station 100’s flexible button is flashing

## Slide 18
A user who is in other QSIG system can activate a remote forward to a station
over the QSIG network.
Operation
To activate Net Call Forward- Follow-Me
1. Press the [MON] button and the [DND/FOR] button
2. Dial Net Call Forward(Follow-Me Code “0”), and dial the forwarding station number of QSIG system.
3. Dial the password of the forwarding station.
4. The [DND/FOR] button will be flashing in the forwarding station and a confirmation tone will be provided if allowed.
5. All call to the forwarding station will be routed to the forwarded QSIG station.
To deactivate Net Call Forward – Follow-Me
1. At the user’s own station, Press [DND/FOR] button flashing.
2. The LED of [DND/FOR] button will be off and the call forward will be cancelled.
Feature Operation (Follow-Me Forward)
IP Net
200
Passsword: 12345
100
System A
System B

## Slide 19
The transit call is printed with a QSIG slave station number at QSIG master system
Up to 4 digits are displayed at station column
Operation
1. The station number, which makes a transit call, is printed instead of CO line number of networking path.
---- Site Name : MASTER ----------------------------------------
NO STA CO TIME START DIALED
----- --------- ------ -------- -------------- ------------------------------
0027 200 001 00:00:05 02/02/01 05:46 O85620140
QSIG Slave Station Number
Feature Operation (Centralized SMDR)
Internet
PSTN
200
Master
Notes: The station number, which makes a transit call, is printed instead of CO line number of networking path.

## Slide 20
MPB IP : 192.168. 23. 10
VOIB IP : 192. 168. 23. 11
[ (A) Admin Programming ]
PGM320-BTN1 NET ENABLE : ON
PGM322-BTN1 NET CO GRP : 01/02/03
(01:VOIB, 02:VOIB, 03:LCOB)
PGM322-BTN4 NET CO TYPE : NET/NET/PSTN
PGM324 NET NUM PLAY TABLE
- 00 : NET 1#*** (00)
- 01 : NET 2*** (01) 192.168.23.13 (CPN INFO)
02 : NET 3*** (02) 192.168.23.15 (CPN INFO)
- 03 : PSTN 9 (02) Digit Repeat : No
MPB IP : 192.168. 23. 12
VOIB IP : 192.168. 23. 13
[ (B) Admin Programming ]
PGM320-BTN1 NET ENABLE : ON
PGM322-BTN1 NET CO GRP : 01/02
(01:VOIB, 02:VOIB)
PGM322-BTN4 NET CO TYPE : NET/NET
PGM324 NET NUM PLAY TABLE
- 00 : NET 2#*** (00)
01 : NET 1*** (01) 192.168.23.11 (CPN INFO)
02 : NET 3*** (02) 192.168.23.15 (CPN INFO)
- 03 : PSTN 9 (01) 192.168.23.11 (CPN INFO)
Digit Repeat : Yes
MPB IP : 192.168. 23. 14
VOIB IP : 192.168. 23. 15
[ (C) Admin Programming ]
PGM320-BTN1 NET ENABLE : ON
PGM322-BTN1 NET CO GRP : 01/02
(01:VOIB, 02:VOIB)
PGM322-BTN4 NET CO TYPE : NET/NET
PGM324 NET NUM PLAY TABLE
- 00 : NET 3#*** (00)
- 01 : NET 1*** (01) 192.168. 23. 11 (CPN INFO)
02 : NET 2*** (02) 192.168. 23. 13 (CPN INFO)
03 : PSTN/9 (01) 192.168. 23. 11 (CPN INFO)
Digit Repeat : Yes
(A) ipLDK-60 (1***)
(B) ipLDK-60 (2***)
(C) ipLDK-60 (3***)
WAN
Internet
PSTN
Practice
VOIB
VOIB
VOIB
1000
1001
…
2000
2001
…
3000
3001
…