## Slide 1
IP TERMINALS

## Slide 2
Overview
Network Configuration
Appearance & Feature
LIP Phone Administrator
Soft Phone Administrator
Admin Programming
Installation Procedure
SIP Administrator
Contents

## Slide 3
Overview
Remote Modes
• LIP-6030D, LIP-6012D
• IP ToS, 802.1p/Q, DiffServ Pretagging
QoS Features
Security Features
• IPSec (DES/3DES, MD5/SHA-1)
NAPT Related Features
• IPKTS STUN, UDP Encapsulation of IPSec Packets
Network Environment Related Features
• PPPoE, DHCP Client

## Slide 4
Network Configuration
Network Configuration
Main Office
Internet
IP Phone
※ISP:Internet Service Provider
Phonetage
Remote Site
Tele-Worker / Biz-Traveler

## Slide 5
Appearance & Feature
LIP-6012D
LIP-6030D
[Network Services]
• QoS : 802.1p/Q, IP ToS
• Protocols : DHCP, HTTP, TFTP, FTP, DNS, Telnet
• Security : IPSec
[Audio Services]
• Voice Codec : G.711, G.723.1, G.729
• Voice Handling : Echo Cancellation, Voice Activity Detection,
Silence Suppression, Comfort Noise Generation, Error Concealment
• Speaker Phone : Full Duplex
[H/W Features]
• LCD Display : 3 x 24 Line
• Built-in Headset Jack, Desk/Wall Mount
• Power Feeding : 48V AC/DC Adaptor or PoE
• Built-in Ethernet Switch
[Operations]
• Caller ID / Caller Information Look-up / Call Log Calling
• Call Transfer / Forward / Hold / Park / Pick-up / Mute /
Redial / Message / Speed Dial / Memory Dial, etc
LIP 6000 Series - Features

## Slide 6
All Features can be used like LIP-24D/DH
Remote Connection for Worldwide Connectivity
Voice Codecs : G.711, G.723 (Voice)
Display Mode : Phone, Keyset, Calendar & Keypad Mode
Phonetage - Features
Appearance & Feature

## Slide 7
LIP 6000 Administration
LIP Phone Administration
Menu mode waiting for user input for connection environment follows after Searching VOIB fails.
Set Menu or Retry Searching VOIB ?
1. Entrance of Connection Environment Menu
2. Connection Environment Menu
Press ‘*’ button and step into connection environment progress.
To go to Next / Previous Step, press [UP/DOWN] key.
NO RESPONSE FROM MFIM[ L ]
SET[ * ] – RETRY[ # ]
2.1 Remote Mode
Change Mode to Remote
MODE [R / L] ?
[REMOTE] – CHANGE[ # ]
Press ‘#’ for change Local / Remote.
ipLDK system supports only Remote Mode

## Slide 8
LIP 6000 Administration
2.1.1 PHONE IP ADDRESS
Set the IP address of Phone
PHONE IP ADDRESS (DOT: * )
218.148.20.27
2.1.2 NETWORK ADDRESS MASK
Set network address mask
PHONE NET MASK (DOT: * )
255.255.255.0
2.1.3 NETWORK ROUTER IP ADDRESS
Set network router IP address (Gateway)
ROUTER IP ADDRESS (DOT:*)
218.148.20.30
2.1.4 MFIM IP ADDRESS
Set the IP address of VOIB
MFIM IP ADDRESS (DOT: * )
150.150.150.2
2.1.5 DEVICE NUMBER
Not Used with ipLDK system
INPUT DEVICE NUMBER :
2.1.6 USER ID
ISP authorization
USER ID :

## Slide 9
LIP 6000 Administration
2.1.7 PASSWORD
ISP authorization
PASSWORD :
2.1.8 PPPoE
Set the Network Service Connection Protocol
PPPoE ?
[DISABLED] – CHANGE [ # ]
2.1.9 DHCP
Dynamic IP assignment or not ?
If PPPoE is enabled then DHCP is enabled automatically
DHCP ?
[ENABLED] – CHANGE [ # ]
2.1.10 VLAN
VLAN Tag Set or Not
2.1.11 WEB PASSWORD
Web Page of Phone Access Password set or not ?
VLAN CONFIGURATION
[NOT SET]
WEB PASSWORD :
[NOT SET]

## Slide 10
Phonetage Administration
Phonetage Administration
1. User ID & Password.
-. enter User ID & Password
2. Select Profile for Connection
-. registration new Profile
3. OK After changing Connect the System.

## Slide 11
Admin Programming
PC Admin Programming
VOIB SLOT ASSIGNMENT for RSG/IP Phone (PGM 380)
IP Phone Port Number ASSIGNMENT (PGM 381)
LOGICAL ASSIGNMENT (PGM 103)
Setting - VOIB Slot / Channel for IP PHONE & Phonetage
Keyset Programming

## Slide 12
Admin Programming
Keyset Programming : IP Phone ATTRIBUTE 1 (PGM 386)
Register the LIP / Phonetage
PC Admin Programming
IP-Phone :
Only need MAC Address
Phonetage :
Only need ID &Passwd

## Slide 13
Installation Procedure
LIP Phone Installation Procedure on MPB
1. Insert the following boards into the ipLDK-60 System
1) VOIB
2. Power on the system (All switches of MPB are set to ON.)
3. Set the 4th DIP-switch to OFF to preserve the programming data.
4. At the admin station (100)
1) Enter the “99” on STA Board in PGM 103/BTN 2.
(“99” means virtual slot for RSG/IP Phone)
2) Reset the system for board configuration
3) Enter the VOIB Slot to be used for RSG/IP Phone in PGM 380/Btn1
4) Enter VOIB channel to be used for RSG/IP Phone in PGM 380/Btn2
5) Enter the IP Phone No. in PGM 381
6) Reset the system for board configuration
5. Re-enter the admin programming mode
1) Enter the MAC ID in PGM 386 (or User ID & Password).
2) Enter the IP Address and Gateway of VOIB in PGM 340.
6. Reset the IP Phone
** If the IP Phone No in PGM 381 or VOIB channel number in PGM 380/Btn2 is changed,
system should be reset for board reconfiguration

## Slide 14
PC Admin Programming
VOIB Mode Select for SIP/Dual (PGM 340)
CO Line Type Selection for SIP (PGM 322)
Setting - VOIB Mode / CO Channel for SIP
SIP Administration

## Slide 15
PC Admin Programming
Setting SIP Proxy Server / Domain Server
Setting SIP User Registrations (User ID, Registrations, Related Stations, … )
Setting – SIP Attributes
SIP Administration

## Slide 16
SIP Admin Programming
Register Related Stations
PC Admin Programming
Registration SIP User Table for SIP Attribute-2 (PGM 111)

## Slide 17
SIP Admin Programming
SIP CO set Enblock Mode
PC Admin Programming
Set SIP related CO enable mode (PGM 143)