## Slide 1
Online PCADMIN
Notes: This time, I will introduce online PC admin.

## Slide 2
1. Contents
Overview
PC Spec. Requirements
Connection Type
S/W Installation
Main Window
Menu
Operation
Demo & Practice
Appendix A,B
Notes: Let me introduce PC admin(Move to next page)

## Slide 3
PC Admin(On-Line)
  Is a PC-based Administration Program for ipLDK system
  Includes all kinds of keyset admin features and more enhanced features.
  Can manage the database of ipLDK system in real time from the remote site.
  Supports 3 types of connections. (Serial port, LAN, Dial Up MODEM)
  Can upgrade the MPB software from the remote site.
  Supports powerful searching engine with PGM code.
  Supports an automatic version detection.
  Supports PPP connection with Analog Line
2. Overview
Notes: PC admin is

## Slide 4
2. PC Spec. Requirements
PC Spec. Requirements
  Pentium Celleron 233MHz CPU or higher
  (Celleron 333 or more high performance CPU is recommended)
  256 color Super VGA (800*600), or higher
  At least 64MB RAM (128MB or more RAM is recommended)
  MS-Windows NT/2000/XP
  NIC(Network Interface Card) for LAN connection
  MODEM for PSTN connection (Optional)
3. PC Spec. Requirements
Notes: The following PC Spec. is required to install PC admin.
Please just refer to the requirements.(Move to next page)

## Slide 5
3. Connection Type
Connection of ipLDK System and PC
  RS-232C(Serial Cable, USB Serial Converter)
  Analog Modem (PPP connection is available)
  TCP/IP(LAN)
PSTN
LAN/WAN
RS-232C
MODU
4. Connection Type
Modem
LAN interface
LAN interface
RS-232C interface
Remote side
Local side
Notes: PC admin supports 3 kinds of connection types as shown in the picture.
RS-232C, Analog modem, LAN. (Move to next page)

## Slide 6
4. S/W Installation
1. Execute “SETUP.EXE”
2. Click [Next] button.
5. Change Directory to be installed.
6. Click [Next] button.
3. Enter User Name and Company Name,
4. Click [Next] button.
7. Click [Finish] button.
PC Admin S/W Installation
5. S/W Installation
Notes: This page shows how to install PC admin.
The installation is not difficult.
Execute setup.exe and then just follow the indication as described in the page.(Move to next page)

## Slide 7
System Message,
System IP & Connection Status
6. Main Window
Main Menu
Basic System Information
Main Admin Menu
Sub Admin Menu
Notes: This page shows the PC admin main window
This window is after connection is established.
PC admin is composed of main menu, basic system information field, admin main menu and sub menu, admin window, message.
I will explain more details from next page. (Move to next page)

## Slide 8
Main Admin Menu
Sub Admin Menu
Admin information Window
Admin Menu
All of admin menu is structured in a tree shape
A related sub admin menus are appeared at the right side of the tree when you click
main admin menu
The information of sub admin menu is displayed at the right side by double click of mouse.
6. Main Window
Notes: This page shows the PC admin main window
PC admin is composed of main menu, basic system information field, admin menu, admin window, message.
I will explain more details from next page. (Move to next page)

## Slide 9
Basic System Information
System : ipLDK System Model
MPB : MPB Software Version and Compiled Date
Connect LED : Connection Status between PC Admin and ipLDK system
Tx/Rx LED : This LED will be turned on when PCADM sends or receives data from ipLDK system.
PC ADM : PC Admin Version and Compiled Date
Nation Code and Site Name : Nation code and site name are shown according to Information
defined in the Location Information (PGM 100)
7. Menu
Notes: Let’s see basic system information field first.
Basic system information shows the following information.
System field shows a kind of LDK system model
(Move to next page)

## Slide 10
File  Connect/Disconnect/Exit
Connect : This menu is for Fast Connection to the site visited last
Disconnect : Disconnection from the system
Exit : Close PC Admin
7. Menu
Notes: Let’s see file menu.
Connect is used to do fast connection to the site visited last.
Connect is to connect the site that just you access before.
Disconnect is used to disconnect the disconnection from the system
Exit is used to close PC Admin.(Move to next page)

## Slide 11
Tools  Site Information/User Management/Level Management
Site Information : Register site with detailed information
User Management : Register PC Admin User, Password and available Level
Level Management : Register Levels
7. Menu
Notes: Let’s see Tools menu.
There are 3 lower menus; site information, user management, level management.
In the site information, we can register site with detailed information
In the user management, we can register pc admin user and password with available level.
In the level management, we can register a level defined in user management. In this menu, we can assign menus
Those should be hided. There is one important thing. Except level 1, other level number does not mean priority.
User management and Level management are shown only for level 1 user.
In other words, user whose level is not level 1 cannot see these two menus.
I will explain again these windows in next presentation.
(Move to next page)

## Slide 12
Site Information
PC Admin can save simple site information and we can connect to the site directly with this list.
[Tools]  [Site Information]
Press [New] button to add site.
Press [OK] button each after entering
site information.
Press [Save] button to save site information
7. Menu
Related file: “sitelist.cds” and “sitelist_detail.cds”.
Notes: With this window, we can edit site information that we want to connection.
If you add your customer site information, it will be very helpful to you when you connect the site.
We can also save this information as file. If you save this information, two files will be created.
One is “sitelist.cds” and another is “sitelist_detail.cds”. These files should be backed up for emergency case.
(Move to next page)
Site 수는 몇 개까지 등록 할 수 있을까?

## Slide 13
User Management
PC Admin supports multiple users with different level.
[Tools]  [User Management]
Press [New] button to add user. Then you will see some dialog box with below order.
 User ID / Password / Level(0~99)
Press the [OK] button each after entering User ID, Password and Level.
Press [Save] button to save changes.
User Management
Menu
7. Menu
Notes: We can manage the access level with different level in this window.
In this window, you can add/delete/Modify the user information.
Default ID is administrator with level 1.
After add new user, you can delete administrator for security. But you cannot recover administrator again after deleting the account.
In such emergency case, you should install again to recover administrator account.
(Move to next page)
Level 1인 user ID를 등록 할 수 있을까?
User ID는 몇 개까지 등록 할 수 있을까?

## Slide 14
Level Management
PC Admin supports multi level of users. Administrator has the highest priority.
[Tools]  [Level Management]
Press [New] button to assign new level
Select the level that you want to add.
Select the features to be disabled
with assigned level.
Press [save] button to save changes.
Level Management
Menu
7. Menu
Notes: This window is very important because we can manage access items with different level.
You should keep in mind that the level 2-99 does not mean the priority. If you want to use the number as priority, you can use it.
Basically, the level number does not mean priority.
If you want to add new level, select level number. If level number is selected, we can hide some menu to the user with selected level.
Right side displays all menus of PCADM. Select the menu and click right button. Then selected menu will be added in left side.
The menus in right side will not be displayed to user with this level.
Menu selection can be done with submenu unit.(?)

## Slide 15
Option  Language
Language : Change PC Admin Language (English and Local Language)
-. Default language is English.
-. The local language can be defined by editing “common.txt and menu.txt ”.
Default File Location  [C:\Program Files\LG Nortel\LDK-PCADMIN\Define]
-. If you backup this file, you can use this file in emergency case.
7. Menu
Notes: Let’s see option menu.
We can change PC admin language. Default language is English.
The local language can be defined by editing a related language txt file, but it is not supported yet.

## Slide 16
ipLDK Utility
PC Admin includes the following utilities;
ipLDK DB Upload Download / ipLDK Remote Diagnostic
/ ipLDK Upgrade / ipLDK Speed Editor path
7. Menu
Notes: Let’s see the LDK utility menu.
There are LDK db up/download menu, remote diagnostic menu, LDK s/w upgrade menu and speed editor path.
(Move to next page)

## Slide 17
Help  About
This menu shows PC Admin general information.
7. Menu
Notes: In the help menu, pc admin general information is displayed.(Move to next page)

## Slide 18
PC Admin Program Execution
  Execute PC admin software, and then “Login Dialog” box shows up.
  Input User ID and Password( Default ID : administrator , Password : 0000 )
  Press the [OK] button, then the main window of PC Admin shows up.
Main Window-Disconnected
Login Dialog
8. Operation
Notes: Now, let’s execute PC admin.
First, execute PCadmin.exe and then Login Dialog box shows up.
(Move to next page)

## Slide 19
Site Information
Open Site Information [Tools]  [Site Information]
Select a site and click mouse right button.
Select and click one of connection types.
Input System Admin Password(PGM 162) and click [OK] button.
The connection between PC Admin and ipLDK system is established.
8. Operation

## Slide 20
Main Window-Connection Status
8. Operation
Notes: When the connection is established, the main window show up like this.

## Slide 21
Advantages…
  Upgrade MPB software without going to the site.
  Save cost and time for going to the site
  Protect the database of MPB during upgrade process
  3 type connection are supported(Serial port, MODEM, TCPIP)
  PPP can be used for Modem.
  Faster process speed
Things that you should keep in mind.
  During receiving the data into DRAM, it will not affect the system operation.(Step 1)
  During writing into the Flash ROM, don’t touch the ipLDK
  system.(Step 2)  Very important !!
  After finishing the whole process, ipLDK system will reset automatically.
  After the system is restarted, we can use the ipLDK system without additional job.
9. Remote Software Upgrade

## Slide 22
Step 1 . Select the system and connection type
1. Select the system
2. Select connection type
3. Check Information and Click Next
① Destination
- Phone number(MODEM)
- IP Address(TCP/IP connection)
② Admin Password
If not programmed, leave it empty.
③ Binary file location
10. Process Diagram for Remote Software Upgrade
①
②
③

## Slide 23
Step 2 : Data Transferring Process
4. Summary Window
If you press [Start] button, the transfer window will be display as like right window.
TCP/IP or PPP connection :
Zmodem protocol is not used
Modem/Serial connection:
Zmodem protocol is used.
10. Process Diagram for Remote Software Upgrade

## Slide 24
Step 3 : Finishing process
If you success transferring and verification, ipLDK
system will disconnect the channel and start
programming Flash ROM.
At this time, don’t touch anything on the system.
After programming, ipLDK system restart automatically.
If you fail transferring or verification, upgrade software will stop transferring process and
display window as like below.
If you want to try again, press [Yes]. But if you don’t want to do, select [No] button.
10. Process Diagram for Remote Software Upgrade
Yes

## Slide 25
Advantages…
  Database Backup for emergence case
  Downloaded DB file can be edited by special program(Off line PC Admin)
  Save time and cost to program.
  Download DB file  Edit DB  Upload DB
  When mistake is occurred during DB programming, restore the downloaded DB file.
  3 type connection are supported(Serial port, MODEM, TCPIP)
  PPP can be used for Modem
  Faster process speed(Only for TCPIP)
Things that you should keep in mind.(Important)
  During downloading the DB from ipLDK system, it will not affect the system operation.
  During uploading into the protected memory, don’t change anything
  in admin item with PC Admin or keyset admin.
  After finishing the upload process, ipLDK system will be reset automatically if you
  selected reset (Recommended) . But if you don’t select reset, ipLDK system will not be reset.
11. DB Upload/download software

## Slide 26
Step 1 . Select the system and connection
1. Select the system
2. Select connection type and operation(download or upload)
3. Check Information and Click Next
① Destination
- Phone number(MODEM)
- IP Address(TCP/IP connection)
② Admin Password
- If not programmed, leave it empty.
③ DB file location
④ Enable this feature in order to reset system
automatically after DB upload finished.
11. Process Diagram for DB up/download
①
②
③
④

## Slide 27
Step 2 : Data Transferring Process(Same as remote Upgrade)
Monitor window
Summary Window
If you press [Start] button, the transfer window will be displayed.
11. Process Diagram for DB up/download

## Slide 28
Step 3 : Finishing process
If you success transferring or verification, DB up/download software will stop process
and display window as like below.
DB up/download software is very similar to the remote upgrade software except the
operation type selection.
So, you will be used to using the two type software with no difficulty.
11. Process Diagram for DB up/download

## Slide 29
Demo & Practice
Install PC Admin S/W
Connecting PC Admin to system
Showing how PC admin works
Practice
12. Demo & Practice
Notes: Now, I will show you how to install PC admin s/w and how it works.
After then, you will do a practice.

## Slide 30
Port Related Program
  -. PGM108 : LAN Configuration (IP address, Gateway address)
  -. PGM170 : Modem Configuration (Station or CO), DID Table.
  -. PGM174 : Serial (MODEM) port speed configuration
    Serial connection : Max 19200bps , Modem Connection : Max 9600bps
Serial and Modem Connection Trouble Shooting
  -. Connection Fail : PGM 174
  -. Data Error : Re-connect after 1~2 Minutes
LAN Connection Trouble Shooting
-. Connection Fail : Check PGM 108
1) ipLDK system should have IP address for LAN connection. So, check PGM108
    2) WAN Connection Fail : Check NAT/PAT and firewall of the site.
  -. Channel disconnection : Re-connect after 1~2 Minutes
  -. Heavy traffic : In some case(Ex : virus), heavy traffic may produce communication error
  in the network.
Appendix A. Trouble shooting

## Slide 31
Logon Fail
-. Check there is another admin or not, Check password
-. Check Connection manager Dialog Box
- Kill the pcadm.exe in task manager using CTRL+ALT+DEL or Exit and restart the LDK PCADM.
Backup and Restore User Management Data
-. Copy attribute.cds in installed directory.
-. Restore copied file when you need
Backup and Restore User Management Data
-. Copy Lmaster.cds and Ldetail.cds in installation directory.
-. When this backup is needed?
Case 1 : When you want restore the database after installing the PCADM again.
Case 2 : When you want to setup the same level data to various customer. In other words,
you can fix several levels and apply this configuration to all customer.
Appendix A. Trouble shooting

## Slide 32
Integrated in PCADM
  Remote Upgrade and DB updown are integrated in one package.
  User can execute each utility in menu.
  If you want to execute each utility without PCADM, user can execute them separately.
  PPP can be used for Modem
  Faster process speed
Appendix B. LDK Utilities