## Slide 1
Offline PCADMIN

## Slide 2
1. Contents
Overview
PC Requirement
Version Compatibility
S/W Installation
Program Window
Procedure
Menu Operation
Demo & Practice
Notes: Let me introduce PC admin(Move to next page)

## Slide 3
1. Overview
2. Overview
PC Admin(Off-Line)
  Is a software of ‘Administration Program’ for ipLDK system using “*.usr” file
  downloaded by DB Up/Download Program indirectly.
  Be used without the connection between ipLDK system.
  Change the value of database in “*.usr” file and Upload the database with DB
  Up/Download Program in the LDK-Admin package.
  Supports powerful searching engine for PGM code.
Notes: PC admin is
PC admin can manage all LDK system series.(Move to next page)

## Slide 4
2. PC Spec. Requirements
3. PC Requirements
  Pentium III CPU 550Mhz CPU or higher(recommended)
  At least 64MB RAM (128MB or more RAM is recommended)
  Minimum 3-button Mouse/ VGA Monitor
  MS-Window 98 at least
  HDD(20MB at least)
Notes: The following PC Spec. is required to install PC admin.
Please just refer to the requirements.(Move to next page)

## Slide 5
3. Connection Type
4. Version Compatibility
PC AdminPro isn’t compatible with every MP version.
So, we should use the PCAdminPro version compatible with MP Version.
When you open the user file(*.usr) and the user file is the one of old version, we will see
the warning message. And, we cannot update the user file and some value of admin field
may be incorrect.
Regardless of installation the old PC AdminPro version, we can install new PC AdminPro
version. If we don’t want to use old PC AdminPro version, please delete the version
before installing new PC AdminPro version.
Notes: PC admin supports 4 kinds of connection type as shown in the picture.
RS-232C, Analog modem, ISDN, LAN. (Move to next page)

## Slide 6
4. S/W Installation
5. S/W Installation
1. Execute “SETUP.EXE”
2. Click [Next] button.
5. Change Directory to be installed.
6. Click [Next] button.
3. Enter User Name and Company Name,
4. Click [Next] button.
7. Click [Finish] button.
PC AdminPro S/W Installation
Notes: This page shows how to install PC admin.
The installation is not difficult.
Execute setup.exe and then just follow the indication as described in the page.(Move to next page)

## Slide 7
6. Procedure
database file(*.usr)
With DB-Updown Program
(Modem/LAN/Serial)
PC with PCAdminPro software
Download
Upload
(with updated database file)
(1)
(2)
(3)
(4)
Notes: This page shows the PC admin main window
PC admin is composed of main menu, basic system information field, admin menu, admin window, message.
I will explain more details from next page. (Move to next page)

## Slide 8
7. Menu Operation
- Open DB File
Open database file from ‘Load File’ Window.
- Save File
To save information to file, click ‘Save File’
button and save file.
Notes: Let’s see basic system information field first.
Basic system information shows the following information.
System field shows a kind of LDK system model
(Move to next page)

## Slide 9
- View DB
To Read data Click ‘Refresh’ button. Information is displayed in detail.
- Update DB
To update DB, change attribute value and click ‘Update’ button. DB is saved to memory.
7. Menu Operation