## Slide 1
SPEED EDITOR

## Slide 2
Overview
LDK-Speed Editor with LAN
Major Features
File Menu
Connection
File Transfer
Editing
Demo & Practice
Contents
Notes: Let me introduce PC admin(Move to next page)

## Slide 3
1. Overview
1. Overview
ipLDK Speed Editor is …
  A MS-Windows application program that can download, edit, and upload speed data of ipLDK system.
  This program can send and receive the speed information such as speed bin no, speed bin name, phone number, co line type, and co number.
The system requirements for using this program are as follows.
  LAN Port is used on BMBU for LAN connection.
    Same port number with ez-Attendant is used.
    So, can’t use ez-Attendant and Speed Editor simultaneously.
  Unique IP Address should be assigned for LAN connection.
  Pentium Celeron 233MHz CPU or Higher CPU
  At least 32MB RAM
  MS-Windows 98/ME/2000/XP
Notes: PC admin is
PC admin can manage all LDK system series.(Move to next page)

## Slide 4
2. PC Spec. Requirements
LAN Connection
  Speed : 10/100Mpbs
  PGM 175 – FLEX10 – Set to NET_PCATD (Default value)
Hub in your office
Connection in PC and MPB with same hub
Connection in PC and ipLDK with different hub
in same segment
Hub A
Hub B
Ethernet
2.ipLDK Speed Editor with LAN
Notes: The following PC Spec. is required to install PC admin.
Please just refer to the requirements.(Move to next page)

## Slide 5
3. ipLDK Speed Editor – Major features
Main Menu Tree
Sub Menu Tree
(1 PGM Number Base)
Main Menu
Editing Area
Major Features
1) Uploading speed bin data to ipLDK System
2) Downloading speed bin data from ipLDK System
3) Editing speed bin data (MS Excel and Text file)
Notes: PC admin supports 4 kinds of connection type as shown in the picture.
RS-232C, Analog modem, ISDN, LAN. (Move to next page)

## Slide 6
4. S/W Installation
[File] menu includes [New], [Open File], [Save File].
4. ipLDK Speed Editor – [File] Menu
Notes: This page shows how to install PC admin.
The installation is not difficult.
Execute setup.exe and then just follow the indication as described in the page.(Move to next page)

## Slide 7
4. ipLDK Speed Editor – [File] Menu
[Open File] Sub-menu
Procedures:
1. Select [Open File] sub-menu in [File] menu. => [Open] Dialog shows up.
2. Select the file type, text, excel
3. Click [OK] button.
[Save File] Sub-menu
Procedures:
1. Select [Save File] sub-menu in [File] menu. => [Save] Dialog shows up.
2. Select the file type, text, excel
3. Click [OK] button.
[New] Sub-menu
Procedures:
1. Select [New] sub-menu in [File] menu.
2. Enter the range you want to edit.
3. Click [OK] button.
Notes: This page shows the PC admin main window
PC admin is composed of main menu, basic system information field, admin menu, admin window, message.
I will explain more details from next page. (Move to next page)

## Slide 8
This program can be connected to LDK system via LAN
* ipLDK Speed Editor uses the same port as ez-Attendant.
* Prior to use the program you must check Admin PGM 175 – FLEX 10 (NET PCATD) – Default value
* If the ez-Attendant is connected to the system, you can’t connect to the system using the Speed Editor
until the ez-Attendant is disconnected.
* Unlike ez-Attendant, ipLDK Speed Editor doesn’t need a lock key to use the system.
5. ipLDK Speed Editor – [Connection] Menu
Notes: This page shows the PC admin main window
PC admin is composed of main menu, basic system information field, admin menu, admin window, message.
I will explain more details from next page. (Move to next page)

## Slide 9
6. ipLDK Speed Editor – [File Transfer] Menu - Upload
Procedure:
1. Select [Upload] sub-menu in [File Transfer] menu.
2. Select [Browse], and select a file to upload.
3. Click [OK] button.
Notes: Let’s see basic system information field first.
Basic system information shows the following information.
System field shows a kind of LDK system model
(Move to next page)

## Slide 10
6. ipLDK Speed Editor – [File Transfer] Menu - Download
Procedure:
1. Select [Download] sub-menu in [File Transfer] menu.
2. Select Range. If you select User Specified, enter the range below.
3. Select [Browse], and name a file you want the speed data to be saved.
4. Click [OK] button to start download.
Notes: Let’s see file menu.
Connect is used to do fast connection to the site visited last.
Disconnect is used to disconnect the disconnection from the system
Exit is used to close PC Admin.(Move to next page)

## Slide 11
7. ipLDK Speed Editor – Editing Data – in Speed Editor View
Procedure:
1. Click on an empty cell.
2. Type the data and press [tab] to move on to next column or click on.
3. Select [Save File] sub-menu in [File] menu. => [Save] Dialog shows up.
4. Select the file type, text, excel
5. Click [OK] button.
** You must enter the correct CO Number.
System CO Line CO Group
ipLDK 1 - 36 1-24
Notes: Let’s see Tools menu.
There are 3 lower menus; site information, user management, level management.
In the site information, we can register site with detailed information
In the user management, we can register pc admin user and password with available level.
In the level management, we can register a level defined in user management.(Move to next page)

## Slide 12
7. ipLDK Speed Editor – Editing Data – Text File
Procedure:
1. Open the file you want to edit using Notepad or
MS-Word.
2. file format looks as example.
3. The number 11 on the first line represents
the total number of speed data in this file.
4. Each item is separated by a separator ’ | ‘
- Speed No|Speed Name|CO Line Type|
CO Number|Phone Number
5. When you write CO Line Type ( “CO Line”,
“CO Group” and “None”), keep an
1 empty space between CO and Line,
between CO and Group.
* Don’t exceed 16 characters when entering Speed Name.
* Don’t exceed 24 characters when entering Phone Number.
* Recommend to edit in speed editor view.

## Slide 13
7. ipLDK Speed Editor – Editing Data – Excel File
Procedure:
1. Open the file you want to edit using excel.
2. file format looks as below.
3. Click a cell to edit.
4. Type data in. Be careful that you should type ‘ before every data, for example ‘5, not just 5.
5. When you write CO Line Type( “CO Line”, “CO Group” and “None”), keep an
1 empty space between CO and Line, between CO and Group.
* Don’t exceed 16 characters when entering Speed Name.
* Don’t exceed 24 characters when entering Phone Number.
* Recommend to edit in speed editor view.