## Slide 1
LG-NORTEL TSP

## Slide 2
Overview
PC Spec. Requirements
Connection Type
S/W Installation
Demo & Practice
Contents
Notes: Let me introduce PC admin(Move to next page)

## Slide 3
1. Overview
TSP (Telephony Service Provider)
  Made by Telephony System Vendors
  Dynamic Link Library (DLL)
  The File Extension is *.tsp and the File is stored in System directory.
1. Overview
LG-Nortel TSP
  Made by LG-Nortel Co.Ltd.
  The File Name of LG-Nortel TSP is Lgnsp.tsp
  The TSP Supports TAPI Version 2.1
  1st party Connection and 3rd Party Connection is supported.
Notes: PC admin is
PC admin can manage all LDK system series.(Move to next page)

## Slide 4
1. Overview
TAPI Application
  Made by S/W Program vendors
  Use TAPI functions like lineMakeCall, lineAnswer
  Ex) Microsoft Outlook, ez Phone, Call Center Program
1. Overview
TAPI (Telephony Application Programming Interface)
  Made by Microsoft
  Included in Windows 98/2000/XP
  TAPI functions (lineMakeCall, lineAnswer etc.)

## Slide 5
Server Computer
  CPU: Pentium III 500MHz or higher
  RAM: 128 MB or higher
  Available Hard Disk: 500 MB or higher
2. PC Spec. Requirements
Client Computer
  CPU: Pentium II 200MHz or higher
  RAM: 32 MB or higher
  Available Hard Disk: 200 MB or higher
Notes: The following PC Spec. is required to install PC admin.
Please just refer to the requirements.(Move to next page)

## Slide 6
3. Connection Type
3. Connection Type
LGN TSP
TAPI application
TAPI v2.1
TAPI Client
LAN
Structure (1st Party Connection)
TAPI Client

## Slide 7
3. Connection Type
1st Party Connection
  PC is connected to the ipLDK-60 system via LAN.
  PC User can use the keyset assigned by Admin PGM (126).
  LG-Nortel TSP is installed on the Client Computer.
  Windows 98 or higher is available.
3. Connection Type
LGN TSP installed(1st)
Keyset: DKT/SLT
PC: Windows
98/2000/XP
LAN
Notes: PC admin supports 4 kinds of connection type as shown in the picture.
RS-232C, Analog modem, ISDN, LAN. (Move to next page)

## Slide 8
3. Connection Type
3. Connection Type
Structure (3rd Party Connection)
TSP v2.1
TAPI v2.1
TAPI application
LAN
LGN TSP
Remote SP
LAN
TAPI application
TAPI v2.1
TAPI Client
TAPI Server

## Slide 9
3. Connection Type
3rd Party Connection
  Server/Client Structure.
  The TSP is installed on the Server Computer (Windows 2000/2003 Server).
  The Server assigns the lines to clients.
  Client Computers use RSP
  (Remote Service Provider) or Proprietary protocol .
3. Connection Type
Server: Windows
2000/2003 Server
LGN TSP installed(3rd)
LAN
Client: Windows
98/2000/XP
Client: Windows
98/2000/XP
Keyset: DKT, SLT
Keyset: DKT, SLT
LAN

## Slide 10
4. S/W Installation
1. Execute “SETUP.EXE”
2. Click [Next] button.
3. Select Service Mode, and Type IP Address of ipLDK-60
4. Click [Next] button.
LG-Nortel TSP S/W Installation
4. S/W Installation

## Slide 11
4. S/W Installation
4. S/W Installation
5. Restart you Computer

## Slide 12
Demo & Practice
1st Party Connection
5. Demo & Practice
Notes: This page shows the PC admin main window
PC admin is composed of main menu, basic system information field, admin menu, admin window, message.
I will explain more details from next page. (Move to next page)

## Slide 13
Procedures
1st party lock key or ez Phone lock key is needed.
In PGM (126), you can insert IP Address of client computers.
Install LG-Nortel TSP. Restart your computer. (Windows 98/2000/XP)
Open [Phone and Modem Options] in Control Panel.
Select Country/region , and type area code and a number to access an outside line.
5. 1st party connection
Notes: This page shows the PC admin main window
PC admin is composed of main menu, basic system information field, admin menu, admin window, message.
I will explain more details from next page. (Move to next page)

## Slide 14
Procedures
On the [Advanced] tab under Providers, click [LG-Nortel TAPI Service Provider].
Click [Configure…].
You can change configurations in this dialog.
Verify System IP Address.
Verify Service Mode [1st Party Connection].
5. 1st party connection
Notes: Let’s see basic system information field first.
Basic system information shows the following information.
System field shows a kind of LDK system model
(Move to next page)

## Slide 15
Make a call using Microsoft outlook.
Run Microsoft Outlook.
Select [Contact].
5. 1st party connection
Click phone Tool bar. Click phone dialer option

## Slide 16
Make a call using Microsoft outlook.
Select phone number. Click OK.
5. 1st party connection
Insert phone number to make and click make a call

## Slide 17
Procedures
3rd party lock key is needed.
On the [Advanced] tab under Providers, click [LG-Nortel TAPI Service Provider].
Click [Configure…].
Select Service Mode [3rd Party Connection]. Click [Apply] button.
Restart your computer.
5. 3rd party connection

## Slide 18
Using Windows 2000/2003 Server and RSP (Remote Service Provider)
LG-Nortel TSP is installed on the Windows 2000/2003 Server
Open Telephony. Type tapimgmt.msc
In the console tree, click Telephony Service Provider for LG-Nortel System.
5. 3rd party connection

## Slide 19
Client Computer
Open a Command Prompt window.
Type tcmsetup /c server computer name.
Ex) tcmsetup /c lgtscserver
5. 3rd party connection

## Slide 20
Proprietary protocol between server and client
LG-Nortel TSP is installed on the Windows 2000/2003 Server or Windows 2000 Pro etc.
Proprietary protocol between server and client is used.
All of Korean call center maker uses this method.
5. 3rd party connection