## Slide 1
ezPhone

## Slide 2
1. Overview
2. Configuration
3. Requirement
4. Connection
5. Major Features
6. Installations
7. Window Description
8. Call Related Features
9. PC Related Features
Contents
Notes: We will introduce ezPhone with the following order.
본문

## Slide 3
1. Overview
Provides easy & powerful control of voice communications on your PC
ezPhone is Easy installed, maintained, graphical, user interface
ezPhone has 2 kinds of packages (Entry, Deluxe)
Provides Powerful features like SMS to extension
ezPhone is Compatible to MS Outlook, ACT, GoldMine and more
ezPhone follows Standard interface : TAPI
Notes: 본문

## Slide 4
1. Overview
There are two types of ez Phone version. One is an entry, the other is a deluxe.
Please refer to the below table for each version’s function.
Entry
Deluxe
Local DB, Capacity Limit
Basic DKTU feature
DB Conversion
SMS to Keyset
Attendant Integration
All Features of Entry Version
Import DB (outlook)
Export DB (outlook)
VMIB control
- MsgWait
- OutMessage
- Paging Message
Flex button assignment
ACNR
E-MAIL
All features for Outlook are available.
(Outlook Contact)
Differential ring by CLI
Scheduled Dial
KeySet SMS
Call Filtering
- VIP/Black List by DND/FWD/Ring
Concept
Functionality
New Database Creation
- Access
- Excel
Call Control
- Make Call
- Hold Call
- Park/Unpark
- Transfer
Import DB (Access, Excel)
Export DB (Access, Excel)
Print Address book
Forward(Internal, Off-net, VMIB)
Always on top
All features for Outlook are not
available.
Notes: There are two types of ez Phone version.
One is an entry, the other is a deluxe.
The entry version have a limit of capacity and local DB.
The deluxe version provides DB conversion,
SMS to Keyset and Attendant Integration.
The following features are provided per each package

## Slide 5
2. Configuration
TSP
Server
LAN
LDK System
PSTN
VOIP
ezPhone
ezPhone
Notes: As you can see, ezPhone is connected to LAN.

## Slide 6
PC : Win 98 or Higher ez Phone Program(CTI Application)
DAO35Registor.exe
Required to install LG TAPI-driver packed together
Operating System : Win 98, Window NT, Window 2000
Win ME, Window XP home/pro.
Processor : Minimum Pentium III 300 MHz
RAM : 128 MB (Min. 64MB)
Available Hard Space : 200 MB
Video Card : SVGA(Min. 256 colors/800x600)
3. Requirement
H/W
Requirements
S/W
Requirements
Notes: We need the following h/w and s/w requirement that the ezPhone is installed.

## Slide 7
4. Connections(1/2)
The following Figure shows the 1st party Interface of LDK system.
IP Address for PC should be installed in PGM 126 Station IP List.
LDK TSP installed(1st)
IP Address B
LAN port on BMBU
IP Address A
Station (DKTU or SLT)
Notes: LDK provides 1st and 3rd party for TSP server.
It shows the 1st party interface.
We need a CTIU module for 1st party connection.

## Slide 8
4. Connections(2/2)
Server : Windows NT/
2000 Server
LDK TSP installed(3rd)
LDK serial port Or LAN
Client : Windows
98/NT/2000/XP
Client : Windows
98/NT/2000/XP
DKT/SLT
Keyset : DKT/SLT
Windows Domain
LAN
Control Path
Server is connected to the LDK system through serial port or LAN.
Server user can use all keysets connected to the LDK system.
Client user can use his keyset assigned by Server PC.
TAPI Server should set each user for
ez Phone line assignment.
This setting should be needed an
expert for TAPI server management
3rd Party
The following Figure shows the 3rd party Interface of LDK system.
DKT/SLT
Notes: It shows the 3rd party interface.
The TSP server is connected to LAN
and communicate with LDK system.

## Slide 9
Local Language Translation : User can change the local language text easily
Using User DB(Deluxe Version Only) : MS Outlook, Access, Symantec ACT, Goldmine
Key Pad & Mouse operation
User can define each key with feature in option window.
This is flexible configuration.
SMS Message(PC to DKT:48 character)
From PC to DKTU : Possible
From DKTU to PC : Not possible
SMS between PC Phones : PC to PC, like MSN Messenger(Deluxe Version Only)
Caller Information Display : Call History(Call Log view feature)
Powerful Graphic User Interface
Differential ring by CLI
VMIB Control, ACNR
Call Filtering : VIP/Black List
Attendant Integration(Deluxe Version Only)
 Scheduled Dial(Deluxe Version Only)
5. Major Features
Notes: ezPhone provides the following major features.
본문

## Slide 10
6. Installations
You must Setup TSP File First. Please refer to TAPI part.
And setup ezPhone.
Select ‘Next’.
Notes: Ok! Let’s see the software installation of ezPhone.
We should install LDK TSP software first.
Just follow the installation procedure.
After finishing the TSP s/w installation,
we should reboot the server.

## Slide 11
Enter ‘User Name’ and ‘Organization’ and select ‘Next’.
6. Installations
Select ezPhone type.

## Slide 12
6. Installations
Confirm folder and select ‘Next’.
Select ‘Install’.

## Slide 13
6. Installations
Select ‘Finish’.

## Slide 14
‘ezPhone’ is shown.
6. Installations

## Slide 15
6. Installations
Start Button  Setup  Control Panel  Phone and Modem Options  Dialing Rules
Loop Code should be set in your desktop PC for making external call. (Both of 1st and 3rd party)
LDK system adds this number when making CO line Call.
This is very important to make CO line call with ‘ez Phone’ or other TAPI Client.
Numbers which are saved in your address book of ez Phone should be more than 6 digits.
* Input one digit [LOOP] number.
ex) In Korea, Loop Number is ‘9’
Notes: After rebooting the server,
we need to check if TSP is installed normally
in the control panel of the server.

## Slide 16
6. Installations – 3rd Party Server side
Enabling TSP Server
1. To open Telephony on Windows 2000/2003 Server,
1) Click Start  Run
2) Type tapimgmt.msc
2. In the Action menu, click Properties.
3. On the Setup tab,
select the Enable telephony server check box
to enable the server the server.
Notes: After rebooting the server,
we need to check if TSP is installed normally
in the control panel of the server.

## Slide 17
Assigning a ez Phone user to a line or phone
1. Open Telephony
2. In the console tree, click Telephony Service Provider for LG System.
3. In the details pane, under Line Name or Phone Name, click the line or phone.
4. In the Action menu, click Edit Users, and then click Add.
5. In Look in, click the domain containing the user.
6. In the list, select the user, and then click Add.
This procedure permits TAPI client programs run by the user to use the line or phone on the server.
A user added for a phone or line must be in the same domain as the TAPI server
or in a domain that has a two-way trust relationship with the domain containing the server.
Before a user can use the telephony line or phone, the TAPI server must be specified on the client computer.
6. Installations – 3rd Party Server side
Notes: After rebooting the server,
we need to check if TSP is installed normally
in the control panel of the server.

## Slide 18
ez Phone Setup
1. Open a Command Prompt window.
2. Type [tcmsetup /c servername]
Ex) In case that a server name is “QE2000server”
tcmsetup /c qe2000server
To specify telephony servers on a client computer
Windows 2000/XP
Client disable from telephony servers
1. Open a Command Prompt window.
2. Type [tcmsetup /c /d]
6. Installations – 3rd Party Client side
Notes: After finishing the ezPhone installation,
we recommend you to reboot the computer
before executing the ezPhone program.

## Slide 19
7. Window Description
Top Tool Bar
Icon Menu(bottom)
Call Window
Station Information Window
(Double Click & Call)
Information Window
Message Window
MS Scheduler
Display Station Type Optional(Icon/List/Report/Small Icon)
Main Window
Main Menu
Notes: This is the ezPhone main window.
Main window consists of Main Menu, Top Tool Bar, Call Window,
Information Window, Message Window, MS Scheduler,
Station Information Window and Icon Menu.

## Slide 20
Main Menu
7. Window Description
Notes: The main menu consists of File, Program, Tools and About.
File menu has these kinds of sub menu.
DB Convert, Print option, and Exit.
Program menu has these kinds of sub menu.
TSP Setting, Language Setting, Forward, VMIB Control,
Flex Btn Assignment, Conference Room, SMS
and My Station Program.
Tools menu has these kinds of sub menu.
Send SMS Mobile, Short Cut Display, Key mapping,
Customize, Option, TaskBar Tray Icon and Always On Top.
Finally in the About, you can see the information of ezPhone.

## Slide 21
Open Outlook
Log
On/Off
Top Toolbar
7. Window Description
Print for Address Book
Notes: This is Top Toolbar.
These features are the same as ezATD.

## Slide 22
Field Option
Filtering
Status
Station Information Windows
7. Window Description
Notes: The station information window provides station info,
address book, log view and schedule dial.
Address book and log view features are the same as ezATD.
I will explain Station info and schedule dial next page.

## Slide 23
2. Display Station Type(ICON)
3. Display Station Type(SMALL ICON)
Display Station
 Can display station more
4. Display Station Type(LIST)
(Double Click & Call)
1. Display Station Type(REPORT)
Display Station Type
7. Window Description
Notes: Station info provides 4 display types;
Report type, icon type, small icon type and list type.

## Slide 24
8. Call Related Features
Call Queuing / Answering Incoming Call
- ICM/CO Line Incoming Call
- Hold State Call
- Transfer / Hold / Park Recall : Has Recent via History
Transferring Call
- Unscreened / Screened Transfer
Making Outgoing Call
- Station Information Window
- Address Book
- Use Log View
Call Park and Retrieve
Conference Room
ACNR(Automatic Call Number Redial)
Forward / DND
Record VMIB
Flexible Button Assignment
Receive Keyset SMS
Call Related Features
Notes: ezATD provides the following call related features.

## Slide 25
9. PC Related Features
Address Book
- Manages Internal User / Customers
- When Incoming Call, Searches Information on Phone Book
DB Converting
- Importing/Exporting(MS-Outlook, MS-Access, MS-Excel, ACT! , Goldmine)
Log View
Schedule Dial
SMS
Customize
Pop up Window
Black List Call Filtering
PC Related Features
Notes: ezATD provides the following PC related features.