## Slide 1
ezAttendant

## Slide 2
1. Overview
2. Requirements
3. Installation
4. Execution of ez Attendant
5. Main Window
6. Menu Description
7. Call Related Feature
8. PC Related Feature
Contents

## Slide 3
Overview
ez Attendant software can manage the various type of call with your PC.
When the attendant works with another type of working
(for example, word processing), the attendant can minimize this software
with button.
If an incoming call is occurred during the word processing, the pop up
windows will be activated with simple information about the caller.
At that time, attendant should do its own operation.
And the call related operation is depending on the LDK system feature.
For example, the capacity of queue size or recall timer are depend on the
LDK system itself.
But PC related features are independent with LDK system.
Notes: <number>
<footer>
<header>
<date/time>
본문

## Slide 4
Operating System : Window 2000/XP
Processor : Minimum Pentium III 800 MHz or Higher
Memory : 256 MB or much more DRAM
Available Hard Space : 100 MB
Monitor : 17’’ Monitor(19’’ Recommended)
Resolution : 1024 x 768(Default), Higher Resolution available
H/W Req.
S/W Req.
Network Environment
LDK system should have unique IP address assigned by network administrator.
There should be LAN cable to connect LDK system.
ez Attendant need to be paired with Keyset Terminal.
MPB Version : 1st Released version
PC : ez Attendant Program
DAO35Registor.exe for using database
Requirements
Notes: <number>
<footer>
<header>
<date/time>
We need the following h/w and s/w requirement that the ezATD is installed.
SLT 는 연동 안 되는지?

## Slide 5
1. Execute “SETUP.EXE”
2. Click [Yes] button to install DAO Ver 3.5
4. Change Directory to be installed.
5. Click [Next] button.
3. Click [Next] button.
6. Click [Finish] button.
Installation
Notes: <number>
<footer>
<header>
<date/time>
Ok! Let’s see the software installation of ez-attendant.
It is very easy!
Just follow the installation procedure.
After finishing the ez-attendant installation,
we recommend you to reboot the computer
before executing the ezATD program.
Rebooting 하는 이유?

## Slide 6
Execution of ez Attendant
Execution of ez Attendant
2. Input System IP Address
3. Input Attendant Extension Number
4. Click [Log On] button
5. Log On is processing
Execution of ez Attendant
1. Select System
Notes: <number>
<footer>
<header>
<date/time>
After rebooting your computer,
click the [ez-attendant] icon and then the main window will be displayed.
To execute ez-attendant, set the following procedure.
Move to [Setting]  [Option]  [Setting]  [Log On Information]
Input LDK system IP Address and Attendant number.
Click the [Log on] button and then log-on is processing.
In this step, ezATD get system information from the LDK system.

## Slide 7
Queue Window
Station Window
Phone Book
Log –View
Optional(Icon/List)
Search and Info
MS scheduler Pre_selection SMS
Tool Up Bar
Main Menu
Tool Down Bar
Park Location
601
Main Window
Active Call Window
Notes: <number>
<footer>
<header>
<date/time>
This is the ezATD main window.
Main window consists of Main Menu, Tool Up Bar,
Queue Window, Station/Phone Book/Log-view Window,
Search/Information Window, MS Scheduler/Pre Selection/
SMS Window, Park Location Window And Tool Down Bar.

## Slide 8
Main Menu
Menu Description
Notes: <number>
<footer>
<header>
<date/time>
The main menu consists of File, Tools, Setting and Help.
- File menu has these kinds of sub menu.
Log On/Off, DB Convert and Print.
- Tools menu has these kinds of sub menu.
Station Name Change, Select Message Type, Paging,
Music Selection, Date/Time Change, SMS,
Attendant Feature and Prepaid Call.
- The setting menu has Customized Message,
Wakeup Setting, Record VMIB, Send E-mail, Group Setting,
Selected Station View, Flex Buttons Setting,
Code Setting, Keymap, Customize and Option.
Finally in the help, you can see the information of ez-attendant.

## Slide 9
Tool Up Bar
Open Outlook
Log On
Log Off
Tool Up Bar
Menu Description
Print for Log View
Notes: <number>
<footer>
<header>
<date/time>
This part is tool up bar.
Tool Up bar has my status, wake up, paging, SMS,
e-mail, print and log on/off button.
If user click each button so you will see the window like this.

## Slide 10
Station Window & Queue Window
Queue Window
Station Window
Net DSS(DND)
DKTU(Busy)
DKTU(Idle)
SLT(Busy)
SLT(Idle)
DND State
Forward State
Net DSS (Idle)
Net DSS(Busy)
Pre-selected Message
Station Window Sub Icon
Station Window Main Icon
ICM Incoming
CO Incoming
Attendant Recall
Transfer Recall
Park Recall
Hold Recall
Hold state Call
Active Call & Queue Window Icon
Menu Description
Active Call Window
CO Line Status Icon
Idle CO Line
Busy CO Line
Transfer Hold CO Line
Invalid CO Line
Notes: <number>
<footer>
<header>
<date/time>
Let’s see station window and queue window.
ezATD provides many icons to display the queue and
station status.
The queue window has ICM Incoming Icon, CO Incoming Icon,
Hold Icon, Park Recall, Hold Recall, Attendant Recall and
Transfer Recall Icon.
The station window has Terminal(DKTU, SLT, WHTU) Icons,
DND Status, FWD Status, Net DSS, Pre Selected Message Icon.

## Slide 11
Phone Book Window
Menu Description
Notes: <number>
<footer>
<header>
<date/time>
ezATD provides phonebook service to store and retrieve
customer or internal user
Phone book includes the following information.
User name, company name, address, contact point and so on.

## Slide 12
Log-View Window
Search Field
Selection Field
Menu Description
Notes: <number>
<footer>
<header>
<date/time>
ezATD provides call log service.
Call log view consists of selection field and search field.

## Slide 13
Call Queuing / Answering Incoming Call
- ICM/CO Line Incoming Call
- Hold State Call
- Attendant / Transfer / Hold / Park Recall : Has Recent via History
Transferring Call
- Unscreened / Screened Transfer
Message Wait / Call Back / Camp On
Making Outgoing Call
- Using Phonebook Data
- Using Keypad Dialog
- Using Station Window(Mouse Operation)
- Using Log View Data(Mouse Operation)
- Using Speed bin Data
Call Park and Retrieve
Call Pick-up(Mouse Operation Only)
Call Related Features
Call Related Feature
Notes: <number>
<footer>
<header>
<date/time>
ezATD provides the following call related features.
본문

## Slide 14
Record VMIB
- Supports Only Start Operation for Recording VMIB
Wakeup Call Registration / Cancel
Pre-selected Message and Customized Message
- Pre-selected Message is fixed
- Customized Message can be changed
Station Name Change
- Maximum 11 Characters
- Just saved on LDK system, not saved on ez Attendant’s database
Change COS / Temporary COS / Attendant Cancel / Music Selection
- COS Down / Restore
- Day /Night COS Setting
- DND/FWD Cancel
- MOH Setting
Call Related Features
Call Related Feature (cont.)
Notes: <number>
<footer>
<header>
<date/time>
본문

## Slide 15
Date Time Change
- Change Date
- 12/24 Time Mode
- dd/mm/yy or mm/dd/yy mode
Paging
- Internal / External / System All Call Paging
- Depends on Admin Configuration on LDK System
Using Keypad(Same as Keyset Operation)
- Supported to DTMF Tone
- Works same as Keyset Button When press each button
Call Related Features
Call Related Feature (cont.)
Notes: <number>
<footer>
<header>
<date/time>
본문

## Slide 16
Powerful Phone Book
- Manages Internal User / Customers
- When Incoming Call, Searches Information on Phone Book
- Can manage speed bin database
DB Converting
- Importing/Exporting MS-Outlook,MS-Access, MS-Excel, ACT! , Goldmine
Information Window
- Searching User (Internal / Customer)
- ①Full name  ②First name  ③Last name  ④Station Number  ⑤Mobile Phone
 ⑥Company Phone  ⑦House Phone  ⑧Department  ⑨E-Mail Address
- Shows Status of Station , Able to Make Call
Pre-Selected Message / Schedule Status Display
- Auto Loading Schedule on MS-Outlook or MS-Exchange Server
- Displays Status When Searching Information about Some User
- Displays Pre-selected Message
PC Related Features
PC Related Feature
Notes: <number>
<footer>
<header>
<date/time>
ezATD provides the following PC related features.
본문

## Slide 17
Screen Popup
- User Minimizes ez-Attendant to work another work
- Get an incoming call
- Shows Popup Window
SMS
- Sending SMS to DECT/DKTU (Maximum 48 Characters)
- Sending SMS to Mobile Phone (GSM Modem Needed)
Log View
- Save whole call history except internal calls
- Save to excel file (used by 3rd party application)
- Recommend to save to file when over 10,000 records
Multi Language Supported
- Able to Change Directly
- Change to Local Language in “pcAttendantll.txt” file
PC Related Features
PC Related Feature (cont.)
Notes: <number>
<footer>
<header>
<date/time>
본문

## Slide 18
Keyboard Mapping for Fast Operation
- Supports Some Call / PC Related Functions
- Can Change Hot-Key
Sending E-mail
Flexible Button Programming
- Same Function as Admin PGM 115
Group Management Window
- Can make/delete group under one company name
- Can add/delete member to/from a group name
Log View Print
Tool Tip Display
- Station Window
- Tool Up/Down Bar
PC Related Features
PC Related Feature (cont.)
Notes: <number>
<footer>
<header>
<date/time>
본문

## Slide 19
Show Demonstration CD
(About 25 Minutes)
Demo CD
Notes: <number>
<footer>
<header>
<date/time>
We will watch the ezATD demonstration.
It will take about 25 minutes.