## Slide 1
ADVANCED FEATURES

## Slide 2
Contents
Station Group
ACD Group
Intercom Tenancy Group
LCR
Conference Room
Hot Desk
Mobile Extension
Notes: 본문(Description)
(Move to the next)

## Slide 3
Station Group (1/6)
Station can be grouped so that incoming calls will search for an idle station in the
group and the call will be answered.
Circular An idle member of the hunt group is called when a call is received. If unavailable
or unanswered, the call is directed to the next station in the group.
Terminal If the call is unanswered or unavailable, it is directed to the next listed station in
the group. The call will continue to be routed until reaching the last station in the
group.
UCD Calls are directed to the station in the group that has been idle for the longest time.
VM This group is assigned for Voice Mail and only SLT is assigned as the member
of the VM group.
Ring All the stations in the group will receive ring for a call of station group when
a call is received.
NET VM Group | Voice Mail system is connected at SLT port of remote system. If this Net SLT number is assigned as Net VM group, Voice mail system of remote system can be used.

## Slide 4
No. of STA Group. & No. of STA in a Group.
No. of Station Group
No. of Station in a Group
10
26
station can be a member of multiple station groups. They have to be the same type station groups. But, pick-up group can be
assigned with the other type station group.
If all stations in the group are busy when a call is received,
the call continues to wait for an available station in the group.
If queued, the call may be sent to MOH until the call is answered or disconnected.
Hardware/Program
 Station Group: PGM 190
 Station Group Attribute: PGM 191
Station Group (2/6)

## Slide 5
Circular Station Group
CO LINE 2
CO LINE 1
STA101
STA102
STA103
STA105
STA104
STA100
Station Group (3/6)
Notes: 내선을 100,101,102,103,104,105 순으로 고리형 내선 그룹이 지정되어 있을 때, 내선100에 국선이 착신되면 순서대로 링이 착신되다 그룹 중 가장 마지막 내선인 105에서 계속 울리게 됩니다.
두 번째 국선이 착신 시 내선100이 아닌 내선101부터 국선 링이 착신되게 됩니다.

## Slide 6
Terminal Station Group
CO LINE 1
CO LINE 2
STA100
STA101
STA102
STA103
STA104
STA105
Station Group (4/6)
Notes: 내선을 100,101,102,103,104,105 순으로 묶었을 때 첫번 째 국선 링이 내선100번에 착신 시 안받으면 순서대로 링을 주며 그룹 내 끝 번호인 내선105번에서 계속 링이 울립니다.
두 번째 국선 링이 착신 시에도 처음 내선인 100번부터 105까지 순차적으로 국선 링을 서비스 합니다.

## Slide 7
UCD Station Group
CO LINE 2
CO LINE 3
CO LINE 1
STA100
STA101
STA102
STA103
STA104
STA105
Station Group (5/6)
Notes: 국선 링 착신은 그룹 내 내선 가입자에게 골고루 분배하여 줍니다. 즉 , 국선이 착신되면 그룹 내 내선 중 가장 오랫동안 전화를 받지 않은 내선 가입자에게만 링을 울려 주며 안 받을 경우 그룹 내 다른 내선으로 넘어가지 않습니다.

## Slide 8
Ring Station Group
CO LINE 1
CO LINE 2
CO LINE 3
STA101
STA103
STA104
STA105
STA100
STA102
Station Group (6/6)
Notes: 국선 링 착신 시 또는 내선 그룹 번호 호출 시 그룹 내 모든 내선에 한꺼번에 링이 울리도록 할 때 사용합니다.

## Slide 9
ACD (Automatic Call distribution) Group (1/3)
Features
Description
An unique supervisor can be assigned in a UCD group, and the
supervisor can monitor the status of UCD group.
The supervisor can monitor and record the conversation of the agents
in the group.
The supervisor can change the status of agents and confirm the statistics
of ACD Group or each ACD Agents.
 When the all agents are busy in a group, the number of queued call will be
displayed in the LCD of supervisor.
When the all agents are busy in a group, the number of queued call also will
be displayed in the LCD of each Agents.
 UCD Group Assignment: PGM 190 - BTN 1 - ‘3’
 Supervisor of UCD Group Assignment: PGM 191
Hardware/Program

## Slide 10
Supervisor
To monitor the conversation of agents,
{ACD STATUS}BTN : [TRANS/PGM] +FLEX_BTN + [TRANS/PGM] + 8* + Group NO + [HOLD/SAVE]
{Two Way Recording}BTN : [TRANS/PGM] +FLEX_BTN + [TRANS/PGM] + 54 + [HOLD/SAVE]
Agent 1
Agent 2
Agent 4
Agent 3
Press {ACD STATUS} button,
When Turn On
at supervisor to monitor.
ACD GROUP
 Two Way Recording Enable : PGM 112 - BTN 10 Pair
 Two Way Recording is available for only CO conversation call.
ACD (Automatic Call distribution) Group (2/3)

## Slide 11
CO LINE
Agent 1
Agent 2
Agent 4
Agent 3
ACD GROUP
All agents are busy in an ACD group,
Supervisor
The supervisor and each Agents LCD
will indicate queued Call Count.
And Supervisor’s {ACD GROUP} BTN
will flash
Call ACD group
  Dial 564 and destination sta
  number or {DSS} in order to
  reroute first queued call.
ACD (Automatic Call distribution) Group (3/3)

## Slide 12
Intercom Tenancy Group (1/3)
Features
Description
A station can be assigned to one of the Intercom Tenancy Groups. Each
Intercom Tenancy Group can be operated independently.
 Each group can be programmed to allow or deny calls to other groups.
 The attendant of each intercom tenancy group can assign Day/Night/
On-demand/Weekend mode.
 Intercom Tenancy Group ATD : PGM 120 - BTN1
Intercom Tenancy Group ACCESS : PGM 120 - BTN2
Station Intercom Group : PGM 111 – BTN 13
CO Tenancy Group : PGM 141 – BTN 10
Program

## Slide 13
Intercom Tenancy Group 1
Intercom Tenancy Group 2
Intercom Tenancy Group 3
When a call to other intercom tenancy group is allowed,
CO/STA call, pick-up or transfer is activated.
Intercom Tenancy Group (2/3)

## Slide 14
When a call to other intercom tenancy group is not allowed, CO/STA call, pick-up or transfer cannot be activated and each group will be operated as different system.
Intercom Tenancy Group 1
Intercom Tenancy Group 2
Intercom Tenancy Group 3
Intercom Tenancy Group (3/3)

## Slide 15
LCR (Least Cost Routing) (1/9)
Description
LCR is a system programmable feature that is automatically selected the least
available expensive route when an outgoing CO call is made.
This programming eliminates the necessity for the user to dial the access code
of the least expensive carrier.
■ Internal LCR - activated during internal dial tone.
■ Loop LCR - activated by dialing First accessible CO group code ('9' or '0'),
or by pressing Loop button.
■ Direct CO LCR - activated during CO dial tone.
(After dialing CO Line or CO group code, or pressing CO Line or CO group button.)
If the dialed digits are matched with COL LCR code,
the system will seize a CO Line from the programmed CO group and send the modified digits
according to LCR programming.

## Slide 16
 LCR can be applied to the following cases;
  Normal outgoing call
  Speed Dial / Off-net Call Forward
  Redial (if the previous call is LCR applied)
  ACNR (If the call is LCR applied when activating ACNR)
 LCR CONTROL ATTRIBUTES : PGM 220
 LDT TABLE : PGM 221
 DMT TABLE : PGM 222
 INITIALIZE LCR DB : PGM 223
Features
Program
LCR (Least Cost Routing) (2/9)

## Slide 17
LCR : Programming (1) (3/9)
BTN 1
Item Default Remark(Range)
LCR Access M00 M00 : Disable LCR
M01 : LCR whose attribute is ‘COL’ can
be accessed only through
common CO access Code(‘9’/’0’)
M02 : Internal LCR and Loop LCR are
activated.
M11 : Loop LCR and Direct CO LCR are
        activated
        M12 : All LCR type are activated
        When the user dial (‘9’/’0’) or loop button, ipLDK does not seize a CO line until LCR is finished.
        M13 : All LCR type are activated
        When the user dial (‘9’/’0’) or loop button, ipLDK first seize a CO line and wait dial to perform LCR.
BTN 2 Day of Week
BTN 1 MONDAY
BTN 2 TUESDAY
BTN 3 WEDNESDAY
Zone : 3, Day:1~7
* Monday (1), Tuesday(2),
Wednesday(3), Thursday(4),
Friday(5), Saturday (6), Sunday(7)
PGM220
BTN 4 THURSDAY
BTN 5 FRIDAY
BTN 6 SATURDAY
BTN 7 SUNDAY
1
1
1
1
1
1
1

## Slide 18
Item Default Remark(Range)
LDT(Leading Digit Table)
BTN2 LCR Type BOTH BOTH: look up this entry for both ‘INT’
and ‘COL’
INT : look up this entry for internal
dialing
COL : look up this entry after dialing
CO Access Code
3-way toggle
BTN3 LCR Code None To be compared with the dialed digits
(Up to 12 digits) by a user
Meaning of 6 digits: each pair(2 digits)
is the index to the DMT for the each time
Zone 1/2/3. (The [SPEED] button is used
to validate the remaining index)
BTN4 DMT index for Day Zone 1
BTN5 DMT index for Day Zone 2
BTN6 DMT index for Day Zone 3
None
(6 digits)
PGM220
Time of
DAY Zone 1
Time of
DAY Zone 2
Time of
DAY Zone 3
BTN1 Zone 1
BTN2 Zone 2
BTN3 Zone 3
Zone 1(00-24)
BTN1 Zone 1
BTN2 Zone 2
BTN3 Zone 3
BTN1 Zone 1
BTN2 Zone 2
BTN3 Zone 3
Zone : 3, Time:00~24
* ipLDK accepts it as same value for 00
and 24 changes to ‘00’, if input is 24
as starting value and vice versa
* Note : The time not belonging to any
zone will be considered as zone 1
* Note : 10~13 means 10:00:00 ~12:59:59
BTN3
BTN4
BTN5
PGM221
BTN1
BTN2
BTN3
BTN4
BTN5
LCR : Programming (2) (4/9)

## Slide 19
LCR : Programming (3) (5/9)
BTN1 Added Digit Stream(A) None Up to 20 digits
BTN3 Number of digits to be None 01~12
removed (RN)
BTN4 Add Position(AP) 01 01~13
BTN5 CO Group(C) 01 01~24
BTN6 Alternative DMT index(ALT) None 00~24(99)
DMT(Digit Modification Table) DMT index :00~24(99)
BTN2 Removal Position(RP) 01 01~12
PGM222
Item Default Remark(Range)
Item Default Remark(Range)
LCR Database change/Initialize
BTN1 Day Zone 1
BTN2 Day Zone 2
BTN3 Day Zone 3
BTN5 ALT Change Change all ALT in DMT table with a new
one
BTN4 CO Group Change Change all CO groups in DMT table with
a new one
BTN6 ALL LCR Database Initialize
None
(6 digits)
Each pair(2 digits) is the index to the
DMT for the each time Zone 1/2/3.
PGM223

## Slide 20
 Assume LCR code is ‘9’, the 001 network is least cost during the daytime,
and the 002 network is least cost during the night
 Caller dials same number and system routes it through least cost network
LCR : Effects on Programming (6/9)
Caller dials ‘9’ and
phone no (850 2600)
Phone no
(850 2600)
Network C
001
002
008
Network
Network A
Network B

## Slide 21
LCR : Programming Example 1 (7/9)
The long distance call access code starts with ‘0’. example) 02, 031, 051
There is a cheaper carrier exist, user can access it with carrier access code
‘082’ and long distance access code without ‘0’.
ipLDK system administrator wants to use this cheaper carrier for all long distance call.
example) user dials 9 + 0314502628  Real dialed digits 082314504628
Situation 1 (Add Prefix Digit)
ADM 220 | LCR MODE : M01 / M02 / M11 / M12 (LOOP LCR enabled)
ADM 221(LDT) | Bin 000) LCR TYPE : COL LCR CODE : 0 DMT : 00 00 00
ADM 222(DMT) | Bin 00) Remove Position : 01 Remove Number : 01 Add Position : 01 Add Digit : 082

## Slide 22
LCR : Programming Example 2 (8/9)
ipLDK system is connected with two carrier.
(Let’s assume one carrier is carrier ‘A’ CO Group 1, the other carrier is carrier ‘B’)
The carrier ‘B’ is used for international calls, and the carrier ‘A’ is for normal calls.
The international call access code is ‘001’.
ipLDK system administrator wants to use the carrier ‘B’ only for international calls.
Situation 2 (Select CO Group)
ADM 141 | set CO Lines from the carrier ‘A’ to CO group 1 set CO Lines from the carrier ‘B’ to CO group 2
ADM 117 | enable access CO group 01, 02
ADM 161 – F3 | Override 1st CO Group : OFF
ADM 220 | LCR MODE : M01 / M02 / M11 / M12 (LOOP LCR enabled)
ADM 221(LDT) | Bin 000) LCR TYPE : COL LCR CODE : 001 DMT : 00 00 00
ADM 222(DMT) | Bin 00) CO Group : 02
example) user dials 9 + 00182314504628  00182314504628(Access CO Group 2)

## Slide 23
LCR : Programming Example 3 (9/9)
ipLDK system has VOIP CO Lines and normal CO Lines.
ipLDK system administrator wants to access VOIP CO using code ‘7’.
and access normal CO Lines using code ‘9’ (If ‘9’ is a default co access code)
Situation 3 (Make another CO Access Code)
ADM 106 | remove / change numbering plan which starts with ‘7’
ADM 141 | set normal CO Lines to CO group 1 set VOIP CO Lines to CO group 2
ADM 117 | enable access CO group 01, 02
ADM 161 – F3 | Override 1st CO Group : OFF
ADM 220 | LCR MODE :M02, M12, M13 (Internal LCR enabled)
ADM 221(LDT) | Bin 000) LCR TYPE : INT, LCR CODE : 7, DMT : 00 00 00
ADM 222(DMT) | Bin 00) Remove Position : 01 Remove Number : 01 CO Group : 02
example) user dials 70314504628 0314504628(Access CO Group 2)

## Slide 24
Allows Internal and External (DID) callers to join in on a conference by dialing pre-assigned “Conference Room Number”(571~ 579).
Conference room feature can be password-protected.
The number of members is the same as normal conference (Max 15).
In case of DID type 2 call, a conference room should be assigned as the DID destination in Flexible DID Table.
Conference rooms can be monitored by the attendant for:
  The number of members in a conference.
  The conference room status (active/non-active) – Conference Room LED
  [TRANS/PGM + FLEX BTN + 571~ 579 + HOLD/SAVE]
Conference Room(1/2)
Description

## Slide 25
Notice to members
Conference call at 14:00,
please join at Conf Room #571.
Conference Room #1
Join CONF internally
e.g. dial *571
Join CONF externally
e.g. DID 8561 1908
To activate a conference room
(1) Press the [PGM] + 4 + 3 + Room Number (1~9)
(2) Dial 5-digit password (It is optional)
(3) Press the [HOLD] button.
To join a conference room in case of internal call
(1) Dial the activated conference room number. (571 ~ 579)
(2) Enter 5 numeric digits password for entering conference room
if password is enabled.
To join a conference room in case of DID call
(1) DID call is routed to conference room.
To check room status by ATD
(1) At ATD, dial a conference room status code
[PGM] + 0 + 4 + 7 + Conference Room Number (1~9).
To delete a conference room forcedly by ATD
(1) At ATD, dial a conference room forced delete code
[PGM] + 0 + 4 + 8 + Conference Room Number (1~9)
(2) Press the [HOLD] button.
(3) When erasing a conference room at ATD, password is not required.
Conference Room(2/2)
Operation

## Slide 26
Enables a user to dynamically select a station by log-in/log-out Operation
without having a fixed station.
For a call center, marketing department people can share working place with one another.
It can be applied to ACD agents.
A Hot Desk User can use dummy station using log-in operation.
The dummy station can be a DKTU (30 BTN) or IP Telephone (30 BTN).
A Hot Desk user can register call forwarding to Off-Net Speed 000 or Mobile Extension or VMIB or VM Group or Station before log-out.
Hot Desk station does not require a hardware(Telephone), but requires extension number.
Dummy station requires hardware(Telephone).
Hot Desk(1/2)
PGM 112 – BTN 23 : Dummy Station On/Off
PGM 227 : Authorization Code
PGM 250 – BTN 1 : Number of Agents
PGM 250 – BTN 2 : Verify Station Number of Agents
PGM 250 – BTN 3 : Agent Auto Logout Timer
Description
Program

## Slide 27
Log-in operation at dummy station
1. User off-hook or press [MON] button.
2. Dial authorization code.
3. Restore user database such as Station number,
COS, Ring assign, etc...
4. Operate as his extension.
Log-out operation
1. Press [PGM] + * + * (User Logout)
or press [Agent Logout] in flexible button.
2. User can select call forward type.
: Off-net speed 000, Mobile extension,
VMIB or VM group and Attendant
3. Press [HOLD] button
4. System backup user database and
station becomes to Dummy Station.
Hot Desk(2/2)
Operation
Physical –Dummy(110)
PSTN
During log-in
During log-off
Personal mail-box
Mobile EXT
Logging
Hot Desk 200
Hot Desk 201
Hot Desk 202

## Slide 28
Permits a DKTU to be “linked” to a mobile phone like a linked pair.
Incoming DID calls / ICM calls / Transferring calls to the station will be routed to the mobile phone as well (both will ring).
When one is answered, the other will stop.
The mobile phone can transfer the call to the ipLDK by dialing [* + extension number].
The mobile phone can reconnect the call by pressing [#] in case the transferred
extension does not answer
If the mobile phone user makes a DID call to own station, they will receive intercom dial tone and can make intercom call or can activate “DISA” function and make outgoing call from ipLDK, sending CLI of the station number.
Mobile extension feature must be enabled for a station in Admin Programming.
Once enabled in system, the user can activate/de-activate feature from his DKTU).
Mobile Extension(1/3)
PGM 236 : Mobile Extension Register
1. Mobile Extension Enable
2. Assign CO Group
3. Assign Mobile phone/House telephone number
4. register the mobile extension CLI number
Description
Program

## Slide 29
To register the mobile extension number in DKT.
1. Press the [PGM] + 33.
2. Dial the mobile number
3. Press the [HOLD] button.
To activate(deactivate) Mobile extension feature.
1. Press the [PGM] + 34 .
2. Dial the ‘1’ to activate, or ‘0’ to deactivate
3. Press the [HOLD] button.
To register the mobile extension CLI number in DKT.
1. Press the [PGM] + 35.
2. Dial the mobile CLI number
3. Press the [HOLD] button.
Mobile Extension(2/3)
Operation
Mobile
Network
E1 DID
101
In the office
when moving
①
②
ipLDK

## Slide 30
Mobile Extension(Practice)
Caller
Calling Party
Called Party
2000
(CLI:031-450-2000)
(CLI/DID:02-818-1005)
①
②
[Admin Programming]
PGM 143 – BTN 4 : DID Conversion Type(1)
PGM 114 – BTN 1 : CLIP Display(On)
PGM 201 : COLP Table Bin 00(02818)
PGM 143 – BTN 2 : CLIP Table Index(00)
[Admin Programming]
PGM 143 – BTN 4 : DID Conversion Type(1)
PGM 114 – BTN 1 : CLIP Display (On)
PGM 201 : COLP Table Bin 00(031450)
PGM 143 – BTN 2 : CLIP Table Index(00)
PGM 236 – BTN 1 : Mobile Extension Usage (On)
PGM 236 – BTN 2 : CO Group Assign(01)
PGM 236 – BTN 3 : Register Mobile Number (1005)
PGM 236 – BTN 4 : Mobile Ext CLI (028181005)
[Keyset Setting]
[TRANS/PGM] + 34 : Active Mobile Extension
[TRANS/PGM] + 33 : PGM 236 – BTN 3
[TRANS/PGM] + 35 : PGM 236 – BTN 4
Mobile Extension(3/3)