## Slide 1
Important Safety Information
To prevent the unexpected danger or damage, please read this information before installing and repairing the phone. There are “Caution” and “Warning”, it means as follows;

## Slide 2
Important Safety Information

## Slide 3
Important Safety Information

## Slide 4
LDP-7000 Series Model
LDP-7004D
LDP-7008D
LDP-7004N

## Slide 5
Input/Output Devices and Button
LDP-7008D
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
LCD Display
Handset
Headphone Socket (Ear/Mic Mode)
Speaker
Speaker Button
Hold/Save Button
Volume Button
Loop Button
Message Waiting LED
Dnd/Fwd Button
Call Back Button
Flexible Button
Speed Button
Trans/Pgm Button
Handsfree Microphone
1
2
3
4
5
6
7
8
9
12
13
14
10
11
15

## Slide 6
1
2
3
4
5
6
7
8
9
10
LCD Display (LDP-7004D only)
Handset
Speaker
OHD Button
Hold/Save Button
Message Waiting LED
Trans/Pgm Button
Speed Button
Flexible Button(Loop Button)
Volume Button
Input/Output Devices and Button
LDP-7004D
1
2
3
4
5
6
7
8
9
10

## Slide 7
Used for handset call.
The optional earphone into the handset to provide a hands-free phone conversation.
Outputs tones and voice.
Used to access speed dialing, speed programming, saved number redial.
The DND (Do Not Disturb) feature blocks all incoming calls. When DND is active, the red LED in this button is illuminated.
It is also used to activate call forward, e.g. to another station or voicemail. When call forward is activated, the red LED flashes.
This button put a call on hold or save information when
programming.
Speaker toggles the speakerphone state, and the red LED is illuminated when the speakerphone is active.
On Hook Dial allows 7004N&D users to dial and monitor call state without lifting the handset.
Handset
Earphone-Jack
Speaker
Speed Button
Dnd/Fwd Button
Hold/Save Button
Speaker Button
OHD Button
Item
Description
Input/Output Devices and Button

## Slide 8
Shows dialed and incoming numbers (where applicable) and on the 7008D it will display other information about call status, dialing directories and message information.
This button is used to initiate a call transfer (TRS) or to enter programming mode (PGM).
The last two (7004D/7004N) or six (7008D) flex buttons can be assigned outside line presentation or as one-touch feature access. (See codes at rear of guide)
A station can initiate a call back request to a busy station. Once that station becomes idle, the initiating station is signaled.
The volume button adjusts the audio levels for ringing, handset and speakerphone or OHD functions .
Microphone for hands-free speakerphone function.
Loop Button(s) are required for presentation of outside lines to the telephone. At least one is required per telephone.
LCD Display
Trans/PGM Button
Flexible Button
Call back Button
Volume Button
Hand-free Microphone
Loop Button
Item
Description
Input/Output Devices and Button

## Slide 9
Cable Connection
A
Cable connection
A Connect the telephone cord (curly cord)
to the handset and the other end to the
handset jack at the bottom of the telephone.
B Connect the line cable to the port at the
bottom of telephone and the other end to
the wall socket.
C Connect the Headphone to the headphone
jack on the left side of the telephone.
(As viewed from the front.)
※Note: 7004N and 7004D does not support integral headphone mode.
B
C

## Slide 10
Placing an Outside Call
● Lift handset, press OHD/Speaker or dial from live keypad.
● Dial 9.
● Dial the desired number.
Placing an Intercom Call
Placing an Outside Call on Hold
Retrieving a Outside Call on Hold
Re-directing an Incoming Call
(Call Pick-up)
Answering an Waiting Call
Basic Function
● Lift handset, press OHD/Speaker or dial from active keypad.
● Dial the station number.
● While connected to an external call, press [HOLD] button.
● Press the flashing flexible button.
※ Note: calls will automatically recall after pre-defined time
When you hear another phone ringing in your area,
● Lift handset, press OHD/Speaker or dial from live keypad.
● Dial 7.
● Dial the extension number of the ringing station.
● You will be connected automatically to the caller.
● Press the flashing CO button.

## Slide 11
Basic Function
Call Wait (Camp-on)
● After receiving station busy tone, dial＊ .
● Camp-on tone is heard in the called station.
● When called party answers, talk or hang up to
transfer another call to the called party.
Last Number Redial
Storing Station Speed Dial Numbers
Using Station Speed Dial Numbers
● Press the [SPEED] button
● Dial the desired speed dial bin number.
Group Call Pick-up
When hearing an unattended phone ringing in your area,
● Lift handset.
● Dial 5 5 6.
● You will be connected automatically to the caller.
※ Note: you must be in the same pick-up group.
● Lift handset, press OHD/Speaker or dial from active keypad.
● Dial 5 5 2 or press speed button + dial ‘＊’ + Hold/Save button.
● Press the [TRANS/PGM] and [SPEED] Button.
● Dial speed bin number. Range (XXX-ZZZ)
● Dial speed dial number you wish to store.
● Press the [HOLD/SAVE] button.
● Enter the name associated to the number.
● Press the [HOLD/SAVE] button.
● You will hear confirmation tone.

## Slide 12
Code for Flexible Button Programming
Register of Flexible Button
Trans/Pgm
Hold/Save
1
2
Press the [Trans/Pgm] button.
Press the [Flexible] button.
Trans/Pgm
3
Press the [Trans/Pgm] button.
4
Enter code number.
5
Press the [Hold/Save] button.

## Slide 13
Code for Flexible Button Programming
Button Assignment for LDP- 4N/4D, 8D
CONF button
CALLBK button
DND/FWD button
FLASH button
MUTE button
MON button
REDIAL button
Ring Type
Enblock mode
Ear-Mic Headset
ICM Ring
CO Ring
COS Down
Walking COS
Auth. Code Register
Auth. Code Change
Set Wake-up Time
Set Pre-selected MSG
Set Customer MSG
Two way Record
Record User Greeting
Listen Time & Date
Listen Station Number
Listen Station Status
Record Page MSG
Erase User Greeting
Erase Page MSG
LCD Display Language
Background Music
Register Station Name
Speakerphone/Headset
Headset Ring Mode
Account Code
DID Call Wait
ICM Hold
LOOP button
Camp-on
Call Log Button
Activate CONF Room
Deactivate CONF Room
TRANS/PGM + 91
TRANS/PGM + 92
TRANS/PGM + 93
TRANS/PGM + 94
TRANS/PGM + 95
TRANS/PGM + 96
TRANS/PGM + 97
TRANS/PGM + 11
TRANS/PGM + 14
TRANS/PGM + 17
TRANS/PGM + 18
TRANS/PGM + 19
TRANS/PGM + 21
TRANS/PGM + 23
TRANS/PGM + 31
TRANS/PGM + 32
TRANS/PGM + 41
TRANS/PGM + 51
TRANS/PGM + 52
TRANS/PGM + 54
TRANS/PGM + 61
TRANS/PGM + 62
TRANS/PGM + 63
TRANS/PGM + 64
TRANS/PGM + 65
TRANS/PGM + 66
TRANS/PGM + 67
TRANS/PGM + 71
TRANS/PGM + 73
TRANS/PGM + 74
TRANS/PGM + 75
TRANS/PGM + 76
TRANS/PGM + 80
TRANS/PGM + 81
TRANS/PGM + 83
TRANS/PGM + 84
TRANS/PGM + 85
TRANS/PGM + 57
TRANS/PGM + 43
TRANS/PGM + 44
Function
Code Number