## Slide 1
Important Safety Information

## Slide 2
Important Safety Information

## Slide 3
Important Safety Information

## Slide 4
Getting Started
LDP-7000 Series Model 7016D & 7024D
Input / Output Devices and Button
Cable Connection
ADP (Additional Device Port)
Placing or answering a call
1. Placing a call
2. Answering a call
3 Soft Button & Navigation Button
Basic Function
1. Idle
1.1 Pickup
1.2 Conference
1.3 Redial
2. Off Hook
3. Intercom Dialing
4. Intercom Ring Back
5. Intercom Busy
6. Intercom Do Not Disturb
7. Intercom Dialing Error
8. Intercom Receiving
9. Intercom Talk
10. CO Line Busy
11. CO Dialing / CO Talk
12. Checking messages
13.Paging
Call Log
1. Received Call
2. Dialed Call
3. Lost Call
3.1 Answer
3.2 Del Cur (Delete Current)
3.3 Del All (Delete All)
3.4 Save
3.5 Name/Tel
8
8
9
11
12
14
14
14
15
16
16
16
17
18
18
18
19
19
19
19
19
20
20
20
21
21
22
22
23
24
24
24
25
25
25
Table of Contents

## Slide 5
Menu
1. Basic Program
1.1 Station name program
1.2 Ring program
1.2.1 Select Ring
1.2.2 Select melody
1.3 Mode (H/T/P) Program
1.4 Password Program
1.4.1 Password Register
1.4.2 Password Change
1.5 Language Program
1.6 ENBLOCK Mode Program
2. Advanced Program
2.1 Wake up Program
2.1.1 Setting
2.1.2 Canceling
2.2 Pre-selected MSG PGM
2.2.1 Select the MSG PGM
2.2.2 Canceling/ Changing
2.3 Station COS Program
2.3.1 COS Down Mode
2.3.2 Restoring COS Mode
2.3.3 Walking COS Mode
2.4 SPK/Headset Program
2.5 EAR MIC Program
3. Speed Program
4. Mobile Extension PGM
4.1 Mobile-EXT. NUM PGM
4.2 Mobile-EXT Enable
5. Conference Room PGM
5.1 Create CONF Room
5.2 Delete CONF Room
6. Hot Desk Program
6.1 Hot Desk Log in
6.2 Hot Desk Log out
Phone Book
1. Dial By ICM Name
2. Dial By STA SPD name
3. Dial By SYS SPD Name
Entering characters
Glossary of Terms
26
27
27
28
29
29
30
31
31
32
33
33
34
34
34
35
36
36
37
38
38
39
40
41
41
42
43
43
43
44
44
44
45
45
46
47
47
48
48
49
50
Table of Contents

## Slide 6
LDP-7000 Series, Model 7016D & 7024D
LDP-7016D/7024D are advanced, user-friendly digital keysets, offering the convenience of 3 soft buttons and a navigation key.
LDP-7024D
Features
-.Trendy and Stylish LDP Family design
-.Multi Level 3 Line LCD (3 x 24)
-.16 or 24 Flexible buttons with dual-color LED’s
-.Additional Device Port (ADP) for SLT or FAX
-.Call Log Feature
-.Call Recording Feature – 7024D only (Optional USB Module).
-.Hands-Free Solution – 7024D only (Optional Blue- Tooth Module).
-.Wall Mountable (Bracket Optional)
LDP-7016D
Getting Started

## Slide 7
Input / Output Devices and Buttons
Handset
Earphone-Jack Socket
(Ear/Mic Mode)
Speaker
Speed Button
Dnd/Fwd Button
Speaker Button
Hold/Save Button
3 Soft Button
LCD Display
Visual Ringing LED
Trans/Pgm Button
Flexible Button (Loop Button)
Call back Button
Volume Button
Hands-free Microphone
Menu Button
Phonebook Button
(Same operate as ‘Speed’)
Getting Started
1
8
11
12
13
3
4
5
6
7
2
9
14
15
16
17
10
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17

## Slide 8
Used for handset call.
Used to connect optional headset to the phone.
Outputs tones and voice.
Used to access speed dialing, speed programming, save number redial, and last number redial.
The DND (Do Not Disturb) feature blocks all incoming calls. When DND is active, the red LED in this button is illuminated.
It is also used to activate call forward, e.g. to another station or voicemail. When call forward is activated, the red LED flashes.
Speaker toggles the speakerphone state, and the red LED is illuminated when the speakerphone is active.
This button is used to put a call on hold or save information when programming.
Used in conjunction with fixed and flexible features, and the function changes in relation to call progress, as indicated on the LCD display.
Displays information about telephone status, dialing directories,and test message information.
Illuminates when the phone is ringing.
This button is used to initiate a call transfer (TRS) or to enter programming mode (PGM)
Some flexible buttons are pre-programmed in the system for line appearances, loop functions etc. The remaining flexible buttons can be user-programmed.
A station can initiate a call back request to a busy station. Once that station becomes idle, the initiating station is signaled.
The volume button adjusts the audio levels for ringing, handset and speakerphone functions.
Microphone is used for hands-free speakerphone function.
The menu button is used to move to the desired option(Dial, MSG, Program), and to select the next screen when indicated by an arrow on the LCD display.
Used to access speed dialing, save number redial, and last number redial, and to access flexible button programming.
Handset
Earphone-Jack Socket
Speaker
Speed Button
Dnd/Fwd Button
Speaker Button
Hold/Save Button
3 Soft Buttons
LCD Display
Visual Ringing LED
Trans/PGM Button
Flexible Button
Call back Button
Volume Button
Hands-free Microphone
Menu Button
Phonebook Button
Getting Started
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17

## Slide 9
Cable Connection
Cable connections
A - Connect the telephone cord (curly cord) to the handset and the other end to the
handset jack at the bottom of the telephone.
B - Connect the line cable to the port at the bottom of telephone and the other end to the
wall socket.
C - Connect the Headphone to the headphone jack on the left side of the telephone.
(As viewed from the front.)
Getting Started
A
B
C

## Slide 10
ADP (Additional Device Port)
Getting Started

## Slide 11
ADP (Additional Device Port)
Getting Started

## Slide 12
1. Placing a Call
Lift handset
▶
Enter the extension number
Dial 9 or select CO line flexible button.
talk
▶
2. Answering an Outside Call
or
Lift handset
or
▶
talk
CO Line
ICM Line
Lift handset
▶
Enter the desired phone number
talk
▶
or
▶
CO Line
ICM Line
Lift handset
or
▶
talk
Press flashing CO line button or loop key.
▶
Getting Started

## Slide 13
The 3 Soft Buttons are located on the bottom of the LCD display. The function of each button changes, subject to call status and progress. The current functions are displayed on the LCD screen, directly above each button. For example, if the user calls a busy extension, busy tone will be heard and the busy status displayed. The LCD screen will display the busy message along with the different options available - “Message Wait”, “Camp-On” and “Flash”. By pressing the relevant button the desired feature is activated.
3 Soft Button
Navigation Button
In some instances, more than 3 current functions are available to the user, and this is indicated by the appearance of a left () or right () arrow in the LCD screen, (see below). By pressing the navigation key (located below the volume button), in the direction corresponding to the arrow, any additional functions will be displayed.
BUSY : STA 100
[CALLBK] CAMP(*) STEP
MSG CAMP-ON FLASH
STATION 100 (T)
FEB 01 04 05:34 pm
FWD CONF REDIAL →
STATION 100 (T)
FEB 01 04 05:34 pm
← ICM
3 Soft Buttons & Navigation Button

## Slide 14
By pressing one of the 3 soft buttons you are able to select the indicated function. For instance, if you want to select call pickup (as shown below), press the first button on the left. If there are more than three functions available at any point, an arrow will be displayed on the LCD display. Use the navigation key to move the next or previous screen to display additional functions.
3 Soft Buttons are located below the LCD display.
1. Idle
PICKUP : press to pickup a call ringing within the same pickup
group.
CONF : press to initiate & activate a conference.
REDIAL : press to redial last number called.
1.1 Pickup
CALL TO STA 104
FROM 100 05:37pm
TRANS CONF MUTE
A station can pickup a call ringing to an unattended station within the same pickup group by using the pickup procedure.
＊ Refer to IP LDK system & LDK system programming manual.
Press [PICKUP] button.
Talk
STATION 100 (T)
FEB 01 04 05:34 pm
PICKUP CONF REDIAL
STATION 100 (T)
FEB 01 04 05:34 pm
PICKUP CONF REDIAL
Basic Function

## Slide 15
1.2 Conference
CALL TO STA 100
FEB 01 04 05:34 pm
MSG FLASH
CALL TO STA 100
FEB 01 04 05:34 pm
TRANS CONF MUTE
Dial the desired station number.
(e.g.100)
Station 100 answers the call.
Press [CONF] button.
CONFERENCE
FEB 01 04 05:34 pm
FWD CONF REDIAL →
Dial the phone number of the next desired station. (e.g.104)
CALL TO STA 104
FEB 01 04 05:34pm
MSG FLASH
Station 104 answers the call.
CALL TO STA 104
FEB 01 04 05:34 pm
TRANS CONF MUTE
Press the [CONF] button twice.
CONFERENCE
FEB 01 04 05:34 pm
CONF MUTE
A 3-party conference is now established.
Basic Function

## Slide 16
1.3 Redial
Press the [REDIAL] button.
＞123456789
BACK OK
Press [OK] button to call.
123456789
LINE 008 00:00:10
TRANS CONF MUTE →
Talk
STATION 100 (T)
FEB 01 04 05:34 pm
PICKUP CONF REDIAL
2. Off Hook
STATION 100 (T)
FEB 01 04 05:34 pm
FWD CONF REDIAL→
FWD : Press the [FWD] button to forward calls to another
station, Voicemail etc.
CONF : Press the [CONF] button to initiate a conference call.
REDIAL : Press the [REDIAL] button to call last number dialed.
3. Intercom Dialing
STATION 100 (T)
FEB 01 04 05:34 pm
FLASH
FLASH : If you wish to terminate an ICM call and make another
call, press [FLASH] to re-seize dial tone.
STATION 100 (T)
FEB 01 04 05:34 pm
← ICM
ICM : If, while on a call, ICM call is received, press the [ICM]
button to place 1st call on hold and answer 2nd call.
Basic Function

## Slide 17
4. Intercom Ring Back
CALL TO STA 100
FEB 01 04 05:34 pm
MSG FLASH
MSG : Press to leave a your station number or message.
FLASH : Press to disconnect the line and re-seize.
5. Intercom Busy
BUSY : STA 100
[CALLBK] CAMP ( * ) STEP
MSG CAMP-ON FLASH
MSG : Press to leave your station number or message.
CAMP-ON : Press to send a call waiting tone to a busy station
(indicating that they have a call waiting).
FLASH : Press to disconnect the line and re-seize.
7. Intercom Dialing Error
INVALID
FEB 01 04 05:34 pm
FLASH
FLASH : Press to disconnect the line and re-seize.
6. Intercom Do Not Disturb
DO NOT DISTURB STA 100
CALLBK FLASH
CALLBK : Press leave a call back request or message.
FLASH : Press to disconnect the line and re-seize.
8. Intercom Receiving
CALL FROM STA 104
FEB 01 04 05:34 pm
DND
DND : Press to block all incoming calls. (Do Not Disturb)
Basic Function

## Slide 18
9. Intercom Talk
CALL FROM STA 104
FEB 01 04 05:34 pm
TRANS CONF MUTE
TRANS : Press to transfer an incoming call to another station.
CONF : Press to initiate a conference call.
MUTE : Press to mute the handset, speakerphone, or headset
microphone. Press the [SPEAK] button to re- activate
microphone.
10. CO Line Busy
CO LINE 001 BUSY
QUEUING ([CALLBK])
CALLBK
CALLBK : If, after dialing ‘9’ for a CO line, busy tone indicates
no lines are available, press [CALLBK] to reserve a CO
line.
11. CO Dialing/CO Talk
123456789
LINE 125 00:00:03
TRANS CONF MUTE →
123456789
LINE 125 00:00:03
← RECORD FLASH ACNR
TRANS : Press to transfer an incoming call to another station.
CONF : Press to initiate a conference call.
MUTE : Press to mute the handset, speakerphone, or headset
microphone. Press the [SPEAK] button to re- activate
microphone.
RECORD : Press to record the current conversation. (if fitted) FLASH : Press to disconnect the line and re-seize.
ACNR : Press to set automatic called number redial.
Basic Function

## Slide 19
12. Checking messages
VMIB MSG FROM EXTERNAL
NEXT REPEAT DELETE →
VMIB MSG FROM EXTERNAL
← ADD REWIND CALLBK
ADD : Press to tag the current message with your comment
before forwarding. Record your comments & then dial
the required station number to complete the transfer.
REWIND : Press momentarily to repeat part of current message.
CALLBK : Press to leave a call back request.
13. Paging
PAGE FROM STA 103
20 AUG 04 11:51am
MEET ME
NEXT : Press to move to the next message.
REPEAT : Press to repeat the current message.
DELETE : Press to erase the current message.
MEET ME : Press to answer a paging request.
Basic Function

## Slide 20
Press the [Call Log] button.
1. Received Call
123456789
02/01 09:02
BACK OK
NOTE
Return to the previous
BACK
Press [OK] or button.
Press [OK] or button.
123456789
LINE 125 00:00:03
TRANS CONF MUTE →
RECEIVED CALL : Received call list *
DIALED CALL : Dialed call list
LOST CALL : Missed call list*
1
1. RECEIVED CALL
2. DIALED CALL
OK
1
1. RECEIVED CALL
2. DIALED CALL
OK
Call Log Button PGM : PGM + Flexible + PGM ’57’
1
3. LOST CALL
∧
OK
Call Log
* CLI (Calling Line ID) mandatory.

## Slide 21
2. Dialed Call
123456789
02/01 09:02
BACK OK
Press [OK] or button.
Press [OK] or button.
123456789
LINE 125 00:00:03
TRANS CONF MUTE →
NOTE
NOTE
Return to the previous
BACK
2
1. RECEIVED CALL
2. DIALED CALL
OK
Call Log

## Slide 22
3. Lost Call
Press [OK] or button.
3
3. LOST CALL
∧
OK
0123456789
03/10 16:02 CNT :01
BACK SELECT> ANSWER
Press the [SELECT] button to select the following functions: ANSWER, DEL CUR (delete current),
DEL ALL (delete all), SAVE, NAME/TEL
3.1 ANSWER
0123456789
LINE XXX 00:00:03
TRANS CONF MUTE →
Press [ANSWER] to call the displayed number.
0123456789
03/10 16:02 CNT :01
BACK SELECT > ANSWER
3.2 DEL CUR
STATION 100 (T)
FEB 01 04 05:34 pm
PICKUP CONF REDIAL
Press [DEL CUR] to erase current number.
0123456789
03/10 16:02 CNT :01
BACK SELECT > DEL CUR
NOTE
NOTE
Return to the previous
BACK
Call Log

## Slide 23
3.3 DEL ALL
ALL CLI DELETE
Press HOLD Key
BACK SELECT > DEL ALL
Press the [HOLD] button to confirm ‘delete all’ function. All numbers are erased.
0123456789
14/07 16:02 CNT :01
BACK SELECT > DEL ALL
3.4 SAVE
ENTER SPD BIN NO (000)
CLI MSG USED
PAUSE FLASH D-TONE
3.5 NAME/TEL
EDWARD
03/10 16:02 CNT :01
BACK SELECT > NAME/TEL
Press [HOLD] or button,
speed dial is registered.
0123456789
03/10 16:02 CNT :01
BACK SELECT > NAME/TEL
※ See the page 42.
To save CLI, press [SAVE] button.
0123456789
03/10 16:02 CNT :01
BACK SELECT > SAVE
OR if a name is displayed, to check the associated number, press the [NAME/TEL] button.
NOTE
NOTE
Return to the previous
BACK
Press [SELECT] until [DEL ALL] appears in display. Press [DEL ALL] to initiate ‘delete all’ function.
To check the name of the selected number,
press the [NAME/TEL] button.
Call Log

## Slide 24
Press the [Menu] button.
Press the [Navigation] button.
Press the [Navigation] button.
1
Press the [Navigation] button.
Press the [Navigation] button.
2
3
4
Press the [Navigation] button.
5
6
3. SPEED PROGRAM
4. MOBILE EXTENSION PGM
OK
5. CONFERENCE ROOM PGM
6. HOT DESK PROGRAM
OK
3. SPEED PROGRAM
4. MOBILE EXTENSION PGM
OK
1. BASIC PROGRAM
2. ADVANCED PROGRAM
OK
5. CONFERENCE ROMM PGM
6. HOT DESK PROGRAM ∧
OK
1. BASIC PROGRAM
2. ADVANCED PROGRAM
OK
NOTE
NOTE
Return to the previous
BACK
※ CONFERENCE ROOM is not available in LDK-20.
Menu

## Slide 25
1. BASIC PROGRAM
Press [OK] or button.
Press the [MENU] button.
1.1 STATION NAME PROGRAM
ENTER NAME ( )
BACK OK
Enter the name.
※ For detailed information about entering name, see the page 49.
1
1. BASIC PROGRAM
2. ADVANCED PROGRAM
OK
1
1. STATION NAME PROGRAM
2. RING PROGRAM
BACK OK
Press [OK] or button.
Menu

## Slide 26
1.2 RING PROGRAM
Press [Navigation] button.
Press [Navigation] button.
Press [Navigation] button.
Press [Navigation] button.
1
3
1. ICM RING
2. ICM MELODY
BACK OK
2
1. ICM RING
2. ICM MELODY
BACK OK
3. CO RING
4. CO MELODY ∧
BACK OK
4
3. CO RING
4. CO MELODY ∧
BACK OK
1
1. STATION NAME PROGRAM
2. RING PROGRAM
BACK OK
Press [OK] or button.
Menu

## Slide 27
RING TYPE : 01 (01-15)
SELECT BY [NEXT]
BACK NEXT OK
Step using [NEXT] or button to select the ring.
1.2.1 Select Ring
RING TYPE : 02 (01-15)
SELECT BY [NEXT]
BACK NEXT OK
Press [OK] or button. The selected ring type is saved.
※ Use same procedure to select CO Ring type.
1
1. ICM RING
2. ICM MELODY
BACK OK
1.2.2 Select Melody
1
1. ICM RING
2. ICM MELODY
BACK OK
CATEGORY SEARCH
← Pleasure (10) →
EXIT OK
Use button to select category.
Pleasure(10)
← [01] Cancan →
BACK EXIT OK
Press the [OK] or button and then the melody is changed.
※ Press the [EXIT] button to cancel.
※ Use same procedure to select CO Melody.
Note : To set the melody, MFU and MU board is required.
Use button to select the desired melody.
Press [OK] or button.
Press [OK] or button.
Menu

## Slide 28
1.3 MODE(H/T/P) PROGRAM
TONE MODE
SELECT BY [NEXT]
BACK NEXT OK
Press [NEXT] or button to select the mode.
PRIVATE MODE
SELECT BY [NEXT]
BACK NEXT OK
Press [OK] or button.
※ There are three types as follows;
-. HANDSFREE MODE
-. TONE MODE
-. PRIVATE MODE
You will hear three bursts of tone and an announcement.
Reply hands-free or lift handset for privacy. The calling party can
hear any conversation in progress.
You will hear repeated bursts of intercom ring tone and
the HOLD button slow flashes. Lift the handset or press
the SPEAKER button to answer.
You will hear three bursts of tone and one-way announcement.
The calling party cannot hear any conversation in progress
NOTE
HANDSFREE
TONE
PRIVATE
STATION 100 (P)
FEB 01 04 05:34 pm
PICKUP CONF REDIAL
The selected mode is saved.
1
3. MODE(H/T/P) PROGRAM
4. PASSWORD PROGRAM
BACK OK
Press the [OK] or button.
Menu

## Slide 29
1.4 PASSWORD PROGRAM
Use [Next] or button to select the password register.
Then press [OK] or button.
ENTER PASSWORD :
BACK
Enter password. (5 digits)
e.g.) 55555
PRESS OK KEY
BACK OK
Press [OK] or button.
> PASSWORD REGISTER
SELECT BY [NEXT]
BACK NEXT OK
1.4.1 PASSWORD REGISTER
1
3. MODE(H/T/P) PROGRAM
4. PASSWORD PROGRAM
BACK OK
Press [OK] or button.
Menu

## Slide 30
Use [Next] or button to select the password change.
Then press [OK] or button.
ENTER CURRENT PASSWORD
BACK
Enter the current password. (5 digits)
e.g.) 55555
ENTER PASSWORD :
BACK
Enter the new password. (5 digits)
e.g.) 33333
1.4.2 PASSWORD CHANGE
> PASSWORD CHANGE
SELECT BY [NEXT]
BACK NEXT OK
Press [OK] or button.
PRESS OK KEY
BACK OK
Menu

## Slide 31
1.5 LANGUAGE PROGRAM
Press [OK] or button.
> KOREAN
LCD LANGUAGE
BACK NEXT OK
> ENGLISH
LCD LANGUAGE
BACK NEXT OK
Use [NEXT] or button to select language.
1.6 ENBLOCK MODE PROGRAM
Press [OK] or button.
ENBLOCK MODE
> ON
BACK NEXT OK
ENBLOCK MODE
> OFF
BACK NEXT OK
Use [NEXT] or button to select ON/OFF.
1
5. LANGUAGE PROGRAM
6. ENBLOCK MODE ∧
BACK OK
1
5. LANGUAGE PROGRAM
6. ENBLOCK MODE ∧
BACK OK
Press [OK] or button.
Press [OK] or button.
Menu

## Slide 32
2. ADVANCED PROGRAM
Press [MENU] button.
2.1 WAKE UP PROGRAM
ENTER YOUR WAKEUP TIME
HH:MM 10:10 am
BACK ERASE OK
Enter the time and select single time or every day.
S:Single (once only - Default)
C:Every Day ( # )
* Set the time : 24 hr format
e.g. :7am = 07:00
:7pm = 19:00
STATION 100 (T)
FEB 01 04 *10:34 pm
PICKUP CONF REDIAL
Flashing [*] preceding time indicates alarm set.
2.1.1 Setting
1
1. BASIC PROGRAM
2. ADVANCED PROGRAM
OK
1
1. WAKE UP PROGRAM
2. PRESELECTED MSG PGM
BACK OK
WAKEUP RING
FEB 01 05 *07:00 am
The alarm will sound at the pre-set time.
ENTER YOUR WAKEUP TIME
07:00-C 10:00am
BACK ERASE OK
Press [OK] or button.
Press [OK] or button.
Press [OK] or button.
Menu

## Slide 33
2.1.2 Canceling
ENTER YOUR WAKEUP TIME
07 : 00-S *10:34 pm
BACK ERASE OK
Press [ERASE] button.
Press [OK] or button.
ERASED WAKEUP TIME
07 : 00-S *10:34 pm
BACK ERASE OK
1
1. WAKE UP PROGRAM
2. PRESELECTED MSG PGM
BACK OK
Press [OK] or button.
Menu

## Slide 34
2.2 PRESELECTED MSG PGM
SELECT BY UP/DOWN KEY
BACK
Use or button
to select the desired type.
Press [OK] or button.
Enter the time (24 hr format)
e.g.) 07:30 am  enter 0730.
07:30 pm  enter 1930.
OUT OF OFFICE
RETURN AT TIME XX:XX
BACK OK
Press [OK] or button.
ENTER TIME
HH:MM
BACK
ENTER TIME
07:30 PRESS OK KEY
BACK P.DVU OK
The selected message is displayed.
OUT OF OFFICE
RETURN AT TIME 07:30
PICKUP CONF REDIAL
1
1. WAKE UP PROGRAM
2. PRESELECTED MSG PGM
BACK OK
2.2.1 Select the MSG PGM
Press [OK] or button.
Menu

## Slide 35
2.2 PRESELECTED MSG PGM
THE PRESELECTED MESSAGE TYPE
0 0 USER CUSTOM MSG 00
0 1 LUNCH RETURN AT XX:XX
0 2 ON VACATION / RETURN AT DATE XX:XX
0 3 OUT OF OFFICE/ RERURN AT TIME XX:XX
0 4 OUT OF OFFICE/ RETURN AT DATE XX:XX
0 5 OUT OF OFFICE/ RETURN UNKNOWN
0 6 CALL TO (PHONE NO : Max. 17 digits)
0 7 IN OFFICE STA ***
0 8 IN A MEETING / RETURN AT TIME XX:XX
0 9 AT HOME
1 0 AT BRANCH OFFICE
2.2.2 Canceling / Changing
OUT OF OFFICE
RETURN AT TIME XX:XX
BACK ERASE OK
SELECT BY UP/DOWN KEY
BACK
[Message select mode]
Press [ERASE] button to cancel the pre-selected message and return to the[Message select mode].
※ Press [BACK] button to return to the previous LCD
screen.
※ Press [OK] button to return to the [enter time mode].
1. WAKE UP PROGRAM
2. PRESELECTED MSG PGM
BACK OK
Press [OK] or button.
Menu

## Slide 36
2.3 STATION COS PROGRAM
> COS DOWN MODE
SELECT BY [NEXT]
BACK NEXT OK
※ To activate STA COS (Station Class Of Service), password is required..
※ There are three types as follows;
-. COS DOWN MODE
-. RESTORE COS MODE
-. WALKING COS MODE
2.3.1 COS DOWN MODE
1
3. STATION COS PROGRAM
4. SPK/HEADSET PROGRAM
BACK OK
Press [OK] or button.
> COS DOWN MODE
ICM ONLY MODE
BACK OK
Press [OK] or button and then the mode is changed.
Use [NEXT] or button to select the
COS DOWN MODE.
Press [OK] or button.
Menu

## Slide 37
2.3.2 RESTORING COS MODE
Use [NEXT] or button to select
the RESTORE COS MODE.
ENTER CURRENT PASSWORD
BACK
Enter the password (5 digits)to change RESTORE COS MODE.
Press [OK] or button.
ORIGINAL COS RESTORED
PRESS OK KEY
BACK OK
> RESTORE COS MODE
SELECT BY [NEXT]
BACK NEXT OK
Press [OK] or button.
Menu

## Slide 38
2.3.3 WALKING COS MODE
Use [NEXT] or button to select the WALKING COS MODE.
ENTER COS OVERRIDE CODE
BACK
Enter the COS Override code
(Password - 5 digits)
e.g.- 12345
> WALKING COS MODE
SELECT BY [NEXT]
BACK NEXT OK
ENTER COS OVERRIDE CODE
PRESS OK KEY
BACK OK
Press [OK] or button.
Press [OK] or button.
Menu

## Slide 39
2.4 SPK/HEADSET PROGRAM
SPEAKER MODE
SELECT BY [NEXT]
BACK NEXT OK
Use [NEXT] or button to toggle the mode.
SPEAKER MODE
SELECT BY [NEXT]
BACK NEXT OK
Press [OK] or button to save selected mode.
※ There are two types as follows;
-. SPEAKER MODE
-. HEADSET MODE
1
3. STATION COS PROGRAM
4. SPK/HEADSET PROGRAM
BACK OK
2.5 EAR MIC PROGRAM
Press [OK] or button.
EAR-MIC HEADSET
> OFF
BACK NEXT OK
EAR-MIC HEADSET
> ON
BACK NEXT OK
Use [NEXT] or button to select the ON/OFF.
1
5. EAR MIC PROGRAM
∧
BACK OK
Press [OK] or button.
Press [OK] or button.
Menu

## Slide 40
3. SPEED PROGRAM
Press [MENU] button.
ENTER SPD BIN NO(000)
BACK
Enter the speed bin number.
e.g.)007
>
ENTER CO-BTN/DIGIT (007)
BACK DELETE
Then press [OK] or button.
>123456789
SPEED 007
BACK OK
Enter the phone number.
e.g.)123456789
Press [DELETE] button
to delete speed bin number.
1
3. SPEED PROGRAM
4. MOBILE EXTENSION PGM
OK
Enter the name.
※ See page 49 for details.
>
ENTER NAME (SPD 007)
BACK OK
Then press [OK] or button.
> ABC
ENTER NAME (SPD 007)
BACK OK
Press [OK] or button.
Menu

## Slide 41
4. MOBILE EXTENSION PGM
Press [MENU] button.
1
3. SPEED PROGRAM
4. MOBILE EXTENSION PGM
OK
Press [OK] or button.
4.1 MOBILE-EXT. NUM PGM
4.2 MOBILE-EXT ENALBLE
> 123456789
MOBILE EXT TEL NO.
BACK OK
Enter the mobile number.
e.g.)2222222
MOBILE EXT. USAGE
> OFF
BACK NEXT OK
Press [OK] or button.
Use [NEXT] or button to toggle ON/OFF.
MOBILE EXT. USAGE
> ON
BACK NEXT OK
Press [OK] or button.
Press [OK] or button.
1. MOBILE-EXT. NUM PGM
2. MOBILE-EXT. ENABLE ∧
BACK OK
1. MOBILE-EXT. NUM PGM
2. MOBILE-EXT. ENABLE ∧
BACK OK
＊ Refer to IP LDK system & LDK system programming manual.
> 2222222
MOBILE EXT TEL NO.
BACK OK
Menu
Press [OK] or button.

## Slide 42
5.1 CREATE CONF ROOM
DIAL NO(1-9) AND PASSWD
BACK OK
5.2 DELETE CONF ROOM
Enter conference room number
and password.
e.g.) 9 + 12345
Press [OK] or button.
PRESS OK KEY
BACK OK
DIAL NO(1-9) AND PASSWD
BACK OK
Enter conference room number
and password.
e.g.) 9 + 12345
Press [OK] or button.
PRESS OK KEY
BACK OK
1. CREATE CONF ROOM
2. DELETE CONF ROOM ∧
BACK OK
1. CREATE CONF ROOM
2. DELETE CONF ROOM ∧
BACK OK
Press [OK] or button.
Press [OK] or button.
5. CONFERENCE ROOM PGM
Press [MENU] button.
1
5. CONFERENCE ROOM PGM
6. HOT DESK PROGRAM ∧
OK
Press [OK] or button.
※ CONFERENCE ROOM is not available in LDK-20.
Menu

## Slide 43
6. HOT DESK PROGRAM
Press [MENU] button.
6.1 HOT DESK LOG IN
1
5. CONFERENCE ROOM PGM
6. HOT DESK PROGRAM ∧
OK
Enter password.(5 digits)
e.g.)55555
DUMMY STATION 100
ENTER PASSWORD :
STATION 217 (T)
06 SEP 04 04:00pm
PICKUP CONF REDIAL
1. HOT DESK LOG IN
2. HOT DESK LOG OUT ∧
BACK OK
＊ Refer to IP LDK system & LDK system programming manual.
Press [OK] or button.
Press [OK] or button.
Menu

## Slide 44
6.2 HOT DESK LOG OUT
Use button or button to select forward type and then Press [OK] or button.
AGENT LOGOUT WITH
NO FORWARD SET ?
1. HOT DESK LOG IN
2. HOT DESK LOG OUT ∧
BACK OK
DUMMY STATION 222
09 SEP 04 10:43am
PICKUP CONF REDIAL
※ Forward type
- NO FORWARD SET
- FORWARD TO VMIB
- FORWARD TO NM…
- FORWARD TO SPD000
- FORWARD TO MOBILE-EXT
- FORWARD TO STA…
Press [OK] or button.
Menu

## Slide 45
Press [OK] or button.
1. Dial By ICM Name
[PHONE BOOK] and [DIAL: BY NAME] are the same feature.
1. DIAL BY ICM NAME
2. DIAL BY STA SPD NAME
OK
3. DIAL BY SYS SPD NAME
∧
OK
NOTE
Return to the previous
BACK
Use the button or button to select the desired number and press the [SEND] button to call.
1
1. DIAL BY ICM NAME
2. DIAL BY STA SPD NAME
OK
1
1:CCC (105)
2:DDD (107)
BACK SEND
Talk.
CALL TO CCC
06 SEP 04 04:06pm
MSG FLASH
Phone Book

## Slide 46
Press [OK] or button.
2. Dial By STA SPD Name
NOTE
Return to the previous
BACK
2
1. DIAL BY ICM NAME
2. DIAL BY STA SPD NAME
OK
Press [OK] or button.
3. Dial By SYS SPD Name
1. TEAM1(2000)
2. TEAM2(2001)
BACK NAME/TEL SEND
To check the number of the selected name, press the [NAME/TEL] button.
Use the button or button to select the desired number and press [SEND] button to call.
123456789
LINE 008 00:00:03
TRANS CONF MUTE →
Talk.
3
3. DIAL BY SYS SPD NAME
∧
OK
123456789
LINE 008 00:00:03
TRANS CONF MUTE →
Talk.
To check the number of the selected name, press the [NAME/TEL] button.
Use the button or button to select the desired number and press [SEND] button to call.
1:ABC(001)
2:DEF(002)
BACK NAME/TEL SEND
Phone Book

## Slide 47
A
B
C
D
E
F
G
H
I
J
K
L
M
N
O
P
Q
R
S
T
U
V
W
X
Y
Z
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
Entering characters

## Slide 48
Intercom – describes internal calls within the telephone system
Central Office Line – also known as a trunk line, exchange line or outside line
A commonly used number stored in a speed bin for easy access
Do Not Disturb – the station is blocked toall incoming calls
Forward – calls can be sent to another location such a voicemail or another station
Direct Dial Inwards or Direct Inwards Dialing – ISDN lines can be provided with multiple telephone numbers which are each routed to individual stations or Hunt Groups
Digital Key Telephone Unit – an LG digital telephone
Single Line Telephone – an analogue telephone
Integrated Services Digital Network. Digital CO lines that come in multiples of 2 channels or more
Voice Message Interface Board – LG’s integral Voice Processing card
Conference – where you can talk to 2 or more internal or external parties
ICM
CO Line
Speed Dial
DND
FWD
DDI or DID
DKTU
SLT
ISDN
VMIB
CONF
Glossary of Terms
1
2
3
4
5
6
7
8
9
10
11