## Slide 1: checknode.pl
TTK tool usage.
Notes: Welcome on Troubleshooting Toolkit checknode script presentation.
2016-05-09
© Ericsson AB 2016
<number>
checknode.pk

## Slide 2: Tool behaviour
RNC
logs
lh mod llog –l
logs
'(Error\s+code\s+:\s+.*);(Process\s+:\s+.*)
RNC
Notes: Execution flow of the tool is presented on this slide.
For each selected “checker”, COLI commands defined are send to observed nodes.
Results are collected in local files.
Which in next step are checked against defined regular expressions.
Based on findings report will be prepared.
Such report is being send by email to all recipients, unless other options are selected while running the tool.
2016-05-09
<number>
checknode.pk
© Ericsson AB 2016

## Slide 3: Disclaimer
mailx command is used to send mails
Configured mail server is need to use mail reports functionality
Tool is able to call any moshell command on the node so be careful, to not change any configuration by mistake !!!
Notes: There are two major things it is worth to mention before start using the tool!
Checknode uses 'mailx' – command to send the report in the mail to the recipients. It requires to have well configured mail server in your environment ;
The second,, more important it is possible to inject any moshell command to the observed nodes, using this tool functionality !
Please be careful with fancy commands which might change node configuration!
2016-05-09
<number>
checknode.pk
© Ericsson AB 2016

## Slide 4: “Main” configuration
Location: $TTK_HOME/Tools/checknode
Core configuration: checknode.conf
[core]
mobatch=mobatch
logdir=$Bin/logdir
mailto=nobody@ericsson.com
[node]
ipdatabse=$HOME/.TTK/ipdatabse
sitefile=$HOME/.TTK/sitefile
rules=$HOME/.TTK/checknode.rules
Notes: Now it is time for introduction to script configuration.
Configuration consists of two parts.
First part is main configuration file located in tool directory.
Lines which needs to be update are the one related to ‘MO-batch’, path to program
, and ‘mailto’ – with recipients of mail report.
2016-05-09
<number>
checknode.pk
© Ericsson AB 2016

## Slide 5: “User” configuration
Location: $HOME/.TTK
Information about observed nodes in mobatch acceptable format:
  $HOME/.TTK/ipdatabse
  $HOME/.TTK/sitefile
Tool checkers & rules:
  $HOME/.TTK/checknode.rules
  contains checkers released with tools
  and place for user-defined checkers
Notes: Second part is connected with user preferences.
Tools puts the files into the user home directory,, to hidden TTK directory.
Main purpose of that was to not destroy users settings while TTK upgrade.
There are two files:
- ip database;
- and site file;
which keeps information about access to observed nodes , like IP addresses, ports and passwords.
There is also core tool file ‘checknode.rules’, which keeps basic checkers provided in TTK release package
Checker, means coli commands, to be executed, and regular expression to extract specific information from logs.
2016-05-09
<number>
checknode.pk
© Ericsson AB 2016

## Slide 6: First run
Directory: $TTK_KHOME/Tools/checknode
Core configuration updates : checknode.conf
  [core]
  mobatch=mobatch  Update mobatch scrit path ($HOME,$Bin variables can be used in paths)
  logdir=$Bin/logdir
  mailto=nobody@ericsson.com  Update mailto field
  [node]
  ipdatabse=$HOME/.TTK/ipdatabse
  sitefile=$HOME/.TTK/sitefile
  rules=$HOME/.TTK/checknode.rules
Initial run: checknode.pl –rules
  Script will create in $HOME/.TTK/ configuration files with rules and node addresses
Put information about the nodes to the files:
  $HOME/.TTK/ipdatabse
  $HOME/.TTK/sitefile
Notes: User configuration file is being created while first run of the tool.
So just after main configuration updates, user should run the script without any options, or as proposed with “rules” option.
This will force the script to 'generate' user configuration default files.
Just after that it will be possible to update them with own preferences.
2016-05-09
<number>
checknode.pk
© Ericsson AB 2016

## Slide 7: Basic usage
checknode.pl --rules
  Found checkers:
  'SppAll-any-check': [ 'lh spb llog -l;lh pdr aalpm' => '(Error\s+code\s+:\s+.*);(Process\s+:\s+Spp_AalDataInd)' ]
  'alarms': [ 'al' => '^Maj\s+;^Cri\s+' ]
  'SppAll-check': [ 'lh spb llog -l;lh pdr aalpm' => '(Error\s+code\s+:\s+0x80020113);(Process\s+:\s+Spp_AalDataInd);(RX-\s+ring\s+overflows\s+:\s+1)' ]
  'check-crashes': [ 'lh all llog -l;' => '(Error\s+code\s+:\s+.*);(Process\s+:\s+.*)' ]
checknode.pl <name>
Default enabled modifiers:
  -B – tries to group output in boards section and match rules within the groups
Search modifiers:
  -F (--free-search) command output does not provide boards prefixes so script match per line
  -X (--at-least-one) script send notification if at least one match found in the scope
Other modifiers:
  -o (--only-match) include to the report only regular expression cut part
  --mail-on-match send mail if checker will match the rules only
Notes: After initial run and whole configuration applied tool is ready to serve,. Basic use case is just call the script with 'checker' name as parameter.
Checkers name are visible in first column, of “rules” option printout.
By default script groups results of commands per board, and than match regular expression, with-in such group.
For some commands board prefix in not available in printout..In such case it is recommended to use patrameters
“free-search” and in some case “at-least-one”,, which will report the issues,, if at least only one provided regular expression will be caught.
From other interesting modifiers is “mail-on-match”.
Tool will send notification only if found issues in the logs.
2016-05-09
<number>
checknode.pk
© Ericsson AB 2016

## Slide 8: User-defined checkers
Add new rules to checknode.rules
Format:
  name=checker_name
  cmd="some command"
  cmd="some command next…"
  rule="(perl-regular-expression-1)"
  rule="(perl-regular-expression-2)"
  message=“optional informational description"
Useful script call option
    -p (--parse-only) <logdir> for testing user-defined rule on already collected data
Notes: Tool provides possibility to extend existing checkers by own-one.
New checkers needs to be added to the checknode rules file. Supported structure should be as on the slide.
Checker consists of the name,, one or more commands,, and one, or more regular expressions, and also informational user to be attached to the report.
To test your own regular expression on the collected logs use “parse only” option with path to directory with previously fetched logs.
You can inform TTK development team about your own checkers you feel might be useful for others,, to add them by default to the tool and be available with new release for everyone.
Please remember to be carful when running you own commands against the node to not break accidentally any configurations!!
2016-05-09
<number>
checknode.pk
© Ericsson AB 2016

## Slide 9
Notes: Thank you for your attention!
Good bye!!
2016-05-09
<number>
checknode.pk
© Ericsson AB 2016