## Slide 1: GSM Signalling

## Slide 2: Objective
The Trainee will be able to understand:
Signalling between MSC/VLR and BSS
Concept of DTAP
Concept of BSSMAP
Signalling between BSC and BTS
Functions of LAPDm
Functions of LAPD
Frame structure of LAPDm And LAPD

## Slide 3: Introduction
There are two different types of communication channels:
Traffic channel at 64 Kbps, carrying speech or data for radio channels.
Signalling channels at 64Kbps, carrying signalling information.
In PCM one time slot is reserved for signalling and remaining are used for transmitting speech or data. As the entire siganlling is done on 64Kbps , there should be special function converting the information to 64Kbps format and back at the receiving end.

## Slide 4: Protocols in GSM Networks
VLR
VLR
MSC
AUC
HLR
EIR
BSC
BTS
BSSAP
LAPD
MAP
MAP
MAP
MAP
MAP
ISDN
GMSC
MSC
PSTN
ISUP
ISUP
MAP
TUP
MS
LAPDm
Switching System
Base Station System

## Slide 5: GSM Signalling Matrix
LAPDm
MS
BTS
MSC
DTAP
RR
RIL3
RIL3
RSM
LAPDm
LAPD
BSC
RSM
BSSMAP
BSSAP
LAPD
SCCP
MTP2 &3
MTP1
MTP1
MTP2 & 3
SCCP
BSSAP
DTAP
BSSMAP
MAP
TCAP
ISUP
Database

## Slide 6
MSC uses ISUP/TUP protocols for PSTN signalling.
MAP siganlling for database applications like HLR, VLR, EIR, AUC, SMS-SC, GMSC.
GSM specific protocol as BSSAP, which comprises of DTAP and BSSMAP.
The BSC on layer 2 uses LAPD protocol, which is an ISDN.
BTS has LAPDm as layer 2 protocol.
Mobile has DTAP for MSC and RR for Radio Resource signalling.

## Slide 7: MAP (Mobile Application Part)
MAP is a protocol specially designed for GSM requirement. It is installed in MSC, VLR, HLR, EIR and communicates in case of:
Location registration
Location cancellation
Handling/management/ retrieval of subscriber data.
Handover
Transfer of security/ authentication data.

## Slide 8: BSS Application Part (BSSAP)
BSSAP is used for signalling between MSC/VLR and BSS. Three groups of signals belong to BSSAP
DTAP
BSSMAP
Initial MS messages

## Slide 9
MSC
MS
BSC/BTS
DTAP
Initial MS Message
BSSMAP
LAPDm
Transparent to BSS

## Slide 10: Direct Transfer Application Part (DTAP)
DTAP is a messages between the MSC and MS, passes through the BSS transparently. These are call control and mobility management messages directed towards a specific mobile.
3 main type of DTAP messages are:
Messages for mobility management like location update, authentication, identity request
Messages for circuit mode connections call control
Messages for supplementary services

## Slide 11: BSSMAP
BSS management messages (BSSMAP) between MSC and BSS (BSC/ BTS), which are necessary for resource management, handover control, paging order etc. The BSSMAP messages can either be connection less or connection oriented.

## Slide 12: Initial MS Messages
These messages are passed unchanged through BSS, but BSS analyses part of the messages and is not transparent like DTAP messages.
Between BSS and MSC, the initial MS message is transferred in the layer 3 information in the BSSMAP.
The Initial MS messages are:
CM Request
Location update request
Paging response

## Slide 13: LAPDm
Link Access Procedures on the Dm channel (LAPDm) is the layer 2 protocol used to convey signaling information between layer 3 entities across the radio interface, using the Dm channel. Dm channel refers to the control channels, independent of the type. This includes broadcast, common or dedicated control channels.
LAPDm is based on the ISDN protocol LAPD, which is used on the Abis interface. Due to the radio environment, the LAPD protocol can not be used in its original form. Therefore, LAPDm segments the message into a number of shorter messages.

## Slide 14
Data exchanged between the data link layer and the physical layer is 23 octets for BCCH, CCCH, SDCCH and FACCH. For SACCH only, 21octets are sent from layer 2 to layer 1.
LAPDm functions include:
LAPDm provides one or more data link connections on a
Dm channel. Data Link Connection Identifier (DLCI) is used for discriminating between data link connections.
It allows layer 3 message units be delivered transparently between layer 3 entities.
It provides sequence control to maintain the sequential order of frames across the data link connections.

## Slide 15: LAPDm Frame Structure
info | length | command | address
N(R) | P/F | N(S) | 0
0 | 0 | 1 | SAPI | CR | 1

## Slide 16
Sequence Number: N(S) send sequence number of the transmitted frame. N(R) is receive sequence number.
P/F : All frames contain the Poll/Final bit. In command frames, the P/F bit is referred to as the P bit. In response frames, the P/F bit is referred to as the F bit.
Service Access Point Identifier: Service Access Points (SAPs) of a layer are defined as gates through which services are offered to an adjacent higher layer.SAP is identified with the Service Access Point Identifier (SAPI).
SAPI = 0 for normal signalling of DTAP & RR
SAPI = 3 for short message services

## Slide 17
LAPDm has no error detection and correction. It is used in two modes:
Acknowledge &
Unacknowledged
and having a different structure for both.

## Slide 18: LAPD
All signaling messages on the Abis interface use the Link Access Procedures on the D-channel. (LAPD protocol). LAPD provides two kinds of signaling:
unacknowledged information
acknowledged information
LAPD link handling is a basic function to provide data links on the 64 kbps physical connections between BSC and BTS.

## Slide 19
Links are provided for operation and maintenance (O&M) of the links, for O&M of the BTS equipment and for transmission of layer 3 Abis messages.
Each physical connection can support a number of data links
(logical connections). On each physical connection each data
link is identified by a unique TEI/SAPI

## Slide 20
LAPD has three sub signalling channels
RSL (Radio Signalling Link), deals with traffic management, TRX signalling.
OML (Operation & Maintenance Link), serves for maintenance related info and transmission of traffic statistics.
L2M (Layer 2 Management), used for management of the different siganlling on the same time slot.

## Slide 21: LAPD Frame Structure
Flag | FCS | info | length | command | address | Flag
N(R ) | P/F | N(S) | 0
TEI | 1 | SAPI | CR | 0

## Slide 22
LAPD Frame structure is made up of:
Flag: Indicates the beginning and end of each frame unit. Flag has a pattern of 01111110.
FCS: Frame Check Sequence, provides the error checking for the frame. If error is found frame will be retransmitted.
Command: It has two types of structure, in acknowledge mode it has N(S) and N(R ). N(S) is a sequence number of frame sent and N(R ) is the sequence number of the frame expected to receive next.

## Slide 23
C/R: This bit indicates whether it is command or response.
P/F: In command frames, the P/F bit is referred to as the P bit and the other end transmits the response by setting this bit to F.
TEI: Terminal Endpoint Identifier, is a unique identification of each physical entity on either side like each TRX within a BTS have a unique TEI.

## Slide 24
SAPI: Service Access Point Identifier, used to identify the type of link.
SAPI = 0 for RSL
SAPI = 62 for OML
SAPI = 63 for L2ML
Each LAPD link is identify by SAPI/TEI pair.

## Slide 25: Exercise
Q1. Name the protocol which is transparent to BSS and what information is used to transfer on this protocol?
Q2. Name the protocols used between
Mobile and BTS
BTS and BSC
BSC to MSC
MSC to PSTN