## Slide 1
LTE LAYERING
L2300, L2100, L1800, L900
NOKIA TEAM

## Slide 2: CONTENT
LTE Layering & Load Balancing Principle
LTE Layering Methodology
  Spectrum Bandwidth
  Layer Coverage
  UE Capability
  Service Bearer Segregation
LTE Layering Parameter Setting
  Idle Mode
  Connected Mode

## Slide 3: CONTENT
LTE Layering & Load Balancing Principle
LTE Layering Methodology
  Spectrum Bandwidth
  Layer Coverage
  UE Capability
  Service Bearer Segregation
LTE Layering Parameter Setting
  Idle Mode
  Connected Mode

## Slide 4: Layering & Load Balancing Guide Principle
The underlying principle in layering is to keep it simple and tractable
Layering is basically implemented via very small number of design parameters:
  Absolute priorities
  “Hard exit threshold” = minimum level to camp in a cell
  “Soft exit threshold” = level to exit the layer if another lower priority layer is available
  “Entry threshold” = level to enter a higher priority layer
All LTE radio RNW parameters are aligned to these three design values!!

## Slide 5: Layering & Load Balancing Guide Principle
The target priority is to roughly balance average User throughput between layers this will compensate imbalance on PRB utilization, Connected User
Factors to consider
  Balancing end user experience on layers
  Layer carrier frequency and bandwidths
  Layer coverage footprints
  Site density per layer
  UE ecosystem distribution at Networks
  Simplicity and uniformity across the network

## Slide 6: CONTENT
LTE Layering & Load Balancing Principle
LTE Layering Methodology
  Spectrum Bandwidth
  Layer Coverage
  UE Capability
  Service Bearer Segregation
LTE Layering Parameter Setting
  Idle Mode
  Connected Mode

## Slide 7: SPECTRUM & COVERAGE FOR LAYERING APPROACH
L2300_20 (7)
L2300_10 (5)
L1800_15 (6)
L2100_5 (4)
L900_5 (3)
-5 dB
-5 dB
2 dB
9 dB
L2300 suitable for capacity densification with less coverage thus it should define as highest layer to grab traffic aggressively
Existing L1800 has higher capacity and wider coverage thus it should define as capacity layer and 2nd highest priority
L2100 has limited bandwidth and limited coverage, it should define as less priority than L1800 to maintain end user experience.
L900 has wider coverage but it only has 5 MHz bandwidth with limited capacity, thus it should define as last priority.
Note : assume same point distance for FSL calculation.

## Slide 8: Geo Location for Layering Verification
Geo – Location can verify implemented Layering strategy by analyzing the distribution of UE among layers within eNode B.
As sample beside, Most of UE camp on L1800 (EARFCN 1875) compare to L2100 (EARFCN 126) this might caused by UE capability
96% UE has RSRP > -100 dBm where this indicate overlay coverage to L2100 as potential target area for load balancing. Probability balancing at L2100 can take over ~16% from total good sample ( > -100dBm) based on coverage approach.
L1800 is still dominance taking over the traffic and possible to be more offloaded to L2100 based on coverage approach
Should Not available or less sample at L2100 need to check whether any layering parameters set is properly define or less UE ecosystem at this area,

## Slide 9: UE CAPABILITY ANALYSIS
Setting L2300 as highest priority still reasonable refers to UE capability information, where around ~ 75% UE are TDD 2300 capable in the network, it indicates potential UE which can be offloaded from L1800 to L2300 for capacity densification when L2300 set as highest priority . This information should be combine with coverage point of view. For Example : Urban area ( Denpasar City and Badung) in Bali case, around 46% of cell has TA < 500 m with number of sample > 80%, these cells are potential to be offloaded to L2300 as red site solution and layering to L2300 will perform effectively
L2100 and L900 capable UE is also quite mature where more less 75% UE in the network capable FDD L900 and more than 85% L2100. This ecosystem will support on layering performance.

## Slide 10: SERVICE BEARER BASED APPROACH
L2300_20 (7)
L2300_10 (5)
L1800_15 (6)
L2100_5 (4)
L900_5 (3)
Service bearer differentiation can be applied for GBR and Non GBR layer.
Specific layer is prioritized handling GBR service, in the other hand other layers are specify for Non GBR traffic in order to maintain non GBR cell throughput services
L900 with wider coverage and limited 5 MHz bandwidth is more priority handling GBR service
L2100 can be the 2nd GBR service handler If there is no colo L900.
L1800 & L2300 are focused handling non GBR traffic capacity
This differentiation is using Service Base Hand Over features. LTE1127 Service based mobility trigger
1st GBR
2nd GBR
Non GBR
Non GBR
Non GBR
Non GBR
Non GBR

## Slide 11: CONTENT
LTE Layering & Load Balancing Principle
LTE Layering Methodology
  Spectrum Bandwidth
  Layer Coverage
  UE Capability
  Service Bearer Segregation
LTE Layering Parameter Setting
  Idle Mode
  Connected Mode

## Slide 12: Layering Parameter Setting
IDLE MODE LAYERING STRATEGY
1
CONNECTED MODE LAYERING STRATEGY
2

## Slide 13: RADIO NETWORK LAYER
U2100 F1 is prioritized layer for PS redirection or PS Handover
U2100 F2 is prioritized for CSFB
U900 is less priority layer for CSFB and redirection. All layer activate reselection from and to LTE, Smart LTE layering is enable at cell with LTE overlay coverage
L2300_20 (7)
L1800_15 (6)
U2100 (2)
U900 (1)
GSM (0)
TDD - L2300 20 MHz reserved highest priority in Layering for capacity issue.
FDD - L1800 15 TDD - L2300 10 MHz set as 2nd priority layering
TDD - L2300 10 MHz reserved 3rd priority in layering
FDD - L2100 5 MHz has 4rd priority in layering since it has limited capacity
FDD - L900 5 MHz has 5rd priority in layering
Load balancing among layers using Idle Mode Load Balancing, Connected load balancing subject to trial
L2300_10 (5)
GSM is will handle voice traffic and encourage for traffic migration to LTE or UTRAN
L2100_5 (4)
L900_5 (3)

## Slide 14: IDLE MODE STRATEGY
RAT_1 f_1
L2100_5
U2100
U2100
U900
CSFB
SLL
U2100
U2100
U900
L2100_5
L1800_15
L1800_15
U2100
U900
Cell Priority Setting: L1800 (6) > L2100 (4) > L900 (3)
CSFB
CSFB
CSFB
SLL
SLL
SLL
L1800 <-116 dBm
L2100> -110 dBm
L1800 >-110 dBm
L1800 >-110 dBm
L1800 <-116 dBm
L900 > -110 dBm
Reselection Intra Frequency
Start measure = -62 dBm all layer
Qrxlevmin = -124 dBm
Applied for all LTE Layer
L900
U2100
U900
L900
CSFB
CSFB
SLL
L2100 <-116 dBm
L900 > -110 dBm
L2100_10 >-100 dBm
SLL
L21/L900 <-116 dBm
U21/900 > -101 dBm
Reselection Inter Frequency
Start measure = -104 dBm L900 & L2100
L900
L900
L2300_20/10
L2300_20/10
L1800_15
L2100_5
L2300_20/10
L2300 <-116 dBm
L1800> -110 dBm
L2300 >-110 dBm

## Slide 15: IDLE MODE LOAD BALANCING
L2100_5
L1800_15
L2300 _20 MHz has highest priority on layering to densify high traffic area and offloading L1800 red site thus it should aggressively grab traffic. Its MLB trigger to exit layer should less aggressive.
L1800_15 MHz has 2nd highest selection priority at SIB Broadcast and it has better capacity, the IMLB trigger should set less aggressively to make UE 2nd prefer camp on L1800 and give better user experience at L1800 instead of L2100 and L900 with limited 5MHz capacity.
Target carrier for load balancing should has RSRP > -95 dBm RSRP for FDD 2100 & L900, > -100 dBm RSRP and -12 dB RSRQ for FDD 1800 and L2300 to avoid ping pong and UE camp to worst carrier
FDD 1800 & L2300 Load balancing will be trigered if Composite Available Capacity (CAC) is less than 30%, while FDD 2100 & FDD 900 will triger if CAC < 70% which means a more aggressive
idleLBCapThresh & idleLBPercentageOfUes are adjustable to obtain expected balancing figure and end user experience trade off.
-100 dBm
-95 dBm
L900_5
L2300_20/10

## Slide 16: IDLE MODE LOAD BALANCING
L2100_5
L1800_15
L900_5
L2100_5
L1800_15
L900_5
100
30
30
Target carrier weighting are set with L1800 has highest weighting for better end user experience.
L900 and L2100 has less weighting as target carrier for reselection due to less capacity (5 MHz)
Weighting is adjustable to obtain expected balancing figure
Load balancing figure is also subject to UE band capability in the network
L2300_20 & 10
L2300_20 & 10

## Slide 17: LAYERING STRATEGY
IDLE MODE LAYERING STRATEGY
1
CONNECTED MODE LAYERING STRATEGY
2

## Slide 18: CONNECTED MODE STRATEGY
RAT_1 f_1
L2100_5
U2100
U2100
U900
U2100
U2100
U900
LTE > -116 dBm
CSFB
L2100_5
LTE > -116 dBm
L1800_15
L1800_15
U2100
U2100
U900
A3 = 5 dB/A5 Event
Intra Freq measurement start = -50 dBm
A3 Event
A3 Event
Redirection < -116 dBm
PS HO < -115 dBm
L900
L900
A3 = 3dB/A5 Event
A3 = 5 dB/A5 Event
L900
L900
A3 = 3dB/A5 Event
Inter Freq measurement start :
L2300_20 MHz = -108 dBm
L2300_10 MHz = -105 dBm
L1800 = -108 dBm
L2100 = -105 dBm L900 = -105 dBm
A3 = 5dB/A5 Event
Redirection < -116 dBm
PS HO < -115 dBm
Redirection < -116 dBm
PS HO < -115 dBm
L2300_20/10
L2300_20/10
L2300_20/10
A3 = 5dB/A5 Event
A3 = 3 dB/A5 Event

## Slide 19: CONNECTED MODE STRATEGY
Handover Measurement Triggers
threshold1 = 75 = -65 dBm
threshold2a = 36 = -104 dBm
threshold2InterFreq = 32 = -108dBm
threshold2Wcdma = 28 = -112 dBm
threshold4 = 24 = -116 dBm
Handover Measurement Triggers
threshold1 = 75 = -65 dBm
threshold2a = 40 = -100 dBm
threshold2InterFreq = 36 = -104dBm
threshold2Wcdma = 24 = -112 dBm
threshold4 = 24 = -116 dBm
L1800 & L2300
L900 & L2100

## Slide 20: IRAT Handover & Redirection Strategy
RAT_1 f_1
L23/L21/L18/L9
U2100
L23/L21/L18/L9
U2100
U900
CSFB with Redirection
PS HO
LTE < -115 dBm
3G > -105 dBm
U2100
U2100
U900
Redirection
LTE < -116dBm
Connected Mode :
CS services by CSFB with Redirection
IRAT PS Handover and PS redirection are implemented for connected mode mobility to UTRAN
Smart LTE Layering used for redirection from 3G to LTE
SRVCC might be applied when VoLTE is implemented in Network
L23/L21/L18/L9
L23/L21/L18/L9

## Slide 21: CSFB & REDIRECTION TO 3G
U2100 F1/F2/F3
U900
U2100 F1/F2/F3
U900
CSFB priority
Redirection
priority
CSFB Priority setting:
U21 F1 > U21 F2 > U9 F3
PS Redirection Priority setting:
U21 F2 > U21 F1 > U9 F3
SLL
3G > -104 dBm
PS Redirection trigger:
-116 dBm
CSFB via redirection Activation
LNBTS
actCSFBRedir= 1 = enabled
Redirection Trigger
LNCEL
threshold4 = 24 = -116 dBm
a2TimeToTriggerRedirect = 5 = 128ms
Redirection to 3G
REDRT
Priority setting:
U21 F1 > U21 F2 > U9 F3 for CSFB
U21 F2 > U21 F1 > U9 F3 for PS Redirect
Redrtid | 0 | 1 | 2
redirFreqUtra | U900 | U2100 | U2100
csfallBPrio | 4 | 1 | 2
emerCallPrio | 4 | 1 | 2
redirectPrio | 4 | 3 | 2
All U21 layers should have same priority and higher than U9
Note : 1 is highest priority
L23/L21/L18/L9
L23/L21/L18/L9

## Slide 22: IRAT PS HO TO 3G
U900
U900
CSFB priority
Serving cell
RSRP < -115 dBm
3G Nbrcell:
EcNo> -14 dBm
Or
RSCP > -105 dBm
SLL
3G > -104 dBm
Handover Activation
LNBTS
actHOtoWcdma= 1 = true
actCsfbPsHoToUtra= 1 = true
Handover Measurement Triggers
LNCEL
threshold2a = 36 = -104 dBm
threshold2Wcdma = 28 = -112 dBm
IRAT HO to 3G Triggers
LNHOW
reportIntervalUtra= 2 = 480 ms
PS Handover
b2Threshold1Utra = 25 = -115 dBm b2Threshold2UtraEcn0 = 24 = -12 dB b2Threshold2UtraRscp = 10 = -105 dBm b2TimeToTriggerUtraMeas = 9 = 480 ms
Neighbours
LNADJW
Create by ANR to UTRAN
IRAT 3G Measurement trigger: -112 dBm
L23/L21/L18/L9
L23/L21/L18/L9
U2100 F1/F2/F3
U2100 F1/F2/F3

## Slide 23: SRVCC TO 3G (OPTIONAL)
U900
U900
CSFB priority
Serving cell
RSRP < -112 dBm
3G Nbrcell:
EcNo> -12 dBm
Or
RSCP > -100 dBm
SLL
3G > -104 dBm
SRVCC Activation
LNBTS
actSrvccToWcdma = 1 = true
actServBasedMobThr= 1 = true
SRVCC Measurement Triggers.
LNCEL (L1800,L2300)
threshold2aQci1 = 34= -106 dBm
threshold2WcdmaQci1 = 30 = -110 dBm
LNCEL (L900,L2100)
threshold2aQci1 = 34= -102 dBm
threshold2WcdmaQci1 = 30 = -104 dBm
SRVCC Threshold ( L1800, L2300)
b2Threshold1UtraQci1 = 25 = -112 dBm b2Threshold2UtraEcnoQci1 = 24 = -12 dB b2Threshold2UtraRscpQci1 = 10 = -100 dBm b2TimeToTriggerUtraMeas = 9 = 480 ms
Neighbours
LNADJW
Create by ANR to UTRAN
SRVCC 3G Measurement trigger
L1800/L2300 : -110 dBm
L900/L2100 : -104 dBm
L23/L21/L18/L9
L23/L21/L18/L9
U2100 F1/F2/F3
U2100 F1/F2/F3
SRVCC Threshold ( L2100, L900)
b2Threshold1UtraQci1 = 25 = -106 dBm b2Threshold2UtraEcnoQci1 = 24 = -12 dB b2Threshold2UtraRscpQci1 = 10 = -100 dBm b2TimeToTriggerUtraMeas = 9 = 480 ms
L900 & L2100 set to early trigger due to throughput performance

## Slide 24: VoLTE Layering ( OPTIONAL)
L2300_20 (7)
L2300_10 (5)
L1800_15 (6)
L2100_5 (4)
L900_5 (3)
VoLTE layering is LTE1127 Service based mobility trigger to specify VoLTE Layers
The objective of this scenario is to maintain Non GBR user throughput when VoLTE is introduced to existing networks
High number of VoIP UEs in the cell degrades total cell throughput and limits throughput for other services due to lower priority resources for non-GBR traffic are limited
1st GBR
2nd GBR
Non GBR
Non GBR
Non GBR
Non GBR
Non GBR
actInterFreqServiceBasedHo = 1
freqLayListServiceBasedHo ( create at MOPR & MODPR) = EARFCN L900 & L2100

## Slide 25: UTRAN – LTE Layering Guideline (U21/U9 – L18/L21/L9)
EcNo: -12 dB
RSCP: -105 dBm
Idle Mode
Cell PCH/URA PCH
Cell FACH
Cell DCH
ECM IDLE
ECM CONNECTED
QRxlevMin : -124 dBm (-124)
QqualMin : -18 (-18)
QrxlevMin : -115 dBm (-58)
Abs Priority L1800 (6) > L2100 (4) > L900 (3)
Abs Priority (2)
RSRP :
-108 dBm
AdjLQrxlevminEUTRA: -124 dBm (-62)
AdjLThreshigh: 16 dB (8)
RSRP :
-116 dBm
qrxlevmin: -124 dBm (-124)
threshSrvLow: 8 dB (8)
qQualMinUtra: -18 dB (-18)
qRxLevMinUtra: -101 dBm (-101)
EcNo: -18 dB
RSCP: -101 dBm
SmartLTELayeringEnabled: (4) or (8)
T1: RRC state change Cell_DCH to CCH
SmartLTELayeringEnabled: (4) or (8)
T2: HSDPA/HSPA to DCH/DCH CTS
T3: CS RAB release
SmartLTELayeringEnabled: (8)
T4: Periodic trigger
AdjLMinRSRPLevel -108 dBm (-54)
AdjLMinRSRQLevel: -12dB (-24)
RSRP :
-108 dBm
AdjLQrxlevminEUTRA: -124 dBm (-62)
AdjLThreshigh: 16 dB (8)
RSRP -108 dBm
RSRQ: -12dB
LTEHandoverEnabled: Disabled (0)
Cell Selection
Re-direction (Blind)
Re-direction (Blind)
Re-direction (Meas)
UE Context Re-direction (Blind)
RSRP : -116 dBm
Threshold4: -116 dBm (24)
hysThreshold4 : 0 dB (0)
Cell Selection
Cell Selection
PS HO
PS HO
CSFB via Re-direction (Blind)
b1ThresholdCSFBUtraRscp: -105 dBm (10)
b1ThresholdCSFBUtraEcn0: -12 dB (24)
SmartLTELayeringRSCP: -95 dBm
Meas RSRP -112 dBm
B2 Reporting RSRP
: -115 dBm
EcNo: -12 dB
RSCP: -105 dBm
threshold2Wcdma: -112 dBm (28)
hysThreshold2Wcdma: 0 dB (0)
b2Threshold1Utra: -115 dBm (25)
b2Threshold2UtraEcn0: -12 dB (24)
b2Threshold2UtraRscp: -105 dBm (10)
CSFB via PSHO

## Slide 26: Intra LTE Neighboring Strategy
L2100_5
L1800_15
L900_5
L2100_5
L1800_15
L900_5
All LTE cells create neighbor toward intra frequency and inter frequency for all carrier
ANR to Intra/inter frequency LTE feature is appled for neighbor creation.
L2300_20 & 10
L2300_20 & 10

## Slide 27: UTRAN - LTE Neighboring Strategy
L1800_15
L2300_20 & 10
L2100_5
U2100_F2
U900_F3
U2100_F1
All LTE cells create neighbor toward all UTRAN carrier (U2100 F1, U2100 F2 and U900) on LNADJW and LNRELW. Create maximum 32 Neighbor each UTRAN carrier.
create HO identifier for each UTRAN Carrier (U2100 F1, U2100 F2 and U900) on LNHOW
ANR to UTRAN feature recommend to be apply for neighbor creation.
All UTRAN cells create neighbor toward all LTE carrier (L2300, L1800 L2100 & L900) on ADJL and ADJE. Create maximum 32 Neighbor each LTE carrier
create HO identifier for each LTE Carrier (L2300, L1800 L2100 & L900) on HOPL
L900_5

## Slide 28
BACK UP

## Slide 29: Average User Throughput Analysis

## Slide 30: Layering strategy and load balancing
LTE entry trigger:
RSRP > -110dBm
LTE exit trigger:
RSRP < -116dBm
UMTS entry trigger:
RSCP > -107dBm
Ec/N0 > -16dB
TD-LTE2300 20M (prio7)
Camping thresholds:
RSRP min > -118dBm
RSCP min > -115dBm
Ec/N0 min > -18dB
rxLevAccessMin > -105dBm (G18)
rxLevAccessMin > -102dBm (G9)
UMTS2100 3x5M (prio3)
UMTS900 1x5M (prio2)
LTE850 10M (prio4)
GSM900 (prio0)
GSM1800 (prio1)
LTE1800 15M (prio6)
TD-LTE2300 10M (prio5)
LTE2100 10M (prio5)
LTE700 15M (prio7)
Layer absolute priorities and entry/exit level thresholds (end state)
Notes: Rationale for having LTE700 at highest priority: LTE700 terminal penetration is around 30% in metro manila (Aug’16). All LTE700 capable UEs should be pushed to LTE700/15MHz. In case of overload, apply idle mode load balancing.

## Slide 31: Layering strategy and load balancing
NOKIA-proposed layering
Initial step prios L7-> L18->L21->L85
Second step prios L18-> L7->L21->L85 (A)
Exit/entry: -116/-112dBm for all layers
L18<->L7 prio swap results in L18 becoming most congested layer
Layer avg UE tputs still about balanced!!
This will change if/when L7/L18 densified
A
UE tput fairly well balanced, L18 worst