## Slide 1: CSFB Performance
February, 2013
Contain NSN INTERNAL SLIDES – please remove those ones from customer presentation

## Slide 2
CSFB overlay performance problems
An overlay solution (Mavenir/Huawei/E/NSN) CSFB always will take place in 2G/3G MSC. In case of MT CSFB call there is following behaviour when overlay is used:
terminated call coming from GMSC to overlay CSFB MSC (or IWF in case of Mavenir)
CSFB MSC paging terminal over the SGs interface
terminal moves to 2G/3G and do Location Update there target MSC do not know this is a CSFB call. After LU radio resources are released
After LU– CSFB MSC is able to re-route MT call to target MSC (it has a VLR address of target MSC)
Target MSC needs to page terminal there  This take additional seconds!!!!!!! So, without any improvements – CSFB call set-up easily takes 4-5 sec. longer than CS call set-up.
We have implemented in M15.1 and also available in M14.6 CD9 and CD10 feature called CSMT-flag (3GPP Release 9). So, when LU take place in target MSC terminal sends this parameter to 2G/3G MSC to indicate this is a CSFB call. So, in this case 2G/3G MSC keeps radio resources reserved few seconds and waiting for coming MT call. This way call set-up time is much faster in target MSC.
NSN INTERNAL SLIDE
Summary:
Make sure you order CSMT-flag feature in all 2G/3G MSC Servers in LTE coverage
Make sure this feature is activated (on) in 2G/3G MSC server when doing our CSFB testing
Make sure this feature is not (off) activated in 2G/3G MSC server in case our competitor is doing their CSFB testing – this feature is part of our CSFB solution.
.
NSN INTERNAL SLIDE

## Slide 3: CSFB call setup time factors
Used mobility method between radios (LTE – 2G/3G)
    Redirect based CSFB to 2G/3G
    PSHO based CSFB to 3G
    Redirect based CSFB to 2G/3G with SIB (System Information Block)
Used MSC Server (MSS) deployment
    CSFB in every MSS
    Overlay CSFB with MTRF (Mobile Terminating Roaming Forwarding )
    Overlay with MTRR (Mobile Terminating Roaming Retry)
    CSMT-flag (3GPP Release 9) support in 2G/3G MSS when MSC Server is changed in CSFB MT call

## Slide 4: Used Hand Over (HO) method between radios (LTE – 2G/3G)
    Redirect based CSFB to 2G/3G - CSFB via redirect allows for a service based redirection from LTE to UTRAN or to GSM during the call setup. The operator can configure priorities for the target frequency bands per cell. eNB selects the highest priority layer supported by UE. UE does not have any pre-information about the target cell.
    PSHO based CSFB to 3G - eNB starts upon the CSFB trigger IRAT measurements to identify suitable target cells. eNB performs a PS handover once a suitable UTRAN target cell has been found. Resources are reserved beforehand in target radio and this way call setup delay is reduced and reliability of call setup is increased. PSHO is used also with SRVCC.
    Redirect based CSFB to 2G/3G with SIB (System Information Block) - System information for up to 16 cells can be configured by O&M; as further optimization, RIM procedure may be deployed for retrieving system information from UTRAN. The system information provided together with the RRC connection release message will reduce the overall call setup time.

## Slide 5: CSFB MSC Server deployment options
CSFB in every MSS (SGs interface is provided by all MSSes )
Terminal fall back from LTE to 2G/3G to the same MSS
Usually no Location Update (LU) needed in CS side
Able to minimize needed signaling between the VLR and HLR, because of no need for VLR update
CSFB MSS have only LTE interface (SGs) and not 2G/3G interfaces (A/Iu)
Terminal fall back from LTE to 2G/3G to the different MSS
Location Update (LU) is needed always in CS side
Cause more signaling between the VLR and HLR due the many VLR updates
2G/3G
LTE
MSS
MME
MSS
MSS
2G/3G
LTE
MSS
MME
MSS
MSS
CSFB MSS

## Slide 6: Average CSFB Call setup times
Delta between 3G CS call setup time and CSFB to 3G call setup time indicated in the table | a) 3G/LTE in same CSFB MSS | b) Overlay CSFB MSS
1) Redirect based CSFB to 2G/3G | + 1.0-1.5 sec | +2.0 –3.0 sec
2) PSHO based CSFB to 3G, (delta to 1) | -0.4 sec | -0.4 sec
3) Redirect based CSFB to 2G/3G with SIB , (delta to 1) | -0.3 sec | -0.3 sec
4) Redirect based CSFB to 3G with deferred SIB 11/12 reading, (delta to 1) | - 0.4 sec | -0.4 sec
Above results based on lab measurements in NSN R&D lab and customers’ test labs. In live networks call set-up times seems to be ~1 sec longer than in optimal lab conditions.
In case CSMT-flag not supported in target MSS, then call set-up time can be 1-5 second longer - depends on network configuration in 2G/3G. Note! See slide nr 2 i.e. do you want to share this info with customer
PSHO is expected to improve call success rate as target (3G) radio resources are reserved beforehand.
CSFB to 2G (GSM) today takes ~1.0-1.5 sec longer than CSFB to 3G (WCDMA) in both MO and MT. Reason is slower reading of SIB information in 2G side compare to 3G.
    Much longer (5-10 seconds) setup time in case CSFB primary target is 3G but only 2G available in that area
.
Note! As call set-up time values vary between the networks in many reasons, these values need to be taken as informative ones. Also measurement methods varied in different cases. In case a) most of the extra delay is coming from radio and terminal. Cases b) and c) voice core configuration increase the delay.
NSN INTERNAL info with red color in a text

## Slide 7: MT CSFB added delay – data from live deployments (LTE/3G) November 2012 – CSFB in every MSS
Average ~2.3s
Average ~2.2s
Data is taken from NSN live network deployments offering commercial CSFB service
MSC Server CSFB counters used for collecting example data
Counter is measured from sending a SGsAP_Paging_Request (from MSS/VLR to MME) until receiving
        Paging_response (Location Area remains same)
        Location_update (Location Area changes)
        Cancel Location from HLR or Send Identification from other MSS (overlay MSS)
      Note! Paging time included (~0.5 sec) these results – paging is part of the CS MT call set-up as well.

## Slide 8: NSN CSFB with possibility for early ring back tone
Calling party can hear continues ring back tone already before CSFB procedure for called party started
Gives the best possible user expediency in case additional time comes from CSFB procedure is seen significant from end user point of view.
Overlay NSN CSFB MSS able to give ring back tone almost instantly thanks to using the MGW. It is definitely much more comfortable to the user than hearing many seconds of silence before it starts, which is a case when CSFB overlay is done without MGW support. (TMN Portugal, 2012)

## Slide 9: How to optimize CSFB time with MSS parameters in overlay configuration

## Slide 10: Usage of CSMT Flag
In the CSFB overlay configuration it is important that the CSMT flag support is enabled in all MSSs in the operator network.
When new MSS receives the CSMT flag in LU request, it will keep the signaling connection to the UE even when LU procedure is finished.
This eliminates the need for a further paging procedure in the new MSS before the call setup, which directly lowers the CSFB setup time by 1.0 - 1.5 s (or even more)
In addition to the lower CSFB setup time, usage of CSMT flag is likely to improve the CSFB call setup success ratio.
CSMT flag support has been available in NSN MSS since M15.1
NSN INTERNAL – see CSMT story in slide nr 2

## Slide 11: Usage of SendIdentification messages
It’s recommended to configure all MSSs to send MAP “SendIdentification” message towards the CSFB MSS to request identity and security info from overlay MSS instead of requesting it from UE.
MSSs needs to have LAC of the overlay MSS configured, as network location area, to be able to send the SendIdentification messages
Case overlay MSS LAC not configured: When the UE performs Location update it sends TMSI and the new MSS sends Identity Request message to the UE to get the IMSI, and then MSS interrogates HLR for Authentication vectors. That process takes an average of 0.5 seconds.
Case overlay MSS LAC Configured: When the UE performs Location update it sends TMSI and the new MSS sends SendIdentification message to old MSS to get IMSI and authentication vectors. That process takes an average of 0.1 seconds.
This configuration has been observed to save in average 0.4 s from CSFB procedure.

## Slide 12: Changing “ROUT_DELAY_TIME_PMTRF” in Overlay MSS
HLR sends MAP Cancel Location to the overlay MSS in the start of the LU procedure or when LU it is finished.
When the overlay MSS receives the MAP Cancel Location message it waits the time given by the parameter ROUT_DELAY_TIME_PMTRF before routing of the call to new MSS, to make sure that the LU is finished with the new MSS.
Lowering the timer value given in ROUT_DELAY_TIME_PMTRF the CSFB call setup time can be directly shorted.
It needs to be verified that the parameter value still allows the LU to finish.
In one customer case CSFB overlay MSS (M15.1) timer changed from 1 seconds (default value) to 0.2 seconds which reduced call setup time by 0.8 seconds

## Slide 13: Changing Location Update parameters
The LU for the new MSS can cause TMSI Allocation or/and Authentication and/or IMEI checking for the UE.
This generates an additional delay for CSFB call set-up time as with overlay CSFB the LU is always executed when CSFB takes place towards to a new MSS.
M16.1 implements feature called “Different frequencies of execution for Authentication, TMSI Reallocation and Identity Check when UE performs CSFB”.
USAGE FREQUENCY COUNTERS (0 = NOT USED)
TMSI ALLOCATION
LOC UP NEW VIS: 1 LOC UP: 0 PER UP: 1
IMSI ATTACH: 1 MO CALL: 20 MO SMS: 20
MT CALL: 0 MT SMS: 0
MT USSD: 0 SS OPER: 0
AUTHENTICATION
LOC UP NEW VIS: 1 LOC UP: 0 PER UP: 0
IMSI ATTACH: 1 MO CALL: 10 MO SMS: 10
MT CALL: 0 MT SMS: 0
MT USSD: 0 SS OPER: 0
IMEI CHECKING
LOC UP NEW VIS: 1 LOC UP: 5 PER UP: 10
IMSI ATTACH: 0 MO CALL: 0 MO SMS: 0
MT CALL: 0 MT SMS: 0
MT USSD: 0 SS OPER: 0
Until M16.1 it is also possible to modify the parameters so that procedures don’t take place for each new visitor.
It should be noted that changing these parameters effects to all LUs for new visitors, not only those caused by CSFB.
In one customers case the operator was able to save in average 0.55 s from CSFB procedure by modifying Authentication and IMEI Check parameters from 1 to 0.45 in M14.6 3G MSS. Parameter value change effects all subscribers in M14.6 – not only CSFB subscribers – need LU procedure.

## Slide 14: Terminal return to LTE

## Slide 15: Terminal return back to LTE
MSC Server functionality when terminal stays in 2G/3G after CSFB and no LU
Terminals remain reachable for MT calls during ‘LTE return back’
Situation: CSFB support in every MSS. The LAI remains the same during the CSFB i.e. no LU. The terminal is in 2G/3G after a CSFB call and a new MT call is coming in.
Option 1: No location update is triggered during the CSFB procedure (LAI remains the same). In this case the CSFB-enabled MSS is able to re-page over the A/Iu interface in reaction to a paging failure over SGs.
Option 2: The CSFB-enabled MSS is configured in a way that the terminal is triggering a location update despite the LAI remaining the same.
R10 enhanced features to make fast return from 2G/3G to LTE
There are 2 method for Fast return solution:
    BSC/RNC solution :When call for LTE capable mobile is released and BSC supports the same LTE mode (FDD or TDD) as mobile then BSC includes LTE neighbour cell frequency/frequencies and other LTE neighbour related data in Channel Release message (LTE neighbour parameters are user configurable). With this information mobile can measure/select adequate target LTE cell and move directly to LTE.
    MSC + BSC/RNC solution: Based on 3GPP 48.008 V11, when MSC send the clear command message, there is a “CSFB indication” to inform BSC, BSC can take fast return action based on this indicator.
When these features are available, UE will get back to LTE in less than 2 seconds. These features are supported by the terminals already.

## Slide 16: Thank you for your reading