## Slide 1
Lu Yueyue/wx445705
2020.1
New
New

## Slide 2: Data Communication Network Basis

## Slide 3
Communication has always been with us ever since the origin of human society. Communication has been playing an increasingly important role especially since human society entered the information era in the 1970s or 1980s.
The communication mentioned in this course refers to the communication implemented through a data communication network. This course describes the concepts related to communication and a data communication network, information transfer process, network devices and their functions, network types, and typical networking. In addition, this course briefly introduces the concepts related to network engineering and network engineers.

## Slide 4
On completion of this course, you will be able to:
  Understand the concepts related to communication and a data communication network.
  Be able to describe the information transfer process.
  Differentiate network devices of different types and understand their basic functions.
  Understand different network types and topology types.
  Understand the concepts related to network engineering and network engineers.

## Slide 5: Huawei Device Icons
General router
General switch
Core switch
Aggregation switch
Access switch
Firewall
Stacked switches
AP
General NMS
Internet
Network cloud 1
Authentication server
FTP server
General server
Enterprise network user
PN user
Enterprise
Base station
Business trip
PC
Pad
Mobile phone
Laptop
IP phone
AC
Wi-Fi signals
Cluster
Network cloud 2

## Slide 6
Communication and Networks
Network Types and Topology Types
Network Engineering and Network Engineers

## Slide 7: Concept of Network Communication
Communication refers to the information transfer and exchange between people, between people and things, and between things through a certain medium and behavior.
Network communication refers to communication between terminal devices through a computer network.
Examples of network communication:
A. Files are transferred between two computers (terminals) through a network cable.
C. A computer (terminal) downloads files through the Internet.
B. Files are transferred among multiple computers (terminals) through a router.
...
Data
Data
Data
Router
Network communication
Data communication network
Notes: Examples of network communication:
  A. Two computers connected with a network cable form the simplest network.
  B. A small network consists of a router (or switch) and multiple computers. In such a network, files can be freely transferred between every two computers through the router or switch.
  C. To download a file from a website, a computer must first access the Internet.
The Internet is the largest computer network in the world. Its predecessor, Advanced Research Projects Agency Network (ARPAnet), was born in 1969. The wide popularization and application of the Internet is one of the landmarks of the information age.

## Slide 8: Information Transfer Process
Virtual information transfer is similar to real object transfer.
Objects
Package
Distribution center
Sky
Distribution center
Package
Objects
Computer
Gateway router
Internet
Gateway router
Computer
Data
Data
Packet
Data
Packet
Data
Network communication
Data communication network
Notes: Comparison between express delivery (object transfer) and network communication:
Objects to be delivered by express delivery:
  The application generates the information (or data) to be delivered.
The objects are packaged and attached with a delivery form containing the name and address of the consignee.
  The application packs the data into the original "data payload", and adds the "header" and "tail" to form a packet. The important information in the packet is the address information of the receiver, that is, the "destination address".
  The process of adding some new information segments to an information unit to form a new information unit is called encapsulation.
The package is sent to the distribution center, where packages are sorted based on the destination addresses and the packages destined for the same city are placed on the same plane.
  The packet reaches the gateway through the network cable. After receiving the packet, the gateway decapsulates the packet, reads the destination address, and then re-encapsulates the packet. Then, the gateway sends the packet to a router based on the destination address. After being transmitted through the gateway and router, the packet leaves the local network and enters the Internet for transmission.
  The network cable functions similarly as the highway. The network cable is the medium for information transfer.

## Slide 9
Notes: Upon arrival at the destination airport, packages are taken out for sorting, and those destined for the same district are sent to the same distribution center.
  After the packet reaches the local network where the destination address resides through the Internet, the gateway or router of the local network decapsulates and encapsulates the packet, and then sends the packet to the next router according to the destination address. Finally, the packet reaches the gateway of the network where the destination computer resides.
The distribution center sorts the packages based on the destination addresses. Couriers deliver packages to recipients. Each recipient unpacks the package and accepts the package after confirming that the objects are intact, indicating that the whole delivery process is complete.
  After the packet reaches the gateway of the network where the destination computer resides, the packet is decapsulated and encapsulated, and then sent to the corresponding computer according to the destination address. After receiving the packet, the computer verifies the packet. If the packet passes the verification, the computer accepts the packet and sends the data payload to the corresponding application for processing, indicating that the network communication process ends.

## Slide 10: Common Terms
Term | Description
Data payload | Information conveyed
Packet | Data unit switched and transmitted on the network
Header | Information segment added before the data payload
Tail | Information segment added after the data payload
Encapsulation | Process of adding a header and a tail to a data payload to form a new packet
Decapsulation | Process of removing the header and tail from a packet to obtain the data payload
Gateway | Network device that provides functions such as protocol conversion, route selection, and data exchange
Router | Network device that selects a forwarding path for packets
Terminal device | End device of a data communication system, used as a sender or receiver of data
Network communication
Data communication network
Notes: Data payload: It can be considered as the information to be transmitted. However, in a hierarchical communication process, the data unit (packet) transmitted from the upper layer to the lower layer can be called the data payload of the lower layer.
Packet: a data unit that is exchanged and transmitted on a network. It is in the format of header+data payload+tail. During transmission, the format and content of packets may change.
Header: The information segment added before the data payload during packet assembly to facilitate information transmission is called the packet header.
Tail: The information segment added after the payload to facilitate information transmission is called the tail of a packet. Note that many packets do not have tails.
Encapsulation: A technology used by layered protocols. When the lower-layer protocol receives a message from the upper-layer protocol, the message is added to the data part of the lower-layer frame.
Decapsulation: It is the reverse process of encapsulation. That is, the header and tail of a packet are removed to obtain the data payload.
Gateway: A gateway is a network device that provides functions such as protocol conversion, route selection, and data exchange when networks using different architectures or protocols communicate with each other. A gateway is a term that is named based on its deployment location and functionality, rather than a specific device type.
Router: a network device that selects a transmission path for a packet.
Terminal device: It is the end device of the data communication system. As the data sender or receiver, the terminal device provides the necessary functions required by the user access protocol operations. The terminal device may be a computer, server, VoIP, or mobile phone.

## Slide 11: Concept of the Data Communication Network
...
...
...
Internet
Office area 1
Office area 2
Office area 3
Core equipment room
Log system
Controller
NMS
Application server
Data communication network:
  Communication network that consists of routers, switches, firewalls, access controllers (ACs), access points (APs), PCs, network printers, and servers
Function:
  To implement data communication
Network communication
Data communication network

## Slide 12: Switches
Switch: a device closest to end users, used to access the network and switch data frames
  Network access of terminals (such as PCs and servers)
  Layer 2 switching
Switch
Broadcast domain
Network communication
Data communication network
Notes: Switches:
  On a campus network, a switch is the device closest to end users and is used to connect terminals to the campus network. Switches at the access layer are usually Layer 2 switches and are also called Ethernet switches. Layer 2 refers to the data link layer of the TCP/IP reference model.
  The Ethernet switch can implement the following functions: data frame switching, access of end user devices, basic access security functions, and Layer 2 link redundancy.
  Broadcast domain: A set of nodes that can receive broadcast packets from a node.

## Slide 13: Routers
Router: a network-layer device that forwards data packets on the Internet. Based on the destination address in a received packet, a router selects a path to send the packet to the next router or destination. The last router on the path is responsible for sending the packet to the destination host.
  Implementing communication between networks of the same type or different types
  Isolating broadcast domains
  Maintaining the routing table and running routing protocols
  Selecting routes and forwarding IP packets
  Implementing WAN access and network address translation
  Connecting Layer 2 networks established through switches
Router
Broadcast domain B
Broadcast domain A
Network communication
Data communication network
Notes: Routers:
  Routers work at the network layer of the TCP/IP reference model.
  Routers can implement the following functions: routing table and routing information maintenance, route discovery and path selection, data forwarding, broadcast domain isolation, WAN access, network address translation, and specific security functions.

## Slide 14: Firewalls
Firewall: a network security device used to ensure secure communication between two networks. It monitors, restricts, and modifies data flows passing through it to shield information, structure, and running status of internal networks from the public network.
  Isolating networks of different security levels
  Implementing access control (using security policies) between networks of different security levels
  Implementing user identity authentication
  Implementing remote access
  Supporting data encryption and VPN services
  Implementing network address translation
  Implementing other security functions
Trust zone
DMZ
Firewall
Untrust zone
Internet
Network communication
Data communication network
Notes: Firewall:
  It is located between two networks with different trust levels (for example, between an intranet and the Internet). It controls the communication between the two networks and forcibly implements unified security policies to prevent unauthorized access to important information resources.

## Slide 15: Wireless devices
AC
Fit AP
Wireless terminal
Wireless terminal
Internet
Fat AP
WLAN (Wi-Fi)
Wired terminal
Wireless terminal
Internet
Network communication
Data communication network
Notes: In a broad sense, WLAN is a network that uses radio waves, laser, and infrared signals to replace some or all transmission media in a wired LAN. Common Wi-Fi is a WLAN technology based on the IEEE 802.11 family of standards.
On a WLAN, common devices include fat APs, fit APs, and ACs.
  AP:
    Generally, it supports the fat AP, fit AP, and cloud-based management modes. You can flexibly switch between these modes based on network planning requirements.
    Fat AP: It is applicable to homes. It works independently and needs to be configured separately. It has simple functions and low costs.
    Fit AP: It applies to medium- and large-sized enterprises. It needs to work with the AC and is managed and configured by the AC.
    Cloud-based management: It applies to small- and medium-sized enterprises. It needs to work with the cloud-based management platform for unified management and configuration. It provides various functions and supports plug-and-play.
  AC:
    It is generally deployed at the aggregation layer of the entire network to provide high-speed, secure, and reliable WLAN services.
    The AC provides wireless data control services featuring large capacity, high performance, high reliability, easy installation, and easy maintenance. It features flexible networking and energy saving.

## Slide 16
Communication and Networks
Network Types and Topology Types
Network Engineering and Network Engineers

## Slide 17: LAN, MAN, and WAN
Based on the geographical coverage, networks can be classified into local area networks (LANs), metropolitan area networks (MANs), and wide area networks (WANs).
  LAN
    A LAN is a network that consists of computers, servers, and network devices in a geographic area. The coverage of a LAN is generally within several thousand square meters.
    Typical LANs include a company's office network, a cyber bar network, a home network.
  MAN
    A MAN is a computer communication network established within a city.
    Typical MANs include broadband MANs, education MANs, and municipal or provincial e-government private lines.
  WAN
    A WAN generally covers a large geographical area ranging from tens of square kilometers to thousands of square kilometers. It can connect networks of multiple cities or even networks of countries (as an international large-scale network) and provide long-distance communication.
    The Internet is a typical WAN.
Network Types
Network Topologies
Notes: Based on the geographical coverage, networks can be classified into LANs, WANs, and MANs.
LAN:
  Basic characteristics:
    An LAN generally covers an area of a few square kilometers.
    The main function is to connect several terminals that are close to each other (within a family, within one or more buildings, within a campus, for example).
  Technologies used: Ethernet and Wi-Fi.
MAN:
  Basic characteristics:
    A MAN is a large-sized LAN, which requires high costs but can provide a higher transmission rate. It improves the transmission media in LANs and expands the access scope of LANs (able to cover a university campus or city).
    The main function is to connect hosts, databases, and LANs at different locations in the same city.
    The functions of a MAN are similar to those of a WAN except for implementation modes and performance.
  Technologies used: such as Ethernet (10 Gbit/s or 100 Gbit/s) and WiMAX.

## Slide 18
Notes: WAN:
  Basic characteristics:
    A WAN generally covers an area of several kilometers or larger (thousands of kilometers for example).
    It is mainly used to connect several LANs or MANs that are far from each other (for example, across cities or countries).
    Telecom operators' communication lines are used.
  Technologies used: HDLC and PPP.

## Slide 19: LAN, MAN, and WAN in the Education Industry
LAN of a college or university
LAN of a college or university
Provincial Level
Municipal Level
County Level
MAN core of the provincial education bureau
MAN core of the municipal education bureau
MAN core of the district-level/county-level education bureau
Internet
LAN of a college or university
LAN of a middle school
LAN of a middle school
LAN of a primary school
LAN of a college or university
LAN of a college or university
WAN node of a district-level/county-level education bureau
WAN node of a provincial education bureau
WAN node of a municipal education bureau
Network Types
Network Topologies

## Slide 20: Network Topologies
A network topology is a structured layout presented using transmission media (such as twisted pairs and optical fibers) to interconnect various devices (such as computer terminals, routers, and switches).
...
...
The network topology is used to describe the physical or logical structure of a network in the network engineering field, and is a very important network concept.
Network Types
Network Topologies
Notes: Network topology drawing:
  It is very important to master professional network topology drawing skills, which requires a lot of practice.
  Visio and Power Point are two common tools for drawing network topologies.

## Slide 21: Network Topology Types
Network topologies are classified into star, bus, ring, tree, full-mesh, and partial-mesh network topologies.
Star network topology
Bus network topology
Ring network topology
Tree network topology
Full-mesh network topology
Partial-mesh network topology
Combined network topology
Network Types
Network Topologies
Notes: Star network topology:
  All nodes are connected through a central node.
  Advantages: New nodes can be easily added to the network. Communication data must be forwarded by the central node, which facilitates network monitoring.
  Disadvantages: Faults on the central node affect the communication of the entire network.
Bus network topology:
  All nodes are connected through a bus (coaxial cable for example).
  Advantages: The installation is simple and cable resources are saved. Generally, the failure of a node does not affect the communication of the entire network.
  Disadvantages: A bus fault affects the communication of the entire network. The information sent by a node can be received by all other nodes, resulting in low security.
Ring network topology:
  All nodes are connected to form a closed ring.
  Advantages: Cables resources are saved.
  Disadvantages: It is difficult to add new nodes. The original ring must be interrupted before new nodes are inserted to form a new ring.

## Slide 22
Notes: Tree network topology:
  The tree structure is actually a hierarchical star structure.
  Advantages: Multiple star networks can be quickly combined, which facilitates network expansion.
  Disadvantages: A fault on a node at a higher layer is more severe.
Full-mesh network topology:
  All nodes are interconnected through cables.
  Advantages: It has high reliability and high communication efficiency.
  Disadvantages: Each node requires a large number of physical ports and interconnection cables. As a result, the cost is high, and it is difficult to expand.
Partial-mesh network topology:
  Only key nodes are interconnected.
  Advantages: The cost of a partial-mesh network is lower than that of a full-mesh network.
  Disadvantages: The reliability of a partial-mesh network is lower than that of a full-mesh network.
In actual networking, multiple types of topologies may be combined based on the cost, communication efficiency, and reliability requirements.

## Slide 23
Communication and Networks
Network Types and Topology Types
Network Engineering and Network Engineers

## Slide 24: Network Engineering
Network engineering
  Network engineering refers to planning and designing feasible solutions based on network application requirements and computer network system standards, specifications, and technologies under the guidance of information system engineering methods and complete organizations, as well as integrating computer network hardware devices, software, and technologies to form a cost-effective network system that meets user requirements.
Technical modules covered by network engineering:
Application
Media
Routing
Calculation
Security
Switching
Wireless
...
Storage
Equipment room
Notes: Network engineering covers a series of activities around the network, including network planning, design, implementation, commissioning, and troubleshooting.
The knowledge field of network engineering design is very wide, in which routing and switching are the basis of the computer network.

## Slide 25: Network Engineer
Network engineer
  Network engineers are technology professionals who master professional network technologies, have professional skills, professionalism, and project implementation experience in the network engineering field, and are able to fully communicate with customers or other project stakeholders onsite. In addition, they can develop implementation solutions and project plans (recognized by project stakeholders) based on customer requirements and environment factors, fully mobilize resources of all parties to ensure timely and high-quality project implementation, and provide training for stakeholders and deliver engineering documents after the project is implemented.
Comprehensive capability models for network engineers:
Professional knowledge
Technical knowledge
Product knowledge
Engineering knowledge
Industry knowledge
Process specification
Basic qualification
Learning competency
Information collection
Service awareness
Values
Business etiquette
Professional skills
Communication capability
Problem solving
Presentation capability
Business management
Team collaboration

## Slide 26: Network Engineers' Technology Development Path
What
Routing and switching
How
How to perform, verify, and query OSPF configurations
Protocol mechanisms
Open Shortest Path First (OSPF) connection establishment process
Detailed working process of the Spanning Tree Protocol (STP)
Packet and underlying mechanisms
Underlying working mechanism of protocols and packet details
Overall capabilities
Solution design, network planning, implementation, troubleshooting, and optimization
From macro to micro and then back to macro

## Slide 27: Huawei Certification Injects Vitality into Talent Development for Enterprises
Cultivate experts who understand both business and technologies.
Cultivate platform construction and service application experts based on HUAWEI CLOUD.
Focuses on ICT infrastructure and cultivates architecture talent in all ICT fields.
Meets enterprise talent's career evolution from an engineer to a senior engineer, and then to an expert.
Provides a hierarchical certification system that provides customized talent growth paths in accordance with job-based capability requirements and supports in-depth professional development, integration, and expansion, reducing the talent cultivation cost for enterprises.
Provides authoritative certification for ICT talent. The ICT talent with authoritative certification helps ensure project delivery quality and improve customer satisfaction.
Enhances the overall performance and productivity of enterprises.
Accelerates business innovation and transformation, and improve the overall operational efficiency.
Certification exam
Providing talent with career development paths
Facilitating enterprise innovation and transformation

## Slide 28: Huawei Certification Portfolio
Huawei certification covers all ICT fields and is committed to providing a leading talent cultivation architecture and certification standards, cultivating ICT professionals in the digital era, and building a healthy ICT talent ecosystem.
Public Safety
Huawei Certification
  GaussDB
Data Center
Storage
Intelligent Computing
Datacom
Security
Finance
  Cloud Service
  Cloud Computing
Intelligent
Video Surveillance
  Enterprise Communication
Kunpeng
Application Developer
Big Data
AI
IoT
ICT Vertical Certification
Platform and Service Certification
ICT Infrastructure Certification
WLAN
SDN
  Huawei Certified ICT Associate
  Huawei Certified ICT Professional
  Huawei Certified ICT Expert
Transmission
Access
5G
LTE
Notes: Huawei talent ecosystem website: https://e.huawei.com/en/talent/#/home

## Slide 29: Huawei Datacom Certification Portfolio
HCIA-Datacom
Aiming to cultivate network engineers with basic datacom theories and skills
HCIP-Datacom
Aiming to cultivate senior network engineers for cross-field solution planning and design or single-field planning and deployment
HCIE-Datacom
Aiming to cultivate network experts with solid theoretical foundation and deployment capabilities for cross-field solutions
HCIA
HCIP
HCIE
Notes: HCIA-Datacom: one course (exam)
  Basic concepts of data communication, basis of routing and switching, security, WLAN, SDN and NFV, basis of programming automation, and network deployment cases
HCIP-Datacom: one mandatory course (exam) and six optional sub-certification courses (exams)
  Mandatory course (exam):
    HCIP-Datacom-Core Technology
  Optional courses (exams):
    HCIP-Datacom-Advanced Routing & Switching Technology
    HCIP-Datacom-Campus Network Planning and Deployment
    HCIP-Datacom-Enterprise Network Solution Design
    HCIP-Datacom-WAN Planning and Deployment
    HCIP-Datacom-SD-WAN Planning and Deployment
    HCIP-Datacom-Network Automation Developer
HCIE-Datacom: one course (exam), integrating two modules
  Classic network:
    Classic datacom technology theory based on command lines
    Classic datacom technology deployment based on command lines
  Huawei SDN solution:
    Enterprise SDN solution technology theory
    Enterprise SDN solution planning and deployment

## Slide 30
(Single) Which of the following type of network topology has the highest reliability? ( )
  Star network topology
  Ring network topology
  Full-mesh network topology
  Tree network topology
Notes: 1. C

## Slide 31
This section describes the concepts of network communication and data communication network. The basic function of a data communication network is to implement network communication.
This section also introduces various network devices, the differences between LAN, MAN and WAN, and various network topologies. In actual networking, multiple topologies are combined according to the requirements of multiple parties.
This section also describes network engineering and network engineers and introduces Huawei datacom certification system.