## Slide 1
V500R002
V100R001
Wan Changli, wx40867
2020-03-25

## Slide 2: OSPF Basics

## Slide 3
Static routes are manually configured. If a network topology changes, static routes have to be manually adjusted, which restricts the large-scale application of static routes on the live network.
Dynamic routing protocols are widely used on live networks because of their high flexibility, high reliability, and easy scalability. The Open Shortest Path First (OSPF) protocol is a widely used dynamic routing protocol.
This course describes basic concepts, working mechanism, and basic configurations of OSPF.

## Slide 4
On completion of this course, you will be able to:
  Describe the advantages and classification of dynamic routing protocols.
  Describe basic OSPF concepts and usage scenarios.
  Describe the working mechanism of OSPF.
  Implement basic OSPF configurations.

## Slide 5
OSPF Overview
OSPF Working Mechanism
Typical OSPF Configuration

## Slide 6: Why Are Dynamic Routing Protocol Used?
Static routes are manually configured and maintained, and the command lines are simple and clear. They apply to small-scale or stable networks. Static routes have the following disadvantages:
  Unable to adapt to large-scale networks: As the number of devices increases, the configuration workload increases sharply.
  Unable to dynamically respond to network changes: If the network topology changes, the network cannot automatically converge, and static routes must be manually modified.
Manually configured static route R1-R3-R2
R1-to-R2 static route
R1
R2
R3
R1
R2
R3
Link fault

## Slide 7: Classification of Dynamic Routing Protocols
Interior Gateway Protocols (IGPs)
RIP
OSPF
IS-IS
By ASs
Exterior Gateway Protocols (EGPs)
BGP
By working mechanisms and algorithms
Distance Vector Routing Protocols
Link-State Routing Protocols
OSPF
IS-IS
RIP
Notes: BGP uses the path-vector algorithm, which is a modified version of the distance-vector algorithm.

## Slide 8: Distance-Vector Routing Protocol
A router running a distance-vector routing protocol periodically floods routes. Through route exchange, each router learns routes from neighboring routers and installs the routes into its routing table.
Each router on a network is clear only about where the destination is and how far the destination is, but unclear about the whole network topology. This is the essence of the distance-vector algorithm.
R1
R2
R3
Routing
table
Routing
table
Routing
table
Destined for 3.3.3.3, through R2!
3.3.3.3

## Slide 9: Link-State Routing Protocol - LSA Flooding
Different from a distance-vector routing protocol, a link-state routing protocol advertises link status information rather than routes in the routing table. Routers that run a link-state routing protocol establish a neighbor relationship and then exchange Link State Advertisements (LSAs).
LSAs, instead of routes, are advertised.
An LSA describes a router interface's status information, such as the cost of the interface and a connected interface name.
R2
R4
R1
R3
LSA
LSA
LSA
LSA
100 Mbit/s
1000 Mbit/s
1.544 Mbit/s
100 Mbit/s
Notes: Each router generates an LSA that describes status information about its directly connected interface. The LSA contains the interface cost and the relationship between the router and its neighboring routers.

## Slide 10: Link-State Routing Protocol - LSDB Creation
Each router generates LSAs and adds the received LSAs to its own link state database (LSDB). Routers learn the whole network topology through the LSDB.
R2
R4
R1
R3
LSA
LSA
LSA
LSA
100 Mbit/s
1000 Mbit/s
1.544 Mbit/s
100 Mbit/s
The router stores LSAs in the LSDB.
The LSDB contains the description of all router interfaces on the network.
The LSDB contains the description of the entire network topology.
LSDB
LSDB
LSDB
LSDB

## Slide 11: Link-State Routing Protocol - SPF Calculation
Each router uses the Shortest Path First (SPF) algorithm and LSDB information to calculate routes. Each router calculates a loop-free tree with itself as the root and the shortest path. With this tree, a router determines the optimal path to each corner of a network.
R2
R4
R1
R3
100 Mbit/s
1000 Mbit/s
1.544 Mbit/s
100 Mbit/s
Each router calculates a loop-free tree with itself as the root over the shortest path.
LSDB
LSDB
LSDB
LSDB
2
4
1
4
Notes: SPF is a core algorithm of OSPF and used to select preferred routes on a complex network.

## Slide 12: Link-State Routing Protocol - Routing Table Generation
Ultimately, the router installs routes for the calculated preferred paths into its routing table.
R2
R4
R1
R3
100 Mbit/s
1000 Mbit/s
1.544 Mbit/s
100 Mbit/s
Based on SPF calculation results, each router installs routes into the routing table.
LSDB
LSDB
LSDB
LSDB
Routing table
Routing table
Routing table
Routing table
Routing table

## Slide 13: Summary of Link-State Routing Protocols
R1
R2
R3
Link status information
Link status information
Link status information
R1
R2
R3
Neighbor relationship setup
Neighbor relationship setup
Neighbor relationship setup
R1
R2
R3
R1
R2
R3
Path computation
Path computation
Path computation
1
2
3
LSDB
LSDB
LSDB
RIB
RIB
RIB
RIB: Routing Information Base
Route generation
1
2
3
4
Notes: The implementation of a link-state routing protocol is as follows:
  Step 1: Establishes a neighbor relationship between neighboring routers.
  Step 2: Exchanges link status information and synchronizes LSDB information between neighbors.
  Step 3: Calculates an optimal path.
  Step 4: Generates route entries based on the shortest path tree and loads the routing entries to the routing table.

## Slide 14: Introduction to OSPF
OSPF is a typical link-state routing protocol and one of the widely used IGPs in the industry.
OSPFv2, as defined in RFC 2328, is designed for IPv4. OSPFv3, as defined in RFC 2740, is designed for IPv6. Unless otherwise specified, OSPF in this presentation refers to OSPFv2.
OSPF routers exchange link status information, but not routes. Link status information is key information for OSPF to perform topology and route calculation.
An OSPF router collects link status information on a network and stores the information in the LSDB. Routers are aware of the intra-area network topology and be able to calculate loop-free paths.
Each OSPF router uses the SPF algorithm to calculate the shortest path to a specific destination. Routers generate routes based on these paths and install the routes to the routing table.
OSPF supports the variable length subnet mask (VLSM) mechanism and manual route summarization.
The multi-area design enables OSPF to support a larger network.

## Slide 15: OSPF Application on a Campus Network
The core switch and aggregation
switches run OSPF to implement
reachable routes
on the campus network.
Internet
Office building 1
Office building 2
Office building 3
Server cluster
Firewall
Core switch
Aggregation switch
Aggregation switch
Aggregation switch

## Slide 16: Basic OSPF Concepts: Area
The OSPF area keyword identifies an OSPF area.
The area is considered as a logical group, and each group is identified by an area ID.
Area 0
R1
R3
R2
Area
Router ID
Cost Value

## Slide 17: Basic OSPF Concepts: Router ID
A router ID uniquely identifies a router in an OSPF area.
The router ID can be manually specified or automatically assigned by the system.
Router ID: 1.1.1.1
R1
R3
R2
Router ID: 2.2.2.2
Router ID: 3.3.3.3
Area
Router ID
Cost Value
I'm 1.1.1.1.
Area 0
Notes: In actual projects, OSPF router IDs are manually set for devices. Ensure that the router IDs of any two devices in an OSPF area are different. Generally, the router ID is set the same as the IP address of an interface (usually a Loopback interface) on the device.

## Slide 18: Basic OSPF Concepts: Cost Value
OSPF uses costs as route metric values. Each OSPF-enabled interface maintains a cost value. Default cost value = , where, 100 Mbit/s is the default reference value specified by OSPF and is configurable.
Generally, the cost of an OSPF route is the sum of costs of all inbound interfaces along a path from the destination network segment to the local router.
FE interface
Default cost = 1
GE interface
Default cost = 1
Serial interface (1.544 Mbit/s)
Default cost = 64
Cost = 1
Cost = 64
Cost = 10
1.1.1.0/24
R1
R2
R3
In the routing table of R3, the cost of the OSPF route to 1.1.1.0/24 is 75 (10 + 1 + 64).
Cost Value of an OSPF Interface
Each OSPF interface has a specific cost because of the particular bandwidth value.
Accumulated Costs on an OSPF Path
Area
Router-ID
Cost Value

## Slide 19: OSPF Packet Types
There are five types of OSPF protocol packets and implement different functions in interaction between OSPF routers.
Packet Name | Function
Hello | Is periodically sent to discover and maintain OSPF neighbor relationships.
Database Description | Describes the summary of the local LSDB, which is used to synchronize the LSDBs of two devices.
Link State Request | Requests a needed LSA from a neighbor. LSRs are sent only after DD packets have been successfully exchanged.
Link State Update | Is sent to advertise a requested LSA to a neighbor.
Link State ACK | Is used to acknowledge the receipt of an LSA.

## Slide 20: Three Types of OSPF Entries - Entries in the Neighbor Table
OSPF provides entries in three important tables: OSPF neighbor table, LSDB table, and OSPF routing table. For the OSPF neighbor table, you need to know:
  Before OSPF transmits link status information, OSPF neighbor relationships must be established.
  OSPF neighbor relationships are established by exchanging Hello packets.
  The OSPF neighbor table describes the status of the neighbor relationship between OSPF routers. You can run the display ospf peer command to view status information.
[R1]display ospf peer
<R1> display ospf peer
OSPF Process 1 with Router ID 1.1.1.1
Neighbors
Area 0.0.0.0 interface 10.1.1.1(GigabitEthernet1/0/0)'s neighbors
Router ID: 2.2.2.2 Address: 10.1.1.2 GR State: Normal
State: Full Mode:Nbr is Master Priority: 1
DR: 10.1.1.1 BDR: 10.1.1.2 MTU: 0
Dead timer due in 35 sec
Retrans timer interval: 5
Neighbor is up for 00:00:05
Authentication Sequence: [ 0 ]
R1
R2
Router ID: 1.1.1.1
Router ID: 2.2.2.2
Neighbor Table
LSDB Table
OSPF Routing table
10.1.1.2/30
10.1.1.1/30
GE 1/0/0
GE 1/0/0
Notes: The OSPF neighbor table contains much key information, such as router IDs and interface addresses of neighboring devices. For more details, see "OSPF Working Mechanism".

## Slide 21: Three Types OSPF Entries - Entries in the LSDB Table
For the OSPF LSDB table, you need to know:
  An LSDB stores LSAs generated by a router itself and received from neighbors. In this example, the LSDB of R1 contains three LSAs.
  The Type field indicates an LSA type, and the AdvRouter field indicates the router that sends the LSA.
  Run the display ospf lsdb command to query the LSDB.
<R1> display ospf lsdb
OSPF Process 1 with Router ID 1.1.1.1
Link State Database
Router ID: 0.0.0.0
Type LinkState ID AdvRouter Age Len Sequence Metric
Router 2.2.2.2 2.2.2.2 98 36 8000000B 1
Router 1.1.1.1 1.1.1.1 92 36 80000005 1
Network 10.1.1.2 2.2.2.2 98 32 80000004 0
Neighbor Table
LSDB Table
OSPF Routing Table
[R1]display ospf lsdb
R1
R2
Router ID: 1.1.1.1
Router ID: 2.2.2.2
10.1.1.2/30
10.1.1.1/30
GE 1/0/0
GE 1/0/0
Notes: For more information about LSAs, see information provided in HCIP-Datacom courses.

## Slide 22: Three Types of OSPF Entries - Entries in the OSPF Routing Table
For the OSPF routing table, you need to know:
  The OSPF routing table and the router routing table are different. In this example, the OSPF routing table contains three routes.
  An OSPF routing table contains information, such as the destination IP address, cost, and next-hop IP address, which guides packet forwarding.
  Run the display ospf routing command to query the OSPF routing table.
<R1> display ospf routing
OSPF Process 1 with Router ID 1.1.1.1
Routing tables
Routing for Network
Destination Cost Type NextHop AdvRouter Area
1.1.1.1/32 0 stub 1.1.1.1 1.1.1.1 0.0.0.0
10.1.1.0/20 1 Transit 10.1.1.1 1.1.1.1 0.0.0.0
2.2.2.2/32 1 stub 10.1.1.2 2.2.2.2 0.0.0.0
Total Nets: 3
Intra Area: 3 Inter Area: 0 ASE: 0 NSSA: 0
Neighbor Table
LSDB Table
OSPF Routing Table
[R1]display ospf routing
R1
R2
Router ID: 1.1.1.1
Router ID: 2.2.2.2
10.1.1.2/30
10.1.1.1/30
GE 1/0/0
GE 1/0/0
Notes: For more information about the OSPF routing table, see information provided in HCIP-Datacom courses.

## Slide 23
OSPF Overview
OSPF Working Mechanism
Typical OSPF Configuration

## Slide 24: Relationships Between OSPF Routers
There are two important concepts about the relationship between OSPF routers: neighbor relationship and adjacency.
On a simple network, two routers are directly connected. OSPF is enabled on interconnected interfaces. The routers start to send and listen to Hello packets. After the two routers discover each other through Hello packets, they establish a neighbor relationship.
The establishment of a neighbor relationship is just the beginning. A series of packets, such as DD, LSR, LSU, and LSAck packets, will be exchanged later. When LSDB synchronization between two routers is complete and the two routers start to calculate routes independently, the two routers establish an adjacency.

## Slide 25: Process of Establishing an OSPF Adjacency Relationship
OSPF adjacency relationship establishment involves four steps: establishing a neighbor relationship, negotiating the master/slave status, exchanging LSDB information, and synchronizing LSDBs.
R1
R2
1
2
3
4
5
Calculates routes.
5
Calculates routes.
Steps 1 to 4 involve interaction between both ends, and Step 5 is performed separately on each device.
Establish a bidirectional neighbor relationship.
Negotiate the master/slave status.
Mutually describe the LSDB (summary information).
Update LSAs and synchronize LSDBs of both ends.

## Slide 26: Process of Establishing an OSPF Adjacency - Step 1
Area 1.1.1.1
Area 2.2.2.2
R1 (1.1.1.1) is discovered and added to the neighbor list. The status of R1 in the neighbor table is Init.
Hello packets
I'm 2.2.2.2. I found my neighbor 1.1.1.1.
Hello packets
I'm 1.1.1.1. I found the neighbor 2.2.2.2.
We're neighbors.
Hello packets
I'm 1.1.1.1. I don't know who's on the link.
Because R1 found me, I change the status of 1.1.1.1 to 2-way in the neighbor table.
R2 (2.2.2.2) is discovered and added to the neighbor list. Because R2 discovered me, I set the status of R2 to 2-way in the neighbor table.
R1
R2
Init
2-way
2-way
Notes: When an OSPF router receives the first Hello packet from another router, the OSPF router changes from the Down state to the Init state.
When an OSPF router receives a Hello packet in which the neighbor field contains its router ID, the OSPF router changes from the Init state to the 2-way state.

## Slide 27: Process of Establishing an OSPF Adjacency - Steps 2 and 3
Router ID: 1.1.1.1
Router ID: 2.2.2.2
Ex-start
DD (The content is empty, and the sequence number is Y.)
I'm the master and my router ID is 2.2.2.2.
DD (sequence number Y)
This is the summary of LSAs in my LSDB.
DD (The content is empty, and the sequence number is X.)
I'm the master and my router ID is 1.1.1.1.
In the Exchange phase, both ends exchange DD packets to describe the summary of their own LSAs.
Ex-start (Exchange Start)
R1
R2
DD (Sequence number Y + 1 in ascending order)
This is the summary of LSAs in my LSDB.
Exchange
(R2 with a larger router ID is preferred.)
I know what R2's LSDB contains.
I know what R1's LSDB contains.
Exchange
DD (sequence number Y+1)
Confirms the DD packet sent by the master router.
Notes: After the neighbor state machine changes from 2-way to Exstart, the master/slave election starts.
  The first DD packet sent from R1 to R2 is empty, and its sequence number is assumed to be X.
  R2 also sends the first DD packet to R1. In the examples provided in this presentation, the sequence number of the first DD packet is Y.
  The master/slave relationship is selected based on the router ID. A larger router ID indicates a higher priority. The router ID of R2 is greater than that of R1. Therefore, R2 becomes the master device. After the master/slave role negotiation is complete, R1's status changes from Exstart to Exchange.
After the neighbor status of R1 changes to Exchange, R1 sends a new DD packet containing its own LSDB description. The sequence number of the DD packet is the same as that of R2. After R2 receives the packet, the neighbor status changes from Exstart to Exchange.
R2 sends a new DD packet to R1. The DD packet contains the description of its own LSDB and the sequence number of the DD packet is Y + 1.
As a backup router, R1 needs to acknowledge each DD packet sent by R2. The sequence number of the response packet is the same as that of the DD packet sent by R2.
After sending the last DD packet, R1 changes the neighbor status to Loading.

## Slide 28: Process of Establishing an OSPF Adjacency - Step 4
Router ID: 1.1.1.1
Router ID: 2.2.2.2
Loading
LSU
This is the complete information about the requested LSA.
LSR
I want to request the complete information about the xx LSA.
Loading
R1
R2
Full
LSDBs of R1 and R2 are synchronized.
LSDBs of R1 and R2 are synchronized.
Full
LSR
I want to request the complete information about the yyy LSA.
LS ACK
Confirms the reception of the LSU and the xx LSA carried in the LSU.
Notes: After the neighbor status changes to Loading, R1 sends an LSR to R2 to request the LSAs that are discovered through DD packets in the Exchange state but do not exist in the local LSDB.
After receiving the LSU, R2 sends an LSU to R1. The LSU contains detailed information about the requested LSAs.
After R1 receives the LSU, R1 replies with an LSAck to R2.
During this process, R2 also sends an LSA request to R1. When the LSDBs on both ends are the same, the neighbor status changes to Full, indicating that the adjacency has been established successfully.

## Slide 29: Review of the OSPF Neighbor Table
<R1> display ospf peer
OSPF Process 1 with Router ID 1.1.1.1
Neighbors
Area 0.0.0.0 interface 10.1.1.1(GigabitEthernet1/0/0)'s neighbors
Area 2.2.2.2 Address: 10.1.1.2 GR State: Normal
State: Full Mode:Nbr is Master Priority: 1
DR: 10.1.1.1 BDR: 10.1.1.2 MTU: 0
Dead timer due in 35 sec
Retrans timer interval: 5
Neighbor is up for 00:00:05
Authentication Sequence: [ 0 ]
Router ID: 1.1.1.1
Router ID: 2.2.2.2
R1
R2
10.1.1.1/30
GE1/0/0
10.1.1.2/30
GE1/0/0
R1 discovers neighbors in area 0 on GE 1/0/0.
Router ID of the neighbor: 2.2.2.2
The neighbor status is Full.
The neighbor at 2.2.2.2 is the master.
Quiz: What is the DR/BDR in the neighbor table?
Notes: Fields displayed in the display ospf peer command output are as follows:
  OSPF Process 1 with Router ID 1.1.1.1: The local OSPF process ID is 1, and the local OSPF router ID is 1.1.1.1.
  Area ID of the neighboring OSPF router.
  Address: address of the neighbor interface.
  GR State: GR status after OSPF GR is enabled. GR is an optimized function. The default value is Normal.
  State: neighbor status. In normal cases, after LSDB synchronization is complete, the neighbor stably stays in the Full state.
  Mode: whether the local device is the master or backup device during link status information exchange.
  Priority: priority of the neighboring router. The priority is used for DR election.
  DR: designated router.
  BDR: backup designated router.
  MTU: MTU of a neighbor interface.
  Retrans timer interval: interval (in seconds) at which LSAs are retransmitted.
  Authentication Sequence: authentication sequence number.

## Slide 30: OSPF Network Types
Before learning concepts of the DR and BDR, understand OSPF network types.
The OSPF network type is a very important interface variable. This variable affects OSPF operations on interfaces. For example, it determines how to send OSPF packets and whether to elect a DR or BDR.
The default OSPF network type of an interface depends on the data link layer encapsulation used by the interface.
As shown in the figure, OSPF has four network types: broadcast, NBMA, P2MP, and P2P.
[R1-GigabitEthernet1/0/0] ospf network-type ?
broadcast Specify OSPF broadcast network
nbma Specify OSPF NBMA network
p2mp Specify OSPF point-to-multipoint network
p2p Specify OSPF point-to-point network
R1
R2
Router ID: 1.1.1.1
Router ID: 2.2.2.2
10.1.1.2/30
10.1.1.1/30
GE 1/0/0
GE 1/0/0

## Slide 31: OSPF Network Types (1)
Generally, the network types of OSPF interfaces at both ends of a link must be the same. Otherwise, the two interfaces cannot establish a neighbor relationship.
An OSPF network type can be manually changed on an interface to adapt to different network scenarios. For example, you can change the BMA network type to P2P.
Broadcast Multiple Access (BMA)
Point-to-Point (P2P)
RTA
RTB
P2P indicates that only two network devices can be connected on a link.
A typical example is a PPP link. When an interface uses PPP encapsulation, the default network type of the OSPF interface is P2P.
BMA is also called broadcast. It refers to an environment that allows multiple devices to access and supports broadcast.
A typical example is an Ethernet network. When an interface uses Ethernet encapsulation, the default network type of the OSPF interface is BMA.
Serial0/0/0
Serial0/0/0
PPP
PPP
GE0/0/0
Ethernet
GE0/0/0
GE0/0/0

## Slide 32: OSPF Network Types (2)
Non-Broadcast Multiple Access (NBMA)
Point-to-Multipoint (P2MP)
NBMA refers to an environment that allows multiple network devices to access but does not support broadcast.
A typical example is a Frame Relay (FR) network.
FR
A P2MP network is formed by bundling endpoints of multiple P2P links.
No link layer protocol is considered as a P2MP network by default. This type must be manually changed from another network type.
For example, a non-full-mesh NBMA network can be changed to a P2MP network.
Frame Relay

## Slide 33: Background of DR and BDR
Multi-access (MA) networks are classified into BMA and NBMA networks. Ethernet is a typical broadcast multi-access network.
On an MA network, if each OSPF router establishes OSPF adjacencies with all the other routers, excessive OSPF adjacencies exist on the network, which increases the load on the devices and the number of OSPF packets flooded on the network.
Once the network topology changes, LSA flooding on the network may waste bandwidth and device resources.
Ethernet
Adjacency

## Slide 34: DR and BDR
To optimize OSPF neighbor relationships on an MA network, the OSPF protocol specifies three types of OSPF routers: DR, BDR, and DRother.
Only the DR and BDR can establish adjacencies with other OSPF routers. DRothers do not establish OSPF adjacencies with one another, and their relationship is in the 2-way state.
The BDR monitors the status of the DR and takes over the role of the DR if the existing DR fails.
BDR
DR
DRother
DRother
DRother
Ethernet
Adjacency
Notes: Election rule: The interface with a higher OSPF DR priority becomes the DR of the MA. If the priorities (default value of 1) are the same, the router (interface) with a higher OSPF router ID is elected as the DR, and the DR is non-preemption.

## Slide 35: OSPF Domain and Single Area
Area 0
An OSPF domain is a network that consists of a series of contiguous OSPF network devices that use the same policy.
An OSPF router floods LSAs in the same area. To ensure that all routers have the same understanding of the network topology, LSDBs need to be synchronized within an area.
If there is only one OSPF area, the number of OSPF routers increases with the network scale. This causes the following problems:
  The LSDB becomes larger and larger, and the size of the OSPF routing table increases. A large number of router resources are consumed, device performance deteriorates, and data forwarding is affected.
  It is difficult to calculate routes based on a large LSDB.
  When the network topology changes, LSA flooding and SPF recalculation on the entire network bring heavy loads.

## Slide 36: Multi-Area OSPF
OSPF introduces the concept of area. An OSPF domain is divided into multiple areas to support larger-scale networking.
The OSPF multi-area design reduces the flooding scope of LSAs and effectively controls the impact of topology changes within an area, optimizing the network.
Routes can be summarized at the area border to reduce the size of the routing table.
Multi-area improves network scalability and facilitates large-scale network construction.
Area 1
Area 0
Area 2
Notes: Types of areas: Areas can be classified into backbone areas and non-backbone areas. Area 0 is a backbone area. All areas except area 0 are called non-backbone areas.
Multi-area interconnection: To prevent inter-area loops, non-backbone areas cannot be directly connected to each other. All non-backbone areas must be connected to a backbone area.

## Slide 37: Types of OSPF Routers
OSPF routers are classified into the following types based on their locations or functions:
  Internal router
  Area border router (ABR)
  Backbone router
  AS boundary router (ASBR)
Area 1
Area 2
ASBR
ABR/BR
IR
Another AS
BR
Notes: Internal router: All interfaces of an internal router belong to the same OSPF area.
ABR: An interface of an ABR belongs to two or more areas, but at least one interface belongs to the backbone area.
Backbone router: At least one interface of a backbone router belongs to the backbone area.
ASBR: exchanges routing information with other ASs. If an OSPF router imports external routes, the router is an ASBR.

## Slide 38: Typical OSPF Single-Area and Multi-Area Networking
OSPF Area 0
OSPF Area 1
OSPF Area 2
OSPF Area 0
Small- and medium-sized enterprise network (single area)
Large enterprise network (multiple areas)
Notes: Small- and medium-sized enterprise networks have a small scale and a limited number of routing devices. All devices can be deployed in the same OSPF area.
A large-scale enterprise network has a large number of routing devices and is hierarchical. Therefore, OSPF multi-area deployment is recommended.

## Slide 39
OSPF Overview
OSPF Working Mechanism
Typical OSPF Configuration

## Slide 40: Basic OSPF Configuration Commands (1)
[Huawei] ospf [ process-id | router-id router-id ]
(System view) Create and run an OSPF process.
The process-id parameter specifies an OSPF process. The default process ID is 1. OSPF supports multiple processes. Multiple OSPF processes can separately run on the same device. The router-id command is used to manually specify the ID of a device. If no ID is specified, the system automatically selects the IP address of an interface as the device ID.
[Huawei] area area-id
(OSPF view) Create an OSPF area and enter the OSPF area view.
The area command creates an OSPF area and displays the OSPF area view.
The area-id value can be a decimal integer or in dotted decimal notation. If the value is an integer, it ranges from 0 to 4294967295.
[Huawei-ospf-1-area-0.0.0.0] network network-address wildcard-mask
3. (OSPF area view) Specify the interface that runs OSPF.
The network command specifies the interface that runs OSPF and the area to which the interface belongs. The network-address parameter specifies the network segment address of the interface. The wildcard-mask parameter is the wildcard of an IP address, which is equivalent to the reverse mask of the IP address (0 is converted to 1, and 1 to 0). For example, 0.0.0.255 indicates that the mask length is 24 bits.
Notes: A router ID is selected in the following order: The largest IP address among Loopback addresses is preferentially selected as a router ID. If no Loopback interface is configured, the largest IP address among interface addresses is selected as a router ID.

## Slide 41: Basic OSPF Configuration Commands (2)
4. (Interface view) Set an OSPF interface cost.
The ospf cost command sets a cost for an OSPF interface. By default, OSPF automatically calculates the cost of an interface based on the interface bandwidth. The cost value is an integer ranging from 1 to 65535.
[Huawei-GE1/0/1] ospf cost cost
5. (OSPF view) Set an OSPF bandwidth reference value.
The bandwidth-reference command sets a bandwidth reference value that is used to calculate interface costs. The value ranges from 1 to 2147483648, in Mbit/s. The default value is 100 Mbit/s.
[Huawei-ospf-1] bandwidth-reference value
[Huawei-GigabitEthernet0/0/0] ospf dr-priority priority
6. (Interface view) Set the priority of an interface for DR election.
The ospf dr-priority command sets a priority for an interface that participates in DR election. A larger value indicates a higher priority. The value ranges from 0 to 255.

## Slide 42: OSPF Configuration Example
Description:
There are three routers, R1, R2, and R3. R1 and R3 are connected to networks 1.1.1.1/32 and 3.3.3.3/32 (simulated by Loopback 0), respectively. OSPF needs to be used to implement interworking between the two networks. Detailed topology was as follows:
R2
R1
R3
10.1.12.1/30
GE0/0/0
10.1.12.2/30
GE0/0/0
10.1.23.1/30
GE0/0/1
10.1.23.2/30
GE0/0/1
Area 0
Area 1
1.1.1.1/32
3.3.3.3/32
The configuration process consists of three steps: configuring device interfaces, configuring OSPF, and verifying the result.
Configure interfaces.
Configure OSPF.
Verify the result.

## Slide 43: OSPF Configuration Example - Configuring Interfaces
R2
R1
R3
10.1.12.1/30
GE0/0/0
10.1.12.2/30
GE0/0/0
10.1.23.1/30
GE0/0/1
10.1.23.2/30
GE0/0/1
Area 0
Area 1
1.1.1.1/32
3.3.3.3/32
Configure interfaces.
Configure OSPF.
Verify the result.
# Configure interfaces of R1.
[R1] interface LoopBack 0
[R1-LoopBack0] ip address 1.1.1.1 32
[R1-LoopBack0] interface GigabitEthernet 0/0/0
[R1-GigabitEthernet0/0/0] ip address 10.1.12.1 30
# Configure interfaces of R3.
[R3] interface LoopBack 0
[R3-LoopBack0] ip address 3.3.3.3 32
[R3-LoopBack0] interface GigabitEthernet 0/0/1
[R3-GigabitEthernet0/0/1] ip address 10.1.23.2 30
Assign IP addresses for GE0/0/0 and GE0/0/1 on R2. For details, see comment in this slide.
Set IP addresses for R1's, R2's, and R3's interfaces according to the plan.
Notes: Configure interfaces of R2.
  [R2] interface GigabitEthernet 0/0/0 [R2-GigabitEthernet0/0/0] ip address 10.1.12.2 30 [R2-GigabitEthernet0/0/0] interface GigabitEthernet 0/0/1 [R2-GigabitEthernet0/0/1] ip address 10.1.23.1 30

## Slide 44: OSPF Configuration Example - Configuring OSPF (1)
R2
R1
R3
10.1.12.1/30
GE0/0/0
Area 0
Area 1
1.1.1.1/32
3.3.3.3/32
# Configure OSPF on R1.
[R1] ospf 1 router-id 1.1.1.1
[R1-ospf-1] area 0
[R1-ospf-1-area-0.0.0.0] network 1.1.1.1 0.0.0.0
[R1-ospf-1-area-0.0.0.0] network 10.1.12.0 0.0.0.3
Planned OSPF parameters: The OSPF process ID is 1. Router IDs of R1, R2, and R3 are 1.1.1.1, 2.2.2.2, and 3.3.3.3 respectively.
Procedure:
  Create and run an OSPF process.
  Create an OSPF area and enter the OSPF area view.
  Specify the interface that runs OSPF..
Router ID 1.1.1.1
Configure interfaces.
Configure OSPF.
Verify the result.
An inverse mask is specified here.

## Slide 45: OSPF Configuration Example - Configuring OSPF (2)
R2
R1
R3
10.1.12.2/30
GE0/0/0
10.1.23.1/30
GE0/0/1
10.1.23.2/30
GE0/0/1
Area 0
Area 1
1.1.1.1/32
3.3.3.3/32
Configure interfaces.
Configure OSPF.
Verify the result.
# Configure OSPF on R2.
[R2] ospf 1 router-id 2.2.2.2
[R2-ospf-1] area 0
[R2-ospf-1-area-0.0.0.0] network 10.1.12.0 0.0.0.3
[R2-ospf-1-area-0.0.0.0] area 1
[R2-ospf-1-area-0.0.0.1] network 10.1.23.0 0.0.0.3
Router ID 2.2.2.2
Router ID 3.3.3.3
# Configure OSPF on R3.
[R3] ospf 1 router-id 3.3.3.3
[R3-ospf-1] area 1
[R3-ospf-1-area-0.0.0.1] network 3.3.3.3 0.0.0.0
[R3-ospf-1-area-0.0.0.1] network 10.1.23.0 0.0.0.3
When configuring OSPF multi-area, be sure to advertise the route destined for a network segment that responds to a specified area.

## Slide 46: OSPF Configuration Example - Verification (1)
R2
R1
R3
1.1.1.1/32
3.3.3.3/32
Configure interfaces.
Configure OSPF.
Verify the result.
<R2> display ospf peer brief
OSPF Process 1 with Router ID 2.2.2.2
Peer Statistic Information
----------------------------------------------------------------------------
Area Id Interface Neighbor id State
0.0.0.0 GigabitEthernet0/0/0 1.1.1.1 Full
0.0.0.1 GigabitEthernet0/0/1 3.3.3.3 Full
----------------------------------------------------------------------------
Check the OSPF neighbor table on R2.
Area 0
Area 1
Area ID of a neighbor
Neighbor status
Verify that the neighbor status is Full, indicating that the adjacency has been established successfully.

## Slide 47: OSPF Configuration Example - Verification (2)
<R1>display ip routing-table
Route Flags: R - relay, D - download to fib
------------------------------------------------------------------------------
Routing tables: Public
Destinations : 10 Routes : 10
Destination/Mask Proto Pre Cost Flags NextHop Interface
1.1.1.1/32 Direct 0 0 D 127.0.0.1 LoopBack0
3.3.3.3/32 OSPF 10 2 D 10.1.12.2 GigabitEthernet 0/0/0
10.1.12.0/30 Direct 0 0 D 10.1.12.1 GigabitEthernet 0/0/0
…
<R1>ping -a 1.1.1.1 3.3.3.3
PING 3.3.3.3: 56 data bytes, press CTRL_C to break
Reply from 3.3.3.3: bytes = 56 Sequence = 1 ttl = 254 time = 50 ms
…
Check the routing table on R1 and ping 3.3.3.3 from 1.1.1.1.
Route to 3.3.3.3/32 learned using OSPF
Set the source IP address to 1.1.1.1 and ping 3.3.3.3.

## Slide 48
(Multiple) In the process of establishing OSPF neighbor relationships and adjacencies, which of the following states are stable? ( )
  Exstart
  Two-way
  Exchange
  Full
(Multiple) In which of the following situation will the establishment of adjacencies between routers be triggered? ( )
  Two routers on a point-to-point link
  DR and BDR on a broadcast network
  DRother and DRother on an NBMA network
  BDR and DRother on a broadcast network
Notes: BD
ABD

## Slide 49
OSPF is a widely used routing protocol on the live network. This presentation describes basic concepts, application scenarios, and basic configurations of OSPF.
The router ID, area, OSPF neighbor table, LSDB table, and OSPF routing table are basic OSPF concepts. Describe the establishment of OSPF neighbor relationships and adjacencies, which helps you better understand the link-state routing protocol.
OSPF has more interesting details, such as LSA types, the SPF calculation process, and the OSPF special area. For more OSPF information, please continue your Huawei HCIP-Datacom certification courses.