## Slide 1
Lu Yueyue/lwx445705
2019.11
New

## Slide 2: ACL Principles and Configuration

## Slide 3
Rapid network development brings challenges to network security and quality of service (QoS). Access control lists (ACLs) are closely related to network security and QoS.
By accurately identifying packet flows on a network and working with other technologies, ACLs can control network access behaviors, prevent network attacks, and improve network bandwidth utilization, thereby ensuring network environment security and QoS reliability.
This course describes the basic principles and functions of ACLs, types and characteristics of ACLs, basic composition of ACLs, ACL rule ID matching order, usage of wildcards, and ACL configurations.
Notes: Note:
  The implementation of ACLs varies with vendors. This course describes the ACL technology implemented on Huawei devices.
  A local area network (LAN) is a computer network that connects computers in a limited area, such as a residential area, a school, a lab, a college campus, or an office building.

## Slide 4
On completion of this course, you will be able to:
  Describe the basic principles and functions of ACLs.
  Understand the types and characteristics of ACLs.
  Describe the basic composition of ACLs and ACL rule ID matching order.
  Understand how to use wildcards in ACLs.
  Complete the basic configurations of ACLs.

## Slide 5
ACL Overview
Basic Concepts and Working Mechanism of ACLs
Basic Configurations and Applications of ACLs

## Slide 6: Background: A Tool Is Required to Filter Traffic
To ensure financial data security, an enterprise prohibits the R&D department's access to the financial department server but allows the president office's access to the financial department server.
Is any tool available for filtering IP traffic?
Denied traffic
Permitted traffic
Internet
VLAN 10
VLAN 20
President office at 192.168.3.0/24
R&D department at 192.168.2.0/24
Financial department server at 192.168.4.4/24
Notes: Rapid network development brings the following issues to network security and QoS:
  Resources on the key servers of an enterprise are obtained without permission, and confidential information of the enterprise leaks, causing a potential security risk to the enterprise.
  The virus on the Internet spreads to the enterprise intranet, threatening intranet security.
  Network bandwidth is occupied by services randomly, and bandwidth for delay-sensitive services such as voice and video cannot be guaranteed, lowering user experience.
These issues seriously affect network communication, so network security and QoS need to be improved urgently. For example, a tool is required to filter traffic.

## Slide 7: ACL Overview
An ACL is a set of sequential rules composed of permit or deny statements.
An ACL matches and distinguishes packets.
IP Header | TCP/UDP Header | Data
Source IP address, destination IP address, and protocol type
Source and destination port numbers
ACL Application
Matching IP traffic
Invoked in a traffic filter
Invoked in network address translation (NAT)
Invoked in a routing policy
Invoked in a firewall policy
Invoked in QoS
Others
Notes: ACLs accurately identify and control packets on a network to manage network access behaviors, prevent network attacks, and improve bandwidth utilization. In this way, ACLs ensure security and QoS.
  An ACL is a set of sequential rules composed of permit or deny statements. It classifies packets by matching fields in packets.
  An ACL can match elements such as source and destination IP addresses, source and destination port numbers, and protocol types in IP datagrams. It can also match routes.
In this course, traffic filtering is used to describe ACLs.

## Slide 8
ACL Overview
Basic Concepts and Working Mechanism of ACLs
Basic Configurations and Applications of ACLs

## Slide 9: ACL Composition
An ACL consists of several permit or deny statements. Each statement is a rule of the ACL, and permit or deny in each statement is the action corresponding to the rule.
ACL Composition
ACL Classification
ACL Matching Rules
rule 5 permit source 1.1.1.0 0.0.0.255
acl number 2000
rule 10 deny source 2.2.2.0 0.0.0.255
rule 15 permit source 3.3.3.0 0.0.0.255
...
rule 4294967294 deny
ACL number
User-defined rules
Rule hidden at the end of the ACL
Rule ID
Action
Matching option
(source IP address)
What does each rule mean?
Notes: ACL composition:
  ACL number: An ACL is identified by an ACL number. Each ACL needs to allocated an ACL number. The ACL number range varies according to the ACL type, which will be described later.
  Rule: As mentioned above, an ACL consists of several permit/deny statements, and each statement is a rule of the ACL.
  Rule ID: Each ACL rule has an ID, which identifies the rule. Rule IDs can be manually defined or automatically allocated by the system. A rule ID ranges from 0 to 4294967294. All rules are arranged in the ascending order of rule ID.
  Action: Each rule contains a permit or deny action. ACLs are usually used together with other technologies, and the meanings of the permit and deny actions may vary according to scenarios.
    For example, if an ACL is used together with traffic filtering technology (that is, the ACL is invoked in traffic filtering), the permit action allows traffic to pass and the deny action rejects traffic.
  Matching option: ACLs support various matching options. In this example, the matching option is a source IP address. The ACL also supports other matching options, such as Layer 2 Ethernet frame header information (including source and destination MAC addresses and Ethernet frame protocol type), Layer 3 packet information (including destination address and protocol type), and Layer 4 packet information (including TCP/UDP port number).
Question: What does rule 5 permit source 1.1.1.0 0.0.0.255 mean? This will be introduced later.

## Slide 10: Rule ID
acl number 2000
rule 5 deny source 10.1.1.1 0
rule 10 deny source 10.1.1.2 0
rule 15 permit source 10.1.1.0 0.0.0.255
Step = 5
Rule ID
How do I add a rule?
acl number 2000
rule 5 deny source 10.1.1.1 0
rule 10 deny source 10.1.1.2 0
rule 11 deny source 10.1.1.3 0
rule 15 permit source 10.1.1.0 0.0.0.255
rule 11 deny source 10.1.1.3 0
Rule ID and Step
Rule ID
Each rule in an ACL has an ID.
Step
A step is an increment between neighboring rule IDs automatically allocated by the system. The default step is 5. Setting a step facilitates rule insertion between existing rules of an ACL.
Rule ID allocation
If a rule is added to an empty ACL but no ID is manually specified for the rule, the system allocates a step value (5 for example) as the ID of the rule. If an ACL contains rules with manually specified IDs and a rule with no manually specified ID is added, the system allocates to this rule an ID that is greater than the largest rule ID in the ACL and is the smallest integer multiple of the step value.
ACL Composition
ACL Classification
ACL Matching Rules
Notes: Rule ID and step:
  Rule ID: Each ACL rule has an ID, which identifies the rule. Rule IDs can be manually defined or automatically allocated by the system.
  Step: When the system automatically allocates IDs to ACL rules, the increment between neighboring rule IDs is called a step. The default step is 5. Therefore, rule IDs are 5, 10, 15, and so on.
    If a rule is manually added to an ACL but no ID is specified, the system allocates to this rule an ID that is greater than the largest rule ID in the ACL and is the smallest integer multiple of the step value.
    The step can be changed. For example, if the step is changed to 2, the system automatically renumbers the rule IDs as 2, 4, 6...
What is the function of a step? Why can't rules 1, 2, 3, and 4 be directly used?
  First, let's look at a question. How do I add a rule?
  We can manually add rule 11 between rules 10 and 15.
  Therefore, setting a step of a certain length facilitates rule insertion between existing rules.

## Slide 11: Wildcard (1)
acl number 2000
rule 5 deny source 10.1.1.1 0
rule 10 deny source 10.1.1.2 0
rule 15 permit source 10.1.1.0 0.0.0.255
Wildcard
Matching rule
  0: matching; 1: random allocation
How do I match the network segment address corresponding to 192.168.1.1/24?
192.168.1.1
0.0.0.255
1 | 1 | 0 | 0 | 0 | 0 | 0 | 0
1 | 0 | 1 | 0 | 1 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 1
0 | 0 | 0 | 0 | 0 | 0 | 0 | 1
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
Strict matching
Random allocation
192.168.1.0/24 network segment
Wildcard
A wildcard is a 32-bit number that indicates which bits in an IP address need to be strictly matched and which bits do not need to be matched.
A wildcard is usually expressed in dotted decimal notation, as a network mask is expressed. However, their meanings are different.
ACL Composition
ACL Classification
ACL Matching Rules
Notes: When an IP address is matched, a 32-bit mask is followed. The 32-bit mask is called a wildcard.
A wildcard is also expressed in dotted decimal notation. After the value is converted to a binary number, the value 0 indicates that the equivalent bit must match and the value 1 indicates that the equivalent bit does not matter.
Let's look at two rules:
  rule 5: denies the packets with the source IP address 10.1.1.1. Because the wildcard comprises all 0s, each bit must be strictly matched. Specifically, the host IP address 10.1.1.1 is matched.
  rule 15: permits the packets with the source IP address on the network segment 10.1.1.0/24. The wildcard is 0.0.0.11111111, and the last eight bits are 1s, indicating that the bits do not matter. Therefore, the last eight bits of 10.1.1.xxxxxxxx can be any value, and the 10.1.1.0/24 network segment is matched.
For example, if we want to exactly match the network segment address corresponding to 192.168.1.1/24, what is the wildcard?
  It can be concluded that the network bits must be strictly matched and the host bits do not matter. Therefore, the wildcard is 0.0.0.255.

## Slide 12: Wildcard (2)
…
A wildcard can be used to match odd IP addresses in the network segment 192.168.1.0/24, such as 192.168.1.1, 192.168.1.3, and 192.168.1.5.
Strict matching
Random allocation
Strict matching
192.168.1 | 1 |  |  |  |  |  |  | 
192.168.1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1
192.168.1 | 3 |  |  |  |  |  |  | 
192.168.1 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1
192.168.1 | 5 |  |  |  |  |  |  | 
192.168.1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1
Wildcard
0.0.0. | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0
192.168.1.1 0.0.0.254
The value 1 or 0 in the wildcard can be inconsecutive.
Special Wildcard
Exactly match the IP address 192.168.1.1.
192.168.1.1 0.0.0.0 = 192.168.1.1 0
Match All IP addresses.
0.0.0.0 255.255.255 = any
ACL Composition
ACL Classification
ACL Matching Rules
Notes: How do I set the wildcard to match the odd IP addresses in the network segment 192.168.1.0/24?
  First, let's look at the odd IP addresses, such as 192.168.1.1, 192.168.1.5, and 192.168.1.11.
  After the last eight bits are converted into binary numbers, the corresponding addresses are 192.168.1.00000001, 192.168.1.00000101, and 192.168.1.00001011.
  We can see the common points. The seven most significant bits of the last eight bits can be any value, and the least significant bit is fixed to 1. Therefore, the answer is 192.168.1.1 0.0.0.254 (0.0.0.11111110).
In conclusion, 1 or 0 in a wildcard can be inconsecutive.
There are two special wildcards.
  If a wildcard comprising all 0s is used to match an IP address, the address is exactly matched.
  If a wildcard comprising all 1s is used to match 0.0.0.0, all IP addresses are matched.

## Slide 13: ACL Classification and Identification
ACL classification based on ACL rule definition methods
Category | Number Range | Description
Basic ACL | 2000 to 2999 | Defines rules based on source IPv4 addresses, fragmentation information, and effective time ranges.
Advanced ACL | 3000 to 3999 | Defines rules based on source and destination IPv4 addresses, IPv4 protocol types, ICMP types, TCP source/destination port numbers, UDP source/destination port numbers, and effective time ranges.
Layer 2 ACL | 4000 to 4999 | Defines rules based on information in Ethernet frame headers of packets, such as source and destination MAC addresses and Layer 2 protocol types.
User-defined ACL | 5000 to 5999 | Defines rules based on packet headers, offsets, character string masks, and user-defined character strings.
User ACL | 6000 to 6999 | Defines rules based on source IPv4 addresses or user control list (UCL) groups, destination IPv4 addresses or destination UCL groups, IPv4 protocol types, ICMP types, TCP source/destination port numbers, and UDP source/destination port numbers.
ACL classification based on ACL identification methods
Category | Description
Numbered ACL | Traditional ACL identification method. A numbered ACL is identified by a number.
Named ACL | A named ACL is identified by a name.
ACL Composition
ACL Classification
ACL Matching Rules
Notes: Based on ACL rule definition methods, ACLs can be classified into the following types:
  Basic ACL, advanced ACL, Layer 2 ACL, user-defined ACL, and user ACL
Based on ACL identification methods, ACLs can be classified into the following types:
  Numbered ACL and named ACL
Note: You can specify a number for an ACL. The ACLs of different types have different number ranges. You can also specify a name for an ACL to help you remember the ACL's purpose. A named ACL consists of a name and number. That is, you can specify an ACL number when you define an ACL name. If you do not specify a number for a named ACL, the system automatically allocates a number to it.

## Slide 14: Basic and Advanced ACLs
Basic ACL
IP Header | TCP/UDP Header | Data
Source IP address
Number range:
2000 to 2999
acl number 2000
rule 5 deny source 10.1.1.1 0
rule 10 deny source 10.1.1.2 0
rule 15 permit source 10.1.1.0 0.0.0.255
IP Header | TCP/UDP Header | Data
acl number 3000
rule 5 permit ip source 10.1.1.0 0.0.0.255 destination 10.1.3.0 0.0.0.255
rule 10 permit tcp source 10.1.2.0 0.0.0.255 destination 10.1.3.0 0.0.0.255 destination-port eq 21
Number range:
3000-3999
Source IP address, destination IP address, and protocol type
Source and destination port numbers
Advanced ACL
ACL Composition
ACL Classification
ACL Matching Rules
Notes: Basic ACL:
  A basic ACL is used to match the source IP address of an IP packet. The number of a basic ACL ranges from 2000 to 2999.
  In this example, ACL 2000 is created. This ACL is a basic ACL.
Advanced ACL:
  An advanced ACL can be matched based on elements such as the source IP address, destination IP address, protocol type, and TCP or UDP source and destination port numbers in an IP packet. A basic ACL can be regarded as a subset of an advanced ACL. Compared with a basic ACL, an advanced ACL defines more accurate, complex, and flexible rules.

## Slide 15: ACL Matching Mechanism
Does the referenced ACL exist?
Does the ACL contain rules?
Analyze the first rule.
Match the rule.
Are there remaining rules?
Analyze the next rule.
Is the ACL action permit
or deny?
The ACL matching result is deny.
The ACL matching result is permit.
The ACL matching result is "negative match."
Yes
Yes
No
Yes
No
No
No
Yes
permit
deny
Matching principle: The matching stops once a rule is matched.
Start
End
ACL Composition
ACL Classification
ACL Matching Rules
Notes: The ACL matching mechanism is as follows:
  After receiving a packet, the device configured with an ACL matches the packet against ACL rules one by one. If the packet does not match any ACL rule, the device attempts to match the packet against the next ACL rule.
  If the packet matches an ACL rule, the device performs the action defined in the rule and stops the matching.
Matching process: The device checks whether an ACL is configured.
  If no ACL is configured, the device returns the result "negative match."
  If an ACL is configured, the device checks whether the ACL contains rules.
    If the ACL does not contain rules, the device returns the result "negative match."
    If the ACL contains rules, the device matches the packet against the rules in ascending order of rule ID.
      If the packet matches a permit rule, the device stops matching and returns the result "positive match (permit)."
      If the packet matches a deny rule, the device stops matching and returns the result "positive match (deny)."
      If the packet does not match any rule in the ACL, the device returns the result "negative match."

## Slide 16
Notes: The ACL matching results include "positive match" and "negative match."
  Positive match: Packets match a rule in an ACL. The result is "positive match" regardless of whether packets match a permit or deny rule in an ACL.
  Negative match: No ACL exists, the ACL does not contain rules, or packets do not match any rule in an ACL.
Matching principle: The matching stops once a rule is matched.

## Slide 17: ACL Matching Order and Result
Configuration order (config mode)
  The system matches packets against ACL rules in ascending order of rule ID. That is, the rule with the smallest ID is processed first.
192.168.1.1/24
192.168.1.2/24
192.168.1.3/24
192.168.1.4/24
192.168.1.5/24
192.168.1.1/24
192.168.1.2/24
192.168.1.4/24
192.168.1.5/24
acl 2000
rule 1 permit source 192.168.1.1 0.0.0.0
rule 2 permit source 192.168.1.2 0.0.0.0
rule 3 deny source 192.168.1.3 0.0.0.0
rule 4 permit 0.0.0.0 255.255.255.255
Object to be matched
Basic ACL
Permitted IP addresses
Does "permit" mean that traffic is allowed to pass?
rule 1: permits packets with the source IP address 192.168.1.1.
rule 2: permits packets with the source IP address 192.168.1.2.
rule 3: denies packets with the source IP address 192.168.1.3.
rule 4: permits packets from all other IP addresses.
ACL Composition
ACL Classification
ACL Matching Rules
Notes: An ACL can consist of multiple deny or permit statements. Each statement describes a rule. Rules may overlap or conflict. Therefore, the ACL matching order is very important.
Huawei devices support two matching orders: automatic order (auto) and configuration order (config). The default matching order is config.
  auto: The system arranges rules according to the precision of the rules ("depth first" principle), and matches packets against the rules in descending order of precision. ––This is complicated and is not detailed here. If you are interested in it, you can view related materials after class.
  config: The system matches packets against ACL rules in ascending order of rule ID. That is, the rule with the smallest ID is processed first. ––This is the matching order mentioned above.
    If another rule is added, the rule is added to the corresponding position, and packets are still matched in ascending order.
Matching result:
  First, let's understand the meaning of ACL 2000.
    rule 1: permits packets with the source IP address 192.168.1.1.
    rule 2: permits packets with the source IP address 192.168.1.2.
    rule 3: denies packets with the source IP address 192.168.1.3.
    rule 4: permits packets from all other IP addresses.

## Slide 18
Notes:   When packets with the source IP address 192.168.1.3 pass through the device configured with the ACL:
    The device matches the packets against rule 1. The matching result is "negative match."
    The device continues to match the packets against rule 2. The matching result is still "negative match."
    The device continues to match the packets against rule 3. The matching result is "positive match," and the action is deny.
Note: ACLs are usually used together with other technologies, and the meanings of the permit and deny actions may vary according to scenarios.For example, if an ACL is used together with traffic filtering technology (that is, the ACL is invoked in traffic filtering), the permit action allows traffic to pass and the deny action rejects traffic.

## Slide 19: ACL Matching Position
Configure an ACL on the interface.
To enable the ACL to take effect for the data packet shown in the figure,
apply the ACL to the inbound direction.
Data packet
Configure an ACL on the interface.
To enable the ACL to take effect for the data packet shown in the figure,
apply the ACL to the outbound direction.
ACL Composition
ACL Classification
ACL Matching Rules

## Slide 20: Inbound and Outbound Directions
Inbound
Outbound
Is the ACL applied to the interface's inbound direction?
Route the data packet.
Does the ACL permit the data packet?
No
Yes
Yes
Data packet
No
Is a matching route entry available?
Is the ACL applied to the outbound interface's outbound direction?
No
Yes
Route the data packet to the outbound interface.
Does the ACL permit the data packet?
Yes
Yes
No
No
Data packet
Data packet
Data packet
ACL Composition
ACL Classification
ACL Matching Rules

## Slide 21
ACL Overview
Basic Concepts and Working Mechanism of ACLs
Basic Configurations and Applications of ACLs

## Slide 22: Basic Configuration Commands of Basic ACLs
[Huawei] acl [ number ] acl-number [ match-order config ]
Create a basic ACL.
Create a numbered basic ACL and enter its view.
[Huawei] acl name acl-name { basic | acl-number } [ match-order config ]
Create a named basic ACL and enter its view.
[Huawei-acl-basic-2000] rule [ rule-id ] { deny | permit } [ source { source-address source-wildcard | any } | time-range time-name ]
Configure a rule for the basic ACL.
In the basic ACL view, you can run this command to configure a rule for the basic ACL.
Notes: Create a basic ACL.
[Huawei] acl [ number ] acl-number [ match-order config ]
  acl-number: specifies the number of an ACL.
  match-order config: indicates the matching order of ACL rules. config indicates the configuration order.
[Huawei] acl name acl-name { basic | acl-number } [ match-order config ]
  acl-name: specifies the name of an ACL.
  basic: indicates a basic ACL.
Configure a rule for the basic ACL.
[Huawei-acl-basic-2000] rule [ rule-id ] { deny | permit } [ source { source-address source-wildcard | any } | time-range time-name ]
  rule-id: specifies the ID of an ACL rule.
  deny: denies the packets that match the rule.
  permit: permits the packets that match the rule.

## Slide 23
Notes:   source { source-address source-wildcard | any }: specifies the source IP address of packets that match the ACL rule. If no source address is specified, packets with any source addresses are matched.
    source-address: specifies the source IP address of packets.
    source-wildcard: specifies the wildcard of the source IP address.
    any: indicates any source IP address of packets. That is, the value of source-address is 0.0.0.0 or the value of source-wildcard is 255.255.255.255.
  time-range time-name: specifies a time range in which the ACL rule takes effect. time-name specifies the name of a time range. If no time range is specified, the ACL rule is always valid.

## Slide 24: Case: Use a Basic ACL to Filter Data Traffic
Requirements:
  To prevent the user host on the network segment 192.168.1.0/24 from accessing the network where the server resides, configure a basic ACL on the router. After the configuration is complete, the ACL filters out the data packets whose source IP addresses are on the network segment 192.168.1.0/24 and permits other data packets.
1. Configure IP addresses and routes on the router.
[Router] acl 2000
[Router-acl-basic-2000] rule deny source 192.168.1.0 0.0.0.255
[Router-acl-basic-2000] rule permit source any
2. Create a basic ACL on the router to prevent the network segment 192.168.1.0/24 from accessing the network where the server resides.
Router
GE 0/0/1
192.168.1.0/24
192.168.2.0/24
Server
10.1.1.1/24
GE 0/0/2
[Router] interface GigabitEthernet 0/0/1
[Router-GigabitEthernet0/0/1] traffic-filter inbound acl 2000
[Router-GigabitEthernet0/0/1] quit
3. Configure traffic filtering in the inbound direction of GE 0/0/1.
Notes: Configuration roadmap:
  Configure a basic ACL and traffic filtering to filter packets from a specified network segment.
Procedure:
  Configure IP addresses and routes on the router.
  Create ACL 2000 and configure ACL rules to deny packets from the network segment 192.168.1.0/24 and permit packets from other network segments.
  Configure traffic filtering.
Note:
  The traffic-filter command applies an ACL to an interface to filter packets on the interface.
  Command format: traffic-filter { inbound | outbound } acl { acl-number | name acl-name }
    inbound: configures ACL-based packet filtering in the inbound direction of an interface.
    outbound: configures ACL-based packet filtering in the outbound direction of an interface.
    acl: filters packets based on an IPv4 ACL.

## Slide 25: Basic Configuration Commands of Advanced ACLs (1)
[Huawei] acl [ number ] acl-number [ match-order config ]
Create an advanced ACL.
Create a numbered advanced ACL and enter its view.
[Huawei] acl name acl-name { advance | acl-number } [ match-order config ]
Create a named advanced ACL and enter its view.
Notes: Create an advanced ACL.
[Huawei] acl [ number ] acl-number [ match-order config ]
  acl-number: specifies the number of an ACL.
  match-order config: indicates the matching order of ACL rules. config indicates the configuration order.
[Huawei] acl name acl-name { advance | acl-number } [ match-order config ]
  acl-name: specifies the name of an ACL.
  advance: indicates an advanced ACL.

## Slide 26: Basic Configuration Commands of Advanced ACLs (2)
Configure a rule for the advanced ACL.
You can configure advanced ACL rules according to the protocol types of IP packets. The parameters vary according to the protocol types.
In the advanced ACL view, you can run this command to configure a rule for the advanced ACL.
  When the protocol type is IP, the command format is:
rule [ rule-id ] { deny | permit } ip [ destination { destination-address destination-wildcard | any } | source { source-address source-wildcard | any } | time-range time-name | [ dscp dscp | [ tos tos | precedence precedence ] ] ]
In the advanced ACL view, you can run this command to configure a rule for the advanced ACL.
  When the protocol type is TCP, the command format is:
rule [ rule-id ] { deny | permit } { protocol-number | tcp } [ destination { destination-address destination-wildcard | any } | destination-port { eq port | gt port | lt port | range port-start port-end } | source { source-address source-wildcard | any } | source-port { eq port | gt port | lt port | range port-start port-end } | tcp-flag { ack | fin | syn } * | time-range time-name ] *
Notes: Configure a rule for the advanced ACL.
When the protocol type is IP:
  rule [ rule-id ] { deny | permit } ip [ destination { destination-address destination-wildcard | any } | source { source-address source-wildcard | any } | time-range time-name | [ dscp dscp | [ tos tos | precedence precedence ] ] ]
    ip: indicates that the protocol type is IP.
    destination { destination-address destination-wildcard | any }: specifies the destination IP address of packets that match the ACL rule. If no destination address is specified, packets with any destination addresses are matched.
    dscp dscp: specifies the differentiated services code point (DSCP) of packets that match the ACL rule. The value ranges from 0 to 63.
    tos tos: specifies the ToS of packets that match the ACL rule. The value ranges from 0 to 15.
    precedence precedence: specifies the precedence of packets that match the ACL rule. The value ranges from 0 to 7.

## Slide 27
Notes: When the protocol type is TCP:
  rule [ rule-id ] { deny | permit } { protocol-number | tcp } [ destination { destination-address destination-wildcard | any } | destination-port { eq port | gt port | lt port | range port-start port-end } | source { source-address source-wildcard | any } | source-port { eq port | gt port | lt port | range port-start port-end } | tcp-flag { ack | fin | syn } * | time-range time-name ] *
    tcp: indicates that the protocol type is TCP. You can set protocol-number to 6 to indicate TCP.
    destination-port { eq port | gt port | lt port | range port-start port-end }: specifies the TCP destination port number of packets that match the ACL rule. The value is valid only when the protocol type is TCP. If no destination port number is specified, packets with any TCP destination port numbers are matched.
      eq port: equal to the destination port number
      gt port: greater than the destination port number
      lt port: less than the destination port number
      range port-start port-end: specifies a source port number range.
    tcp-flag: indicates the SYN Flag in the TCP packet header.

## Slide 28: Case: Use Advanced ACLs to Prevent User Hosts on Different Network Segments from Communicating (1)
1. Configure IP addresses and routes on the router.
[Router] acl 3001
[Router-acl-adv-3001] rule deny ip source 10.1.1.0 0.0.0.255 destination 10.1.2.0 0.0.0.255
[Router-acl-adv-3001] quit
2. Create ACL 3001 and configure rules for the ACL to deny packets from the R&D department to the marketing department.
[Router] acl 3002
[Router-acl-adv-3002] rule deny ip source 10.1.2.0 0.0.0.255 destination 10.1.1.0 0.0.0.255
[Router-acl-adv-3002] quit
3. Create ACL 3002 and configure rules for the ACL to deny packets from the marketing department to the R&D department.
Requirements:
  The departments of a company are connected through the router. To facilitate network management, the administrator allocates IP addresses of different network segments to the R&D and marketing departments.
  The company requires that the router prevent the user hosts on different network segments from communicating to ensure information security.
Internet
Router
GE 0/0/1
10.1.1.1/24
R&D department
10.1.1.0/24
Marketing department
10.1.2.0/24
GE 0/0/2
10.1.2.1/24
Notes: Configuration roadmap:
  Configure an advanced ACL and traffic filtering to filter the packets exchanged between the R&D and marketing departments.
Procedure:
  Configure IP addresses and routes on the router.
  Create ACL 3001 and configure rules for the ACL to deny packets from the R&D department to the marketing department.
  Create ACL 3002 and configure rules for the ACL to deny packets from the marketing department to the R&D department.

## Slide 29: Case: Use Advanced ACLs to Prevent User Hosts on Different Network Segments from Communicating (2)
[Router] interface GigabitEthernet 0/0/1
[Router-GigabitEthernet0/0/1] traffic-filter inbound acl 3001
[Router-GigabitEthernet0/0/1] quit
[Router] interface GigabitEthernet 0/0/2
[Router-GigabitEthernet0/0/2] traffic-filter inbound acl 3002
[Router-GigabitEthernet0/0/2] quit
4. Configure traffic filtering in the inbound direction of GE 0/0/1 and GE 0/0/2.
Internet
Router
GE 0/0/1
10.1.1.1/24
R&D department
10.1.1.0/24
Marketing department
10.1.2.0/24
GE 0/0/2
10.1.2.1/24
Requirements:
  The departments of a company are connected through the router. To facilitate network management, the administrator allocates IP addresses of different network segments to the R&D and marketing departments.
  The company requires that the router prevent the user hosts on different network segments from communicating to ensure information security.
Notes: Procedure:
  Configure traffic filtering in the inbound direction of GE 0/0/1 and GE 0/0/2.
Note:
  The traffic-filter command applies an ACL to an interface to filter packets on the interface.
  Command format: traffic-filter { inbound | outbound } acl { acl-number | name acl-name }
    inbound: configures ACL-based packet filtering in the inbound direction of an interface.
    outbound: configures ACL-based packet filtering in the outbound direction of an interface.
    acl: filters packets based on an IPv4 ACL.

## Slide 30
(Single) Which one of the following rules is a valid basic ACL rule? ( )
  rule permit ip
  rule deny ip
  rule permit source any
  rule deny tcp source any
Which parameters can you use to define advanced ACL rules?
Notes: C
parameters such as the source/destination IP address, source/destination port number, protocol type, and TCP flag (SYN, ACK, or FIN).

## Slide 31
ACL is a widely used network technology. Its principle is as follows: packets are matched against configured ACL rules and actions are taken on the packets as configured in the ACL rules. The matching rules and actions are configured based on network requirements. Due to the variety of matching rules and actions, ACLs can implement a lot of functions.
ACLs are often used with other technologies, such as firewall, routing policy, QoS, and traffic filtering.