## Slide 1
Update
Update
Update
Update
Zhang Xiaohao/ZWX477809
2019.10
New
Update

## Slide 2: AAA Principles and Configuration

## Slide 3
User management is one of the most basic security management requirements for any network.
Authentication, authorization, and accounting (AAA) is a management framework that provides a security mechanism for authorizing some users to access specified resources and recording the operations of these users. AAA is widely used because of its good scalability and easy implementation of centralized management of user information. AAA can be implemented through multiple protocols. In actual applications, the Remote Authentication Dial-In User Service (RADIUS) protocol is the most commonly used to implement AAA.
This course describes the basic concepts, implementation, basic configurations, and typical application scenarios of AAA.

## Slide 4
Upon completion of this course, you will be able to:
  Understand the fundamentals of AAA.
  Describe the application scenarios of AAA.
  Understand the fundamentals of RADIUS.
  Get familiar with the basic configurations of AAA.

## Slide 5
AAA Overview
AAA Configuration

## Slide 6: Basic Concepts of AAA
Authentication, authorization, and accounting (AAA) provides a management mechanism for network security.
Step 1
Step 2
Step 3
Step 4
User identity
Identifies users by information such as the account and password.
Authentication
Identifies and authenticates users who attempt to access resources.
Authorization
Determines whether the access is granted authorization.
Accounting
Checks and records access information.
Notes: Authentication: determines which users can access the network.
Authorization: authorizes users to access specific services.
Accounting: records network resource utilization.
The Internet service provider (ISP) needs to authenticate the account and password of a home broadband user before allowing the user to access the Internet. In addition, the ISP records the online duration or traffic of the user. This is the most common application scenario of the AAA technology.

## Slide 7: Common AAA Architecture
A common AAA architecture includes the user, network access server (NAS), and AAA server.
The NAS collects and manages user access requests in a centralized manner.
Multiple domains are created on the NAS to manage users. Different domains can be associated with different AAA schemes, which include the authentication scheme, authorization scheme, and accounting scheme.
When receiving a user access request, the NAS determines the domain to which the user belongs based on the username and performs user management and control based on the AAA schemes configured for the domain.
Common AAA architecture
User
IP Network
IP Network
User 1@Domain 1
User 2@Domain 2
User 3@Domain 3
NAS
AAA Server
Notes: The NAS manages users based on domains. Each domain can be configured with different authentication, authorization, and accounting schemes to perform authentication, authorization, and accounting for users in the domain.
Each user belongs to a domain. The domain to which a user belongs is determined by the character string following the domain name delimiter @ in the user name. For example, if the user name is user 1@domain 1, the user belongs to domain 1. If the user name does not end with @, the user belongs to the default domain.

## Slide 8: Authentication
AAA supports the following authentication modes: non-authentication, local authentication, and remote authentication.
IP Network
IP Network
User 1@Domain 1
User 2@Domain 2
User 3@Domian 3
Username and password
Username and password
NAS
AAA Server
User 3's username and password
Returning an authentication result
User | Domain | Authentication Mode
User 1@Domain 1 | Domain 1 | Non-authentication
User 2@Domain 2 | Domain 2 | Local authentication
User 3@Domain 3 | Domain 3 | Remote authentication
Notes: AAA supports three authentication modes:
  Non-authentication: Users are fully trusted and their identities are not checked. This authentication mode is seldom used for security purposes.
  Local authentication: Local user information (including the username, password, and attributes) is configured on the NAS. In this case, the NAS functions as the AAA server. Local authentication features fast processing and low operational costs. The disadvantage is that the amount of stored information is limited by device hardware. This authentication mode is often used to manage login users, such as Telnet and FTP users.
  Remote authentication: User information (including the username, password, and attributes) is configured on the authentication server. Remote authentication can be implemented through RADIUS or HWTACACS. The NAS functions as a client to communicate with the RADIUS or HWTACACS server.

## Slide 9: Authorization
AAA supports the following authorization modes: non-authorization, local authorization, and remote authorization.
Authorization information includes the user group, VLAN ID, and ACL number.
IP Network
User 1@Domain 1
User 2@Domain 2
User 3@Domain 3
Delivers permissions to user 2 after authentication succeeds.
AAA Server
NAS
IP Network
User | Domain | Authorization Mode | Authorization Content
User 1@Domain 1 | Domain 1 | Non-authorization | None
User 2@Domain 2 | Domain 2 | Local authorization | Internet access is allowed.
User 3@Domain 3 | Domain 3 | Remote authorization | Authorization is granted by a remote server.
Notes: The AAA authorization function grants users the permission to access specific networks or devices. AAA supports the following authorization modes:
  Non-authorization: Authenticated users have unrestricted access rights on a network.
  Local authorization: Users are authorized based on the domain configuration on the NAS.
  Remote authorization: The RADIUS or HWTACACS server authorizes users.
    In HWTACACS authorization, all users can be authorized by the HWTACACS server.
    RADIUS authorization applies only to the users authenticated by the RADIUS server. RADIUS integrates authentication and authorization. Therefore, RADIUS authorization cannot be performed singly.
When remote authorization is used, users can obtain authorization information from both the authorization server and NAS. The priority of the authorization information configured on the NAS is lower than that delivered by the authorization server.

## Slide 10: Accouting
The accounting function monitors the network behavior and network resource utilization of authorized users.
AAA supports two accounting modes: non-accounting and remote accounting.
IP Network
AAA Server
NAS
User 1@Domain 1
User 2@Domain 2
User 3@Domain 3
Accounting-Start request
Accounting-Start response
IP Network
User | Domain | Accounting Mode
User 1@Domain 1 | Domain 1 | Non-accounting
User 2@Domain 2 | Domain 2 | Non-accounting
User 3@Domain 3 | Domain 3 | Remote accounting
Notes: AAA supports the following accounting modes:
  Non-accounting: Users can access the Internet for free, and no activity log is generated.
  Remote accounting: Remote accounting is performed through the RADIUS server or HWTACACS server.

## Slide 11: AAA Implementation Protocol - RADIUS
Of the protocols that are used to implement AAA, RADIUS is the most commonly used.
The user enters a username and a password.
Access-Request
The authentication is accepted or rejected, and the corresponding packet is delivered.
Accounting-Start request
Accounting-Start response
User
RADIUS Server
NAS
The user is notified of the authentication result.
The user requests to go offline.
Accounting-Stop response
Accounting-Stop request
The user is notified of the completion of network access.
The user starts to access network resources.
Notes: Of the protocols that are used to implement AAA, RADIUS is the most commonly used. RADIUS is a distributed information exchange protocol based on the client/server structure. It implements user authentication, accounting, and authorization.
Generally, the NAS functions as a RADIUS client to transmit user information to a specified RADIUS server and performs operations (for example, accepting or rejecting user access) based on the information returned by the RADIUS server.
RADIUS servers run on central computers and workstations to maintain user authentication and network service access information. The servers receive connection requests from users, authenticate the users, and send the responses (indicating that the requests are accepted or rejected) to the clients. RADIUS uses the User Datagram Protocol (UDP) as the transmission protocol and uses UDP ports 1812 and 1813 as the authentication and accounting ports, respectively. RADIUS features high real-time performance. In addition, the retransmission mechanism and standby server mechanism are also supported, providing good reliability.
The message exchange process between the RADIUS server and client is as follows:
  When a user accesses the network, the user initiates a connection request and sends the username and password to the RADIUS client (NAS).
  The RADIUS client sends an authentication request packet containing the username and password to the RADIUS server.

## Slide 12
Notes:   If the request is valid, the RADIUS server completes authentication and sends the required authorization information to the RADIUS client. If the request is invalid, the RADIUS server sends the authorization failure information to the RADIUS client.
  The RADIUS client notifies the user of whether authentication is successful.
  The RADIUS client permits or rejects the user according to the authentication result. If the user is permitted, the RADIUS client sends an Accounting-Request (Start) packet to the RADIUS server.
  The RADIUS server sends an Accounting-Response (Start) packet to the RADIUS client and starts accounting.
  The user starts to access network resources.
  When a user does not want to access network resources, the user sends a logout request to stop accessing network resources.
  The RADIUS client sends an Accounting-Request (Stop) packet to the RADIUS server.
  The RADIUS server sends an Accounting-Response (Stop) packet to the RADIUS client and stops accounting.
  The RADIUS client notifies the user of the processing result, and the user stops accessing network resources.

## Slide 13: Common AAA Application Scenarios
Local Authentication and Authorization for Administrative Users
AAA for Internet Access Users Through RADIUS
NAS
RADIUS server
Internet access user
AAA schemes are configured on the NAS to implement interworking between the NAS and RADIUS server.
After the user enters a username and a password on the client, the NAS sends the username and password to the RADIUS server for authentication.
If the authentication succeeds, the user is granted the Internet access permission.
The RADIUS server can record the user's network resource utilization during Internet access.
Network administrator
Router
(NAS)
After local AAA schemes are configured on Router, Router compares the username and password of the network administrator with the locally configured username and password when the network administrator logs in to Router.
After the authentication succeeds, Router grants certain administrator permissions to the network administrator.
Login through Telnet/SSH

## Slide 14
AAA Overview
AAA Configuration

## Slide 15: AAA Configuration (1)
Create an authentication scheme.
[Huawei-aaa] authentication-scheme authentication-scheme-name
Create an authentication scheme and enter the authentication scheme view.
[Huawei-aaa-authentication-scheme-name] authentication-mode { hwtacacs | local | radius }
Set the authentication mode to local authentication. By default, the authentication mode is local authentication.
Exit the system view and enter the AAA view.
[Huawei] aaa
Enter the AAA view.
Notes: The authorization-scheme authorization-scheme-name command configures an authorization scheme for a domain. By default, no authorization scheme is applied to a domain.
The authentication-mode { hwtacacs | local | radius } command configures an authentication mode for the current authentication scheme. By default, local authentication is used.

## Slide 16: AAA Configuration (2)
[Huawei-aaa] domain domain-name
Create a domain and enter the domain view.
Create a domain and bind an authentication scheme to the domain.
[Huawei-aaa-domain-name] authentication-scheme authentication-scheme-name
Bind the authentication scheme to the domain.
[Huawei-aaa] local-user user-name password cipher password
Create a local user and configure a password for the local user.
If the username contains a delimiter "@", the character before "@" is the username and the character after "@" is the domain name.
If the value does not contain "@", the entire character string represents the username and the domain name is the default one.
Create a user.

## Slide 17: AAA Configuration (3)
Configure a user access type.
[Huawei-aaa] local-user user-name service-type { { terminal | telnet | ftp | ssh | snmp | http } | ppp | none }
Configure the access type of the local user. By default, all access types are disabled for a local user.
[Huawei-aaa] local-user user-name privilege level level
Specify the permission level of the local user.
Configure a user level.

## Slide 18: AAA Configuration Examples
After a user password and a user level are configured on R1, host A can use the configured username and password to remotely log in to R1.
[R1]aaa
[R1-aaa]local-user huawei password cipher huawei123
[R1-aaa]local-user huawei service-type telnet
[R1-aaa]local-user huawei privilege level 0
[R1]user-interface vty 0 4
[R1-ui-vty0-4]authentication-mode aaa
Host A
R1
GE 0/0/0
10.1.1.1/24

## Slide 19: Configuration Verification (1)
In AAA, each domain is associated with an authentication scheme, an authorization scheme, and an accounting scheme. In this example, the default domain is used.
[R1]display domain name default_admin
Domain-name: default_admin
Domain-state: Active
Authentication-scheme-name: default
Accounting-scheme-name: default
Authorization-scheme-name: -
Service-scheme-name: -
RADIUS-server-template: -
HWTACACS-server-template: -
User-group: -
Notes: The display domain [ name domain-name ]command displays the configuration of a domain.
If the value of Domain-state is Active, the domain is activated.
If the username does not end with @, the user belongs to the default domain. Huawei devices support the following default domains:
  The default domain is for common users.
  The default_admin domain is the default domain for administrators.

## Slide 20: Configuration Verification (2)
After the user properly logs in and logs out, you can view the user record.
[R1]display aaa offline-record all
-------------------------------------------------------------------
User name: huawei
Domain name: default_admin
User MAC: 00e0-fc12-3456
User access type: telnet
User IP address: 10.1.1.2
User ID: 1
User login time: 2019/12/28 17:59:10
User offline time: 2019/12/28 18:00:04
User offline reason: user request to offline
Notes: The display aaa offline-record command displays user offline records.

## Slide 21
What authentication, authorization, and accounting modes are supported by AAA?
When a new common user is configured with local authentication but is not associated with a user-defined domain, which domain does the user belong to?
Notes: AAA supports the following authentication modes: non-authentication, local authentication, and remote authentication. AAA supports the following authorization modes: non-authorization, local authorization, and remote authorization. AAA supports two accounting modes: non-accounting and remote accounting.
If the domain to which a user belongs is not specified when the user is created, the user is automatically associated with the default domain (the administrator is associated with the default_admin domain).

## Slide 22
AAA improves enterprise network security and prevents unauthorized users from logging in to enterprise networks by authenticating the identities of enterprise employees and external users, authorizing accessible resources, and monitoring Internet access behavior.
  Authentication: determines which users can access the network.
  Authorization: authorizes users to access specific services.
  Accounting: records network resource utilization.
AAA technology can be implemented either locally or through a remote server.
Of the protocols that are used to implement AAA, RADIUS is the most commonly used.