## Slide 1
Shi Miaomiao/swx791350
2019.10.23
New
Update

## Slide 2: Network Address Translation

## Slide 3
With the development of the Internet and the increase of network applications, limited public IPv4 addresses have become the bottleneck of network development. To solve this problem, Network Address Translation (NAT) was introduced.
NAT enables hosts on an internal network to access an external network. It not only helps alleviate IPv4 address shortage but also improves the security of the internal network as NAT prevents devices on the external network from directly communicating with hosts on the internal network that uses private addresses.
This course describes the motivation behind NAT, and implementations and application scenarios of different types of NAT.

## Slide 4
On completion of this course, you will be able to:
  Understand the motivation behind NAT.
  Master NAT classification and implementations.
  Master NAT selection in different scenarios.

## Slide 5
NAT Overview
Static NAT
Dynamic NAT
NAPT and Easy IP
NAT Server

## Slide 6: Motivation Behind NAT
As the number of Internet users increases, public IPv4 addresses become scarcer.
What's worse, uneven allocation of these addresses has resulted in a severe shortage of available public IPv4 addresses in some areas.
To overcome public IPv4 address shortage, it is necessary to use transition technologies.
Internet users
0
Public IPv4 addresses

## Slide 7: Private IP Addresses
Public IP addresses: managed and allocated by a dedicated organization and can be used for direct communication on the Internet
Private IP addresses: can be used by organizations or individuals randomly on internal networks, but cannot be used for direct communication on the Internet
The following Class A, B, and C addresses are reserved as private IP addresses:
  Class A: 10.0.0.0–10.255.255.255
  Class B: 172.16.0.0–172.31.255.255
  Class C: 192.168.0.0–192.168.255.255
Internet
Enterprise office campus
School campus network
10.0.0.0/8
Home network
192.168.1.0/16
Coffee shop
192.168.1.0/16
Small-scale factory park
192.168.1.0/16

## Slide 8: NAT Implementation
NAT: translates IP addresses in IP data packets. It is widely used on live networks and is usually deployed on network egress devices, such as routers or firewalls.
Typical NAT application scenario: Private addresses are used on private networks (enterprises or homes), and NAT is deployed on egress devices. For traffic from an internal network to an external network, NAT translates the source addresses of the data packets into specific public addresses. For traffic from an external network to an internal network, NAT translates the destination address of the data packets.
NAT+private addresses effectively conserve public IPv4 addresses.
PC
192.168.1.10/24
Web server
200.1.2.3
Private network
122.1.2.1
NAT
Source IP: 192.168.1.10
Destination IP: 200.1.2.3
Source IP: 122.1.2.1
Destination IP: 200.1.2.3
Source IP: 200.1.2.3
Destination IP: 192.168.1.10
Source IP: 200.1.2.3
Destination IP: 122.1.2.1
1
2
4
3
192.168.1.254
Internet
Notes: Because packets with private IP addresses cannot be routed and forwarded on the Internet, IP packets destined for the Internet cannot reach the egress device of the private network due to lack of routes.
If a host that uses a private IP address needs to access the Internet, NAT must be configured on the network egress device to translate the private source address in the IP data packet into a public source address.

## Slide 9
NAT Overview
Static NAT
Dynamic NAT
NAPT and Easy IP
NAT Server

## Slide 10: Static NAT Implementation
Static NAT: A private IP address is mapped to a fixed public IP address.
Bidirectional access: When an internal host with a private IP address accesses the Internet, the egress NAT device translates the private IP address into a public IP address. Similarly, when an external network device sends packets to access an internal network, the NAT device translates the public address (destination address) carried in the packets into a private address.
Private Address | Public Address
192.168.1.1 | 122.1.2.1
192.168.1.2 | 122.1.2.2
192.168.1.3 | 122.1.2.3
192.168.1.2/24
Web server
200.1.2.3
122.1.2.1
NAT
192.168.1.1/24
192.168.1.3/24
192.168.1.254
Internet
Private network
NAT mapping table
-------------------------------

## Slide 11: Static NAT Example
The source address 192.168.1.1 is translated into 122.1.2.1 for Internet access.
The destination IP address 122.1.2.1 of the packet returned from the Internet is translated into 192.168.1.1.
When the external host sends a packet to proactively access 122.1.2.3, the destination address of the packet is translated into 192.168.1.3 by the egress device through NAT.
The source IP address of the packet sent from 192.168.1.3 is translated into 122.1.2.3 by NAT when the packet passes through the egress device.
Source IP: 192.168.1.1
Destination IP: 200.1.2.3
1
Source IP: 200.1.2.3
Destination IP: 122.1.2.1
3
Source IP: 200.1.2.3
Destination IP: 192.168.1.1
4
Source IP: 122.1.2.1
Destination IP: 200.1.2.3
2
192.168.1.2/24
Web server
200.1.2.3
122.1.2.1
NAT
192.168.1.1/24
192.168.1.3/24
Source IP: 202.1.2.3
Destination IP: 192.168.1.3
2
Source IP: 122.1.2.3
Destination IP: 202.1.2.3
4
Source IP: 192.168.1.3
Destination IP: 202.1.2.3
3
Source IP: 202.1.2.3
Destination IP: 122.1.2.3
1
External host
202.1.2.3
192.168.1.254
Internet

## Slide 12: Configuring Static NAT
[Huawei-GigabitEthernet0/0/0] nat static global { global-address} inside {host-address }
Method 1: Configure static NAT in the interface view.
global { global-address} is used to configure an external public IP address, and inside {host-address } is used to configure an internal private IP address.
[Huawei] nat static global { global-address} inside {host-address }
Method 2: Configure static NAT in the system view.
The command format in the system view is the same as that in the interface view. After this configuration, enable static NAT on a specific interface.
[Huawei-GigabitEthernet0/0/0] nat static enable
This command enables static NAT on the interface.

## Slide 13: Example for Configuring Static NAT
Private network
192.168.1.2/24
Web server
200.1.2.3
GE0/0/1
122.1.2.1
R1
NAT
192.168.1.1/24
192.168.1.3/24
192.168.1.254
[R1]interface GigabitEthernet0/0/1
[R1-GigabitEthernet0/0/1]ip address 122.1.2.1 24
[R1-GigabitEthernet0/0/1]nat static global 122.1.2.1 inside 192.168.1.1
[R1-GigabitEthernet0/0/1]nat static global 122.1.2.2 inside 192.168.1.2
[R1-GigabitEthernet0/0/1]nat static global 122.1.2.3 inside 192.168.1.3
Configure static NAT on R1 to map private addresses of internal hosts to public addresses in one-to-one mode.
Internet

## Slide 14
NAT Overview
Static NAT
Dynamic NAT
NAPT and Easy IP
NAT Server

## Slide 15: Dynamic NAT Implementation
Dynamic NAT: A private IP address is mapped to a public IP address from a NAT address pool containing a group of public IP addresses. Static NAT strictly maps addresses in one-to-one mode. As a result, even if an internal host is offline for a long time or does not send data, the public address is still occupied by the host.
Dynamic NAT prevents such address wastes. When an internal host accesses an external network, an available IP address in a NAT address pool is temporarily assigned to the host and marked as In Use. When the host no longer accesses the external network, the assigned IP address is reclaimed and marked as Not Use.
122.1.2.1 | Not Use
122.1.2.2 | Not Use
122.1.2.3 | Not Use
192.168.1.2/24
Web server
200.1.2.3
122.1.2.1
NAT
192.168.1.1/24
192.168.1.3/24
192.168.1.254
Internet
Private network
NAT address pool
--------------------

## Slide 16: Dynamic NAT Example (1)
Select
192.168.1.2/24
Web server
200.1.2.3
NAT
192.168.1.1/24
122.1.2.1 | In Use
122.1.2.2 | Not Use
122.1.2.3 | Not Use
Source IP: 192.168.1.1
Destination IP: 200.1.2.3
1
Source IP: 122.1.2.2
Destination IP: 200.1.2.3
2
Step 1
Selects an unused address in the address pool as the post-translated address and marks the address as In Use.
Step 2
Generates a temporary NAT mapping table.
Internet
NAT address pool
--------------------
NAT mapping table
Private Address | Public Address
192.168.1.1 | 122.1.2.2
192.168.1.2 | 122.1.2.1
192.168.1.3/24

## Slide 17: Dynamic NAT Example (2)
Match
192.168.1.2/24
Web server
200.1.2.3
NAT
192.168.1.1/24
192.168.1.3/24
Private Address | Public Address
192.168.1.1 | 122.1.2.2
192.168.1.2 | 122.1.2.1
Source IP: 200.1.2.3
Destination IP: 122.1.2.2
3
Source IP: 200.1.2.3
Destination IP: 192.168.1.1
4
Searches the NAT mapping table for the desired private IP address based on the public IP address and translates the destination IP address of the IP data packet into the private address.
Internet
NAT mapping table
-----------------------------

## Slide 18: Configuring Dynamic NAT
[Huawei] nat address-group group-index start-address end-address
Create an address pool.
Configure a public address range. group-index specifies the address pool ID, and start-address and end-address specify the start and end addresses of the address pool, respectively.
[Huawei] acl number
[Huawei-acl-basic-number ] rule permit source source-address source-wildcard
Configure an ACL rule for NAT.
Configure a basic ACL to match the source address range that requires dynamic NAT.
[Huawei-GigabitEthernet0/0/0] nat outbound acl-number address-group group-index [ no-pat ]
Configure outbound NAT with the address pool in the interface view.
Associate the ACL rule with the address pool for dynamic NAT on the interface. The no-pat parameter specifies that port translation is not performed.

## Slide 19: Example for Configuring Dynamic NAT
Private network
[R1]nat address-group 1 122.1.2.1 122.1.2.3
[R1]acl 2000
[R1-acl-basic-2000]rule 5 permit source 192.168.1.0 0.0.0.255
[R1-acl-basic-2000]quit
[R1]interface GigabitEthernet0/0/1
[R1-GigabitEthernet0/0/1]nat outbound 2000 address-group 1 no-pat
Configure dynamic NAT on R1 to dynamically map private addresses of internal hosts to public addresses.
192.168.1.2/24
Web server
200.1.2.3
NAT
R1
192.168.1.1/24
192.168.1.3/24
Internet
GE0/0/1

## Slide 20
NAT Overview
Static NAT
Dynamic NAT
NAPT and Easy IP
NAT Server

## Slide 21: NAPT Implementation
Dynamic NAT does not translate port numbers. It belongs to No-Port Address Translation (No-PAT). In this mode, the mapping between public and private addresses is still 1:1, which cannot improve public address utilization.
Network Address and Port Translation (NAPT): translates both IP addresses and port numbers from multiple internal hosts to one public IP address in an address pool. In this way, 1:n mapping between public and private addresses is implemented, which effectively improves public address utilization.
NAT mapping table
-------------
Private network
192.168.1.2/24
Web server
200.1.2.3
122.1.2.1
NAT
192.168.1.1/24
192.168.1.3/24
122.1.2.1
122.1.2.2
122.1.2.3
Private IP Address:Port Number | Public IP Address:Port Number
192.168.1.1:10321 | 122.1.2.2:1025
192.168.1.2:17087 | 122.1.2.2:1026
192.168.1.254
Internet
NAT address pool
--------------------
Notes: NAPT enables a public IP address to map multiple private IP addresses through ports. In this mode, both IP addresses and transport-layer ports are translated so that different private addresses with different source port numbers are mapped to the same public address with different source port numbers.

## Slide 22: NAPT Example (1)
Select
Mapping table
-------------
Source: 192.168.1.1:10321
Destination: 200.1.2.3:80
1
Source: 122.1.2.2:1025
Destination: 200.1.2.3:80
2
122.1.2.1
122.1.2.2
122.1.2.3
Step 1
Selects an address from the address pool and translates both the source IP address and port number.
Step 2
Generates a temporary NAT mapping table, which records:
[Source IP address:port number before translation], [IP address:port number after translation].
Private IP Address:Port Number | Public IP Address:Port Number
192.168.1.1:10321 | 122.1.2.2:1025
192.168.1.2:17087 | 122.1.2.2:1026
192.168.1.2/24
Web server
200.1.2.3
NAT
192.168.1.1/24
192.168.1.3/24
Internet
NAT address pool
-------------

## Slide 23: NAPT Example (2)
NAT mapping table
-------------
192.168.1.2/24
Web server
200.1.2.3
NAT
192.168.1.1/24
192.168.1.3/24
Match
Searches the NAT mapping table for the desired private IP address and port number based on the public IP address and port number, and translates the destination IP address and port number of the IP data packet.
Private IP Address:Port Number | Public IP Address:Port Number
192.168.1.1:10321 | 122.1.2.2:1025
192.168.1.2:17087 | 122.1.2.2:1026
Source: 200.1.2.3:80
Destination: 122.1.2.2:1025
3
Source: 200.1.2.3:80
Destination: 192.168.1.1:10321
4
Internet

## Slide 24: Example for Configuring NAPT
Private network
[R1]nat address-group 1 122.1.2.1 122.1.2.1
[R1]acl 2000
[R1-acl-basic-2000]rule 5 permit source 192.168.1.0 0.0.0.255
[R1-acl-basic-2000]quit
[R1]interface GigabitEthernet0/0/1
[R1-GigabitEthernet0/0/1]nat outbound 2000 address-group 1
Configure NAPT on R1 to allow all hosts with private IP addresses on the internal network to access the public network through 122.1.2.1.
192.168.1.2/24
Web server
200.1.2.3
NAT
R1
192.168.1.1/24
192.168.1.3/24
192.168.1.254
GE0/0/1
Internet

## Slide 25: Easy IP
Easy IP: translates both IP addresses and transport-layer port numbers. The implementation of Easy IP is the same as that of NAPT. The difference is that Easy IP does not involve address pools. It uses an interface address as a public address for NAT.
Easy IP applies to scenarios where public IP addresses are not fixed, such as scenarios where public IP addresses are dynamically obtained by egress devices on private networks through DHCP or PPPoE dialup.
NAT mapping table
-------------
Private network
192.168.1.2/24
Web server
200.1.2.3
122.1.2.1
NAT
192.168.1.1/24
192.168.1.3/24
Private IP Address:Port Number | Public IP Address:Port Number
192.168.1.1:10321 | 122.1.2.1:1025
192.168.1.2:17087 | 122.1.2.1:1026
192.168.1.254
Internet
Notes: DHCP: Dynamic Host Configuration Protocol
PPPoE: Point-to-Point Protocol over Ethernet

## Slide 26: Example for Configuring Easy IP
[R1-acl-basic-2000]rule 5 permit source 192.168.1.0 0.0.0.255
[R1-acl-basic-2000]quit
[R1]interface GigabitEthernet0/0/1
[R1-GigabitEthernet0/0/1]nat outbound 2000
Configure Easy IP on R1 to allow all hosts with private IP addresses on the internal network to access the public network through 122.1.2.1.
Private network
192.168.1.2/24
Web server
200.1.2.3
NAT
R1
192.168.1.1/24
192.168.1.3/24
192.168.1.254
GE0/0/1
Internet

## Slide 27
NAT Overview
Static NAT
Dynamic NAT
NAPT and Easy IP
NAT Server

## Slide 28: NAT Server
NAT Server: maps an internal server to a public network through a one-to-one mapping between a [public IP address:port number] and a [private IP address:port number]. This function is used when the internal server needs to provide services for the public network.
An external host proactively accesses the [public IP address:port number] to communicate with the internal server.
Private network
Private IP Address:Port Number | Public IP Address:Port Number
192.168.1.10:80 | 122.1.2.1:80
200.1.2.3
Web server
192.168.1.10
192.168.1.254
122.1.2.1
NAT
Internet
NAT mapping table
-----------------------

## Slide 29: NAT Server Example
Match
Private IP Address:Port Number | Public IP Address:Port Number
192.168.1.10:80 | 122.1.2.1:80
Source: 122.1.2.1:80
Destination: 202.1.2.3:47819
4
Source: 192.168.1.10:80
Destination: 202.1.2.3:47819
3
Source: 200.1.2.3:47819
Destination: 122.1.2.1:80
1
Source: 200.1.2.3:47819
Destination: 192.168.1.10:80
2
Searches the NAT mapping table for the desired private address:port number based on the public address:port number, and translates the destination address:port number of the IP data packet to the private address:port number.
Reversely translates the source IP address:port number based on the NAT mapping table.
200.1.2.3
Web server
192.168.1.10
192.168.1.254
122.1.2.1
NAT
Internet
NAT mapping table
-----------------

## Slide 30: Example for Configuring NAT Server
[R1]interface GigabitEthernet0/0/1
[R1-GigabitEthernet0/0/1]ip address 122.1.2.1 24
[R1-GigabitEthernet0/0/1]nat server protocol tcp global 122.1.2.1 www inside 192.168.1.10 8080
Configure NAT Server on R1 to map the internal server's IP address 192.168.1.10 and port number 80 to the public IP address 122.1.2.1 and port number 8080.
200.1.2.3
Web server
192.168.1.10
192.168.1.254
122.1.2.1
NAT
Internet
Private network

## Slide 31
What types of NAT can enable external devices to proactively access an internal server?
What are the advantages of NAPT over No-PAT?
Notes: Static NAT and NAT Server Static NAT implements bidirectional communication, meaning that external devices are allowed to access an internal server. NAT Server is designed to allow external devices to proactively access an internal server.
NAPT can translate multiple private IP addresses into one public IP address, improving public IP address utilization.

## Slide 32
Using private addresses on private networks and using NAT at the network egress effectively reduce the number of required public IPv4 addresses. NAT effectively alleviates the shortage of public IPv4 addresses.
Dynamic NAT, NAPT, and Easy IP provide source address translation for private network hosts to access the public network.
NAT Server enables internal servers to provide services for public networks.
Static NAT provides one-to-one mapping and supports bidirectional communication.