## Slide 1
V5R2
V1R1
Lu Yueyue/lwx445705
2019-12
New

## Slide 2: WLAN Overview

## Slide 3
Wired LANs are expensive and lack mobility. The increasing demand for portability and mobility requires wireless local area network (WLAN) technologies.
WLAN is now the most cost-efficient and convenient network access mode.
This course introduces the development of WLAN in different phases, concepts related to WLAN technologies, implementation and basic configurations of common WLAN networking architectures, and WLAN development trends.

## Slide 4
On completion of this course, you will be able to:
  Understand basic concepts of WLAN and the history of the 802.11 protocol family.
  Learn about different WLAN devices.
  Distinguish between different WLAN networking architectures.
  Understand the WLAN working process.
  Complete basic WLAN configurations.

## Slide 5
WLAN Overview
Basic Concepts of WLAN
WLAN Fundamentals
WLAN Configuration Implementation
Next-Generation WLAN Solutions

## Slide 6: Introduction to WLAN
A wireless local area network (WLAN) is constructed using wireless technologies. It uses high-frequency (2.4 GHz or 5 GHz) signals such as radio waves, lasers, and infrared rays to replace the traditional media used for transmission on a wired LAN.
WLAN technology allows users to easily access a wireless network and move around within the coverage of the wireless network.
Wired Network
Switch
Switch
Router
PC
Access Point
Radio signals
Wireless Network
Notes: A wireless local area network (WLAN) is constructed using wireless technologies.
  Wireless technologies mentioned here include not only Wi-Fi, but also infrared, Bluetooth, and ZigBee.
  WLAN technology allows users to easily access a wireless network and move around within the coverage of the wireless network.
Wireless networks can be classified into WPAN, WLAN, WMAN, and WWAN based on the application scope.
  Wireless personal area network (WPAN): Bluetooth, ZigBee, NFC, HomeRF, and UWB technologies are commonly used.
  Wireless local area network (WLAN): The commonly used technology is Wi-Fi. WPAN-related technologies may also be used in WLANs.
  Wireless metropolitan area network (WMAN): Worldwide Interoperability for Microwave Access (WiMAX) is commonly used.
  Wireless wide area network (WWAN): GSM, CDMA, WCDMA, TD-SCDMA, LTE, and 5G technologies are commonly used.

## Slide 7
Notes: Advantages of WLAN:
  High network mobility: WLANs are easily connected, and are not limited by cable and port positions. This makes WLANs most suitable for scenarios where users are often moving, such as in office buildings, airport halls, resorts, hotels, stadiums, and cafes.
  Flexible network deployment: WLANs provide wireless network coverage in places where cables are difficult to deploy, such as subways and highways. WLANs reduce the number of required cables, offer low-cost, simplify deployment, and have high scalability.
Note: WLAN technology described in this document is implemented based on 802.11 standards. That is, a WLAN uses high-frequency (2.4 GHz or 5 GHz) signals as transmission media.

## Slide 8: IEEE 802.11、WLAN and Wi-Fi
IEEE 802.11 suites are standards for WLANs which are definded by the Institute of Electrical and Electronics Engineering (IEEE).
Wi-Fi Alliance was formed by a group of major manufacturers and the logo "Wi-Fi" was created. The Wi-Fi standards are WLAN technologies based on IEEE 802.11 standards.
LAN
Ethernet
IEEE 802.3
WLAN
Wi-Fi
IEEE 802.11
IEEE 802.11 Standards and Wi-Fi Generations
Released In
Standard
Throughput
Frequency
Band
802.11
2Mbit/s
2.4GHz
802.11b
11Mbit/s
2.4GHz
802.11a、802.11g
54Mbit/s
2.4GHz、5GHz
802.11n
300Mbit/s
2.4GHz & 5GHz
802.11ac wave1
1300Mbit/s
5GHz
1997
1999
2003
2009
2013
2015
Wi-Fi
Wi-Fi 4
802.11ac wave2
6.9Gbit/s
5GHz
Wi-Fi 5
802.11ax
Wi-Fi 6
9.6Gbit/s
2.4GHz & 5GHz
Wi-Fi 3
Wi-Fi 1
Wi-Fi 2
2018
Notes: IEEE 802.11 standards are located on the lower two layers of the equivalent TCP/IP model.
  Data link layer: provides channel access, addressing, data frame check, error detection, and security mechanisms.
  Physical layer: transmits bit streams over an air interface, for example, specifying the frequency band.
When created in 1999, the Wi-Fi Alliance was called the Wireless Ethernet Compatibility Alliance (WECA) at that time. In October 2002, the WECA was renamed Wi-Fi Alliance.
The first version of IEEE 802.11 was released in 1997. Since then, more IEEE 802.11-based supplementary standards have been gradually defined. The most well-known standards that affect the evolution of Wi-Fi are 802.11b, 802.11a, 802.11g, 802.11n, and 802.11ac.
When the IEEE 802.11ax standard is released, the Wi-Fi Alliance renames the new Wi-Fi specification to Wi-Fi 6, the mainstream IEEE 802.11ac to Wi-Fi 5, and IEEE 802.11n to Wi-Fi 4. The same naming convention applies to other generations.

## Slide 9: Wi-Fi Development Trends in Office Scenarios
Early 1990s
Late 1990s
Today
Mobile 1.0
Mobile 2.0
Mobile 3.0
Fixed office
Desktop computer:
Data service
Primary mobile office
Laptop:
Voice and data services
802.11b/a/g
BYOD
Wireless office era
Mobile phone, tablet, and Ultrabook:
Video, voice, and data services
A large number of real-time services
802.11n -> 802.11ac
All-wireless era
Diversified terminals:
Refined online service
802.11ax/ad...
VR/4K video
VR/AR
4K
...
Wireless networks as a supplement to wired networks
Wired and wireless integration
All-wireless office, wireless-centric
Notes: Phase 1: Initial Mobile Office Era — Wireless Networks as a Supplement to Wired Networks
  WaveLAN technology is considered as the prototype of enterprise WLAN. Early Wi-Fi technologies were mainly applied to IoT devices such as wireless cash registers. However, with the release of 802.11a/b/g standards, wireless connections have become increasingly advantageous. Enterprises and consumers are beginning to realize the potential of Wi-Fi technologies, and wireless hotspots are found to be deployed in cafeterias, airports, and hotels.
  The name Wi-Fi was also created during this period. It is the trademark of the Wi-Fi Alliance. The original goal of the alliance was to promote the formulation of the 802.11b standard as well as the compatibility certification of Wi-Fi products worldwide. With the evolution of standards and the popularization of standard-compliant products, people tend to equate Wi-Fi with the 802.11 standard.
  The 802.11 standard is one of many WLAN technologies, and yet it has become a mainstream standard in the industry. When a WLAN is mentioned, it usually is a WLAN using the Wi-Fi technology.
  The first phase of WLAN application eliminated the limitation of wired access, with the goal to enable devices to move around freely within a certain range. That is, WLAN extends wired networks with the utilization of wireless networks. In this phase, WLANs do not have specific requirements on security, capacity, and roaming capabilities. APs are still single access points used for wireless coverage in single-point networking. Generally, an AP using a single access point architecture is called a Fat AP.

## Slide 10
Notes: Phase 2: Wireless Office Era — Integration of Wired and Wireless Networks
  With the increasing popularity of wireless devices, WLANs have evolved from the supplement of wired networks to necessities.
  In this phase, a WLAN, as a part of the network, needs to provide network access for enterprise guests.
  Numerous large-bandwidth services, such as video and voice, are required in office scenarios, thereby imposing higher bandwidth requirements on WLANs. Since 2012, the 802.11ac standard has become mature and implemented many improvements in the working frequency bands, channel bandwidths, as well as modulation and coding schemes (MCSs). Compared with earlier 802.11 standards, the 802.11ac standard includes higher traffic volumes and less interference, and it allows more users to access networks.
Phase 3: All-Wireless Office Era, Wireless-Centric
  Currently, WLANs have entered the third phase. In office environments, wireless networks are used in preference to wired networks, and each office area is covered entirely by Wi-Fi. Furthermore, office areas do not include a wired network port, making the office environment more open and intelligent.
  In the future, high-bandwidth services, including cloud desktop office, telepresence conference, and 4K video, will be migrated from wired to wireless networks. Likewise, new technologies such as virtual reality (VR)/augmented reality (AR) will be directly deployed on wireless networks. These new application scenarios pose higher requirements on WLAN design and planning.
  The year 2018 marked the release of the next-generation Wi-Fi standard, referred to as Wi-Fi 6 and 802.11ax by the Wi-Fi Alliance and IEEE, respectively. This represents another milestone in Wi-Fi development. In that regard, the core value of Wi-Fi 6 is further improvements in capacity, leading wireless communications into the 10-gigabit era. The concurrent performance has improved fourfold, ensuring excellent service capabilities in high-density access and heavy-load scenarios.

## Slide 11
WLAN Overview
Basic Concepts of WLAN
WLAN Fundamentals
WLAN Configuration Implementation
Next-Generation WLAN Solutions

## Slide 12: WLAN Devices
Basic Concepts
Wired Network
Wireless Network
Wireless Router
PoE Switch
AP (Access Point)
AC (Access Controller)
Network
Home
Enterprise
Notes: Huawei WLAN products provide high-speed, secure, and reliable wireless network connections in various scenarios, such as indoor and outdoor scenarios and home and enterprise scenarios.
Wireless routers are Fat APs in most cases.
  A wireless router converts wired network signals into wireless signals to be received by devices such as home computers and mobile phones so that they can access the Internet in wireless mode.
Enterprise WLAN products:
  AP
    The AP can switch flexibly among the Fat, Fit, and cloud modes based on the network plan.
    Fat AP: applies to home WLANs. A Fat AP works independently and requires separate configurations. It provides only simple functions and is cost-effective. The Fat AP independently implements functions such as user access, authentication, data security, service forwarding, and QoS.
    Fit AP: applies to medium- and large-sized enterprises. Fit APs are managed and configured by the AC in a unified manner, provide various functions, and have high requirements on network maintenance personnel's skills. Fit APs must work with an AC for user access, AP going-online, authentication, routing, AP management, security, and QoS.
    Cloud AP: applies to small- and medium-sized enterprises. Cloud APs are managed and configured by a cloud management platform in a unified manner, provide various functions, support plug-and-play, and have low requirements on network maintenance personnel's skills.

## Slide 13
Notes:   AC
    An AC is usually deployed at the aggregation layer of a network to provide high-speed, secure, and reliable WLAN services.
    Huawei ACs provide a large capacity and high performance. They are highly reliable, easy to install and maintain, and feature such advantages as flexible networking and energy conservation.
  PoE Switch
    Power over Ethernet (PoE) provides electrical power through the Ethernet. It is also called Power over LAN (PoL) or active Ethernet.
    PoE transmits power to terminals through data transmission lines or idle lines.
    On a WLAN, a PoE switch can be used to supply power to APs.
    PoE can be used to effectively provide centralized power for terminals such as IP phones, APs, portable device chargers, POS machines, cameras, and data collection devices. With PoE, terminals are provided with power when they access the network. Therefore, indoor cabling of power supply is not required.

## Slide 14: Basic WLAN Networking Architecture
Fat AP Architecture
AC + Fit AP Architecture
Campus Network
Campus
Egress Gateway
Fit AP
CAPWAP
CAPWAP
AC
STA
Radio signal
Campus Network
Campus
Egress Gateway
STA
Fat AP
Radio signal
Wired Network
Ethernet Protocols
Wireless Network
802.11 Protocols
Basic Concepts
Wired Network
Wireless Network
Internet
Internet
Notes: A WLAN involves both wired and wireless sides. On the wired side, APs connect to the Internet using Ethernet. On the wireless side, STAs communicate with APs using 802.11 standards.
The wireless side uses the centralized architecture. The original Fat AP architecture evolves to the AC + Fit AP architecture.
  Fat AP architecture
    This architecture is also called autonomous network architecture because it does not require a dedicated device for centralized control. It can implement functions such as connecting wireless users, encrypting service data, and forwarding service data packets.
    Applicable scope: home and small-sized enterprises
    Characteristics: A Fat AP works independently and is configured separately. It provides only simple functions and is cost-effective.
    Disadvantages: The increase in the WLAN coverage area and the number of access users requires more and more Fat APs. No unified control device is available for these independently working Fat APs. Therefore, it is difficult to manage and maintain the Fat APs.

## Slide 15
Notes:   AC + Fit AP architecture
    In this architecture, an AC is responsible for WLAN access control, forwarding and statistics collection, AP configuration monitoring, roaming management, AP network management agent, and security control. A Fit AP encrypts and decrypts 802.11 packets, provides 802.11 physical layer functions, and is managed by an AC.
    Applicable scope: medium- and large-sized enterprises
    Characteristics: Fit APs are managed and configured by the AC in a unified manner, provide various functions, and have high requirements on network maintenance personnel's skills.
Note: This course uses the AC + Fit AP architecture as an example.
Basic WLAN Concepts
  Station (STA)
    802.11-compliant terminal, for example, PC with wireless network interface cards (NICs) or mobile phone that supports WLAN
  AC
    Controls and manages all Fit APs on an AC + Fit AP network. For example, an AC can connect to an authentication server to authenticate WLAN users.
  AP
    Provides 802.11-compliant wireless access for STAs. APs connect wired networks to wireless networks.
  Control And Provisioning of Wireless Access Points (CAPWAP)
    An encapsulation and transmission mechanism defined in RFC 5415 to implement communication between APs and ACs.
  Radio signal (radio electromagnetic wave)
    High-frequency electromagnetic wave that has long-distance transmission capabilities. Radio signals provide transmission media for 802.11-compliant WLANs. Radio signals described in this course are electromagnetic waves on the 2.4 GHz or 5 GHz frequency band.

## Slide 16: Agile Distributed Architecture
Architecture Characteristics
The agile distributed architecture divides an AP into a central AP and remote units (RUs). The central AP can manage multiple RUs, which provides good coverage and reduces costs. RUs can be used in the Fat AP, AC + Fit AP, and cloud management architectures.
Application scope: densely distributed rooms
Central AP
Room 1
Room 2
Room 3
Room N
Central AP
Room 1
Room 2
Room 3
Room N
AC
RU
RU
Basic Concepts
Wired Network
Wireless Network

## Slide 17: CAPWAP
Basic Concepts
Wired Network
Wireless Network
Campus Network
CAPWAP Tunnel
AC
STA
AP1
STA
STA
...
AP2
APn
CAPWAP Tunnel
CAPWAP Tunnel
What Is a CAPWAP Tunnel?
Control And Provisioning of Wireless Access Points (CAPWAP): defines how to manage and configure APs. That is, an AC manages and controls APs in a centralized manner through CAPWAP tunnels.
Maintains the running status of the AC and APs.
Allows the AC to manage APs and deliver service configurations to the APs.
Allows APs to exchange data sent by STAs with the AC through CAPWAP tunnels when the tunnel forwarding mode is used.
CAPWAP Tunnel Functions
Transfer:
Control information
User data
Notes: To meet the requirements of large-scale networking and unified management of APs on the network, the Internet Engineering Task Force (IETF) sets up a CAPWAP Working Group and formulates the CAPWAP protocol. This protocol defines how an AC manages and configures APs. That is, CAPWAP tunnels are established between the AC and APs, through which the AC manages and controls the APs.
CAPWAP is an application-layer protocol based on UDP transmission.
  CAPWAP functions in the transmission of two types of messages:
    Data messages, which encapsulate wireless data frames through the CAPWAP data tunnel.
    Control messages, which are exchanged for AP management through the CAPWAP control tunnel.
  CAPWAP data and control packets are transmitted on different UDP ports:
    UDP port 5246 for transmitting control packets
    UDP port 5247 for transmitting data packets

## Slide 18: AP-AC Networking
The AP-AC networking modes are classified into Layer 2 networking and Layer 3 networking.
Basic Concepts
Wired Network
Wireless Network
AP1
AC
Layer 2 Network
APn
...
Layer 2 Networking
AP1
AC
Layer 3 Network
APn
...
Layer 3 Networking
Layer 2 networking: APs are connected to an AC directly or across a Layer 2 network.
The Layer 2 networking features quick deployment. It is applicable to simple or temporary networking but not to large networking.
Layer 3 networking: APs are connected to an AC across a Layer 3 network.
In the actual networking, an AC can connect to dozens or even hundreds of APs, which is usually complex. In most cases, the Layer 3 networking is used on a large network.
Notes: AP-AC networking: The Layer 2 or Layer 3 networking can be used between the AC and APs. In the Layer 2 networking, APs can go online in plug-and-play mode through Layer 2 broadcast or DHCP. In the Layer 3 networking, APs cannot directly discover an AC. We need to deploy DHCP or DNS, or manually specify the AC's IP address.
In the actual networking, an AC may connect to dozens or even hundreds of APs, which is complex. For example, on an enterprise network, APs can be deployed in offices, meeting rooms, and guest rooms, and the AC can be deployed in the equipment room. This constructs a complex Layer 3 network between the AC and APs. Therefore, the Layer 3 networking is often used on large-scale networks.

## Slide 19: AC Connection Mode
ACs can be connected in in-path or off-path mode.
Basic Concepts
Wired Network
Wireless Network
In-Path Networking
Off-Path Networking
In the in-path networking, the APs, AC, and core network are connected in a chain. All data destined for the core layer passes through the AC.
In this networking, the AC also functions as an aggregation switch to forward and process data traffic and management traffic of APs.
In the off-path networking, the AC connects to the network between APs and the core network, but does not directly connect to APs.
In this networking, the AC is connected to APs in off-path mode, the service data of APs reaches the uplink network without passing through the AC.
AP1
AC
IP Network
APn
...
Core Network
CAPWAP
CAPWAP
AP1
IP Network
APn
...
Core Network
AC
CAPWAP
CAPWAP
Notes: AC connection mode: In in-path mode, the AC is deployed on the traffic forwarding path, and user traffic passes through the AC. This consumes the AC's forwarding capability. In off-path mode, traffic does not pass through the AC.
In-path networking:
  In the in-path networking, the AC must be powerful in throughput and processing capabilities, or the AC becomes the bandwidth bottleneck.
  This networking has a clear architecture and is easy to deploy.
Off-path networking:
  Most wireless networks are deployed after wired networks are constructed and are not planned in early stage of network construction. The off-path networking makes it easy to expand the wireless network. Customers only need to connect an AC to a network device, for example, an aggregation switch, to manage APs. Therefore, the off-path networking is used more often.
  In the off-path networking, the AC only manages APs, and management flows are encapsulated and transmitted in CAPWAP tunnels. Data flows can be forwarded to the AC over CAPWAP tunnels, or forwarded to the uplink network by the aggregation switch and do not pass through the AC.

## Slide 20: Wireless Communications System
In a wireless communications system, information may be an image, a text, a sound, or the like. The transmit device first applies source coding to convert information into digital signals that allow for circuit calculation and processing, and then into radio waves by means of channel coding and modulation.
Basic Concepts
Wired Network
Wireless Network
Source
Coding
Channel
(transmission media)
Decoding
Sink
Noise source
Modulation
Transmit device
Receive device
Wireless Communications System
Demodulation
Notes: Coding
  Source coding is a process of converting raw information into digital signals by using a coding scheme.
  Channel coding is a technology for correcting and detecting information errors to improve channel transmission reliability. With wireless transmission that is prone to noise interference, information arriving at the receive device may be erroneous. Channel coding is introduced to restore information to the maximum extent on the receive device, thereby reducing the bit error rate.
Modulation is a process of superimposing digital signals on high-frequency signals generated by high-frequency oscillation circuits so that the digital signals be converted into radio waves over antennas and then transmitted.
A channel transmits information, and a radio channel is a radio wave in space.
The air interface is used by radio channels. The transmit device and receive device are connected through the air interfaces and channels. The air interfaces in wireless communication are invisible and connected over the air.

## Slide 21: Radio Wave
A radio wave is an electromagnetic wave whose frequency is between 3 Hz and about 300 GHz. Radio technology converts sound signals or other signals and transmits them by using radio waves.
WLAN technology enables transmission of information by radio waves over the air. Currently, the WLAN uses the following frequency bands:
  2.4 GHz frequency band (2.4–2.4835 GHz)
  5 GHz frequency band (5.15–5.35 GHz, 5.725–5.85 GHz)
Basic Concepts
Wired Network
Wireless Network
3
30
300
3
30
300
3
30
300
3
30
300
Hz
kHz
MHz
GHz
 | Extremely low frequency (ELF) | Super low frequency (SLF) | Ultra low frequency (ULF) | Very low frequency (VLF) | Low frequency (LF) | Intermediate frequency (IF) | High frequency (HF) | Very high frequency (VHF) | Ultra high frequency (UHF) | Super high frequency (SHF) | Extremely high frequency (EHF) | 
Infrared, visible light, ultraviolet light, and ray
Radio wave spectrum:
2.4 GHz frequency band
IEEE 802.11b/g/n/ax
5 GHz frequency band
IEEE 802.11a/n/ac/ax
Notes: ELF (3 Hz to 30 Hz): Used for submarine communication or directly converted into sound
SLF (30 Hz to 300 Hz): Directly converted into sound or used for AC transmission system (50–60 Hz)
ULF (300 Hz to 3 kHz): Used for communications in mining farms or directly converted into sound
VLF (3 kHz to 30 kHz): Directly converted into sound and ultrasound or used for geophysics
LF (30 kHz to 300 kHz): Used for international broadcasting
IF (300 kHz to 3 MHz): Used for amplitude modulation (AM) broadcasting, maritime communications, and aeronautical communications
HF (3 MHz to 30 MHz): Used for short-wave and civil radios
VHF (30 MHz to 300 MHz): Used for frequency modulation (FM) broadcasting, television broadcasting, and aeronautical communications
UHF (300 MHz to 3 GHz): Used for television broadcasting, radio telephone communications, wireless network, and microwave oven
SHF (3 GHz to 30 GHz): Used for wireless network, radar, and artificial satellite
EHF (30 GHz to 300 GHz): Used for radio astronomy, remote sensing, and millimeter wave scanner
Higher than 300 GHz: Infrared, visible light, ultraviolet light, and ray

## Slide 22: Radio Channel
A channel transmits information, and a radio channel is a radio wave in space. Given that radio waves are ubiquitous, the random use of spectrum resources will cause endless interference issues. Therefore, in addition to defining the usable frequency bands, wireless communication protocols must also accurately divide the frequency ranges. Each frequency range is a channel.
Basic Concepts
Wired Network
Wireless Network
2.4 GHz Frequency Band
5 GHz Frequency Band
The 5 GHz frequency band has richer spectrum resources. In addition to 20 MHz channels, APs working on the 5 GHz frequency band support 40 MHz, 80 MHz, and higher-bandwidth channels.
The 2.4 GHz frequency band is divided into 14 channels with overlapping or non-overlapping relationships, each with a bandwidth of 20 MHz.
  Overlapping channels, such as channels 1 and 2, interfere with each other.
  Non-overlapping channels, such as channels 1 and 6, do not interfere with each other.
Notes: On a WLAN, the operating status of APs is affected by the radio environment. For example, a high-power AP can interfere with adjacent APs if they work on overlapping channels.
In this case, the radio calibration function can be deployed to dynamically adjust channels and power of APs managed by the same AC to ensure that the APs work at the optimal performance.

## Slide 23: BSS/SSID/BSSID
Basic service set (BSS):
  An area covered by an AP.
  STAs in a BSS can communicate with each other.
Basic service set identifier (BSSID):
  An identifier of a WLAN, which is represented by the AP's MAC address.
Service set identifier (SSID):
  An identifier of a WLAN, which is represented by a string of characters.
  SSIDs can replace BSSIDs to help users identify different WLANs.
Basic Concepts
Wired Network
Wireless Network
Discover guest
SSID: guest
BSSID: 00e0.fc45.24a0
AP
Discover guest
Discover guest
BSS
Notes: BSS:
  A BSS, the basic service unit of a WLAN, consists of an AP and multiple STAs. The BSS is the basic structure of an 802.11 network. Wireless media can be shared, and therefore packets sent and received in a BSS must carry the BSSID (AP's MAC address).
BSSID:
  AP's MAC address on the data link layer.
  STAs can discover and find an AP based on the BSSID.
  Each BSS must have a unique BSSID. Therefore, the AP's MAC address is used to ensure the uniqueness of the BSSID.
SSID:
  A unique identifier that identifies a wireless network. When you search for available wireless networks on your laptop, SSIDs are displayed to identify the available wireless networks.
  If multiple BSSs are deployed in a space, the STA may discover not only one BSSID. You only need to select a BSSID as required. For easier AP identification, a string of characters is configured as the AP name. This character string is the SSID.

## Slide 24: VAP
In the early stage, APs support only one BSS. If multiple BSSs are deployed in a space, we must also deploy multiple APs, which increases costs and occupies channel resources. To resolve this problem, APs now support creation of multiple virtual access points (VAPs).
VAP:
  A physical AP can be virtualized into multiple VAPs, each of which provides the same functions as the physical AP.
  Each VAP corresponds to one BSS. In this way, one AP may provide multiple BSSs that can have different SSIDs specified.
Basic Concepts
Wired Network
Wireless Network
BSS1: VAP1
SSID: guest
BSSID: 00e0.fc45.24a0
BSS2: VAP2
SSID: internal
BSSID: 00e0.fc45.24a9
Discover guest and internal
Discover guest and internal
Discover guest and internal
AP
Notes: VAP:
  A VAP is a functional entity virtualized on a physical AP. You can create different VAPs on an AP to provide the wireless access service for different user groups.
The use of VAPs simplifies WLAN deployment, but it does not mean that we need to configure as many as VAPs. VAPs must be planned based on actual requirements. Simply increasing the number of VAPs will increase the time for STAs to find SSIDs and make AP configuration more complex. Additionally, a VAP is not equivalent to a real AP. All VAPs virtualized from a physical AP share software and hardware resources of the AP, and all users associated with these VAPs share same channel resources. The capacity of an AP will not change or multiply with the increasing number of VAPs.

## Slide 25: ESS
The coverage of a BSS is limited. An extended service set (ESS) can be used to expand the coverage. When a STA moves from one BSS to another BSS, an ESS ensures that the STA does not sense the change of the SSID.
ESS:
  A larger-scale virtual BSS that consists of multiple BSSs with the same SSID.
Basic Concepts
Wired Network
Wireless Network
AP1
SSID: huawei
BSSID:
00e0.fc45.24a0
BSS
AP2
SSID: huawei
BSSID:
00e0.fc45.3100
BSS
ESS
Notes: ESS:
  A large-scale virtual BSS consisting of multiple BSSs with the same SSID.
  A STA can move and roam within an ESS and considers that it is within the same WLAN regardless of its location.
WLAN roaming:
  WLAN roaming allows STAs to move within the coverage areas of APs belonging to the same ESS with nonstop service transmission.
  The most obvious advantage of the WLAN is that a STA can move within a WLAN without physical media restrictions. WLAN roaming allows the STA to move within a WLAN without service interruption. Multiple APs are located within an ESS. When a STA moves from an AP to another, WLAN roaming ensures seamless transition of STA services between APs.

## Slide 26
WLAN Overview
Basic Concepts of WLAN
WLAN Fundamentals
WLAN Configuration Implementation
Next-Generation WLAN Solutions

## Slide 27: WLAN Working Process Overview
WLAN Working Process
An AP obtains an IP address, discovers an AC, and sets up a connection with the AC.
AP onboarding
1
The AC delivers WLAN service configurations to the AP.
WLAN service configuration delivery
2
STAs find the SSID transmitted by the AP, connect to the network, and go online.
STA access
3
The WLAN starts to forward service data.
WLAN service data forwarding
4
AC
DHCP Server
Campus Network
AP
AP
AP Onboarding
Configuration Delivery
STA Access
Data Forwarding
Notes: In the AC + Fit AP networking architecture, the AC manages APs in a unified manner. Therefore, all configurations are performed on the AC.

## Slide 28: WLAN Working Process: Step 1
WLAN Working Process
The AC can manage and control Fit APs in a centralized manner and deliver services only after they go online. The procedure is as follows:
An AP obtains an IP address.
The AP discovers the AC and establishes a CAPWAP tunnel with it.
AP access control
AP upgrade
CAPWAP tunnel maintenance
AP onboarding
1
WLAN service configuration delivery
2
STA access
3
WLAN service data forwarding
4
AP Onboarding
Configuration Delivery
STA Access
Data Forwarding
AC
DHCP Server
Campus Network
AP
AP

## Slide 29: APs Obtain IP Addresses
An AP can communicate with an AC only after obtaining an IP address.
IP Address Allocation
An AP can obtain an IP address in either of the following modes:
  Static mode: A user logs in to the AP and configures its IP address.
  DHCP mode: The AP serves as a DHCP client and requests an IP address from a DHCP server.
  Typical solutions:
  Deploy a dedicated DHCP server to assign IP addresses to APs.
  Configure the AC to assign IP addresses to APs.
  Use a device on the network, such as a core switch, to assign IP addresses to APs.
AP Onboarding
Configuration Delivery
STA Access
Data Forwarding
IP address allocation
CAPWAP
tunnel establishment
AP access control
AP upgrade
(Optional)
CAPWAP
tunnel maintenance

## Slide 30: DHCP IP Address Allocation
AC
DHCP Server
DHCP packet
DHCP packet
AP
DHCP Discover (broadcast)
Discover DHCP servers on the network
DHCP Server
DHCP Request (broadcast)
Notify the DHCP server of the IP address selected
DHCP Ack (unicast)
Acknowledge address allocation
DHCP Offer (unicast)
Select an available IP address from the address pool and respond to the AP
AP Onboarding
Configuration Delivery
STA Access
Data Forwarding
IP address allocation
CAPWAP
tunnel establishment
AP access control
AP upgrade
(Optional)
CAPWAP
tunnel maintenance

## Slide 31: CAPWAP Tunnel Establishment
The AC manages and controls APs in a centralized manner through CAPWAP tunnels.
Step 1: AC Discovery
An AP sends a Discovery Request packet to find an available AC.
APs can discover an AC in either of the following ways:
  Static: AC IP address list preconfigured on the APs
  Dynamic: DHCP, DNS, and broadcast
Step 2: CAPWAP Tunnel Establishment
APs associate with the AC and establish CAPWAP tunnels, including data tunnels and control tunnels.
  Data tunnel: transmits service data packets from APs to the AC for centralized forwarding.
  Control tunnel: transmits control packets between the AC and APs.
AP
AC
Discovery Request
Discovery Response
AP Onboarding
Configuration Delivery
STA Access
Data Forwarding
IP address allocation
CAPWAP
tunnel establishment
AP access control
AP upgrade
(Optional)
CAPWAP
tunnel maintenance
Notes: CAPWAP tunnels provide the following functions:
  Maintains the running status of the AC and APs.
  Allows the AC to manage APs and deliver configurations to APs.
  Transmits service data to the AC for centralized forwarding.
AC discovery phase:
  Static: An AC IP address list is preconfigured on the APs. When an AP goes online, the AP unicasts a Discovery Request packet to each AC whose IP address is specified in the preconfigured AC IP address list. After receiving the Discovery Request packet, the ACs send Discovery Response packets to the AP. The AP then selects an AC to establish a CAPWAP tunnel according to the received Discovery Request packets.
  Dynamic: DHCP, DNS, and broadcast. This course describes DHCP and broadcast modes.

## Slide 32: Step 1: APs Dynamically Discover the AC
DHCP Mode (Layer 3 Networking)
AP
AC
DHCP Discover
Broadcast Mode (Layer 2 Networking)
DHCP Server
DHCP Offer
(option 43)
DHCP Request
DHCP Ack
(option 43)
Discovery Request
Discovery Response
Layer 2 Campus Network
Layer 3 Campus Network
AC
AP
Broadcast query
AP Onboarding
Configuration Delivery
STA Access
Data Forwarding
IP address allocation
CAPWAP
tunnel establishment
AP access control
AP upgrade
(Optional)
CAPWAP
tunnel maintenance
Notes: DHCP mode:
  Obtain the AC IP address through a four-way DHCP handshake process.
    When no AC IP address list is preconfigured, the AP starts the dynamic AC auto-discovery process. The AP obtains an IP address through DHCP and the AC address list through the Option field in the DHCP packets. (The DHCP server is configured to carry Option 43 in the DHCP Offer packet, and Option 43 contains the AC IP address list.)
    First, the AP sends a DHCP Discover packet to the DHCP server in broadcast mode. When receiving the DHCP Discover packet, the DHCP server encapsulates the first free IP address and other TCP/IP configuration in a DHCP Offer packet containing the lease duration, and sends the packet to the AP.
    A DHCP Offer packet can be a unicast or broadcast packet. When the AP receives DHCP Offer packets from multiple DHCP servers, it selects only one DHCP Offer packet (usually the first DHCP Offer packet) and broadcasts a DHCP Request packet to all DHCP servers. Then, the AP sends a DHCP Request packet to the specified server from which will allocate an IP address.
    When the DHCP server receives the DHCP Request packet, it responds with a DHCP Ack packet, which contains the IP address for the AP, lease duration, gateway information, and DNS server IP address. By now, the lease contract takes effect and the DHCP four-way handshake is completed.

## Slide 33
Notes:   The AC discovery mechanism allows APs to associate with the AC.
    After obtaining the AC's IP address from the DHCP server, the AP finds available ACs through the AC discovery mechanism and decides to associate with the optimal AC and establish CAPWAP tunnels.
    The AP starts the CAPWAP protocol discovery mechanism and sends unicast or broadcast request packets to attempt to associate with an AC. The ACs respond to the Discovery Request packets with unicast discovery response packets, containing the AC priority and the number of APs. The AP determines to associate with the appropriate AC based on the AC priority and the number of APs.
Broadcast mode:
  After an AP is started, if DHCP-based and DNS-based AC discovery procedures fail, the AP initiates a broadcast AC discovery procedure and broadcasts an AC discovery request.
  The AC receiving discovery request packets checks whether the AP is authorized to access (or whether the AP has authorized MAC addresses or sequence numbers). If so, the AC returns a discovery response to the AP. If not, the AC rejects its discovery request.
  Broadcast AC discovery is applicable to a Layer 2 network between the AP and the AC.

## Slide 34: Step 2: CAPWAP Tunnel Establishment
Step 2: CAPWAP Tunnel Establishment
APs associate with the AC and establish CAPWAP tunnels, including data tunnels and control tunnels.
  Data tunnel: transmits service data packets from APs to the AC for centralized forwarding. Datagram Transport Layer Security (DTLS) encryption can be enabled over the data tunnel to ensure security of CAPWAP data packets. Subsequently, CAPWAP data packets will be encrypted and decrypted using DTLS.
  Control tunnel: transmits control packets between the AC and APs. DTLS encryption can be enabled over the control tunnel to ensure security of CAPWAP control packets. Subsequently, CAPWAP control packets will be encrypted and decrypted using DTLS.
AP Onboarding
Configuration Delivery
STA Access
Data Forwarding
AC
DHCP Server
CAPWAP tunnel
CAPWAP
CAPWAP
IP address allocation
CAPWAP
tunnel establishment
AP access control
AP upgrade
(Optional)
CAPWAP
tunnel maintenance

## Slide 35: AP Access Control
AP Access Control
After discovering and AC, the AP sends a Join Request packet to the AC. The AC then determines whether to allow the AP access and sends a Join Response packet to the AP.
The AC supports three AP authentication modes: MAC address authentication, SN authentication, and non-authentication.
AP
AC
Discovery Request
Discovery Response
Join Request
Join Response
AP Onboarding
Configuration Delivery
STA Access
Data Forwarding
IP address allocation
CAPWAP
tunnel establishment
AP access control
AP upgrade
(Optional)
CAPWAP
tunnel maintenance
Notes: After receiving the Join Request packet from an AP, an AC authenticates the AP. If authentication is successful, the AC adds the AP.
The AC supports the following AP authentication modes:
  MAC address authentication
  SN authentication
  Non-authentication
APs can be added to an AC in the following ways:
  Manual configuration: Specify the MAC addresses and SNs of APs in offline mode on the AC in advance. When APs are connected the AC, the AC finds that their MAC addresses and SNs match the preconfigured ones and establish connections with them.
  Automatic discovery: If the AP authentication mode is set to non-authentication, or the AP authentication mode is set to MAC or SN authentication and the AP is whitelisted, the AC automatically discovers connected APs and establish connections with them.
  Manual confirmation: If the AP authentication mode is set to MAC or SN authentication and the AP is not imported offline or whitelisted, the AC adds the AP to the list of unauthorized APs. You can manually confirm the identity of such an AP to bring it online.

## Slide 36: AP Upgrade
AP Upgrade
The AP determines whether its system software version is the same as that specified on the AC according to parameters in the received Join Response packet. If they are different, the AP sends an Image Data Request packet to request the software package and then upgrades its software version in AC, FTP, or SFTP mode.
After the software version is updated, the AP restarts and repeats steps 1 to 3.
AP
AC
Discovery Request
Discovery Response
Join Request
Join Response
Image Data Response
Image Data Request
AP Onboarding
Configuration Delivery
STA Access
Data Forwarding
IP address allocation
CAPWAP
tunnel establishment
AP access control
AP upgrade
(Optional)
CAPWAP
tunnel maintenance
Notes: APs can be upgraded on an AC in the following modes:
  Automatic upgrade: mainly used when APs have not gone online on an AC. In this mode, we need to configure the automatic upgrade parameters for APs to go online before configuring AP access. Then the APs are automatically upgraded when they go online. An online AP will be automatically upgraded after the automatic upgrade parameters are configured and the AP is restarted in any mode. Compared with the automatic upgrade mode, the in-service upgrade mode reduces the service interruption time.
    AC mode: applies when a small number of APs are deployed. APs download the upgrade file from the AC during the upgrade.
    FTP mode: applies to file transfer without high network security requirements. APs download the upgrade file from an FTP server during the upgrade. In this mode, data is transmitted in clear text, which brings security risks.
    SFTP mode: applies to scenarios that require high network security and provides strict encryption and integrity protection for data transmission. APs download the upgrade file from an SFTP server during an upgrade.
  In-service upgrade: mainly used when APs are already online on the AC and carry WLAN services.
  Scheduled upgrade: mainly used when APs are already online on the AC and carry WLAN services. The scheduled upgrade is usually performed during off-peak hours.

## Slide 37: CAPWAP Tunnel Maintenance
CAPWAP Tunnel Maintenance
Data tunnel maintenance:
  The AP and AC exchange Keepalive packets to detect the data tunnel connectivity.
Control tunnel maintenance:
  The AP and AC exchange Echo packets to detect the control tunnel connectivity.
AP
AC
Discovery Request
Discovery Response
Join Request
Join Response
Image Data Response
Image Data Request
Keepalive
Keepalive
Echo Response
Echo Request
Data tunnel
Control tunnel
AP Onboarding
Configuration Delivery
STA Access
Data Forwarding
IP address allocation
CAPWAP
tunnel establishment
AP access control
AP upgrade
(Optional)
CAPWAP
tunnel maintenance
Notes: Data tunnel maintenance:
  The AP and AC exchange Keepalive packets (through the UDP port 5247) to detect the data tunnel connectivity.
Control tunnel maintenance:
  The AP and AC exchange Echo packets (through the UDP port 5246) to detect the control tunnel connectivity.

## Slide 38: Preconfigurations on the AC for APs to Go Online
Configure network connectivity
Create an AP group
Configure the country code on the AC
(regulatory domain profile)
Configure a source interface or address
(for establishing CAPWAP tunnels with APs)
(Optional) Configure the automatic AP upgrade
Add APs
(configure the AP authentication mode)
Configure DHCP servers to assign IP addresses to APs and STAs. The AC can function as a DHCP server.
Configure network connectivity between APs and the DHCP server, and between APs and the AC.
Each AP will be added and can be added to only one AP group. In most cases, we configure an AP group to provide the same configurations for multiple APs.
A country code identifies the country in which the APs are deployed. Country codes regulate different AP radio attributes, including the transmit power and supported channels.
Specify a unique source IP address or source interface on each AC. APs must learn the specified source IP address or the IP address of the source interface to communicate with the AC and establish CAPWAP tunnels.
In automatic upgrade mode, an AP checks whether its version is the same as that configured on the AC, SFTP server, or FTP server when going online. If the two versions are different, the AP upgrades its version, restarts, and goes online again. If the two versions are the same, the AP does not upgrade its version.
You can add APs by importing them in offline mode, automatic discovery, and manual confirmation.
AP Onboarding
Configuration Delivery
STA Access
Data Forwarding
Notes: Regulatory domain profile:
  A regulatory domain profile provides configurations of the country code, calibration channel, and calibration bandwidth for an AP.
  A country code identifies the country in which the APs are deployed. Country codes regulate different AP radio attributes, including the transmit power and supported channels. Correct country code configuration ensures that radio attributes of APs comply with local laws and regulations.
Configure a source interface or address on the AC.
  Specify a unique IP address, VLANIF interface, or Loopback interface on an AC. In this manner, APs connected to the AC can learn the specified IP address or the IP address of the specified interface to establish CAPWAP tunnels with the AC. This specified IP address or interface is called the source address or interface.
  Only after the unique source interface or address is specified on an AC, can APs establish CAPWAP tunnels with the AC.
  A VLANIF or Loopback interface can be used as the source interface, and their IP addresses can be configured as the source address.
Add APs: Configure the AP authentication mode and enable APs to go online.
  You can add APs by importing them in offline mode, automatic discovery, and manual confirmation.

## Slide 39: WLAN Working Process: Step 2
AP Onboarding
Configuration Delivery
STA Access
Data Forwarding
The AC sends a Configuration Update Request to an AP. If the AC receives a Configuration Update Response from the AP, the AC then delivers service configuration to the AP.
WLAN Working Process
AP onboarding
1
WLAN service configuration delivery
2
STA access
3
WLAN service data forwarding
4
Configuration Update Request
Configuration Update Response
1
2
AC
DHCP Server
Campus Network
AP
AP
Notes: After an AP goes online, it sends a Configuration Status Request containing its running configuration to the AC. The AC then compares the AP's running configuration with the local AP configuration. If they are inconsistent, the AC sends a Configuration Status Response message to the AP.
Note: After an AP goes online, it obtains the existing configuration from the AC. The AC then manages the AP and delivers service configurations to the AP.

## Slide 40: WLAN Profiles
Various profiles are designed based on different functions and features of WLAN networks to help users configure and maintain functions of WLAN networks. These profiles are called WLAN profiles.
AP or
AP group
regulatory domain profile
Radio profile
Radio profiles are used to optimize radio parameters, and control the in-service channel switching function.
VAP profile
Configure parameters in the VAP profile and reference the SSID profile, security profile, and authentication profile.
Other profiles
AP System Profile, Location Profile, WIDS Profile, Mesh Profile and etc.
A regulatory domain profile provides configurations of country code, calibration channel, and calibration bandwidth for an AP.
Bound to
Bound to
Bound to
Configure radio parameters
Configure the bandwidth, channel, antenna gain, transmit power, coverage distance, and operating frequency band of a specified radio.
Bound to
AP Onboarding
Configuration Delivery
STA Access
Data Forwarding
Notes: To simplify the configuration of a large number of APs, you can add them to an AP group and perform centralized configuration.However, APs may have different configurations. These configurations cannot be uniformly performed but can be directly performed on each AP.Each AP must and can only join one AP group when going online. If an AP obtains both AP group and specific configurations from an AC, the AP specific configurations are preferentially used.
Various profiles can be bound to the AP group and AP: regulatory domain profile, radio profile, VAP profile, Location profile, AP system profile, WIDS profile, AP wired port profile, WDS profile, and Mesh profile. Some of the listed profiles can further reference other profiles.
  Regulatory domain profile
    A country code identifies the country to which AP radios belong. Different countries support different AP radio attributes, including the transmit power and supported channels. Correct country code configuration ensures that radio attributes of APs comply with laws and regulations of countries and regions to which the APs are delivered.
    A calibration channel set limits the dynamic AP channel adjustment range when the radio calibration function is configured. Radar channels and the channels that are not supported by STAs are avoided.

## Slide 41
Notes:   Radio profile
    You can adjust and optimize radio parameters to adapt to different network environments, enabling APs to provide required radio capabilities and improving signal quality of WLANs. After parameters in a radio profile are delivered to an AP, only the parameters supported by the AP can take effect.
    Parameters that can be configured include the radio type, radio rate, multicast rate of radio packets, and interval at which an AP sends Beacon frames.
  VAP profile
    After parameters in a VAP profile are configured, and the VAP profile is bound to an AP group or AP, virtual access points (VAPs) are created on APs. VAPs provide wireless access services for STAs. You can configure parameters in the VAP profile to enable APs to provide different wireless services.
    A VAP profile can also reference an SSID profile, a security profile, a traffic profile and etc.
  Configure radio parameters:
    Configure different radio parameters for AP radios based on actual WLAN environments, so that the AP radios can work at the optimal performance.
    If working channels of adjacent APs have overlapping frequencies, signal interference occurs and affects AP working status. To prevent signal interference and enable APs to work at the optimal performance with higher WLAN quality, configure any two adjacent APs to work on non-overlapping channels.
    Configure the transmit power and antenna gain for radios according to actual network environments so that the radios provide sufficient signal strength, improving signal quality of WLANs.
    In actual application scenarios, two APs may be connected over dozens of meters to dozens of kilometers. Due to different AP distances, the time to wait for ACK packets from the peer AP varies. A proper timeout value can improve data transmission efficiency between APs.

## Slide 42: VAP Profile
VAP Profile
Create an
SSID profile
Create a
security profile
You can configure WLAN security policies to authenticate STAs and encrypt user packets, protecting the security of the WLAN and users.
Configure the data forwarding mode
Control packets (management packets) and data packets are transmitted on a WLAN.
Configure service VLANs
Layer 2 data packets delivered from the VAP to an AP carry the service VLAN IDs.
An SSID specifies a wireless network. When you search for available wireless networks on a STA, the displayed wireless network names are SSIDs.
An SSID profile is used to configure the SSID name of a WLAN.
Bound to
Bound to
AP Onboarding
Configuration Delivery
STA Access
Data Forwarding
Notes: An SSID profile is used to configure the SSID name and other access parameters of a WLAN. The following parameters are set in an SSID profile:
  SSID hiding: This functions enables an AP to hide the SSID of a WLAN. Only the users who know the SSID can connect to the WLAN, improving security.
  Maximum number of STAs on a VAP: More access users on a VAP indicate fewer network resources that are available to each user. To ensure Internet experience of users, you can configure a proper maximum number of access users on a VAP according to actual network situations.
  SSID hiding when the number of STAs reaches the maximum: When this function is enabled and the number of access users on a WLAN reaches the maximum, the SSID of the WLAN is hidden and new users cannot find the SSID.
Security profile: You can configure WLAN security policies to authenticate STAs and encrypt user packets, protecting the security of the WLAN and users.
  The supported WLAN security policies include open system authentication, WEP, WPA/WPA2-PSK, and WPA/WPA2-802.1X. You can configure one of them in a security profile.
Data forwarding mode:
  Control packets are forwarded through CAPWAP control tunnels. Data packets are forwarded in tunnel forwarding (centralized forwarding) or direct forwarding (local forwarding) mode. The data forwarding modes will be detailed later in the course.

## Slide 43
Notes: Service VLAN:
  Since WLANs provide flexible access modes, STAs may connect to the same WLAN at the office entrance or stadium entrance, and then roam to different APs.
    If a single VLAN is configured as the service VLAN, IP address resources may become insufficient in areas where many STAs access the WLAN, and IP addresses in the other areas are wasted.
    After a VLAN pool is created, add multiple VLANs to the VLAN pool and configure the VLANs as service VLANs. In this way, an SSID can use multiple service VLANs to provide wireless access services. Newly connected STAs are dynamically assigned to VLANs in the VLAN pool, which reduces the number of STAs in each VLAN and also the size of the broadcast domain. Additionally, IP addresses are evenly allocated, preventing IP address waste.

## Slide 44: WLAN Working Process: Step 3
AP Onboarding
Configuration Delivery
STA Access
Data Forwarding
STAs can access a WLAN after CAPWAP tunnels are established.
The STA access process consists of six phases: scanning, link authentication, association, access authentication, DHCP, and user authentication.
WLAN Working Process
AP onboarding
1
WLAN service configuration delivery
2
STA access
3
WLAN service data forwarding
4
AC
DHCP Server
Campus Network
AP
AP

## Slide 45: Scanning
In active scanning, a STA periodically searches for nearby wireless networks.
The STA can send two types of Probe Request frames: probes containing an SSID and probes that do not contain an SSID.
Scanning
Link authentication
Access authentication
DHCP
User authentication
Association
AP Onboarding
Configuration Delivery
STA Access
Data Forwarding
Active Scanning by Sending a Probe Request Frame Containing an SSID
AP1
(SSID: huawei)
STA
Probe Response
Probe Request
(SSID: huawei)
Active Scanning by Sending a Probe Request Frame Containing No SSID
The STA periodically broadcasts a Probe Request frame that does not contain an SSID on the supported channels. The APs return Probe Response frames to notify the STA of the wireless services they can provide.
AP1
STA
Probe Response
Probe Request
(SSID: Null)
Probe Request
(SSID: Null)
APn
.
.
.
The STA sends a Probe Request containing an SSID on each channel to search for the AP with the same SSID. Only the AP with the same SSID will respond to the STA.
Notes: Active scanning:
  Probes containing an SSID: applies when a STA actively scans wireless networks to access a specified wireless network.
  Probes that do not contain an SSID: applies when a STA actively scans wireless networks to determine whether wireless services are available.
Passive scanning:
  STAs can passively scan wireless networks.
  In passive scanning mode, a STA listens to Beacon frames (containing the SSID and supported rate) periodically sent by an AP to discover surrounding wireless networks. By default, an AP sends Beacon frames at an interval of 100 TUs (1 TU = 1024 us).

## Slide 46: WLAN Security Protocols
As WLAN technologies use radio signals to transmit service data, service data can be easily intercepted or tampered with by attackers when being transmitted on open wireless channels. Ensuring WLAN security is crucial to building safe and effective wireless networks.
Common security policy:
AP Onboarding
Configuration Delivery
STA Access
Data Forwarding
Security Policy | Link Authentication | Access Authentication | Data Encryption | Description
WEP | Open system | N/A | No encryption or WEP | Insecure policy
 | Shared-key Authentication | N/A | WEP | Insecure policy
WPA/WPA2-802.1X | Open system | 802.1X (EAP) | TKIP or CCMP | A more secure policy, applicable to large enterprises
WPA/WPA2-PSK | Open system | PSK | TKIP or CCMP | More secure policy, applicable to small- and medium-sized enterprises or household users
Scanning
Link authentication
Access authentication
DHCP
User authentication
Association
Notes: Three WLAN security policies are available: Wired Equivalent Privacy (WEP), Wi-Fi Protected Access (WPA), and WPA2. Each security policy has a series of security mechanisms, including link authentication used to establish a wireless link, user authentication used when users attempt to connect to a wireless network, and data encryption used during data transmission.
WEP
  WEP, defined in IEEE 802.11, is used to protect data of authorized users from being intercepted during transmission on a WLAN. WEP uses the RC4 algorithm to encrypt data through a 64-bit, 128-bit, or 152-bit key. Each encryption key contains a 24-bit initialization vector (IV) generated by the system. Therefore, the length of the key configured on the WLAN server and client is 40 bits, 104 bits, or 128 bits. WEP uses a static encryption key. All STAs associating with the same SSID use the same key to connect to the WLAN.

## Slide 47
Notes: WPA/WPA2
  WEP shared key authentication uses the Rivest Cipher 4 (RC4) symmetric stream cipher to encrypt data. Therefore, the same static key must be preconfigured on the server and clients. Both the encryption mechanism and algorithm, however, are prone to security threats. To address this challenge, the Wi-Fi Alliance developed WPA to overcome WEP defects. In addition to the RC4 algorithm, WPA defines the Temporal Key Integrity Protocol (TKIP) encryption algorithm on the basis of WEP, uses the 802.1X identity authentication framework, and supports Extensible Authentication Protocol-Protected Extensible Authentication Protocol (EAP-PEAP) and EAP-Transport Layer Security (EAP-TLS) authentication. Later, 802.11i defined WPA2. WPA2 uses a more secure encryption algorithm, that is, Counter Mode with CBC-MAC Protocol (CCMP).
  Both WPA and WPA2 can use 802.1X access authentication and the TKIP or CCMP encryption algorithm, giving better compatibility. WPA and WPA2 provide almost the same security level, with the only difference being the protocol packet format.
  The WPA/WPA2 security policy involves four phases: link authentication, access authentication, key negotiation, and data encryption.

## Slide 48: Link Authentication
To ensure wireless link security, an AP needs to authenticate STAs that attempt to access the AP.
IEEE 802.11 defines two authentication modes: open system authentication and shared key authentication.
Open System Authentication
AP
STA
Authentication Response
Authentication Request
Open system authentication requires no authentication, allowing any STA to be successfully authenticated.
Shared Key Authentication
Shared key authentication requires that the STA and AP have the same shared key preconfigured. The AP checks whether a STA has the same shared key to determine the authentication result. If the STA has the same shared key as the AP, the STA is authenticated. Otherwise, STA authentication fails.
AP
STA
Authentication Response
(Challenge)
Authentication Request
Authentication Response
(Encrypted Challenge)
Authentication Response
(Success)
Scanning
Link authentication
Access authentication
DHCP
User authentication
Association
AP Onboarding
Configuration Delivery
STA Access
Data Forwarding
Notes: A WLAN needs to ensure validity and security of STA access. To achieve this, STAs need to be authenticated before accessing the WLAN. This process is known as link authentication, which is usually considered the beginning of STA access.
Shared key authentication:
  The same shared key is configured for STAs and APs in advance. The AP checks whether the STA has the same shared key during link authentication. If so, the STA is successfully authenticated. Otherwise, STA authentication fails.
  Authentication process:
    The STA sends an Authentication Request packet to the AP.
    The AP generates a challenge and sends it to the STA.
    The STA uses the preconfigured key to encrypt the challenge and sends the encrypted challenge to the AP.
    The AP uses the preconfigured key to decrypt the encrypted challenge and compares the decrypted challenge with the challenge sent to the STA. If the two challenges are the same, the STA is successfully authenticated. Otherwise, STA authentication fails.

## Slide 49: Association
After link authentication is complete, a STA initiates link service negotiation using Association packets.
The STA association process is actually a link service negotiation process, during which the supported rate, channel, and the like are negotiated.
Association Response
Association Request
Association Request
Association Response
STA
AP
AC
Scanning
Link authentication
Access authentication
DHCP
User authentication
Association
AP Onboarding
Configuration Delivery
STA Access
Data Forwarding
Notes: STA association in the Fit AP architecture consists of the following steps:
  The STA sends an Association Request packet to the AP. The Association Request packet carries the STA's parameters and the parameters selected by the STA according to the service configuration, including the transmission rate, channel, and QoS capabilities.
  After receiving the Association Request packet, the AP encapsulates the packet into a CAPWAP packet and sends the CAPWAP packet to the AC.
  The AC determines whether to permit the STA access according to the received Association Request packet and replies with a CAPWAP packet containing an Association Response.
  The AP decapsulates the CAPWAP packet to obtain the Association Response, and sends the Association Response to the STA.

## Slide 50: Access Authentication
User access authentication differentiates users and controls access rights of users. Compared with link authentication, access authentication is more secure.
Major access authentication modes include PSK authentication and 802.1X authentication.
Scanning
Link authentication
Access authentication
DHCP
User authentication
Association
STA
AP
Access authentication is performed on the wireless-side interface, allowing STAs to send data over wireless links.
AP Onboarding
Configuration Delivery
STA Access
Data Forwarding
Notes: Data encryption:
  In addition to user access authentication, data packets need to be encrypted to ensure data security, which is also implemented in the access authentication phase. After a data packet is encrypted, only the device that holds the key can decrypt the packet. Other devices cannot decrypt the packet even if they receive the packet because they do not have the corresponding key.

## Slide 51: STA Address Allocation
The prerequisite for APs and STAs to go online properly is that they have obtained IP addresses.
If STAs obtain IP addresses through DHCP, the AC or aggregation switch can function as a DHCP server to assign IP addresses to the STAs. In most cases, the aggregation switch is used as the DHCP server.
AP Onboarding
Configuration Delivery
STA Access
Data Forwarding
Scanning
Link authentication
Access authentication
DHCP
User authentication
Association
AP
DHCP Discover
DHCP Server
(Aggregation Switch)
DHCP Offer
DHCP Request
DHCP Ack
IP Network
STA

## Slide 52: User Authentication
User authentication is an end-to-end security architecture, supporting 802.1X, MAC address, and Portal authentication modes.
AP Onboarding
Configuration Delivery
STA Access
Data Forwarding
Scanning
Link authentication
Access authentication
DHCP
User authentication
Association
Portal Authentication
  Portal authentication is also known as web authentication. Portal authentication websites are referred to as web portals.
  To access the Internet, users must be authenticated on web portals. The users can access network resources only after successful authentication.
Huawei-Guest
Just for Guest
+86
Phone Number
Password
Get Password
Login
Notes: With the application and development of enterprise networks, threats increasingly bring risks, such as viruses, Trojan horses, spyware, and malicious network attacks. On a traditional enterprise network, the intranet is considered secure and threats come from the extranet. However, research shows that 80% of cyber security vulnerabilities come from inside the network. The network security threats and viruses affect the network seriously, leading to system or network crashes. In addition, when intranet users browse websites on the external network, the spyware and Trojan horse software may be automatically installed on users' computers, which cannot be sensed by the users. The malicious software may spread on the intranet.
Therefore, as security challenges keep escalating, traditional security measures are far from enough. The security model needs to be changed from the passive mode to active mode. Thoroughly solving network security problems from the root (terminal) can improve the information security level of the entire enterprise.

## Slide 53: WLAN Working Process: Step 4
AP Onboarding
Configuration Delivery
STA Access
Data Forwarding
Control packets (management packets) and data packets are transmitted over CAPWAP tunnels.
Control packets are forwarded through the CAPWAP control tunnel.
User data packets can be forwarded in tunnel forwarding (centralized forwarding) or direct forwarding (local forwarding) mode.
WLAN Working Process
AP onboarding
1
WLAN service configuration delivery
2
STA access
3
WLAN service data forwarding
4
AC
DHCP Server
Campus Network
AP
AP

## Slide 54: Data Forwarding Mode
AP Onboarding
Configuration Delivery
STA Access
Data Forwarding
Tunnel Forwarding
In tunnel forwarding mode, APs encapsulate user data packets over a CAPWAP data tunnel and send them to an AC. The AC then forwards these packets to an upper-layer network.
Direct Forwarding
In direct forwarding mode, an AP directly forwards user data packets to an upper-layer network without encapsulating them over a CAPWAP data tunnel.
AC
AP
AP
AC
AP
AP
Service data traffic
Management traffic
CAPWAP tunnel
Service data traffic
Management traffic
CAPWAP tunnel
Notes: Tunnel forwarding mode:
  Advantages: An AC forwards all data packets, ensuring security and facilitating centralized management and control.
  Disadvantages: Service data must be forwarded by an AC, which is inefficient and increases the load on the AC.
Direct forwarding mode:
  Advantages: Service data packets do not need to be forwarded by an AC, improving packet forwarding efficiency and reducing the burden on the AC.
  Disadvantages: Service data is difficult to manage and control in a centralized manner.

## Slide 55
WLAN Overview
Basic Concepts of WLAN
WLAN Fundamentals
WLAN Configuration Implementation
Next-Generation WLAN Solutions

## Slide 56: Basic WLAN Configuration Commands: Configuring an AP to Go Online (1)
[AC-ip-pool-pool1] option code [ sub-option sub-code ] { ascii ascii-string | hex hex-string | cipher cipher-string | ip-address ip-address
Configure the AC as a DHCP server and configure the Option 43 field.
Configure the user-defined option that a DHCP server assigns to a DHCP client.
[AC] wlan
[AC-wlan-view]
Create a regulatory domain profile and configure the country code.
Enter the WLAN view.
[AC-wlan-view] regulatory-domain-profile name profile-name
[AC-wlan-regulate-domain-profile-name]
Create a regulatory domain profile and enter the regulatory domain profile view, or enter the view of an existing regulatory domain profile.
[AC-wlan-regulate-domain-profile-name] country-code country-code
Configure the country code.
AP Onboarding
WLAN Services
Notes: Command: option code [ sub-option sub-code ] { ascii ascii-string | hex hex-string | cipher cipher-string | ip-address ip-address }
  code: specifies the code of a user-defined option. The value is an integer that ranges from 1 to 254, except values 1, 3, 6, 15, 44, 46, 50, 51, 52, 53, 54, 55, 57, 58, 59, 61, 82, 121 and 184.
  sub-option sub-code: specifies the code of a user-defined sub-option. The value is an integer ranging from 1 to 254. For details about well-known options, see RFC 2132.
  ascii | hex | cipher: specifies the user-defined option code as an ASCII character string, hexadecimal character string, or ciphertext character string.
  ip-address ip-address: specifies the user-defined option code as an IP address.
Command: regulatory-domain-profile name profile-name
  name profile-name: specifies the name of a regulatory domain profile. The value is a string of 1 to 35 case-insensitive characters. It cannot contain question marks (?) or spaces, and cannot start or end with double quotation marks (").

## Slide 57
Notes: Command: country-code country-code
  country-code: specifies a country code. The value is a string of characters in enumerated type.
  The AC supports multiple country codes, such as:
    CN (default value): China
    AU: Australia
    CA: Canada
    DE: Germany
    FR: France
    US: United States
    ...

## Slide 58: Basic WLAN Configuration Commands: Configuring an AP to Go Online (2)
[AC-wlan-view] ap-group name group-name
[AC-wlan-ap-group-group-name]
Configure a source interface or address.
Create an AP group and enter the AP group view, or enter the view of an existing AP group.
[AC-wlan-ap-group-group-name] regulatory-domain-profile profile-name
Bind the regulatory domain profile to an AP or AP group.
[AC] capwap source interface { loopback loopback-number | vlanif vlan-id }
Specify a source interface on the AC for establishing CAPWAP tunnels with APs.
[AC] capwap source ip-address ip-address
Configure the source IP address on the AC.
AP Onboarding
WLAN Services
Notes: Command: ap-group name group-name
  name group-name: specifies the name of an AP group. The value is a string of 1 to 35 characters. It cannot contain question marks (?), slashes (/), or spaces, and cannot start or end with double quotation marks (").

## Slide 59: Basic WLAN Configuration Commands: Configuring an AP to Go Online (3)
[AC-wlan-view] ap auth-mode { mac-auth | sn-auth }
Add APs in offline mode.
Set the AP authentication mode to MAC address or SN authentication. By default, MAC address authentication is used.
[AC-wlan-view] ap-id ap-id [ [ type-id type-id | ap-type ap-type ] { ap-mac ap-mac | ap-sn ap-sn | ap-mac ap-mac ap-sn ap-sn } ]
[AC-wlan-ap-ap-id] ap-name ap-name
Manually add an AP in offline mode or enter the AP view, and configure the name of a single AP.
[AC-wlan-view] ap-id 0
[AC-wlan-ap-0] ap-group ap-group
Add the AP to an AP group.
[AC] display ap { all | ap-group ap-group }}
Verify the configuration.
Check AP information.
AP Onboarding
WLAN Services
Notes: Command: ap-id ap-id [ [ type-id type-id | ap-type ap-type ] { ap-mac ap-mac | ap-sn ap-sn | ap-mac ap-mac ap-sn ap-sn } ]
  ap-id: specifies the ID of an AP. The value is an integer that ranges from 0 to 8191.
  type-id: specifies the ID of an AP type. The value is an integer that ranges from 0 to 255.
  ap-type: specifies the type of an AP. The value is a string of 1 to 31 characters.
  ap-mac: specifies the MAC address of an AP. The value is in H-H-H format. An H is a 4-digit hexadecimal number.
  ap-sn: specifies the SN of an AP. The value is a string of 1 to 31 characters, and can contain only letters and digits.

## Slide 60: Basic WLAN Configuration Commands: Configuring Radios (1)
[AC-wlan-view] ap-id 0
[AC-wlan-ap-0] radio radio-id
[AC-wlan-radio-0]
Enter the radio view.
[AC-wlan-radio-0/0] channel { 20mhz | 40mhz-minus | 40mhz-plus | 80mhz | 160mhz } channel
Warning: This action may cause service interruption. Continue?[Y/N]y
Configure the working bandwidth and channel for a radio.
Configure the working bandwidth and channel for all APs in an AP group or for a specified radio of a single AP.
AP Onboarding
WLAN Services
[AC-wlan-radio-0/0] channel 80+80mhz channel1 channel2
Warning: This action may cause service interruption. Continue?[Y/N]y
[AC-wlan-radio-0/0] antenna-gain antenna-gain
Configure the antenna gain.
Configure the antenna gain for all APs in an AP group or for a specified radio of a single AP.
Notes: Command: radio radio-id
  radio-id: specifies the ID of a radio. The radio ID must exist.
Commands:
  channel { 20mhz | 40mhz-minus | 40mhz-plus | 80mhz | 160mhz } channel
  channel 80+80mhz channel1 channel2
  20mhz: sets the working bandwidth of a radio to 20 MHz.
  40mhz-minus: sets the working bandwidth of a radio to 40 MHz Minus.
  40mhz-plus: sets the working bandwidth of a radio to 40 MHz Plus.
  80mhz: sets the working bandwidth of a radio to 80 MHz.
  160mhz: sets the working bandwidth of a radio to 160 MHz.
  80+80mhz: sets the working bandwidth of a radio to 80+80 MHz.
  channel/channel1/channel2: specifies the working channel for a radio. The channel is selected based on the country code and radio mode. The parameter is an enumeration value. The value range is determined according to the country code and radio mode.
Command: antenna-gain antenna-gain
  antenna-gain: specifies the antenna gain. The value is an integer that ranges from 0 to 30, in dB.

## Slide 61: Basic WLAN Configuration Commands: Configuring Radios (2)
[AC-wlan-radio-0/0] eirp eirp
Configure the transmit power for a radio.
[AC-wlan-radio-0/0] coverage distance distance
Configure the radio coverage distance.
AP Onboarding
WLAN Services
Configure the transmit power for all APs in an AP group or for a specified radio of a single AP.
Configure the radio coverage distance for all APs in an AP group or for a specified radio of a single AP.
[AC-wlan-radio-0/0] frequency { 2.4g | 5g }
Configure the operating frequency for a radio.
Notes: Command: eirp eirp
  eirp: specifies the transmit power. The value is an integer that ranges from 1 to 127, in dBm.
Command: coverage distance distance
  distance: specifies the radio coverage distance. Each distance corresponds to a group of slottime, acktimeout, and ctstimeout values. You can configure the radio coverage distance based on the AP distance, so that APs adjust the values of slottime, acktimeout, and ctstimeout values accordingly. The value is an integer that ranges from 1 to 400, in 100 meters.
Command: frequency { 2.4g | 5g }
  By default, radio 0 works on the 2.4 GHz frequency band, and radio 2 works on the 5 GHz frequency band.

## Slide 62: Basic WLAN Configuration Commands: Configuring Radios (3)
[AC-wlan-view] radio-2g-profile name profile-name
Create a radio profile.
AP Onboarding
WLAN Services
Create a 2G radio profile and enter the 2G radio profile view, or enter the view of an existing 2G radio profile.
[AC-wlan-view] ap-group name group-name
[AC-wlan-ap-group-group-name] radio-2g-profile profile-name radio { radio-id | all }
Bind the radio profile.
Bind the specified 2G radio profile to the 2G radio in the AP group.
Notes: Command: radio-2g-profile name profile-name
  name profile-name: specifies the name of a 2G radio profile. The value is a string of 1 to 35 case-insensitive characters. It cannot contain question marks (?) or spaces, and cannot start or end with double quotation marks (").
  By default, the system provides the 2G radio profile default.
Command: radio-2g-profile profile-name radio { radio-id | all }
  profile-name: specifies the name of a 2G radio profile. The 2G radio profile must exist.
  radio radio-id: specifies the ID of a radio. The value is an integer that can be 0 or 2.
  radio all: specifies all radios.

## Slide 63: Basic WLAN Configuration Commands: Configuring VAPs (1)
[AC-wlan-view] vap-profile name profile-name
[AC-wlan-vap-prof-profile-name]
Create a VAP profile.
Create a VAP profile and enter the VAP profile view, or enter the view of an existing VAP profile.
[AC-wlan-vap-prof-profile-name] forward-mode { direct-forward | tunnel }
Configure the data forwarding mode.
Set the data forwarding mode in the VAP profile to direct or tunnel.
[AC-wlan-vap-prof-profile-name] service-vlan { vlan-id vlan-id | vlan-pool pool-name }
Configure service VLANs.
Configure service VLANs configured for the VAP.
AP Onboarding
WLAN Services

## Slide 64: Basic WLAN Configuration Commands: Configuring VAPs (2)
[AC-wlan-view] security-profile name profile-name
[AC-wlan-sec-prof-profile-name]
Configure a security profile.
Create a security profile and enter the security profile view.
By default, security profiles default, default-wds, and default-mesh are available in the system.
[AC-wlan-view] vap-profile name profile-name
[AC-wlan-vap-prof-profile-name] security-profile profile-name
Bind the security profile to the VAP profile.
AP Onboarding
WLAN Services

## Slide 65: Basic WLAN Configuration Commands: Configuring VAPs (3)
[AC-wlan-view] ssid-profile name profile-name
[AC-wlan-ssid-prof-profile-name]
Configure an SSID profile.
Create an SSID profile and enter the SSID profile view, or enter the view of an existing SSID profile.
By default, the system provides the SSID profile default.
[AC-wlan-ssid-prof-profile-name] ssid ssid
Configure an SSID for the SSID profile.
By default, the SSID HUAWEI-WLAN is configured in an SSID profile.
[AC-wlan-view] vap-profile name profile-name
[AC-wlan-vap-prof-profile-name] ssid-profile profile-name
Bind the SSID profile to the VAP profile.
AP Onboarding
WLAN Services
Notes: Command: ssid ssid
  ssid: specifies an SSID. The value is a string of 1 to 32 case-sensitive characters. It supports Chinese characters or Chinese + English characters, without tab characters.
  To start an SSID with a space, you need to encompass the SSID with double quotation marks ("), for example, " hello". The double quotation marks occupy two characters. To start an SSID with a double quotation mark, you need to add a backslash (\) before the double quotation mark, for example, \"hello. The backslash occupies one character.

## Slide 66: Basic WLAN Configuration Commands: Configuring VAPs (4)
[AC-wlan-view] ap-group name group-name
[AC-wlan-ap-group-group-name] vap-profile profile-name wlan wlan-id radio { radio-id | all } [ service-vlan { vlan-id vlan-id | vlan-pool pool-name } ]
Bind the VAP profile.
Bind the specified VAP profile to radios in an AP group.
[AC] display vap { ap-group ap-group-name | { ap-name ap-name | ap-id ap-id } [ radio radio-id ] } [ ssid ssid ]
Check VAP information.
Display information about service VAPs.
[AC] display vap { all | ssid ssid }
AP Onboarding
WLAN Services
Notes: Command: display vap { ap-group ap-group-name | { ap-name ap-name | ap-id ap-id } [ radio radio-id ] } [ ssid ssid ]
  ap-group-name: displays information about all service VAPs in a specified AP group. The AP group must exist.
  ap-name: displays information about service VAPs on the AP with a specified name. The AP name must exist.
  ap-id: displays information about service VAPs on the AP with a specified ID. The AP ID must exist.
  radio-id: Displays information about service VAPs of a specified radio. The value is an integer that ranges from 0 to 2.
  ssid: Displays information about service VAPs of a specified SSID. The SSID must exist.
Command: display vap { all | ssid ssid }
  all: displays information about all service VAPs.

## Slide 67: Example for Configuring Layer 2 Tunnel Forwarding in Off-Path Mode
Data | Configuration
Management VLAN for APs | VLAN 100
Service VLAN for STAs | VLAN 101
DHCP server | The AC functions as a DHCP server to assign IP addresses to APs. The aggregation switch S2 functions as a DHCP server to assign IP addresses to STAs. The default gateway address of STAs is 10.23.101.1.
IP address pool for APs | 10.23.100.2–10.23.100.254/24
IP address pool for STAs | 10.23.101.2–10.23.101.254/24
IP address of the AC's source interface | VLANIF 100: 10.23.100.1/24
AP group | Name: ap-group1 Referenced profiles: VAP profile wlan-net and regulatory domain profile
Regulatory domain profile | Name: default Country code: CN
SSID profile | Name: wlan-net SSID name: wlan-net
Security profile | Name: wlan-net Security policy: WPA-WPA2+PSK+AES Password: a1234567
VAP profile | Name: wlan-net Forwarding mode: tunnel forwarding Service VLAN: VLAN 101 Referenced profiles: SSID profile wlan-net and security profile wlan-net
IP Network
AP
STA
S1
S2
VLANIF 101
10.23.101.1/24
GE0/0/3
GE0/0/2
GE0/0/1
GE0/0/2
GE0/0/1
GE0/0/1
VLANIF 100
10.23.100.1/24
AC
Notes: Service requirements
  An enterprise wants to enable users to access the Internet through a WLAN, meeting the basic mobile office requirements.
Networking requirements
  AC networking mode: Layer 2 networking in off-path mode
  DHCP deployment mode:
    The AC functions as a DHCP server to assign IP addresses to APs.
    The aggregation switch S2 functions as a DHCP server to assign IP addresses to STAs.
  Service data forwarding mode: tunnel forwarding
Configuration roadmap
  Configure network connectivity between the AC, APs, and other network devices.
  Configure the APs to go online.
    Create an AP group and add APs that require the same configuration to the group for unified configuration.
    Configure AC system parameters, including the country code and source interface used by the AC to communicate with the APs.
    Configure the AP authentication mode and imports the APs in offline mode for them to go online.
  Configure WLAN service parameters for STAs to access the WLAN.

## Slide 68: Configuring Network Connectivity
Create VLANs and interfaces on S1, S2, and AC.
[AC] dhcp enable
[AC] interface vlanif 100
[AC-Vlanif100] ip address 10.23.100.1 24
[AC-Vlanif100] dhcp select interface
Configure DHCP servers to assign IP addresses to APs and STAs.
[S2] dhcp enable
[S2] interface vlanif 101
[S2-Vlanif101] ip address 10.23.101.1 24
[S2-Vlanif101] dhcp select interface
# Configure VLANIF 100 on the AC to assign IP address to APs.
# Configure VLANIF 101 on S2 to assign IP addresses to STAs and specify 10.23.101.1 as the default gateway address of the STAs.
Network Connectivity
AP Onboarding
WLAN Services
IP Network
AP
STA
S1
S2
VLANIF 101
10.23.101.1/24
GE0/0/3
GE0/0/2
GE0/0/1
GE0/0/2
GE0/0/1
GE0/0/1
VLANIF 100
10.23.100.1/24
AC
Notes: 1. Create VLANs and interfaces on S1, S2, and AC.
  S1 configuration:
    [S1] vlan batch 100
    [S1] interface gigabitethernet 0/0/1
    [S1-GigabitEthernet0/0/1] port link-type trunk
    [S1-GigabitEthernet0/0/1] port trunk pvid vlan 100
    [S1-GigabitEthernet0/0/1] port trunk allow-pass vlan 100
    [S1-GigabitEthernet0/0/1] quit
    [S1] interface gigabitethernet 0/0/2
    [S1-GigabitEthernet0/0/2] port link-type trunk
    [S1-GigabitEthernet0/0/2] port trunk allow-pass vlan 100
    [S1-GigabitEthernet0/0/2] quit

## Slide 69
Notes:   S2 configuration:
    [S2] vlan batch 100 101
    [S2] interface gigabitethernet 0/0/1
    [S2-GigabitEthernet0/0/1] port link-type trunk
    [S2-GigabitEthernet0/0/1] port trunk allow-pass vlan 100
    [S2-GigabitEthernet0/0/1] quit
    [S2] interface gigabitethernet 0/0/2
    [S2-GigabitEthernet0/0/2] port link-type trunk
    [S2-GigabitEthernet0/0/2] port trunk allow-pass vlan 100 101
    [S2-GigabitEthernet0/0/2] quit
    [S2] interface gigabitethernet 0/0/3
    [S2-GigabitEthernet0/0/3] port link-type trunk
    [S2-GigabitEthernet0/0/3] port trunk allow-pass vlan 101
    [S2-GigabitEthernet0/0/3] quit
  AC configuration:
    [AC] vlan batch 100 101
    [AC] interface gigabitethernet 0/0/1
    [AC-GigabitEthernet0/0/1] port link-type trunk
    [AC-GigabitEthernet0/0/1] port trunk allow-pass vlan 100 101
    [AC-GigabitEthernet0/0/1] quit

## Slide 70: Configuring APs to Go Online (1)
Create an AP group.
[AC] wlan
[AC-wlan-view] ap-group name ap-group1
[AC-wlan-ap-group-ap-group1] quit
Create a regulatory domain profile and configure the country code.
AC-wlan-view] regulatory-domain-profile name default
[AC-wlan-regulate-domain-default] country-code cn
[AC-wlan-regulate-domain-default] quit
[AC-wlan-view] ap-group name ap-group1
[AC-wlan-ap-group-ap-group1] regulatory-domain-profile default
Warning: Modifying the country code will clear channel, power and antenna gain configurations of the radio and reset the AP. Continu
e?[Y/N]:y
[AC-wlan-ap-group-ap-group1] quit
[AC-wlan-view] quit
Network Connectivity
AP Onboarding
WLAN Services
IP Network
AP
STA
S1
S2
VLANIF 101
10.23.101.1/24
GE0/0/3
GE0/0/2
GE0/0/1
GE0/0/2
GE0/0/1
GE0/0/1
VLANIF 100
10.23.100.1/24
AC

## Slide 71: Configuring APs to Go Online (2)
Configure the AC's source interface.
[AC] capwap source interface vlanif 100
Import an AP in offline mode on the AC.
[AC] wlan
[AC-wlan-view] ap auth-mode mac-auth
[AC-wlan-view] ap-id 0 ap-mac 60de-4476-e360
[AC-wlan-ap-0] ap-name area_1
Warning: This operation may cause AP reset. Continue? [Y/N]:y
[AC-wlan-ap-0] ap-group ap-group1
Warning: This operation may cause AP reset. If the country code changes, it will clear channel, power and antenna gain configurations of the radio, Whether to continue? [Y/N]:y
[AC-wlan-ap-0] quit
Network Connectivity
AP Onboarding
WLAN Services
IP Network
AP
STA
S1
S2
VLANIF 101
10.23.101.1/24
GE0/0/3
GE0/0/2
GE0/0/1
GE0/0/2
GE0/0/1
GE0/0/1
VLANIF 100
10.23.100.1/24
AC
Notes: Import an AP in offline mode on the AC.
  Add the AP to the AP group ap-group1. Assume that an AP's MAC address is 60de-4476-e360. Configure a name for the AP based on the AP's deployment location, so that you can know where the AP is deployed from its name. For example, name the AP area_1 if it is deployed in area 1.

## Slide 72: Verifying the AP Onboarding Configuration
After the AP is powered on, run the display ap all command to check the AP state. If the State field displays nor, the AP has gone online.
[AC-wlan-view] display ap all
Total AP information:
nor : normal [1]
Extra information:
P : insufficient power supply
-------------------------------------------------------------------------------------------------------------------------
ID MAC Name Group IP Type State STA Uptime ExtraInfo
-------------------------------------------------------------------------------------------------------------------------
0 60de-4476-e360 area_1 ap-group1 10.23.100.254 AP5030DN nor 0 10S -
-------------------------------------------------------------------------------------------------------------------------
Total: 1
Network Connectivity
AP Onboarding
WLAN Services
Notes: Description of the display ap command output:
  ID: AP ID.
  MAC: AP MAC address.
  Name: AP name.
  Group: Name of the AP group to which an AP belongs.
  IP: IP address of an AP. In NAT scenarios, APs are on the private network and the AC on the public network. This value is an AP's private IP address. To check the public IP address of an AP, run the display ap run-info command.
  Type: AP type.
  State: AP state.
    normal: An AP has gone online on an AC and is working properly.
    commit-failed: WLAN service configurations fail to be delivered to an AP after it goes online on an AC.
    download: An AP is in upgrade state.
    fault: An AP fails to go online.
    idle: It is the initialization state of an AP before it establishes a link with the AC for the first time.
  STA: Number of STAs connected to an AP.
  Uptime: Online duration of an AP.
  ExtraInfo: Extra information. The value P indicates an AP has no sufficient power supply.

## Slide 73: Configuring WLAN Service Parameters (1)
Create security profile wlan-net and configure a security policy.
[AC-wlan-view] security-profile name wlan-net
[AC-wlan-sec-prof-wlan-net] security wpa-wpa2 psk pass-phrase a1234567 aes
[AC-wlan-sec-prof-wlan-net] quit
Create SSID profile wlan-net and set the SSID name to wlan-net.
[AC-wlan-view] ssid-profile name wlan-net
[AC-wlan-ssid-prof-wlan-net] ssid wlan-net
[AC-wlan-ssid-prof-wlan-net] quit
Network Connectivity
AP Onboarding
WLAN Services
IP Network
AP
STA
S1
S2
VLANIF 101
10.23.101.1/24
GE0/0/3
GE0/0/2
GE0/0/1
GE0/0/2
GE0/0/1
GE0/0/1
VLANIF 100
10.23.100.1/24
AC

## Slide 74: Configuring WLAN Service Parameters (2)
Create VAP profile wlan-net, set the data forwarding mode and service VLAN, and bind the security profile and SSID profile to the VAP profile.
[AC-wlan-view] vap-profile name wlan-net
[AC-wlan-vap-prof-wlan-net] forward-mode tunnel
[AC-wlan-vap-prof-wlan-net] service-vlan vlan-id 101
[AC-wlan-vap-prof-wlan-net] security-profile wlan-net
[AC-wlan-vap-prof-wlan-net] ssid-profile wlan-net
[AC-wlan-vap-prof-wlan-net] quit
Bind the VAP profile to the AP group and apply configurations in VAP profile wlan-net to radio 0 and radio 1 of the APs in the AP group.
[AC-wlan-view] ap-group name ap-group1
[AC-wlan-ap-group-ap-group1] vap-profile wlan-net wlan 1 radio 0
[AC-wlan-ap-group-ap-group1] vap-profile wlan-net wlan 1 radio 1
[AC-wlan-ap-group-ap-group1] quit
Network Connectivity
AP Onboarding
WLAN Services
IP Network
AP
STA
S1
S2
VLANIF 101
10.23.101.1/24
GE0/0/3
GE0/0/2
GE0/0/1
GE0/0/2
GE0/0/1
GE0/0/1
VLANIF 100
10.23.100.1/24
AC

## Slide 75: Checking VAP Profile Information
The AC automatically delivers WLAN service configuration to the AP. After the service configuration is complete, run the display vap ssid wlan-net command. If Status in the command output is displayed as ON, the VAPs have been successfully created on AP radios.
[AC-wlan-view] display vap ssid wlan-net
WID : WLAN ID
-----------------------------------------------------------------------------------------------------------------
AP ID AP name RfID WID BSSID Status Auth type STA SSID
-----------------------------------------------------------------------------------------------------------------
0 area_1 0 1 60DE-4476-E360 ON WPA/WPA2-PSK 0 wlan-net
0 area_1 1 1 60DE-4476-E370 ON WPA/WPA2-PSK 0 wlan-net
-----------------------------------------------------------------------------------------------------------------
Total: 2
Network Connectivity
AP Onboarding
WLAN Services
Notes: Description of the display vap command output:
  AP ID: AP ID.
  AP name: AP name.
  RfID: Radio ID.
  WID: VAP ID.
  SSID: SSID name.
  BSSID: MAC address of a VAP.
  Status: Current status of a VAP.
    ON: The VAP service is enabled.
    OFF: The VAP service is disabled.
  Auth type: VAP authentication mode.
  STA: Number of STAs connected to a VAP.

## Slide 76
WLAN Overview
Basic Concepts of WLAN
WLAN Fundamentals
WLAN Configuration Implementation
Next-Generation WLAN Solutions

## Slide 77: Huawei WLAN Solutions Meet Future Wireless Network Construction Requirements
All-scenario
Use scenario-based customized solutions for complex and diversified application scenarios
Complete WLAN deployment and management solutions for campus networks and branch networks
High bandwidth
802.11ac Wave 2 protocol, dual-5G radio coverage, and up to 3.46 Gbps wireless access bandwidth
Huawei is a key contributor to the next-generation 802.11ax standard (Wi-Fi 6) with a single 5 GHz radio rate of up to 9.6 Gbps.
Roaming and multiple wireless QoS protocols such as Wi-Fi multimedia (WMM) to ensure QoS
High security
Mainstream authentication and encryption modes, such as WPA, WPA2, WPA3, and WAPI
Wireless intrusion detection
Portal and 802.1X authentication, protecting intranet security
Easy deployment
APs support plug-and-play, automatic upgrade, automatic channel selection, dynamic rate and power adjustment, and load balancing.
IoT APs and APs with built-in high-density antennas, simplifying installation and enabling fast deployment
APs support cloud management and can work in dual-stack mode to smoothly switch between the cloud and local management modes.

## Slide 78: Dual Drivers (Technology Advances + Application Development) Promote the Arrival of the Wi-Fi 6 Era
Technology
Application
2015
2016
2017
2018
2019
2020
2014
2021
802.11ax
802.11n
802.11ac Wave 1
802.11ac Wave 2
2011
Wi-Fi standards are upgraded every four to five years.
Wi-Fi 4
Wi-Fi 5
Wi-Fi 6
October 2018
New Wi-Fi naming convention released by the WFA
Social networking
Wireless office
Video surveillance
HD video
E-classroom
Video conferencing
4K video conferencing
3D diagnosis
Bandwidth per user > 50 Mbps
Latency < 10 ms
4K
Bandwidth per user: 2 to 4 Mbps
Latency < 50 ms
Bandwidth per user: 4 to 12 Mbps
Latency < 30 ms
Interactive VR/AR
Notes: Wi-Fi 5 cannot meet the low service latency and high bandwidth requirements of 4K/8K video conferencing scenarios.
Powered by Huawei SmartRadio intelligent application acceleration, Wi-Fi 6 achieves a latency of as low as 10 ms.

## Slide 79: Wi-Fi 6 Vs. Wi-Fi 5
High Bandwidth
Low Latency
High Concurrency Rate
Rate of up to 9.6 Gbps
Bandwidth increased by 4 times
Low Power Consumption
1024-QAM
8x8 MU-MIMO
User 1
User 2
User 3
User 4
Frequency
Time
UL/DL OFDMA
UL/DL MU-MIMO
Access of 1024 STAs per AP
Number of concurrent users increased by 4 times
OFDMA
Spatial Reuse
Service latency reduced to 20 ms
Average latency reduced by 30%
TWT
20 MHz-Only
Target wakeup time (TWT) mechanism
STA power consumption reduced by 30%
Notes: Currently, the theoretical rate of all Wi-Fi 5 products (Wave 2) is 2.5 Gbit/s, and that of Wi-Fi 6 products is 9.6 Gbit/s. Therefore, Wi-Fi 6 increases the rate by four folds compared with Wi-Fi 5.
Wi-Fi 6 increases the number of concurrent users by four folds compared with Wi-Fi 5. In the actual test, at a per user bandwidth of 2 Mbit/s, the concurrent number of users supported by Wi-Fi 5 is 100, and that supported by Wi-Fi 6 is 400.
The average latency supported by Wi-Fi 6 is about 20 ms (about 30 ms in Wi-Fi 5). Huawei SmartRadio intelligent application acceleration technology further reduces the service latency to as low as 10 ms.
TWT is not supported by Wi-Fi 5.

## Slide 80: Next-Generation Campus Network: Intent-Driven Campus (Small- and Medium-Sized)
Egress Gateway
Switch
Cloud AP
STA
Campus HQ
Branch Office
Cloud AP
STA
Campus Branch
Basic Concepts
The cloud management platform allows centralized management and maintenance of devices at any place, greatly reducing network deployment and O&M costs.
Applicable scope: small- and medium-sized enterprises
Plug-and-play and automatic deployment reduce network deployment costs.
All network elements (NEs) are monitored and managed on the cloud management platform in a unified manner.
Cloud solutions usually provide various tools on the cloud, reducing costs.
Advantages (Compared with the AC + Fit AP Architecture)
Internet
Notes: Disadvantages of traditional network solutions:
  Traditional network solutions have many network deployment problems, such as high deployment costs and O&M difficulties. These problems are obvious in enterprises with many branches or geographically dispersed branches.
Cloud management architecture:
  The cloud management architecture can solve the problems faced by traditional network solutions. The cloud management platform can manage and maintain devices in a centralized manner at any place, greatly reducing network deployment and O&M costs.
  After a cloud AP is deployed, the network administrator does not need to go to the site for cloud AP software commissioning. After power-on, the cloud AP automatically connects to the specified cloud management platform to load system files such as the configuration file, software package, and patch file. In this manner, the cloud AP can go online with zero touch configuration. The network administrator can deliver configurations to the cloud APs through the cloud management platform at anytime and anywhere, facilitating batch service configurations.

## Slide 81: Next-Generation Campus Network: Intent-Driven Campus (Medium- and Large-Sized)
Egress Zone
Core Layer
Aggregation Layer
Access Layer
DC
Native AC
Native AC
NMS O&M Zone
iStack/CSS Link
Internet
WAN
Architecture Characteristics
iMaster NCE manages and configures APs in a unified manner and provides various functions. By further integrating with wired networks and leveraging Big Data and AI technologies, this architecture implements simplified, intelligent, and secure campus networks.
Applicable scope: medium- and large-sized enterprises

## Slide 82
What are the advantages and disadvantages of in-path and off-path networking modes?
(Multiple) Which of the following methods are supported by Fit APs to discover an AC?( )
  Static discovery
  Dynamic discovery through DHCP
  Dynamic discovery through FTP
  Dynamic discovery through DNS
Notes: Answer:
  In-path networking advantages: Direct forwarding is often used on an in-path network. This networking mode simplifies the network architecture and applies to large-scale centralized WLANs.
  Off-path networking advantages: The off-path networking mode is commonly used. Wireless user service data does not need to be processed by an AC, eliminating the bandwidth bottleneck and facilitating the usage of existing security policies. Therefore, this networking mode is recommended.
ABD

## Slide 83
WLAN technology allows users to easily access a wireless network and freely move around within the coverage of the wireless network, eliminating the constraints of wired networks.
In this course, we have learned WLAN technologies on enterprise networks, including the basic concepts, fundamentals, network architectures, configuration implementation, and development trend of WLAN technologies.