## Slide 1
He Junjian/WX580230
New
Ren Jie/WX504966
New
Lu Yueyue/WX445705
2020.6
Update

## Slide 2: Advanced IGP Features

## Slide 3
Both Open Shortest Path First (OSPF) and Intermediate System to Intermediate System (IS-IS) are link-state Interior Gateway Protocols (IGPs). Routers that run them synchronize link state databases (LSDBs) and use the shortest path first (SPF) algorithm to calculate optimal routes.
In response to network topology changes, OSPF and IS-IS support multiple fast convergence and protection mechanisms, which minimize traffic loss caused by network faults.
To control the size of a routing table, OSPF and IS-IS support route selection and routing information control.
This course describes the advanced features of OSPF and IS-IS, including fast convergence and route control.

## Slide 4
On completion of this course, you will be able to:
  Describe various fast convergence techniques of OSPF and IS-IS.
  Configure OSPF and IS-IS equal-cost routes.
  Configure OSPF and IS-IS to advertise default routes.
  Describe the application scenarios of OSPF and IS-IS multi-process.
  Describe the application scenarios of OSPF forwarding address (FA).
  Describe the implementation of IS-IS LSP fragment extension.

## Slide 5
OSPF Fast Convergence
OSPF Route Control
Other OSPF Features
Advanced IS-IS Features

## Slide 6: Overview of OSPF Fast Convergence
OSPF fast convergence is an extended feature of OSPF to speed up route convergence. It features partial route calculation (PRC) and the intelligent timer.
In addition, OSPF supports fast convergence upon fault rectification. For example, OSPF IP fast reroute (FRR) can be used to implement fast traffic switchover to a backup link, and OSPF can also be associated with BFD to implement fast fault detection.
Overview
PRC
Intelligent Timer
FRR
BFD Association

## Slide 7: PRC
PRC only calculates routes that have been changed on a network.
PRC does not calculate nodes. Instead, it updates routes based on the shortest path tree (SPT) calculated using the SPF algorithm.
In route calculation, a node represents a router, and a leaf represents a route. PRC processes only the changed leaf information.
R1 (root)
R2
R3
R4
R5
Scenario description:
  OSPF runs on a network. The figure shows the SPT with R1 as the root after network convergence. When R1 accesses R5, traffic is sent to the destination based on [outbound interface of R1's downlink, IP address of R3's uplink interface].
  OSPF is enabled on Loopback0 of R5. This means that a new network segment is added to the OSPF network.
PRC:
  R5 floods a new LSA on the entire network.
  After receiving the LSA, R1 creates a new route that inherits the original path and next hop used when R1 accesses R5. In this case, the SPT remains unchanged, and only a leaf is added to R5.
  Therefore, when R1 accesses Loopback0 of R5, traffic is sent to the destination based on [outbound interface of R1's downlink, IP address of R3's uplink interface].
Benefits:
  PRC focuses only on routes that are changed due to the addition of network segments to an OSPF network, thereby speeding up route calculation.
Loopback0: A directly connected network segment is added.
Overview
PRC
Intelligent Timer
FRR
BFD Association
Notes: Note: On Huawei devices, OSPF PRC is enabled by default.

## Slide 8: Intelligent Timer
The intelligent timer is used for SPF calculation and LSA generation.
It can quickly respond to a small number of external incidents and prevent excessive CPU consumption.
Controlling LSA Generation and Reception
To prevent network connections or frequent route flapping from consuming excessive device resources, OSPF complies with the following rules:
After an LSA is generated, it cannot be generated again within 1s. The interval for updating LSAs is 5s.
The interval for receiving LSAs is 1s.
On a stable network where routes need to be fast converged, the intelligent timer can be used to set the interval for updating LSAs to 0s in order to cancel this interval. In this manner, topology or route changes can be immediately advertised to the network through LSAs or be immediately detected, thereby speeding up route convergence on the network.
Controlling Route Calculation
When a network changes, the OSPF LSDB changes, and the shortest path needs to be recalculated. If a network changes frequently, the shortest path is calculated accordingly, which results in excessive consumption of system resources and compromises device efficiency.
You can configure the intelligent timer to set a proper interval for SPF calculation in order to prevent excessive consumption of a router's memory and bandwidth resources.
Overview
PRC
Intelligent Timer
FRR
BFD Association
Notes: If the interval for triggering route calculation is long, the network convergence speed is affected.
The first timeout period of the intelligent timer is fixed. Before the intelligent timer expires, if an event that triggers the timer occurs, the next timeout period of the intelligent timer becomes longer.

## Slide 9: Basic Intelligent Timer Configuration Commands (1)
After the intelligent timer is used:
  The initial interval for updating LSAs is specified by start-interval.
  The interval at which LSAs are updated for the nth (n ≥ 2) time equals hold-interval x 2(n – 2).
  When the interval specified by hold-interval x 2(n – 2) reaches the maximum interval specified by max-interval, OSPF updates LSAs at the maximum interval for three consecutive times. Then, OSPF returns to the first step and updates LSAs at the initial interval specified by start-interval.
[Huawei-ospf-1] lsa-originate-interval { 0 | { intelligent-timer max-interval start-interval hold-interval | other-type interval } * }
Set an interval for updating OSPF LSAs.
By default, the intelligent timer is enabled; the maximum interval, initial interval, and hold interval at which LSAs are updated are 5000 ms, 500 ms, and 1000 ms, respectively.
Overview
PRC
Intelligent Timer
FRR
BFD Association
Notes: Command: [Huawei-ospf] lsa-originate-interval { 0 | { intelligent-timer max-interval start-interval hold-interval | other-type interval } }
  0: sets the interval for updating LSAs to 0s, that is, cancels the interval of 5s for updating LSAs.
  intelligent-timer: uses the intelligent timer to set the update interval for router-LSAs and network-LSAs.
  max-interval: specifies the maximum interval for updating OSPF LSAs. The value is an integer ranging from 1 to 120000, in milliseconds. The default value is 5000.
  start-interval: specifies the initial interval for updating OSPF LSAs. The value is an integer ranging from 0 to 60000, in milliseconds. The default value is 500.
  hold-interval: specifies the hold interval for updating OSPF LSAs. The value is an integer ranging from 1 to 60000, in milliseconds. The default value is 1000.
  other-type: sets an update interval for OSPF LSAs except router-LSAs and network-LSAs.
  interval: specifies the interval for updating LSAs. The value is an integer ranging from 0 to 10, in seconds. The default value is 5.

## Slide 10: Basic Intelligent Timer Configuration Commands (2)
After the intelligent timer is used:
  The initial interval for receiving LSAs is specified by start-interval.
  The interval at which LSAs are received for the nth (n ≥ 2) time equals hold-interval x 2(n – 2).
  When the interval specified by hold-interval x 2(n – 2) reaches the maximum interval specified by max-interval, OSPF receives LSAs at the maximum interval for three consecutive times. Then, OSPF returns to the first step and receives LSAs at the initial interval specified by start-interval.
[Huawei-ospf-1] lsa-arrival-interval { interval | intelligent-timer max-interval start-interval hold-interval }
Set an interval for receiving OSPF LSAs.
By default, the intelligent timer is enabled; the maximum interval, initial interval, and hold interval at which LSAs are received are 1000 ms, 500 ms, and 500 ms, respectively.
Overview
PRC
Intelligent Timer
FRR
BFD Association
Notes: Command: [Huawei-ospf-1] lsa-arrival-interval { interval | intelligent-timer max-interval start-interval hold-interval }
  interval: specifies the interval for receiving LSAs. The value is an integer ranging from 0 to 10000, in milliseconds.
  intelligent-timer: uses the intelligent timer to set the receive interval for LSAs.
  max-interval: specifies the maximum interval for receiving OSPF LSAs. The value is an integer ranging from 1 to 120000, in milliseconds. The default value is 1000.
  start-interval: specifies the initial interval for receiving OSPF LSAs. The value is an integer ranging from 0 to 60000, in milliseconds. The default value is 500.
  hold-interval: specifies the hold interval for receiving OSPF LSAs. The value is an integer ranging from 1 to 60000, in milliseconds. The default value is 500.

## Slide 11: Basic Intelligent Timer Configuration Commands (3)
After the intelligent timer is used, the interval for SPF calculation is as follows:
  The initial interval for SPF calculation is specified by start-interval.
  The interval for SPF calculation for the nth (n ≥ 2) time equals hold-interval x 2(n – 2).
  When the interval specified by hold-interval x 2(n – 2) reaches the maximum interval specified by max-interval, OSPF performs SPF calculation at the maximum interval for three consecutive times. Then, OSPF returns to the first step and performs SPF calculation at the initial interval specified by start-interval.
[Huawei-ospf-1] spf-schedule-interval { interval1 | intelligent-timer max-interval start-interval hold-interval | millisecond interval2 }
Set an interval for OSPF route calculation.
By default, the intelligent timer is enabled; the maximum interval, initial interval, and hold interval for SPF calculation are 10000 ms, 500 ms, and 1000 ms, respectively.
Overview
PRC
Intelligent Timer
FRR
BFD Association
Notes: Command: [Huawei-ospf-1] spf-schedule-interval { interval1 | intelligent-timer max-interval start-interval hold-interval | millisecond interval2 }
  interval1: specifies an interval for OSPF SPF calculation. The value is an integer ranging from 1 to 10, in seconds.
  intelligent-timer: uses the intelligent timer to set the interval for OSPF SPF calculation.
  max-interval: specifies the maximum interval for OSPF SPF calculation. The value is an integer ranging from 1 to 120000, in milliseconds. The default value is 10000.
  start-interval: specifies the initial interval for OSPF SPF calculation. The value is an integer ranging from 1 to 60000, in milliseconds. The default value is 500.
  hold-interval: specifies the hold interval for OSPF SPF calculation. The value is an integer ranging from 1 to 60000, in milliseconds. The default value is 1000.
  millisecond interval2: specifies an interval for OSPF SPF calculation. The value is an integer ranging from 1 to 10000, in milliseconds.

## Slide 12: OSPF IP FRR
OSPF IP fast reroute (FRR) is a dynamic IP FRR technology that uses the loop-free alternate (LFA) algorithm to pre-calculate a backup path and saves it in the forwarding table. If the primary link fails, traffic is rapidly switched to the backup link, ensuring traffic continuity and achieving traffic protection. OSPF IP FRR can reduce the fault recovery time to less than 50 ms.
The LFA algorithm calculates a backup link based on the following principles:
  A device uses the SPF algorithm to calculate shortest paths to the destination, with each neighbor that provides a backup link as a root node. The device then uses the inequality to calculate a loop-free backup link with the minimum cost.
Overview
PRC
Intelligent Timer
FRR
BFD Association

## Slide 13: Networking of OSPF IP FRR
OSPF IP FRR protects traffic against either a link failure or a node-and-link failure.
Link protection
Link protection inequality:
Distance_opt (N, D) < Distance_opt (N, S) + Distance_opt (S, D)
This ensures that the traffic from node N to node D does not pass through node S. That is, this ensures that no loop occurs.
S
Cost = 10
Cost = 5
Cost = 10
Cost = 5
N
R1
D
Node-and-link protection
Link protection inequality:
Distance_opt (N, D) < Distance_opt (N, S) + Distance_opt (S, D)
Node protection inequality:
Distance_opt (N, D) < Distance_opt (N, E) + Distance_opt (E, D)
This ensures that the traffic from node N to node D does not pass through nodes S and E. That is, this ensures that no loop occurs.
S
Cost = 10
Cost = 5
Cost = 10
Cost = 5
N
E
D
S: source node
D: destination node
N: node along the backup link
Distance_opt (X, Y)
indicates the shortest path from node X to node Y.
S: source node
D: destination node
N: node along the backup link
E: faulty node
Traffic flows from node S to node D. The link cost satisfies the link protection inequality. If the primary link fails, node S switches the traffic to the backup link. This ensures that the traffic interruption time is less than 50 ms.
Node-and-link protection must meet the preceding two inequalities.
Overview
PRC
Intelligent Timer
FRR
BFD Association
Notes: Node-and-link protection:
  As shown in the right figure, traffic flows from node S to node D. The link cost satisfies the node-and-link protection inequality. If the primary link fails, node S switches the traffic to the backup link. This ensures that the traffic interruption time is less than 50 ms.
OSPF IP FRR protects traffic against either a link failure or a node-and-link failure.
  Link protection takes effect when the traffic to be protected flows along a specified link.
  Node-and-link protection takes effect when the traffic to be protected flows along a specified device. Node-and-link protection takes precedence over link protection.

## Slide 14: Basic OSPF IP FRR Configuration Commands
[Huawei-ospf-1] frr
[Huawei-ospf-1-frr]
Enable OSPF IP FRR.
Create OSPF FRR and enter its view.
[Huawei-ospf-1-frr] loop-free-alternate
After OSPF IP FRR is enabled, the device uses the LFA algorithm to calculate the next hop and outbound interface for a backup link.
[Huawei-GigabitEthernet0/0/1] ospf frr block
(Optional) Disable OSPF IP FRR on an interface.
OSPF IP FRR can be disabled on an interface of a specific device that is running important services and resides on an FRR backup link. This setting prevents the device connected to this interface from being a part of a backup link and being burdened after FRR switches traffic to the backup link.
Overview
PRC
Intelligent Timer
FRR
BFD Association

## Slide 15: Example for Configuring OSPF IP FRR
OSPF
area 0
R1
Cost = 10
Cost = 5
Cost = 10
Cost = 5
R2
R3
R4
GE0/0/1
GE0/0/2
GE0/0/1
If the link between R1 and R3 fails, traffic forwarded by R1 can be quickly switched to the backup link and forwarded by R2.
Device | Router ID | Interface | IP Address
R1 | 10.1.1.1 | GE0/0/0 | 10.1.13.1/24
 |  | GE0/0/1 | 10.1.12.1/24
R2 | 10.1.2.2 | GE0/0/1 | 10.1.12.2/24
 |  | GE0/0/2 | 10.1.23.2/24
R3 | 10.1.3.3 | GE0/0/0 | 10.1.13.3/24
 |  | GE0/0/1 | 10.1.34.3/24
 |  | GE0/0/2 | 10.1.23.3/24
R4 | 10.1.4.4 | GE0/0/1 | 10.1.34.4/24
1. Assign an IP address to each interface and configure OSPF on each device. (The configuration details are not provided here.)
[R1] interface GigabitEthernet 0/0/0
[R1-GigabitEthernet 0/0/0] ospf cost 10
[R1-GigabitEthernet 0/0/0] quit
[R1] interface GigabitEthernet 0/0/1
[R1-GigabitEthernet 0/0/1] ospf cost 10
[R1-GigabitEthernet 0/0/1] quit
2. Configure an OSPF cost for each device. The following example uses the command output on R1.
The cost configurations of R2, R3, and R4 are similar to the configuration of R1.
GE0/0/0
3. Enable OSPF IP FRR on R1.
[R1] ospf
[R1-ospf-1] frr
[R1-ospf-1-frr] loop-free-alternate
[R1-ospf-1-frr] quit
[R1-ospf-1] quit
Overview
PRC
Intelligent Timer
FRR
BFD Association

## Slide 16: Checking the OSPF IP FRR Configuration
R1
Cost = 10
Cost = 5
Cost = 10
Cost = 5
R2
R3
R4
GE0/0/0
GE0/0/1
GE0/0/2
GE0/0/1
If the link between R1 and R3 fails, traffic forwarded by R1 can be quickly switched to the backup link and forwarded by R2.
Device | Router ID | Interface | IP Address
R1 | 10.1.1.1 | GE0/0/0 | 10.1.13.1/24
 |  | GE0/0/1 | 10.1.12.1/24
R2 | 10.1.2.2 | GE0/0/1 | 10.1.12.2/24
 |  | GE0/0/2 | 10.1.23.2/24
R3 | 10.1.3.3 | GE0/0/0 | 10.1.13.3/24
 |  | GE0/0/1 | 10.1.34.3/24
 |  | GE0/0/2 | 10.1.23.3/24
R4 | 10.1.4.4 | GE0/0/1 | 10.1.34.4/24
Check information about the route from R1 to GE0/0/1 of R4.
[R1]display ospf routing 10.1.34.4
OSPF Process 1 with Router ID 10.1.1.1
Destination : 10.1.34.0/24
AdverRouter : 10.1.4.4 Area : 0.0.0.0
Cost : 15 Type : Transit
NextHop : 10.1.13.3 Interface : GigabitEthernet0/0/0
Priority : Low Age : 00h01m59s
Backup Nexthop : 10.1.12.2 Backup Interface:GigabitEthernet0/0/1
Backup Type : LFA LINK
You can find that OSPF generates a backup link after OSPF IP FRR is enabled on R1.
OSPF
area 0
Overview
PRC
Intelligent Timer
FRR
BFD Association

## Slide 17: BFD for OSPF
A link fault or a topology change causes devices to recalculate routes. Fast and efficient routing protocol convergence is necessary to improve network availability.
BFD for OSPF associates BFD with OSPF. If a fault occurs on the link between a device and its neighbor, BFD can rapidly detect the link fault to speed up OSPF's response to network topology changes.
OSPF
BFD
The working principle of BFD for OSPF is as follows:
  OSPF neighbor relationships are established between R1, R2, and R3. When the neighbor relationships enter the Full state, BFD is instructed to set up a BFD session.
  If a fault occurs on the link between R1 and R2, BFD detects the fault and notifies R1. R1 processes the BFD session down event and recalculates the route. The new path is R1-R3-R2.
R1
R3
S1
R2
Overview
PRC
Intelligent Timer
FRR
BFD Association
Notes: OSPF periodically sends Hello packets to neighbors to detect faults. It takes more than 1s to detect a fault. By default, when the OSPF Dead timer expires, the neighbor is considered invalid. The default value of the OSPF Dead timer is 40s. With the development of technologies, voice, video, and video on demand (VOD) services are widely used. These services are sensitive to the packet loss rate and delay. When the traffic rate reaches gigabit per second (Gbit/s), long-time fault detection causes a large number of packets to be lost. This cannot meet high reliability requirements of the carrier-class network.
BFD for OSPF is introduced to resolve this problem. After BFD for OSPF is configured in a specified process or on a specified interface, the link status can be rapidly detected and fault detection can be completed in milliseconds. This speeds up OSPF convergence when the link status changes.

## Slide 18: Basic BFD for OSPF Configuration Commands
[Huawei-ospf-1] bfd all-interfaces enable
Configure BFD for OSPF.
Enable BFD in an OSPF process.
[Huawei-ospf-1] bfd all-interfaces { min-rx-interval receive-interval | min-tx-interval transmit-interval | detect-multiplier multiplier-value | frr-binding }
Configure BFD session parameters.
[Huawei-GigabitEthernet0/0/1] ospf bfd enable
Configure BFD on a specified interface.
Enable BFD on an OSPF interface.
[Huawei-GigabitEthernet0/0/1] ospf bfd { min-rx-interval receive-interval | min-tx-interval transmit-interval | detect-multiplier multiplier-value | frr-binding }
Configure BFD session parameters on the OSPF interface.
Overview
PRC
Intelligent Timer
FRR
BFD Association
Notes: Prerequisites:
  Before using BFD to quickly detect link faults, run the bfd command in the system view to enable BFD globally.
The BFD configuration on an interface takes precedence over that in a process. If BFD is enabled on an interface, the BFD parameters on the interface are used to establish BFD sessions.
OSPF IP FRR can be associated with BFD.
  During the OSPF IP FRR configuration, the underlying layer needs to fast respond to a link status change so that traffic can be switched to the backup link immediately.
  OSPF IP FRR and BFD can be bound to rapidly detect link faults. This ensures that traffic is rapidly switched to the backup link in the case of link failures.
Command: [Huawei-ospf-1] bfd all-interfaces { min-rx-interval receive-interval | min-tx-interval transmit-interval | detect-multiplier multiplier-value | frr-binding }
  min-rx-interval receive-interval: specifies an expected minimum interval for receiving BFD packets from the peer. The value is an integer ranging from 10 to 2000, in milliseconds. The default value is 1000.
  min-tx-interval transmit-interval: specifies a minimum interval for sending BFD packets to the peer. The value is an integer ranging from 10 to 2000, in milliseconds. The default value is 1000.
  detect-multiplier multiplier-value: specifies a local detection multiplier. The value is an integer ranging from 3 to 50. The default value is 3.
  frr-binding: binds the BFD session status to the link status of an interface. If a BFD session goes down, the physical link of the bound interface also goes down, triggering traffic to be switched to the backup link.

## Slide 19
OSPF fast convergence
OSPF Route Control
Other OSPF Features
Advanced IS-IS Features

## Slide 20: Overview of OSPF Route Control
OSPF route control includes:
  Adjusting the OSPF interface cost
  Setting the maximum number of equal-cost routes for load balancing
  Importing external routes
  Configuring route summarization
  Configuring default route advertisement
  Configuring filter-policies
  Configuring OSPF to filter outgoing LSAs
  Configuring an ABR to filter Type3 LSAs
  Setting the maximum number of External LSAs in the LSDB
Overview
Equal-Cost Route
Default Route
LSA Filtering
Configuration Case
Notes: This course describes only equal-cost routes, default routes, and LSA filtering. For other information, see HCIP-Datacom-Core Technology.

## Slide 21: Equal-Cost Route
If the destinations and costs of the multiple routes discovered by one routing protocol are the same, these routes are equal-cost routes and can participate in load balancing.
The device sends packets to the same destination address through multiple equal-cost routes in load balancing mode.
Set the maximum number of equal-cost routes for load balancing.
[Huawei-ospf-1] maximum load-balancing number
Overview
Equal-Cost Route
Default Route
LSA Filtering
Configuration Case
Notes: Command: [Huawei-ospf-1] maximum load-balancing number
  number: specifies the maximum number of equal-cost routes for load balancing. The value range varies according to the device model. For details, see the product documentation of the corresponding device.

## Slide 22: Example for Configuring the Number of Equal-Cost Routes for Load Balancing
It is required that R1 can access the loopback interface address of R3 through the path R1 -> R3 or the path R1 -> R2 -> R3.
OSPF
Area 0
R1
Cost = 10
Cost = 5
Cost = 5
R3
GE 0/0/0
GE 0/0/1
GE 0/0/2
R2
Device | Interface | IP Address
R1 | GE 0/0/0 | 10.1.13.1/24
 | GE 0/0/1 | 10.1.12.1/24
R2 | GE 0/0/1 | 10.1.12.2/24
 | GE 0/0/2 | 10.1.23.2/24
R3 | Loopback0 | 10.1.3.3/32
 | GE 0/0/0 | 10.1.13.3/24
 | GE 0/0/2 | 10.1.23.3/24
1. Assign an IP address to each interface and configure OSPF on each device. (Details are not provided here.)
[R1] ospf
[R1-ospf-1] maximum load-balancing 2
2. Configure the maximum number of OSPF equal-cost routes for load balancing on R1.
[R1]display ip routing-table
Route Flags: R - relay, D - download to fib
-------------------------------------------------------------------------------------------
Destination/Mask Proto Pre Cost Flags NextHop Interface
10.1.3.3/32 OSPF 10 10 D 10.1.13.3 GigabitEthernet0/0/0
OSPF 10 10 D 10.1.12.2 GigabitEthernet0/0/1
3. Verify the configuration.
Overview
Equal-Cost Route
Default Route
LSA Filtering
Configuration Case

## Slide 23: Default Route
On the area border and AS border of an OSPF network generally reside multiple routers for egress backup or traffic load balancing. In this case, a default route can be configured to reduce the number of routing entries in the routing table and ensure high availability of the network.
OSPF default routes are generally applied to the following scenarios:
  An ABR advertises Type 3 LSAs carrying the default route so that routers in an area forward inter-area packets accordingly.
  An ASBR advertises Type 5 or Type 7 LSAs carrying the default route so that routers in an AS forward AS-external packets.
Area Type | Trigger Condition | Advertised by | LSA Type | Flooding Scope
Common area | The default-route-advertise command is run. | ASBR | Type 5 LSA | Common area
Stub area and totally stubby area | Automatically generated | ABR | Type 3 LSA | Stub area
NSSA | The nssa [ default-route-advertise ] command is run. | ASBR | Type 7 LSA | NSSA
Totally NSSA | Automatically generated | ABR | Type 3 LSA | NSSA
Overview
Equal-Cost Route
Default Route
LSA Filtering
Configuration Case
Notes: Default routes have all 0s as the destination address and mask. A device uses a default route to forward packets when no matching route is available. Hierarchical management of OSPF routes prioritizes the default route carried in Type 3 LSAs over the default route carried in Type 5 or Type 7 LSAs.
Common area:
  By default, routers in a common OSPF area do not generate default routes. To enable a router in a common OSPF area to advertise a default route to OSPF, run the default-route-advertise command on the router. After the command is run, the router generates a default ASE LSA (Type 5 LSA) and advertises it to the entire OSPF AS.
Stub area:
  Type 5 LSAs cannot be advertised within a stub area. All routers within a stub area can learn AS external routes only through an ABR.
  The ABR in a stub area automatically generates a default Type 3 LSA and advertises it to the entire stub area. The ABR uses the default route to divert traffic destined for a destination outside the AS to itself and then forwards the traffic.

## Slide 24
Notes: Totally stub area:
  Neither Type 3 nor Type 5 LSAs can be advertised within a totally stub area. All routers within a totally stub area can learn AS external routes and other areas' routes only through an ABR.
  The ABR in a totally stub area automatically generates a default Type 3 LSA and advertises it to the entire stub area. The ABR uses the default route to divert traffic destined for a destination outside the AS to itself and then forwards the traffic.
NSSA:
  To enable packets destined for routers outside an AS to be sent by way of an ASBR in an NSSA, and other packets destined for routers outside the AS to be sent by way of an ABR in the NSSA, configure the ABR to generate a default Type 7 LSA and advertise this LSA within the entire NSSA. In this case, a default Type 7 LSA will be generated on the ABR, regardless of whether the default route 0.0.0.0 exists in the routing table.
  To enable all packets destined for routers outside the AS to be sent by way of an ASBR in the NSSA, run the nssa [default-route-advertise] command on the ASBR so that the ASBR generates a default NSSA LSA (Type7 LSA) and advertises it to the entire NSSA. In this case, a default Type 7 LSA is generated only when the default route 0.0.0.0 exists in the routing table on the ASBR.
  Note: Default routes are flooded only within the local NSSA and are not flooded within the entire OSPF AS. If routers in the local NSSA have no routes to the outside of the AS, the routers can forward packets outside of the AS through an ASBR. However, packets of other OSPF areas cannot be sent outside the AS through this ASBR. An ABR does not translate default Type 7 LSAs into default Type 5 LSAs for flooding in the entire AS.
Totally NSSA:
  The ABR in a totally NSSA automatically advertises the default route through a Type 3 LSA to the NSSA. The ASBR in a totally NSSA, however, does not automatically advertise default routes. In this scenario, the routers in the area can reach the corresponding external network segments through the external routes imported by the ASBR and reach other network segments through the default routes delivered by the ABR.
  If you want routers in a totally NSSA to select an ASBR (rather than an ABR) as the default egress, you need to configure the ASBR to deliver the default route.

## Slide 25: Configuring Default Route Advertisement to OSPF Areas
Note:
  The import-route (OSPF) command cannot import the default route of another routing protocol. To enable a router to advertise the default route of another routing protocol, run the default-route-advertise command on an ASBR so that the default route is advertised to all common OSPF areas.
  Before advertising a default route, OSPF compares the preferences of default routes in an OSPF area and then advertises a default route with the highest preference. If a static default route is configured on an OSPF device, ensure that the preference of the static default route is lower than that of the default route to be advertised by OSPF. This ensures that the default route advertised by OSPF will be added to the routing table of the OSPF device.
[Huawei-ospf-1] default-route-advertise [ [ always | permit-calculate-other ] | cost cost | type type | route-policy route-policy-name [ match-any ] ]
Configure default route advertisement to common OSPF areas.
By default, OSPF devices in a common OSPF area do not generate default routes.
[Huawei-ospf-1] default-route-advertise summary cost cost
Configure default route advertisement through a Type 3 summary LSA and set a cost for the route.
Overview
Equal-Cost Route
Default Route
LSA Filtering
Configuration Case
Notes: Command: [Huawei-ospf-1] default-route-advertise [[always | permit-calculate-other] | cost cost | type type | route-policy route-policy-name [match-any]]
  always: An LSA that describes the default route is generated and advertised regardless of whether the local device has an active default route that does not belong to the current OSPF process.
    If always is configured, the device does not calculate the default routes from other devices.
    If always is not configured, an LSA that describes the default route can be generated only if an active default route that does not belong to the current OSPF process exists in the routing table of the local device.
  permit-calculate-other: An LSA that describes the default route is generated and advertised only if the device has an active default route that does not belong to the current OSPF process, and the device still calculates the default routes from other devices.
  type type: specifies the type of an external route. The value is 1 or 2. The default value is 2.
    1: Type 1 external route
    2: Type 2 external route
  route-policy route-policy-name: specifies the name of a route-policy. The device advertises default routes according to the configuration of the route-policy when the routing table of the device contains a default route that matches the route-policy but does not belong to the current OSPF process. The value is a string of 1 to 40 case-sensitive characters. If spaces are used, the string must start and end with double quotation marks (").

## Slide 26
Notes:   match-any: The device advertises default routes according to the configuration of the route-policy when the routing table contains routes that match the route-policy.
Command: [Huawei-ospf-1] default-route-advertise summary cost cost
  summary: Advertises the Type 3 summary LSA of the specified default route. Before specifying this parameter, ensure that a VPN is enabled. Otherwise, routes cannot be advertised.
  cost cost: specifies the cost of the LSA. The value is an integer ranging from 0 to 16777214. The default value is 1.
always:
  If the ASBR has a default route, the default-route-advertise command enables the ASBR to advertise the default route 0.0.0.0 to all OSPF areas.
  If the ASBR has no default route, the default-route-advertise always command or the default-route-advertise command can be used as required:
    With always configured, the ASBR can advertise the default route 0.0.0.0 even if there is no default route, and the ASBR does not calculate the default routes sent by other devices.
    Without always configured, the ASBR generates the LSA of the default route only when the local routing table contains an active default route (non-BGP route) that does not belong to the current OSPF process.
match-any:
  If a route-policy is configured with match-any, and multiple routes match the policy, a default LSA will be generated based on the optimal route. The rules for optimal route selection are as follows:
    A route configured with type takes precedence over that not configured with type. A route configured with a smaller type value takes precedence over that configured with a larger type value.
    A route configured with cost takes precedence over that not configured with cost. A route configured with a smaller cost value takes precedence over that configured with a larger cost value.
    A route configured with tag takes precedence over that not configured with tag. A route configured with a smaller tag value takes precedence over that configured with a larger tag value.

## Slide 27: Configuring OSPF to Filter Outgoing LSAs
When multiple links exist between two routers, you can enable the function to filter outgoing LSAs, preventing them from being sent to particular links. This function can help reduce unnecessary retransmission of LSAs and reduce bandwidth consumption.
Filtering the outgoing LSAs on a specified OSPF interface can prevent unwanted LSAs from being sent to neighbors, thus reducing the LSDB sizes of the neighbors and speeding up network convergence.
To filter outgoing LSAs on an OSPF interface, run the following command:
[Huawei-GigabitEthernet0/0/1] ospf filter-lsa-out { all | { summary [ acl { acl-number | acl-name } ] | ase [ acl { acl-number | acl-name } ] | nssa [ acl { acl-number | acl-name } ] } }
The command configuration does not take effect for the LSAs that have been sent out before the command is run. The aging time of such an LSA is still 3600 seconds.
Overview
Equal-Cost Route
Default Route
LSA Filtering
Configuration Case
Notes: Command: [Huawei-GigabitEthernet0/0/1] ospf filter-lsa-out { all | { summary [ acl { acl-number | acl-name } ] | ase [ acl { acl-number | acl-name } ] | nssa [ acl { acl-number | acl-name } ] } }
  all: filters all outgoing LSAs, except grace LSAs.
  summary: filters outgoing network-summary-LSAs (Type 3).
  ase: filters outgoing AS-external-LSAs (Type 5).
  nssa: filters outgoing NSSA-LSAs (Type 7).
  acl acl-number: specifies the number of a basic ACL. The value is an integer ranging from 2000 to 2999.
  acl acl-name: specifies the name of an ACL. The value is a string of 1 to 32 case-sensitive characters. It cannot contain spaces and must start with a letter (a to z or A to Z).

## Slide 28: Configuring OSPF to Filter ABR Type 3 LSAs
Configure filtering policies for incoming and outgoing ABR Type 3 LSAs (network-summary-LSAs) in an area, allowing only those that pass the filtering to be sent and accepted.
Filtering Type 3 LSAs in a specified OSPF area can prevent unwanted LSAs from being sent to neighbors, thus reducing the LSDB sizes and speeding up network convergence.
To filter outgoing Type3 LSAs in an OSPF area, run the following command:
To filter incoming Type3 LSAs in an OSPF area, run the following command:
[Huawei-ospf-1-area-0.0.0.1] filter { acl-number | acl-name acl-name | ip-prefix ip-prefix-name | route-policy route-policy-name } export
[Huawei-ospf-1-area-0.0.0.1] filter { acl-number | acl-name acl-name | ip-prefix ip-prefix-name | route-policy route-policy-name } import
Overview
Equal-Cost Route
Default Route
LSA Filtering
Configuration Case
Notes: Command: [ Huawei-ospf-1-area-0.0.0.1 ] filter { acl-number | acl-name acl-name | ip-prefix ip-prefix-name | route-policy route-policy-name } export
  acl-number: specifies the number of a basic ACL. The value is an integer ranging from 2000 to 2999.

## Slide 29: Overview of OSPF Database Overflow
The LSDBs of OSPF devices in the same area are synchronized after routes are converged. However, achieving such a state can be difficult as the number of routes on a network continuously increases, causing some devices to be unable to carry excess routing information due to limited system resources. This is called an OSPF database overflow.
One way to solve such an issue is to configure stub areas or NSSAs, which reduces the amount of routing information on devices. However, such an approach cannot prevent an OSPF database overflow caused by a sharp increase in dynamic routes. To resolve this issue, set the maximum number of non-default external LSAs allowed in the LSDB of a device to dynamically control the LSDB size.
Set the maximum number of non-default external LSAs allowed in the LSDB.
[Huawei-ospf-1] lsdb-overflow-limit number
Overview
Equal-Cost Route
Default Route
LSA Filtering
Configuration Case
Notes: When the number of external LSAs (Type 5 and Type 7) imported by OSPF exceeds the maximum number supported, excessive external LSAs cannot be processed properly and are discarded. To address this issue, you can set a proper upper limit for the number of non-default external LSAs in the LSDB, so as to adjust and optimize the OSPF network.
Command: [Huawei-ospf-1] lsdb-overflow-limit number
  number: specifies the maximum number of non-default external LSAs allowed in the LSDB. The value is an integer ranging from 1 to 1000000.

## Slide 30: Preventive Measures for OSPF Database Overflows
Setting the maximum number of non-default external routes on a router can prevent OSPF database overflows.
Set the same maximum number for all routers on an OSPF network. When the number of non-default external routes on a router reaches the maximum number, the router enters the Overflow state and starts the Overflow state timer (default timeout period: 5s). After the timer expires, the router automatically exits the Overflow state.
Enters the Overflow state.
Stays in the Overflow state.
Exits the Overflow state.
Overflow Phase | OSPF Processing
Enters the Overflow state. | Deletes all non-default external routes generated by the router itself. Starts the Overflow state timer.
Stays in the Overflow state. | Does not generate non-default external routes. Discards newly received non-default external routes and does not reply with LSAck packets. Checks whether the number of external routes still exceeds the maximum number when the overflow state timer expires. If not, the router exits the Overflow state. If so, the router restarts the Overflow state timer.
Exits the Overflow state. | Deletes the Overflow state timer. Generates non-default external routes. Accepts newly received non-default external routes and replies with LSAck packets. Gets ready to enter the Overflow state again.
Restarts the timer.
Enters the Overflow state again.
Overview
Equal-Cost Route
Default Route
LSA Filtering
Configuration Case

## Slide 31: Example for Configuring OSPF Route Control (1)
To reduce the number of LSAs on R3 and ensure that R3 can properly communicate with routers in other areas, check that the following requirements are met:
  R2 does not inject Type 3 LSAs into Area 1.
  R2 advertises default routes.
OSPF
R1
R2
R3
Area1
Type3 LSA
1. Assign an IP address to each interface and configure OSPF on each device. (omitted).
[R2] acl 2000
[R2-acl-basic-2000] rule deny
[R2-acl-basic-2000] quit
[R2] ospf
[R2-ospf-1] area 1
[R2-ospf-1-area-0.0.0.1] filter 2000 import
2. Configure R2 to filter Type 3 LSAs.
[R2] ospf
[R2-ospf-1] default-route-advertise always
3. Configure R2 to advertise default routes.
Overview
Equal-Cost Route
Default Route
LSA Filtering
Configuration Case
Area0

## Slide 32: Example for Configuring OSPF Route Control (2)
OSPF
R1
R2
R3
Area0
Area1
Type3 LSA
1. Check the LSDB of R3.
[R3]display ospf lsdb
OSPF Process 1 with Router ID 10.1.23.3
Link State Database
Area: 0.0.0.1
Type LinkState ID AdvRouter Age Len Sequence Metric
Router 10.1.23.3 10.1.23.3 731 48 80000004 1
Router 10.1.12.2 10.1.12.2 406 36 80000008 1
Network 10.1.23.2 10.1.12.2 730 32 80000002 0
AS External Database
Type LinkState ID AdvRouter Age Len Sequence Metric
External 0.0.0.0 10.1.12.2 406 36 80000001 1
2. Check the routing table of R3.
[R3]dis ip routing-table
Route Flags: R - relay, D - download to fib
-----------------------------------------------------------------------------------------
Routing Tables: Public
Destinations : 9 Routes : 9
Destination/Mask Proto Pre Cost Flags NextHop Interface
0.0.0.0/0 O_ASE 150 1 D 10.1.23.2 GigabitEthernet0/0/1
…
The LSDB of R3 in Area1 does not contain Type 3 LSAs but contains a default Type 5 LSA.
R3 can access devices in other areas through the default route.
Overview
Equal-Cost Route
Default Route
LSA Filtering
Configuration Case

## Slide 33: OSPF Route Control Case Analysis
Network deployment:
  An enterprise network is divided into two networks, one for the finance department and the other for the marketing department.
  The enterprise network uses OSPF to allow internal network connectivity. The backbone network is deployed in area 0, clients of the finance department's network are deployed in area 1, and clients of the marketing department's network are deployed in area 2.
  Border devices access department servers through static routes, which are imported to the OSPF process.
Requirements:
  As long as the border-1 router and its uplink work properly, the data flows of the finance department are forwarded only through the border-1 router.
  As long as the core-1 router and its uplink work properly, the data flows of the finance department are forwarded only through the core-1 router.
  For details about the data forwarding requirements of the marketing department, see the comment of this slide.
AGG-1
Finance department client
Marketing department client
Core-1
Border-1
AGG-2
Core-2
Border-2
OSPF
Area 0
OSPF
Area 1
OSPF
Area 2
Data flow of the finance department
Static routing
Finance department server
Marketing department server
Overview
Equal-Cost Route
Default Route
LSA Filtering
Configuration Case
Notes: Data forwarding requirements of the marketing department:
  As long as the border-2 router and its uplink work properly, the data flows of the marketing department are forwarded only through the border-2 router.
  As long as the core-2 router and its uplink work properly, the data flows of the marketing department are forwarded only through the core-2 router.
This case uses the data forwarding path of the finance department as an example. The data forwarding path of the marketing department is not described here.

## Slide 34: Requirement Analysis
Controlling the network egress for data forwarding:
  Data of the finance department is always forwarded through border-1.
  Data of the marketing department is always forwarded through border-2.
AGG-1
Finance department server
Marketing department server
Core-1
Border-1
AGG-2
Core-2
Data flow of the finance department
Controlling the precise internal path of data flows:
  Load-balancing path should not exist.
To ensure that fixed ASBRs are used to forward data, the internal network changes must be ignored. That is, the internal route cost is not calculated.
—Use Type 2 external routes of OSPF.
Data needs to be sent to a specific ASBR along the planned path on the network.
—Adjust the internal path cost.
Finance department client
Marketing department client
Border-2
Overview
Equal-Cost Route
Default Route
LSA Filtering
Configuration Case
Notes: Type 2 external route:
  Because a Type 2 external route offers low reliability, its cost is considered to be much greater than the cost of any internal route to an ASBR.
  Cost of a Type 2 external route = Cost of the route from an ASBR to the destination

## Slide 35: Traffic Egress Control
Implementation:
  Import static routes destined for the finance department server to the OSPF processes of R1 (border-1) and R2 (border-2) to implement egress backup through route-policies.
  Set the type of the imported external route to Type 2.
  On R1, set the cost of the external route to 100; on R2, set the cost of the external route to 200.
Configuration result:
  When there are two Type 2 external routes with different costs on the same network segment, the network device prefers the route with a smaller cost. In this case, each network device preferentially selects R1 as the egress.
Imported finance department routes
Type: Type 2
Cost: 100
Imported finance department routes
Type: Type 2
Cost: 200
Finance department server
Marketing department server
Finance department client
Marketing department client
AGG-1
Core-1
Border-1
R1
AGG-2
Core-2
Border-2
R2
Overview
Equal-Cost Route
Default Route
LSA Filtering
Configuration Case
Notes: The internal path cost to each ASBR is not considered during traffic egress control.

## Slide 36: Controlling Internal Paths
Network requirement analysis:
  If the network is running properly, S3 (AGG-1) selects path 1.
  If the link between S1 (core-1) and R1 fails, S3 selects path 2.
  If S1 fails, S3 selects path 3.
Implementation:
  Path 1-cost < Path 2-cost < Path 3-cost
1
2
3
Finance department server
Marketing department server
Finance department client
Marketing department client
AGG-1
S3
Core-1
S1
AGG-2
S4
Core-2
S2
Data flow of the finance department
Border-1
R1
Border-2
R2
Overview
Equal-Cost Route
Default Route
LSA Filtering
Configuration Case

## Slide 37: Controlling Internal Paths: Adjusting the Cost Between Aggregation Devices and Core Devices
If the link between S1 and R1 fails, S3 preferentially selects path 1 and then path 2 because S1 is working properly.
Implementation:
  Path 1-cost < Path 2-cost, that is:
  Path 1 can be achieved by adjusting the path cost between aggregation devices and core devices.
1
2
[Cost (S3 - S1) + Cost (S1 - S2) + Cost (S2 - R1)] < [Cost (S3 - S2) + Cost (S2 - R1)]
Cost=10
Cost=10
Cost=50
Cost=50
Cost=10
Cost=50
Finance department server
Marketing department server
Finance department client
Marketing department client
AGG-1
S3
Core-1
S1
AGG-2
S4
Core-2
S2
Data flow of the finance department
Border-1
R1
Border-2
R2
Overview
Equal-Cost Route
Default Route
LSA Filtering
Configuration Case

## Slide 38: Controlling the Internal Path: Adjusting the Cost Between Core Devices and Boundary Devices
If the link between S3 and S1 fails, S3 preferentially selects path 1 and then path 2 because S1 is working properly.
Implementation:
  Path 1-cost < Path 2-cost, that is:
  Path 1 can be preferentially selected by adjusting the path cost between core devices and boundary devices.
1
2
[Cost (S3 - S2) + Cost (S2 - S1) + Cost (S1 - R1)] < [Cost (S3 - S2) + Cost (S2 - R1)]
Cost=10
Cost=10
Cost=50
Cost=50
Cost=10
Cost=50
Finance department server
Marketing department server
Finance department client
Marketing department client
AGG-1
S3
Core-1
S1
AGG-2
S4
Core-2
S2
Data flow of the finance department
Border-1
R1
Border-2
R2
Overview
Equal-Cost Route
Default Route
LSA Filtering
Configuration Case

## Slide 39: Example for Configuring OSPF Route Control (1)
Configure a route-policy on R1 and set the cost to 100.
192.168.10.0/24
192.168.20.0/24
OSPF
Area 0
OSPF
Area 1
OSPF
Area 2
Static routing
[R1] acl 2000
[R1-acl-basic-2000] rule permit source 192.168.10.0 0.0.0.255
[R1-acl-basic-2000] quit
[R1] route-policy static2ospf permit node 10
[R1-route-policy] if-match acl 2000
[R1-route-policy] apply cost 100
[R1-route-policy] quit
[R1] route-policy static2ospf permit node 20
[R1-route-policy] quit
[R1] ospf
[R1-ospf-1] import-route static route-policy static2ospf type 2
Import static routes to the OSPF process on R1.
Imported finance department routes
Type: Type 2
Cost: 100
Finance department server
Marketing department server
Finance department client
Marketing department client
AGG-1
S3
Core-1
S1
AGG-2
S4
Core-2
S2
Border-1
R1
Border-2
R2
Imported finance department routes
Type: Type 2
Cost: 200
Overview
Equal-Cost Route
Default Route
LSA Filtering
Configuration Case

## Slide 40: Example for Configuring OSPF Route Control (2)
Configure a route-policy on R2 and set the cost to 200.
192.168.10.0/24
192.168.20.0/24
OSPF
Area 0
OSPF
Area 1
Static routing
[R2] acl 2000
[R2-acl-basic-2000] rule permit source 192.168.10.0 0.0.0.255
[R2-acl-basic-2000] quit
[R2] route-policy static2ospf permit node 10
[R2-route-policy] if-match acl 2000
[R2-route-policy] apply cost 200
[R2-route-policy] quit
[R2] route-policy static2ospf permit node 20
[R2-route-policy] quit
[R2] ospf
[R2-ospf-1] import-route static route-policy static2ospf type 2
Import static routes to the OSPF process on R2.
Imported finance department routes
Type: Type 2
Cost: 100
Finance department server
Marketing department server
Finance department client
Marketing department client
AGG-1
S3
Core-1
S1
AGG-2
S4
Core-2
S2
Border-1
R1
Border-2
R2
Imported finance department routes
Type: Type 2
Cost: 200
OSPF
Area 2
Overview
Equal-Cost Route
Default Route
LSA Filtering
Configuration Case

## Slide 41: Example for Configuring OSPF Route Control (3)
Set the OSPF cost of an interface (GE0/0/1 of R1 is used as an example).
192.168.10.0/24
192.168.20.0/24
OSPF
Area 1
OSPF
Area 2
Static routing
[R1] interface GigabitEthernet 0/0/1
[R1-GigabitEthernet0/0/1] ospf cost 50
Cost=10
Cost=10
Cost=50
Cost=10
Cost=50
Cost=50
GE0/0/1
Finance department server
Marketing department server
Finance department client
Marketing department client
AGG-1
S3
Core-1
S1
AGG-2
S4
Core-2
S2
Border-1
R1
Border-2
R2
OSPF
Area 0
Overview
Equal-Cost Route
Default Route
LSA Filtering
Configuration Case

## Slide 42
OSPF fast convergence
OSPF Route Control
Other OSPF Features
Advanced IS-IS Features

## Slide 43: OSPF Multi-Process
OSPF supports multiple processes that can separately run on the same device and do not affect each other. Route exchange between different OSPF processes is similar to route exchange between different routing protocols.
An interface on a router can belong to only one OSPF process.
VPN1
Site 1
CE1
VPN2
Site 2
CE2
PE
OSPF 100 VPN1
Area0
Area0
OSPF 200 VPN2
Usage scenario:
  A typical application of OSPF multi-process is in the VPN scenario.
  As shown in the figure, a PE connects to two different VPN customers, and OSPF is deployed between the PE and CEs. Therefore, multiple processes can be deployed on the PE to isolate the VPN customers.
[PE] ospf 100 vpn-instance VPN1
[PE-ospf-100] quit
[PE] ospf 200 vpn-instance VPN2
[PE-ospf-200] quit
Multi-Process
Association with BGP
Forwarding Address
Notes: VPN: virtual private network
If a VPN instance is specified for an OSPF process that is to be created, the OSPF process belongs to this instance. Otherwise, the OSPF process belongs to the global instance.

## Slide 44: Association Between OSPF and BGP (1)
When a new device is added or a device is restarted, network traffic may be lost during BGP convergence. This is because IGP route convergence is faster than BGP route convergence.
AS 100
R1
R3
R4
R2
10.1.5.5/32
IBGP
EBGP
AS 101
OSPF runs on R1, R2, R3, and R4 and full-mesh IBGP connections are established. R3 is the backup device of R2.
When the network is stable, the traffic from R1 to 10.1.5.5/32 passes through the path R1 -> R2 -> R4 -> R5.
R5
If R2 fails, traffic is switched to the path R1 -> R3 -> R4 -> R5.
After R2 recovers, OSPF converges first because IGP route convergence is faster than BGP route convergence. If R1 needs to access 10.1.5.5/32, it searches for a BGP route with the next hop being R5. R2 then searches for the IGP route and sends traffic to R2 over the route.
After receiving the traffic, R2 searches for the BGP route. Because BGP route convergence is not complete, R2 does not find a route to 10.1.5.5/32 and therefore does not forward traffic. As a result, traffic is lost.
1
2
3
Multi-Process
Association with BGP
Forwarding Address

## Slide 45: Association Between OSPF and BGP (2)
OSPF-BGP synchronization can be enabled to prevent traffic loss.
After OSPF-BGP synchronization is enabled on a device, the device remains as a stub router within the set synchronization period. That is, the link metric in the LSA advertised by the device is the maximum value 65535. Therefore, the device instructs other OSPF devices not to use it for data forwarding.
AS 100
R1
R3
R4
R2
10.1.5.5/32
IBGP
EBGP
AS 101
R5
Enable BGP association on R2. In this way, R1 continues to forward traffic through R3, but does not forward traffic to R2 until BGP route convergence on R2 is complete.
Configure the stub router.
[Huawei-ospf-1] stub-router [ on-startup [ interval ] ]
Configure it as a stub router.
Configuring a stub router is a special route selection method. The path with a stub router configured is not preferred.
The implementation is to set the metric to the maximum value (65535) to prevent data from being forwarded through the router. It is used to protect the link of the router and is usually used in maintenance scenarios, such as upgrade.
Multi-Process
Association with BGP
Forwarding Address
Notes: Command: [Huawei-ospf-1] stub-router [ on-startup [ interval ] ]
  on-startup [ interval ]: specifies the interval for a device to remain as a stub router when the device restarts or fails. The value is an integer ranging from 5 to 65535, in seconds. The default value is 500s.
    If on-startup is not configured, the device is always a stub router. That is, the cost of all routes sent by this device is 65535.
    If on-startup is specified, the device remains as a stub router only when it restarts or fails. The duration is determined by interval. If interval is not specified, the default value of 500s is used.

## Slide 46: OSPF Forwarding Address
Forwarding address (FA):
  The FA is the address to which a data packet is forwarded before the packet reaches the advertised destination address. If the forwarding address is 0.0.0.0, the packet is forwarded to the originating ASBR.
  Type 5 AS-External LSAs and Type 7 NSSA LSAs:
Network Mask |  | 
E | 0 | Metric
Forwarding Address |  | 
External Route Tag |  | 
... |  | 
LS Age | Options | LS Type
Link State ID |  | 
Advertising Router |  | 
LS Sequence Number |  | 
LS Checksum | Length | 
OSPF Type 5 and Type 7 LSAs contain a special FA field. The introduction of FA enables OSPF to avoid the sub-optimal path problem in some special scenarios.
Forwarding Address
Multi-Process
Association with BGP

## Slide 47: Problem Occurring When No FA Is Used
OSPF runs on R2, R3, and R4 that are deployed in Area 0. OSPF is enabled on GE0/0/1 of R2 and GE0/0/1 of R3, and OSPF adjacencies are established between the two routers. However, no OSPF adjacencies are established between R1 and the two routers.
  Configure a static route destined for 10.1.1.1/32 on R2, with 10.1.123.1 as the next hop.
  R2 imports the static route to OSPF and generates a Type 5 LSA to be flooded in the area.
  After R3 receives the Type 5 LSA from R2, it calculates an external route to 10.1.1.1/32 and sets the next-hop address of the route to R2 (10.1.123.2).
The path from a router (for example, R4) in the OSPF domain to 10.1.1.1/32 is R4 -> R3 -> R2 -> R1, which is the sub-optimal path.
10.1.1.1/32
R1
R2
R3
R4
GE0/0/1
10.1.123.1
10.1.123.2
GE0/0/1
10.1.123.3
GE0/0/1
Static route to 10.1.1.1/32
The next hop is 10.1.123.1.
Type 5 LSA
10.1.1.1/32
OSPF
Imports the route to OSPF.
1
2
3
Type 5 LSA
10.1.1.1/32
Forwarding Address
Multi-Process
Association with BGP

## Slide 48: Using FA to Solve the Suboptimal Path Problem
When advertising an external route destined for 10.1.1.1/32 in the OSPF area, R2 sets the FA of the corresponding Type 5 LSA to 10.1.123.1, which is the next hop of the external route.
When R3 receives the LSA, it calculates the route to 10.1.1.1/32 and finds that the FA is not 0. Therefore, R3 considers that the next hop to 10.1.1.1/32 is the address specified by the FA, that is, 10.1.123.1.
10.1.1.1/32
R1
R2
R3
R4
GE0/0/1
10.1.123.1
10.1.123.2
GE0/0/1
10.1.123.3
GE0/0/1
Type 5 LSA
10.1.1.1/32
FA=10.1.123.1
Type 5 LSA
10.1.1.1/32
FA=10.1.123.1
OSPF
2
3
Data packets sent to 10.1.1.1/32
Static route to 10.1.1.1/32
The next hop is 10.1.123.1.
1
Imports the route to OSPF.
Forwarding Address
Multi-Process
Association with BGP

## Slide 49: FA Values
When an ASBR imports external routes, if the FA field in the Type 5 LSA is 0, the router considers that the data packets destined for the destination network segment should be sent to the ASBR. If the FA field in a Type 5 LSA is not 0, the router considers that the data packet destined for the destination network segment should be sent to the device identified by the FA.
The FA field can be set to a non-zero value only when all the following conditions are met:
  The ASBR activates OSPF on the interface (outbound interface of the external route) connected to the external network.
  The preceding interface is not configured as a silent interface.
  The OSPF network type of such an interface is broadcast or NBMA.
  The IP address of the interface is within the network segment specified by the network command in the OSPF configuration.
  The route to the FA must be an OSPF intra-area route or an inter-area route. In this manner, the router that receives the external LSA can add the LSA into the routing table. The next hop of the route generated using the loaded external LSA is the same as the next hop to the FA.
Forwarding Address
Multi-Process
Association with BGP
Notes: Type 7 LSAs in an NSSA are translated into Type 5 LSAs.
  To advertise external routes imported by an NSSA to other areas, Type 7 LSAs must be translated into Type 5 LSAs. By default, the translator is the ABR with the largest router ID in an NSSA.
  The propagate bit (P-bit) in the Options field of an LSA header is used to notify a translator whether the Type 7 LSA needs to be translated into a Type 5 LSA. A Type 7 LSA can be translated into a Type 5 LSA only when the P-bit is set to 1 and the FA is not 0.
  The P-bit is not set for Type 7 LSAs generated by an ABR.
Note: All OSPF LSAs have the same LSA header, and the P-bit is in the Options field of the LSA header.

## Slide 50: Case: Typical FA Application in NSSA Scenarios
When multiple ABRs exist in an NSSA, the system automatically selects an ABR as a translator to translate Type 7 LSAs into Type 5 LSAs. Other ABRs do not perform LSA translation.
As shown in the figure, if the FA is not considered, R1 considers that the packet must pass through the ABR (R3) to reach the destination because the router ID of R3 is greater than that of R2. In this way, traffic is diverted to the low-bandwidth link R1 -> R3 -> R4 -> R5.
R1
Router ID 10.1.3.3
R3
R2
Router ID 10.1.2.2
R4
R5
10.1.45.5
Type 7 LSA
10.1.5.0/24
FA=10.1.45.5
Type 5 LSA
10.1.5.0/24
FA=10.1.45.5
Low-bandwidth link
Low-bandwidth link
High-bandwidth link
High-bandwidth link
Data sent to 10.1.5.0/24
Route transfer
10.1.5.0/24
Type 7 to Type 5
After the FA is introduced, traffic is transmitted to the destination network segment through a high-bandwidth link.
NSSA
Area 0
Import direct external routes.
Path without the FA used
Path with the FA used
Type7 LSA
10.1.5.0/24
FA=10.1.45.5
Forwarding Address
Multi-Process
Association with BGP
Notes: As shown in the figure:
  Configure R5 to import direct external routes and set the IP address of the FA to 10.1.45.5, which is used by R5 to access the destination network segment 10.1.5.0/24.
  R3 translates Type 7 LSAs into Type 5 LSAs and the LSAs continue to carry the FA 10.1.45.5.
  Upon receipt, R1 searches its OSPF routing table for a route to the FA and uses the next hop address of the route as the next hop address of the external route.
  Therefore, R1 will finally access the destination network segment 10.1.5.0/24 through the path R1 -> R2 -> R4 -> R5.

## Slide 51
OSPF fast convergence
OSPF Route Control
Other OSPF Features
Advanced IS-IS Features

## Slide 52: Overview of IS-IS Fast Convergence
IS-IS fast convergence is an extended feature designed to speed up route convergence. It provides a series of functions, covering incremental SPF (I-SPF), PRC, intelligent timer, and LSP fast flooding.
IS-IS supports fast convergence after a fault is rectified. For example, IS-IS auto FRR can be used to quickly switch traffic to a backup link, and IS-IS can be associated with BFD to quickly detect faults.
Fast Convergence
Route Control
Other Features
Notes: The functions, including PRC, intelligent timer, and FRR, of IS-IS are similar to those of OSPF and therefore not detailed here.

## Slide 53: I-SPF
I-SPF implementation: When the network topology changes, I-SPF recalculates routes only for affected nodes instead of all nodes, speeding up route calculation.
In route calculation, a node represents a router, and a leaf represents a route. I-SPF processes the information of only changed nodes.
R1 (root)
R2
R3
R4
R5
Scenario description:
  On an IS-IS network, an SPT with R1 as the root is calculated after route convergence, as shown in the left figure. When R1 accesses R5, the traffic of R1 is forwarded to R5 based on [the outbound interface of R1's downlink and the IP address of the inbound interface of R3's uplink].
  R6 is added as a downstream device of R5. IS-IS is enabled on R6, meaning that there is a new network node on the IS-IS network.
I-SPF calculation:
  R5 and R6 both flood LSPs carrying information about their neighbor relationship on the entire network.
  After receiving such an LSP, R1 performs I-SPF calculation only for R5 and R6 to generate a new SPT.
  Therefore, when R1 accesses R5 and R6, the traffic of R1 is forwarded to R5 and R6 based on [the outbound interface of R1's downlink and the IP address of the inbound interface of R3's uplink].
R6 (new)
Fast Convergence
Route Control
Other Features
Notes: SPF for route calculation: If a node on a network changes, SPF recalculates routes for all the nodes on the network, which takes a long time, consumes a large number of CPU resources, and consequently reduces the network-wide convergence speed.
I-SPF is an improvement of SPF. Unlike SPF that calculates all nodes, I-SPF calculates only affected nodes. The SPT generated using I-SPF is the same as that generated using SPF. This significantly decreases CPU usage and speeds up network convergence.
I-SPF and PRC are used together on an IS-IS network.
  If the SPT calculated by I-SPF changes, PRC processes all the leaves (routes) of only the changed node.
  If the SPT calculated by I-SPF does not change, PRC processes only the changed leaves (routes). For example, if IS-IS is newly enabled on an interface of a node, the SPT on the network remains unchanged. In this case, PRC updates only the routes of this interface, which consumes less CPU resources.

## Slide 54: LSP Fast Flooding
LSP fast flooding: speeds up the flooding of LSPs.
  Generally, when an IS-IS router receives new or updated LSPs from other routers, it updates the local LSDB and periodically floods the involved LSPs.
  LSP fast flooding speeds up LSDB synchronization because it allows a device to flood a number of LSPs (not exceeding the upper limit) before route calculation when the device receives one or more new or updated LSPs. This flooding mode significantly speeds up the network-wide convergence speed.
  Enable LSP fast flooding.
[Huawei-isis-1] flash-flood [ lsp-count | max-timer-interval interval | [ level-1 | level-2 ] ]
Note: You can specify the maximum number of LSPs to be flooded at a time. Once specified, the number takes effect on all IS-IS interfaces. The actual number of LSPs that can be sent at a time is limited to the number specified by lsp-count.
Fast Convergence
Route Control
Other Features
Notes: Command: [Huawei-isis-1] flash-flood [ lsp-count | max-timer-interval interval | [ level-1 | level-2 ] ]
  lsp-count: specifies the maximum number of LSPs that can be flooded on each interface at a time. The value is an integer ranging from 1 to 15. The default value is 5.
  max-timer-interval interval: specifies the maximum interval at which LSPs are flooded. The value is an integer ranging from 10 to 50000, in milliseconds. The default value is 10.
  level-1: enables the LSP flash-flood function in the Level-1 area. If no level is specified in the command, this function is enabled in both Level-1 and Level-2 areas.
  level-2: enables the LSP flash-flood function in the Level-2 area. If no level is specified in the command, this function is enabled in both Level-1 and Level-2 areas.

## Slide 55: Overview of IS-IS Route Control
In real-world applications, IS-IS routes calculated using SPF sometimes cannot meet network planning and traffic management requirements, which may lead to various problems, such as slow table lookup due to a large number of routing entries in routing tables and unbalanced link usage on a network. To optimize IS-IS networks and facilitate traffic management, more precise route control is required. You can use any of the following methods to implement the control:
  Adjusting the IS-IS preference
  Adjusting the IS-IS interface cost
  Configuring equal-cost routes
  Configuring IS-IS route leaking
  Configuring default route advertisement
  Importing external routes
  Configuring filter-policies
Fast Convergence
Route Control
Other Features
Notes: This course involves only equal-cost and default routes. For details about other control methods, see HCIP-Datacom-Core Technology.

## Slide 56: Equal-Cost Route
If there are multiple redundant links on an IS-IS network, multiple equal-cost routes to the same destination may exist. In this case, you can use either of the following methods to configure equal-cost routes:
  Configure load balancing so that traffic is evenly distributed to relevant links.
    This method improves link utilization and reduces the possibility of congestion caused by overloaded links. However, because traffic will be randomly forwarded, this method may make traffic management difficult.
  Configure a preference for each equal-cost route so that the route with the highest preference is preferentially selected and the others function as backups.
    This method is used to specify the preferred route among multiple equal-cost routes, without the need to modify original configurations. It facilitates traffic management and improves network reliability.
    Note: After preferences are configured for equal-cost routes, IS-IS devices forward traffic to the next hop with the highest preference, instead of forwarding traffic in load balancing mode.
Fast Convergence
Route Control
Other Features

## Slide 57: Configuration of Equal-Cost IS-IS Routes
If the number of equal-cost routes is greater than the number specified using the maximum load-balancing command, routes are selected for load balancing according to the following rules in sequence:
  Route preference: Routes with smaller preference values (higher preferences) are selected for load balancing.
  Next-hop system ID: If all equal-cost routes have the same preference, routes with smaller next-hop system IDs are selected for load balancing.
  Local outbound interface index: If all equal-cost routes have the same preference and next-hop system ID, routes with smaller local outbound interface indexes are selected for load balancing.
[Huawei-isis-1] maximum load-balancing number
Configure load balancing among equal-cost IS-IS routes.
Configure the maximum number of equal-cost routes that participate in load balancing.
[Huawei-isis-1] nexthop ip-address weight value
Configure preferences for equal-cost IS-IS routes.
By default, no preferences are configured for equal-cost IS-IS routes. A smaller value indicates a higher preference.
Fast Convergence
Route Control
Other Features
Notes: Command: [Huawei-isis-1] maximum load-balancing number
  number: specifies the maximum number of equal-cost routes that participate in load balancing. The value varies according to the device model.
Command: [Huawei-isis-1] nexthop ip-address weight value
  ip-address: specifies the IP address of the next hop. The value is in dotted decimal notation.
  weight value: specifies the weight of the next hop. A smaller value indicates a higher preference. The value is an integer ranging from 1 to 254.

## Slide 58: Example for Configuring Equal-Cost Routes (1)
On the network shown in the figure, IS-IS runs on R1, R2, and R3. It is required that R1 be able to access the loopback interface address of R3 through path R1 -> R3 or R1 -> R2 -> R3.
IS-IS
R1
Cost=10
Cost=5
Cost=5
R3
GE0/0/0
GE0/0/1
GE0/0/2
R2
Device | Interface | IP Address
R1 | GE0/0/0 | 10.1.13.1/24
 | GE0/0/1 | 10.1.12.1/24
R2 | GE0/0/1 | 10.1.12.2/24
 | GE0/0/2 | 10.1.23.2/24
R3 | Loopback0 | 10.1.3.3/32
 | GE0/0/0 | 10.1.13.3/24
 | GE0/0/2 | 10.1.23.3/24
1. Assign IP addresses to device interfaces and configure IS-IS on each device. (Omitted)
[R1] isis
[R1-isis-1] maximum load-balancing 2
2. Configure the number of IS-IS equal-cost routes for load balancing on R1.
[R1]display ip routing-table
Route Flags: R - relay, D - download to fib
-------------------------------------------------------------------------------------------
Destination/Mask Proto Pre Cost Flags NextHop Interface
10.1.3.3/32 ISIS-L2 15 10 D 10.1.13.3 GigabitEthernet0/0/0
ISIS-L2 15 10 D 10.1.12.2 GigabitEthernet0/0/1
3. Verify the configuration.
Fast Convergence
Route Control
Other Features

## Slide 59: Example for Configuring Equal-Cost Routes (2)
On the network shown in the figure, IS-IS runs on R1, R2, and R3. It is required that R1 access the loopback interface address of R3 preferentially through path R1 -> R3.
1. Assign IP addresses to device interfaces and configure IS-IS on each device. (Omitted)
[R1] isis
[R1-isis-1] nexthop 10.1.13.3 weight 1
[R1-isis-1] nexthop 10.1.12.2 weight 2
2. (Optional) Configure preference for equal-cost routes on R1.
3. Verify the configuration.
[R1]display ip routing-table
Route Flags: R - relay, D - download to fib
-------------------------------------------------------------------------------------------
Destination/Mask Proto Pre Cost Flags NextHop Interface
10.1.3.3/32 ISIS-L2 15 10 D 10.1.13.3 GigabitEthernet0/0/0
IS-IS
R1
Cost=10
Cost=5
Cost=5
R3
GE0/0/0
GE0/0/1
GE0/0/2
R2
Device | Interface | IP Address
R1 | GE0/0/0 | 10.1.13.1/24
 | GE0/0/1 | 10.1.12.1/24
R2 | GE0/0/1 | 10.1.12.2/24
 | GE0/0/2 | 10.1.23.2/24
R3 | Loopback0 | 10.1.3.3/32
 | GE0/0/0 | 10.1.13.3/24
 | GE0/0/2 | 10.1.23.3/24
Fast Convergence
Route Control
Other Features

## Slide 60: Default Route
IS-IS allows you to control the generation and advertisement of default routes using the following methods:
  On Level-1-2 devices, configure a rule for setting the attached (ATT) bit in Level-1 LSPs.
  Configure Level-1 devices not to automatically generate default routes even if they receive Level-1 LSPs with the ATT bit set to 1.
  Configure devices to advertise default routes to the IS-IS routing domain.
LSP packet format:
  The ATT bit is generated by a Level-1-2 router to identify whether the originating router connects to other areas. Note that the ATT field has four bits, and Huawei datacom products use only one of the four bits.
PDU Common Header
PDU Specific Header
Variable Length Fields (TLV)
PDU Length |  |  | 
Remaining Lifetime |  |  | 
LSP ID |  |  | 
Sequence Number |  |  | 
Checksum |  |  | 
P | ATT | OL | IS Type
Fast Convergence
Route Control
Other Features

## Slide 61: Setting the ATT Bit to Control the Generation of Default Routes
In IS-IS, if a Level-1-2 device determines based on LSDB information that it can reach more areas through a Level-2 area than through a Level-1 area, the device sets the ATT bit to 1 in Level-1 LSPs before advertising these LSPs. Upon receipt, Level-1 devices generate default routes destined for this Level-1-2 device.
The preceding rules are applied by default. The ATT bit can be set as required on a live network.
[Huawei-isis-1] attached-bit advertise { always | never }
(Level-1-2 device) Configure a rule for setting the ATT bit in LSPs.
By default, the Level-1-2 device sets the ATT bit in LSPs following the default rules.
[Huawei-isis-1] attached-bit avoid-learning
(Level-1 device) Configure the device not to generate a default route after it receives LSPs carrying ATT bit 1.
By default, a Level-1 device generates a default route after it receives LSPs carrying ATT bit 1.
Fast Convergence
Route Control
Other Features
Notes: Command: [Huawei-isis-1] attached-bit advertise { always | never }
  always: indicates that the ATT bit is set to 1. After receiving an LSP with ATT bit 1, a Level-1 device generates a default route.
  never: indicates that the ATT bit is set to 0. This prevents the Level-1 device from generating default routes and reduces the size of the routing table.
Although the ATT bit is defined in both Level-1 and Level-2 LSPs, it is set to 1 only in Level-1 LSPs advertised by Level-1-2 devices. Therefore, this command takes effect only on Level-1-2 devices.
To prevent Level-1 devices from advertising default routes to their routing tables, perform either of the following operations:
  Run the attached-bit advertise never command on Level-1-2 devices to disable them from advertising LSPs with ATT bit 1.
  Run the attached-bit avoid-learning command on Level-1 devices that connect to Level-1-2 devices.
The difference between the preceding commands lies in that the attached-bit avoid-learning command applies to specified Level-1 devices.

## Slide 62: Configuring Devices to Advertise Default Routes to the IS-IS Routing Domain
After the default-route-advertise command is run on a boundary device in the IS-IS domain, the device advertises default route 0.0.0.0/0 to the IS-IS routing domain. After that, all traffic destined for other routing domains is forwarded to this boundary device first, and the device then forwards the traffic outside the IS-IS routing domain.
Generally, if other routing protocols are configured in addition to IS-IS, use the following two methods to forward traffic in the IS-IS routing domain to other routing domains:
  Configure boundary devices to advertise default routes to the IS-IS routing domain. This method is simple and does not require external route learning.
  Configure boundary devices to import routes of other routing protocols into IS-IS.
[Huawei-isis-1] default-route-advertise [ always | match default | route-policy route-policy-name ] [ cost cost | tag tag | [ level-1 | level-1-2 | level-2 ] ] [ avoid-learning ]
Configure an IS-IS device to generate a default route.
By default, an IS-IS device does not generate the default route.
Fast Convergence
Route Control
Other Features
Notes: Command: [Huawei-isis-1] default-route-advertise [ always | match default | route-policy route-policy-name ] [ cost cost | tag tag | [ level-1 | level-1-2 | level-2 ] ] [ avoid-learning ]
  always: configures an IS-IS device to unconditionally advertise the default route and set itself as the next hop in the route.
  match default: advertises the default route generated by another routing protocol or IS-IS process through LSPs if such a route already exists in the routing table.
  route-policy route-policy-name: specifies the name of the route-policy. A Level-1-2 device advertises the default route to the IS-IS routing domain only when external routes matching the route-policy exist in the routing table of the device. This prevents routing blackholes caused by the advertisement of the default route when link faults make some important external routes unavailable. This route-policy does not affect the import of external routes into IS-IS. The value is a string of 1 to 40 case-sensitive characters, spaces not supported. If spaces are used, the string must start and end with double quotation marks (").
  cost cost: specifies the cost of the default route. The value is an integer. The value range depends on cost-style. When cost-style is narrow, narrow-compatible, or compatible, the value ranges from 0 to 63. When cost-style is wide or wide-compatible, the value ranges from 0 to 4261412864.

## Slide 63
Notes:   tag tag: specifies the tag value of the default route to be advertised. The advertised LSPs carry the tag value only when the IS-IS cost type is wide, wide-compatible, or compatible. The value is an integer ranging from 1 to 4294967295.
  level-1: sets the level of the default route to be advertised to Level-1. If the level is not specified, a Level-2 default route is generated by default.
  level-2: sets the level of the default route to be advertised to Level-2. If the level is not specified, a Level-2 default route is generated by default.
  level-1-2: sets the level of the default route to be advertised to Level-1-2. If the level is not specified, a Level-2 default route is generated by default.
  avoid-learning: prevents an IS-IS process from learning default routes or adding them to the routing table. If a default route exists in the routing table and is in the active state, set the route to inactive.
After this command is run on a device, all traffic in the IS-IS routing domain will be forwarded by this device to a destination outside the domain. Compared with configuring a static default route on each router in an IS-IS routing domain, running this command simplifies configurations, because this command only needs to be run on boundary routers in the IS-IS routing domain. In addition, the default-route-advertise command enables dynamic default route advertisement, and you can specify different parameters to allow the default route to be advertised in different ways.
If this command is run on a Level-1 device, the device advertises the default route only to the Level-1 area.

## Slide 64: Example for Configuring Default Routes
OSPF
As shown in the figure, OSPF runs on GE0/0/1 and Loopback0 of R1 and GE0/0/1 of R2, and IS-IS runs on GE0/0/2 of R2 and R3.
To enable R3 to access the OSPF network, configure R2 to advertise the default route to the IS-IS routing domain.
Similarly, R2 also needs to advertise the default route to the OSPF routing domain.
IS-IS
R1
R2 L2
R3 L2
GE0/0/1
GE0/0/2
10.1.12.0/24
10.1.23.0/24
Loopback0:
10.1.1.1/32
1. Assign an IP address to each interface and configure OSPF/IS-IS on each device.
[R2] isis
[R2-isis-1] default-route-advertise always
2. Configure R2 to advertise the default route to the IS-IS routing domain.
[R2] ospf
[R2-ospf-1] default-route-advertise always
3. Configure R2 to advertise the default route to the OSPF routing domain.
[R3]display ip routing-table
Route Flags: R - relay, D - download to fib
---------------------------------------------------------------------------------------
Routing Tables: Public
Destinations : 8 Routes : 8
Destination/Mask Proto Pre Cost Flags NextHop Interface
0.0.0.0/0 ISIS-L2 15 10 D 10.1.23.2 GigabitEthernet0/0/2
…
4. Check routing entries on R3.
Fast Convergence
Route Control
Other Features

## Slide 65: IS-IS Multi-Instance and Multi-Process
In IS-IS multi-instance, multiple IS-IS processes are created on the same router, with each process associated with one VPN instance.
In IS-IS multi-process, multiple IS-IS processes are created in the same VPN instance (or in the same public network instance). These IS-IS processes are independent of each other. IS-IS processes function similarly to different routing protocols in route exchange.
A network may carry different services, which need to be isolated for security. You can bind each IS-IS process to a different VPN instance.
VPN1
Site1
CE1
VPN2
Site2
CE2
PE
isis 100 VPN1
Isis 200 VPN2
Application scenarios:
  IS-IS multi-instance and multi-process are typically used in VPN scenarios.
  As the figure shown, a PE is connected to two VPNs, each belonging to a different customer, and IS-IS is deployed between the PE and CEs. You can configure multiple IS-IS processes on the PE to isolate the VPN customers.
[PE] isis 100 vpn-instance VPN1
[PE-isis-100] quit
[PE] isis 200 vpn-instance VPN2
[PE-isis-200] quit
Fast Convergence
Route Control
Other Features
Notes: IS-IS multi-process and multi-instance have the following characteristics:
  In IS-IS multi-process, processes share the same global routing table. IS-IS multi-instance, however, uses the routing tables of VPNs, with each VPN having a separate routing table.
  IS-IS multi-process allows a set of interfaces to be associated with a specified IS-IS process. This ensures that the protocol operations in the specified IS-IS process are confined only to this set of interfaces. In this way, multiple IS-IS processes can work on a single router, with each process responsible for a unique set of interfaces.
  When creating an IS-IS process, you can bind it to a VPN instance. The IS-IS process then accepts and processes only the events related to the VPN instance. When the bound VPN instance is deleted, the IS-IS process is also deleted.
Command: [Huawei] isis [ process-id ] [ vpn-instance vpn-instance-name ]
  process-id: specifies the ID of an IS-IS process. If no IS-IS process is specified, IS-IS process 1 is started. The value is an integer ranging from 1 to 65535. The default value is 1.
  vpn-instance vpn-instance-name: specifies the name of a VPN instance. If this parameter is not specified, no VPN instance is associated with the IS-IS process. The value is a string of 1 to 31 case-sensitive characters. If spaces are used, the string must start and end with double quotation marks (").

## Slide 66: LSP Fragment
When a PDU to be advertised by IS-IS contains too much information, an IS-IS router generates LSP fragments to carry the information.
LSP packet format
An IS-IS LSP fragment is identified by the 1-byte LSP Number field in LSP ID. So, an IS-IS process can generate a maximum of 256 LSP fragments, which means only limited information can be carried.
PDU Common Header
PDU Specific Header
Variable Length Fields (TLV)
PDU Length |  |  | 
Remaining Lifetime |  |  | 
LSP ID |  |  | 
Sequence Number |  |  | 
Checksum |  |  | 
P | ATT | OL | IS Type
System ID (6 bytes)
Pseudonode ID (1 byte)
LSP Number (1 byte)
Fast Convergence
Route Control
Other Features

## Slide 67: Basic Concepts of LSP Fragment Extension
You can configure a virtual system ID for IS-IS to generate virtual IS-IS LSPs to carry routing information.
  Originating system: a router that actually runs IS-IS. A single IS-IS process can advertise LSPs like multiple virtual routers, and the originating system refers to the "actual" (not virtual) IS-IS process.
  Normal system ID: system ID of the originating system.
  Virtual system: system identified by an additional system ID to generate extended LSP fragments. These fragments carry additional system IDs in their LSP IDs.
  Additional system ID: system ID of a virtual system. It is assigned by a network administrator to identify a virtual system. A maximum of 256 extended LSP fragments can be generated for each additional system ID.
  TLV 24 (IS Alias ID TLV): carried in LSP fragments and describes the relationship between the originating and virtual systems.
After LSP fragment extension is configured, the system prompts you to restart the IS-IS process if information is lost because LSPs overflow. After the IS-IS process is restarted, the originating system loads as much routing information as possible to its LSPs. The information that cannot be loaded is placed in the LSPs of virtual systems for transmission. The originating system then notifies other routers of its relationship with the virtual systems through TLV 24.
Type=24
Length
Value: Normal System-ID
Fast Convergence
Route Control
Other Features
Notes: The additional and normal system IDs must be unique throughout a routing domain.

## Slide 68: Implementation of LSP Fragment Extension
In IS-IS, each normal system ID identifies a system, which can generate a maximum of 256 LSP fragments. With additional system IDs, up to 50 virtual systems can be configured, and an IS-IS process can then generate a maximum of 13,056 LSP fragments.
LSP fragment extension can work in two modes.
Mode-1
Used when some routers on the network do not support LSP fragment extension.
As the figure shown, R1 loads some routing information to the LSPs of R1-1 and R1-2 for transmission. When R2 receives the LSPs from R1, R1-1, and R1-2, it considers that there are three independent routers at the peer end and calculates routes as normal. The costs of the routes from R1 to R1-1 and from R1 to R1-2 are both 0, meaning that the routes from R2 to R1 and from R2 to R1-1/R1-2 share the same cost.
Mode-2
Used when all the routers on the network support LSP fragment extension.
As the figure shown, R1 loads some routing information to the LSPs of R1-1 and R1-2 for transmission. When R2 receives LSPs from R1-1 and R1-2, it knows that their originating system is R1 based on TLV 24. R2 then considers information advertised by R1-1 and R1-2 as information of R1.
R2
Does not support LSP fragment extension.
R1
R1-1
R1 virtual system
R1-2
R1 virtual system
LSP
LSP-1
LSP-2
R2
R1
R1-1
R1 virtual system
R1-2
R1 virtual system
LSP
LSP-1
LSP-2
Calculates routes separately for the received LSP-1 and LSP-2.
Considers received LSP-1 and LSP-2 both the routing information of R1 and calculates routes uniformly.
Fast Convergence
Route Control
Other Features
Notes: Mode-1 implementation:
  Virtual systems participate in SPF calculation. The LSPs advertised by the originating system contain information about links to each virtual system. Similarly, the LSPs advertised by each virtual system contain information about links to the originating system. In this way, virtual systems function like physical routers that connect to the originating system.
  Mode-1 is a transitional mode used to support earlier versions that are incapable of LSP fragment extension. In these earlier versions, IS-IS cannot identify TLV 24. As a result, the LSPs sent by a virtual system must look like LSPs sent by an originating system.
  Precautions:
    The LSPs sent by a virtual system must contain the same area address and overload bit as those in LSPs sent by an originating system. Other TLVs must also be the same.
    The neighbor of a virtual system must point to an originating system, and the metric is the maximum value minus 1. The neighbor of the originating system must point to the virtual system, and the metric must be 0. This ensures that the virtual system is the downstream node of the originating system when other routers calculate routes.

## Slide 69
Notes: Mode-2 implementation:
  Virtual systems do not participate in SPF calculation. All the routers on the network know that the LSPs generated by the virtual systems actually belong to the originating system.
  IS-IS working in mode-2 can identify TLV 24, which is used as the basis for calculating an SPT and routes.
Note: In both modes, the originating system and virtual systems must include TLV 24 in their LSPs whose LSP Number is 0 to indicate which is the originating system.

## Slide 70: Basic Configuration Commands of LSP Fragment Extension
Note: The preceding two commands must be used together. The configured virtual system ID takes effect only after LSP fragment extension is enabled and the IS-IS process is restarted using the reset isis all command.
[Huawei-isis-1] lsp-fragments-extend [ [ level-1 | level-2 | level-1-2 ] | [ mode-1 | mode-2 ] ]
Enable LSP fragment extension for an IS-IS process.
By default, LSP fragment extension is disabled for IS-IS processes.
If no mode or level is specified during the configuration of LSP fragment extension, mode-1 and level-1-2 are used by default.
[Huawei-isis-1] virtual-system virtual-system-id
Configure a virtual system.
By default, no virtual system is configured.
To enable a device to generate extended LSP fragments, you must configure at least one virtual system ID. This ID must be unique throughout a routing domain.
An IS-IS process can be configured with up to 50 virtual system IDs.
Fast Convergence
Route Control
Other Features
Notes: Command: [Huawei-isis-1] lsp-fragments-extend [ [ level-1 | level-2 | level-1-2 ] | [ mode-1 | mode-2 ] ]
  level-1: enables LSP fragment extension in Level-1.
  level-2: enables LSP fragment extension in Level-2.
  level-1-2: enables LSP fragment extension in Level-1-2.
  mode-1: allows routers to be compatible with other routers running earlier versions that are incapable of LSP fragment extension.
  mode-2: requires all routers to support LSP fragment extension.
Command: [Huawei-isis-1] virtual-system virtual-system-id
  virtual-system-id: specifies a virtual system ID of an IS-IS process. The length is 6 bytes (48 bits), and the format is XXXX.XXXX.XXXX.

## Slide 71
(Multiple) Which of the following fast convergence mechanisms are supported by OSPF? ( )
  I-SPF
  LSP fast flooding
  Intelligent timer
  OSPF IP FRR
(TorF) The FA field in Type 5 LSAs of OSPF must be 0.0.0.0. ( )
  True
  False
(TorF) On an IS-IS network, if a device runs mode-2 LSP fragment extension, virtual systems do not participate in SPF calculation. All routers on the network know that the LSPs generated by the virtual systems actually belong to the originating system. ( )
  True
  False
Notes: CD
B
A

## Slide 72
To better adapt to network topology changes, OSPF and IS-IS support multiple fast convergence modes. I-SPF and PRC algorithm speed up route calculation; FRR enables fast traffic switching to the backup link; and intelligent timers allow you to control the speeds at which link state information is generated and routes are calculated.
To control the size of routing tables and improve network performance, OSPF and IS-IS support route filtering, equal-cost routes, and default routes.
To isolate protocol routing tables, OSPF and IS-IS support multi-process deployment on the same device. Protocol routing tables of different processes do not affect each other.
To prevent a sub-optimal route from being selected when external routes are imported, OSPF uses the FA in Type 5 or Type 7 LSAs to guide data packet forwarding.
To carry more routing information, IS-IS provides LSP fragment extension.
Thanks to the preceding features, OSPF and IS-IS are widely and flexibly used on live networks.