## Slide 1
Update
Update
Update
Update
Lu Yueyue/lwx445705
2020.6
New
Update

## Slide 2: Advanced BGP Features

## Slide 3
Border Gateway Protocol (BGP) is usually deployed on large-scale networks. Compared with an Interior Gateway Protocol (IGP), BGP has more flexible route control capabilities. Each BGP route can carry multiple path attributes. Special route matching tools, such as AS_Path and community filters, are available for matching the route attributes. Routing policies can be used to control route advertisement and acceptance according to the actual networking requirements.
In addition, BGP provides various advanced features and networking deployment solutions to improve network performance.
This course describes the fundamentals and configurations of BGP route control, common advanced BGP features, such as ORF, peer group, and security, as well as the networking modes of BGP route reflectors (RRs).

## Slide 4
On completion of this course, you will be able to:
  Use regular expressions during the configurations of AS_Path and community filters.
  Use AS_Path and community filters to control BGP routes.
  Apply the ORF and peer group functions of BGP.
  Perform basic configurations of BGP security.
  Learn about the networking modes of BGP RRs.

## Slide 5
BGP Route Control
Introduction to BGP Features
Networking Modes of BGP RRs

## Slide 6: Overview of BGP Route Control
BGP route control involves controlling the advertisement and acceptance of routes.
AS 102
AS 101
R1
Net1
Net2
Net3
R2
R3
R4
BGP routing table
*> Net1
*> Net3
BGP routing table
*> Net1
*> Net2
*> Net3
BGP routing table
*> Net1
*> Net3 (R4 is preferred as the egress)
BGP routing table
*> Net1 (R3 is preferred as the egress)
*> Net3
Filter out the Net2 route.
Modify the attributes of the Net1 and Net3 routes to control route selection.
Modify the attributes of the Net1 and Net3 routes to control route selection.
Route
Route
Route
Generally, BGP route control is implemented using routing policies. Specifically, a route matching tool is used to match specific routes, and then a routing policy tool is used to control route advertisement and acceptance.
  Route matching tools: access control list (ACL), IP prefix list, AS_Path filter, and community filter
  Routing policy tools: filter-policy and route-policy
BGP route control usually affects the AS_Path and community attributes.
Overview
AS_Path Filter
Community Filter
Notes: As shown in the figure:
  R1 and R2 reside in AS 101, and establish an IBGP peer relationship with each other. R3 and R4 reside in AS 102, and each establishes an EBGP peer relationship with R2.
  R1 is directly connected to three network segments: Net1, Net2, and Net3. R1 advertises routes to the three network segments to its BGP routing table.
  R2 can filter out the Net2 route through BGP route control so that R2's BGP routing table does not contain the Net2 route.
  R3 and R4 can implement BGP route control by modifying the attributes of the Net1 and Net3 routes, respectively. In this way, when a device in AS 102 accesses Net1, R3 is preferentially selected as the egress device; when the device accesses Net3, R4 is preferentially selected as the egress device.
Note: For details about the ACL, IP prefix list, filter-policy, route-policy, and BGP path attributes, see the "HCIP-Datacom-Core Technology" course.

## Slide 7: Regular Expression
A regular expression (regex) is a formula used to match character strings based on a specific template. It consists of common characters (for example, letters from a to z) and special characters.
Common characters are used to match themselves in a string:
  Include all upper-case and lower-case letters, digits, punctuations, and special symbols.
  For example, the regex a matches the letter "a" in "abc", the regex 10 matches the digits "10" in "10.113.25.155", and the regex @ matches the symbol "@" in "xxx@xxx.com".
Special characters, together with common characters, are used to match complex or special character strings:
  A special character that precedes or follows a common character is used to restrict or extend the independent control character or placeholder of the common character.
  A special character describes how the character that precedes the special character is reused.
  A special character specifies a complete range.
Overview
AS_Path Filter
Community Filter
Notes: A regex has the following functions:
  Checks and obtains the sub-character string that matches a specific rule in the character string.
  Replaces the character string based on matching rules.

## Slide 8: Example of Special Characters (1)
Type 1
. | Matches any single character, including a space. | 0.0 matches 0x0, 020, and so on.
^ | Matches the start position of a character string. | ^10 matches 10.1.1.1 but not 20.1.1.1.
$ | Matches the end position of a character string. | 1$ matches 10.1.1.1 but not 10.1.1.2.
_ | Underscore, which matches any separator. Matches a comma (,), left brace ({), right brace (}), left parenthesis ((), or right parenthesis ()). (Same as ^) Matches the start position of an input character string. (Same as $) Matches the end position of an input character string. Matches a space. | _10 matches (10, {10, space10, and so on. 10_ matches 10), 10}, 10space, and so on.
¦ | Pipeline character, which is a logical OR operator. x¦y matches x or y. | 100¦200 matches 100 or 200.
\ | Defines an escape character, which is used to mark the next character (common or special character) as a common character. | \* matches *.
* | Matches a sub-regular expression that it follows zero or multiple times. | 10* matches 1, 10, 100, 1000, and so on. | (10) * matches null, 10, 1010, 101010, and so on.
+ | Matches a sub-regular expression that it follows once or multiple times. | 10+ matches 10, 100, 1000, and so on. | (10)+ matches null, 10, 1010, 101010, and so on.
? | Matches a sub-regular expression that it follows zero times or once. | 10? matches 1 or 10. | (10)? matches null or 10.
Type 2
Overview
AS_Path Filter
Community Filter
Notes: Note: The parentheses () can be used to define the scope and priority of an operator. For example, gr(a|e)y is equivalent to gray|grey.

## Slide 9: Example of Special Characters (2)
Type 3
[xyz] | Matches any character contained in a regex. | [123] matches the character 2 in 255.
[^xyz] | Matches any character that is not contained in a regex. | [^123] matches any character except 1, 2, and 3.
[a-z] | Matches any character within a specified range in a regex. | [0-9] matches all digits in the range from 0 to 9.
[^a-z] | Matches any character beyond the range specified in a regex. | [^0-9] matches all non-digit characters (matching any characters except digits 0 to 9).
Think about character strings that can be matched against the regexes of the following types.
  Type 1 Type 2 Type 3
^a.$
^100_
^100$
100$|400$
^\(65000\)$
abc*d
abc+d
abc?d
a(bc)?d
[abcd]
[a-c 1-2]$
[^act]$
[123].[7-9]
Overview
AS_Path Filter
Community Filter
Notes: Quiz:
Type 1:
  ^a.$: matches a character string that starts with the character a and ends with any single character, for example, a0, a!, ax, and so on.
  ^100_: matches a character string starting with 100, for example, 100, 100 200, 100 300 400, and so on.
  ^100$: matches only 100.
  100$|400$: matches a character string ending with 100 or 400, for example, 100, 1400, 300 400, and so on.
  ^\(65000\)$: matches (65000) only.
Type 2:
  abc*d: matches the character c zero or multiple times, for example, abd, abcd, abccd, abcccd, abccccdef, and so on.
  abc+d: matches the character c once or multiple times, for example, abcd, abccd, abcccd, abccccdef, and so on.
  abc?d: matches the character c zero times or once, for example, abd, abcd, abcdef, and so on.
  a(bc)?d: matches the character string bc zero times or once, for example, ad, abcd, aaabcdef, and so on.
Type 3:
  [abcd]: matches any character in the string abcd, for example, ax, b!, abc, d0, and so on.
  [a-c 1-2]$: matches a character string ending with any of a, b, c, 1, and 2, for example, a, a1, 62, xb, 7ac, and so on.
  [^act]$: matches a character string that does not end with a, c, or t, for example, ax, b!, d, and so on.
  [123].[7-9]: matches the character strings such as 1 7, 2x9, and 348.

## Slide 10: Route Matching Tool: AS_Path Filter
An AS_Path filter uses the AS_Path attribute of BGP routes as a matching condition to filter BGP routes.
If you do not want routes from certain ASs, you can use an AS_Path filter to filter out the routes that carry the associated AS numbers.
AS 104
AS 103
AS 102
AS 101
R1
10.1.1.0/24
R2
10.1.1.0/24
AS_Path = 101
Route
10.1.1.0/24
AS_Path = 102 101
The BGP route originated from AS 101 is filtered out.
Route
Route
Set an AS_Path filter to filter out the BGP route that contains the AS number 101.
Overview
AS_Path Filter
Community Filter
Notes: The AS_Path attribute is a well-known mandatory attribute of BGP. All BGP routes must carry this attribute. This attribute records the numbers of all the ASs that a BGP route traversed during transmission.
The value of the AS_Path attribute can be 0, 1, or a set of multiple AS numbers.

## Slide 11: Using a Regex to Match the AS_Path Attribute
A regex can be used to match the AS_Path attribute of routes.
  For example, a regex can match the AS number 103 in AS_Path = 103 102 101.
You can use different regexes to meet different requirements, for example, using ^101$ to match AS 101, and _101$ to match the AS_Path lists ending with AS 101.
AS 104
Route
10.1.12.0/24 AS_Path = 103 102 101
10.1.15.0/24 AS_Path = 103 105 101
10.1.78.0/24 AS_Path = 103 107 108
...
R1 receives many BGP routes, each of which has its own AS_Path value.
To meet a specific requirement, R1 needs to apply a policy to the routes carrying the AS number 101 in their AS_Path attribute. In this case, you can associate an AS_Path filter with a regex to match routes, regardless of the route prefixes.
R1
AS_Path:
103
102
101
Character string:
103
102
101
Regex:
^103, ^103_, and so on.
Other examples:
Overview
AS_Path Filter
Community Filter
^$ | Matches the AS_Path list that does not contain any AS number, that is, matching routes in the local AS.
.* | Match all or any routes.
^10[012349]$ | Matches the AS numbers 100, 101, 102, 103, 104, and 109.
^10[^0-6]$ | Matches the AS_Path lists that exclude the AS numbers 100 to 106.
^10. | Matches the AS numbers 100 to 109 and 10.
^12(_34)?_56$ | Matches the AS_Path lists 12 56 and 12 34 56.

## Slide 12: Basic AS_Path Filter Configuration Commands
[Huawei] ip as-path-filter { as-path-filter-number | as-path-filter-name } { deny | permit } regular-expression
Create an AS_Path filter.
An AS_Path filter uses a regex to define a matching rule.
Note: The default behavior of an AS_Path filter is deny.
[Huawei-bgp-af-ipv4] peer { group-name | ipv4-address | ipv6-address } as-path-filter { as-path-filter-number | as-path-filter-name } { import | export }
Apply the AS_Path filter.
A routing policy associated with the AS_Path filter is applied to BGP routes in the BGP address family view to filter out the unqualified routes.
[Huawei-route-policy] if-match as-path-filter { as-path-filter-number | as-path-filter-name }
A matching rule based on the AS_Path filter is created in the route-policy view.
Overview
AS_Path Filter
Community Filter
Notes: Multiple matching rules (each in permit or deny mode) can be specified in an AS_Path filter. These rules are in the OR relationship, which means that if a route matches one of the matching rules, the route is considered to match the AS_Path filter.
Command: [Huawei] ip as-path-filter {as-path-filter-number | as-path-filter-name} {deny | permit} regular-expression
  as-path-filter-number: specifies the number of an AS_Path filter. The value is an integer ranging from 1 to 256.
  as-path-filter-name: specifies the name of an AS_Path filter. The value is a string of 1 to 51 case-sensitive characters. It cannot be comprised of only digits. If spaces are used, the string must start and end with double quotation marks (").
  deny: sets the matching mode of the AS_Path filter to deny.
  permit: sets the matching mode of the AS_Path filter to permit.
  regular-expression: specifies a regex for the AS_Path filter. The value is a string of 1 to 255 characters and can contain spaces.
The default behavior of an AS_Path filter is deny. That is, if a route is not permitted in a filtering, the route fails to match the AS_Path filter. If all matching rules in an AS_Path filter work in deny mode, all BGP routes are denied by the filter. To prevent this problem, configure a matching rule in permit mode after one or more matching rules in deny mode so that the routes except for those denied by the preceding matching rules can match the filter.

## Slide 13: Examples for Configuring AS_Path Filters (1)
R2 transmits EBGP routes to R3. Among these routes, some are locally originated by R2, and others are transmitted from AS 101 to R2 and then updated by R2 to R3.
A routing policy is configured on R2 to deny the routes originated from AS 101.
[R2] ip as-path-filter 1 deny _101$
[R2] ip as-path-filter 1 permit .*
1. Create an AS_Path filter.
2. (Direct reference) Apply the AS_Path filter.
The AS_Path filter is configured to filter out the routes originated from AS 101 and permit the other routes.
[R2] bgp 102
[R2-bgp] peer 10.1.23.3 as-number 103
[R2-bgp] ipv4-family unicast
[R2-bgp-af-ipv4] peer 10.1.23.3 as-path-filter 1 export
AS 104
AS 101
AS 102
R1
R2
R4
R3
Route
10.1.34.0/24
.2
.3
Loopback0:
10.1.1.1/32
10.1.12.0/24
.1
.2
.4
.3
10.1.23.0/24
AS 103
Route filtering
Overview
AS_Path Filter
Community Filter

## Slide 14: Examples for Configuring AS_Path Filters (2)
R2 transmits EBGP routes to R3. Among these routes, some are locally originated by R2, and others are transmitted from AS 101 to R2 and then updated by R2 to R3.
A routing policy is configured on R2 to deny the routes originated from AS 101.
1. Create an AS_Path filter.
2. (Through a route-policy) Apply the AS_Path filter.
The AS_Path filter is configured to filter out the routes originated from AS 101 and permit the other routes.
[R2] route-policy AS_Path permit node 10
[R2-route-policy] if-match as-path-filter 1
[R2-route-policy] quit
[R2] bgp 102
[R2-bgp] peer 10.1.23.3 as-number 103
[R2-bgp] ipv4-family unicast
[R2-bgp-af-ipv4] peer 10.1.23.3 route-policy AS_Path export
AS 104
AS 101
AS 102
R1
R2
R4
R3
Route
10.1.34.0/24
.2
.3
Loopback0:
10.1.1.1/32
10.1.12.0/24
.1
.2
.4
.3
10.1.23.0/24
AS 103
Route filtering
Overview
AS_Path Filter
Community Filter
[R2] ip as-path-filter 1 deny _101$
[R2] ip as-path-filter 1 permit .*

## Slide 15: Checking the AS_Path Filter Information
[R2]display ip as-path-filter 1
As path filter number: 2
deny _101$
permit .*
1. Check the AS_Path filter.
2. Check all the routes whose AS_Path lists match the specified regex in the BGP routing table.
[R2]display bgp routing-table regular-expression _101$
Total Number of Routes: 1
BGP Local router ID is 10.1.12.2
Status codes: * - valid, > - best, d - damped,
h - history, i - internal, s - suppressed, S - Stale
Origin : i - IGP, e - EGP, ? - incomplete
Network NextHop MED LocPrf PrefVal Path/Ogn
*> 10.1.1.1/32 10.1.12.1 0 0 101i
AS 104
AS 101
AS 102
AS 103
R1
R2
R4
R3
Route
10.1.34.0/24
.2
.3
Loopback0:
10.1.1.1/32
10.1.12.0/24
.1
.2
.4
.3
10.1.23.0/24
The route 10.1.1.1/32 originated from AS 101 is filtered by the AS_Path filter.
Route filtering
Overview
AS_Path Filter
Community Filter

## Slide 16: Route Matching Tool: Community Filter
AS 102
The community filter and community attribute can be used together to simplify route management when the IP prefix list and AS_Path filter are not available.
There are two types of community filters:
  Basic community filter, which matches the community number or well-known community attribute.
  Advanced community filter, which uses a regex to match the community number.
AS 103
AS 101
R1
10.1.1.0/24
10.1.2.0/24
R2
10.1.1.0/24 with community 101:1
10.1.2.0/24 without the community attribute
Route
Route
Set a community filter to deny the routes whose community value is 101:1.
10.1.2.0/24
The route 10.1.1.0/24 with community 101:1 is filtered out.
R3
Overview
AS_Path Filter
Community Filter
Notes: The community attribute is an optional transitive attribute. It can identify the routes with the same characteristics, regardless of the scattered route prefixes and various AS numbers. That is, a specific community value can be assigned to some routes so that these routes can be matched against the community value instead of the network number or mask. Then, a corresponding routing policy can be applied to the matched routes.

## Slide 17: Community Attributes
Well-known community attributes
Name | Number | Description
Internet | 0 (0x00000000) | After a device receives a route with this attribute, the device can advertise this route to any BGP peer. By default, all routes belong to the Internet community.
No_Advertise | 4294967042 (0xFFFFFF02) | After a device receives a route with this attribute, the device does not advertise this route to any BGP peer.
No_Export | 4294967041 (0xFFFFFF01) | After a device receives a route with this attribute, the device does not advertise this route outside the local AS.
No_Export_Subconfed | 4294967043 (0xFFFFFF03) | After a device receives a route with this attribute, the device does not advertise this route outside the local AS. If a confederation is used, the device does not advertise this route to the other sub-ASs in the confederation.
Community attribute format:
  The length of a community attribute is 32 bits, which can be presented in either of the following formats:
    Decimal integer
    In the AA:NN format, AA indicates an AS number, and NN is a user-defined number.
Overview
AS_Path Filter
Community Filter

## Slide 18: Basic Community Configuration Commands
[Huawei-route-policy] apply community { community-number | aa:nn | internet | no-advertise | no-export | no-export-subconfed } [ additive ]
Set a community value or multiple community values for the matched routes in a route-policy.
Overview
AS_Path Filter
Community Filter
[Huawei-bgp-af-ipv4] peer { group-name | ipv4-address | ipv6-address } advertise-community
Configure the device to advertise the community attribute(s) to a specified peer or peer group.
By default, a device advertises no community attribute to its peer or peer group.
Notes: Command: [Huawei-route-policy] apply community { community-number | aa:nn | internet | no-advertise | no-export | no-export-subconfed } [ additive ]
  community-number | aa:nn: specifies a community number for a community attribute. A maximum of 32 community numbers can be specified at a time using this command. The value of community-number is an integer ranging from 0 to 4294967295. The values of aa and nn are also integers ranging from 0 to 65535.
  internet: allows the matched routes to be advertised to any peers. By default, all routes belong to the Internet community.
  no-advertise: prevents the matched routes from being advertised to any peer. After a device receives a route with this attribute, it cannot advertise this route to any other BGP peers.
  no-export: prevents the matched routes from being advertised outside the local AS but allows them to be advertised to other sub-ASs in the local AS. After a device receives a route with this attribute, it cannot advertise this route outside the local AS.
  no-export-subconfed: prevents the matched routes from being advertised outside the local AS or to other sub-ASs in the local AS. After a device receives a route with this attribute, it cannot advertise this route to any other sub-ASs.
  additive: adds community attributes to the routes that match the filtering conditions.

## Slide 19: Basic Community Filter Configuration Commands (1)
[Huawei] ip community-filter { basic comm-filter-name | basic-comm-filter-num } { permit | deny } [ community-number | aa:nn | internet | no-export-subconfed | no-advertise | no-export ]
Create a basic community filter.
[Huawei] ip community-filter { advanced comm-filter-name | adv-comm-filter-num } { permit | deny } regular-expression
Create an advanced community filter.
The number of an advanced community filter ranges from 100 to 199. A regex can be specified as a matching condition in an advanced community filter.
The number of a basic community filter ranges from 1 to 99. Only the community number or well-known community attribute can be specified in a basic community filter.
Overview
AS_Path Filter
Community Filter
Notes: Command: [Huawei] ip community-filter { basic comm-filter-name | basic-comm-filter-num } { permit | deny } [ community-number | aa:nn | internet | no-export-subconfed | no-advertise | no-export ]
  basic comm-filter-name: specifies the name of a basic community filter. The value is a string of 1 to 51 case-sensitive characters. It cannot be comprised of only digits.
  basic-comm-filter-num: specifies the number of a basic community filter. The value is an integer ranging from 1 to 99.
  deny: sets the matching mode of the community filter to deny.
  permit: sets the matching mode of the community filter to permit.
  community-number: specifies a community number. The value is an integer ranging from 0 to 4294967295.
  aa:nn: specifies a community number. A maximum of 20 community numbers can be specified at a time using this command. The values of aa and nn are integers ranging from 0 to 65535.
  internet: allows the matched routes to be advertised to any peers.
  no-export-subconfed: prevents the matched routes from being advertised outside the local AS. If a confederation is used, the matched routes will not be advertised to the other sub-ASs in the confederation.
  no-advertise: prevents the matched routes from being advertised to any other peers.
  no-export: prevents the matched routes from being advertised outside the local AS. If a confederation is used, the matched routes will not be advertised outside the confederation but will be advertised to the other sub-ASs in the confederation.

## Slide 20: Basic Community Filter Configuration Commands (1)
[Huawei] ip community-filter { basic comm-filter-name | basic-comm-filter-num } { permit | deny } [ community-number | aa:nn | internet | no-export-subconfed | no-advertise | no-export ]
Create a basic community filter.
[Huawei] ip community-filter { advanced comm-filter-name | adv-comm-filter-num } { permit | deny } regular-expression
Create an advanced community filter.
The number of an advanced community filter ranges from 100 to 199. A regex can be specified as a matching condition in an advanced community filter.
The number of a basic community filter ranges from 1 to 99. Only the community number or well-known community attribute can be specified in a basic community filter.
Overview
AS_Path Filter
Community Filter
Notes: Command: [Huawei] ip community-filter { advanced comm-filter-name | adv-comm-filter-num } { permit | deny } regular-expression
  advanced comm-filter-name: specifies the name of an advanced community filter. The value is a string of 1 to 51 case-sensitive characters. It cannot be comprised of only digits.
  adv-comm-filter-num: specifies the number of an advanced community filter. The value is an integer ranging from 100 to 199.
  regular-expression: specifies a regex for the community filter. The value is a string of 1 to 255 case-sensitive characters and can contain spaces.

## Slide 21: Basic Community Filter Configuration Commands (2)
[Huawei-route-policy] if-match community-filter { basic-comm-filter-num [ whole-match ] | adv-comm-filter-num }
Apply a community filter.
A matching rule based on the community filter is created in the route-policy view.
[Huawei-route-policy] if-match community-filter comm-filter-name [ whole-match ]
Overview
AS_Path Filter
Community Filter
Notes: Command: [Huawei-route-policy] if-match community-filter { basic-comm-filter-num [ whole-match ] | adv-comm-filter-num }
Command: [Huawei-route-policy] if-match community-filter comm-filter-name [ whole-match ]
  basic-comm-filter-num: specifies the number of a basic community filter. The value is an integer ranging from 1 to 99.
  adv-comm-filter-num: specifies the number of an advanced community filter. The value is an integer ranging from 100 to 199.
  comm-filter-name: specifies the name of a community filter. The value is a string of 1 to 51 case-sensitive characters. It cannot be comprised of only digits. If spaces are used, the string must start and end with double quotation marks (").
  whole-match: indicates complete matching. That is, all the community attributes in the specified community filter must be matched. This parameter applies only to basic community filters.

## Slide 22: Examples for Configuring Community Filters
ip community-filter 1 permit 100:1 200:1 300:1
Example for configuring a basic community filter
Match the routes carrying community values [100:1, 200:1, 300:1]. (The relationship between multiple community values in a command configuration is AND.)
ip community-filter 1 permit 100:1
ip community-filter 1 permit 200:1 300:1
Match the routes carrying community value [100:1] or community values [200:1, 300:1]. (The relationship between different groups of community values is OR. A set of community values in a command configuration is called a group.)
ip community-filter 100 permit ^10
Example for configuring an advanced community filter
Match the routes carrying community values starting with 10.
Overview
AS_Path Filter
Community Filter

## Slide 23: Configuring Community Attributes (1)
[R1] ip ip-prefix 1 permit 10.1.1.1 32
[R1] route-policy Community permit node 10
[R1-route-policy] if-match ip-prefix 1
[R1-route-policy] apply community 101:1
[R1-route-policy] quit
[R1] route-policy Community permit node 20
[R1-route-policy] quit
[R1] bgp 101
[R1-bgp] peer 10.1.12.2 as-number 102
[R1-bgp] peer 10.1.12.2 route-policy Community export
[R1-bgp] peer 10.1.12.2 advertise-community
[R1-bgp] network 10.1.1.1 32
[R1-bgp] network 10.1.2.2 32
1. Configure a routing policy on R1 to add a community attribute to matched routes, and enable R1 to advertise the community attribute to the EBGP peer R2.
AS 101
AS 102
AS 103
R1
R2
R3
10.1.1.1/32 Community = 101:1
10.1.2.2/32
Loopback0:
10.1.1.1/32
Loopback 1:
10.1.2.2/32
10.1.12.0/24
.1
.2
10.1.23.0/24
.2
.3
Configure a routing policy on R1 to allow the community value 101:1 to be carried only in the BGP route 10.1.1.1/32 when R1 advertises this route.
Overview
AS_Path Filter
Community Filter
Notes: Command: [R1] route-policy Community permit node 20
Run this command to allow the route 10.1.2.2/32 to be advertised properly.

## Slide 24: Configuring Community Attributes (2)
[R2] ip ip-prefix 1 permit 10.1.1.1 32
[R2] route-policy Community permit node 10
[R2-route-policy] if-match ip-prefix 1
[R2-route-policy] apply community no-expert additive
[R2-route-policy] quit
[R2] route-policy Community permit node 20
[R2-route-policy] quit
[R2] bgp 102
[R2-bgp] peer 10.1.12.1 as-number 101
[R2-bgp] peer 10.1.23.3 as-number 102
[R2-bgp] peer 10.1.23.3 advertise-community
[R2-bgp] peer 10.1.23.3 route-policy Community export
2. Configure R2 to advertise the community attribute to the EBGP peer R3.
AS 101
AS 102
AS 103
R1
R2
R3
Loopback0:
10.1.1.1/32
Loopback 1:
10.1.2.2/32
10.1.12.0/24
.1
.2
10.1.23.0/24
.2
.3
10.1.1.1/32 Community = 101:1 no-export
10.1.2.2/32
Configure a routing policy on R1 to allow the community value 101:1 to be carried only in the BGP route 10.1.1.1/32 when R1 advertises this route.
Configure a routing policy on R2 to allow the community attribute no-expert to be added to the BGP route 10.1.1.1/32 when R2 advertises this route.
Overview
AS_Path Filter
Community Filter

## Slide 25: Configuring Community Attributes (3)
[R3] bgp 103
[R3-bgp] peer 10.1.23.2 as-number 102
[R3-bgp] quit
[R3] display bgp routing-table 10.1.1.1
BGP local router ID : 10.1.23.3
Local AS number : 103
Paths: 1 available, 1 best, 1 select
BGP routing table entry information of 10.1.1.1/32:
From: 10.1.23.2 (10.1.12.2)
Route Duration: 00h00m21s
Direct Out-interface: GigabitEthernet0/0/2
Original nexthop: 10.1.23.2
Qos information : 0x0
Community:<101:1>, no-export
AS-path 102 101, origin igp, pref-val 0, valid, external, best, select, active, pre 255
Not advertised to any peer yet
3. Check the BGP routing information on R3.
AS 101
AS 102
AS 103
R1
R2
R3
Loopback0:
10.1.1.1/32
Loopback 1:
10.1.2.2/32
10.1.12.0/24
.1
.2
10.1.23.0/24
.2
.3
10.1.1.1/32 Community = 101:1 no-export
10.1.2.2/32
Check the route 10.1.1.1/32 on R3. The command output shows that the route carries two community values: 101:1 and no-export.
Overview
AS_Path Filter
Community Filter
Configure a routing policy on R1 to allow the community value 101:1 to be carried only in the BGP route 10.1.1.1/32 when R1 advertises this route.
Configure a routing policy on R2 to allow the community attribute no-expert to be added to the BGP route 10.1.1.1/32 when R2 advertises this route.

## Slide 26: Configuring a Community Filter (1)
AS 102
AS 103
AS 101
R1
10.1.1.1/32
10.1.2.2/32
R2
Route:
10.1.1.1/32 Community = 101:1
10.1.2.2/32 Community = 101:2
R3
[R2] ip community-filter 1 permit 101:1
10.1.12.0/24
.1
.2
.2
.3
10.1.23.0/24
R2 transmits routes to the EBGP peer R3. Configure a routing policy on R2 to filter out the route carrying the community value 101:1.
1. Configure a community filter to match the route carrying the community value 101:1.
Route
10.1.2.2/32 Community = 101:2
Route filtering
Overview
AS_Path Filter
Community Filter
[R2] route-policy Community deny node 10
[R2-route-policy] if-match community-filter 1
[R2-route-policy] quit
[R2] route-policy Community permit node 20
[R2-route-policy] quit
[R2] bgp 102
[R2-bgp] peer 10.1.23.3 route-policy Community export
2. Configure a matching rule that is based on the community filter.
3. Check the community filter information on R2.
[R2]display ip community-filter 1
Community filter Number: 1
permit 101:1

## Slide 27: Configuring a Community Filter (2)
AS 102
AS 103
AS 101
R1
10.1.1.1/32
10.1.2.2/32
R2
Route:
10.1.1.1/32 Community = 101:1
10.1.2.2/32 Community = 101:2
R3
4. Check the BGP routing information on R2.
10.1.12.0/24
.1
.2
.2
.3
10.1.23.0/24
R2 transmits routes to the EBGP peer R3. Configure a routing policy on R2 to filter out the route carrying the community value 101:1.
[R2]dis bgp routing-table 10.1.1.1
BGP local router ID : 10.1.12.2
Local AS number : 102
Paths: 1 available, 1 best, 1 select
BGP routing table entry information of 10.1.1.1/32:
From: 10.1.12.1 (10.1.1.1)
Route Duration: 00h13m39s
Direct Out-interface: GigabitEthernet0/0/1
Original nexthop: 10.1.12.1
Qos information : 0x0
Community:<101:1>
AS-path 101, origin igp, MED 0, pref-val 0, valid, external, best, select, active, pre 255
Not advertised to any peer yet
Route
10.1.2.2/32 Community = 101:2
Check the route 10.1.1.1/32 on R2. The command output shows that the route carries the community value 101:1.
Use the community filter to filter out this route.
Route filtering
Overview
AS_Path Filter
Community Filter

## Slide 28: Configuring a Community Filter (3)
[R3]display bgp routing-table
BGP Local router ID is 10.1.23.3
Status codes: * - valid, > - best, d - damped,
h - history, i - internal, s - suppressed, S - Stale
Origin : i - IGP, e - EGP, ? - incomplete
Total Number of Routes: 1
Network NextHop MED LocPrf PrefVal Path/Ogn
*> 10.1.2.2/32 10.1.23.2 0 102 101i
AS 102
AS 103
AS 101
R1
10.1.1.1/32
10.1.2.2/32
R2
Route:
10.1.1.1/32 Community = 101:1
10.1.2.2/32 Community = 101:2
R3
10.1.12.0/24
.1
.2
.2
.3
10.1.23.0/24
R2 transmits routes to the EBGP peer R3. Configure a routing policy on R2 to filter out the route carrying the community value 101:1.
5. Check the BGP routing table on R3.
Route
10.1.2.2/32 Community = 101:2
R3 does not receive the BGP route 10.1.1.1/32.
Route filtering
Overview
AS_Path Filter
Community Filter

## Slide 29
BGP Route Control
Introduction to BGP Features
Networking Modes of BGP RRs

## Slide 30: On-Demand Route Advertisement by BGP Peers
AS 101
10.1.1.1/32
10.1.2.2/32
If a device expects to receive only required routes from a remote device, and the remote device cannot maintain a separate outbound routing policy for each connected peer, you can configure a prefix-based outbound route filter (ORF) to implement on-demand route advertisement.
R1
R2
AS 102
BGP route advertisement:
10.1.1.1/32
10.1.2.2/32
R2 filters routes on the inbound interface and accepts only the route 10.1.1.1/32.
For the routes that are filtered out (for example, route 10.1.2.2/32), actually R1 does not need to advertise them to R2.
Route filtering
Prefix-based ORF enables a device to send locally configured prefix-based import policies to its BGP peers through Route-refresh messages. The BGP peers construct export policies based on the received policies (in Route-refresh messages) to filter routes to be advertised.
This prevents the local device from receiving a large number of unwanted routes, lowers the CPU usage of the local device, reduces the configuration workload on BGP peers, and lowers the link bandwidth usage.
ORF
Peer Group
Security

## Slide 31: Basic ORF Configuration Commands
[Huawei-bgp-af-ipv4] peer { group-name | ipv4-address } ip-prefix ip-prefix-name { import | export }
Configure a routing policy based on an IP prefix list to be associated with a specified peer or peer group.
[Huawei-bgp] peer { group-name | ipv4-address } capability-advertise orf [ non-standard-compatible ] ip-prefix { both | receive | send } [ standard-match ]
Enable the prefix-based ORF capability on the local device for the peer or peer group.
Note: The ORF function must be enabled on both ends of a peer relationship.
ORF
Peer Group
Security
Notes: Command: [Huawei-bgp-af-ipv4] peer { group-name | ipv4-address } ip-prefix ip-prefix-name { import | export }
  import: applies the routing policy to the routes received from the peer or peer group.
  export: applies the routing policy to the routes to be advertised to the peer or peer group.
Command: [Huawei-bgp] peer { group-name | ipv4-address } capability-advertise orf [ non-standard-compatible ] ip-prefix { both | receive | send } [ standard-match ]
  non-standard-compatible: indicates that the ORF capability supported by the Huawei device is compatible with that supported by a non-Huawei device.
  both: enables the local device to both send and accept ORF packets.
  receive: enables the local device to only accept ORF packets.
  send: enables the local device to only advertise ORF packets.
  standard-match: matches routes according to the prefix matching rules defined in an RFC standard.

## Slide 32: Example for Configuring ORF
[R2] ip ip-prefix 1 permit 10.1.1.1 32
[R2] bgp 102
[R2-bgp] peer 10.1.12.1 as-number 101
[R2-bgp] peer 10.1.12.1 ip-prefix 1 import
[R2-bgp] peer 10.1.12.1 capability-advertise orf ip-prefix send
1. Configure a routing policy on R2 to filter the route 10.1.1.1/32, and enable ORF on R2 to allow R2 to send ORF packets.
AS 101
AS 102
R1
R2
Route:
10.1.1.1/32
10.1.1.1/32
10.1.2.2/32
10.1.3.3/32
10.1.12.0/24
.1
.2
R2 expects R1 to only advertise the route 10.1.1.1/32, and sends an ORF packet to R1 to meet this expectation.
[R1] bgp 101
[R1-bgp] peer 10.1.12.2 as-number 102
[R1-bgp] peer 10.1.12.2 capability-advertise orf ip-prefix receive
[R1-bgp] network 10.1.1.1 32
[R1-bgp] network 10.1.2.2 32
[R1-bgp] network 10.1.3.3 32
2. Enable ORF on R1 to allow R1 to accept ORF packets.
1
ORF
2
ORF
Peer Group
Security

## Slide 33: Verifying the ORF Configuration
[R1]display bgp peer 10.1.12.2 orf ip-prefix
Total number of ip-prefix received: 1
Index Action Prefix MaskLen MinLen MaxLen
10 Permit 10.1.1.1 32
1. On R1, check the prefix-based ORF information sent by R2.
AS 101
AS 102
R1
R2
Route:
10.1.1.1/32
10.1.1.1/32
10.1.2.2/32
10.1.3.3/32
10.1.12.0/24
.1
.2
[R2]display bgp routing-table peer 10.1.12.1 received-routes
BGP Local router ID is 10.1.12.2
Status codes: * - valid, > - best, d - damped,
h - history, i - internal, s - suppressed, S - Stale
Origin : i - IGP, e - EGP, ? - incomplete
Total Number of Routes: 1
Network NextHop MED LocPrf PrefVal Path/Ogn
*> 10.1.1.1/32 10.1.12.1 0 0 101i
2. Check the BGP routing information on R2.
1
ORF
2
Check the ORF information on R1. The command output shows that the route 10.1.1.1/32 is required.
Check the BGP routing information on R2. The command output shows that R2 has received only the route 10.1.1.1/32.
ORF
Peer Group
Security

## Slide 34: BGP Peer Group
A peer group is a set of peers with the same policies. When a peer is added to a peer group, it inherits the configurations of the peer group. If the configurations of the peer group change, the configurations of all the peers in the group change accordingly.
A large number of BGP peers may exist on a large-scale BGP network, many of which need the same policies, you can configure a peer group to simplify configuration.
ORF
Peer Group
Security
Notes: Each peer in a peer group can be configured with its own policies for route advertisement and acceptance.

## Slide 35: Basic Peer Group Configuration Commands
[Huawei-bgp] group group-name [ external | internal ]
Create a BGP peer group.
[Huawei-bgp] peer group-name as-number { as-number-plain | as-number-dot }
(Optional) Configure an AS number for the specified peer group.
A peer group is created in the BGP view, BGP-VPN instance IPv4 address family view, or BGP-VPN instance IPv6 address family view.
[Huawei-bgp] peer { ipv4-address | ipv6-address } group group-name
Add a specified peer to the peer group.
[Huawei-bgp] peer group-name connect-interface interface-type interface-number [ ipv4-source-address ]
Specify the source interface for sending BGP messages and the source address for initiating a BGP connection.
An AS number is configured for the EBGP peer group. The AS number of an IBGP peer group is the local AS number of the device with the IBGP peer group configured.
ORF
Peer Group
Security
Notes: Command: [Huawei-bgp] group group-name [ external | internal ]
  group-name: specifies the name of a peer group. The value is a string of 1 to 47 case-sensitive characters. If spaces are used, the string must start and end with double quotation marks (").
  external: creates an EBGP peer group.
  internal: creates an IBGP peer group.

## Slide 36: Example for Configuring a BGP Peer Group
[R1] bgp 101
[R1-bgp] peer 10.1.12.2 as-number 102
[R1-bgp] network 10.1.1.1 32
1. Complete the basic BGP configuration on R1.
AS 101
R2
R4
10.1.1.1/32
10.1.12.0/24
.1
.4
After R2 (ASBR) receives a route from its EBGP peer (R1), it advertises the route to all its IBGP peers (R3, R4, and R5). If R2 supports the BGP peer group function, its BGP forwarding performance will be greatly improved.
[R2] bgp 102
[R2-bgp] peer 10.1.12.1 as-number 101
[R2-bgp] group in internal
[R2-bgp] peer 10.1.3.3 group in
[R2-bgp] peer 10.1.4.4 group in
[R2-bgp] peer 10.1.5.5 group in
[R2-bgp] peer in connect-interface Loopback 0
2. Complete the basic EBGP configuration and basic IBGP peer group configuration on R2.
.2
R1
R3
R5
10.1.23.0/24
10.1.24.0/24
10.1.25.0/24
.2
.2
.2
.3
.5
AS 102
Device | Interface | Interface Address | Device | Interface | Interface Address
R1 | Loopback0 | 10.1.1.1/32 | R4 | Loopback0 | 10.1.4.4/32
R2 | Loopback0 | 10.1.2.2/32 | R5 | Loopback0 | 10.1.5.5/32
R3 | Loopback0 | 10.1.3.3/32 | / |  | 
[R3] bgp 102
[R3-bgp] peer 10.1.2.2 as-number 102
[R3-bgp] peer 10.1.2.2 connect-interface Loopback 0
3. Complete the basic IBGP configuration on R3.
The configurations of R4 and R5 are similar to the configuration of R3, and are not provided here.
ORF
Peer Group
Security
Notes: As shown in the figure, assume that static routes are used or OSPF is used to ensure internal network reachability in AS 102. The configuration details are not provided here.

## Slide 37: Verifying the BGP Peer Group Configuration
[R2]display bgp group in
BGP peer-group: in
Remote AS: 102
Authentication type configured: None
Type : internal
Configured hold timer value: 180
Keepalive timer value: 60
Connect-retry timer value: 32
Minimum route advertisement interval is 15 seconds
Connect-interface has been configured
PeerSession Members:
10.1.3.3 10.1.4.4 10.1.5.5
Peer Preferred Value: 0
No routing policy is configured
Peer Members:
Peer V AS MsgRcvd MsgSent OutQ Up/Down State PrefRcv
10.1.3.3 4 102 5 7 0 00:03:33 Established 0
10.1.4.4 4 102 5 6 0 00:03:11 Established 0
10.1.5.5 4 102 4 6 0 00:02:52 Established 0
1. Check the BGP peer group information on R2.
R2
R4
.4
.2
R3
R5
10.1.23.0/24
10.1.24.0/24
10.1.25.0/24
.2
.2
.2
.3
.5
AS 102
The command output shows that the peer group created on R2 is named in and has three IBGP peer members: 10.1.3.3, 10.1.4.4, and 10.1.5.5. All these members have established peer relationships with R2.
ORF
Peer Group
Security

## Slide 38: BGP Security
Common BGP attacks are as follows:
  A rogue BGP peer relationship is established, and invalid routes are advertised to disturb the normal routing table.
  A router receives a large number of bogus BGP messages and sends them to the CPU. As a result, the CPU usage goes excessively high.
Sends a large number of bogus BGP messages.
Rogue router
R1
Attacker
Establishes a rogue IBGP peer relationship and advertise the invalid Net1 route.
IBGP
AS 101
R2
IBGP
1
2
BGP routing table
*> Net1
The routing table of the authorized router is disturbed.
The CPU usage surges.
BGP uses authentication and Generalized TTL Security Mechanism (GTSM) to ensure the security of message exchange between BGP peers.
R3
ORF
Peer Group
Security

## Slide 39: BGP Authentication
BGP authentication is classified as MD5 authentication or keychain authentication. Authenticating BGP peer relationships can prevent rogue BGP peer relationships from being established.
BGP uses the Transmission Control Protocol (TCP) as its transport layer protocol. To enhance BGP security, MD5 authentication can be implemented when a TCP connection is established. You can set an MD5 authentication password for a TCP connection so that TCP implements MD5 authentication for BGP.
MD5 Authentication
R1
R2
TCP packets exchanged during the three-way handshake
Open messages
Update messages
Keepalive messages
Notification messages
The MD5 field in TCP packets is used for authentication.
Keychain is a set of key IDs. A key ID uniquely identifies authentication information, including the authentication password and algorithm.
You must configure keychain authentication for TCP-based applications on both BGP peers. Note that encryption algorithms and passwords configured for keychain authentication on both peers must be the same; otherwise, a TCP connection cannot be set up between BGP peers and BGP messages cannot be exchanged.
Keychain Authentication
R1
R2
When an application sends a packet, it uses the authentication information carried in a key ID to generate a message authentication code (MAC).
Fills the obtained MAC information
into the TCP Enhanced Authentication Option
After receiving the packet, the application uses the authentication information carried in the key ID to verify the MAC.
Returns a result (authentication success or failure)
BGP peer relationship
BGP peer relationship
ORF
Peer Group
Security
Notes: BGP uses TCP as its transport layer protocol and considers a TCP packet valid only if the source IP address, destination IP address, source port number, destination port number, and TCP sequence number in the packet are correct. Most of the preceding parameters in a TCP packet can be easily obtained by attackers. To protect BGP from attacks, use MD5 authentication or keychain authentication between BGP peers to reduce the possibility of attacks.
  The MD5 algorithm is easy to configure and generates a single password, which can only be manually changed.
  The keychain algorithm is complex to configure and generates a set of passwords. Keychain authentication allows passwords to be changed automatically based on configurations. Therefore, keychain authentication is applicable to networks requiring high security.
Note: BGP MD5 authentication and BGP keychain authentication are mutually exclusive.

## Slide 40: BGP GTSM
BGP GTSM can check whether the time to live (TTL) value in the IP packet header is within a preset range, and drop the packets whose TTL values are not within the preset range. This prevents bogus BGP messages from attacking the device.
Sends a large number of bogus BGP messages.
GTSM is deployed, and the minimum TTL value of the BGP messages to be accepted is set to 255.
The bogus BGP messages have excessively small TTL values after reaching R2 and are therefore dropped.
R1
R2
Attacker
IBGP
When an attacker continuously sends bogus BGP messages to attack R2, the TTL values of such messages are smaller than 255.
If BGP GTSM is enabled on R2 and the valid TTL range for messages sent by the IBGP peer is set to [255, 255], the system checks the TTL values of all BGP messages and drops the bogus messages whose TTL values are smaller than 255. This prevents the bogus messages from consuming CPU resources.
AS 101
ORF
Peer Group
Security
Notes: As shown in the figure, if BGP GTSM is not enabled, the device finds that the received numerous bogus BGP messages are destined for itself, and directly sends them to the control plane for processing. As a result, the control plane has to process a large number of bogus messages, causing the CPU usage to go excessively high and the system to be unexpectedly busy.

## Slide 41: Basic BGP Authentication Configuration Commands
[Huawei-bgp] peer { group-name | ipv4-address | ipv6-address } password { cipher cipher-password | simple simple-password }
Configure MD5 authentication for BGP messages exchanged during the establishment of a TCP connection with a specified peer or peer group.
[Huawei-bgp] peer { group-name | ipv4-address | ipv6-address } keychain keychain-name
Configure keychain authentication for the establishment of a TCP connection with a specified peer or peer group.
ORF
Peer Group
Security
Notes: Command: [Huawei-bgp] peer { group-name | ipv4-address | ipv6-address } keychain keychain-name
  keychain-name: specifies the name of a keychain. The value is a string of 1 to 47 case-insensitive characters. It cannot contain question marks (?). If spaces are used, the string must start and end with double quotation marks (").

## Slide 42: Basic GTSM Configuration Commands
[Huawei-bgp] peer { group-name | ipv4-address | ipv6-address } valid-ttl-hops [ hops ]
Apply the GTSM function to a BGP peer or peer group.
[Huawei] gtsm default-action { drop | pass }
(Optional) Set a default action to take on messages that do not match the GTSM policy.
[Huawei] gtsm log drop-packet all
(Optional) Enable the logging function on all boards to record log information when GTSM discards messages.
By default, no log information is recorded on any board when GTSM drops messages.
You can run this command to enable the logging function so that the device can record information about the messages dropped by GTSM in logs. The recorded logs facilitate fault locating.
By default, the messages that do not match a GTSM policy can pass filtering.
GTSM configurations are symmetrical. That is, you need to enable GTSM on both ends of BGP peer relationship.
ORF
Peer Group
Security
Notes: Command: [Huawei-bgp] peer { group-name | ipv4-address | ipv6-address } valid-ttl-hops [ hops ]
  hops: specifies the number of TTL hops to be checked. The value is an integer ranging from 1 to 255. The default value is 255. If you specify hops, the valid range of TTL values in the messages to be checked is [255 – hops + 1, 255].
Command: [Huawei] gtsm default-action { drop | pass }
  drop: indicates that the messages that do not match the GTSM policy cannot pass filtering and are dropped.
  pass: indicates that the messages that do not match the GTSM policy can pass filtering.
Command: [Huawei] gtsm log drop-packet all
  all: indicates all boards.

## Slide 43: Example for Configuring GTSM (1)
[R1] bgp 101
[R1-bgp] peer 10.1.2.2 as-number 101
[R1-bgp] peer 10.1.2.2 connect-interface Loopback 0
[R1-bgp] peer 10.1.3.3 as-number 101
[R1-bgp] peer 10.1.3.3 connect-interface Loopback 0
[R1-bgp] network 10.1.1.1 32
1. Establish full-mesh IBGP connections.
R1
R2
.2
R1, R2, and R3 all belong to AS 101 and use loopback0 interfaces to establish full-mesh IBGP connections. GTSM needs to be enabled on them to prevent CPU attacks.
R3
10.1.12.0/24
10.1.23.0/24
.1
AS 101
Device | Interface | Interface Address
R1 | Loopback0 | 10.1.1.1/32
R2 | Loopback0 | 10.1.2.2/32
R3 | Loopback0 | 10.1.3.3/32
.2
.3
IBGP peer relationship
IBGP peer relationship
IBGP peer relationship
[R2] bgp 101
[R2-bgp] peer 10.1.1.1 as-number 101
[R2-bgp] peer 10.1.1.1 connect-interface Loopback 0
[R2-bgp] peer 10.1.3.3 as-number 101
[R2-bgp] peer 10.1.3.3 connect-interface Loopback 0
[R3] bgp 101
[R3-bgp] peer 10.1.1.1 as-number 101
[R3-bgp] peer 10.1.1.1 connect-interface Loopback 0
[R3-bgp] peer 10.1.2.2 as-number 101
[R3-bgp] peer 10.1.2.2 connect-interface Loopback 0
ORF
Peer Group
Security
Notes: As shown in the figure:
  Assume that static routes are used or OSPF is used to ensure internal network reachability in AS 101. The configuration details are not provided here.
  R1 advertises the route destined for the IP address of its loopback0 interface to the BGP routing table.

## Slide 44: Example for Configuring GTSM (2)
[R1-bgp] peer 10.1.2.2 valid-ttl-hops 1
2. Enable GTSM between R1 and R2. As the two routers are directly connected, the valid TTL range of the messages from one router to the other is [255, 255]. In this case, the value of valid-ttl-hops is 1.
R1
R2
.2
R1, R2, and R3 all belong to AS 101 and use loopback0 interfaces to establish full-mesh IBGP connections. GTSM needs to be enabled on them to prevent CPU attacks.
R3
10.1.12.0/24
10.1.23.0/24
.1
AS 101
Device | Interface | Interface Address
R1 | Loopback0 | 10.1.1.1/32
R2 | Loopback0 | 10.1.2.2/32
R3 | Loopback0 | 10.1.3.3/32
.2
.3
IBGP peer relationship
IBGP peer relationship
IBGP peer relationship
[R2-bgp] peer 10.1.1.1 valid-ttl-hops 1
[R2-bgp] peer 10.1.3.3 valid-ttl-hops 1
3. Enable GTSM between R2 and R3. As the two routers are directly connected, the valid TTL range of the messages from one router to the other is [255, 255]. In this case, the value of valid-ttl-hops is 1.
[R3-bgp] peer 10.1.2.2 valid-ttl-hops 1
[R1-bgp] peer 10.1.3.3 valid-ttl-hops 2
4. Enable GTSM between R1 and R3. As the two routers are connected through R2, the valid TTL range of the messages from one end to the other is [254, 255]. In this case, the value of valid-ttl-hops is 2.
[R3-bgp] peer 10.1.1.1 valid-ttl-hops 2
ORF
Peer Group
Security

## Slide 45: Verifying the GTSM Configuration
[R1]display bgp peer 10.1.3.3 verbose
BGP Peer is 10.1.3.3, remote AS 101
Type: IBGP link
BGP version 4, Remote router ID 10.1.3.3
Update-group ID: 1
BGP current state: Established, Up for 00h02m17s
BGP current event: KATimerExpired
BGP last state: OpenConfirm
BGP Peer Up count: 1
Received total routes: 0
Received active routes total: 0
Advertised total routes: 1
Port: Local - 179 Remote - 51077
Configured: Connect-retry Time: 32 sec
Configured: Active Hold Time: 180 sec Keepalive Time:60 sec
Received : Active Hold Time: 180 sec
Negotiated: Active Hold Time: 180 sec Keepalive Time:60 sec
Peer optional capabilities:
Peer supports bgp multi-protocol extension
Peer supports bgp route refresh capability
Peer supports bgp 4-byte-as capability
Received: Total 5 messages
Update messages 0
Open messages 1
KeepAlive messages 3
Notification messages 0
Refresh messages 1
Sent: Total 8 messages
Update messages 2
Open messages 2
KeepAlive messages 3
Notification messages 0
Refresh messages 1
Authentication type configured: None
Last keepalive received: 2020/06/22 17:34:13 UTC-08:00
Last keepalive sent : 2020/06/22 17:34:13 UTC-08:00
Last update sent : 2020/06/22 17:34:02 UTC-08:00
Minimum route advertisement interval is 15 seconds
Optional capabilities:
Route refresh capability has been enabled
4-byte-as capability has been enabled
Connect-interface has been configured
GTSM has been enabled, valid-ttl-hops: 2
Peer Preferred Value: 0
Routing policy configured:
No routing policy is configured
To be continued on the right
Run the display bgp peer command to check BGP peer information.
By specifying the verbose parameter, you can check information about the BGP timer, numbers of received and sent routes, capabilities supported by the peer, and enabled functions.
GTSM is enabled on R1, and the number of valid hops between R1 and its IBGP peer 10.1.3.3 (R3) is 2.
ORF
Peer Group
Security

## Slide 46
BGP Route Control
Introduction to BGP Features
Networking Modes of BGP RRs

## Slide 47: RR
Using RRs can avoid the need for full-mesh IBGP connections and reduce the burden on the network and CPU.
AS 103
R5
OSPF
AS 101
RR
R3
R2
IBGP
AS 102
R4
10.1.1.1/32
IBGP
BGP Update message
R1
After an RR is introduced, three roles exist:
  Route reflector
  Client
  Non-client
The RR reflects the learned routes so that IBGP routes are advertised in the AS, avoiding the need to establish full-mesh IBGP connections.
After the RR receives routes from its peers, it selects the optimal route based on BGP route selection rules and advertises the optimal route to IBGP peers based on certain rules.
Client
Non-client
EBGP
EBGP
Notes: RR-related roles:
  RR: BGP device that reflects the routes learned from an IBGP peer to other IBGP peers. An RR is similar to the designated router (DR) on an OSPF network.
  Client: IBGP peer whose routes are reflected by the RR to other IBGP peers. In an AS, clients only need to be directly connected to the RR.
  Non-client: IBGP device that is neither an RR nor a client. In an AS, full-mesh connections still must be established between non-clients and RRs, and between all non-clients.
  Originator: device that originates routes in an AS. The Originator_ID attribute is used to prevent routing loops in a cluster.
  Cluster: a set of RRs and their clients. The Cluster_List attribute is used to prevent routing loops between clusters.
When configuring a BGP router as an RR, you also need to specify a client of the RR. A client does not need to be configured because it is not aware that an RR exists on the network.
Rules for an RR to advertise routes:
  After learning routes from non-clients, the RR selects and advertises the optimal route to all its clients.
  After learning routes from clients, the RR selects and advertises the optimal route to all its non-clients and clients (except the originating client).
  After learning routes learned from EBGP peers, the RR selects and advertises the optimal route to all its clients and non-clients.

## Slide 48: Common Networking Modes: Backup RR Networking
To improve network reliability and prevent a single point of failure (SPOF) from affecting the network, multiple RRs need to be configured in a cluster.
Routers on a forwarding path establish IBGP peer relationships with all RRs. Any of the RRs has complete BGP routes.
RR1
RR2
Client 1
Client 2
AS 101
Cluster
IBGP
IBGP
IBGP
R1
AS 102
EBGP
10.1.1.1/32
RR1 and RR2 are in the same cluster and configured with the same cluster ID.
Route reflection in single-cluster RR networking (RR1 is used as an example):
  When client 1 receives an updated route from an EBGP peer, it advertises this route to RR1 and RR2 through IBGP peer relationships.
  After RR1 and RR2 receive this route, they add the local cluster ID to the top of the cluster list of the route, and then reflect the route to client 2 and to each other.
  After RR1 and RR2 receive the reflected route, they check the cluster list of the route, finding that the cluster list contains their local cluster ID. RR1 and RR2 discard this route to prevent routing loops.
1
2
3
IBGP peer relationship
BGP Update message

## Slide 49: Common Networking Modes: Multi-Cluster RR Networking (1)
If multiple clusters exist in an AS, RRs of the clusters establish IBGP peer relationships with each other.
When RRs reside at the same network layer, RRs of different clusters can establish full-mesh connections to implement flat RR.
An AS on a backbone network may be divided into multiple clusters. RRs of the clusters are non-clients of each other and establish full-mesh IBGP connections with each other.
Although each client in a cluster establishes an IBGP connection only with the RR in the same cluster, each RR and client can receive all the routing information.
As shown in the figure, four RRs reside in cluster 1, cluster 2, cluster 3, and cluster 4. IBGP connections are established between the four RRs. Each client in a cluster establishes an IBGP connection only with the RR in the same cluster.
RR
Client 1
AS 101
IBGP
IBGP peer relationship
Cluster 1
Cluster 3
Cluster 4
Cluster 2
RR
RR
RR
Client 2
Client 1
Client 2
Client
Client

## Slide 50: Common Networking Modes: Multi-Cluster RR Networking (2)
Client
If multiple clusters exist in an AS, RRs of the clusters establish IBGP peer relationships with each other.
When the RRs reside at different network layers, the RRs at the lower network layer can be configured as clients to implement hierarchical RR.
Level-1 RR1
Level-1 RR2
Client 1/
Level-2 RR
AS 101
Cluster 1
IBGP
IBGP
IBGP
Client
In practice, hierarchical RR deployment is used more widely.
As shown in the figure, AS 101 is divided into three clusters:
  The four devices in cluster 1 are core routers and work in master/backup mode to ensure high reliability. Two Level-1 RRs are deployed in cluster 1, and the other two routers function as clients of the RRs.
  A Level-2 RR is deployed in each of cluster 2 and cluster 3. The Level-2 RRs are also clients of the Level-1 RRs. An IBGP connection does not need to be established between the Level-2 RRs.
Client 2/
Level-2 RR
Cluster 2
Cluster 3
IBGP peer relationship
Level-1 reflection
Level-2 reflection
Notes: The route advertisement rules for hierarchical RR networking are the same as those for single-cluster RR networking.
The following factors need to be considered for hierarchical RR design:
  Size of the top-layer full-mesh topology: If the number of full-mesh IBGP connections has exceeded the management capacity, hierarchical RR networking can be deployed.
  Number of alternate paths: This factor affects load balancing and resource consumption. More layers reduce the number of links for load balancing but require fewer router resources.

## Slide 51: Single-Cluster Problem
To provide the desired redundancy in an RR-based architecture, it is important to properly divide an AS into clusters.
AS 101
AS 102
R1
Route:
10.1.5.5/32
10.1.5.5/32
R2
R3
R4
R5
Cluster
RR1
RR2
Client
Scenario description:
  As shown in the figure, AS 101 uses the backup RR networking. RR1 and RR2 use the same cluster ID, and provide a redundant link for traffic from R1 to access 10.1.5.5/32.
  After R4 advertises the route 10.1.5.5/32, the two RRs advertise the route to R1 and to each other. Because RR1 and RR2 have the same cluster ID, the Update messages exchanged between the RRs are discarded.
An IBGP session failure causes the redundancy failure:
  Assume that the IBGP session between R3 and R4 fails (for example, due to incorrect configurations). As R3 ignores the route 10.1.5.5/32 advertised by R2, no redundant link is available for traffic from R1 to access 10.1.5.5/32.

## Slide 52: Multi-Cluster Design
Multi-cluster design not only provides physical redundancy in response to link failures, but also provides logical redundancy in response to IBGP session failures between clients and RRs.
AS 101
AS 102
R1
Route:
10.1.5.5/32
10.1.5.5/32
R2
R3
R4
R5
Cluster 1
RR1
RR2
Client
As shown in the figure, R2 and R4 are added to cluster 1, and R3 and R4 are added to cluster 2.
If the IBGP session between R3 and R4 fails, R3 can still forward traffic because R3 learns the route 10.1.5.5/32 advertised by R2.
Cluster 2

## Slide 53
(Single) Which of the following AS_Path value is matched against the ip as-path-filter 1 permit ^(100|200)$ command? ( )
  AS_Path 100
  AS_Path 200
  AS_Path 100 200
  AS_Path 100 or AS_Path 200
(TorF) Authenticate BGP peer relationships can prevent unauthorized BGP peer relationships from being established. ( )
  True
  False
(TorF) In the backup RR networking of BGP, the master and backup RRs discard the routes reflected by each other to prevent routing loops. ( )
  True
  False
Notes: D
A
A

## Slide 54
The AS_Path and community filters are dedicated route matching tools of BGP. You can use them to match BGP routes based on the AS_Path and community attributes, respectively. After routing policies are applied to the matched routes, BGP route control can be implemented.
BGP also supports various advanced features, including ORF to achieve on-demand route advertisement, peer group to simplify configurations, and BGP security features to prevent the establishment of rogue peer relationships as well as attacks from bogus BGP messages.
BGP uses RRs to break the split horizon rule of IBGP, avoid the need for full-mesh IBGP connections, and reduce the burden on the network and CPU. Common RR networking modes include backup RR networking and multi-cluster RR networking.