## Slide 1
Chen Qibiao/cwx47601
2020.03
Zhu Shigeng/00261992
New
Zhang Linrui/zwx570554
2020.06
Update
Update
Update
Update
Update

## Slide 2: MPLS Implementation and Configuration

## Slide 3
In the mid-1990s, Internet traffic grew rapidly. Traditional IP packets were forwarded by routers based on routing tables. However, due to hardware technology limitations, the forwarding performance of routers is low. As a result, this mode becomes a bottleneck for network data forwarding.
As such, the Multiprotocol Label Switching (MPLS) protocol is proposed. It is designed to speed up packet forwarding on routers. On an MPLS network, IP packet headers are analyzed on network edges only, and MPLS uses labels to guide packet forwarding inside the MPLS network. Label-based forwarding features high efficient, shortening the packet processing time.
With the continuous improvement of devices' hardware performance, the advantage of MPLS in improving the data forwarding speed is gradually weakened. However, as MPLS supports multi-layer label nesting and forwarding-and-control separation inside a device, MPLS is applicable to many scenarios, such as virtual private network (VPN) and quality of service (QoS).
This course describes the principles and label-based forwarding process of MPLS, as well as the method for configuring static label switched paths (LSPs).

## Slide 4
On completion of this course, you will be able to:
  Understand basic MPLS concepts and terms.
  Understand the principles of MPLS.
  Configure static LSPs.
  Describe the MPLS forwarding process.

## Slide 5
MPLS Basics
  MPLS Overview
  MPLS Terms
  MPLS Labels
MPLS Forwarding
Static LSP Configuration

## Slide 6: Traditional IP Routing and Forwarding
Traditional IP forwarding uses the hop-by-hop forwarding mode, in which a packet is decapsulated by all routers that receive the packet. Each router needs to obtain the network layer information and search its routing table for a route based on the longest match rule. The repeated processes of decapsulating packets, searching routing tables, and re-encapsulating the packets on routers result in low forwarding performance.
Destination/Mask | Protocol | Preference | Cost | Next Hop | Interface
192.168.1.0/24 | Direct | 0 | 0 | 192.168.1.254 | GE0/0/0
192.168.0.0/16 | Direct | 0 | 0 | 192.168.12.1 | GE0/0/2
0.0.0.0/0 | Static | 60 | 0 | 192.168.12.2 | GE0/0/2
R1
R2
R5
R6
R3
R4
PC1: 192.168.1.1/24
PC2: 192.168.2.1/24
IGP
GE0/0/2
R1 routing table
Characteristics of traditional IP routing and forwarding:
All routers need to know the network-wide routes.
The length of an IP header is not fixed, and the processing efficiency is low.
Traditional IP forwarding is connectionless and cannot provide good end-to-end QoS guarantee.
IP header
Data
IP header
Data
IP header
Data
IP header
Data
IP header
Data

## Slide 7: Basic MPLS Concepts
MPLS is located between the data link layer and the network layer in the TCP/IP protocol stack and can provide services for all network layers.
An MPLS header is added between a data-link-layer header and a network-layer header, and data can be forwarded quickly based on the Label field in the MPLS header.
This course describes the application of MPLS on IP networks only.
Destination: 3.3.3.3
MPLS label-based forwarding
MPLS label-based forwarding
IP header-based forwarding
IP network
IP network
3.3.3.0/24
IP
Packet
MPLS
Header
Ethernet
Header
Notes: MPLS is derived from the Internet Protocol version 4 (IPv4). Core MPLS technologies can be extended to support multiple network protocols, such as the Internet Protocol version 6 (IPv6), Internet Packet Exchange (IPX), Appletalk, DECnet, and Connectionless Network Protocol (CLNP). MPLS uses label-based forwarding to replace IP forwarding. A label is a short connection identifier of fixed length that is meaningful only to a local end.

## Slide 8
MPLS Basics
  MPLS Overview
  MPLS Terms
  MPLS Labels
MPLS Forwarding
Static LSP Configuration

## Slide 9: MPLS Terms - LSR and MPLS Domain
MPLS domain: consists of a series of consecutive network devices that run MPLS.
Label switching router (LSR): a routing device, such as a router or switch, that runs MPLS. An LSR that resides at the edge of an MPLS domain and connects to a non-MPLS network is called a label edge router (LER). An LSR that resides inside an MPLS domain is called a core LSR.
MPLS Domain
LER
Core LSR
LER
IP network
IP network
IP
Packet
MPLS
Header
Ethernet
Header

## Slide 10: MPLS Terms - LSR Classification
In addition to location-based LSR classification, LSRs can also be classified according to data processing modes:
  Ingress LSR: generally pushes an MPLS header into an IP packet and generates an MPLS packet.
  Transit LSR: generally pushes a label, swaps a label, or pops out a label in a received MPLS packet, and then forwards the packet inside the MPLS domain.
  Egress LSR: generally pops out an MPLS header to restore the IP packet.
MPLS Domain
Ingress LSR
Transit LSR
Egress LSR
IP network
IP network
IP
Packet
MPLS
Header
Ethernet
Header
Notes: MPLS label operations will be introduced in following courses.

## Slide 11: MPLS Terms - FEC
Forwarding equivalence class (FEC): a set of packets with similar or identical characteristics and forwarded in the same way by LSRs.
  On an MPLS network, FECs can be classified based on destination IP addresses, network masks, DSCP values, and so on.
  When a packet enters an MPLS domain, the ingress LSR determines the LSP to which the packet belongs.
  MPLS labels match FECs. A mechanism must be available for LSRs to obtain label information about FECs.
IP network
IP network
3.3.3.0/24
MPLS Domain
Destination: 3.3.3.3
Ingress LSR
Transit LSR
Egress LSR
The ingress LSR determines the LSP to which the data belongs and adds a label to the packet.
IP
Packet
MPLS
Header
Ethernet
Header
Notes: In traditional IP forwarding that uses the longest match algorithm, all packets that match the same route belong to the same FEC.
In MPLS, the most common example of FEC is: Packets whose destination IP addresses match the same IP route are considered to belong to the same FEC.

## Slide 12: MPLS Terms - LSP
Label switched path (LSP): a path through which a labeled packet traverses an MPLS domain to reach a destination.
The packets of the same FEC usually traverse an MPLS domain through the same LSP. Therefore, an LSR always uses the same label to forward the packets of the same FEC.
MPLS Domain
IP network
3.3.3.0/24
R1
R2
R3
R4
R5
R6
R7
IP network
1.1.1.0/24
IP network
2.2.2.0/24
IP
Packet
MPLS
Header
Ethernet
Header
Destination: 3.3.3.3
Destination: 3.3.3.3
R8
LSP1
LSP2
Notes: An LSP is composed of an ingress LSR, an egress LSR, and a variable number of transit LSRs. Therefore, an LSP can be considered as an ordered set of these LSRs.
An LSP must be established before a packet is forwarded; otherwise, the packet fails to traverse an MPLS domain.
LSPs can be established in static or dynamic mode.
An LSP is a unidirectional path from the start point to the end point. If bidirectional data communication is required, an LSP for return traffic needs to be established between the two ends.

## Slide 13
MPLS Basics
  MPLS Overview
  MPLS Terms
  MPLS Labels
MPLS basic principles
Static LSP Configuration

## Slide 14: MPLS Labels
Before an IP packet enters an MPLS domain, the ingress LSR pushes an MPLS header (also called an MPLS label) into the packet to form an MPLS labeled packet. An MPLS labeled packet can contain one or more labels.
Label: carries a label value and is 20 bits long.
Experimental use (EXP): is mainly used for class of service (CoS) and is 3 bits long.
Bottom of stack (S): indicates whether a label header is the last label and is 1 bit long. If its value is 1, the current label header is at the bottom of the label stack. If its value is 0, the current label header is not at the bottom and is followed by other label headers.
Time to live (TTL): prevents a labeled packet from being infinitely forwarded when a loop occurs. It is 8 bits long and has the same meaning as the TTL field in an IP packet header.
IP header
Payload
Layer 2 frame header
Label header
MPLS labeled packet
Label
EXP
S
TTL
A label is inserted between the Layer 2 frame header and the IP header.
32 bits
Notes: The EXP field is defined in early MPLS standards and is an experimental field. Actually, this field is mainly used for CoS. To avoid ambiguity, this field is renamed Traffic Class in RFC 5462.

## Slide 15: MPLS Label Stack
MPLS allows one or more layers of label headers to be added in a packet. The ordered set of these label headers is called label stack.
When there are multiple labels in the label stack:
  The label closest to the Layer 2 header is the top label, and the S field in the label is 0.
  The label closest to the IP header is the bottom label, and the S field in the label is 1.
Label header 2
Label header 3
Layer 2 frame header
Label header 1
IP header
Payload
Label
EXP
1
TTL
Label
EXP
0
TTL
Label
EXP
0
TTL
Label stack
Stack top
Stack bottom
Notes: When the upper layer is the MPLS label stack, the Type field in the Ethernet header is 0x8847, and the Protocol field in the PPP header is 0x8281.

## Slide 16: Label Space
A label is a short and fixed-length identifier that has only local significance. A label space means a label value range. The label value range and planning are as follows:
Label Value | Description
0 to 15 | Special label values. For example, 0 indicates an IPv4 explicit null label, and 3 indicates an implicit null label.
16 to 1023 | Label space shared by static LSPs and static CR-LSPs.
1024 to 1048575 | Label space for dynamic signaling protocols, such as Label Distribution Protocol (LDP), Resource Reservation Protocol-Traffic Engineering (RSVP-TE), and Multiprotocol Extensions for Border Gateway Protocol (MP-BGP). Each dynamic signaling protocol uses an independent and contiguous label space, which is not shared with other dynamic signaling protocols.
Notes: The label spaces of different LSRs are independent of each other, indicating that each router can use the entire label space.

## Slide 17: MPLS Label Processing
LSRs can perform the following operations on labels: push, swap, and pop.
Push
Pop
Swap
IP
IP
300
Push
IP
400
Push
IP
400
300
When an IP packet enters an MPLS domain, the ingress adds a label between the Layer 2 frame header and IP header of the packet. When the packet reaches a transit node, the transit node can also add a new label at the top of the label stack.
IP
300
Swap
IP
200
IP
400
Swap
300
IP
400
200
When the packet is forwarded inside the MPLS domain, a transit node searches the label forwarding table and replaces the top label with the label that is assigned by the next hop.
IP
Pop
IP
300
Pop
IP
400
300
IP
400
Before the packet leaves the MPLS domain, the egress removes the label of the MPLS packet.

## Slide 18
MPLS Basics
MPLS Forwarding
Static LSP Configuration

## Slide 19: MPLS Forwarding Overview
The essence of MPLS forwarding is to categorize a packet into the corresponding FEC and forward it based on the LSP pre-established for this FEC.
  For the entire MPLS domain, an LSP is the path through which a packet enters and leaves the domain. An LSP can be considered as an ordered set of LSRs.
  For a single LSR, it needs to establish a label forwarding table, use labels to identify FECs, and bind label processing and forwarding behaviors to the FECs.
R2
R3
R1
R4
MPLS Domain
IP network
1.1.1.0/24
Destination: 4.4.4.4
IP network
2.2.2.0/24
Destination: 4.4.4.4
IP network
3.3.3.0/24
Destination: 4.4.4.4
IP network
4.4.4.0/24
FEC1
Label: 100
LSP1: {R1, R2, R3, R4}
FEC1
Label: 100
LSP2: {R2, R3, R4}
FEC1
Label: 200
LSP3: {R3, R4}
Basic Concepts
LSP Establishment
Label-based Forwarding
Notes: If the ingress LSRs of packets belonging to the same FEC are different, the LSPs for forwarding the packets are different.
An LSR uses the same way to process packets in the same FEC, regardless of where the packets' inbound interfaces are the same.
An LSP is composed of the forwarding actions of LSRs, and the label forwarding table determines the forwarding action. Therefore, establishing a label forwarding table can also be considered as establishing an LSP.
As shown in the figure, the three packets belong to the same FEC, FEC1, because they have the same destination. However, as their ingress LSRs are different, the packets are forwarded along different LSPs (LSP1, LSP2, and LSP3, respectively). The labels assigned by different LSRs to the same FEC can be the same or different, because labels are valid only on their local LSRs.

## Slide 20: MPLS Architecture
The MPLS architecture consists of a control plane and a forwarding plane.
User plane
Control plane
LIB
LDP
RIB
IP routing protocols
FIB
LFIB
Control plane:
Generates and maintains routing information and label information.
Runs IP routing protocols and LDP, and stores a RIB and a LIB.
Forwarding plane (also called data plane)
Forwards common IP packets and MPLS labeled packets.
Stores a FIB and an LFIB.
Basic Concepts
LSP Establishment
Label-based Forwarding
Notes: Control plane:
  The control plane is connectionless. It generates and maintains routing and label information.
  The control plane includes:
    Routing information base (RIB): stores static routes, direct routes, and routes generated by IP routing protocols. Routes can be selected from the RIB to guide packet forwarding.
    Label information base (LIB): stores and manages labels statically configured and dynamically generated by label switching protocols (such as LDP and RSVP).
Forwarding plane
  The forwarding plane, also called the data plane, is connection-oriented. It forwards common IP packets and MPLS labeled packets.
  The forwarding plane includes:
    Forwarding information base (FIB): stores forwarding information that is generated based on the routing information extracted from the RIB. The forwarding information is used to guide common IP packet forwarding.
    Label forwarding information base (LFIB): stores label-based forwarding information to guide MPLS labeled packet forwarding.

## Slide 21: Control Plane and Forwarding Plane
User plane
Control plane
LDP
RIB
IP routing protocols
FIB
LFIB
Routing information exchange
Label information exchange
User plane
Control plane
LDP
RIB
IP routing protocols
FIB
LFIB
Incoming IP data packet
Outgoing IP data packet
Incoming labeled packet
Outgoing labeled packet
Exchanging Route and Label Information
Transmitting IP Data Packets and MPLS Labeled Data Packets
Basic Concepts
LSP Establishment
Label-based Forwarding

## Slide 22: LSP Establishment Principles
When the network layer protocol is IP, the route for a FEC must exist in the IP routing table of an LSR. Otherwise, the label forwarding entry of the FEC does not take effect.
An LSR uses labels to identify a FEC, and it can correctly process an incoming packet of a FEC only if the packet carries the correct label.
FEC: 4.4.4.0/24
Out Label=1027
In Label=Null
FEC: 4.4.4.0/24
Out Label=1026
In Label=1027
FEC: 4.4.4.0/24
Out Label=1025
In Label=1026
FEC: 4.4.4.0/24
Out Label=Null
In Label=1025
R2
R3
R1
R4
MPLS Domain
IP network
1.1.1.0/24
Destination: 4.4.4.4
IP network
4.4.4.0/24
A device provides an incoming label and an outgoing label for each FEC. The incoming label indicates the one that needs to be carried in a received packet. The outgoing label indicates the one that needs to be carried in a sent packet.
Assume that a packet destined for 4.4.4.0/24 is sent from R1 to R2. R1 is the upstream LSR of R2, and R3 is the downstream LSR of R2. To ensure that a labeled packet is correctly processed and forwarded, the outgoing label carried in the packet sent from R1 to R2 must be the same as the incoming label on R2 for the FEC to 4.4.4.0/24. Similarly, the outgoing label on R2 for the FEC to 4.4.4.0/24 must be the same as the incoming label of R3.
Basic Concepts
LSP Establishment
Label-based Forwarding

## Slide 23: LSP Establishment Methods
MPLS needs to distribute labels to packets and establish LSPs before it can forward packets. LSPs can be either static or dynamic.
Static LSP
Basic concepts:
A static LSP is established by manually configuring labels for a FEC.
The establishment of static LSPs does not involve label distribution protocols or control packet exchanging. Therefore, this LSP establishment mode consumes less resources.
Static LSPs cannot adapt to network topology changes, and require manual adjustment when the network topology changes.
Application scenarios:
Stable and small-sized network with a simple topology
Label distribution principles:
A packet's outgoing label value on the current node should be the same as the incoming label value on the next hop.
Dynamic LSP
Basic concepts:
Dynamic LSPs are established automatically by a label distribution protocol.
Label distribution protocols, also called signaling protocols, are MPLS control protocols used to identify FECs, distribute labels, and create and maintain LSPs.
Common label distribution protocol: LDP
Full name: Label Distribution Protocol
Definition: LDP is a control protocol for MPLS. It is responsible for FEC classification, label distribution, and LSP establishment and maintenance. LDP defines the messages used in label distribution and how to process these messages.
Application scenario: LDP is widely in VPN scenarios as it features simple networking and configuration, supports dynamic establishment of LSPs based on routes, and supports a large number of LSPs.
Basic Concepts
LSP Establishment
Label-based Forwarding
Notes: Static LSP:
  A static LSP is meaningful only to the local node, and the local node cannot be aware of the entire LSP.
Dynamic LSP:
  Other label distribution protocols:
    Resource Reservation Protocol-Traffic Engineering (RSVP-TE): an extension based on RSVP. RSVP-TE is used to establish constraint-based routed LSPs (CR-LSPs). Unlike LDP LSPs, CR-LSPs support parameters, such as bandwidth reservation requests, bandwidth constraints, link colors, and explicit paths.
    Multiprotocol Border Gateway Protocol (MP-BGP): an extension based on BGP. MP-BGP distributes labels to MPLS VPN routes and inter-AS VPN labeled routes.

## Slide 24: MPLS Label-based Forwarding
An LSR processes packets mainly based on the FTN, NHLFE, and ILM.
FTN
FEC-to-NHLFE (FTN): is used when an LSR receives an IP packet and needs to perform MPLS forwarding. FTNs exist only on ingresses.
An FTN contains a tunnel ID and mapping from an FEC to an NHLFE.
NHLFE
Next hop label forwarding entry (NHLFE): is used when an LSR performs MPLS forwarding for a packet (MPLS or IP packet). NHLFEs exist on ingresses and transit nodes.
An NHLFE contains the following information: tunnel ID, outbound interface, next hop, outgoing label, and label operation type.
ILM
Incoming label map (ILM): guides MPLS packet forwarding (MPLS or IP forwarding). ILMs exist only on egresses and transit nodes.
An ILM contains the following information: tunnel ID, incoming label, inbound interface, and label operation type.
Out IF | Tunnel ID | NH | Out Label
In Label | In IF | Tunnel ID | OPER
FEC | Tunnel ID
An ingress searches its FIB for the entry with a non-0x0 tunnel ID to learn detailed FTN information.
1
A transit node searches for an NHLFE that matches the tunnel ID in the ILM table.
2
The OPER field in the ILM table on an egress is Pop. If a packet contains only one label, the egress removes it and then performs IP forwarding.
3
Basic Concepts
LSP Establishment
Label-based Forwarding
Notes: Tunnel ID: an ID automatically allocated to a tunnel, providing a unified interface for upper-layer applications (such as VPN and route management) that use the tunnel. A tunnel ID is 32 bits long and is valid only on the local device. During MPLS forwarding, LSRs find matching FIB entries, ILMs, and NHLFEs based on tunnel IDs.

## Slide 25: Packet Processing on an Ingress LSR
IF1
3.3.3.1/24
Push
IP: 3.3.3.1
IP: 3.3.3.1
Z
IP: 3.3.3.1
Y
IP: 3.3.3.1
Ingress
Transit
Egress
IF2
IF1
IF2
IF1
IF2
1.1.1.1/24
1.1.1.2/24
2.2.2.1/24
2.2.2.2/24
DEST | Tunnel ID
3.3.3.1/24 | 0x11
FIB
Out IF | Tunnel ID | OPER | NH | Out Label
IF2 | 0x11 | Push | 1.1.1.2 | Z
NHLFE
1
2
When an IP packet enters an MPLS domain:
The ingress LSR searches the FIB table and checks whether the tunnel ID corresponding to the destination IP address is 0x0. If the tunnel ID is 0x0, the ingress LSR performs IP forwarding for the packet.
If the tunnel ID is not 0x0, the ingress searches for the NHLFE matching the tunnel ID in the FIB table, and associates the FIB entry with the NHLFE.
The ingress LSR checks the NHLFE to learn the outbound interface, next hop, outgoing label, and label operation type.
The ingress LSR pushes an outgoing label into the IP packet, processes the TTL, and then sends the encapsulated MPLS packet to the next hop.
3
4
Note:
NH=NEXTHOP
IF=Interface
Basic Concepts
LSP Establishment
Label-based Forwarding
Notes: An ingress LSR searches the FIB table (to learn FTN information) and NHLFE table to guide packet forwarding.
When an IP packet enters an MPLS domain, the ingress searches the FIB to check whether the tunnel ID corresponding to the destination IP address is 0x0.
  If the tunnel ID is 0x0, the ingress LSR performs IP forwarding for the packet.
  If the tunnel ID is not 0x0, the ingress LSR performs MPLS forwarding for the packet.

## Slide 26: Packet Processing on a Transit LSR
NHLFE
IF1
3.3.3.1/24
Push
IP: 3.3.3.1
IP: 3.3.3.1
Z
IP: 3.3.3.1
Y
IP: 3.3.3.1
Swap
Ingress
Transit
Egress
IF2
IF1
IF2
IF1
IF2
1.1.1.1/24
1.1.1.2/24
2.2.2.1/24
2.2.2.2/24
In Label | In IF | Tunnel ID
Z | IF1 | 0x15
ILM
Out IF | Tunnel ID | OPER | NH | Out Label
IF2 | 0x15 | Swap | 2.2.2.2 | Y
5
6
7
When an MPLS packet is forwarded in an MPLS domain:
The transit LSR searches for the ILM that matches the MPLS label value to learn the tunnel ID.
The transit LSR searches for the NHLFE that matches the tunnel ID in the ILM table.
The transit LSR checks the NHLFE to learn the outbound interface, next hop, outgoing label, and label operation type. If the label operation type is Swap, the transit LSR performs label swapping.
Note:
NH=NEXTHOP
IF=Interface
Basic Concepts
LSP Establishment
Label-based Forwarding
Notes: A transit LSR searches for ILMs and NHLFEs to guide MPLS packet forwarding.

## Slide 27: Packet Processing on an Egress LSR
IF1
3.3.3.1/24
Push
IP: 3.3.3.1
IP: 3.3.3.1
Z
IP: 3.3.3.1
Y
IP: 3.3.3.1
Swap
Ingress
Transit
Egress
IF2
IF1
IF2
IF1
IF2
1.1.1.1/24
1.1.1.2/24
2.2.2.1/24
2.2.2.2/24
In Label | In IF | Tunnel ID | OPER
Y | IF1 | 0x22 | 
ILM
8
When an MPLS packet leaves an MPLS domain:
An egress LSR searches the ILM table for the operation type that matches the FEC of the packet. The operation type is always pop on an egress LSR. As such, the egress LSR removes the label from the packet.
The egress LSR performs further processing based on the inner header in the packet.
Note:
NH=NEXTHOP
IF=Interface
Pop
S = 1: The current label is the bottom label, and IP forwarding is performed for the packet.
S = 0: The current label is not the bottom label, and a lower-layer label exists. In this case, the packet is performed based on the lower-layer label.
9
Basic Concepts
LSP Establishment
Label-based Forwarding
Notes: The egress LSR searches the ILM table to guide MPLS packet forwarding.

## Slide 28: Detailed MPLS Packet Forwarding Process
IF1
3.3.3.1/24
Push
Note:
NH=NEXTHOP
IF=Interface
IP: 3.3.3.1
IP: 3.3.3.1
Z
IP: 3.3.3.1
Y
IP: 3.3.3.1
Swap
Ingress
Transit
Egress
IF2
IF1
IF2
IF1
IF2
1.1.1.1/24
1.1.1.2/24
2.2.2.1/24
2.2.2.2/24
DEST | Tunnel ID
3.3.3.1/24 | 0x11
In Label | In IF | Tunnel ID
Z | IF1 | 0x15
In Label | In IF | Tunnel ID
Y | IF1 | 0x22
FIB
LIM
Out IF | Tunnel ID | OPER | NH | Out Label
IF2 | 0x15 | Swap | 2.2.2.2 | Y
Out IF | Tunnel ID | OPER | NH | Out Label
IF2 | 0x11 | Push | 1.1.1.2 | Z
NHLFE
1
2
4
5
6
7
8
9
Performs further processing based on the inner packet header.
Basic Concepts
LSP Establishment
Label-based Forwarding

## Slide 29
MPLS Basics
MPLS Forwarding
Static LSP Configuration

## Slide 30: Basic MPLS Configuration Commands
[Huawei] mpls lsr-id lsr-id
Set an LSR ID.
The mpls lsr-id command sets an LSR ID. An LSR ID uniquely identifies an LSR on a network. By default, no LSR ID is set for an LSR, and an LSR ID can only be manually set. To improve network reliability, you are advised to use the IP address of a loopback interface on an LSR as the LSR ID and plan the LSR IDs of all LSRs on the network in a unified manner before configuration.
[Huawei] mpls
Enable MPLS.
The mpls command enables MPLS on the current node and displays the MPLS view.
[Huawei-GigabitEthernet0/0/0] mpls
Enable MPLS on an interface. Before running this command, enable MPLS globally.

## Slide 31: Static LSP Configuration Commands (1)
[Huawei] static-lsp ingress lsp-name destination ip-address { mask-length | mask } { nexthop next-hop-address | outgoing-interface interface-type interface-number } * out-label out-label
Configure a static LSP on an ingress LSR.
The static-lsp ingress command configures a static LSP on an ingress.
You are advised to specify the next-hop parameter to configure a static LSP. This ensures that the local routing table contains the routing entry that exactly matches the specified destination IP address and next-hop IP address. If the outbound interface of the LSP is an Ethernet interface, you must specify nexthop next-hop-address to ensure normal forwarding along the LSP.
The value of out-label ranges from 16 to 1048575.
[Huawei] static-lsp transit lsp-name [ incoming-interface interface-type interface-number ] in-label in-label { nexthop next-hop-address | outgoing-interface interface-type interface-number }* out-label out-label
Configure a static LSP on a transit LSR.
The static-lsp transit command configures a static LSP on a transit node.
The configuration rules of the next hop and outbound interface are the same as those for an ingress LSR.
The value of in-label ranges from 16 to 1023.
The value of out-label ranges from 16 to 1048575.
Notes: An outgoing label occupies the label space of the downstream LSR, but the label distribution mode used by the downstream space is uncertain. As such, the value of an outgoing label ranges from 16 to 1048575.
An incoming label occupies the label space of the current LSR. When a static LSP is used, the value of an incoming label ranges from 16 to 1023.

## Slide 32: Static LSP Configuration Commands (2)
[Huawei] static-lsp egress lsp-name [ incoming-interface interface-type interface-number ] in-label in-label
Configure a static LSP on an egress LSR.
The static-lsp egress command configures a static LSP on an egress LSR.
The value of in-label ranges from 16 to 1023.
[Huawei] display mpls static-lsp [ lsp-name ] [ { include | exclude } ip-address mask-length ] [ verbose ]
Check information about static LSPs.
The display mpls static-lsp command displays information about static LSPs.

## Slide 33: Static LSP Configuration Example (1)
Use case: An IGP has been deployed on R1, R2, and R3. The networks 1.1.1.0/24 and 3.3.3.0/24 can communicate with each other. In this scenario, configure static LSPs to allow the two networks to communicate through MPLS. The following figure shows the distributed labels.
Configuration roadmap:
  Enable MPLS on the devices and interfaces.
  Configure static LSPs as planned.
FEC: 3.3.3.0/24
Out Label=200
In Label=Null
FEC: 3.3.3.0/24
Out Label=300
In Label=200
FEC: 3.3.3.0/24
Out Label=Null
In Label=300
R2
R1
R3
MPLS Domain
IP network
1.1.1.0/24
IP network
3.3.3.0/24
LSP
GE0/0/0
10.0.12.1/24
GE0/0/0
10.0.12.2/24
GE0/0/1
10.0.23.2/24
GE0/0/0
10.0.23.3/24

## Slide 34: Static LSP Configuration Example (2)
FEC: 3.3.3.0/24
Out Label=200
In Label=Null
FEC: 3.3.3.0/24
Out Label=300
In Label=200
FEC: 3.3.3.0/24
Out Label=Null
In Label=300
R2
R1
R3
MPLS Domain
IP network
1.1.1.0/24
IP network
3.3.3.0/24
LSP
GE0/0/0
10.0.12.1/24
GE0/0/0
10.0.12.2/24
GE0/0/1
10.0.23.2/24
GE0/0/0
10.0.23.3/24
The LSR IDs of the three routers are 10.1.1.1, 10.1.1.2, and 10.1.1.3, respectively. The following example uses R1 to describe the configuration. Enable MPLS globally and on interfaces on R1.
[R1]mpls lsr-id 10.1.1.1
[R1]mpls
Info: Mpls starting, please wait... OK!
[R1-mpls]quit
[R1]interface GigabitEthernet 0/0/0
[R1-GigabitEthernet0/0/0]mpls
[R1-GigabitEthernet0/0/0]quit]

## Slide 35: Static LSP Configuration Example (3)
FEC: 3.3.3.0/24
Out Label=200
In Label=Null
FEC: 3.3.3.0/24
Out Label=300
In Label=200
FEC: 3.3.3.0/24
Out Label=Null
In Label=300
R2
R1
R3
MPLS Domain
IP network
1.1.1.0/24
IP network
3.3.3.0/24
LSP
GE0/0/0
10.0.12.1/24
GE0/0/0
10.0.12.2/24
GE0/0/1
10.0.23.2/24
GE0/0/0
10.0.23.3/24
Configure a static LSP from R1 to R3.
[R1] static-lsp ingress 1to3 destination 3.3.3.0 24 nexthop 10.0.12.2 out-label 200
[R2] static-lsp transit 1to3 incoming-interface GigabitEthernet 0/0/0 in-label 200 nexthop 10.0.23.3 out-label 300
[R3] static-lsp egress 1to3 incoming-interface GigabitEthernet 0/0/0 in-label 300

## Slide 36: Static LSP Configuration Example - Checking the Configuration
[R1]display mpls lsp
---------------------------------------------------------------------
LSP Information: STATIC LSP
---------------------------------------------------------------------
FEC In/Out Label In/Out IF Vrf Name
3.3.3.0/24 NULL/200 -/GE0/0/0
[R3]display mpls lsp
---------------------------------------------------------------------
LSP Information: STATIC LSP
---------------------------------------------------------------------
FEC In/Out Label In/Out IF Vrf Name
3.3.3.0/24 300/NULL GE0/0/0/-
[R2]display mpls lsp
---------------------------------------------------------------------
LSP Information: STATIC LSP
---------------------------------------------------------------------
FEC In/Out Label In/Out IF Vrf Name
3.3.3.0/24 200/300 GE0/0/0/GE0/0/1
The ping test from the host on the 1.1.1.0/24 network segment to the host on the 3.3.3.0/24 network segment is successful.
Why can bidirectional communication be implemented when only a unidirectional static LSP from 1.1.1.0/24 to 3.3.3.0/24 is configured?

## Slide 37: Static LSP Configuration Example - Packet Header Obtaining Analysis
According to the obtained packet information, the packets from the host on the 1.1.1.0/24 network segment to the host on the 3.3.3.0/24 network segment are forwarded based on MPLS labels.
The packets from the host on the 3.3.3.0/24 network segment to the host on the 1.1.1.0/24 network segment are forwarded based on IP packet headers.
No. Time Source Destination Protocol Length Info
5 12.109000 1.1.1.1 3.3.3.3 ICMP 102 Echo (ping) request
Frame 5: 102 bytes on wire (816 bits), 102 bytes captured (816 bits) on interface 0
Ethernet II, Src: HuaweiTe_b1:15:3e (00:e0:fc:b1:15:3e), Dst: HuaweiTe_49:20:bb (00:e0:fc:49:20:bb)
MultiProtocol Label Switching Header, Label: 300, Exp: 0, S: 1, TTL: 254
Internet Protocol Version 4, Src: 1.1.1.1, Dst: 3.3.3.3
Internet Control Message Protocol
No. Time Source Destination Protocol Length Info
6 12.141000 3.3.3.3 1.1.1.1 ICMP 98 Echo (ping) reply
Frame 6: 98 bytes on wire (784 bits), 98 bytes captured (784 bits) on interface 0
Ethernet II, Src: HuaweiTe_49:20:bb (00:e0:fc:49:20:bb), Dst: HuaweiTe_b1:15:3e (00:e0:fc:b1:15:3e)
Internet Protocol Version 4, Src: 3.3.3.3, Dst: 1.1.1.1
Internet Control Message Protocol

## Slide 38
(Multi-Answer) Which of the following statements about an MPLS header are correct?
  An MPLS header is 32 bits long.
  The value of the Label field in an MPLS header ranges from 0 to 65535.
  MPLS can implement multi-layer MPLS header nesting.
  The max_hop field in an MPLS header can be used to prevent labeled packets from being infinitely forwarded.
(Single-Answer) The values of the incoming and the outgoing label both range from 16 to 1023 for a static LSP to be configured on a transit LSR.
  True
  False
Notes: AC
B

## Slide 39
MPLS was originally proposed to solve the problem of low forwarding speed of traditional IP routers. MPLS implements fast forwarding through label headers.
An MPLS label is a short and fixed-length identifier that has only local significance. It is used to uniquely identify the FEC to which a packet belongs. Label operations on an LSR include push, swap, and pop.
MPLS consists of the control plane and data plane. The control plane transmits routing information and distributes labels, and the data plane forwards data.
With the development of technologies, the advantage of MPLS in the data forwarding speed is weakened gradually, but MPLS is widely used in the VPN area due to its pros.