## Slide 1
Zhang Linrui/zwx570554
2020.06
Chen Qibiao/cwx47601
2020.03
Zhu Shigeng/z00261992
New

## Slide 2: LDP Principles and Configurations

## Slide 3
Multiprotocol Label Switching (MPLS) implements data forwarding based on short and fixed-length labels carried in packets.
A fundamental concept in MPLS is that two LSRs must agree on the meaning of the labels used to forward traffic between them. The Label Distribution Protocol (LDP) can be used by an LSR to send its label binding information to other LDP-capable LSRs, helping implement correct forwarding of labeled packets.
This course describes the principles, features, and basic configurations of LDP.
Notes: LDP mentioned in this course refers to that defined in RFC 3036 for the first time. This protocol has been replaced by RFC 5036.
Other label distribution protocols include MP-BGP and RSVP.

## Slide 4
On completion of this course, you will be able to:
  Understand LDP's basic concepts and working mechanisms.
  Describe the MPLS label distribution control mode, advertisement mode, and retention mode.
  Perform basic LDP configurations.

## Slide 5
Basic LDP Concepts
LDP Principles
Basic LDP Configurations

## Slide 6: LDP Overview
LDP is an MPLS control protocol, which is similar to a signaling protocol on a traditional network. LDP is responsible for FEC classification, label distribution, and LSP establishment and maintenance. LDP defines the messages used in label distribution as well as the message processing procedures.
The working process of LDP involves:
  LDP session establishment between LSRs
  Dynamic exchange of FEC-label mapping information between LSRs over LDP sessions, as well as LSP establishment based on label information
FEC: 192.168.3.0/24
Incoming label: 1024
192.168.3.0/24
192.168.1.0/24
R1
R2
R3
FEC: 192.168.1.0/24
Incoming label: 1024
LDP session
LDP session
FEC: 192.168.3.0/24
Incoming label: 1025
FEC: 192.168.1.0/24
Incoming label: 1026
Question: LSRs exchange incoming labels only. What about outgoing labels?

## Slide 7: LDP Session, Adjacency, and Peer
An LDP session must be established before LSRs can exchange label binding information. LDP sessions are classified into the following types:
  Local LDP session: can be established between two LSRs that are directly connected.
  Remote LDP session: can be established between two LSRs that are directly or indirectly connected.
An adjacency is established between two LSRs after they exchange Hello messages.
After an adjacency is established between two LSRs, they exchange LDP session messages to establish an LDP session. An LDP peer relationship is then established between them.
Local LDP session
Remote LDP session
192.168.3.0/24
192.168.1.0/24
R1
R2
R3
Label distribution
Label distribution
Label distribution

## Slide 8: LSR ID and LDP ID
Each LDP-capable LSR must have an LDP ID, in addition to an LSR ID.
  An LDP ID is 48 bits long and consists of a 32-bit LSR ID and a 16-bit label space ID.
  An LDP ID is presented in the format of "LSR ID:Label space ID", for example, 2.2.2.2:0.
The meaning of a label space ID varies according to its value:
  0: indicates a device-based label space.
  Non-zero value: indicates an interface-based label space.
R1
R2
GE0/0/0
10.0.12.1/24
GE0/0/0
10.0.12.2/24
LSR ID 1.1.1.1
LDP ID 1.1.1.1:0
LSR ID 2.2.2.2
LDP ID 2.2.2.0:0
LSR ID (32 bits):Label space ID (16 bits)
Notes: This course takes the device-based label space as an example.

## Slide 9: LDP Messages
LDP-capable LSRs exchange LDP messages to discover peers, establish and maintain sessions, and manage labels.
Message Category | Message Name | Transport Layer Protocol | Function
Discovery message | Hello | UDP | Advertises local LSRs and discovers peers in the LDP discovery process.
Session message | Initialization | TCP | Negotiates parameters in an LDP session establishment process.
 | KeepAlive |  | Monitors the TCP connection integrity of LDP sessions.
Advertisement message | Address |  | Advertises interface addresses.
 | Address Withdraw |  | Withdraws interface addresses.
 | Label Mapping |  | Advertises FEC-label mapping information.
 | Label Request |  | Requests label mappings for FECs.
 | Label Abort Request |  | Aborts undone Label Request messages.
 | Label Withdraw |  | Withdraws FEC-label mappings.
 | Label Release |  | Releases labels.
Notification message | Notification |  | Informs LDP peers of errors.
Notes: LDP messages are classified into four types by function: discovery, session, advertisement, and notification.
  Discovery messages: announce and maintain the presence of LSRs on a network. Hello messages belong to this category.
  Session messages: establish, maintain, and terminate sessions between LDP peers. Initialization and KeepAlive messages belong to this category.
  Advertisement messages: generate, change, and delete label mappings for FECs.
  Notification messages: provide advisory information and signal error information.
LDP messages are carried over UDP or TCP, with the port number being 646. Discovery messages, which are used to discover peers, are carried over UDP. Other LDP messages must be transmitted in a reliable and ordered manner. Therefore, LDP uses TCP to establish sessions. Session, advertisement, and notification messages are transmitted over TCP.

## Slide 10: LDP Packet Encapsulation
An LDP packet consists of an LDP header and an LDP message.
  An LDP header carries information such as the LDP version and packet length.
  An LDP message carries information such as the message type and message length.
2 bytes
2 bytes
6 bytes
2 bytes
2 bytes
4 bytes
Variable length
Variable length
Variable length
IP Header
TCP/UDP Header
LDP Header
LDP Message
10 bytes
Version
PDU Length
LDP Identifier
Type
Message Length
Message ID
U
1 bit
Mandatory Parameters
Optional Parameters
Notes: An LDP header is 10 bytes long. It consists of three parts: Version, PDU Length, and LDP Identifier.
  The Version field occupies 2 bytes. It indicates the LDP version number. The current version number is 1.
  The PDU Length field occupies 2 bytes. It indicates the packet length in bytes, excluding the Version and PDU Length fields.
  The LDP Identifier field (that is, LDP ID) occupies 6 bytes. The first 4 bytes uniquely identify an LSR, and the last 2 bytes identify the label space of the LSR.
An LDP message consists of five parts.
  The U field occupies 1 bit, which is an unknown message. When an LSR receives an unknown message, the LSR returns a notification message to the message originator if the U field is 0, but ignores the message and does not respond with a notification message if the U field is 1.
  Message Length occupies 2 bytes. It indicates the total length of Message ID, Mandatory Parameters, and Optional Parameters, in bytes.
  Message ID occupies 32 bits. It identifies a message.
  Each of the Mandatory Parameters and Optional Parameters fields has a variable length.
  Message Type indicates a specific message type. Currently, common messages defined by LDP include Notification, Hello, Initialization, KeepAlive, Address, Address Withdraw, Label Mapping, Label Request, Label Abort Request, Label Withdraw, and Label Release.

## Slide 11
Basic LDP Concepts
LDP Principles
  LDP Session Establishment
  LDP-based Label Distribution
  LDP Working Process
Basic LDP Configurations

## Slide 12: LDP Session State Machine
LDP uses five states to describe the LDP session state machine.
All other LDP messages
Non-Existent
OpenSent
OpenRec
TCP connection setup
A received message is not an Initialization message, or no message is received.
The passive LSR receives an acceptable Initialization message.
Action: Sends Initialization and KeepAlive messages.
Active LSR
Action: Sends an Initialization message.
A received message is not an Initialization message, or no message is received.
Action: Sends an NAK message.
An acceptable Initialization message is received.
Action: Sends a KeepAlive message.
A KeepAlive message is received.
Action: none
Operational
A received message is a Shutdown message , or no message is received.
Action: Sends a Shutdown message.
A received message is not a KeepAlive message, or no message is received.
Action: Sends an NAK message.
Initialized
1
2
3
3
4
Notes: The LDP session negotiation process can be described through the state machine. As shown in the figure, there are five states. They are Non-Existent, Initialized, OpenRec, OpenSent, and Operational.
  Non-Existent: It is the initial state of an LDP session. In this state, both LSRs send Hello messages to elect the active LSR. After a TCP connection establishment success event is received, the state changes to Initialized.
  Initialized: In this state, the active LSR sends an Initialization message to the passive LSR, sets the session state to OpenSent, and waits for an Initialization message. The passive LSR waits for the Initialization message sent by the active LSR. If the parameters in the received Initialization message are accepted, the passive LSR sends Initialization and KeepAlive messages, and sets the session state to OpenRec. When the active and passive LSRs receive any non-initialization message or the waiting period times out, both of them set the session state to Non-Existent.
  OpenSent: It is a state after the active LSR sends an Initialization message. In the OpenSent state, the active LSR waits for the passive LSR to respond to the Initialization and KeepAlive messages. If the parameters in the received Initialization message are accepted, the active LSR sets the session state to OpenRec. However, if the parameters are not accepted or the Initialization message times out, the active LSR tears down the TCP connection and sets the session state to Non-Existent.
  OpenRec: In this state, both the active and passive LSRs wait for a KeepAlive message from the peer end after they send KeepAlive messages. An LSR sets the session state to Operational state after receiving a KeepAlive message, but sets the session state to Non-Existent if a non-KeepAlive message is received or the KeepAlive message times out.

## Slide 13
Notes:   Operational: This state indicates that an LDP session is established successfully. In this state, all other LDP messages can be sent and received. The state changes to Non-Existent if a KeepAlive message times out, a notification message indicating a fatal error (such as a Shutdown message) is passively received, or a Shutdown message is actively sent to terminate the current session.
The LDP state change information can be viewed using the debug mpls ldp session command.

## Slide 14: LDP Session Establishment: Peer Discovery and TCP Session Establishment
Hello (UDP)
10.0.12.1:646 -> 224.0.0.2:646
Hello (UDP)
224.0.0.2:646 <-10.0.12.2 :646
TCP SYN
1.1.1.1:646 <- 2.2.2.2:22139
TCP SYN ACK
1.1.1.1:646 -> 2.2.2.2:22139
TCP ACK
2.2.2.2:22139 -> 1.1.1.1:646
The LSR with a larger transport address initiates a TCP connection request.
Transport address:
1.1.1.1
Transport address:
2.2.2.2
R1
R2
GE0/0/0
10.0.12.1
GE0/0/0
10.0.12.2
Non-Existent
Initialized
TCP Connection Establishment Phase
A Hello message carries a transport address, which will be used to establish an LDP session.
The LSR with a larger transport address is the active LSR and initiates a TCP connection request.
After the TCP three-way handshake, a TCP connection will be established.
Discovery phase
An LSR periodically sends LDP Link Hello messages to implement the basic LDP discovery mechanism.
LDP Link Hello messages are encapsulated in UDP packets, with the destination address being a multicast address 224.0.0.2. If an LSR receives LDP Link Hello messages on an interface, it indicates that this interface has established LDP peer relationships.
Discovery
Phase
TCP connection establishment phase
Notes: In addition to the basic discovery mechanism, the extended discovery mechanism is supported, which can be used to discover indirectly connected remote adjacencies. For details, see RFC 5036.
LDP transport addresses are used to establish TCP connections with peers.
  Before establishing an LDP session, two LSRs need to establish a TCP connection to exchange LDP packets.
  A transport address of an LSR is contained in LDP Hello messages, through which an LSR can learn the transport addresses of its peers.
  After two LSRs discover each other and learn each other's transport address through Hello messages, the LSRs attempt to perform the TCP three-way handshake (based on the transport addresses), and exchange LDP Initialization messages, Label Mapping messages, and so on. All these messages use the transport addresses of the two ends as source and destination IP addresses.
  An LSR must have a route to the transport address of its peer.
  By default, the transport address for a device on a public network is the LSR ID of the device, and the transport address for a device on a private network is the primary IP address of an interface on the device.
  The mpls ldp transport-address command can be run in the interface view to change a transport address.

## Slide 15: LDP Session Establishment - Session Establishment and Maintenance
Transport address:
1.1.1.1
Transport address:
2.2.2.2
GE0/0/0
10.0.12.1
GE0/0/0
10.0.12.2
Completion of peer discovery and TCP three-way handshake
Initialization
Sends an Initialization message to negotiate related parameters.
Initialization + KeepAlive
Replies with a KeepAlive message if the peer's parameters are accepted,
and initiates an Initialization message.
KeepAlive
Sends a KeepAlive message if these parameters are accepted.
R1
R2
OpenSent
OpenRec
The LDP session enters the Operational state.
After a TCP connection is established, R2 (active LSR with a larger transport address) sends an LDP Initialization message to negotiate parameters related to LDP session establishment.
These parameters include the LDP version, label distribution mode, KeepAlive timer value, maximum PDU length, and label space.
After R1 receives the Initialization message, it replies with a KeepAlive message if it accepts R2's parameters. To improve transmission efficiency, R1 also sends an Initialization message.
After R2 receives the Initialization message, it replies with a KeepAlive message if it accepts R1's parameters.
After both ends receive each other's KeepAlive message, the session is established successfully. They periodically send KeepAlive messages to maintain the session.
LDP session establishment phase

## Slide 16: LDP Peer State
PeerID: LDP ID of the peer
  2.2.2.2: LSR ID of the peer
  0: device-based label space
TransportAddress: transport address of the peer
  2.2.2.2: IP address used to establish a TCP connection
R1
R2
GE0/0/0
10.0.12.1/24
GE0/0/0
10.0.12.2/24
LSR ID 1.1.1.1
Transport address: 1.1.1.1
LSR ID 2.2.2.2
Transport address: 2.2.2.2
<R1>display mpls ldp peer
LDP Peer Information in Public network
A '*' before a peer means the peer is being deleted.
------------------------------------------------------------------------------
PeerID TransportAddress DiscoverySource
------------------------------------------------------------------------------
2.2.2.2:0 2.2.2.2 GigabitEthernet0/0/0
------------------------------------------------------------------------------
TOTAL: 1 Peer(s) Found.

## Slide 17: LDP Session States
Status: state of the LDP session
  Operational: The LDP session is established successfully.
LAM: label advertisement mode:
  There are two label advertisement modes: DU and DoD (described later).
  This example uses the DU mode.
  SsnRole: role that an LSR plays in an LDP session:
  Active and Passive indicate the active role and passive role in LDP session establishment, respectively.
<R1>display mpls ldp session
LDP Session(s) in Public Network
Codes: LAM(Label Advertisement Mode), SsnAge Unit(DDDD:HH:MM)
A '*' before a session means the session is being deleted.
------------------------------------------------------------------------------
PeerID Status LAM SsnRole SsnAge KASent/Rcv
------------------------------------------------------------------------------
2.2.2.2:0 Operational DU Passive 0000:00:33 133/133
------------------------------------------------------------------------------
TOTAL: 1 session(s) Found.
R1
R2
GE0/0/0
10.0.12.1/24
GE0/0/0
10.0.12.2/24
LSR ID 1.1.1.1
Transport address: 1.1.1.1
LSR ID 2.2.2.2
Transport address: 2.2.2.2
Notes: LDP session states:
  NonExistent: initial state of an LDP session. In this state, the two ends send Hello messages to each other. After the TCP connection establishment success event is triggered, the session enters the Initialized state.
  Initialized: The LDP session is being initialized.
  OpenSent: The active LSR sends an Initialization message to the passive LSR and waits for a reply.
  Open Recv: LDP peers at both ends of the LDP session wait for a KeepAlive message from each other after the session enters the initialization state. If they receive each other's KeepAlive message, the LDP session enters the Operational state.
  Operational: The LDP session is established successfully.

## Slide 18
Basic LDP Concepts
LDP Principles
  LDP Session Establishment
  LDP-based Label Distribution
  LDP Working Process
Basic LDP Configurations

## Slide 19: Label Advertisement and Management
On an MPLS network, a downstream LSR determines the bindings between labels and FECs and advertises the bindings to its upstream LSR.
To establish LSPs, LDP sends Label Request and Label Mapping messages to advertise the bindings between labels and FECs.
Label advertisement and management are determined by the label advertisement mode, label distribution control mode, and label retention mode.
Item | Mode | Default Mode (Yes/No)? | Description
Label advertisement mode | Downstream unsolicited (DU) | Yes | An LSR assigns and distributes labels to a FEC without receiving Label Request messages from its upstream LSR.
 | Downstream on demand (DoD) | No | An LSR assigns and distributes labels to a FEC only after receiving Label Request messages from its upstream LSR.
Label distribution control mode | Independent | No | A local LSR assigns and binds a label to a FEC and then advertises the binding to the upstream LSR, without waiting for the label distributed by the downstream LSR.
 | Ordered | Yes | An LSR sends the label mapping of a FEC to its upstream device only if the LSR has received Label Mapping messages from the next hop of the FEC or if the LSR is the egress of the FEC.
Label retention mode | Liberal | Yes | An LSR retains all label mappings received from a peer, regardless of whether the peer is its next hop.
 | Conservative | No | An LSR retains the label mappings received from a peer only if the peer is its next hop.

## Slide 20: Upstream and Downstream
MPLS Domain
MPLS determines the upstream and downstream relationships based on the data forwarding direction. Labeled packets are sent from an upstream LSR, and received and processed by a downstream LSR.
As shown in the figure, for the LSP to 192.168.3.0/24, R3 is the downstream LSR of R2, and R1 is the upstream LSR of R2.
R1
R2
R3
192.168.3.0/24
Data transmission direction

## Slide 21: Label Advertisement Mode — DU
DU mode
  An LSR assigns and distributes labels to a FEC without having to receive Label Request messages from its upstream LSR.
  An LSR actively advertises the labels of a FEC to its upstream peer without having to receive Label Request messages from the peer.
R1
R2
R3
Advertises label mappings to the upstream node.
192.168.3.0/24
Advertises label mappings to the upstream node.
Notes: Label assignment: An LSR assigns a label from the local label space and binds it with a FEC.
Label distribution: An LSR notifies the upstream LSR of the binding between labels and FECs.
When the DU label advertisement mode is used, an LSR can assign labels to all its peers by default. Specifically, each LSR can distribute label mappings to all its peers, regardless of whether the LSR is an upstream or a downstream one. If an LSR distributes labels only to upstream peers, it must identify its upstream and downstream nodes based on routing information before sending Label Mapping messages. An upstream node cannot send Label Mapping messages to its downstream node.

## Slide 22: Label Advertisement Mode — DoD
DoD mode
  An LSR assigns and distributes labels to a FEC only after receiving Label Request messages from its upstream LSR.
  Generally, a Label Request message is triggered when an access request to a particular FEC arises.
R1
R2
R3
Advertises label mappings to the upstream node.
Advertises label mappings to the upstream node.
Requests labels.
Requests labels.
R1 requires to access the 192.168.3.0/24 network segment.
192.168.3.0/24
Notes: An LSR advertises label mappings to an upstream peer only after receiving Label Request messages from the upstream peer.

## Slide 23: Label Distribution Control Mode — Independent
Independent mode
  A local LSR assigns and binds a label to a FEC and then advertises the binding to the upstream LSR, without waiting for the label distributed by the downstream LSR.
Advertises label mappings to the upstream node.
Advertises label mappings to the upstream node.
R1
R2
R3
R4
192.168.4.0/24
DU
+
Independent
Advertises label mappings to the upstream node.
Advertises label mappings to the upstream node.
R1
R2
R3
R4
DoD
+
Independent
Requests labels.
Requests labels.
Unordered
Unordered
192.168.4.0/24
Notes: The label distribution control mode works with the label advertisement mode:
  If the network shown in the figure uses the DU label advertisement mode, R2 and R3 can actively notify the upstream LSR of the label binding for the FEC 192.168.4.0/24 even if the upstream LSR does not send Label Request messages and R2 and R3 do not receive label binding information from the downstream LSR.
  If the network uses the DoD label advertisement mode, R2 and R3 can notify the upstream LSR of the label binding for the FEC 192.168.4.0/24 given that R2 and R3 have received Label Request messages from the upstream LSR, regardless of whether R2 and R3 have received label binding information from the downstream LSR.

## Slide 24: Label Distribution Control Mode — Ordered
Ordered mode
  An LSR sends the label mapping of a FEC to its upstream device only if the LSR has received Label Mapping messages from the downstream of the FEC or if the LSR is the egress of the FEC.
Advertises label mappings to the upstream node.
Advertises label mappings to the upstream node.
R1
R2
R3
R4
DU
+
Ordered
Advertises label mappings to the upstream node.
Advertises label mappings to the upstream node.
Advertises label mappings to the upstream node.
R1
R2
R3
R4
DoD
+
Ordered
Advertises label mappings to the upstream node.
Requests labels.
Requests labels.
Requests labels.
1
2
3
6
5
4
1
2
3
Egress LSR
Egress LSR
192.168.4.0/24
192.168.4.0/24
Notes: In ordered label distribution control mode, an LSR can send a Label Mapping message to its upstream node only when the LSR receives Label Mapping messages of a FEC from the downstream of the FEC or when the LSR is the egress of an LSP.
  If the network shown in the figure uses the DU label advertisement mode, an LSR sends the label binding information of the FEC 192.168.4.0/24 to its upstream node only after the LSR receives the label binding information of the FEC from its downstream node, even if the upstream node has sent Label Request messages. Therefore, the initiator for LSP establishment must be an egress LSR (R4 in this example).
  If the network uses the DoD label advertisement mode, an LSR advertises the label binding information of the FEC 192.168.4.0/24 to the upstream node only after the LSR receives Label Request messages from the upstream node as well as the label binding information of the FEC from the downstream node. Therefore, a Label Request message can be initiated by the ingress LSR (R1) only. After a Label Request is sent hop by hop to the egress LSR (R4), R4 advertises a Label Mapping message to the upstream LSR to establish an LSP.

## Slide 25: Label Retention Mode — Liberal
Liberal mode
  An LSR can receive label mappings from its next hop or non-next hop nodes.
  An LSR retains all label mappings received from a peer, regardless of whether the peer is its next hop.
R1
R2
R3
R4
192.168.1.0/24
R5
Advertises label mappings to the upstream node.
Advertises label mappings to the upstream node.
Next hop
Not next hop
Notes: If MPLS is deployed on an IP network, an LSR uses the IP routing table to determine whether a label mapping is received from the next hop.
In liberal mode, a new LSP can be quickly established when routes change, because all received labels are retained, which is the biggest advantage of this mode. The disadvantage is that unnecessary label mappings are distributed and maintained.
  In DU label advertisement mode, if the liberal label retention mode is used, R3 retains the labels of the FEC 192.168.1.0/24 sent by all LDP peers (R2 and R5 in this example), regardless of whether R2 and R5 are the next hops of the routes to 192.168.1.0/24 in the IP routing table.
  In DoD label advertisement mode, if the liberal label retention mode is used, an LSR requests labels from all LDP peers. However, the DoD label advertisement mode is generally used together with the conservative label retention mode.

## Slide 26: Label Retention Mode — Conservative
Conservative
  An LSR retains the label mappings received from a peer only if the peer is its next hop.
R1
R2
R3
R4
R5
Advertises label mappings to the upstream node.
Advertises label mappings to the upstream node.
Not retained
Assume that the next hop of the IP route from R3 to 192.168.1.0/24 is R2.
192.168.1.0/24
Notes: The advantage of the conservative mode is that only the labels that will be used to forward data are retained and maintained, thereby saving the label space.
  In DU label advertisement mode, an LSR may receive Label Mapping messages for the same network segment (FEC) from multiple LDP peers. As shown in the figure, R3 receives Label Mapping messages for the network segment 192.168.1.0/24 from both R2 and R5. If the conservative label retention mode is used, R3 retains only the label sent by the next hop R2 and discards the label sent by the non-next hop R5.
  In DoD label advertisement mode, an LSR uses routing information to determine its next hop and requests labels only from the next hop.
If the next hop of a FEC changes, either of the following situations occurs:
  In liberal label retention mode, the LSR can use an existing label advertised by a non-next hop LSR to quickly establish an LSP. The liberal mode requires more memory and label space.
  In conservative label retention mode, the LSR retains the labels advertised by the next hop only. This mode saves memory and label space but consumes more time to reestablish the LSP.
  An LSR that has a limited label space usually uses the conservative mode and DoD mode.

## Slide 27: PHP
Penultimate hop popping (PHP): If PHP is enabled, an egress assigns a special label (3), to a local route. This label is called an implicit null label. When an LSR forwards a labeled packet and finds that the outgoing label value is 3, the LSR removes the top label from the packet and forwards the inner data to the downstream LSR.
192.168.3.0/24
R1
R2
R3
1033
To 192.168.3.3
MPLS Domain
To 192.168.3.3
To 192.168.3.3
To 192.168.3.3
IP Packet
Label
192.168.3.0/24 Label=3
192.168.3.0/24 Label=1033
Notes: During label advertisement, R3 is the egress of the FEC 192.168.3.0/24. During label distribution, R3 assigns label 3 to the FEC and advertises the label binding information to R2.
During data forwarding, R2, as the penultimate hop to 192.168.3.0, finds that the outgoing label value is 3. Then, R2 removes the label header and forwards the IP packet to R3. R3 only needs to query the FIB once to obtain the corresponding forwarding information, improving the forwarding efficiency.

## Slide 28: Implicit Null Label and Explicit Null Label (1)
By default, an egress assigns implicit null labels, that is, label 3, to the penultimate hop.
However, if QoS is deployed, after the label is popped out, the priority in the label is lost.
R1
R2
R3
R4
192.168.4.0/24
192.168.1.0/24
10.0.12.1/24
200
EXP
To 192.168.4.4
300
EXP
The label is popped out on the penultimate hop.
QoS information is lost.
10.0.12.2/24
10.0.23.2/24
10.0.23.3/24
10.0.34.3/24
10.0.34.4/24
To 192.168.4.4
To 192.168.4.4

## Slide 29: Implicit Null Label and Explicit Null Label (2)
In the explicit null label mechanism, an egress assigns label 0 to the penultimate hop.
When R3 forwards a labeled packet of which the outgoing label is 0, R3 does not pop out the label header, and therefore QoS information is retained. When R4 receives a packet with label 0, it directly pops out the label without searching for an ILM entry.
By default, an egress assigns implicit null labels. You can run the label advertise explicit-null command to enable the egress to assign explicit null labels to the penultimate hop.
QoS information is retained.
R1
R2
R3
R4
192.168.4.0/24
192.168.1.0/24
10.0.12.1/24
200
EXP
To 192.168.4.4
300
EXP
10.0.12.2/24
10.0.23.2/24
10.0.23.3/24
10.0.34.3/24
10.0.34.4/24
To 192.168.4.4
To 192.168.4.4
Notes: Run the label advertise { explicit-null | implicit-null | non-null } command in the MPLS view to configure the label to be assigned to the penultimate hop.
You can specify one of the following parameters:
  implicit-null: is the default value. If this parameter is set, an egress assigns an implicit null label with the value of 3 to the penultimate hop.
  explicit-null: If this parameter is set, an egress assigns an explicit null label with the value of 0 to the penultimate hop. The explicit-null parameter can be set if MPLS QoS attributes need to be used.
  non-null: If this parameter is set, an egress assigns a common label with a value greater than or equal to 16 to the penultimate hop.

## Slide 30
Basic LDP Concepts
LDP Principles
  LDP Session Establishment
  LDP-based Label Distribution
  LDP Working Process
Basic LDP Configurations

## Slide 31: Networking Overview
OSPF has been deployed on the network, and devices can learn routes from each other.
MPLS and LDP have been enabled on devices and interfaces, and local LDP sessions have been established between neighboring devices.
All LSRs use the DU + Independent + Liberal modes.
R1
R2
R4
192.168.4.0/24
OSPF
LDP
R3
Destination/Mask | Proto | Cost | NH
192.168.4.0/24 | Direct | 0 | -
LDP Session
LDP Session
LDP Session
LDP Session
Destination/Mask | Proto | Cost | NH
192.168.4.0/24 | OSPF | 1 | R4
Destination/Mask | Proto | Cost | NH
192.168.4.0/24 | OSPF | 10 | R4
Destination/Mask | Proto | Cost | NH
192.168.4.0/24 | OSPF | 2 | R2
Notes: Currently, Huawei devices use the DU + Ordered + Liberal modes by default.
For a packet that enters the MPLS domain from R1 and is destined for 192.168.4.0/24, R1 is the ingress LSR, and R4 is the egress LSR.

## Slide 32: Label Distribution — Egress LSR
R4 is directly connected to the network segment 192.168.4.0/24. R4 actively assigns labels, such as 1041, to routes destined for this network segment and advertises label mapping information to its LDP peers (R2 and R3) through LDP packets.
R1
R2
R4
192.168.4.0/24/24
OSPF
LDP
R3
LDP Session
LDP Session
LDP Session
LDP Session
192.168.4.0/24
Label=1041
192.168.4.0/24
Label=1041
LDP label mapping advertisement
Destination/Mask | Proto | Cost | NH
192.168.4.0/24 | OSPF | 1 | R4
Destination/Mask | Proto | Cost | NH
192.168.4.0/24 | OSPF | 10 | R4
Notes: Note: By default, 32-bit host IP routes are used to trigger LSP establishment. You can manually trigger the establishment of an LSP with non-32-bit host IP routes.

## Slide 33: Label Distribution — Transit LSR
Take R2 as an example. In its routing table, the next hop of the route 192.168.4.0/24 is R4. When R2 receives a Label Mapping message for the route 192.168.4.0/24 from R4, R2 assigns label 1021 to the route because the message is sent by a downstream LDP peer, and advertises the label mapping to the LDP peer, for example, R1. This process also applies to R3.
R1
R2
R4
192.168.4.0/24
OSPF
LDP
R3
LDP Session
LDP Session
LDP Session
LDP Session
192.168.4.0/24
Label=1041
192.168.4.0/24
Label=1041
192.168.4.0/24
Label=1021
192.168.4.0/24
Label=1031
Destination/Mask | Proto | Cost | NH
192.168.4.0/24 | OSPF | 1 | R4
Destination/Mask | Proto | Cost | NH
192.168.4.0/24 | OSPF | 10 | R4
LDP label mapping advertisement

## Slide 34: Label Distribution — Ingress LSR
After R1 receives the label mappings for the route 192.168.4.0/24 advertised by R2 and R3, R1 stores both of the label mappings. However, R1 only uses label 1021 advertised by R2, because the next hop of the route to 192.168.4.0/24 is R2, as shown in R1's routing table.
R1
R2
R4
192.168.4.0/24
OSPF
LDP
R3
LDP Session
LDP Session
LDP Session
LDP Session
192.168.4.0/24
Label=1041
192.168.4.0/24
Label=1041
192.168.4.0/24
Label=1021
192.168.4.0/24
Label=1031
LDP label mapping advertisement
Destination/Mask | Proto | Cost | NH
192.168.4.0/24 | OSPF | 2 | R2
Notes: Note: If R2 fails, OSPF routes re-converge. The next hop of the route 192.168.4.0/24 in the routing table of R1 is switched to R3. In this case, R1 uses the label advertised by R3 for 192.168.4.0/24.

## Slide 35: Label-based Forwarding — Ingress LSR
As an ingress LSR, R1 pushes a label into each received IP packet, and forwards packets based on labels.
R1
R2
R4
192.168.4.0/24
OSPF
LDP
R3
Tunnel ID | Out intf | OPER | NH | Out Label
0x12 | GE0/0/0 | push | R2 | 1021
Destination/Mask | Proto | Cost | NH
192.168.4.0/24 | OSPF | 2 | R2
Routing table of R1
FIB of R1
NHLFE table of R1
Destination/Mask | Proto | Cost | NH | Tunnel ID
192.168.4.0/24 | OSPF | 2 | R2 | 0x12
GE0/0/0
LSP
LSP
To 192.168.4.1
To 192.168.4.1
1021
1
2
3
4
Notes: When R1 receives an IP packet destined for 192.168.4.1, it searches the FIB for a forwarding entry matching the destination IP address of the packet, and finds that the tunnel ID in the matching entry is not 0. As such, R1 continues to search for an NHLFE matching the tunnel ID, pushes a label to the IP packet, and forwards the packet. The outbound interface is GE 0/0/0, the next hop is R2, and the outgoing label is 1021. Therefore, R1 adds a label header to the packet and forwards the packet.

## Slide 36: Label-based Forwarding — Transit LSR
As a transit LSR, R2 needs to swap labels in received IP packets and forward the packets.
R1
R2
R4
OSPF
LDP
R3
Tunnel ID | Out intf | OPER | NH | Out Label
0x12 | GE0/0/1 | Swap | R4 | 1041
ILM table of R2
NHLFE table of R2
In Label | Tunnel ID
1021 | 0x12
GE0/0/0
LSP
To 192.168.4.1
1021
To 192.168.4.1
1041
1
2
3
4
GE0/0/1
192.168.4.0/24
Notes: When R2 receives a packet with label 1021, it searches for a matching ILM entry and an NHLFE matching the ILM entry. Then, R2 changes the label of the packet to 1041 and forwards the packet through the matching outbound interface.

## Slide 37: Label-based Forwarding — Egress LSR
As an egress LSR, R4 needs to perform the pop operation on received IP packets to remove labels and forward the packets through IP.
ILM table of R4
2
R1
R2
R4
OSPF
LDP
R3
In Label | Tunnel ID | Out intf | OPER | NH | Out Label
1041 | 0x12 | GE0/0/0 | Pop | - | Null
GE0/0/0
LSP
To 192.168.4.1
1041
3
1
GE0/0/1
To 192.168.4.1
192.168.4.0/24
Notes: When R4 receives a packet with label 1041, it searches for a matching ILM entry and finds that the operation type is pop. R4 then performs a pop operation to remove the outer label from the packet. The packet then becomes a standard IP packet, and therefore R4 performs the standard IP forwarding on the packet.
When R4 forwards the packet, it searches the LFIB and FIB. How can the forwarding efficiency be improved on the egress LSR (R4)?

## Slide 38: Summary of an LDP-Capable LSR's Operations on an MPLS Network
An LSR runs an IGP (such as OSPF or IS-IS) to construct a routing table and FIB.
LDP assigns labels to route prefixes (FECs) in the routing table based on the label assignment mode it uses.
LDP advertises the labels assigned to the route prefixes to LDP peers through LDP Label Mapping messages based on the label advertisement mode it uses.
An LSR stores the labels that it assigns to route prefixes and the labels that LDP peers advertise to the route prefixes, and associates the labels with information such as outbound interfaces and next-hop addresses (label forwarding entries).
When an LSR forwards a labeled packet destined, the LSR always uses the outgoing label advertised by the downstream LDP peer. The downstream peer is the next-hop device to the destination network in the routing table.

## Slide 39
Basic LDP Concepts
LDP Principles
Basic LDP Configurations

## Slide 40: Basic LDP Configuration Commands (1)
[Huawei] mpls ldp
Enable LDP.
The mpls ldp command enables LDP and displays the LDP view.
[Huawei-GigabitEthernet0/0/0] mpls ldp
Enable LDP on an interface. Before running this command, enable LDP globally.
[Huawei] mpls ldp remote-peer remote-peer-name
Configure a remote LDP peer.
The mpls ldp remote-peer command creates a remote peer and displays the remote peer view.
[Huawei-mpls-ldp-remote-PeerName] remote-ip ip-address
Set the remote-ip ip-address parameter to the IP address of a remote LDP peer.

## Slide 41: Basic LDP Configuration Commands (2)
[Huawei-mpls] lsp-trigger { all | host | ip-prefix ip-prefix-name | none }
Configure a policy for triggering LSP establishment.
The lsp-trigger command configures the routes (static and IGP routes) that are used to trigger LSP establishment, which are IP routes with a 32-bit mask by default.
all: All static and IGP routes are used to trigger LSP establishment. If this parameter is set, a significant of LSPs will be established, consuming label resources excessively and slowing down network-wide LSP convergence. Therefore, setting this parameter is not recommended.
host: IP routes with a 32-bit mask are used to trigger LSP establishment.
ip-prefix ip-prefix-name: Routes matching a specified IP prefix list are used to trigger LSP establishment.
none: LSP establishment cannot be triggered.
Configure a label advertisement mode.
The default label advertisement mode is downstream unsolicited (DU).
If the label advertisement mode is DU, the label retention mode is liberal.
If the label advertisement mode is DoD, the label retention mode is conservative.
[Huawei-GigabitEthernet0/0/0] mpls ldp advertisement { dod | du }
Notes: BGP routes can also be used to trigger LDP LSP establishment. This trigger policy is not covered in this course.

## Slide 42: Basic LDP Configuration Commands (3)
Configure PHP.
By default, an egress distributes implicit null labels to a penultimate hop.
explicit-null: An egress assigns explicit null label to the penultimate hop.
implicit-null: An egress assigns implicit null labels to the penultimate hop.
non-null: An egress assigns common labels to the penultimate hop.
[Huawei-mpls] label advertise { explicit-null | implicit-null | non-null }
[Huawei-mpls-ldp] label distribution control-mode { independent | ordered }
The default LDP label distribution control mode is ordered.
Configure an LDP label distribution control mode.

## Slide 43: Configuration Examples
R1
R2
R3
R4
GE0/0/0
10.0.12.1/24
GE0/0/1
10.0.23.2/24
GE0/0/1
192.168.1.254/24
GE0/0/0
10.0.23.3/24
GE0/0/1
10.0.34.3/24
GE0/0/0
10.0.34.4/24
Loopback0
10.0.1.1/32
Loopback0
10.0.2.2/32
Loopback0
10.0.3.3/32
Loopback0
10.4.4.4/32
Scenario: R1, R2, R3, and R4 run an IGP to implement IP interworking.
Requirement: Configure MPLS and LDP to implement mutual access between the network segments 192.168.1.0/24 and 192.168.4.0/24 through MPLS forwarding.
PC1
IP:192.168.1.1/24
GW:192.168.1.254
PC2
IP:192.168.4.1/24
GW:192.168.4.254
GE0/0/1
192.168.4.254/24
GE0/0/0
10.0.12.2/24

## Slide 44: Configuration Procedure (1)
R1
R2
R3
R4
GE0/0/0
10.0.12.1/24
GE0/0/0
10.0.12.2/24
GE0/0/0
10.0.23.3/24
GE0/0/1
10.0.34.3/24
GE0/0/0
10.0.34.4/24
Loopback0
10.0.1.1/32
Loopback0
10.0.2.2/32
Loopback0
10.0.3.3/32
Loopback0
10.4.4.4/32
PC1
IP:192.168.1.1/24
GW:192.168.1.254
PC2
IP:192.168.4.1/24
GW:192.168.4.254
Enable basic MPLS and LDP functions on the devices. The following example uses R1.
[R1]mpls
[R1-mpls]quit
[R1]mpls ldp
[R1-mpls-ldp]quit
[R1]interface GigabitEthernet 0/0/0
[R1-GigabitEthernet0/0/0]mpls
[R1-GigabitEthernet0/0/0]mpls ldp
[R1-GigabitEthernet0/0/0]quit
GE0/0/1
10.0.23.2/24
GE0/0/1
192.168.1.254/24
GE0/0/1
192.168.4.254/24

## Slide 45: Configuration Procedure (2)
R1
R2
R3
R4
GE0/0/0
10.0.12.1/24
GE0/0/0
10.0.12.2/24
GE0/0/0
10.0.23.3/24
GE0/0/1
10.0.34.3/24
GE0/0/0
10.0.34.4/24
Loopback0
10.0.1.1/32
Loopback0
10.0.2.2/32
Loopback0
10.0.3.3/32
Loopback0
10.4.4.4/32
PC1
IP:192.168.1.1/24
GW:192.168.1.254
PC2
IP:192.168.4.1/24
GW:192.168.4.254
Because 192.168.1.0/24 is not a route with a 32-bit mask, you need to configure a policy for trigging LSP establishment.
[R1]ip ip-prefix ldp permit 192.168.1.0 24
[R1-mpls]lsp-trigger ip-prefix ldp
GE0/0/1
10.0.23.2/24
Perform similar configuration on R4.
[R4]ip ip-prefix ldp permit 192.168.4.0 24
[R4-mpls]lsp-trigger ip-prefix ldp
GE0/0/1
192.168.4.254/24
GE0/0/1
192.168.1.254/24

## Slide 46: Checking the Configuration - Checking LSP Information
# Check information about the LDP LSPs created on R1.
[R1]display mpls ldp lsp
LDP LSP Information
-------------------------------------------------------------------------------------------------------------------
DestAddress/Mask In/OutLabel UpstreamPeer NextHop OutInterface
-------------------------------------------------------------------------------------------------------------------
10.0.2.2/32 1024/3 10.0.2.2 10.0.12.2 GE0/0/0
10.0.3.3/32 1025/1025 10.0.2.2 10.0.12.2 GE0/0/0
192.168.1.0/24 3/NULL 10.0.2.2 192.168.1.254 GE0/0/1
*192.168.1.0/24 Liberal/1027 DS/10.0.2.2
192.168.4.0/24 1027/1028 10.0.2.2 10.0.12.2 GE0/0/0

## Slide 47
(Single) Which of the following commands can be used to display a label distributed for a specific FEC? ( )
  display mpls ldp
  display mpls ldp interface
  display mpls lsp
  display mpls ldp session
(Single) What is the default combination of label advertisement mode, label distribution control mode, and label retention mode on Huawei devices?
  DU + Independent + Conservative
  DU + Ordered+ Liberal
  DoD + Independent+ Liberal
  DoD + Ordered + Conservative
Notes: C
B

## Slide 48
MPLS supports multiple label distribution protocols, among which LDP is widely used.
LDP is a process in which LSRs negotiate the meaning of labels. LDP uses discovery, session, advertisement, and notification packets to establish sessions and distribute labels.
LDP determines label advertisement and management based on the label advertisement mode, label distribution control mode, and label retention mode. By default, Huawei datacom devices use the DU label advertisement mode + ordered label distribution control mode + liberal label retention mode.
LDP can directly map network-layer routing information to label information in order to establish LSPs. LSRs are connected according to the incoming label, next hop, and outgoing label corresponding to a specified FEC in the local forwarding table. In this manner, the LSP crossing the entire MPLS domain can be formed.