## Slide 1
Zhang Linrui/ZWX570554
2020.11
New

## Slide 2: Campus Network and Solution Overview

## Slide 3
Campuses are everywhere in our cities. Some examples of campuses include factories, government buildings and facilities, shopping malls, office buildings, school campuses, and parks. According to statistics, 90% of urban residents work and live in campuses, 80% of gross domestic product (GDP) is created in campuses, and each person stays in campuses for 18 hours every day.
Campus networks, as the infrastructure for campuses to connect to the digital world, are an indispensable part of campus construction and play an increasingly important role in daily working, R&D, production, and operation management.
Campus networks vary in sizes and differ with industry attributes. From the perspective of industries that campus networks serve, there are different campus networks. Typical industry campus networks include school, government, commercial, office, and manufacturing campus networks.
This course introduces the concepts, typical networking scenarios, and typical architectures of enterprise campus networks, as well as the requirements, trends, and challenges of campus networks. It also briefly introduces Huawei CloudCampus Solution.

## Slide 4
Upon completion of this course, you will be able to:
  Describe concepts of campus networks.
  Distinguish different types of campus networks and describe their main characteristics.
  Describe typical campus networks in industries and their characteristics.
  Describe the logical and physical architectures of a typical campus network.
  Describe the trends and challenges of campus networks.
  Describe Huawei CloudCampus Solution.

## Slide 5
Introduction to Campus Networks
Typical Campus Network Scenarios
Campus Network Trends and Challenges
Huawei CloudCampus Solution

## Slide 6: Campuses Are Everywhere
5 h & 22 h
90%+
80%+
90%+
of city residents work and live in campuses.
spent in using smart terminals & staying in the campus every day
of GDP is created in campuses.
of innovations are made in campuses.

## Slide 7: Overview of a Campus Network
A campus network generally refers to the internal network of an enterprise or organization, which is connected to the wide area network (WAN) and data center network.
A campus network is built to ensure that key enterprise services are running more efficiently.
Campus networks can be classified into large- and medium-sized campus networks and small- and medium-sized campus networks by scale.
Some enterprises have branches dispersed in different geographical locations. Each branch network can be considered as a single campus network.

## Slide 8: Smart City Communication Network: Panorama
The smart city communication network is a pipe for information transmission and exchange in smart cities.
It is a metro network that connects various industries and covers diversified services from the urban area to the rural area.
Smart city communication network backbone
Smart city
application platform
Wired
Wireless
Village
committee
County- or district-
level government
Municipal
government
School
School
School
Community
Community
Community
Village healthcare
center
Enterprise
Enterprise
Safe city
Smart street lamp
Commercial
center
Hospital
Backbone transmission ring
Access and aggregation ring
Municipal core
District/County aggregation
Village/Town aggregation

## Slide 9: Smart City Communication Network: Campus
District/County core
District/County core
Government building
Smart street lamp
School
Hospital
Community
Industrial park
Safe city
Operations center
Municipal
core
Primary data center
Backup data center
Enterprise
Shopping
mall/Supermarket
Government building
Campus networks from diverse industries are interconnected via the smart city communication backbone network.

## Slide 10: Campus Network Classification (1)
Large campus network
Classification by the number of terminal users or NEs
Midsize campus network
Small campus network
Number of terminal users > 2000
Number of NEs > 100
Number of terminal users: 200–2000
Number of NEs: 25–100
Number of terminal users < 200
Number of NEs < 25
Classification based on service objects of campus networks
Users: internal personnel only
Security requirements: network access control and external threat defense
Users: including external personnel, such as the public
Security requirements: access control, identity identification, behavior control, security defense, etc.
Closed campus network
Open campus network
Scale
Served
objects
Networks of different scales have different requirements and pain points.
A running campus network usually has both closed and open subnets.

## Slide 11: Campus Network Classification (2)
Single-service campus network
Classification by services carried on campus networks
Multi-service campus network
Single services
Simple network architecture
The network needs to carry a large number of services, and the
network scale is large. Different services need to be isolated
and guaranteed.
Campus network architecture begins to become complex and virtualized.
Wired campus network
Classification by access modes of campus networks
Wireless
campus network
Each device accessing a network must be connected to the preset network port through a network cable.
The architecture is structured and hierarchical, and the logic is clear, so faults are easy to locate.
The network is based on the 802.11 protocol (Wi-Fi) and is also called WLAN.
AP deployment and installation affect the coverage effect. Interference and conflicts exist, so the network need to be optimized periodically.
Faults are difficult to locate.
Service
Access
mode
Currently, most campus networks are a mix of wired and wireless networks.
The complexity of the campus network architecture depends on the complexity of services carried on the campus network.

## Slide 12: Campus Network Classification (3)
To meet requirements of different industry campuses, the campus network architecture is designed based on the characteristics of industries that campus networks serve. Ultimately, campus network solutions with industry attributes are developed.
Enterprise campus network
It refers to the Ethernet-based enterprise office network.
The enterprise campus network focuses on network reliability and advancement, continuously improves employees' office experience, and ensures the efficiency and quality of operation and production.
School campus network
School campus networks are classified into primary/secondary education and higher education campus networks.
Higher education campus networks are complex and usually have teaching and research networks, student networks, and operational dormitory networks.
There are high requirements on network manageability and security, and specific requirements on network advancement.
Government campus network
It usually refers to the internal network of a government agency.
High security is required. Generally, the internal network and external network are isolated to ensure high security of confidential information.
Business campus network
Campus networks of this type involve shopping malls, supermarkets, hotels, and parks.
Such networks are mainly used to serve consumers. In addition, they include subnets for internal office work.
Such networks provide Internet access services and help build business intelligence (BI) systems for better user experience, lower O&M costs, higher efficiency, and value transfer.

## Slide 13: Typical Logical Architecture of a Campus Network
Service application
platform
LBS
applications
IoT
applications
Big data
applications
Security
applications
Network management platform
Security platform
Device monitoring, configuration
management, fault management...
Security monitoring, policy control,
and threat detection
Campus data network
Access
terminal
The campus data network is built based on the Ethernet or WLAN technology, including various network devices.
It is used to carry different services, such as office, IoT, and video conferencing.
Access terminals include wired and wireless terminals from internal or external users of a campus network.
Device access and security management must be considered.
The next-generation NMS needs to implement automation, intelligence, and capability openness based on the traditional NMS, and meanwhile interact with the security platform.
The advanced security platform can identify and defend against advanced persistent threats (APTs), display the security situation of the entire network, and interwork with the network to isolate and block threat flows after detecting threats.
The network management platform can be used to develop many service applications, creating a service application platform based on the campus network.
Notes: Location Based Service (LBS) uses various types of location technologies to obtain the current location of a device and provides information resources and basic services for the device through the mobile Internet.

## Slide 14: Typical Physical Architecture of a Campus Network
Egress area: serves as the border between the campus internal network and the external network. Through this egress area, internal users can access the public network and external users (including customers, partners, branch users, and remote users) can access the internal network. Firewalls can be deployed at the egress area to ensure the security of the internal network.
Core layer: serves as the core of data switching on the campus network. It connects various parts of the campus network, such as the data center, O&M area, and egress area.
Aggregation layer: forwards not only horizontal traffic between users, but also vertical traffic to the core layer. It can also function as the switching core for a department or zone and further extend the quantity of access terminals.
Access layer: provides various access modes for users and is the first layer for terminals to access the network.
Terminal layer: has terminals deployed to connect to the campus network. Terminals include computers, printers, IP phones, mobile phones, and cameras.
Data center: has servers and application systems deployed to provide data and application services for internal and external users of the enterprise.
O&M area: manages network servers such as the NMS and authentication server.
iStack/CSS link
Egress area
Core layer
Aggregation layer
Access layer
Terminal layer
Internet
WAN
O&M area
Data center

## Slide 15
Introduction to Campus Networks
Typical Campus Network Scenarios
Campus Network Trends and Challenges
Huawei CloudCampus Solution

## Slide 16: Higher Education Campus Network
NMS center
Data center
Internet
CERNET
Private line or VPN link
Main campus
Branch campus
Dormitory
Lecture hall
Library
Multimedia classroom
Teaching building
Digital
library
Remote
education
Virtual
experiment
Mobile
learning
A higher education campus network is a computer network that provides teaching, research, and comprehensive information services for teachers and students (as well as family members and visitors).
A higher education campus network is generally divided into the dormitory area, living area, teaching area, and public area. It provides wired and wireless network access services to help the campus enter the digital era and improve talent cultivation and innovation capabilities.
Internet
Notes: China Education and Research Network (CERNET) is a nationwide education and research computer network in China. The CERNET project is funded by the Chinese government and directly managed by the Chinese Ministry of Education. It is constructed and operated by Tsinghua University and the other leading Chinese universities.

## Slide 17: Primary/Secondary Education Campus Network (Education MAN)
Internet
CERNET
e-
Schoolbag
Health
monitoring
Personnel
locating
AR/VR
Primary/Secondary education campus networks refer to campus networks of general education institutions, for example, campus networks of primary and secondary schools. They provide basic network platforms for primary and secondary schools to support teaching, research, teaching affairs, and services.
Compared with higher education campus networks, primary/secondary education campus networks have small scales.
Typical primary/secondary education campus networks are uniformly planned and constructed by an upper-level network management department and connected to the education MAN to implement full data convergence for teaching, learning, management, testing, evaluation, service, etc.
Education MAN
Center of district X
Center of district Y
Center of district Z
Education committee
Education committee
Education committee
School
School
School
School
School
School
Remote
education
AR
VR
Municipal education committee's NMS center
Smart education
data center

## Slide 18: Shopping Mall/Supermarket Campus Network
or
Internet
AP
AR
Firewall
AR
Firewall
AP
AP
Switch
or
AP
Switch
Micro store
Small/Midsize store
Large supermarket or flagship store
AC
Cloud management platform
Device management, network management, user management, Portal page/advertisement customization, network quality visualization...
Cloud service
LBS, big data analytics, logistics, AI-based identification...
The shopping mall or supermarket campus network is used to implement digital offices and more importantly, realize digital consumption experience spaces. Example use cases include:
  Guest Wi-Fi access
  Digital advertising signage
  Smart guided shopping
  Electronic shelf label (ESL), etc.
Market competition and consumer demand evolution drive digital transformation of brick-and-mortar retail stores. With the rise of new retail, shopping malls and supermarkets must focus more on:
  Shopping experience
  Operational efficiency
LTE
Carrier's LTE base station

## Slide 19
Introduction to Campus Networks
Typical Campus Network Scenarios
Campus Network Trends and Challenges
Huawei CloudCampus Solution

## Slide 20: Driven by Business and Technology, Digital Is Changing the Way We Work and Live
Two drivers: Business needs and technology advances
Digital consumption experience spaces
Cloud computing
Big data analytics
AI
Automation
IoT
Advertisement pushing
Digital signage
Smart shelf
Smart help-seeking
Electronic Shelf Label (ESL)
Smart shopping cart
Robot-assisted goods replenishment
Smart lighting and temperature control
Asset positioning
Smart fitting room
Smart shopping guide
Self-service checkout
Shopping experience
Efficiency improvement
Business needs
Technology advances
Externally: Better customer satisfaction
Internally: Higher work efficiency
Source: Accenture's editorial article ─ The Internet of Things: Revolutionizing the Retail Industry

## Slide 21: Industry Digital Transformation Improves Efficiency and Customer Satisfaction
Digital workspace
Digital manufacturing
"At least 55% of the organizations will be firm advocates of digitalization by 2020.“
Source: IDC FutureScape: Worldwide Digital Transformation 2019 Predictions
"84.9% of manufacturing enterprises are going digital, driving business model innovations and reshaping the business ecosystem.“
Source: IDC's 2018 manufacturing industry survey
Digital education
"86% of higher education CIOs will regard IT as a key factor in enabling education business transformation.“
Source: 2019 Higher Education Industry Insights, Gartner
Always-on mass terminals/sensors
Real-time collection of production data
Automated and precise control
All-wireless access
Anytime, anywhere workstyles
One-click conference reservation via an app
Auto-adjustable lighting and temperature
Shift from spoon-feeding education to immersive education
On-demand access to high-quality teaching
Practical-scene teaching
Notes: CIO: Chief Information Officer

## Slide 22: In the Digital Era, How Should Campus Networks Support Digital Transformation Across Industries?
On-demand services
Quick service deployment and adjustment
Rapid rollout of value-added applications
Access anytime, anywhere
High-quality service support
Ubiquitous connectivity
Precise measurement and evaluation of user experience
AI-powered automatic adjustment of resource allocation
Perceptible and visible experience
Configuration delivery based on services
Fast and accurate fault locating
Efficient and intelligent O&M

## Slide 23: Constantly Evolving Campus Network
Today, we stand on the cusp of the fourth industrial revolution, as represented by AI. It is foreseeable that new ICT will lead us from the information era to the intelligence era. As a key engine of the fourth industrial revolution, AI will drive the progress and development of all industries around the world. Data networks, which are a key driving force in the IT era, will be developed and optimized first with AI.
Campus networks gradually become intelligent and provide simplified service deployment and network O&M capabilities for customers.
1st generation
From "sharing" to "switching"
Late 1980s
2nd generation
Layer 3 routed switching
Early 1990s
3rd generation
Multi-service converged support
Mid 2000s
Today and Future
Autonomous driving
Intelligent O&M
Intelligent connectivity
Intelligent ultra-broadband
…
Notes: 1st-generation campus network:
  In 1980, IEEE released the IEEE 802.3 standard, signaling the birth of Ethernet technology. By using twisted pair connections, Ethernet was more cost-effective and easier to implement than previous networking technologies. Consequently, Ethernet quickly became the mainstream technology for campus networks. During the early days, campus networks used hubs as access devices. A hub was a shared-medium device that worked at the physical layer. It was limited in the number of users it could support for concurrent access. If many users connected to a hub simultaneously, network performance degraded severely due to the expanded collision domain. In the late 1980s, Ethernet switches emerged. Due to their more advantageous working scheme than hubs, Ethernet switches therefore quickly replaced hubs to become the standard components of campus networks

## Slide 24
Notes: 2nd-generation campus network:
  In the 1990s, the growing popularity of World Wide Web (WWW) and instant messaging software posed great bandwidth challenges for campus networks. This, however, could not be met on a router-based campus backbone network. Against this backdrop, Layer 3 switches were developed in 1996. A Layer 3 switch is also called a routed switch because it integrates both Layer 2 switching and Layer 3 routing functions. Such a switch came with a simple and efficient Layer 3 forwarding engine designed and optimized for campus scenarios. Its Layer 3 routing capabilities were approximately equivalent to Layer 2 switching performance. Layer 3 switches allow computers to access the campus network, provide high-performance network connections, and meet the requirements of various WWW-based multimedia services and office systems.
3rd-generation campus network
  As we all know, smart mobile terminals first emerged in 2007. Since then, they quickly became popular and reached a wide audience. Driven by this, Wi-Fi technology also developed rapidly. Wi-Fi has subsequently become deeply integrated into and a typical feature of campus networks. SDN has also been introduced to campus networks in order to simplify services. This generation of campus networks generally meets the requirements of enterprises that are in the early stages of wireless transformation. However, Wi-Fi networks cannot deliver a high enough service quality, and therefore can only be used as a supplement to wired networks.
Campus networks have constantly evolved and made dramatic improvements in terms of bandwidth, scale, and service convergence. However, they face new challenges in connectivity, experience, O&M, security, and ecosystem as digital transformation sweeps across all industries. For example, IoT services require ubiquitous connections; HD video, Augmented Reality (AR), and Virtual Reality (VR) services call for high-quality networks; and a huge number of devices require simplified service deployment and network O&M. To address these challenges, industry vendors gradually introduce new technologies such as Artificial Intelligence (AI) and big data to campus networks, and they also launch a series of new solutions.

## Slide 25: Service Requirements and Challenges of Large- and Medium-sized Campus Networks
Converged network
Requirement:
Diversified access terminals and services call for a converged network.
Challenge:
Wi-Fi and IoT services are independently planned, deployed, and managed. The overall network construction cost is high.
The workload of network management and O&M is heavy.
User experience awareness
Requirement:
Network O&M needs to be automated and intelligent to perceive user experience anytime and anywhere.
Challenge:
Service faults cannot be detected in a timely manner.
After a fault occurs, the fault cause is located by relying heavily on the personal O&M experience of professionals. As a result, the fault cannot be quickly located.
The network cannot be automatically optimized.
Network automation
Requirement:
Networks need to be automated to cope with complex deployment and policies caused by the surge of applications and services.
Challenge:
The workload of repetitive tasks is heavy, and manual configuration is complex.
New service provisioning requires configuration of devices one by one, which is time-consuming and costly.

## Slide 26: Service Requirements and Challenges of Small- and Medium-sized Campus Networks
Multi-site O&M
Requirement:
Unified O&M is required for sites scattered in geographical locations.
Challenge:
There are a large number of sites that are geographically dispersed.
Each site is not equipped with onsite O&M professionals. Part-time O&M personnel cannot efficiently monitor the network health status.
Site provisioning period
Requirement:
New sites (such as chain stores) often need to be set up, requiring quick deployment of site networks.
Challenge:
Network engineers need to manually configure devices and services onsite, which requires high skills and results in low efficiency.
Unified policy
Requirement:
The network model of each site is basically the same. Therefore, unified network access policies need to be deployed.
Challenge:
Policy configuration is complex and manual configuration is error-prone.
Policy change is not flexible.

## Slide 27: Service Requirements and Challenges of Multi-Campus Network Interconnection
Branch interconnection cost
Requirement:
The cost of WAN interconnection between branches needs to be reduced.
Challenge:
Although the quality of carriers' physical private lines or MPLS VPNs can be guaranteed, they are expensive.
Service experience
Requirement:
The application identification capability needs to be enhanced to ensure key service experience.
Challenge:
Different enterprise applications have different requirements on link quality.
Traditional private lines cannot detect the application status and cannot guarantee key services at any time.
Management and O&M
Requirement:
Visualized measures are required to simplify management and O&M.
Challenge:
CLI-based O&M is inefficient and there are no visualized O&M methods.
If an enterprise has a large number of branches, onsite O&M results in high costs.
Unified management
Requirement:
LAN-side and WAN-side services need to be managed in a unified manner.
Challenge:
Unified configuration management and O&M cannot be implemented.

## Slide 28
Introduction to Campus Networks
Typical Campus Network Scenarios
Campus Network Trends and Challenges
Huawei CloudCampus Solution

## Slide 29: CloudCampus: One-Stop Autonomous Driving Solution for Campus Networks
Automated network design, accurately aligning with service intents
The one-stop management platform can accurately convert service intents into configuration commands.
Automated network deployment, provisioning services in minutes
Plug-and-play devices and automatic deployment of physical networks
Network resource pooling, multi-purpose network, and automatic service provisioning
Fine-grained control using intelligent policies (covering access policies, bandwidth, priorities, etc.) based on virtual networks, security groups, and applications
Automated intelligent O&M, improving network-wide performance
Real-time visualized experience: Visualized network experience for each user in each area at each moment
Precise fault analysis: Proactively identifying typical network issues and providing remediation suggestions
Intelligent network optimization: Predictive optimization of wireless networks based on historical data
Analysis
Management
Control
Design
Deployment
Policy
One-stop management
platform
NETCONF/YANG
WAN/
Internet
Multi-service campus
Simple-service campus
Campus network
interconnection
OA VN
R&D VN
OA VN
R&D VN
Security
group 1
Security
group 2
Security
group 3
Security
group 4
Security
group 5
Access policy
Bandwidth
Priority

## Slide 30: Full Scenarios: Full Coverage from Simple-Service Campuses to Multi-Branch Interconnection Campuses
Multi-branch interconnection campus
Multi-service campus
Simple-service campus
Internet
Higher education, large enterprise
VN 1
VN 2
VN 3
Internet
MPLS
 | Simple-service Campus | Multi-service Campus | Multi-branch Interconnection Campus
Network characteristics | Small scale, simple services Large numbers of sites, with similar models | Large scale, complex services, and coexistence of multiple services | Multiple branch sites, which need to communicate with each other through hybrid WAN links
Typical scenarios | Multi-branch and small/midsize enterprise campuses, such as hotels and primary/secondary schools | Higher education institutions, governments, large enterprise campuses, etc. | Large enterprises, financial branches, etc.
Hotel
Small/Midsize
enterprise
Primary/Secondary education
Store

## Slide 31: Full Lifecycle: Planning, Deployment, O&M, and Optimization
Planning (Day 0)
Deployment (Day 1-2)
O&M (Day N)
Optimization (Day N)
Wired network planning
Site design
Network resource planning
Wireless network planning
Physical network deployment
Virtual network deployment
Service policy provisioning
Hardware installation
Routine device maintenance
System maintenance (controller)
User experience visibility
Network monitoring
Network
optimization
WLAN Planner
Manual planning
Manual installation
Exception
identification
Fault demarcation
The green part indicates the network lifecycle management service provided by iMaster NCE-Campus.

## Slide 32: Full Convergence: One Controller Manages Both LAN and WAN
Simple O&M
Value extension
Forwarding-control separation
Central management of the control plane implements
flexible control while improving scalability
Control
plane
Forwarding
plane
Regional controller
Visibility into network service data, thereby easily monitoring and analyzing the status of the entire network
Services provided by the carrier can be extended from WAN to LAN and even value-added services.
WAN side
LAN side
Private
line
Internet
WAN side
LAN side
Wired
Wireless
Simplified configuration
IPsec VPN
EVPN
Centralized management
GUI
GUI, flexible networking, plug-and-play devices
Easy deployment
One set of controller manages only LAN or manages both LAN and WAN.
WAN side
LAN side (large or small/midsize campus)
WAN
Real-time
monitoring
Topology
visualization
Various reports
Intelligent analysis
Notes: Huawei CloudCampus Solution integrates service configuration and management models across LAN and WAN. It achieves LAN-WAN convergence by not only configuring and managing LAN services, but also managing WAN interconnection services.

## Slide 33
(Multiple-choice) Which of the following are typical characteristics of Huawei CloudCampus Solution? ( )
  Full convergence
  Full services
  Full lifecycle
  Full scenarios
Notes: Answer: ACD

## Slide 34
This course starts by describing the concepts, typical networking scenarios, and typical architectures of enterprise campus networks, as well as the requirements, trends, and challenges of campus networks. Finally, this course briefly introduces Huawei CloudCampus Solution.
The principles of typical features involved in this course, such as "multi-purpose network" and intelligent policy, will be explained in subsequent courses.