## Slide 1
Zhang Linrui/zwx570554, Shi Miaomiao/swx791350
2020-10-31
New

## Slide 2: Campus Network Architecture and Typical Technology Applications

## Slide 3
Campus networks are closely related to people's work and life. A typical campus network can be divided into multiple layers, including the egress layer, core layer, aggregation layer, and access layer. Each layer has its own functions, features, and common technologies and protocols.
This course describes the overall campus network architecture, common technologies and protocols, and typical networking scenarios, laying a foundation for learning key technologies of campus networks.

## Slide 4
Upon completion of this course, you will be able to:
  Describe the typical architecture of campus networks.
  Describe common Ethernet switching technologies.
  Describe common WLAN networking architectures.
  Describe common technologies of network reliability on campus networks.
  Describe common technologies for campus network service and management.
  Describe common technologies of network security on campus networks.
  Describe common VPN technologies on campus networks.

## Slide 5
Campus Network Architecture
Ethernet Switching Basics
Wireless Access
Network Reliability
Network Service and Management
Network Security
VPN

## Slide 6: Typical Architecture of a Campus Network
iStack/CSS link
Egress area
Core layer
Aggregation layer
Access layer
Terminal layer
Internet
WAN
O&M area
Data center
Data center area: has servers and application systems deployed to provide data and application services for internal and external users of an enterprise.
Egress area: is the edge between the campus internal network and the external network. Through the egress area, internal users can access the public network and external users (including customers, partners, branch users, and remote users) can access the internal network.
Core layer: is the backbone area of a campus network and is the data switching core. It connects various parts of the campus network, such as the data center, management center, and egress area.
Aggregation layer: is located at the middle layer of a campus network to implement data aggregation or switching and provide key network functions, such as routing, QoS, and security.
Access layer: provides campus network access for terminal users and is the boundary of the campus network.

## Slide 7
Campus Network Architecture
Ethernet Switching Basics
Wireless Access
Network Reliability
Network Service and Management
Network Security
VPN

## Slide 8: VLAN Technology Overview
Virtual Local Area Network (VLAN) technology logically divides a physical LAN into multiple broadcast domains, each of which is called a VLAN.
All devices in a VLAN belong to the same broadcast domain. Different VLANs belong to different broadcast domains.
Devices in a VLAN can directly communicate with each other, whereas devices in different VLANs cannot communicate directly.
Services in different VLANs are isolated from each other. Devices in different VLANs communicate with each other through Layer 3 devices.
Generally, a VLAN is a logical subnet.
Members of a VLAN are allocated based on interfaces of a switch. Generally, an interface of a switch is added to a specified VLAN. In this case, the device connected to the interface is added to the VLAN.
Core switch
Access switch 1
Access switch 2
Terminal 1
1.1.1.1/24
Terminal 2
1.1.1.2/24
Terminal 3
1.1.1.3/24
Terminal 4
2.2.2.1/24
VLAN 10 (office)
VLAN 20
(monitoring)

## Slide 9: VLAN Assignment Methods
VLAN Assignment Method | Implementation | Usage Scenario
Interface-based assignment | VLANs are assigned based on interfaces. | Networks of any scale and with devices at fixed locations
MAC address-based assignment | VLANs are assigned based on source MAC addresses of frames. | Small-scale networks where user terminals often change physical locations but their NICs seldom change
IP subnet-based assignment | VLANs are assigned based on source IP addresses and subnet masks. | Scenarios where there are high requirements for mobility and simplified management and low requirements for security
Protocol-based assignment | VLANs are assigned based on protocol (suite) types and encapsulation formats of frames. | Networks using multiple protocols
Policy-based VLAN assignment (MAC addresses, IP addresses, and interfaces) | VLANs are assigned based on policies such as combinations of interfaces, MAC addresses, and IP addresses. | Complex networks

## Slide 10: Overview of Voice VLAN Technology
Multiple types of flows are transmitted on a network simultaneously. Packet loss and delay seriously affect voice communication quality. Users are more sensitive to the quality of the voice service than data and video services. Therefore, voice data flows must be preferentially transmitted when there is limited bandwidth available.
Voice VLAN technology is used to exclusively transmit voice data.
After a voice VLAN is configured on a switch, the switch can identify voice data flows, transmit the voice data flows to the voice VLAN, and provide QoS guarantee for the voice data flows.
Network
PC
IP Phone
Switch
You can use just one interface of a switch to transmit voice and data services simultaneously.
Network
IP phone
Switch
An IP phone is connected to a switch independently.
Typical networking of voice VLAN technology
Notes: Voice data flows must be identified first so that measures can be taken to improve the transmission priority.
Some IP phones send tagged voice packets and some IP phones (for example, Huawei MC850) send untagged voice packets.

## Slide 11: MAC Address-based Voice VLAN
Configure MAC address-based voice VLAN when voice packets are untagged or tagged with VLAN 0.
After receiving untagged packets from PCs and IP phones, the switch processes the packets as follows:
  If the source MAC address matches the OUI configured on the switch (the result of the AND operation between the source MAC address and the OUI mask is equal to the OUI), the switch tags the voice VLAN ID to the packet and increases the packet priority.
  If they do not match, the switch adds the PVID to the voice packet.
Run the voice-vlan mac-address command to specify the MAC address and mask
Data packet
Voice packet
Network
PC
IP phone
Switch
Notes: An OUI is the first 24 bits of a 48-bit MAC address assigned to each vendor by the Institute of Electrical and Electronics Engineers (IEEE). Voice packets sent by IP phones can be identified by the MAC address ranges requested by IP phone vendors.
In voice VLAN, the OUI is user-defined and not necessarily 24 bits long. The OUI is the result of the AND operation between the source MAC address and the OUI mask in the voice-vlan mac-address command.

## Slide 12: VLAN ID-based Voice VLAN
If the IP phone can obtain the voice VLAN ID of the switch through a protocol, the IP phone sends voice packets with VLAN tags. In this case, you can configure VLAN ID-based voice VLAN.
After receiving packets from the PC and IP phone, the switch determines whether the VLAN IDs in the packets match the configured voice VLAN ID. If they match, the switch handles data as voice data and increases the priority. The switch adds the PVID to untagged packets from the PC.
When VLAN ID-based voice VLAN is configured, the IP phone must be able to obtain voice VLAN information from the switch. IP phones can obtain voice VLAN information from switches using multiple methods, such as the Link Layer Discovery Protocol (LLDP).
Data packet
Send LLDPDUs
Return the voice VLAN ID
Tagged voice packet
Network
PC
IP phone
Switch
Notes: In this example, after the IP phone goes online, it sends an LLDPDU to request voice VLAN information from the switch.

## Slide 13
Campus Network Architecture
Ethernet Switching Basics
Wireless Access
Network Reliability
Network Service and Management
Network Security
VPN

## Slide 14: WLAN Network Architectures (1)
Fat AP
Internet
Networking characteristics: A Fat AP works independently and needs to be configured separately. It provides only simple functions and is cost-effective.
Applicable scenario: Families or mini-stores
AC + Fit AP
Networking characteristics: A Fit AP provides multiple functions and is used with the AC. It is managed and configured by the AC in a unified manner. There are high requirements on skills of maintenance personnel.
Applicable scenario: Medium- and large-sized enterprises
Fat AP
Fit AP
AC

## Slide 15: WLAN Network Architectures (2)
Networking characteristics: APs need to work with iMaster NCE-Campus. iMaster NCE-Campus manages and configures APs in a unified manner, and provides rich functions and supports plug-and-play. There are low requirements for maintenance personnel's skills.
Applicable scenario: small- and medium-sized enterprises
Internet
Cloud AP
CloudCampus solution (small- and medium-sized campus network scenarios)

## Slide 16: WLAN Network Architectures (3)
Next-generation campus network: CloudCampus solution (large- and medium-sized campus network scenarios)
Networking characteristics: The solution uses the native AC function of switches to manage APs on a network, implements wired and wireless network convergence, and leverages big data and AI technologies to implement simplified, smart, and secure campus networks.
Applicable scenario: large- and medium-sized enterprises
Egress area
Core layer
Aggregation layer
Access layer
Data center
Native AC
Native AC
O&M area
iStack/CSS Link
Internet
WAN

## Slide 17: WLAN Network Architectures (4)
Leader AP
Networking characteristics: A leader AP can work independently or manage a small number of common APs to implement basic roaming functions. The cost is low, and there are low requirements for maintenance personnel's skills.
Applicable scenario: small and micro enterprises
Agile distributed AP
Networking characteristics: The agile distributed architecture divides an AP into a central AP and remote units (RUs). The central AP can manage multiple RUs, which provides good coverage and reduces costs. Agile distributed APs can be used in the Fat AP, AC + Fit AP, and cloud management architectures.
Applicable scenario: scenarios where rooms are densely distributed
Internet
Leader AP
Central AP
Room 1
Room 2
Room 3
Room N
Central AP
Room 1
Room 2
Room 3
Room N
AC
Agile distributed AP
Agile distributed AP

## Slide 18
Campus Network Architecture
Ethernet Switching Basics
Wireless Access
Network Reliability
Network Service and Management
Network Security
VPN

## Slide 19: Using VRRP to Implement Gateway Redundancy
Basic VRRP application
Typical application of MSTP+VRRP
Aggregation switch 1
Aggregation switch 2
Access switch
Aggregation switch 1
Aggregation switch 2
Access switch
VRRP
Virtual router
192.168.1.254
IP address: 192.168.1.1/24
Default gateway: 192.168.1.254
Redundancy
Load balancing
Association
VLANs 11, 12,...,20
VLANIF11-20 VRRP Master
VLANIF21-30 VRRP Backup
MSTI 10 Primary root bridge
MSTI 20 Secondary root bridge
MSTP
VLANIF11-20 VRRP Backup
VLANIF21-30 VRRP Master
MSTI 10 Secondary root bridge
MSTI 20 Primary root bridge
MSTP
VRRP
VRRP
VLANs 21,12,...,30
VRRP and MSTP are used to implement gateway redundancy, load balancing, Layer 2 loop prevention, and reliability.
Notes: Generally, all hosts on the same network segment are configured with the same default route with the gateway address as the next-hop address. The hosts use the default route to send packets to the gateway and the gateway forwards the packets to other network segments. When the gateway fails, hosts with the same default route cannot communicate with external networks.
The Virtual Router Redundancy Protocol (VRRP) virtualizes several routing devices into a virtual router and uses the IP address of the virtual router as the default gateway address to communicate with external networks. If a gateway fails, VRRP selects a different gateway to forward traffic, thereby ensuring reliable communication.
  Redundancy: Multiple routing devices enabled with VRRP constitute a VRRP group and the VRRP group is used as the default gateway. When a single point of failure (SPOF) occurs, services are transmitted through the backup link. This reduces the possibility of network faults and ensures nonstop transmission of various services.
  Load balancing: VRRP enables multiple available routers to share the load more uniformly, reducing the traffic burden on the master.
  Association: VRRP can monitor faults on uplinks. When the upstream interface or uplink is faulty, the priority of the original master decreases, and an optimal backup becomes the master, ensuring proper traffic forwarding. Association between VRRP and BFD speeds up the active/standby switchover. To speed up the active/standby switchover in the VRRP group, configure a BFD session between the master and backup and associate the BFD session with the VRRP group. This is because BFD can fast detect faults. When the link between the master and backup becomes Down, the backup immediately switches to the master and takes over traffic.

## Slide 20: Using Link Aggregation, iStack, and CSS Technologies to Implement Link- and Device-level Reliability
Ethernet link aggregation, also called Eth-Trunk, bundles multiple physical links into a logical link to increase link bandwidth, without having to upgrade hardware.
Intelligent stack (iStack) enables multiple stacking-capable switches to function as a single logical switch. iStack is applicable to Huawei fixed switches.
A cluster switch system (CSS) combines two clustering-capable switches into a single logical switch. A CSS is also called a cluster. CSS is applicable to Huawei modular switches.
Link aggregation can be used with iStack or CSS to implement link-level and device-level reliability and increase network bandwidth.
iStack
CSS
iStack
iStack
iStack/CSS Link
Eth-Trunk
Network

## Slide 21: Overview of NQA
To visualize the quality of network services and allow users to check whether the quality of network services meets requirements, the following measures must be taken:
  Enable the device to provide network service quality information.
  Deploy probe devices to monitor network service quality.
The preceding measures require devices to provide statistical parameters such as the delay, jitter, and packet loss ratio and require dedicated probe devices. These requirements increase investments on devices.
When NQA is deployed on devices, dedicated probe devices do not need to be deployed, which effectively reduces costs. NQA can accurately test the network running status and output statistics.
NQA measures network performance and collects statistics on the delay, jitter, and packet loss ratio.
Network
TCP detection
DNS detection
HTTP detection
NQA test instance
NQA client
NQA server
ICMP detection
Notes: NQA measures the performance of various protocols running on networks, which helps users collect statistics about network operation indexes in real time.

## Slide 22: NQA Association
NQA association involves the monitoring module, track module, and application module.
Monitoring module
NQA detection
module
Track module
Application module
VRRP
Static route
PBR
Interface backup
IGMP proxy
IP address pool
DNS server
Notes: The monitoring module monitors the link status and network performance and notifies the track module of the detection result.
After receiving the detection result from the monitoring module, the track module changes the status of the tracking item in a timely manner and notifies the application module of the change.
The application module performs corresponding processing according to the status of the tracking item.

## Slide 23: NQA Fundamentals
NQA tests the service quality on the live network by sending data packets of a specific service.
In an NQA test instance, the two ends are called the client and server (or source and destination). The NQA client initiates an NQA test instance. After the NQA test instance is configured on the NQA client, NQA places the test instance into a test instance queue for scheduling.
An NQA test instance can be associated with multiple modules. The NQA module notifies other modules of the test result, and other modules take measures according to the detection result.
Network
NQA test instance
NQA client
NQA server
NQA test
Data
Add the timestamp to NQA test data
NQA test
Data
The NQA server returns a packet after receiving data
NQA test
Data
Compare the timestamp with the local time of the device to determine the test result
NQA test results
Other modules, such as VRRP and static route
NQA test results can be used by other modules
TCP detection
DNS detection
HTTP detection
ICMP detection
Notes: NQA can be associated with VRRP, static route, interface backup, IGMP proxy, IP address pool, DNS server, and PBR.
The maximum delay, packet loss ratio, and jitter can be configured for an NQA test instance. If the delay, jitter, or packet loss ratio of the NQA test instance exceeds the configured values, the NQA test instance fails.

## Slide 24: NQA Test Instance Types
NQA can be used to test the network quality of the following common services.
Application layer
DHCP test
DNS test
FTP test
HTTP test
Transport layer
TCP test
UDP test
UDP jitter test
SNMP test
Connectivity
ICMP test
ICMP jitter test
LSP ping
LSP trace
Trace
VPLS ping
VPLS trace
VPLS PW ping

## Slide 25
Campus Network Architecture
Ethernet Switching Basics
Wireless Access
Network Reliability
Network Service and Management
Network Security
VPN

## Slide 26: DHCP
Using the Dynamic Host Configuration Protocol (DHCP) to automatically configure IP addresses
Typical application of DHCP on a large-scale campus network
DHCP client
Layer 2 switch
DHCP server
The DHCP client broadcasts a DHCP Discover message.
1
2
The DHCP server responds with a DHCP Offer message.
The DHCP client broadcasts a DHCP Request message.
3
4
The DHCP server responds with a DHCP ACK message.
Search for the DHCP server on the network
Provide information such as the IP address
Specify the IP address provided by a DHCP server
Check the IP address allocation
DHCP Server
DHCP client
DHCP client
Layer 3 gateway
Deploy a DHCP relay agent
DHCP is widely used on various campus networks to implement automatic IP address configuration for wired or wireless terminals.
A DHCP relay agent forwards DHCP messages between a DHCP server and DHCP clients to help the DHCP server to dynamically allocate network parameters to the DHCP clients.
Layer 3 gateway
Deploy a DHCP relay agent
Notes: DHCP dynamically configures and uniformly manages IP addresses of hosts. DHCP is defined in RFC 2131 and uses the client/server communication mode. A DHCP client requests configuration information from a DHCP server, and the DHCP server returns the configuration information allocated to the DHCP client.
  DHCP enables a host to obtain an IP address dynamically, but does not specify an IP address for each host.
  DHCP can allocate other configuration parameters, such as the boot file of a client, so that the client can obtain all the required configuration information by using only one message.
  DHCP supports dynamic and static IP address allocation. A network administrator can select different address allocation modes for hosts as required.
    Dynamic allocation: DHCP allocates an IP address with a limited validity period (known as a lease) to a client. This mechanism applies to scenarios where hosts temporarily access the network and the number of idle IP addresses is less than the total number of hosts.
    Static allocation: DHCP allocates fixed IP addresses to clients as configured. Compared with manual IP address configuration, DHCP static allocation prevents manual configuration errors and enables unified maintenance and management.
DHCP offers the following benefits:
  Reduced client configuration and maintenance costs
  Centralized management of limited IP addresses

## Slide 27: Option Fields of DHCP
DHCP client
DHCP server
DHCP Offer
IP address assigned to a DHCP client
…
Options
It stores control information and parameters allocated to a DHCP client.
A DHCP message can carry multiple Options fields.
DHCP predefines a large number of Options fields for various purposes, for example, setting the gateway address and DNS server address.
Option fields in DHCP messages
The Option field can be used to set the IP address of the NTP server.
The Option field can be vendor-defined. For example, the CloudCampus solution uses Option 148 to implement plug-and-play of network devices. The information is used to notify the DHCP client of controller information so that the device can obtain the controller address and port number.
Option 43 is used to implement AP plug-and-play in WLAN scenarios.
Typical application scenarios

## Slide 28: LLDP
Network management requirements and overview of LLDP
Application of LLDP in Huawei CloudCampus solution
Most NMSs can detect Layer 3 network topologies, but they cannot detect detailed Layer 2 topologies or configuration conflicts.
LLDP provides a standard link-layer discovery method:
  Obtains the topology status of the connected devices.
  Displays paths between devices.
  Detects configuration conflicts between devices and queries network failure causes.
You can use an NMS to monitor the link status on devices running LLDP and quickly locate network faults.
SW1
SW2
SW3
GE1/0/1
GE1/0/1
[SW3] display lldp neighbor brief
Local Intf Neighbor Dev Neighbor Intf Exptime(s)
GE1/0/1 SW2 GE1/0/1 101
The device reports LLDP information to the controller.
1
2
3
The controller restores and displays the network topology based on the LLDP information reported by devices.
Notes: LLDP is a standard Layer 2 topology discovery protocol defined in IEEE 802.1ab. LLDP collects local device information including the management IP address, device ID, and port ID and advertises the information to neighboring devices. Neighboring devices save the received information in their management information bases (MIBs). The NMS can use data in MIBs to query the link status.
An NMS must be capable of managing multiple network devices with diverse functions and complex configurations. Most NMSs can detect Layer 3 network topologies, but they cannot detect detailed Layer 2 topologies or configuration conflicts. A standard protocol is required to exchange Layer 2 information between network devices.
LLDP provides a standard link-layer discovery method. Layer 2 information obtained from LLDP allows the NMS to detect the topology of neighboring devices, and display paths between clients, switches, routers, application servers, and network servers. The NMS can also detect configuration conflicts between network devices and identify causes of network failures. Enterprise users can use an NMS to monitor the link status on devices running LLDP and quickly locate network faults.

## Slide 29: SNMP
Network management standard widely used on TCP/IP networks.
SNMP uses a central computer (a network management station) that runs network management software to manage devices.
By employing the "network management over networks" mode, SNMP is used for efficient and batch network device management. In addition, SNMP enables unified management of network devices of different types and from different vendors.
Overview of SNMP
SNMP
NMS (SNMP server)
Example: iMaster NCE
Managed device (SNMP client)
Example: Routers and switches
Agent
MIB

## Slide 30: NETCONF
SNMP is not a configuration-oriented protocol. On a large-sized network with a complex topology, SNMP cannot meet network management requirements, especially configuration management requirements.
SNMP weaknesses
NETCONF
NMS (NETCONF server)
Example: iMaster NCE
Managed device (NETCONF client)
Example: Routers and switches
NETCONF provides a mechanism for communication between the NMS and network devices.
A network administrator can use NETCONF to add, modify, or delete configurations of network devices, and obtain configurations and status of network devices.
Overview of NETCONF
Notes: In Huawei CloudCampus Solution, a managed device can be managed by the NMS only after a NETCONF session is established between the managed device and iMaster NCE-Campus. Therefore, the managed device needs to know the IP address and port information of iMaster NCE-Campus. The managed device can obtain iMaster NCE-Campus information in the following ways:
  DHCP server: Option 148 is configured on the DHCP server on the network. Option 148 contains the NETCONF status and iMaster NCE-Campus address. Managed devices obtain the information through DHCP.
  Registration query center: The IP address corresponding to the URL of the registration query center is configured in DNS information of the DHCP server on the network. A switch accesses the registration query center through the preset URL and port number of the registration query center or through software upgrade.
  Manual configuration through the CLI or GUI: You can manually configure a switch based on iMaster NCE-Campus information that you have learned.
Note: For details, see Huawei CloudCampus Solution.

## Slide 31: Telemetry
Telemetry is also called network telemetry. It is used to monitor networks, including packet check and analysis, intrusion and attack detection, intelligent data collection, and application performance management. Generally, telemetry is used together with NETCONF. The analyzer analyzes the data collected by telemetry. The analyzer associates with the controller and automatically modifies device configurations based on the analysis result.
Collector
Controller
Analyzer
Telemetry
Upload data
NETCONF
Deliver configurations
Network device
Subsecond-level
Telemetry has the following advantages:
  Supports multiple implementation modes, meeting diversified user requirements.
  Collects a wide variety of data with high precision to fully reflect network status.
  Continuously reports data with only one-time data subscription.
  Locates faults rapidly and accurately.
Notes: With the popularization of networks and emergence of new technologies, the network scale is growing, network deployment is increasingly complex, and users have higher requirements on service quality. To meet user requirements, network O&M must be more refined and intelligent. Network O&M are faced with the following challenges:
  Ultra-large scale: A large number of devices need to be managed and massive amount of information is monitored.
  Quick fault locating: Users want faults to be located within seconds or even subseconds on complex networks.
  Refined monitoring: Various types of data need to be monitored at a finer granularity to reflect the network status completely and accurately. With the monitoring information, possible faults can be predicted, providing a sound foundation for network optimization. Network O&M involves monitoring not only traffic statistics on interfaces, packet loss on each flow, CPU usage, and memory usage, but also the latency and jitter of each flow, latency of each packet on its transmission path, and buffer usage on each device.

## Slide 32
Notes: The collector, analyzer, and controller are components of the network management system.
  The collector receives and stores monitoring data reported by network devices.
  The analyzer analyzes the monitoring data received by the collector and processes the data, for example, displays the data on the graphical user interface.
  The controller uses NETCONF to deliver configurations to devices to manage network devices. The controller can deliver configurations to network devices based on the analysis data provided by the analyzer and adjust forwarding behaviors of network devices. The network device can be configured to sample and report specified data.

## Slide 33
Campus Network Architecture
Ethernet Switching Basics
Wireless Access
Network Reliability
Network Service and Management
Network Security
VPN

## Slide 34: Deploying NAC to Implement Network Access Control on Access Users
User terminal
Authentication server
Internet
WAN
WLAN AC
WLAN AC
Data
center
O&M area
How to ensure that terminal identities are valid
How to ensure that authorized terminals are authorized correctly
Network Admission Control (NAC) is an end-to-end security technology that authenticates clients and users to ensure network security.
NAC provides three authentication modes: 802.1X authentication, MAC address authentication, and Portal authentication.
Authentication device
Notes: In addition to using NAC to authenticate access users and control their rights, a campus network also needs to authenticate and control rights of administrators (also called login users) who can log in to devices through FTP, HTTP, SSH, Telnet, or console ports.

## Slide 35: Port Isolation
VLAN 10 (office VLAN)
Core switch
Access switch 1
Terminal 1
1.1.1.1/24
Terminal 2
1.1.1.2/24
Users in the same VLAN are isolated to enhance user communication security, and prevent invalid broadcast packets from affecting services.
Data exchanged between different users in the same VLAN can be forwarded by the upper-layer device in a centralized manner.
Requirement
Port isolation can isolate ports in the same VLAN.
That is, you only need to add ports to a port isolation group to implement Layer 2 isolation between these ports.
The port isolation mode can be Layer 2 isolation and Layer 3 interworking or Layer 2 and Layer 3 isolation.
  To isolate broadcast packets in the same VLAN but allow users connected to different interfaces to communicate at Layer 3, you can set the port isolation mode to Layer 2 isolation and Layer 3 interworking.
  To prevent interfaces in the same VLAN from communicating at both Layer 2 and Layer 3, you can set the port isolation mode to Layer 2 and Layer 3 isolation.
Solution
Terminal 3
1.1.1.3/24
Enable port isolation and add the ports to the same port isolation group
Notes: Port isolation provides secure and flexible networking schemes.
Port isolation can be used together with the proxy ARP function. In some scenarios, data exchanged between terminals in a VLAN needs to be forwarded by an upper-layer device instead of an access switch. This ensures that traffic is forwarded by the upper-layer device instead of the access switch, so that traffic management and control policies can be deployed on the upper-layer device. This mode is called centralized forwarding mode. In centralized forwarding mode, port isolation is configured for all downlink Layer 2 devices. Therefore, proxy ARP should be configured on the core gateway. In most cases, intra-VLAN proxy ARP is used.

## Slide 36: Introduction to Ethernet Port Security
Point that allows for port security
Core switch
Access switch 1
Access switch 2
Terminal 1
Terminal 2
Terminal 3
Terminal 4
An enterprise requires that each access switch interface connected to terminals allow only one PC to access the network so as to limit the number of MAC addresses.
If an employee tries to connect a small switch or hub to an interface to extend the Internet access interface, this behavior should be detected or prohibited.
In addition, some enterprises may require that only data frames sent by terminals with trusted MAC addresses can be forwarded to the upper-layer network by a switch. Employees are not allowed to change their locations, that is, change access interfaces of the switch.
Requirement
Port security converts the dynamic MAC addresses learned on an interface into secure MAC addresses (including dynamic and static secure MAC addresses, and sticky MAC addresses). This function prevents unauthorized users from using this interface to communicate with the switch and therefore enhances device security.
Solution
Notes: Configuring port security on an interface of a switch can limit the number of MAC addresses learned by the interface. Then punishment measures can be taken when a violation occurs.
The interface configured with port security can convert the learned MAC addresses into secure MAC addresses to prevent devices with other MAC addresses from accessing the network through the interface.
Port security converts the dynamic MAC addresses learned on an interface into secure MAC addresses (including dynamic and static secure MAC addresses, and sticky MAC addresses). This function prevents unauthorized users from using this interface to communicate with the switch and therefore enhances device security.

## Slide 37: Ethernet Port Security: Classification of Secure MAC Addresses
Point that allows for port security
Core switch
Access switch 1
Access switch 2
Terminal 1
1.1.1.1/24
5469-98AB-0001
Terminal 2
1.1.1.2/24
5469-98AB-0002
Terminal 3
1.1.1.3/24
5469-98AB-0003
Terminal 4
2.2.2.1/24
5469-98AB-0004
Type | Definition | Description
Secure dynamic MAC address | MAC address that is converted on an interface with port security enabled but sticky MAC disabled | By default, secure dynamic MAC addresses are not aged out, and can be aged out only when the configured aging time is reached. After a device restarts, secure dynamic MAC addresses are lost and need to be relearned.
Secure static MAC address | MAC address that is manually configured on an interface with port security enabled | Secure static MAC addresses are not aged out and are not lost after a device restart.
Sticky MAC address | MAC address that is converted on an interface with both port security and sticky MAC enabled | 

## Slide 38: Ethernet Port Security: Protection Actions
Port security is deployed, the MAC address of the camera is bound, and only one MAC address is allowed.
Core switch
Access switch 1
Access switch 2
Terminal 4
2.2.2.1/24
5469-98AB-0004
If a switch receives packets with a nonexistent source MAC address after the number of secure MAC addresses reaches the limit, the switch considers that the packets are sent from an unauthorized user, regardless of whether the destination MAC address of packets is valid. The switch then takes the configured action on the interface.
Replace the terminal with an unauthorized terminal
Action | Description
restrict | Discards packets with a nonexistent source MAC address and generates an alarm. This action is recommended.
protect | Discards packets with a nonexistent source MAC address but does not generate an alarm.
shutdown | Sets the interface state to Error-Down and generates an alarm.

## Slide 39: MACsec Provides Secure Layer 2 Data Transmission
Site 1
Site 2
Internet
MACsec
MACsec
IPsec
Background
Most data is transmitted in plaintext on LAN links, failing to meet requirements of scenarios demanding high security.
MACsec overview
Media Access Control Security (MACsec), in compliance with 802.1AE, defines a method for secure data communication based on the Ethernet. Data is encrypted hop by hop to ensure data transmission security.
Data source integrity check
User data encryption
Data source authenticity verification
Replay protection
Typical application scenarios
MACsec is deployed between switches to ensure data security. For example, MACsec is deployed between access switches and uplink aggregation or core switches.
When transmission devices exist between switches, MACsec can be deployed to ensure data security.

## Slide 40: DHCP Snooping
Some attacks are launched based on DHCP. These attacks include the bogus DHCP server attack, DHCP server DoS attack, and bogus DHCP message attack.
DHCP snooping ensures that DHCP clients obtain IP addresses from authorized DHCP servers and records mappings between IP addresses and MAC addresses of DHCP clients, preventing DHCP attacks on the network.
DHCP client
DHCP client
Authorized DHCP server
Unauthorized DHCP server
Invalid DHCP ACK, NAK, and Offer messages
2
3
Obtain an incorrect IP address
1
2
Notes: DHCP snooping ensures that DHCP clients obtain IP addresses from authorized DHCP servers and records mappings between IP addresses and MAC addresses of DHCP clients, preventing DHCP attacks on the network. DHCP snooping is equivalent to a firewall between DHCP clients and the DHCP server to prevent DHCP attacks on the network, ensuring security for communication services. DHCP snooping is classified into DHCPv4 snooping and DHCPv6 snooping. The working mechanisms of DHCPv4 snooping and DHCPv6 snooping are similar.
The DHCP snooping-enabled device forwards DHCP Request messages of users (DHCP clients) to an authorized DHCP server through the trusted interface, and then generates DHCP snooping binding entries according to the DHCP ACK messages received from the DHCP server. When receiving DHCP messages from users through the DHCP snooping-enabled interfaces, the device checks the messages against the binding table, to prevent attacks initiated by unauthorized users. In addition, DHCP snooping supports multiple security features, such as limiting the rate of sending DHCP messages.

## Slide 41: DHCP Snooping Trust Function
The DHCP snooping trust function ensures that clients obtain IP addresses from an authorized DHCP server. DHCP snooping involves two interface roles: trusted and untrusted interfaces.
  The trusted interface can receive DHCP ACK, NAK, and Offer messages sent by the DHCP server. In addition, the device only forwards DHCP Request messages from DHCP clients to the authorized DHCP server through the trusted interface.
  The untrusted interface discards DHCP ACK, NAK, and Offer messages sent by the DHCP server.
DHCP snooping trusted interface
DHCP snooping untrusted interface
Other interfaces enabled with DHCP snooping
DHCP client
DHCP client
Authorized DHCP server
Unauthorized DHCP server
Invalid DHCP ACK, NAK, and Offer messages

## Slide 42: DHCP Snooping Binding Table
After DHCP snooping is enabled on a Layer 2 switch, the switch listens to DHCP messages.
The switch extracts key information from the DHCP message and obtains information about the DHCP snooping-enabled interface connected to the PC. Based on the information, the switch generates a DHCP snooping binding table.
The DHCP snooping binding table records the mappings between IP addresses and MAC addresses of DHCP clients. The switch can check DHCP messages against the DHCP snooping binding table to prevent attacks initiated by unauthorized users.
PC1
with 0000-0000-1111
obtains 1.1.1.1/24
PC2
with 0000-0000-2222
obtains 1.1.1.2/24
Authorized DHCP server
DHCP message exchange
DHCP message exchange
IP Address | MAC Address | VLAN ID | Interface
1.1.1.1 | 0000-0000-1111 | 10 | GE0/0/1
1.1.1.2 | 0000-0000-2222 | 10 | GE0/0/2
GE0/0/1
GE0/0/2
DHCP snooping binding table
Notes: After DHCP snooping is enabled on a Layer 2 switch, the switch listens to DHCP messages. The switch obtains required information, such as the PC's MAC address, IP address, and address lease, from the DHCP messages, learns information (interface number and VLAN ID) about the DHCP snooping-enabled interface connected to the PC, and generates a DHCP snooping binding entry for the PC.
For example, when receiving a DHCP ACK message for PC1, the Layer 2 access device obtains IP address 1.1.1.1, MAC address 0000-0000-1111, and GE0/0/1 connected to the PC from the DHCP ACK message, and then generates a DHCP snooping binding entry for PC1.
The DHCP snooping binding entries are aged out when the DHCP lease expires, or the entries are deleted when users send DHCP Release messages to release IP addresses.

## Slide 43: Using DAI to Prevent ARP Spoofing Attacks
ARP attacks are frequently launched on networks. A man-in-the-middle (MITM) attack is a common ARP spoofing attack.
To defend against MITM attacks, configure dynamic ARP inspection (DAI) on a switch.
DAI defends against MITM attacks using a DHCP snooping binding table. When a device receives an ARP packet, it compares the source IP address, source MAC address, interface number, and VLAN ID of the ARP packet with DHCP snooping binding entries.
  If the ARP packet matches a binding entry, the device considers the ARP packet valid and allows the packet to pass.
  If the ARP packet matches no binding entry, the device considers the ARP packet invalid and discards the packet.
ARP packet:
Sender IP address: 1.1.1.1
Sender MAC address: 0000-0000-2222
DHCP snooping binding table
PC1
with 0000-0000-1111
obtains 1.1.1.1/24
PC2
with 0000-0000-2222
obtains 1.1.1.2/24
Authorized DHCP server
GE0/0/1
GE0/0/2
IP Address | MAC Address | VLAN ID | Interface
1.1.1.1 | 0000-0000-1111 | 10 | GE0/0/1
1.1.1.2 | 0000-0000-2222 | 10 | GE0/0/2
Notes: ARP attacks are frequently launched on networks. An MITM attack is a common ARP spoofing attack. An MITM attacker establishes connections with two ends and exchanges data between them. The two ends consider that they are directly communicating, but actually the attacker has controlled the entire session. In an MITM attack, the attacker intercepts all packets exchanged between the two ends and inserts new ones.
To defend against MITM attacks, configure DAI on a switch.
  DAI defends against MITM attacks using a DHCP snooping binding table. When a device receives an ARP packet, it compares the source IP address, source MAC address, interface number, and VLAN ID of the ARP packet with DHCP snooping binding entries. If the ARP packet matches a binding entry, the device considers the ARP packet valid and allows the packet to pass. If the ARP packet matches no binding entry, the device considers the ARP packet invalid and discards the packet.
  DAI is available only when DHCP snooping is configured. The device enabled with DHCP snooping generates DHCP snooping binding entries when DHCP users go online. If a user is configured with a static IP address, you need to manually configure a static binding entry for the user.
  When an attacker connected to the DAI-enabled switch sends bogus ARP packets, the switch detects the attacks based on the binding entries and discards the bogus ARP packets. When both the DAI and packet discarding alarm functions are enabled on the switch, the switch generates alarms when the number of discarded ARP packets matching no binding entry exceeds the alarm threshold.

## Slide 44: IPSG
IP Source Guard (IPSG) implements source IP address filtering based on Layer 2 interfaces. IPSG prevents malicious hosts from simulating authorized hosts using forged IP addresses. In addition, IPSG prevents unauthorized hosts from accessing or attacking networks using forged IP addresses.
IPSG checks IP packets on Layer 2 interfaces against a binding table that contains the bindings of source IP addresses, source MAC addresses, VLAN IDs, and inbound interfaces. Only packets matching the binding table are forwarded, and other packets are discarded.
Authorized terminal 1
1.1.1.2/24
0000-0000-2222
Unauthorized terminal
1.1.1.2/24
0000-0000-FFFF
1
The authorized terminal is powered off.
2
An unauthorized terminal accesses the network, forges authorized terminal 1, and uses terminal 1's IP address to access the network.
Binding table
GE0/0/1
GE0/0/2
3
The unauthorized terminal sends data.
4
The switch identifies and discards invalid traffic based on the binding table.
IP Address | MAC Address | VLAN ID | Interface
1.1.1.1 | 0000-0000-1111 | 10 | GE0/0/1
1.1.1.2 | 0000-0000-2222 | 10 | GE0/0/2
Notes: As networks continue to increase in scale, many attackers are forging source IP addresses to initiate network attacks (IP address spoofing attacks). Some attackers forge IP addresses of authorized users to obtain network access rights and access networks. As a result, authorized users are unable to access networks or sensitive information may be intercepted.
IPSG provides a mechanism to effectively defend against IP address spoofing attacks.
  The binding table can be static or dynamic.
  IPSG checks only the IP packets from hosts. It does not check non-IP packets such as ARP packets.

## Slide 45: Using VRF Technology for Logical Isolation
Terminal 4
2.2.2.1/24
Core switch
Access switch 1
Access switch 2
Terminal 1
1.1.1.1/24
Terminal 3
1.1.1.2/24
Terminal 4
2.2.2.2/24
VLAN 10 (office)
VLAN 20 (monitoring)
Isolation
Isolation
Isolation
VLANIF 10 1.1.1.254/24
VLANIF 20 2.2.2.254/24
Multiple logical networks, such as the office network and monitoring network, can be constructed on a simple physical campus network.
The office network is completely isolated from the monitoring network.
Requirement
ACL: ACLs can be used to isolate traffic between VLANs. However, the scalability is poor.
Independent physical network construction: Office and monitoring networks use different physical networks to isolate services, increasing network construction costs.
Virtual Routing and Forwarding (VRF): It is also called a VPN instance, which is similar to a virtual device. A VPN instance uses a routing table independent of the root device to completely isolate the VPN instance from the root device, without increasing hardware costs.
Solution

## Slide 46
Campus Network Architecture
Ethernet Switching Basics
Wireless Access
Network Reliability
Network Service and Management
Network Security
VPN

## Slide 47: GRE
R1
PC1
2001:0DB8:0:0::1/64
R2
PC2
2001:0DB8:0:1::1/64
1.1.1.1
2.2.2.2
GRE tunnel
Source IP | 2001:0DB8:0:0::1
Destination IP | 2001:0DB8:0:1::1
Payload | Data
Source IP | 1.1.1.1
Destination IP | 2.2.2.2
GRE header | 
Source IP | 2001:0DB8:0:0::1
Destination IP | 2001:0DB8:0:1::1
Payload | Data
Generic Routing Encapsulation (GRE) is a mechanism used for encapsulating data of some network-layer protocols (IPX, IPv6, and IPv4) and transmitting the encapsulated packets using another network-layer protocol such as IPv6 and IPv4.
GRE is a Layer 3 tunneling technology that transparently transmits packets over GRE tunnels. It solves the transmission problems on the network that uses different network-layer protocols.
  GRE is easy to implement and increases only a few loads on devices at both ends of a tunnel.
  GRE sets up tunnels over an IPv4 network to connect networks running different protocols, reusing the original network architecture and reducing costs.
  GRE connects non-contiguous subnets and sets up virtual private networks (VPNs) to ensure secure connections between the enterprise headquarters and branches.
  GRE provides only simple password authentication and does not provide the encryption function.
Source IP | 2001:0DB8:0:0::1
Destination IP | 2001:0DB8:0:1::1
Payload | Data

## Slide 48: IPsec VPN
R1
PC1
192.168.1.1/24
R2
PC2
172.16.1.1/24
1.1.1.1
2.2.2.2
IPsec VPN tunnel
Source IP | 192.168.1.1
Destination IP | 172.16.1.1
Payload | Data
Source IP | 1.1.1.1
Destination IP | 2.2.2.2
Security protocol header | 
Source IP | 192.168.1.1
Destination IP | 172.16.1.1
Payload | Data
Source IP | 192.168.1.1
Destination IP | 172.16.1.1
Payload | Data
Internet Protocol Security (IPsec) is a set of open network security protocols defined by the Internet Engineering Task Force (IETF) and is used to protect transmitted data and reduce the risk of information leakage.
Through encryption and authentication, IPsec ensures secure service data transmission over the Internet from the following dimensions:
  Data source authentication
  Data encryption
  Data integrity verification
  Anti-replay

## Slide 49: L2TP VPN
LAC
Remote OA user
L2TP VPN tunnel
Enterprise headquarters
External network
LAC
Enterprise branch
L2TP VPN tunnel
L2TP extends the application of the Point-to-Point Protocol (PPP). It is a VPN that provides access services for traveling employees or enterprise branches to remotely access intranet resources.
The L2TP network architecture includes an L2TP access concentrator (LAC) and an L2TP network server (LNS).
  An LAC provides PPP and L2TP processing capabilities. The LAC establishes an L2TP tunnel with the LNS. In different networking environments, the LAC can be a gateway or a terminal. The LAC can initiate requests of establishing multiple L2TP tunnels to isolate data flows.
  The LNS is the remote device of the LAC. That is, an L2TP tunnel is established between the LAC and the LNS. The LNS is located at the border between the private network and public network of the enterprise headquarters and is usually the gateway of the enterprise headquarters.

## Slide 50: SSL VPN
DMZ
Remote OA user
SSL VPN tunnel
Server
Intranet
Secure Shell (SSL) VPN is a VPN remote access technology based on the SSL protocol. This technology allows mobile users (referred to as remote users in SSL VPN) to securely and conveniently access enterprise intranets and intranet resources, improving work efficiency.
SSL VPN uses the browser/server (B/S) architecture. Remote users can directly use a web browser to access intranet resources securely and quickly, without the need to install extra client software. SSL VPN supports the following functions:
  Fine-grained permission control based on the type of accessed resources
  Flexible identity authentication
  Host check policies used to check whether the operating systems, ports, processes, and antivirus software of remote users' devices meet security requirements, and anti-nested remote desktop connections and anti-snapshot functions to eliminate security risks from remote user devices
External network

## Slide 51: VXLAN
External network
VXLAN tunnel
Campus network
Virtual Extensible LAN (VXLAN) is a VPN technology that can build a Layer 2 virtual network over a network with reachable routes.
VXLAN gateways can be used to implement communication within a VXLAN network and between a VXLAN network and a traditional non-VXLAN network.
VXLAN uses MAC-in-UDP encapsulation to extend Layer 2 networks and encapsulates Ethernet packets into IP packets.

## Slide 52
(Multiple-choice) After IPSG is enabled on a switch, which of the following methods can be used to generate binding entries? ( )
  Manually configured entries
  Dynamic entries delivered by the NMS
  Dynamic entries generated by DHCP snooping
  Dynamic entries discovered by LLDP
Notes: Answer: AC

## Slide 53
This course describes typical application scenarios of campus network technologies, including Ethernet switching basics, wireless access, network reliability, network service and management, network security, and VPN.
This document cannot list all technologies used on campus networks. After completing this course, you will be able to understand the typical architecture of campus networks and the application of typical technologies on campus networks. This will help lay a solid foundation for you learn the following courses.
In subsequent courses, we will discuss key technologies, which are essential to campus network solutions.