## Slide 1
New
Yao Ning/00276205
2020.06.22
CloudCampus
V100R019C10
Wan Yunfei/00364921
2019.11.25
Update
Shi Miaomiao/swx791350
Yao Ning/00276205
Update
Update
Update

## Slide 2: Campus Multi-Branch Interconnection Technology

## Slide 3
A campus network typically refers to the internal network of an enterprise or organization. It primarily aims to enable more efficient operations of enterprises' main businesses.
A Wide Area Network (WAN) is a long-distance communications network that connects multiple Local Area Networks (LANs) or Metropolitan Area Networks (MANs) across different geographic areas. A WAN is generally provided by a carrier and connects the egress of a campus to other campuses. A typical WAN covers distances of tens to tens of thousands of kilometers. It spans a large geographic area such as across cities, regions, or countries.
Enterprises use the WANs provided by carriers to interconnect their branches, headquarters, and data centers (DCs) across different geographic areas. Mission-critical applications, information, and data of traditional enterprises are typically stored inside the enterprise. As such, the WAN bandwidth requirements are small, and service changes are not frequent. This traditional enterprise WAN architecture has long been playing an important role in enterprise branch interconnections and meets the service requirements of enterprise users.
Enterprise WANs are developing and changing, driven by dynamic business environments and technologies. In recent years, new business trends and technologies that affect WANs have been constantly emerging.

## Slide 4
Upon completion of this course, you will be able to:
  Describe the development of enterprise WAN technologies.
  Describe typical campus network interconnection solutions.
  Describe the basic concepts, application scenarios, and working principles of IPsec VPN.
  Describe the basic concepts of Software-Defined WAN (SD-WAN).
  Describe the technical architecture of Huawei SD-WAN interconnection solution.
  Describe the implementation of Huawei SD-WAN interconnection solution.

## Slide 5
Overview of Campus Multi-Branch Interconnection Technology
Campus Multi-Branch Interconnection Technology: IPsec VPN
Campus Multi-Branch Interconnection Technology: SD-WAN

## Slide 6: Overview of Traditional Enterprise WANs
A WAN is a long-distance communications network that connects multiple LANs or MANs across different geographic areas. With WANs, enterprises can connect their branches across the globe.
Traditional enterprise WANs have two major interconnection modes:
Enterprises deploy or rent carriers' fiber lines to build an interconnection network.
Enterprises rent carriers' transmission or data networks to achieve interconnection.
Concept of enterprise WANs
Constantly evolving WAN private line technologies
DC
HQ
Branch
1990s
2000s
2010s
With the rapid development of the Internet, it is possible to achieve branch interconnection through the Internet.
Mission-critical applications, information, and data of traditional enterprises are typically stored inside the enterprise. As such, a small WAN bandwidth is required, service changes are not frequent, and WAN O&M is generally performed by local teams.
TDM
Cloud
IP/MPLS
SDH/PDH
MPLS VPN
/IPsec VPN/OTN, etc
SD-WAN
(Hybrid WAN, SDN controller)
Technological revolutions
Private line solution
Traditional carrier private line/MPLS
Notes: A WAN, generally provided by a carrier, is a long-distance communications network that connects multiple LANs or MANs across different geographic areas. A typical WAN covers distances of tens to tens of thousands of kilometers. It spans a large geographic area such as across cities, regions, or countries. Through WANs, enterprises can set up an interconnection network for their branches worldwide, facilitating their daily operations.
With the rapid development of the Internet, it is possible to achieve branch interconnection through the Internet. However, the Internet has certain weaknesses, such as low reliability and a lack of end-to-end quality assurance. That's why large enterprises generally do not simply rely on the Internet to construct WANs for multi-branch interconnections. The Internet is often used as a remote access mode for traveling employees or as a backup solution for branch interconnections. Only some non-mission-critical services are carried via the Internet.
Enterprises use the WANs provided by carriers to interconnect their branches, headquarters, and DCs across different geographic areas. Mission-critical applications, information, and data of traditional enterprises are typically stored inside the enterprise. As such, a small WAN bandwidth is required, service changes are not frequent, and WAN O&M is generally performed by local teams. This traditional enterprise WAN architecture has long been playing an important role in enterprise branch interconnections and meets the service requirements of enterprise users.

## Slide 7: Enterprise WAN Connection Mode
HQ
Branch 3
Branch 1
IPsec or GRE or L2TP VPN
Internet
MPLS
Branch 2
MPLS VPN
1
2
3
Physical private lines are used for interconnections, ensuring stable line quality and high bandwidth but at high cost.
1
MPLS VPN features stable quality, high price, and low bandwidth.
2
The VPN is established over the Internet. The cost is low and the bandwidth is high, but the stability is poor and depends on the Internet connection quality.
3

## Slide 8: Development of Enterprise WAN Technologies (1)
Migration of enterprise services to the cloud
Enterprise services are migrated to the cloud, and enterprise egress traffic increases sharply.
WAN traffic (%) on an enterprise network
Source: IDC
Intelligence
Cloud
Video
Mobility
2016
2020
20%
80%
HQ
Branch 1
Branch 2
MPLS VPN
GRE/IPsec VPN or MPLS VPN
DC1
DC2
DCI
With the cloud-based deployment of enterprise services, traffic between enterprise branches increases sharply. Traffic between the intranet of the campus network and DC is migrated to the enterprise WAN. Compared with the internet bandwidth (dozens of gigabit per second), the enterprise WAN egress bandwidth is low. In case of traffic surge, the cost of the enterprise WAN egress increases.
MPLS/
Internet
Notes: DCI is short for Data Center Interconnect.

## Slide 9: Development of Enterprise WAN Technologies (2)
The gap between the quality of the Internet and traditional private lines is rapidly narrowing.
The coverage and network performance of the Internet are continuously improving, and the gap between the quality of the Internet and traditional private lines is narrowing rapidly. As such, more and more enterprises are using the Internet for interconnection with external organizations.
Enterprises do not use only MPLS VPNs (private lines) for service communication because of higher requirements for WAN-side interconnection bandwidth, high costs of MPLS VPNs (or physical private lines), and improved Internet link quality.
Traditional carrier private lines/MPLS
Internet
High-speed development of the Internet

## Slide 10: Huawei Multi-Campus Interconnection Solution
Model 1: Static IPsec VPN
Model 2: SD-WAN interconnection
IPsec VPN tunnel
MPLS/Internet
An IPsec VPN is a type of static VPN, in which IPsec tunnels are established between devices at different sites to create VPN tunnels. Traffic is diverted to the VPN tunnels based on the configured static routes to implement inter-site communication.
Inter-site VPN setup and communication are orchestrated by the controller and traditionally require manual control.
BGP EVPN can be used to establish tunnels between sites and dynamically advertise routes on demand. The forwarding plane supports GRE or GRE over IPsec. High-quality links can be selected based on applications and policies for data transmission, implementing application- and policy-based intelligent traffic steering.
IPsec VPN tunnel
VPN tunnel
MPLS/Internet
VPN tunnel
BGP EVPN
HQ
Branch 1
Branch 2
HQ
Branch 1
Branch 2
HQ
(RR)
Branch 1
Branch 2
Management and control channel
Management and control channel
Notes: The multi-campus network interconnection solution is a sub-solution provided in the CloudCampus Solution for the interconnection between branch campuses and between branches and the headquarters or DCs. With SD-WAN functions integrated, the multi-campus network interconnection solution provides two models for WAN interconnection: static IPsec VPN and EVPN.
An IPsec VPN is a type of static VPN, in which IPsec tunnels are established between devices at different sites to create VPN tunnels. Traffic is diverted to the VPN tunnels based on the configured static routes so that services between sites can be accessed through the VPN tunnels.
BGP EVPN used by SD-WAN is a type of dynamic VPN that can establish tunnels between sites and dynamically advertise routes on demand. EVPN establishes GRE tunnels between sites to establish VPN tunnels and supports IPsec encryption on GRE tunnels to ensure tunnel encryption security. In addition, the BGP EVPN interconnection solution offers application- and policy-based intelligent traffic steering, allowing high-quality links to be chosen based on applications and policies for data transmission.

## Slide 11: Interconnection Solution 1: IPsec VPN Interconnection Solution
DC
HQ
MPLS
Internet
Branch site
Branch site
Branch site
On iMaster NCE-Campus, create sites, record device information, and configure service deployment information for the devices. The devices then register with iMaster NCE-Campus.
Define the subnet segments that can access VPN services.
On iMaster NCE-Campus, orchestrate the site VPNs and define the IPsec VPN interconnection model (hub-spoke or full-mesh).
When adding devices to site VPNs, specify their network segment. During IPsec link establishment, the network segment is sent to the peer end to generate static user network routes (UNRs). This ensures that traffic can be properly transmitted between sites.
In the hub-spoke model, configure a template IPsec policy for the hub sites to monitor the link establishment requests from the spoke. The spoke node proactively sends link establishment requests to the hub. In this way, IPsec VPN channels are established between the headquarters and branches.
iMaster NCE-Campus
UI
Southbound NE layer
Site configuration
Inter-site VPN
O&M
IPsec VPN
Management channel

## Slide 12: Interconnection Solution 2: EVPN Interconnection Solution
MPLS
DC
HQ
Internet
Branch site
Branch site
SD-WAN-powered EVPN interconnection solution:
  The WAN is abstracted and modeled to decouple upper-layer network services from lower-layer networks, implementing network automation.
  An independent BGP EVPN control plane is deployed to separate network forwarding and control planes, thereby implementing centralized network control.
  Centralized network monitoring and visualization enable centralized management of WANs in an E2E manner, implementing intelligent O&M.
This course focuses on the implementation of the control plane and data plane. In this solution, BGP EVPN on the control plane and GRE on the data plane are extended based on standard protocols.
GRE/IPsec VPN
iMaster NCE-Campus
UI
Southbound NE layer
Site configuration
Virtual network
O&M
Management channel
Control plane: BGP EVPN peer relationship
RR

## Slide 13
Overview of Campus Multi-Branch Interconnection Technology
Campus Multi-Branch Interconnection Technology: IPsec VPN
  Basic Concepts
  IPsec
  IKE
  Advanced IPsec Functions
  IPsec Configuration Examples
  Example for Configuring Campus IPsec VPN Interconnection
Campus Multi-Branch Interconnection Technology: SD-WAN

## Slide 14: VPN Background and Basic Concepts
Enterprise A has branches in different places, which need to communicate with the other branches and the headquarters securely and reliably. Private lines can meet such requirements but are costly. If data is directly transmitted over the Internet, there may be security risks.
HQ
Branch
Branch
Internet
An IP-based VPN is a dedicated network infrastructure simulated on a shared IP network infrastructure by using related technologies. VPN has two outstanding features: private and virtual.
Notes: A VPN is a secure private virtual network established on a shared network (or a public network), and therefore saves the cost of leasing private lines.

## Slide 15: Tunneling Technologies
A tunnel is similar to a bridge. Forwarding channels are established on the underlying network (for example, the Internet). Users can establish a tunnel network by themselves without the intervention of the underlying network provider (for example, a carrier).
There are many tunneling technologies, such as MPLS, GRE, L2TP, IPsec and VXLAN. Although there are various tunneling technologies, their fundamentals are the same.
100.1.1.1
200.2.2.2
Tunnel
PC1
PC2
Internet
SA: 1.1.1.1
DA: 2.2.2.2
Payload
SA: 1.1.1.1
DA: 2.2.2.2
Payload
SA: 100.1.1.1
DA: 200.2.2.2
SA: 1.1.1.1
DA: 2.2.2.2
Payload
SA: 100.1.1.1
DA: 200.2.2.2
SA: 1.1.1.1
DA: 2.2.2.2
Payload
Original packet
Original packet
Encapsulate the outer header
(tunnel header)
Decapsulate the outer header
SA: source address
DA: destination address
1.1.1.1
2.2.2.2

## Slide 16: Background of IPsec VPN
Enterprise branches can use many interconnection modes to interconnect with each other, for example, WAN private lines or the Internet.
Considering costs and requirements, some enterprises choose to use the Internet for interconnection. However, data may be intercepted or tampered with during transmission on the Internet, posing security risks.
IPsec encrypts data packets to ensure secure interconnection for enterprises.
Carrier network
Branch 2
Branch 3
HQ
Branch 1
Enterprise WAN interconnection
WAN
IPsec tunnel
IPsec tunnel
IPsec tunnel
Notes: IPsec VPN secures data transmission in VPN tunnels through IPsec.

## Slide 17: IPsec VPN Fundamentals
100.1.1.1
200.2.2.2
IPsec tunnel
Branch 1
PC1 1.1.1.1
Branch 2
PC2 2.2.2.2
Security protocol
Tunnel
Security protocol
Payload
Payload
SA: 1.1.1.1
DA: 2.2.2.2
Encrypted data
SA: 100.1.1.1
DA: 200.2.2.2
Payload
Security protocol header
Encrypted data
SA: 100.1.1.1
DA: 200.2.2.2
Security protocol header
SA: 1.1.1.1
DA: 2.2.2.2
Payload
Internet

## Slide 18
Overview of Campus Multi-Branch Interconnection
Campus Multi-Branch Interconnection Technology: IPsec VPN
  Basic Concepts
  IPsec
  IKE
  Advanced IPsec Functions
  IPsec Configuration Examples
  Example for Configuring Campus IPsec VPN Interconnection
Campus Multi-Branch Interconnection Technology: SD-WAN

## Slide 19: IPsec Overview
Internet Protocol Security (IPsec) is an open network-layer framework protocol designed by the Internet Engineering Task Force (IETF). It is a collection of protocols and services that provide security for IP networks.
Taking advantages of encryption and authentication, IPsec secures service data transmission over the Internet through the following capabilities:
  Data origin authentication: The receiver verifies whether the sender's identity is authorized.
  Data encryption: The sender encrypts data packets and transmits them in cipher text on an open network. The receiver decrypts or directly forwards the received data packets.
  Data integrity check: The receiver verifies received data to determine whether the data has been tampered with.
  Anti-replay: The receiver rejects old or duplicate data packets to prevent attacks that malicious users initiate by re-sending obtained packets.
IPsec Overview
Encapsulation Mode
Security Protocol
IPsec Framework
Encryption and Authentication
Security Association

## Slide 20: IPsec Framework
IPsec framework uses a set of open standards.
Security Protocol
Encryption
Authentication
Key exchange
ESP
DES
3DES
AES
SM1/SM4
AH
Not supported
MD5
SHA1
SHA2
SM3
MD5
SHA1
SHA2
SM3
IKE (ISAKMP, DH)
IPsec framework
IPsec Overview
Encapsulation Mode
Security Protocol
IPsec
Framework
Encryption and Authentication
Security Association
Notes: IPsec implements secure transmission of IP packets using two security protocols: Authentication Header (AH) and Encapsulating Security Payload (ESP).
  AH provides data origin authentication, data integrity check, and anti-replay, but does not provide encryption.
  ESP provides encryption, data origin authentication, data integrity check, and anti-replay.
Security functions provided by AH and ESP depend on authentication and encryption algorithms used by IPsec.
  Both AH and ESP can provide data origin authentication and data integrity check using the following authentication algorithms: Message Digest 5 (MD5), Secure Hash Algorithm 1 (SHA1), SHA2-256, SHA2-384, SHA2-512, and Senior Middle 3 (SM3).
  ESP can only encrypt IP packets using symmetric encryption algorithms, including Data Encryption Standard (DES), Triple Data Encryption Standard (3DES), Advanced Encryption Standard (AES), SM1, and SM4.
The keys used for IPsec encryption and authentication can be manually configured or dynamically negotiated using the Internet Key Exchange (IKE) protocol. IKE works in the Internet Security Association and Key Management Protocol (ISAKMP) framework. It uses the Diffie-Hellman (DH) algorithm to securely deliver keys and authenticate identities over an insecure network, ensuring data transmission security. IKE improves key security and simplifies IPsec management.

## Slide 21: IPsec Encapsulation Mode - Tunnel Mode
IPsec encapsulation is a process of adding AH or ESP fields to original IP packets for packet authentication and encryption. This process is implemented in transport or tunnel mode.
IP Header
SA: 1.1.1.1
DA: 2.2.2.2
Payload
IP Header
SA: 1.1.1.1
DA: 2.2.2.2
Payload
IPsec Header
ESP/AH
IP Header
SA: 200.1.1.1
DA: 200.2.2.2
IP Header
SA: 1.1.1.1
DA: 2.2.2.2
Payload
Original packet
Original packet
Original packet
New header
100.1.1.1
200.2.2.2
IPsec tunnel
Branch 1
PC1
Branch 2
PC2
Internet
In tunnel mode, an AH or ESP header is added in front of the raw IP header, and a new IP header added in front of the AH or ESP header to protect the IP header and payload. The tunnel mode applies to communication between two VPN gateways or between a host and a VPN gateway.
1.1.1.1
2.2.2.2
IPsec Overview
Encapsulation
Mode
Security Protocol
IPsec Framework
Encryption and Authentication
Security Association
Notes: In tunnel mode, AH checks the integrity of the entire IP packet including the new IP header. ESP checks the integrity of the ESP header, raw IP header, transport-layer protocol header, data, and ESP trailer, excluding the new IP header. ESP cannot protect the new IP header. ESP encrypts the raw IP header, transport-layer protocol header, data, and ESP trailer.
Note: In this example, the ESP trailer and authentication data are not shown in the figure.

## Slide 22: IPsec Encapsulation Mode - Transport Mode
IPsec encapsulation is a process of adding AH or ESP fields to original IP packets for packet authentication and encryption. This process is implemented in transport or tunnel mode.
IP Header
SA: 1.1.1.1
DA: 2.2.2.2
Payload
Payload
IPsec Header
ESP/AH
IP Header
SA: 1.1.1.1
DA: 2.2.2.2
Payload
Original packet
Original packet
New header
Branch 1
PC1
Branch 2
PC2
Internet
In transport mode, an AH or ESP header is added between an IP header and a transport-layer protocol (TCP/UDP/ICMP) header to protect the TCP, UDP, or ICMP payload. The transport mode does not change the IP header, so the source and destination addresses of an IPsec tunnel must be the same as those in the IP header. This encapsulation mode applies only to communication between two hosts or between a host and a VPN gateway.
IPsec tunnel
IP Header
SA: 1.1.1.1
DA: 2.2.2.2
1.1.1.1
2.2.2.2
IPsec Overview
Encapsulation
Mode
Security Protocol
IPsec Framework
Encryption and Authentication
Security Association
Notes: In transport mode, AH checks the integrity of the entire IP packet. ESP checks the integrity of the ESP header, transport-layer protocol header, data, and ESP trailer, excluding the IP header. ESP cannot protect the IP header. ESP encrypts the transport-layer protocol header, data, and ESP trailer.
Note: In this example, the ESP trailer and authentication data are not shown in the figure.

## Slide 23: IPsec Security Protocols
IPsec uses AH and ESP to transmit and encapsulate data. The security protocols provide security services such as authentication and encryption.
  AH provides functions such as data origin authentication, data integrity check, and anti-replay.
  Data encryption is not supported.
ESP
  ESP provides functions such as data origin authentication, data integrity check, anti-replay, and data encryption.
AH
Security functions provided by AH and ESP depend on authentication and encryption algorithms used by IPsec.
  Both AH and ESP can provide data origin authentication and data integrity check using the following authentication algorithms: Message Digest 5 (MD5), Secure Hash Algorithm 1 (SHA1), SHA2-256, SHA2-384, SHA2-512, and Senior Middle 3 (SM3).
  ESP can only encrypt IP packets using symmetric encryption algorithms, including Data Encryption Standard (DES), Triple Data Encryption Standard (3DES), Advanced Encryption Standard (AES), SM1, and SM4.
IPsec Overview
Encapsulation
Mode
Security
Protocol
IPsec Framework
Encryption and Authentication
Security Association

## Slide 24: Security Protocol Structure (1)
AH header format
32 bits
AH is an IP-based protocol with protocol number 51.
According to the AH protocol, an AH header is appended to the standard IP header in each packet.
The sender performs hash calculation on packets and an authentication key. After packets carrying the calculation result arrive at the receiver, the receiver also performs hash calculation and compares the calculation result with the received calculation result. Any changes to the data during transmission will make the calculation result invalid.
AH performs an integrity check for an entire IP packet.
IPsec Overview
Encapsulation
Mode
Security
Protocol
IPsec Framework
Encryption and Authentication
Security Association
Notes: AH header fields:
  Next Header: 8 bits. This field identifies the type of the payload following the AH header. In transport mode, the Next Header field value is the number of the protected upper-layer protocol (TCP or UDP) or ESP. In tunnel mode, the Next Header field value is the number of the IP or ESP protocol.
  Payload Len: 8 bits. The value of this field is the AH header length in 32-bit words minus 2. The default value is 4.
  Reserved: 16 bits. This field is reserved and defaults to 0.
  SPI: 32 bits. This field uniquely identifies an IPsec security association (SA).
  Sequence Number: 32 bits. This field is a counter that monotonically increases from 1. It uniquely identifies a packet to prevent replay attacks.
  Authentication Data: a variable-length field. The field length is an integral multiple of 32 bits, usually 96 bits. This field contains the ICV and is used by the receiver for data integrity check. AH supports the following authentication algorithms: Message Digest 5 (MD5), Secure Hash Algorithm 1 (SHA-1), SHA-2, and SM3. MD5, SHA-1, and SHA-2 are listed in ascending order of security. A more secure encryption algorithm has a slower computing speed because its implementation is more complex. The SM3 cryptographic hash algorithm is an IPsec protocol standard published by the China State Cryptography Administration.

## Slide 25: Security Protocol Structure (2)
ESP header format
32 bits
ESP
Header
ESP
Trailer
Encrypted
ESP
Authentication
Authentication
ESP is an IP-based protocol with protocol number 50.
According to the ESP protocol, an ESP header is appended to the standard IP header in each packet, and an ESP trailer and ESP authentication data are appended to each packet.
Unlike AH, ESP encrypts the valid payload and then encapsulates it into a packet to ensure data confidentiality. However, ESP does not protect an IP header.
IPsec Overview
Encapsulation
Mode
Security
Protocol
IPsec Framework
Encryption and Authentication
Security Association
Notes: ESP header fields
  SPI: 32 bits. This field uniquely identifies an IPsec SA.
  Sequence Number: 32 bits. This field is a counter that monotonically increases from 1. It uniquely identifies a packet to prevent replay attacks.
  Payload Data: This field contains variable-length data identified by the Next Header field.
  Padding: This field extends the size of an ESP header. The Padding field length depends on the payload data length and algorithm. If the plaintext length of the packet to be encrypted does not comply with the encryption algorithm, the Padding field is used.
  Pad Len: 8 bits. This field specifies the length of the Padding field. The value 0 indicates no padding.
  Next Header: 8 bits. This field identifies the type of the payload following the ESP header. In transport mode, the Next Header field value is the number of the protected upper-layer protocol (TCP or UDP). In tunnel mode, the Next Header field is the IP protocol number.
  Authentication Data: a variable-length field. The length is an integral multiple of 32 bits, usually 96 bits. This field contains the ICV and is used by the receiver for data integrity check. Authentication algorithms are the same as those of AH. The authentication function of ESP is optional. If data check is enabled, an ICV value is appended to encrypted data.

## Slide 26: Combination of Security Protocols and Encapsulation Modes
Tunnel Mode
Transport Mode
IP Header | AH Header | Data
IP Header | ESP Header | Data | ESP Trailer | ESP Auth data
IP Header | AH Header | ESP Header | Data | ESP Trailer | ESP Auth data
New IP Header | AH Header | Raw IP Header | Data
New IP Header | ESP Header | Raw IP Header | Data | ESP Trailer | ESP Auth data
New IP Header | AH Header | ESP Header | Raw IP Header | Data | ESP Trailer | ESP Auth data
ESP
AH-ESP
Authenticated
Authenticated
Encrypted
ESP authenticated
Encrypted
AH authenticated
Authenticated
Authenticated
Encrypted
ESP authenticated
Encrypted
AH authenticated
AH-ESP
ESP
AH
AH
IPsec Overview
Encapsulation
Mode
Security
Protocol
IPsec Framework
Encryption and Authentication
Security Association
Notes: In transport mode, an AH or ESP header is added between an IP header and a transport-layer protocol (TCP/UDP/ICMP) header to protect the TCP, UDP, or ICMP payload. Because no additional IP header is added, IP addresses in the original packets are visible in the IP header of the post-encrypted packet.
In tunnel mode, an AH or ESP header is added in front of the raw IP header and a new IP header added in front of the AH or ESP header to protect the IP header and payload.

## Slide 27: Comparison Between AH and ESP
Security feature | AH | ESP
Protocol number | 51 | 50
Data integrity check | Supported (checking the entire IP packet) | Supported (not checking the IP header)
Data origin authentication | Supported | Supported
Data encryption | Not supported | Supported
Anti-replay | Supported | Supported
IPsec NAT traversal (NAT-T) | Not supported | Supported
IPsec Overview
Encapsulation
Mode
Security
Protocol
IPsec Framework
Encryption and Authentication
Security Association

## Slide 28: Encryption Algorithms
Encryption is a process of converting plaintext data into ciphertext data using an algorithm. The receiver can decrypt ciphertext data only when it has a correct key. The encryption mechanism ensures data confidentiality and prevents data from being eavesdropped during transmission.
IPsec uses symmetric encryption algorithms to encrypt and decrypt data. Symmetric encryption algorithms require that the sender and receiver use the same key (a symmetric key) to encrypt and decrypt data.
The symmetric key can be manually configured or automatically negotiated through IKE.
Common symmetric encryption algorithms include: Triple Data Encryption Standard (3DES) and Advanced Encryption Standard (AES).
IPsec sender
IPsec receiver
Encryption
algorithm
Encrypted IP packet
Encryption
algorithm
IP packet
Encrypted IP packet
Encryption
Decryption
IP packet
Symmetric key
Manually configured or automatically negotiated through IKE
IPsec Overview
Encapsulation
Mode
Security
Protocol
IPsec Framework
Encryption and
Authentication
Security Association

## Slide 29: Authentication Algorithms (1)
A one-way function is a function that is easy to compute on every input, but hard to invert given the image of a random input.
A hash function uses a variable-length message as its input, compresses it, and generates a fixed-length digest.
A function that has the characters of both a one-way function and a hash function is called a one-way hash function. That is, one-way hash functions produce completely different fixed-length outputs from a variable-length input, and (basically) reverse calculation cannot be performed on the outputs.
Currently, widely used one-way hash functions include: MD5 and SHA.
Digest A
0000 1111 0000
One-way hash
Digest B
0000 1111 1000
One-way hash
The output varies according to the input.
If the same one-way hash function is used for calculation, the lengths of digests A and B are the same.
IPsec Overview
Encapsulation
Mode
Security
Protocol
IPsec Framework
Encryption and
Authentication
Security Association

## Slide 30: Authentication Algorithms (2)
One-way hash functions cannot ensure that data is not modified during transmission. When modifying original data, anyone can run a hash function on the modified data.
One-way hash functions are typically used to verify data integrity, for example, to ensure that a downloaded file is not damaged during transmission (by comparing digest information).
Digest A
0000 1111 0000
One-way hash
Digest B
0000 1111 1000
Sender
The receiver receives the modified original data and digest.
The man-in-the-middle intercepts and modifies the data.
Digest B
0000 1111 1000
One-way hash
IPsec Overview
Encapsulation
Mode
Security
Protocol
IPsec Framework
Encryption and
Authentication
Security Association

## Slide 31: Authentication Algorithms (3)
To check whether data is modified during transmission, hash-based message authentication code (HMAC) technology is typically used.
The technology divides a data stream into data blocks that are easy to digest, and then calculates a MAC based on each data block and the key agreed by both parties. Then these MACs become a part of the data stream so that the integrity of the data stream can be checked after the data stream is completely received.
0000 1111 0001
0000
1111
0001
Key
Digest 1
0000
One-way hash
1111
Digest 2
0000
Digest 3
Sender
Key
Digest 1
0000
One-way hash
1111
Digest 2
0000
Digest 3
Receiver
Digest 1
Digest 2
Digest 3
Digest 1
Digest 2
Digest 3
Comparison
IPsec Overview
Encapsulation
Mode
Security
Protocol
IPsec Framework
Encryption and
Authentication
Security Association
Notes: In the HMAC technology, the sender and receiver use the same key to prevent man-in-the-middle from modifying data and digests.

## Slide 32: Authentication Algorithms (4)
Authentication is an operation that a receiver performs to verify the identity of the sender (source origin authentication) and whether data has been tampered with during transmission (data integrity check).
IPsec uses the HMAC function to compare digital signatures to check integrity and authenticity of data packets.
Encryption and authentication are often used together.
Like an encryption key, a symmetric authentication key can be manually configured or automatically negotiated through IKE.
Common authentication algorithms include MD5, SHA1, and SHA2.
IPsec sender
IPsec receiver
Encrypted IP packet
IP packet
Encrypted IP packet
Encryption
Decryption
IP packet
Encryption
Encrypted IP packet
Digest
Encrypted IP packet
Digest
Digest
Symmetric key
Manually configured or automatically negotiated through IKE
Symmetric key
Manually configured or automatically negotiated through IKE
Encryption
Digest
Comparison
Whether the digests are the same
Yes
No
Discard
Encryption
algorithm
Encryption
algorithm
Authentication algorithm
HMAC
Authentication algorithm
HMAC
IPsec Overview
Encapsulation
Mode
Security
Protocol
IPsec Framework
Encryption and
Authentication
Security Association
Notes: Although encrypted data can only be decrypted using the original encryption key, the decrypted data cannot be proved to be the original data. Additionally, data encryption and decryption consume many CPU resources, and malicious users may send spoofing packets to consume CPU resources. HMAC compares digests to check data integrity and authenticity. This process consumes only a few CPU resources and is very efficient. Therefore, IPsec uses HMAC for authentication.
Encryption and authentication are often used together on the IPsec sender. The sender encrypts IP packets, generates a digest during HMAC calculation, and then sends both the encrypted IP packets and digest to the receiver. The receiver compares the received digest with the locally generated one to check data integrity and authenticity in the received IP packets. The receiver discards the packets that fail the authentication and decrypts those that pass the authentication.

## Slide 33: Security Association
An IPsec security association (SA) is an agreement between two peers on certain elements. For example, DES is used as the encryption algorithm, MD5 is used as the authentication algorithm, and the tunnel mode is used as the encapsulation mode.
IPsec SAs can be established manually or through IKE and are applicable to small-sized networks and large-/medium-sized networks, respectively.
Automatically establishing IPsec SAs through IKE
IKE module
IKE module
IKE SA negotiation
Authentication and encryption policy 1
Key 1
...
IPsec SA negotiation
Manually establishing IPsec SAs
Manually configured
Authentication policy 1
Encryption policy 1
Key 1
...
Authentication policy 1
Encryption policy 1
Key 1
...
IPsec SA
IPsec SA
IPsec SA
IPsec SA
Authentication policy 1
Encryption policy 1
Key 1
...
Authentication policy 1
Encryption policy 1
Key 1
...
IPsec Overview
Encapsulation
Mode
Security
Protocol
IPsec Framework
Encryption and
Authentication
Security
Association
Notes: Because SAs are unidirectional, at least two SAs are required to protect incoming and outgoing data flows between two IPsec peers (two parties that use IPsec for secure encrypted communication).
An IPsec SA is established either manually or through IKE negotiation. The two methods differ in the following:
  Key generation: In manual mode, all the parameters used to establish an SA, including the encryption key and authentication key, need to be manually configured and updated, leading to high key management costs on large- and medium-sized networks. In IKE negotiation mode, the encryption key and authentication key are generated using the DH algorithm and can be dynamically updated, reducing key management costs and improving security.
  SA lifetime: In manual mode, an SA exists permanently. In IKE negotiation mode, how long an SA can exist depends on the lifetime parameters configured on two peers.
Based on the differences, the manual mode applies to small networks with a small number of IPsec peers, whereas the IKE negotiation mode is recommended on large and medium-sized networks.

## Slide 34
Overview of Campus Multi-Branch Interconnection
Campus Multi-Branch Interconnection Technology: IPsec VPN
  Basic Concepts
  IPsec
  IKE
  Advanced IPsec Functions
  IPsec Configuration Examples
  Example for Configuring Campus IPsec VPN Interconnection
Campus Multi-Branch Interconnection Technology: SD-WAN

## Slide 35: IKE Overview
IKE is a UDP-based application-layer protocol built on the Internet Security Association and Key Management Protocol (ISAKMP) framework.
It implements automatic key negotiation and IPsec SA establishment, to simplify IPsec use and management, and facilitate IPsec configuration and maintenance.
IKE provides the following functions:
  Simplifies IPsec configuration.
  Periodically updates SAs.
  Periodically updates keys.
  Performs dynamic authentication between IPsec peers.
IKE Overview
IKEv2
Defining IPsec-Protected Data Flows
IKEv1

## Slide 36: Relationship Between IKE and IPsec
IKE is an application-layer protocol based on UDP and is the signaling protocol of IPsec.
An IKE SA is established to transmit the parameters and key (generated by IKE algorithms) required to establish an IPsec SA.
IPsec uses the IPsec SA established by IKE to encrypt or authenticate IP packets.
IPsec peer 1
IPsec tunnel
IPsec peer 2
IKE module
UE data
UE data
Encryption and authentication module
IKE SA negotiation
Exchange user data
IKE module
Encryption and authentication module
Encrypts, decrypts, and authenticates user data based on IPsec SA
IKE SA
IPsec SA
IPsec
SA negotiation
Encrypts IPsec SA negotiation packets based on the IKE SA
IKE negotiation phase 1
IKE negotiation phase 2
IPsec SA
IKE tunnel
IKE Overview
IKEv2
Defining IPsec-Protected Data Flows
IKEv1
Notes: The figure shows the relationship between IKE and IPsec. Two peers establish an IKE SA for identity authentication and key exchange. Protected by the IKE SA, the peers negotiate a pair of IPsec SAs using the AH or ESP protocol and other configured parameters. Subsequently, data is encrypted and transmitted between the peers over an IPsec tunnel.

## Slide 37: IKE Authentication Methods
IKE provides the following methods to authenticate the identity (IP address or name) of a remote peer:
  Pre-shared key (PSK) authentication
  Rivest-Shamir-Adleman (RSA) signature authentication
  Digital envelope authentication
IKE Overview
IKEv2
Defining IPsec-Protected Data Flows
IKEv1
Notes: Two peers authenticate the identity (IP address or name) of each other, using PSK authentication, RSA signature authentication, or digital envelope authentication.
  PSK authentication: An authentication key is used to generate a key. The two peers compute the hash value of packets using a shared key and check whether they obtain the same hash value. If they obtain the same hash value, the authentication succeeds. Otherwise, the authentication fails.
  RSA signature authentication: The two peers use a certificate issued by a certificate authority (CA) to verify validity of a digital certificate. Each peer has a public key (transmitted over the network) and a private key (possessed by itself). The sender computes a hash value for original packets, and then encrypts the hash value using its private key to generate a digest. The receiver decrypts the digest using the public key received from the sender, and then computes a hash value. If the computed hash value is the same as that decrypted from the digest, the authentication succeeds. Otherwise, the authentication fails.
  Digital envelope authentication: The sender generates a random symmetric key and uses the public key of the receiver to encrypt this symmetric key, which is called a digital envelop. The sender then uses the symmetric key to encrypt packets and uses its private key to generate a digest. The receiver uses its private key to decrypt the digital envelop to obtain the symmetric key, uses the symmetric key to decrypt packets, and decrypts the digest based on the sender's public key to verify the sender's digest. If the digest is correct, authentication succeeds. Otherwise, the authentication fails.

## Slide 38: IKE Negotiation
IKE has two versions: IKEv1 and IKEv2.
IKEv1 goes through two phases to negotiate the key and establish IPsec SAs.
IKEv2 generates the key and establishes IPsec SAs in one negotiation.
Comparison
  IKEv2 simplifies SA negotiation and improves negotiation efficiency.
  IKEv2 fixes many cryptographic vulnerabilities and enhances security.
IKE Overview
IKEv2
Defining IPsec-Protected Data Flows
IKEv1

## Slide 39: IKEv1
IKEv1 goes through two phases to establish SAs.
  In phase 1, two peers negotiate and establish a secure tunnel, which is an IKE SA.
  In phase 2, the peers establish a pair of IPsec SAs for secure data transmission through the secure tunnel established in phase 1.
IKE module
IKE SA negotiation
IKE module
IKE SA
IPsec
SA negotiation
Encrypts IPsec SA negotiation packets based on the IKE SA
IKE negotiation phase 1
IKE negotiation phase 2
IKEv1 negotiation process
IKE tunnel
IKE Overview
IKEv2
Defining IPsec-Protected Data Flows
IKEv1

## Slide 40: IKEv1 Negotiation Phase 1
In IKEv1 negotiation phase 1, an IKE SA is established. After an IKE SA is established, all the IKE packets transmitted between the two IPsec peers will be encrypted and authenticated. The secure tunnel established in phase 1 enables IPsec peers to communicate securely in phase 2.
IKEv1 negotiation phase 1 supports two negotiation modes: main mode and aggressive mode.
Main Mode
Aggressive Mode
Sends an IKE proposal.
Searches for a matching proposal.
Accepts the proposal.
Sends the confirmed IKE proposal.
Sends key generation information.
Generates a key.
Generates a key.
Sends key generation information.
Sends identity and authentication data.
Authenticates identity and key exchange.
Authenticates identity and key exchange.
Sends identity and authentication data.
Negotiation initiator
Negotiation responder
1
2
4
6
3
5
Initiates an IKE proposal and generates key and identity information.
Searches for the matching proposal algorithm, generates a key, and authenticates the identity.
Accepts the proposal and generates a key.
Sends key generation information, identity information, and authentication data.
Sends authentication data.
Verifies key exchange.
Negotiation initiator
Negotiation responder
1
2
3
Encrypted data
IKE Overview
IKEv2
Defining IPsec-Protected Data Flows
IKEv1
Notes: The main mode involves six ISAKMP messages in three exchanges. The three exchanges are described as follows:
  Messages 1 and 2 are used for IKE proposal exchange.
    The initiator sends one or more IKE proposals to the responder. The responder searches for the first matching IKE proposal and then sends the matching proposal to the initiator. IKE proposals of the initiator and responder match if they have the same encryption algorithm, authentication algorithm, authentication method, and Diffie-Hellman group identifier.
  Messages 3 and 4 are used for key information exchange.
    The initiator and responder exchange the Diffie-Hellman public value and nonce value to generate the IKE SA authentication and encryption key.
  Messages 5 and 6 are used for identity and authentication information exchange. (Both parties use the generated key to exchange information.)
    The initiator and responder use the generated key to authenticate each other and the information exchanged in main mode.
The aggressive mode uses only three messages. Messages 1 and 2 are used to negotiate an IKE proposal and exchange the Diffie-Hellman public value, mandatory auxiliary information, and identity information. Message 2 also contains the identity information sent by the responder to the initiator for authentication. Message 3 is used by the responder to authenticate the initiator.

## Slide 41
Notes: Compared with the main mode, the aggressive mode reduces the number of exchanged messages and speeds up the negotiation. However, the aggressive mode does not encrypt identity information. Although the aggressive mode does not provide identity protection, it applies to the following scenarios:
  When a Network Address Translation (NAT) device exists on an IPsec tunnel, NAT traversal needs to be enabled. However, NAT will change the IP address of a peer. The aggressive mode does not depend on an IP address for identity authentication. Therefore, NAT traversal can be implemented only in aggressive mode when the pre-shared key is used for authentication.
  If the IP address of the initiator is variable or unknown, and both the initiator and responder need to use a pre-shared key to establish an IKE SA, only the aggressive mode can be used.
  If the initiator already knows the IPsec policy used by the responder, it is faster to establish an IKE SA in aggressive mode.

## Slide 42: IKEv1 Negotiation Phase 2
In IKEv2 negotiation phase 2, IPsec SAs are established to securely transmit data and generate the key for data transmission.
This phase uses the quick mode. This mode uses the keys generated in phase 1 to verify the integrity of ISAKMP messages and identities of the initiator and responder, and to encrypt ISAKMP messages, ensuring exchange security.
Quick Mode
Sends an IPsec proposal, identity, and authentication data.
Searches for the matching proposal and generates a key.
Accepts the proposal and generates a key.
Sends the confirmed proposal, identity, and authentication data.
Sends authentication data.
Receives information.
Negotiation initiator
Negotiation responder
1
2
3
Encrypted data
IKE Overview
IKEv2
Defining IPsec-Protected Data Flows
IKEv1
Notes: In IKEv1 phase 2, two IPsec SAs are established through three ISAKMP messages:
  The initiator sends local security parameters and identity authentication information to the responder.
    Security parameters include protected data flows and parameters to be negotiated such as IPsec proposal. Identity authentication information includes the key generated in phase 1 and key materials generated in phase 2, and can be used to authenticate the peer again.
  The responder sends confirmed security parameters and identity authentication information, and generates a new key.
    The encryption key and authentication key used for IPsec SA data transmission are generated based on the key generated in phase 1 and parameters such as SPI and protocols, to ensure that each IPsec SA has a unique key.
    If Perfect Forward Secrecy (PFS) needs to be enabled, the shared key calculated through the DH algorithm needs to be used again to generate the encryption key and authentication key. During parameter negotiation, a DH key group needs to be negotiated for PFS.
  The initiator sends confirmed information to communicate with the responder. IKEv1 negotiation then ends.

## Slide 43: IKEv2
The process of establishing an SA through IKEv2 negotiation is much simpler than that through IKEv1 negotiation.
In normal cases, IKEv2 can establish a pair of IPsec SAs through only four messages in two exchanges. One additional Create_Child_SA Exchange can be used to establish another pair of IPsec SAs if required, during which only two messages are exchanged.
IKEv2 defines three exchanges: Initial Exchanges, Create_Child_SA Exchange, and Informational Exchange.
IKE Overview
IKEv2
Defining IPsec-Protected Data Flows
IKEv1
Notes: IKEv2 retains most IKEv1 features, and provides extended features such as NAT traversal.
IKEv2 uses a request/response mechanism. The responder must acknowledge messages sent from the initiator. If the initiator does not receive a response within the specified time, it retransmits the request. This request/response process improves security.
IKEv2 defines three exchanges:
  Initial Exchanges
  Create_Child_SA Exchange
  Informational Exchange
    Informational Exchange must be performed under the protection of an IKE SA. Specifically, Informational Exchange is performed after Initial Exchanges are complete. Control information may belong to an IKE SA or a child SA. Therefore, Informational Exchange must be protected by the IKE SA or the IKE SA based on which child IPsec SAs are established accordingly.

## Slide 44: IKEv2 Initial Exchanges
IKEv2 establishes the first pair of IPsec SAs through Initial Exchanges. Initial Exchanges involves four messages in two exchanges.
Initial Exchanges process
Negotiation initiator
Negotiation responder
Encrypted data
Sends IKE SA parameters.
Searches for the matching IKE SA parameters.
Accepts the parameters.
Sends the matching IKE SA parameters.
Sends identity information.
Authenticates identity and key exchange.
Authenticates identity and key exchange.
Sends identity information.
2
4
1
3
IKE Overview
IKEv2
Defining IPsec-Protected Data Flows
IKEv1
Notes: Messages 1 and 2 are used in exchange 1 (called IKE_SA_INIT) to negotiate IKE SA parameters in plain text, including the encryption key and authentication key, random number, and DH key. After IKE_SA_INIT is complete, shared keying material is generated, from which all keys used by IPsec SAs are derived.
Messages 3 and 4 are used in exchange 2 (called IKE_AUTH) to authenticate identities of the two parties and the first two messages, and to negotiate IPsec SA parameters. The two messages are encrypted. IKEv2 supports RSA signature authentication, PSK authentication, and Extensible Authentication Protocol (EAP) authentication. The initiator omits the AUTH payload in message 3 to indicate that EAP authentication is required.

## Slide 45: IKEv2 Create_Child_SA Exchange
After one pair of IPsec SAs is established based on an IKE SA, Create_Child_SA Exchange can be performed to negotiate more pairs of IPsec SAs. In addition, Create_Child_SA Exchange can be performed for IKE SA re-negotiation.
Create_Child_SA Exchange involves two messages in one exchange and maps phase 2 in IKEv1 negotiation. The initiator can be the initiator or responder in Initial Exchanges.
Create_Child_SA Exchange process
Negotiation initiator
Negotiation responder
Encrypted data
Sends identity information.
Authenticates identity and key exchange.
Authenticates identity and key exchange.
Sends identity information.
2
1
IKE Overview
IKEv2
Defining IPsec-Protected Data Flows
IKEv1

## Slide 46: IKEv2 Informational Exchange
IKEv2 peers perform Informational Exchange to exchange control information, including error information and notifications.
Informational Exchange must be performed under the protection of an IKE SA. Specifically, Informational Exchange is performed after Initial Exchanges are complete. Control information may belong to an IKE SA or a child SA. Therefore, Informational Exchange must be protected by the IKE SA or the IKE SA based on which child IPsec SAs are established accordingly.
Informational Exchange process
Negotiation initiator
Negotiation responder
Encrypted data
Sends control information.
Performs operations according to the control information.
Receives information.
Responds to the control information.
2
1
IKE Overview
IKEv2
Defining IPsec-Protected Data Flows
IKEv1

## Slide 47: Defining IPsec-Protected Data Flows
You can define the data flows to be protected by IPsec using either of the following methods:
  Use an ACL.
    An ACL defines data flows to be protected by an IPsec tunnel. The packets matching permit clauses in the ACL are protected.
  Configure a route.
    A route can be configured to define data flows to be protected by an IPsec tunnel established through IPsec virtual tunnel interfaces. Then all packets routed to these interfaces are protected.
    On live networks, GRE over IPsec defines protected flows based on routes.
IKE Overview
IKEv2
Defining IPsec-
Protected Data Flows
IKEv1
Notes: This method of configuring a route has the following advantages:
  Simplifies the IPsec configuration: IPsec-protected data flows are routed to virtual tunnel interfaces, without the need to use an ACL to define characteristics of traffic to be encrypted or decrypted.
  Supports dynamic routing protocols.
  Protects multicast traffic through GRE over IPsec.

## Slide 48
Overview of Campus Multi-Branch Interconnection
Campus Multi-Branch Interconnection Technology: IPsec VPN
  Basic Concepts
  IPsec
  IKE
  Advanced IPsec Functions
  IPsec Configuration Examples
  Example for Configuring Campus IPsec VPN Interconnection
Campus Multi-Branch Interconnection Technology: SD-WAN

## Slide 49: IPsec Policy Template
The traditional IPsec VPN configuration requires a specific peer IP address. However, in many scenarios, one end (usually a small branch or store) that needs to establish an IPsec VPN does not have a public or fixed IP address.
When there are a large number of branches, the headquarters needs to maintain configurations for each branch, leading to high configuration workload.
The biggest improvement offered by a template IPsec policy is that the peer IP address does not need to be fixed. You can specify a single peer IP address, a peer IP address range (IP address segment), or no peer IP address (that is, any peer IP address).
HQ
Branch n
Branch 1
IPsec Tunnel 1
IPsec Tunnel n
Only one IKE peer and one IPsec policy need to be configured.

## Slide 50: NAT Traversal - Background
By default, the ESP header or AH header follows the outer IP header during IPsec data transmission. No matter which encapsulation mode is used, problems such as communication failures may occur when a NAT device is deployed on the transmission path.
Internet
IPsec tunnel
Gateway 1
NAT device
Gateway 2
IP: X
IP: Z
IP: Y
IP Header SA: X DA: Z | AH Header | Raw IP Header | Data
Authenticated
IP Header SA: Y DA: Z | AH Header | Raw IP Header | Data
Authenticated
SNAT (NAPT)
After gateway 2 receives an IPsec packet from gateway 1, it checks the Authentication Data field in the AH header of the packet. Because the IP address in the outer IP header of the packet has changed, the check fails, so gateway 2 discards the packet. As a result, the communication fails.
SNAT (NAPT)
ESP does not check the outer IP header. Therefore, SNAT does not affect the check result. However, ESP encrypts the original packet and the ESP header does not contain any field that supports source port translation. Therefore, NAPT cannot translate packets encapsulated using both IP and ESP.
IP Header SA: X DA: Z | ESP Header | Raw IP Header | Data | ESP Trailer | ESP Auth data
Authenticated
Encrypted
ESP
AH
Notes: SA: Source Address
DA: Destination Address
SP: Source Port
DP: Destination Port

## Slide 51: NAT Traversal - Solution
NAT traversal is introduced to solve the preceding problem. This function needs to be enabled on the two gateways that need to establish an IPsec tunnel.
After NAT traversal is enabled, if a NAT device is detected during IKE negotiation between two gateways, ESP packets are encapsulated with a UDP header with both the source and destination port numbers being 4500. In this way, ESP packets can pass through the NAT device.
Internet
IPsec tunnel
Gateway 1
NAT device
Gateway 2
IP: X
IP: Z
IP: Y
SNAT (NAPT)
IP Header SA: X DA: Z | UDP SP: 4500 DP: 4500 | ESP Header | Raw IP Header | Data | ESP Trailer | ESP Auth data
IP Header SA: Y DA: Z | UDP SP: 4891 DP: 4500 | ESP Header | Raw IP Header | Data | ESP Trailer | ESP Auth data
During SNAT (NAPT), the source IP address in the outer IP header and the source port number in the UDP header are translated.

## Slide 52: NAT Traversal - Detection Mechanism
Internet
IPsec tunnel
Gateway 1
NAT device
Gateway 2
IP: X
IP: Z
IP: Y
SNAT (NAPT)
ISAKMP
NAT-T
ISAKMP
NAT-T
2
1
ISAKMP
NAT-D Remote hash: A Local hash: B
3
After receiving packet 3, gateway 2 calculates the remote hash value based on the source IP address (Y) in the IP header and source port number (not 500) of the packet. The calculated hash value is not A, indicating that a NAT device exists between gateways 1 and 2.
4
ISAKMP
NAT-D Remote hash: C Local hash: A
Local hash: local IP address + port number 500 (default value)
Remote hash: local IP address + port number 500 (default value)
When a NAT device is detected, ISAKMP changes the source UDP port number from 500 to 4500.
Notes: When NAT traversal is enabled, the first two messages used in IKEv1 negotiation phase 1 carry the Vendor ID payload that identifies the NAT traversal capability (both in main mode and aggressive mode). Two communication parties perform NAT traversal negotiation only when their messages carry the Vendor ID payload.
The NAT Discovery (NAT-D) payload is carried in messages 3 and 4 involved in main mode or in messages 2 and 3 involved in aggressive mode. The NAT-D payload is used to detect whether a NAT device exists between two gateways that need to establish an IPsec tunnel and detect the location of the NAT device. By calculating the hash values of the source and destination IP addresses and ports, the two ends can check whether the IP addresses and ports are changed during transmission. If the calculated hash value is the same as the received one, there is no NAT device between the two ends. Otherwise, there is a NAT device between the two ends and the IP addresses or port numbers are translated using NAT during transmission.
After the NAT device is discovered, the port number of subsequent ISAKMP messages (message 5 in main mode and message 3 in aggressive mode) is translated into 4500.

## Slide 53: NAT Traversal - Scenario 1
In this scenario, the NAT device is located outside the branch network. Private IP address X of the outbound interface on gateway 1 in the branch is translated into public IP address Y on the NAT device. Because the headquarters cannot obtain the post-NAT public IP address of the branch, the public IP address of the peer end cannot be specified on gateway 2 at the headquarters. Therefore, IPsec needs to be configured using an IPsec policy template on gateway 2, and NAT traversal needs to be enabled on the gateways at the headquarters and branch.
Since the headquarters uses a template IPsec policy, the headquarters cannot initiate access to the branch and only the branch can initiate ISAKMP negotiation with the headquarters.
HQ
Internet
IPsec tunnel
Gateway 1
NAT device
Gateway 2
IP: X
IP: Z
IP: Y
Branch
Enable NAT traversal.
Enable NAT traversal.
Establish an IPsec VPN using an IPsec policy template.
Only the branch can initiate ISAKMP negotiation.
S
S
SNAT (NAPT)

## Slide 54: NAT Traversal - Scenario 2
In this scenario, the NAT device is located outside the branch network and managed by the branch. Private IP address X of the outbound interface on gateway 1 in the branch is translated into a fixed public IP address Y. Therefore, IPsec can be configured by using an IPsec policy template or manually specifying the IKE peer.
The NAT device translates only the source address. Therefore, only the branch can initiate ISAKMP negotiation.
HQ
Internet
IPsec Tunnel
Gateway 1
NAT device
Gateway 2
IP: X
IP: Z
IP: Y
Branch
Enable NAT traversal.
Enable NAT traversal.
Configure IPsec by using an IPsec policy template or manually specifying the peer.
Only the branch can initiate ISAKMP negotiation.
S
S
SNAT (NAPT)

## Slide 55: NAT Traversal - Scenario 3
In this scenario, the NAT device is managed by the branch and provides the NAT Server function and SNAT functions to allow both the headquarters and branch to initiate ISAKMP negotiation to access each other. IPsec can be configured on gateway 2 at the headquarters by manually specifying the IKE peer.
HQ
Internet
IPsec tunnel
Gateway 1
NAT device
Gateway 2
IP: X
IP: Z
IP: Y
Branch
Enable NAT traversal.
Enable NAT traversal.
IPsec can be configured by using an IPsec policy template or manually specifying the IKE peer.
N
N
SNAT (NAPT) + NAT Server
Both the headquarters and branch can initiate ISAKMP negotiation.

## Slide 56: NAT Traversal - Session Keepalive (1)
Gateway 1 is behind the NAT (NAPT) device. Only gateway 1 can initiate traffic access, whereas gateway 2 cannot. If the NAT session generated when gateway 1 sends a VPN packet to gateway 2 exists on the NAT device, gateway 2 can send packets to gateway 1. To enable both gateways 1 and 2 to initiate traffic access over a VPN tunnel, a mechanism is required to ensure that the NAT session for the VPN tunnel does not time out.
HQ
Internet
IPsec tunnel
Gateway 1
NAT device
Gateway 2
IP: X
IP: Z
IP: Y
Branch
S
S
SNAT (NAPT)
1
Gateway 2 initiates traffic access. The NAT device is not configured with NAT Server and does not forward the traffic.
2
3
After gateway 1 initiates traffic access over a VPN tunnel, gateway 2 can initiate traffic access to gateway 1 before the NAT session times out.

## Slide 57: NAT Traversal - Session Keepalive (2)
HQ
To ensure that the sessions on the NAT device do not age out, the device (gateway 1) behind the NAT device periodically sends NAT Keepalive packets to keep the NAT session alive. In this scenario, after detecting the NAT device on the intermediate path, gateway 1 sends a NAT Keepalive packet every 20s by default.
Internet
IPsec tunnel
Gateway 1
NAT device
Gateway 2
IP: X
IP: Z
IP: Y
Branch
S
S
SNAT (NAPT)
IP | UDP (port 4500) | FF
Update NAT entries
Notes: The format of NAT Keepalive packets is simple. The UDP header is followed by two hexadecimal Fs, which are used to update the session entries of a NAT device.

## Slide 58
Overview of Campus Multi-Branch Interconnection
Campus Multi-Branch Interconnection Technology: IPsec VPN
  Basic Concepts
  IPsec
  IKE
  Advanced IPsec Functions
  IPsec Configuration Examples
  Example for Configuring Campus IPsec VPN Interconnection
Campus Multi-Branch Interconnection Technology: SD-WAN

## Slide 59: Configuring an IKE Proposal (1)
[Huawei] ike proposal proposal-number
Create an IKE proposal.
Create an IKE proposal and enter the IKE proposal view.
[Huawei-ike-proposal-10]authentication-method { pre-share | rsa-signature | digital-envelope [ version 2.0 ] }
Configure the authentication method for the IKEv1 proposal.
By default, an IKE proposal uses PSK authentication.
In IKE negotiation, the authentication methods in the IKE proposals used by the IKE peers on both ends must be the same. Otherwise, IKE negotiation fails.
[Huawei-ike-proposal-10]authentication-algorithm { md5 | sha1 | sha2-256 | sha2-384 | sha2-512 | sm3 }
Configure the authentication algorithm used in IKEv1 negotiation.
By default, the SHA2-256 authentication algorithm is used for IKEv1 negotiation.

## Slide 60: Configuring an IKE Proposal (2)
[Huawei-ike-proposal-10]encryption-algorithm { des | 3des | aes-128 | aes-192 | aes-256 | sm1 | sm4 }
Configure the encryption algorithm used in IKE negotiation.
By default, the AES-256 encryption algorithm is used for IKE negotiation.
[Huawei-ike-proposal-10]dh { group1 | group2 | group5 | group14 | group15 | group16 | group18 | group19 | group20 | group21 | group24 }
Configure the DH group used in IKE negotiation.
By default, the DH group used in IKE negotiation is group14.

## Slide 61: Configuring an IKE Peer (1)
[Huawei] ike peer peer-name
Create an IKE peer and enter the IKE peer view.
By default, no IKE peer is created in the system.
[Huawei-ike-peer-R2] version { 1 | 2 }
Configure the IKE protocol version used by IKE peers.
By default, an IKE peer supports IKEv1 and IKEv2.
[Huawei-ike-peer-R2] exchange-mode { main | aggressive | auto }
Configure the negotiation mode in IKEv1 phase 1.
By default, the main mode is used in IKEv1 phase 1.
Main mode: protects identities.
Aggressive mode: provides faster negotiation speed, but cannot protect identities.
Auto-sensing mode: A device uses the main mode if it serves as the IKE negotiation initiator. If it serves as the responder, it can use either the main or aggressive mode.

## Slide 62: Configuring an IKE Peer (2)
[Huawei-ike-peer-R2]remote-address { [ vpn-instance vpn-instance-name ] { start-ipv4-address [ end-ipv4-address ] | start-ipv6-address [ end-ipv6-address ] | host-name host-name } | ip-pool pool-number | authentication-address start-ipv4-address [ end-ipv4-address ] }
Configure the remote IP address, an address segment, or a domain name used in IKE negotiation.
By default, an IKE peer has no remote IP address, address segment, or domain name configured.
[Huawei-ike-peer-R2] pre-shared-key key
Configure identity authentication parameters.
By default, the PSK used by IKE peers is not configured when IKE peers use PSK authentication during IKE negotiation.

## Slide 63: Configuring an IPsec Proposal (1)
[Huawei] ipsec proposal proposal-name
Create an IPsec proposal and enter the IPsec proposal view.
[Huawei-IPsec-proposal-1] transform { ah | esp | ah-esp }
Configure the security protocol.
By default, an IPsec proposal uses the ESP protocol.
[Huawei-IPsec-proposal-1] encapsulation-mode { transport | tunnel | auto }
Configure the IPsec data encapsulation mode.
By default, the data encapsulation mode is the tunnel mode.

## Slide 64: Configuring an IPsec Proposal (2)
[Huawei-IPsec-proposal-1] ah authentication-algorithm { md5 | sha1 | sha2-256 | sha2-384 | sha2-512 | sm3 }
Configure an authentication or encryption algorithm for the security protocol.
When AH is used, AH can only authenticate packets and only the AH-supported authentication algorithms can be configured. By default, AH uses SHA2-256 as the authentication algorithm.
[Huawei-IPsec-proposal-1]esp authentication-algorithm { md5 | sha1 | sha2-256 | sha2-384 | sha2-512 | sm3 }
By default, ESP uses the SHA2-256 authentication algorithm.
[Huawei-IPsec-proposal-1] esp encryption-algorithm { des | 3des | aes-128 | aes-192 | aes-256 | sm1 | sm4 | aes-128-gcm-128 | aes-192-gcm-128 | aes-256-gcm-128 | aes-128-gmac | aes-192-gmac | aes-256-gmac }
By default, ESP uses the AES-256 encryption algorithm.

## Slide 65: Configuring an ISAKMP IPsec Policy (1)
[Huawei] IPsec policy policy-name seq-number isakmp
Create an ISAKMP IPsec policy, and enter the ISAKMP IPsec policy view.
By default, no IPsec policy is created.
[Huawei-IPsec-policy-isakmp-1-10] ike-peer peer-name
Reference an IKE peer in the IPsec policy.
By default, an IPsec policy does not reference an IKE peer, and peer-name specifies an existing IKE peer.
[Huawei-IPsec-policy-isakmp-1-10] proposal proposal-name
Reference an IPsec proposal in the IPsec policy.
By default, an IPsec policy does not reference an IPsec proposal, and proposal-name specifies an existing IPsec proposal.

## Slide 66: Configuring an ISAKMP IPsec Policy (2)
[Huawei-IPsec-policy-isakmp-1-10] acl number acl-number
Define the data flow to be protected.
Create an advanced ACL (ACL number: 3000-3999) to define the matching traffic. For example, if gateway A needs to protect network segment 10.1.1.0/24 and gateway B needs to protect network segment 192.168.196.0/24, the ACL rule is rule permit ip source 10.1.1.0 0.0.0.255 destination 192.168.196.0 0.0.0.255.
Before referencing an ACL in an IPsec policy, you need to define the ACL.
[Huawei-IPsec-policy-isakmp-1-10] security acl { ipv6 acl-number | acl-number }
Reference an ACL in an IPsec policy.
By default, an IPsec policy does not reference an ACL. acl-number specifies an advanced ACL that has been created.
An IPsec policy can reference only one ACL. Before an IPsec policy references a new ACL, you need to unbind the existing ACL from the IPsec policy. By default, no IPsec policy is created.

## Slide 67: Configuring a Template IPsec Policy
[Huawei] IPsec policy policy-name seq-number isakmp template template-name
Reference an IPsec policy template in an IPsec policy.
The name of the referenced policy template specified by template-name must be different from the IPsec policy name specified by policy-name. Before running this command, ensure that the referenced policy template has been created.
[Huawei] IPsec policy-template template-name seq-number
Create an IPsec policy template, and enter the policy template view.
By default, there is no IPsec policy template in the system. The configuration items in an IPsec policy template are the same as those in an ISAKMP IPsec policy.

## Slide 68: Referencing an IPsec Policy
[Huawei-GigabitEthernet0/0/0] IPsec policy policy-name
Enter the interface view and apply the IPsec policy group.

## Slide 69: IPsec Configuration Logic - an ISAKMP IPsec Policy
Security ACL
Rule
Define data flows to be protected.
IKE proposal
authentication-method
authentication-algorithm
encryption-algorithm
dh
1
Configure an IKE proposal.
2
IKE peer
version
exchange-mode
pre-shared-key
IKE proposal
Remote-address
Configure an IKE peer.
3
IPsec proposal
encapsulation-mode
AH or ESP parameter
Configure an IPsec proposal.
4
IPsec policy X seq isakmp
Security ACL
IPsec proposal
IKE peer
Configure an ISAKMP IPsec policy.
5
interface
IPsec policy X
Apply the IPsec policy to an interface.
6

## Slide 70: IPsec Configuration Logic - a Template IPsec Policy
Security ACL
Rule
Define data flows to be protected.
IKE proposal
authentication-method
authentication-algorithm
encryption-algorithm
dh
1
Configure an IKE proposal.
2
IKE peer
version
exchange-mode
pre-shared-key
IKE proposal
Configure an IKE peer.
3
IPsec proposal
encapsulation-mode
AH or ESP parameter
Configure an IPsec proposal.
4
IPsec policy-template X
Security ACL
IPsec proposal
IKE peer
Configure a template IPsec policy.
5.1
interface
IPsec policy Y
Apply the IPsec policy to an interface.
6
IPsec policy Y seq isakmp template X
Associate the IPsec policy template with an IPsec policy.
5.2

## Slide 71: IPsec VPN Configuration Example (1)
Internet
IPsec tunnel
R1
R2
GE0/0/0
1.1.1.1/24
GE0/0/0
2.2.2.2/24
10.1.1.0/24
10.2.2.0/24
Establish an ISAKMP IPsec VPN between two egress routers to implement communication between intranet subnets 10.1.1.0/24 and 10.2.2.0/24.
IPsec proposal parameters: ESP, tunnel mode, SHA1, AES-256
IKE peer parameters: IKEv1, main mode, PSK Huawei@123
IKE proposal parameters: SHA1, AES-256, DH group 1
[R1]ike proposal 10
[R1-ike-proposal-10] authentication-method pre-share
[R1-ike-proposal-10] encryption-algorithm aes-cbc-256
[R1-ike-proposal-10] authentication-algorithm sha1
[R1-ike-proposal-10] dh group1
R1 configuration - Create IKE proposal 10.
[R1]ike peer R2
[R1-ike-peer-R2] version 1
[R1-ike-peer-R2] exchange-mode main
[R1-ike-peer-R2] remote-address 2.2.2.2
[R1-ike-peer-R2] ike-proposal 10
[R1-ike-peer-R2] pre-shared-key simple Huawei@123
R1 configuration - Create IKE peer R2.

## Slide 72: IPsec VPN Configuration Example (2)
[R1]ipsec proposal R1
[R1-ipsec-proposal-R1]transform esp
[R1-ipsec-proposal-R1]encapsulation-mode tunnel
[R1-ipsec-proposal-R1]esp authentication-algorithm sha1
[R1-ipsec-proposal-R1]esp encryption-algorithm aes-256
R1 configuration - Create an IPsec proposal.
[R1]acl number 3001
[R1-acl-adv-3001]rule 1 permit ip source 10.1.1.0 0.0.0.255 destination 10.2.2.0 0.0.0.255
R1 configuration - Create an ACL to match IPsec-protected data flows.
Internet
IPsec tunnel
R1
R2
GE0/0/0
1.1.1.1/24
GE0/0/0
2.2.2.2/24
10.1.1.0/24
10.2.2.0/24
Establish an ISAKMP IPsec VPN between two egress routers to implement communication between intranet subnets 10.1.1.0/24 and 10.2.2.0/24.
IPsec proposal parameters: ESP, tunnel mode, SHA1, AES-256
IKE peer parameters: IKEv1, main mode, PSK Huawei@123
IKE proposal parameters: SHA1, AES-256, DH group 1

## Slide 73: IPsec VPN Configuration Example (3)
[R1]ipsec policy R1 10 isakmp
[R1-ipsec-policy-isakmp-R1-10]security acl 3001
[R1-ipsec-policy-isakmp-R1-10]proposal R1
[R1-ipsec-policy-isakmp-R1-10]ike-peer R2
R1 configuration - Create an IPsec policy.
[R1-GigabitEthernet0/0/0]ipsec policy R1
R1 configuration - Apply the IPsec policy.
The configurations of R1 and R2 are similar. The difference lies in the traffic matching ACLs and remote address in the ike peer command.
Note that the IP addresses of GE0/0/0 interfaces on R1 and R2 must be reachable.
R1 and R2 need to use specific static routes (to the remote network segment) or default routes to ensure that traffic destined for the remote network segment passes through GE0/0/0 so that IPsec VPN negotiation can be triggered.
Establish an ISAKMP IPsec VPN between two egress routers to implement communication between intranet subnets 10.1.1.0/24 and 10.2.2.0/24.
IPsec proposal parameters: ESP, tunnel mode, SHA1, AES-256
IKE peer parameters: IKEv1, main mode, PSK Huawei@123
IKE proposal parameters: SHA1, AES-256, DH group 1
Internet
IPsec tunnel
R1
R2
GE0/0/0
1.1.1.1/24
GE0/0/0
2.2.2.2/24
10.1.1.0/24
10.2.2.0/24

## Slide 74: IPsec VPN Configuration Example (4)
[R1]ping -a 10.1.1.254 10.2.2.254
R1 configuration - Trigger IPsec VPN.
<R1>display ike sa
Conn-ID Peer VPN Flag(s) Phase
---------------------------------------------------------------
18 2.2.2.2 0 RD|ST 2
17 2.2.2.2 0 RD|ST 1
R1 configuration - Check the configuration.
Run the ping command on one side to construct IPsec-protected data flows and trigger ISAKMP negotiation.
Run the display ipsec sa command to check detailed IPsec SA information. In the command output, phase 1 and phase 2 SAs are displayed, and their Flag(s) fields display RD|ST, indicating that an IPsec VPN has been successfully established.
Establish an ISAKMP IPsec VPN between two egress routers to implement communication between intranet subnets 10.1.1.0/24 and 10.2.2.0/24.
IPsec proposal parameters: ESP, tunnel mode, SHA1, AES-256
IKE peer parameters: IKEv1, main mode, PSK Huawei@123
IKE proposal parameters: SHA1, AES-256, DH group 1
Internet
IPsec tunnel
R1
R2
GE0/0/0
1.1.1.1/24
GE0/0/0
2.2.2.2/24
10.1.1.0/24
10.2.2.0/24

## Slide 75
Overview of Campus Multi-Branch Interconnection
Campus Multi-Branch Interconnection Technology: IPsec VPN
  Basic Concepts
  IPsec
  IKE
  Advanced IPsec Functions
  IPsec Configuration Examples
  Example for Configuring Campus IPsec VPN Interconnection
Campus Multi-Branch Interconnection Technology: SD-WAN

## Slide 76: Typical Case Analysis: Requirements
Employee
Employee
Enterprise A has one headquarters site and multiple branch sites.
Service servers are deployed at the headquarters site. Employees at branches need to securely access these servers over the Internet.
IPsec VPN tunnels are established between branches and the headquarters to protect enterprise service traffic.
A hub-spoke network is constructed between the headquarters and branch sites, and traffic is centrally controlled at the headquarters. In this networking, traffic exchanged between branches (spokes) is also forwarded by the HQ/DC (hub).
Employee
HQ/DC
Branch 1
Branch 2
Internet

## Slide 77: Typical Case Analysis: Inter-Site VPN Management
VPNs between sites:
Configure the hub-spoke topology for the VPN between sites. Configure the firewall at the headquarters site to function as the hub, and the customer-premises equipment (CPE) at branch 1 and the access point (AP) at branch 2 to function as spokes. Specify the intranet subnet of each site.
Select or create an IPsec policy template and set the PSK and identity authentication type.
iMaster NCE-Campus delivers the configurations to network devices.
Establish IPsec VPN tunnels between the branch sites and headquarters site.
HQ/DC
Branch 1
Branch 2
Internet
CPE (Spoke)
AP (Spoke)
Firewall (Hub)
IPsec VPN
IPsec VPN
Employee network
VLAN 30: 10.1.30.0/24
Employee network
VLAN 31: 10.1.31.0/24
Employee network
VLAN 32: 10.1.32.0/24

## Slide 78: Typical Case Analysis: Access Between Employees
Access from employee A to employee B:
When employee A sends traffic to employee B, the traffic first arrives at the CPE of branch 1. The CPE checks the route (static or imported route) for the traffic and finds that the outbound interface is a tunnel interface. The CPE then encrypts the packets and forwards them to the firewall at the headquarters through the IPsec VPN tunnel.
The firewall decrypts and decapsulates the packets and routes the inner packets to employee B after security processing.
HQ/DC
Branch 1
Branch 2
Internet
CPE (Spoke)
AP (Spoke)
Firewall (Hub)
IPsec VPN
Employee network
VLAN 32: 10.1.32.0/24
A
B

## Slide 79
Overview of Campus Multi-Branch Interconnection
Campus Multi-Branch Interconnection Technology: IPsec VPN
Campus Multi-Branch Interconnection Technology: SD-WAN

## Slide 80: SD-WAN Architecture Overview
iMaster NCE-Campus: controls network elements (NEs) on the entire SD-WAN network, orchestrates network services, and performs monitoring and O&M.
Route reflector (RR): advertises VPN routing and tunnel information between CPEs based on VPN topology policies.
Edge: egress CPE of an enterprise SD-WAN site. At least one edge node needs to be deployed at each site for interconnection between enterprise sites. To ensure network reliability, two edge nodes can be deployed at a site. Each edge node can connect to one or more WAN links. An edge node is essentially the SD-WAN boundary.
Gateway (GW): is a gateway that can connect to the SD-WAN overlay network and multiple types of traditional VPN networks. In different service scenarios, there are three types of gateways: inter-working gateway (IWG), cloud gateway, and point of presence (POP) gateway. A gateway can be regarded as a special edge node.
HQ/DC site
Branch site
Branch site
Management channel
Control plane: BGP EVPN peer relationship
RR
Edge
Edge
GW
MPLS
Internet
Typical SD-WAN Applications
SD-WAN Overview
Notes: CPE: is the egress access router (AR) of the headquarters or branch network.

## Slide 81: SD-WAN Virtual Network Layers and Concepts
Virtual network (overlay network)
Physical network (underlay network)
MPLS
Internet
Virtual network 1
HQ edge
Branch edge
Branch edge
Branch edge
Underlay network (physical network): It refers to the WAN private lines provided by carriers or built by enterprises, such as MPLS VPN private lines and Internet links.
Overlay network (virtual network): SD-WAN introduces the IP overlay technology to construct one or more virtual overlay networks on the physical network, implementing interconnection between the HQ/DC and enterprise branches.
  Multiple overlay networks can be deployed to provide different services under the same tenant (for example, services for multiple departments) or provide different services for different tenants.
Virtual network 2
Typical SD-WAN Applications
SD-WAN Overview
Notes: Huawei EVPN Interconnection Solution uses the EVPN and IP tunneling technologies to establish a logical network isolated from the carrier's physical network. The physical network and logical network are the underlay and overlay networks, respectively. Because user traffic is encapsulated in tunnels, only the overlay network is involved in site interconnection. In this way, multiple WAN service technologies can be flexibly applied, improving enterprise network deployment efficiency and user experience.

## Slide 82: SD-WAN Network Model
Site2
Site3
Site1
CPE1
CPE2
Site ID 1.1.1.1
TN1
TN2
TN2
CPE4
CPE5
Site ID 3.3.3.3
CPE3
Site ID 2.2.2.2
RD1
RD2
Site ID: A site ID uniquely identifies an enterprise site under a tenant and is usually represented by an IP address.
CPE ID: A CPE ID uniquely identifies a CPE under a tenant and is usually expressed by the IP address of the Loopback0 interface of the CPE. A CPE ID is also called a CPE router ID.
Transport network (TN): A TN is a WAN that interconnects branches of an enterprise over public networks or legacy networks. The TN is the underlay network in the EVPN Interconnection Solution.
Routing domain (RD): On a public network, access networks are provided by different network service providers (NSPs) and are accessible to each other. These networks are categorized into the same RD. Links between TNs in the same RD can function as the backup transmission links between sites.
Transport network port (TNP): A TNP is a physical network interface used by a CPE to connect to a carrier's WAN. Branch sites of an enterprise are interconnected through WAN interfaces of devices at both ends. Key information about a WAN interface of a CPE includes the site ID, CPE ID, transport network ID, public IP address of the interface, private IP address of the interface, weight, and encapsulation type of the overlay tunnel (for example, GRE tunnel).
TNP
MPLS
Internet
Internet
Typical SD-WAN Applications
SD-WAN Overview
Notes: Other concepts:
  WAN link: A WAN link refers to a link connecting to a WAN interface. The IP address obtaining mode, link negotiation rate, and bandwidth can be configured for a WAN link.
  Overlay tunnel: An overlay tunnel refers to the connection of TNPs between different sites. Multiple connections can be established between two sites, and packets are distributed simultaneously through intelligent traffic steering.

## Slide 83: Construction of SD-WAN Virtual Networks
Management plane
NETCONF
Control plane
BGP EVPN
RR
CPE
CPE
MPLS
Internet
HQ/DC site
Branch site
Forwarding plane
GRE or GRE over IPsec
Management plane:
iMaster NCE-Campus connects to all devices through NETCONF to manage NEs and orchestrate services on the entire network.
Control plane:
The RR centrally controls and distributes service routes between branch sites.
The enhanced BGP EVPN protocol is used to separate a tenant's VPN routes from the next-hop IP address and implement IPsec SA negotiation.
Forwarding plane:
Data is forwarded based on GRE or GRE over IPsec tunnels. The extended GRE tunnel carries virtual network (VN) IDs to differentiate tenants or departments, thereby transmitting data of multiple VNs over the same tunnel.
Typical SD-WAN Applications
SD-WAN Overview

## Slide 84: GRE over IPsec
GRE is a simple tunneling protocol. However, data is transmitted over a GRE tunnel in clear text, prone to interception.
Typically, GRE is used together with IPsec on the live network. GRE is used to establish interconnection channels between campuses, and IPsec is used to encrypt GRE tunnel packets.
GRE over IPsec data encapsulation
Internet
IPsec tunnel
IPsec tunnel (external)
GRE tunnel (internal)
1.1.1.1
2.2.2.2
IP Header
SA: 1.1.1.1
DA: 2.2.2.2
Payload
IP Header
SA: 1.1.1.1
DA: 2.2.2.2
Payload
IP Header
SA: 1.1.1.1
DA: 2.2.2.2
Payload
GRE Header
ESP Header
100.1.1.1
200.2.2.2
IP Header
SA: 100.1.1.1
DA: 200.2.2.2
Encryption
Note: The IPsec transport mode is used as an example.
Typical SD-WAN Applications
SD-WAN Overview

## Slide 85: Extensions to GRE in SD-WAN
In SD-WAN, the GRE header is extended to enable a GRE tunnel to function as the tunnel on the forwarding plane.
  GRE tunnels are shared between sites as logical tunnels established between the TNPs at the local and peer sites.
  Different VPNs within a site use the GRE extension header (ExtGRE) to identify different VPN instances in the site. Packets received from a TNP port are forwarded to the corresponding service VRF based on the VPN identifier in the GRE extension header.
VRF1
VRF2
IPsec encryption
GRE tunnel
VRF1
LAN1
LAN2
VRF2
LAN1
LAN2
TNP1
TNP2
Data
Data
GRE header (VRF2)
IP
ESP
Data
Data
Data
GRE header (VRF1)
IP
ESP
Data
Typical SD-WAN Applications
SD-WAN Overview

## Slide 86: SD-WAN Uses Enhanced EVPN to Transmit Routing Information
Enhanced Ethernet Virtual Private Network (EVPN) defines several types of BGP EVPN routes by extending BGP. These BGP EVPN routes can be used to transmit TNP routes, service routes, and IPsec SA information.
CPE1
CPE2
BGP EVPN peer relationship
TNP route: TNP reachability information of a WAN interface on a CPE, such as the public IP address, private IP address, site ID, route distinguisher (RD), TN, and route preference.
Service route: VPN route information from branch sites, which is sourced from the LAN-side route of the VPN on a CPE and carries the next-hop site ID.
IPsec SA information: information such as the IPsec-related key required for data encryption of the IPsec channel between CPEs.
RR
Typical SD-WAN Applications
SD-WAN Overview
Notes: The EVPN data plane is combined with MPLS to overcome many limitations of the VPLS L2VPN technology. For details, see RFC 7209 Requirements for Ethernet VPN.
In a network virtualization overlay (NVO) scenario, BGP EVPN is used together with Virtual Extensible LAN (VXLAN) as the control plane protocol for VXLAN.
Enhanced EVPN is a Huawei proprietary implementation, which is different from the standard BGP EVPN.

## Slide 87: Tunnel Table Generated Based on TNP Routes
Tunnel table on CPE2
Peer Site | Local TNP | Peer TNP | Packet Loss | Jitter | Delay
Site1 | TNP2 | TNP1 | 100 | 11 | 100 ms
Site1 | TNP4 | TNP3 | 10 | 22 | 10 ms
A TNP route contains the TNP reachability information of a WAN interface on a CPE, including the public IP address, private IP address, site ID, and route preference.
A VPN route is imported to the forwarding table of a CPE only when the post-NAT public IP address in TNP information related to the VPN route is reachable.
TNPs are the endpoints of SD-WAN tunnels. TNP information includes the site ID, CPE ID, TN ID, and tunnel encapsulation information (such as GRE or IPsec information). TNP information also includes the TNP private IP address, public IP address, carrier, priority, site ID, and weight.
The local TNP and peer TNP establish a forwarding plane tunnel. The service level agreement (SLA) indicators of the tunnel can be obtained through the link quality detection mechanism.
CPE1
CPE2
BGP EVPN
RR
TNP1 route
TNP3 route
TNP2 route
TNP4 route
Internet
MPLS
1
3
2
4
TNP1 1.1.1.1
TNP3 2.2.2.1
TNP2 1.1.1.2
TNP4 2.2.2.2
Site1
Site2
Typical SD-WAN Applications
SD-WAN Overview

## Slide 88: Searching for Tunnels Based on Service Routes
CPE1
CPE2
BGP EVPN
The next hop of a service route is changed from an IP address to a site ID. A CPE searches the routing table for a matching route based on the route prefix, finds the target site ID, determines the optimal TNP port based on TNP information, and sends packets to the target device through the TNP port. The following example describes the process of forwarding service packets from Site2:
RR
Internet
MPLS
1
3
2
4
Step 2: Search the tunnel table and recurse the route to a specific tunnel.
Step 1: Search the service routing table in the VPN to which the service belongs.
Destination Network Segment | Next Hop | VPN
192.168.1.0/24 | Site1 | VN1
Peer Site | Local TNP | Peer TNP | Packet Loss | Jitter | Delay
Site1 | TNP2 | TNP1 | 100 | 11 | 100 ms
Site1 | TNP4 | TNP3 | 10 | 22 | 10 ms
Step 3: Based on the intelligent traffic steering policy delivered by iMaster NCE-Campus, a GRE over IPsec tunnel is selected to forward packets. If the packets need to be encrypted using IPsec, these packets are encapsulated based on the IPsec SA information reflected by the RR.
192.168.1.0/24
192.168.2.0/24
Site1
Site2
192.168.1.0/24 Site1
192.168.2.0/24 Site2
192.168.1.0/24 Site1
192.168.2.0/24 Site2
Typical SD-WAN Applications
SD-WAN Overview

## Slide 89: Typical Case Analysis: Requirements
Employee
Employee
Employee
HQ/DC
Branch 1
Branch 2
MPLS
Internet
Enterprise A has one headquarters site and multiple branch sites.
Each site has employees.
Service access is required between branches and between branches and the headquarters. The SD-WAN Interconnection Solution implements interconnection between sites.
The SD-WAN Interconnection Solution constructs the hub-spoke interconnection topology for the office network. The HQ/DC site functions as the hub, and branch sites function as spokes. Traffic exchanged between branches is forwarded through the hub, implementing centralized control.
The CPE at the HQ/DC site functions as an RR.
Typical SD-WAN Applications
SD-WAN Overview

## Slide 90: Typical Case Analysis: Physical Network Management
Employee
Employee
Employee
HQ/DC
Branch 1
Branch 2
Setting up and configuring a physical network:
Configure the CPE at the HQ/DC site as an RR.
Establish a BGP EVPN connection between the CPE at each site and the RR.
iMaster NCE-Campus delivers the configurations to network devices.
The CPEs at branches establish a BGP EVPN channel on the control plane with the RR to transmit information such as TNP routes and IPsec SA parameters.
CPE
CPE
CPE (RR)
BGP EVPN
Typical SD-WAN Applications
SD-WAN Overview

## Slide 91: Typical Case Analysis: Overlay Network Management
HQ/DC
Branch 1
Branch 2
CPE
CPE
CPE (RR)
Employee network
VLAN 30: 10.1.30.0/24
Employee network
VLAN 31: 10.1.31.0/24
Employee network
VLAN 32: 10.1.32.0/24
Creating an overlay network:
Create an office overlay network, set the topology type to hub-spoke, specify the VLANs and Layer 3 interfaces on the LAN side, and configure routes so that the CPE at a site can communicate with the LAN side at the local site.
iMaster NCE-Campus delivers the configurations to network devices.
Establish a GRE over IPsec tunnel on the forwarding plane between a branch site and the HQ/DC site.
MPLS
Internet
GRE over IPsec
Typical SD-WAN Applications
SD-WAN Overview

## Slide 92: Typical Case Analysis: Service Route Advertisement
HQ/DC
Branch 1
Branch 2
CPE
CPE
CPE (RR)
Employee network
VLAN 30: 10.1.30.0/24
Employee network
VLAN 31: 10.1.31.0/24
Employee network
VLAN 32: 10.1.32.0/24
The LAN-side service routes of the office overlay network are transmitted to the CPE at the local site through dynamic routing protocols (for example, OSPF or BGP) or static routing protocols. The CPE then advertises the routes to the RR through BGP EVPN.
The RR reflects the routes to the CPEs at other sites.
The office network uses the hub-spoke topology. When the RR reflects routes, it changes the next-hop site ID of the routes to the site ID of the hub.
Branch 1: 10.1.31.0/24
BGP EVPN
HQ/DC: 10.1.31.0/24
Typical SD-WAN Applications
SD-WAN Overview

## Slide 93: Typical Case Analysis: Communication Between Branches
MPLS
Internet
HQ/DC
Branch 1
Branch 2
CPE1
CPE2
CPE3 (RR)
Access from employee B to employee A:
Employee B wants to communicate with employee A. When a packet from employee B reaches CPE2, CPE2 searches the routing table and finds that the next hop is the HQ/DC site. Then, CPE2 encapsulates the packet using GRE over IPsec and sends the packet to CPE3.
When the packet reaches CPE3, CPE3 searches the routing table and finds that the next hop is branch 1. Then, CPE3 encapsulates the packet using GRE over IPsec and forwards the packet to CPE1.
After receiving the packet, CPE1 decrypts and decapsulates the packet, queries the overlay route on the LAN side, and forwards the packet to employee A.
Employee B
10.1.32.20/24
Employee A
10.1.31.10/24
Typical SD-WAN Applications
SD-WAN Overview

## Slide 94
(Essay)What encapsulation modes are supported by IPsec?
(Essay)In the SD-WAN Interconnection Solution, what protocols are used on the control plane? And what technologies are used on the forwarding plane?
Notes: Answers:
  Tunnel mode and transport mode
  The SD-WAN control plane uses enhanced BGP EVPN, and the forwarding plane uses extended GRE.

## Slide 95
To reduce costs of interconnection between campuses, VPN technology has been widely used in campus interconnection.
Traditional VPN technologies can only implement interconnection between campuses. When multiple paths exist between campuses, the transmission paths cannot be intelligently adjusted based on the path quality, service, or application requirements.
To optimize multi-link transmission between campuses, iMaster NCE-Campus provides the SD-WAN interconnection solution for WAN interconnection. This solution optimizes multiple transmission paths between campuses and effectively improves service transmission quality.