## Slide 1
Zhu Shigeng 00261992
2020.04.15
Zhang Linrui wx570554
2020.9

## Slide 2: Huawei CloudCampus Solution

## Slide 3
As we constantly make breakthroughs in exploring the digital world, a game-changing digital transformation is taking place in all industries. The adoption of new technologies, such as IoT, big data, cloud computing, and AI, is changing the operation and production modes of different industries while creating more and more new business models. Amid these, digital transformation is the only way for any enterprise and organization to keep up and stay competitive. For enterprises and organizations, campus networks are the cornerstone for their digital transformation and also serve as a bridge between physical and digital worlds. With the constant emergence of new technologies and applications, each enterprise and organization urgently need to easily and quickly deploy an intelligent and reliable campus network.
Huawei CloudCampus Solution is designed especially for enterprises of all sizes to build ultra-broadband, intelligent, simplified, secure, and open intent-driven campus networks. This innovative solution makes it easy to gain real-time insights into and quickly respond to network and service needs.
This course systematically introduces Huawei CloudCampus Solution, including the solution architecture and key components. It also describes the key functions and features of the solution from multiple dimensions, such as simplified network, multi-purpose network, intelligent policy, and intelligent O&M.

## Slide 4
Upon completion of this course, you will be able to:
  Describe the architecture, key components, and highlights of the CloudCampus Solution.
  Describe the ultra-broadband and simplified networks defined in the CloudCampus Solution.
  Understand VXLAN-based virtualized campus networks and their application scenarios.
  Distinguish common access authentication solutions for campus networks.
  Describe the methods of implementing intelligent policy and intelligent O&M in the CloudCampus Solution.

## Slide 5
CloudCampus Overview
Full-Lifecycle Management
Ultra-Broadband Connectivity
Simplified Network
Multi-Purpose Network
Access Authentication
Intelligent Policy
Intelligent O&M

## Slide 6: CloudCampus Network Architecture
Three layers from top to bottom: application layer, management layer, and network layer
Application Layer
Network layer
Management layer
MDM
e-Schoolbag
Asset management
Health management
AAA
……
Intelligent OAM
VN 1
VN 3
VN 2
Virtual network
Internet/
WAN
Native AC
AP
Switch
Switch
Switch
Switch
Switch
Firewall
Physical network
Open API
SNMP
NETCONF/
YANG
Telemetry
Notes: Application layer
  The CloudCampus Solution provides standard APIs based on iMaster NCE-Campus. Through these APIs, the solution opens up various information, such as user identities, network resources, service quality, network location information, and network topology, to upper-layer services. Third parties can use these APIs to customize innovative service applications based on their service requirements, meeting service needs in multiple fields, such as education, business, enterprise, and government.

## Slide 7
Notes: Management layer
  The management layer provides network-level management capabilities, such as configuration management, service management, maintenance and fault detection, and security threat analysis. Traditional campus networks use a network management system (NMS) for network management. Although the NMS can display the network status, it lacks flexible and automatic management capabilities. Once service requirements change, the network administrator needs to re-plan services and manually modify configurations on network devices (including routers, switches, and firewalls), which is inefficient and error-prone. Therefore, to maintain network flexibility is critical in rapidly changing service environments, which requires the use of automation tools to assist in network and service management. Huawei's CloudCampus Solution uses iMaster NCE-Campus to implement automatic network and service provisioning.
  iMaster NCE-Campus abstracts network devices and applications, and rapidly develops and automatically deploys applications through orchestration and by invoking abstract models. iMaster NCE-Campus illustrates the entire network but not independent devices (such as switches, routers, and APs) or discrete configurations (such as access control, QoS, and routing policies) on devices.
Network layer
  Virtualization technologies are introduced to divide the network layer into a physical network and a virtual network.
    The physical network is also called the underlay network and provides basic connection services for campus networks. To meet access requirements of multiple types of terminals, the physical network provides a unified three-network access capability, which allows access of wired, wireless, and IoT terminals simultaneously.
    The virtual network is also called the overlay network. Virtualization technology is used to construct one or more overlay networks over the underlay network. Service policies are deployed on the overlay networks and are separated from the underlay network, decoupling services from networks. Multiple overlay networks can serve different services or customer segments.

## Slide 8: Solution Component 1: Hardware Products
CloudEngine
switches
CloudEngine S12700E: new campus core switches for the Wi-Fi 6 era
AirEngine
Wi-Fi 6 AP
CloudEngine S6730-H: full-featured 10GE routing switches
CloudEngine S5732-H: enhanced GE/multi-GE/hybrid optical-electrical switches
CloudEngine S5735-S: standard gigabit access switches
CloudEngine S5735-L: compact gigabit access switches
HiSecEngine AI firewalls
NetEngine ARs
AirEngine 8760-X1-PRO: Wi-Fi 6 indoor flagship AP
AirEngine 6760-X1/X1E: Wi-Fi 6 indoor high-end APs
AirEngine 5760-22W: Wi-Fi 6 wall plate AP
AirEngine 8760R-X1/X1E: Wi-Fi 6 outdoor APs
6760R-51/51E
8760R-X1/X1E
8760-X1-PRO
6760-X1/X1E
5760-51
AirEngine 9700D-M + 5760-22WD: Wi-Fi 6 agile distributed AP and RU
5760-22W
S5735-S/L
S5730-H/S
S12700E-4
S12700E-12
S12700E-8
S7700
S6730-H/S
USG6300E
USG6500E
USG6600E
USG6700E
AR6100
AR6200
AR6300
AR610
AR650
CloudEngine S7700: high-end intelligent routing switches

## Slide 9: Solution Component 2: iMaster NCE-Campus
iMaster NCE-Campus is a main configuration and management platform in the CloudCampus Solution. It is a main portal for CloudCampus service configuration, O&M, and monitoring.
Management + Control + Analysis
Unified data base
Centralized detection/locating/processing
Plan + Deploy + Maintain + Optimize
Full-lifecycle management
Simulation/Verification/Monitoring/Optimization
iMaster NCE-Campus, an autonomous driving campus network management and control system
Application service layer
Infrastructure layer
Management, control, and analysis layer
MDM
e-Schoolbag
Asset management
Health management
……
Intelligent OAM
Automated + Intelligent
SDN-based automatic service configuration/deployment
AI-powered intelligent analysis/prediction/troubleshooting
All-in-one

## Slide 10: Solution Component 3: iMaster NCE-CampusInsight
Device-centric, lacking insights into user experience
Passive response, unable to identify potential faults
Heavy reliance on onsite fault locating by experienced engineers
SNMP
Minute-level network data collection
Topology mgmt.
Performance mgmt.
Alarm mgmt.
Configuration mgmt.
Visualized experience: Telemetry-based second-level data collection, visualizing experience of any user in any application at any moment
Minute-level identification and root cause locating for potential faults
Identifies potential faults based on dynamic baselines and big data correlation analysis.
Accurately locates root causes using KPI correlation analysis and protocol trace.
Predictive network optimization: AI is used to intelligently analyze the load trends of APs so as to complete predictive optimization of wireless networks.
In addition to using algorithms to improve efficiency, intelligent O&M leverages scenario-based continuous learning and accumulated expert experience to free O&M personnel from complex alarms and alerts, making O&M more automated and intelligent.
Traditional NMS
Telemetry
Second-level network data collection
Visualized experience management
User journey playback
Potential fault identification
Root cause identification
Predictive network optimization
AS-IS: device-centric network management
TO-BE: AI-powered intelligent O&M centered on user experience
Notes: AS-IS: the current status
TO-BE: future ideal status

## Slide 11: Three Deployment Modes of CloudCampus
Operational entity
Customer
MSP, carrier
Huawei
On-Premise
MSP-owned Cloud
Scenario definition
Target customers
Huawei Public Cloud
Customers purchase and own software entities, such as the controller and analyzer, which can be deployed in their data centers or on the public cloud platform.
MSP-operated: MSPs purchase software, such as the controller and analyzer, for operational purposes. The software can be deployed in their data centers or on the public cloud platform.
Huawei-operated: Customers do not need to purchase the controller or analyzer software. Instead, they just purchase Huawei's cloud managed network service.
Customers in industries such as government, education, large enterprise, retail, and finance
MSP, carrier
Customers in industries such as government, education, large enterprise, retail, and finance
Perpetual license + SnS
Term based license (TBL) mode
SaaS mode
Software transaction mode
Notes: A managed service provider (MSP) delivers and manages network-based services, applications, and equipment for enterprises, residential areas, or other service providers.
Perpetual license + SnS: A perpetual license is sold together with subscription and support (SnS) services (e.g. software updates, software upgrades [including new features of new releases], and remote support). Under this model, customers pay the fees regularly. When Huawei sells a software product to a customer for the first time, the customer has to buy both the license and SnS services that are valid for a certain period of time. If the customer does not renew the SnS upon expiry, the customer can only use the licensed functions of the current software version, and can no longer use the SnS services.
SaaS: Under the SaaS model, the MSP deploys or leases out hardware infrastructure, and operates, maintains, and manages software and hardware, while customers use the software as cloud services and make regular payments on a pay-per-use basis.
TBL: The difference between TBL and "perpetual license + SnS" is that under the TBL model, customers receive a limited-time license. They lose the right to use the software if they do not renew the license upon its expiry.
SnS: The SnS business model mainly consists of two parts: software support and software subscription. SnS and software licenses form a complete software charging mode.

## Slide 12: iMaster NCE-Campus Administrator Structure
iMaster NCE-Campus defines three levels of administrators. Administrators at each level take different responsibilities and are granted different operational menus. The rights of administrators are isolated from each other. This ensures network security.
System administrator
MSP administrator
Tenant administrator
A system administrator has all system rights and is responsible for system management and configuration.
The default system administrator account is admin.
A system administrator can create other system administrators and assign specific rights to them as required.
An MSP administrator is a management account created by the system administrator for an MSP. The MSP can use this account to management the networks of managed tenants. The rights of different MSP administrators are isolated from each other.
An MSP administrator can create other MSP administrators and assign specific rights to them as required.
A tenant administrator is an entity for network configuration and maintenance.
A tenant administrator can create other tenant administrator and assign specific rights to them as required. The rights of different tenant administrators are isolated from each other.
Create an MSP administrator
Create a tenant administrator
Authorize the MSP to manage tenant networks

## Slide 13: CloudCampus APP: Delivering End-to-End Simplicity Across Planning, Deployment, and O&M
Site survey
Network planning
Deployment
O&M
Acceptance
Mobile APP that covers full lifecycle management for campus networks
Connects to the cloud-based WLAN Planner to record photos and texts based on drawings.
Connects to the cloud-based WLAN Planner to display network planning results, heat maps, and AP attributes anytime anywhere.
One-click test, single service test, project test
Deployment position acceptance based on the cloud-based network planning project
Deployment by scanning barcode
Mobile O&M, device and application monitoring
AP access through Bluetooth/management VAP, AP offline diagnosis

## Slide 14
CloudCampus Overview
Full-Lifecycle Management
Ultra-Broadband Connectivity
Simplified Network
Multi-Purpose Network
Access Authentication
Intelligent Policy
Intelligent O&M

## Slide 15: Full-Lifecycle Management
Planning (Day 0)
Deployment (Day 1-2)
O&M (Day N)
Optimization (Day N)
Wired network planning
Site design
Network resource planning
Wireless network planning
Physical network deployment
Virtual network deployment
Service policy provisioning
Hardware installation
Routine device maintenance
System maintenance (controller)
User experience visibility
Network monitoring
Network
optimization
WLAN Planner
Manual planning
Manual installation
Exception
identification
Fault demarcation
Note: The parts in green indicate the full-lifecycle network management services provided by iMaster NCE.

## Slide 16: Day 0: Cloud-based WLAN Planner
Planning
Deployment
O&M
Optimization
Log in to Huawei online WLAN Planner.
https://serviceturbo-cloud-cn.huawei.com/serviceturbocloud/dist/#/toolappmarket
Use the network planning report to provide guidance for onsite construction.
The network planning result can be imported into iMaster NCE.
2
4
Obtain the floor plan.
1
1. Environment setting
2. Region setting
3. Device deployment
4. Signal simulation
5. Report export
With Huawei cloud-based WLAN Planner, users can complete WLAN planning in five steps.
3
Notes: Cloud-based WLAN Planner Shortens the Planning Time and Ensures Coverage Based on the Built-In Experience Base.

## Slide 17: Day 0: 3D Network Planning (1)
3D signal simulation, presenting an intuitive view of the coverage effect
Planning
Deployment
O&M
Optimization
Logo wall
Office area
Reception room
Storage room
Notes: 3D Network Planning Intuitively Presents the Planning Effect and Roaming Simulation.

## Slide 18: Day 0: 3D Network Planning (2)
Planning
Deployment
O&M
Optimization
Strongest AP AP-25 CH: 6/36
RSSI 2.4G: -49.7 dBm 5G: -47.5 dBm
Application-layer rate 2.4G: 138 Mbit/s 5G: 135 Mbit/s
Walking route
1. Preset roaming path
2. Display the AP to which the terminal is connected, the access rate, and radio signal information.
Notes: 3D Network Planning Easily Determine the Roaming Effect in Advance Through Roaming Simulation.

## Slide 19: Day 1: Automated Deployment of Physical Network
Interconnection VLAN
Interconnection IP address
IGP (OSPF)
Underlay
Overlay
OA VN
R&D VN
IoT VN
Large enterprises who want to reduce the proportion of time required for initial device installation and configuration as well as device upgrade to the entire network management and O&M period
Simplified network device installation, shortened deployment period
Simplified configuration related to Layer 3 routing, improved configuration correctness
Scenario
Requirements
Huawei solution and advantages
Device plug-and-play
Automatic route config
Visualized configuration interfaces and network planning
Service pre-deployment on the controller in advance, greatly accelerating deployment
GUI-based operations, reducing the probability of configuration errors
Automatic generation of IP and routing protocol-related configurations based on topology planning
Configuration simulation and verification technologies
Planning
Deployment
O&M
Optimization
Notes: Configuration can be performed before or after installation. If configuration is performed before installation, topology information must be recorded in advance. If installation is performed before configuration, the topology can be automatically discovered.

## Slide 20: Automated Deployment of Physical Network Device Plug-and-Play (1)
Through CloudCampus APP (barcode scanning)
Internet
Scan barcode
Tenant: Tenant X
Site: Site Y
Device: AP (ESN...)
1
2
The APP obtains the ESN and MAC address of the AP.
Report AP information.
3
4
5
Register and get managed.
Through registration center
1.1.1.1:8080
Devices supported: AP
Devices supported: AR, firewall, switch, AP
Huawei registration center
1
Record device information.
2
Synchronize device information.
4
Automatically initiate a query request to Huawei registration center to obtain the IP address and port number of iMaster NCE.
Internet
6
Register and get managed.
Tenant: Tenant X
iMaster NCE: 1.1.1.1:8080
Device: AP (ESN...)
3
5
Initiate a registration request to iMaster NCE.
Site network
Site network
Planning
Deployment
O&M
Optimization

## Slide 21: Automated Deployment of Physical Network Device Plug-and-Play (2)
Through web system
Through CLI
Devices supported: AR, firewall, switch, AP
Devices supported: AR, firewall, switch, AP
Internet
2
Register and get managed.
1
In the web system, configure Internet access parameters, and IP address/URL and port number of iMaster NCE.
WEB
Internet
2
Register and get managed.
1
On the CLI, configure Internet access parameters, and IP address/URL and port number of iMaster NCE.
CLI
Site network
Site network
Planning
Deployment
O&M
Optimization

## Slide 22: Automated Deployment of Physical Network Device Plug-and-Play (3)
Through DHCP Option 148
Internet
AR
1
The network administrator has deployed the DHCP service on the network in advance (by deploying the DHCP service on the egress device or deploying an independent DHCP server.)
In addition to delivering IP addresses to the devices to be deployed, the DHCP server uses DHCP Option 148 to notify the devices of the iMaster NCE-Campus IP address and port number.
2
DHCP request
3
DHCP response carrying Option 148
4
Initiate a registration request to iMaster NCE-Campus.
Devices supported: AR, switch, AP
Switch to be deployed
Site network
Planning
Deployment
O&M
Optimization

## Slide 23: Automated Deployment of Physical Network Device Plug-and-Play (4)
Email-based deployment
Devices supported: AR
Internet
1
Network administrator
Email server
Site deployment personnel
AR
2
3
4
The network administrator configures ZTP and selects the email-based deployment mode on iMaster NCE-Campus.
iMaster NCE-Campus packs the deployment configuration into a series of character strings and sends them to the email address specified by the administrator.
The site deployment personnel log in to the email box on a PC at the site and receive the deployment email.
During site deployment, the site deployment personnel connect the PC to the AR in wired or wireless mode and click the hyperlink in the email body. The PC then automatically logs in to the AR, parses the parameters in the hyperlink to obtain the deployment configuration of the AR, and writes the configuration into the AR.
The AR connects to the Internet and automatically sends a registration request to iMaster NCE-Campus.
Site network
3
5
Planning
Deployment
O&M
Optimization

## Slide 24: Day 1: Automated Deployment of Virtual Network
Higher education, government campus, commercial building, and other scenarios where isolated virtual networks need to be provided for multiple services or tenants to achieve "one network for multiple purposes" and improve network resource utilization.
Underlay
Overlay
OA VN
R&D VN
IoT VN
A physical network is divided into multiple virtual networks that are isolated from each other.
Virtual networks are automatically deployed.
Scenario
Requirements
Huawei solution and customer benefits
Multi-purpose
network
Automation
Smooth
evolution
VXLAN-based multi-purpose network
Automatic tunnel establishment through BGP-EVPN
NETCONF/YANG
iMaster NCE-Campus GUI
Policy association at the aggregation and access layers (access switches do not need to support VXLAN)
iMaster NCE-Campus supports automatic deployment of VLAN networks.
Planning
Deployment
O&M
Optimization

## Slide 25: Day 2: Fine-Grained Policy Control and Automatic Deployment of Free Mobility
User A
User A
Move
Consistent policy, consistent experience
Security group (R&D)
Security group (R&D)
Office building 1
Office building 2
Security group-based communication matrix
 | Sales | R&D | Marketing
Sales | √ | × | √
R&D | × | √ | √
Marketing | √ | √ | √
Security group (marketing)
User B
User B
Enterprises, higher education institutions, governments, and other scenarios where fine-grained management of network policies is required
Fine-grained policy control, allowing users to move across the entire network with consistent policies and service experience
Flexible and simplified policy deployment, lowering OPEX
Scenario
Requirements
Huawei solution and customer benefits
Security group-
based
SDN
Natural
language
User- and application-based policy/experience
Permissions, bandwidth, and QoS included
Centralized policy control based on the SDN controller
Service intent-oriented
GUI
Natural language-based configuration
Security group (marketing)
Planning
Deployment
O&M
Optimization
Notes: OPEX means the operating expense, which is the sum of various costs during the enterprise operations, including maintenance cost, marketing expense, labor cost, and depreciation expense.

## Slide 26: Day 2: LAN-WAN Convergence Simplifies Management
MPLS
CPE1
Internet
CPE2
CPE3
HQ campus
Multi-service campus
Branch 1
Simple-service campus
Branch 2
Simple-service campus
SD-WAN
LAN management
Site management
Campus VXLAN
Free mobility
Site configuration
Access authentication
Resource management
WAN VPN
Route management
Intelligent traffic steering
One-stop management
Integrated GUI, improving deployment and O&M efficiency
Integrated deployment, integrated policy, integrated O&M
Abundant SD-WAN policies, improving application experience
Precise identification of 6000+ applications, application-based intelligent traffic steering, application-specific fine-grained QoS scheduling
One platform, reducing customer investment
iMaster NCE-Campus can be deployed in a single-node system or a cluster.
Planning
Deployment
O&M
Optimization

## Slide 27: Day N: Network-Wide Monitoring Based on iMaster NCE-Campus
Site health overview
Inter-site monitoring (overlay topology and interconnection status)
360-degree terminal, application, and device monitoring
...
Health status
Current alarms, historical alarms, masked alarms
Alarm notification mode setting (notification by mail)
...
Alarms
Statistical analysis (including terminal behavior analysis)
Agile report
...
Reports
Terminal authentication events
Key device events
Device go-online and go-offline logs
Event logs
Planning
Deployment
O&M
Optimization

## Slide 28: Day N: Simplified O&M Based on iMaster NCE-Campus
View device configuration results
Save device configurations
Configuration maintenance
Monitor device assets (subracks, boards, subcards, etc.)
Upgrade devices
Activate device licenses
Back up and restore device configuration files
...
Device maintenance
Ping, trace, obtain packet header, trace packet paths, collect diagnosis information, detect application quality ...
Diagnostic tools
Planning
Deployment
O&M
Optimization

## Slide 29: Day N: Improving User and Service Experience Based on Predictive Insights and AI
Intelligent network optimization
Real-time experience visibility
Minute-level fault locating
Proactive issue identification: proactively identifies 85% of potential network issues using the AI algorithms that are continuously trained via Huawei's 200,000+ terminals.
Minute-level fault locating: uses the fault inference engine to locate issues within minutes, identify root causes of the issues, and provide effective fault rectification suggestions.
Intelligent fault prediction: uses AI to learn historical data and dynamically generate a baseline, and compares and analyzes real-time data against the baseline to predict possible faults.
Real-time simulation feedback: evaluates channel conflicts on wireless networks in real time and provides optimization suggestions based on neighbor and radio information about devices on each floor.
Predictive optimization: identifies edge APs and predicts the load trend of APs based on historical data analysis, performs predictive optimization on wireless networks, and compares the gains before and after the optimization. This practice improves the network-wide performance by 50%+ (Tolly certification).
Per-area: intuitively displays the network status and user experience on the entire network or in each area through the multi-dimensional evaluation system.
Per-user: displays network experience (who connects to which AP at what time, experience, and issue) of each user in real time throughout the journey, making faults easier to be traced.
Per-application: perceives experience of voice and video applications in real time, demarcates faulty devices quickly and intelligently, and analyzes the root cause of poor quality.
Planning
Deployment
O&M
Optimization

## Slide 30: AI-Powered Intelligent Radio Calibration
Air interface environment is complex and changeable.
Signal interference and channel conflicts frequently occur.
Traditional radio calibration cannot effectively improve wireless experience.
Scenario 1: manual calibration
Challenge 1: The result of manual planning is not optimal.
Challenge 2: Network environment and interference changes cannot be detected in real time.
Real-time simulation feedback
Displays real-time feedback based on environmental changes, and provides prediction and simulation tools to drive network optimization.
Scenario 2: automatic calibration
Challenge 1: Load balancing-based calibration, without considering AP load
Challenge 2: Only the current status can be detected, but historical load and interference cannot.
Predictive calibration
Leverages big data and AI to provide calibration capability based on service weights.
Planning
Deployment
O&M
Optimization

## Slide 31
CloudCampus Overview
Full-Lifecycle Management
Ultra-Broadband Connectivity
Simplified Network
Multi-Purpose Network
Access Authentication
Intelligent Policy
Intelligent O&M

## Slide 32: End-to-End Bandwidth Upgrade, Meeting the Needs of Digital Terminals and Service Growth
Core layer
Aggregation layer
Access layer (switch)
Access layer (AP)
40GE
10GE
GE, 100 m PoE
802.11n/11ac
100GE
40GE
Multi-GE, 300 m PoE
802.11ax
Scenario requirements
Scenario: government/enterprise offices, school campuses, and other scenarios with increasing bandwidth requirements
Requirements
  Reuses existing cabling and improves end-to-end bandwidth
  Increases the PoE transmission distance without sacrificing the AP uplink bandwidth to meet the ever-growing AP deployment density
Huawei solution and advantages
Multi-GE → 40GE → 100GE: meets future evolution over the next five years
No need to replace existing cables: reduces CAPEX by using existing CAT5E cables while increasing bandwidth by five times (GE → 5GE) and supporting PoE at a long distance of 300 m
Notes: End-to-end campus bandwidth involves three parts: wired backbone, wired access, and wireless access. Of them, wired backbone will evolve along the "25 Gbit/s  100 Gbit/s  400 Gbit/s" path, wired access along the "2.5 Gbit/s  5 Gbit/s  10 Gbit/s" path, and wireless access along the "Wi-Fi 4  Wi-Fi 5  Wi-Fi 6" path. Category 5 enhanced cable (CAT5E cable)
Technology details behind 300 m PoE
  Use shielded cables to reduce internal crosstalk, thus improving the signal-to-noise ratio (SNR)
  Specially package the PHY chips and customize drivers, improving anti-interference
  Raise the technical specifications for signaling cabling for connectors and ports, avoiding crosstalk between ports

## Slide 33: CloudEngine S12700E: All-New Campus Core Switch with Superior Performance
50K
terminals
Native AC
10K APs
Free
mobility
MPLS
CloudEngine
S12700E-4
CloudEngine
S12700E-12
CloudEngine
S12700E-8
VXLAN
Telemetry
MPUE
SFUE
100GE interface cards - X6E/X6S
10GE interface cards - X6E/X6S
GE optical interface cards - X6E/X6S
GE electrical interface cards - X5E/X5S
Scenario | Typical Application
Medium- and large-sized campus networks | Functioning as the core switch, CloudEngine S12700E integrates the AC function to improve the wireless traffic forwarding capability. It also integrates wired and wireless policy control to reduce configuration and failure points.
Campus virtualization | Functioning as the border node of a VXLAN-based virtualized campus network, CloudEngine S12700E works with the controller to implement multi-purpose campus network, thus improving network resource utilization.
High-bandwidth campus interconnection | CloudEngine S12700E enables 100GE interconnection between campus and data center networks, between campus and WAN networks, and within a campus network, meeting the requirements of fast-growing services.
Cell
switching
MAC
max. 512K
FIB
max. 512K
Massive throughput
4.8T per slot
Wired and wireless convergence
10K APs managed
Full programmability
& service agility
24-port 100GE
card
Control-forwarding separation
4.8T per slot

## Slide 34: All-Scenario WLAN: High-Density Access in Indoor and Outdoor Scenarios
Densely populated outdoor scenario: stadiums (AP installation height: > 15 m)
AP + directional antenna
Triple-radio + built-in small-angle directional antenna
Densely populated indoor scenario: small summit venues and auditoriums (AP installation height: 3 m to 15 m)
Traditional omnidirectional antenna
Built-in small-angle directional antenna
Traffic burst scenario: e-classrooms and conference rooms (AP installation height: < 3 m; bandwidth per capita: > 4 Mbps)
Indoor multi-partition scenario: multi-partition office area (AP installation height: < 3 m)
2.4 GHz
5 GHz
5 GHz
5 GHz
2.4 GHz
Dual-radio
Triple-radio
Omnidirectional antenna
Smart antenna

## Slide 35: AirEngine 8760-X1-PRO: Huawei 5G-Powered Wi-Fi 6 AP
Parameter Name | Specifications | Parameter Name | Specifications
Port | 2 x 10GE electrical ports + 1 x 10GE SFP+ | Antenna | Built-in smart antenna
Bluetooth | BLE5.0 | Power supply | DC: 42.5 V to 57 V PoE++, dual power supplies in backup mode
AP speed | 1.15 Gbps (2.4 GHz) + 9.6 Gbps (5 GHz) | USB port | 1
Built-in IoT module | ZigBee, RFID, asset management, electronic shelf label | Security | Hardware encryption: IPsec, DTLS, WPA3
      16 spatial streams
Ultra-high capacity
10.75 Gbps
Multiple radio modes: 4+8+independent scanning radio/4+12/4+8+4
AirEngine 8760-X1-PRO
16 spatial streams + flexible choices of radio modes
2 x 10GE uplink ports
Dual PoE power supplies, improving AP reliability
Optical port: 1 x 10GE SFP+
Electrical port: 2 x 10GE
Hybrid cable
10GE
10GE
Mini air duct + liquid cooling
Mini air duct system for excellence in heat dissipation
Liquid cooling
Independent probe
Independent hardware + dual-band scanning
Real-time network optimization
4 degrees
Big data-based radio calibration with CampusInsight

## Slide 36
CloudCampus Overview
Full-Lifecycle Management
Ultra-Broadband Connectivity
Simplified Network
Multi-Purpose Network
Access Authentication
Intelligent Policy
Intelligent O&M

## Slide 37: Native AC, Achieving Wired and Wireless Convergence
NM Area
CAPWAP
Unified forwarding: Wired and wireless traffic is centrally processed by the core switch before being forwarded.
Unified authentication: The core switch functions as the unified authentication point and Layer 3 gateway for both wired and wireless users.
Unified policy execution: The core switch is the unified policy enforcement point for wired and wireless users.
Native AC
Notes: The switch integrates the AC function to eliminate bottlenecks in wireless traffic forwarding, reduce failure points, and manage wired and wireless traffic in a centralized manner:
  Uniformly manages and forwards wired and wireless services.
  Functions as the gateway of both wired and wireless users and manages both types of users.
  Used as the authentication point for both wired and wireless access.
  Enforces policies for both wired and wireless services.

## Slide 38: Wi-Fi & IoT Convergence, Unifying Network Deployment and O&M
Internet
IoT AP
Store
IoT service management platform
Wi-Fi
tag
Wi-Fi
terminal
Bluetooth
tag
RFID
tag
IoT
sensor
Wristband
Bluetooth
RFID
ZigBee
Scenarios and challenges
Scenarios: retail, healthcare, education, enterprise, and other campuses where innovative digital services need to be provided based on IoT
Challenges: Wi-Fi and IoT (such as Bluetooth and RFID) networks are deployed separately. Numerous wireless networks coexist, resulting in high costs and inflexible service expansion. There is also radio frequency interference between these wireless networks, affecting service experience.
Huawei IoT AP
Wi-Fi & IoT converged architecture
Converged site for the AP and IoT base station, reducing auxiliary resources (such as access and power supply management) by 50%
Cloud-based management and plug-and-play, facilitating service configuration
Wi-Fi and IoT configuration association, allowing automatic Wi-Fi channel switching in case of conflict
ESL management
Medical IoT
Health management
Asset management
2.4 GHz (Wi-Fi)
Channel-6
2.4 GHz (RFID)
Channel-11

## Slide 39: CSS and iStack
Two core devices are virtualized into one device using CSS, reducing the number of managed NEs by 50%.
Aggregation devices implement uplink aggregation using Eth-Trunk, increasing the bandwidth by 100%.
CSS: "2-to-1" virtualization, with "1+1" link protection
Physical topology
Logical topology
CSS
Virtualizes multiple devices into one device, greatly simplifying network configuration and device management.
Works with Eth-Trunk to provide uplink aggregation and load balancing, improving uplink reliability.
Supports service port stacking, without requiring dedicated stack ports or stack cards, making networking convenient and flexible.
iStack: "N-to-1" virtualization, simplifying device configuration and management
Physical topology
Logical topology
CSS
iStack
iStack
iStack
Notes: CSS/iStack can be used with Eth-Trunk to form a logical tree topology. This simplifies network topology, prevents Layer 2 loops, and improves network reliability.

## Slide 40
CloudCampus Overview
Full-Lifecycle Management
Ultra-Broadband Connectivity
Simplified Network
Multi-Purpose Network
Access Authentication
Intelligent Policy
Intelligent O&M

## Slide 41: "1-to-N" Virtualization Implements Multi-Purpose Network
OA
Videoconferencing
Security protection
Internet
OA
Videoconferencing
Security protection
Internet
OA
Videoconferencing
Security protection
VXLAN
VN1
(for OA)
VN2
(for videoconferencing)
VN3
(for security protection)
Multiple services carried on one physical network
Automatic deployment of physical network
Automatic deployment of virtual network
Automatic delivery of service policy

## Slide 42: Diversified Networking Models
VXLAN
Two-layer physical network
Access switches function as edge nodes.
Three-layer physical network
Access switches function as edge nodes.
Aggregation switches do not need to support VXLAN.
Three-layer physical network
Aggregation switches function as edge nodes.
Access switches do not need to support VXLAN and can work with aggregation switches to implement policy association.
Legacy access switches can be reused.
Aggregation switches function as edge nodes and provide the native AC function.
APs are managed by aggregation switches. APs do not need to support VXLAN and can be reused.
Border
Edge
Transparent
Edge
Edge
Edge
Access

## Slide 43: Multi-Border Networking
Data center
Border 1
Edge
Edge
Internet
Border 2
VXLAN
Networking description: There is one campus. Multiple border nodes are deployed and connected to the same egress, achieving redundancy.
Applicable scenario: Multiple border nodes exist in one campus, and they connect to the same external network, achieving reliability in non-stack scenarios.
Border 1
Edge
Edge
Internet
Border 2
VXLAN
Networking description: There is one campus. Multiple border nodes are deployed and connected to different egresses. Different services are transmitted through different border nodes.
Applicable scenario: One campus has different external networks.
Internet
Border 1
Edge
Edge
Internet
Border 2
VXLAN
Networking description: There are multiple campuses. Each campus connects to its external network through its independent border node.
Applicable scenario: Multiple campuses belong to the same fabric, and each campus network has its independent border node and egress network.
Campus 1
Campus 2

## Slide 44
CloudCampus Overview
Full-Lifecycle Management
Ultra-Broadband Connectivity
Simplified Network
Multi-Purpose Network
Access Authentication
Intelligent Policy
Intelligent O&M

## Slide 45: User Access Authentication
User terminal
Authentication
device
Configuration
NETCONF
Authentication
HTTP/2
Authentication
RADIUS
User management
Portal page customization
Portal server
RADIUS server
Social media authentication
QQ, Weibo, Facebook, Twitter
Third-party
RADIUS server
Authentication modes:
Portal authentication: user name and password authentication, anonymous authentication, SMS authentication, QQ authentication, Sina Weibo authentication, Facebook authentication, Twitter authentication, passcode authentication
MAC address authentication
802.1X authentication
Transmission protocols:
HTTP/2 and RADIUS for authentication data transmission
NETCONF for configuration data transmission
Open authentication:
Interconnection with third-party Portal servers
Interconnection with social media such as QQ, Weibo, Facebook, and Twitter
Third-party
Portal server

## Slide 46: Intelligent Policy Engine Achieves Fine-Grained Policy Control
Permission
Bandwidth
QoS
Application
Security
Access time
When
User identity
Who
Access position
Where
Device attribute
Whose
Access mode
How
Terminal type
What
Condition: 5W1H-based policy
Result: fine-grained permission control
User/User group/Role
Site, region, device group, device type, device, SSID, IP address
Day/Hour
PC/iOS/Android, etc.
Company-issued/BYOD terminal
Wired/Wireless
Portal/MAC address/802.1X authentication
VLAN/ACL/Security group, VIP user...
Uplink/Downlink bandwidth, DSCP value
High/Medium/Low
Traffic duration control (for Portal authentication only)
Application group/Application
URL filtering
Intelligent
policy engine

## Slide 47: Portal Authentication: Supporting Portal Page Customization
With this function, enterprises can conveniently customize their own Portal pages so as to launch VASs such as brand promotion and advertisement push.

## Slide 48: Terminal Identification and Policy Automation
Difficult to locate bogus terminals
Example: an enterprise
10+ authentication faults reported every day
50+ types of smart terminals
Example: higher education institution
Data of smart terminals collected by level-2 departments
Difficult and error-prone MAC address collection
Terminal type-based
Automatic authorization
Recognized as a camera
Automatically added to a video surveillance group
Set as a VIP user
Terminal type-based
Automatic authentication
Recognized as a printer
Automatic MAC address authentication, without the need of manual MAC address input
Terminal type-based
Bogus terminal detection
Recognized as an IP phone first and then a PC
Report a bogus terminal alarm.
Requirements & challenges
Terminal identification and policy automation
Terminal fingerprint database
Information reporting
Proactive scanning
>
Notes: On a campus network, access terminals include smart terminals (such as PCs and mobile phones) and dumb terminals (such as IP phones, printers, and IP cameras). Currently, terminal management on campus networks faces the following challenges:
  The network management system (NMS) can only display the IP and MAC addresses of access terminals, but cannot identify the specific terminal type. As a result, the NMS cannot provide refined management for network terminals.
  Network service configurations and policies vary according to the terminal type. Consequently, administrators need to manually configure different services and policies for each type of service terminals, complicating service deployment and operations.
To address these challenges, Huawei provides the automatic terminal identification and policy delivery solution, which delivers the following functions:
  iMaster NCE-Campus can display the network-wide terminal types and operating systems, for example, dumb terminals including printers, IP cameras, smart all-in-one cards, and access control systems. iMaster NCE-Campus can also collect statistics and display traffic by terminal type.
  Administrators do not need to manually configure different services and policies for different types of dumb terminals such as IP phones, printers, and IP cameras on the campus network. This is because iMaster NCE-Campus can automatically identify terminals and deliver the corresponding access policies and service configurations to them.

## Slide 49: Terminal Identification: Supports Proactive and Passive Detection
Terminal visibility: collects terminal type statistics (by vendor and OS), displays the relationship between terminals and access ports, queries access policies (covering VLAN, QoS, and authentication mode), and exports reports
Terminal policy automation:
  Supports automatic terminal access based on terminal types, thereby achieving automatic MAC address authentication of dumb terminals
  Authorizes policies (covering VLAN, security group, access permission, and QoS) on a per-terminal group basis
  Supports IPv4/IPv6 dual-stack terminals
Passive detection
Proactive detection
Scan-and-detect
Feedback
1
2
4
Deliver configurations/policies
3
Display identification result
Administrator
5
Deliver configurations/policies
4
Display identification result
Administrator
1
Send traffic
Collect fingerprint
2
3
Report fingerprint

## Slide 50: Terminal Identification Methods
Type | Identification Method | Description | Applicable Scenario
Information reporting | MAC OUI | The first three bytes of a MAC address indicate the manufacturer. | Identify the device manufacturer only
 | HTTP User-Agent | User-Agent contains the manufacturer, terminal type, operating system, browser type, and other information. | Mobile phones, tablets, PCs, workstations, intelligent voice and video terminals
 | DHCP Option | Some options of a terminal's DHCP packets can be used to classify terminals, for example, DHCP options 55, 60, and 12. | Mobile phones, tablets, PCs, workstations, IP cameras, IP phones, printers, etc.
 | LLDP | LLDPDUs carry device model information. | IP phones, IP cameras, network devices, etc.
 | mDNS | mDNS packets contain terminal model and service information. | Apple devices, printers, IP cameras, etc.
Proactive scanning | SNMP Query | Obtains identification information by querying device information-related SNMP MIB objects. | Network devices, printers, etc.
 | Nmap | Scans the OS and services of terminals to detect the terminal model and OS information. | PCs, workstations, printers, phones, IP cameras, etc.

## Slide 51: Automatic Policy Delivery Process Based on Terminal Types
On the iMaster NCE-Campus web UI, an administrator enables the terminal identification function, selects terminal types, and specifies the corresponding policies.
iMaster NCE-Campus delivers terminal identification configurations to network devices.
When terminals access the network, network devices collect the fingerprint information of the terminals and report the information to iMaster NCE.
iMaster NCE-Campus automatically matches the terminals' fingerprint information against the fingerprint database to identify the terminal types.
iMaster NCE-Campus automatically delivers access and authorization policies for the terminals based on the policies defined by the administrator.
The administrator enables terminal identification and configures terminal policies.
1
The network device reports terminal fingerprint information.
2
iMaster NCE-Campus delivers configurations to the network device.
4
iMaster NCE-Campus matches the terminal's fingerprint information against the fingerprint database and identifies the terminal type.
5
iMaster NCE-Campus delivers access and authorization policies for the terminals to the network device.
3

## Slide 52
CloudCampus Overview
Full-Lifecycle Management
Ultra-Broadband Connectivity
Simplified Network
Multi-Purpose Network
Access Authentication
Intelligent Policy
Intelligent O&M

## Slide 53: Free Mobility Achieves Security Group-Based Policy Management
Campus network
User A
User B
User C
Access authentication
Access authentication
Access authentication
Deliver security groups and policies
1
2
3
4
3
4
2
Sales
security group
R&D
security group
Server resource
security group
Permission policies
1
Security groups are defined, each specifying a group of users with the same network access policies.
Permission control policies and user experience policies are configured based on security groups and delivered to network devices.
Security groups are authorized to the users who pass access authentication.
After user traffic enters a network, network devices enforce policies based on source and destination security groups of the traffic.
Notes: Free mobility: grants a user consistent network permissions and enforces the corresponding policies, regardless of the user's location and the IP address used to access the network.

## Slide 54: Preferential Access of VIP Users
Access denied for non-VIP users
Access permitted for VIP users
If a VIP user attempts to connect to an AP when the number of users connected to the AP reaches the threshold, the AP forcibly disconnects a non-VIP user and connects the VIP user to the network.
AP
STA
AC
STA
A user who has connected to the network
Access of a non-VIP user is denied.
A connected user is forced to go offline.
If a non-VIP user attempts to connect to an AP when the number of users connected to the AP reaches the threshold, the connection attempt will fail.
The number of access users reaches the threshold.
1
2
3
2
Identified as a VIP user
AP
AC
The number of access users reaches the threshold.
1
STA
STA
A user who has connected to the network
4
Connect successfully
Notes: In high-density scenarios, such as exhibition halls and stadiums, a limit is usually imposed on the maximum number of users who can associate with a radio and VAP so as to improve user experience. In addition, preferential access of VIP users is deployed to ensure that new VIP users can still access the network even when the number of access users reaches the threshold. This function improves user experience of VIP users.
Identification of VIP users
  A device identifies a user as a VIP if the user belongs to a VIP user group. The priority field is added to the user authorization structure. After users are added to a VIP user group and the authorization information is delivered to the VIP user group, users in the VIP user group inherit the priority of the VIP user group.

## Slide 55
Notes: Preferential access of VIP users
  Configure preferential access for VIP users on the device. If the number of users on a VAP reaches the maximum or if the number of users reaches the CAC (call admission control) threshold, any new network access attempt will undergo the following process: The user will first be authenticated. Then the system checks whether the user is a VIP during the authorization phase. If the user is a VIP, the system allows the user to access the network, by forcing a non-VIP user to go offline. If the user is not a VIP, the user is forced to go offline.
  In Portal authentication scenarios, priorities of users in pre-connection state cannot be determined. These users are considered high-priority users and will not be disconnected even when VIP users attempt to access the WLAN.
Preferential service scheduling for VIP users
  After a user is marked as a VIP user in the user authorization process:
    The user's services will not be rate-limited.
    The user's services are scheduled preferentially.
    Priority is re-marked.

## Slide 56: Bandwidth Reservation for VIP Users: Guaranteeing Sufficient Bandwidth
When the number of users in a conference room increases sharply, mobile user terminals preempt air interface resources, deteriorating wireless experience of conference terminals.
Identify VIP users and guarantee sufficient bandwidth for them.
Scenario
Requirements
Define VIP users.
Define the percentage of bandwidth to be reserved for VIP users.
1
2
Conference terminal
VIP user
User terminal
Common user
20% bandwidth reserved
Bandwidth contention
Common user
Frequency bandwidth
Time
OFDMA spectrum resources reserved for VIP users
VIP user
OFDMA spectrum resources are reserved for VIP users.
On-demand bandwidth reservation:
  No bandwidth is reserved when no VIP user accesses an AP.
  Sufficient resources are reserved only for VIP users.
Solution
3
Spectra dedicated for VIP users
Reserved fixed subcarriers
Spectra shared by common users
Shared subcarriers

## Slide 57: Intelligent HQoS: User- and Application-Based QoS Policies
Traditional QoS schedules traffic based on port bandwidth, allowing differentiation of traffic based on service levels. However, it is difficult to differentiate services based on users.
Traditional QoS cannot manage and schedule traffic of multiple services from multiple users simultaneously.
Challenges
Hierarchical QoS (HQoS) can not only differentiate traffic of different users but also schedule traffic based on service priorities.
HQoS differentiates service traffic using multi-level queues, and manages and schedules transport objects such as multiple users and services in a unified manner.
Solution
User terminal
Network device
Management,
Control, and
analysis
VIP user
Common user
Defines VIP users
Defines application priorities
1
VIP user
Common user
Two-level scheduling: user and application queue
2

## Slide 58: SD-WAN Featuring Fine-Grained Application Control
Internet
MPLS
Site 1
Site 2
CPE
CPE
Video
HTTP
Precise identification of 6000+ well-known and user-defined applications
Application identification
Application- and traffic classifier-based
IP FPM in-line service quality detection
Intelligent traffic steering
Application- and VPN-based multi-level queues
Bandwidth allocation for different VPNs
HQoS intelligent scheduling

## Slide 59: Intelligent Traffic Steering (1)
(Mandatory) Link quality–based traffic steering
(Optional) Load balancing–based traffic steering
Voice and video services are sensitive to delay and packet loss rate. You can configure the good-quality MPLS link as the primary link and the Internet link as the secondary link for the two types of service. In addition, you need to configure SLA requirements for the services so that intelligent traffic steering can be performed based on link SLA.
MPLS
Internet
CPE1
CPE2
Voice data
When an enterprise has multiple links, you can configure load balancing-based traffic steering to make full use of the link bandwidth.
1
2
3
4
1
2
The link SLA deteriorates to the lowest level that can be tolerated by voice services.
Dynamically adjust traffic.
3
4
MPLS
Internet
CPE1
CPE2
1
2
3
4
Data flow A
1
2
3
4
Data flow B
Notes: Link quality-based traffic steering: Different applications have different requirements on link quality. For example, voice and video services are sensitive to delay and packet loss rate and have high requirements on link quality. Therefore, you can configure the good-quality MPLS link as the primary link and the Internet link as the secondary link for the two types of service. In addition, you need to configure SLA requirements for the services so that intelligent traffic steering can be performed based on link SLA, thus meeting the SLA and bandwidth requirements of applications.
Load balancing-based traffic steering: If an enterprise has multiple links, you can configure load balancing-based traffic steering to fully utilize link bandwidth. During service forwarding, the devices can select different links for different applications based on link weights, thereby improving the bandwidth utilization.

## Slide 60: Intelligent Traffic Steering (2)
(Optional) Application priority–based traffic steering
If multiple types of service packets are transmitted on the same link, traffic of high-priority applications is preferentially processed in the case of congestion, ensuring user experience of high-priority applications.
MPLS
Internet
CPE1
CPE2
Voice and video
File transfer
High priority
Low priority
High-quality link
(network congestion)
Low-quality link
Notes: Application priority–based traffic steering: If multiple types of service packets are transmitted on the same link, traffic of high-priority applications is preferentially processed in the case of congestion, ensuring user experience of high-priority applications. For example, voice, video, and file transfer services are carried on an MPLS link. If the link bandwidth is insufficient, the experience of the voice and video services is preferentially guaranteed.

## Slide 61
CloudCampus Overview
Full-Lifecycle Management
Ultra-Broadband Connectivity
Simplified Network
Multi-Purpose Network
Access Authentication
Intelligent Policy
Intelligent O&M

## Slide 62: Panorama of Intelligent O&M
Fault prediction & autonomous self-healing
Fault identification & root cause analysis
(Big data & ML-powered)
Experience visualization
(Telemetry)
Individual fault analysis
Group fault analysis
Fault prediction
Access analysis:
Protocol trace
Experience analysis:
Poor-QoE user analysis
Application analysis:
Voice/Video application quality awareness
Analysis of four types of issues:
Quick root cause analysis based on the rule engine
Optical module fault prediction
Experience visualization
Per-user journey playback
Autonomy and self-healing
CampusInsight:
Network dialing test
for access service
Cloud-based deployment
Single-node deployment
Cluster deployment
Integrated wired and wireless topology
Automatic optimization in the event of high interference
Wi-Fi signal heat map
Visualized and comparable WLAN optimization
Network-wide quality evaluation system
Notes: Machine learning is a science of the artificial intelligence. The field's main objects of study are artifacts, specifically algorithms that improve their performance with experience. ML is a program or system that builds a predictive model from input data. The system uses the learned model to make useful predictions from new (never-before-seen) data drawn from the same distribution as the one used to train the model. Machine learning also refers to the field of study concerned with these programs or systems.

## Slide 63
(Multiple-choice) Which of the following intelligent traffic steering modes are supported in Huawei SD-WAN Solution? ( )
  Link quality–based traffic steering
  Load balancing–based traffic steering
  Application priority–based traffic steering
  User-based traffic steering
(TorF) When free mobility is deployed on a campus network, the authentication point of user terminals must be a Huawei device. ( )
  True
  False
Notes: Answer
  ABC
  B

## Slide 64
Huawei delivers end-to-end intent-driven campus network solutions that build on four-engine (CloudEngine, AirEngine, NetEngine, and HiSecEngine) products as well as iMaster NCE-Campus, and iMaster NCE-CampusInsight across the access layer, aggregation layer, and management layer.
Huawei CloudCampus Solution helps customers to build ultra-broadband, simplified, intelligent, secure, and open campus networks needed to address challenges they face in connectivity, experience, O&M, security, and ecosystem development during digital transformation.