## Slide 1
CloudCampus
V100R019C10
Lu Yueyue/WX445705
2020-11-19
Zhu Shigeng/00261992,
Yao Ning/00276205, Zhang Linrui/WX570554
Optimized

## Slide 2: VXLAN-based Virtualized Campus Network Design Guide

## Slide 3
A campus network typically refers to the internal network of an enterprise or organization. It primarily aims to enable more efficient operations of enterprises' main businesses.
Campus networks vary with scale, and generally fall into two types: large- and medium-sized campus networks and small- and medium-sized campus networks.
Huawei's CloudCampus Solution, ideal for campus networks of all sizes, introduces an intent-driven network (IDN) concept. By incorporating big data analytics and AI on the basis of cloud and software-defined networking (SDN), Huawei's CloudCampus Solution helps enterprises build an intelligent, simplified, converged, open, and secure campus network.
In this course, we focus on large- and medium-sized campus networks (> 2000 terminals). Such a network usually covers multiple buildings. Multiple aggregation layers centralize networks of multiple buildings to the core layer, so the entire network topology needs to be designed as a three-layer model. To support access of massive terminals, the access layer must provide high-density wired ports and a large number of wireless APs, and implement differentiated access control based on terminal types. Additionally, the campus network needs to provide advanced capabilities such as virtual networks (VNs) and free mobility so as to ensure service continuity.

## Slide 4
Upon completion of this course, you will be able to:
  Describe the requirements and challenges faced by large- and medium-sized campus networks.
  Describe the layers and architectures of large- and medium-sized campus networks.
  Describe the concepts and relationships of underlay, fabric, and overlay on a campus network.
  Design the underlay for a VXLAN-based virtualized campus network according to your actual project requirements.
  Design the fabric and overlay for a VXLAN-based virtualized campus network according to your actual project requirements.
  Design WLAN services, admission authentication, and O&M for a VXLAN-based virtualized campus network according to your actual project requirements.

## Slide 5
VXLAN-based Virtualized Campus Network and Solution
Underlay Design
Fabric Design
Overlay Design
Admission Control and Free Mobility Design
WLAN Design
O&M Design

## Slide 6: Service Requirements and Challenges of Large- and Medium-Sized Campus Networks
Enterprises' campus networks are the cornerstone of their digital transformation. Nowadays, mobile office, cloud computing, SDN, Internet of Things (IoT), artificial intelligence (AI), and big data are gaining momentum. Driven by this, new technologies and applications are constantly emerging and are making inroads to enterprise campus networks, which imposes many new challenges for the campus networks.
Converged network
Requirement:
Diversified access terminals and services require a converged campus network.
Challenge:
Wi-Fi and IoT services are independently planned, deployed, and managed, resulting in high network construction costs.
The network management and O&M workload is heavy.
User experience awareness
Requirement:
Network O&M should become automated and intelligent, with insights into user experience anytime, anywhere.
Challenge:
Service faults cannot be detected in a timely manner.
Fault locating heavily relies on the O&M skills and experience of professionals, so faults cannot be quickly located.
The network cannot be self-optimized.
Network automation
Requirement:
The network should become automated to address the growing complexity of deployment and policies due to the surge of applications and services.
Challenge:
Manual configuration is repetitive, complex, and labor-intensive.
New service rollout requires configuring devices one by one, which is time-consuming and costly.
The workload of network policy deployment and adjustment is heavy.

## Slide 7: Huawei CloudCampus Solution Introduction
Huawei's CloudCampus Solution, ideal for campus networks of all sizes, introduces an IDN concept. By incorporating big data analytics and AI on the basis of cloud and SDN, Huawei's CloudCampus Solution helps enterprises build an intelligent, simplified, converged, open, and secure campus network.
Analysis
Management
Control
Design
Deployment
Policy
One-stop management platform
NETCONF/YANG
WAN/
Internet
Large- or medium-sized campus
Small- or medium-sized campus
Campus interconnection
OA VN
R&D VN
OA VN
R&D VN
Security group 1
Security group 2
Security group 3
Security group 4
Security group 5
Access policy
Bandwidth
Priority

## Slide 8: CloudCampus — Ultra-Broadband, Converged Campus Network Architecture
Wired, wireless, and IoT convergence
Wired and wireless convergence
Switch integrating the WLAN AC function
Unified management and experience for wired and wireless users
IoT AP
All-scenario WLAN
Hybrid optical-electrical switch
& 300-m PoE++
Indoor scenario
High-density stadium
Outdoor scenario
Dense-room scenario
Latest Wi-Fi 6 APs, high-density APs, and distributed Wi-Fi solutions, delivering WLAN capabilities in all scenarios
Wi-Fi 6 AP, powered by Huawei 5G
PoE++
300 m
Hybrid optical-electrical switch
Hybrid cable
Wi-Fi 6 AP
Co-site of AP and IoT base station
Wi-Fi & IoT network convergence, simplifying management
Notes: Wired, wireless, and IoT network convergence, allowing diversified terminals and services
  Huawei S series switches integrate the WLAN access controller (AC) functionality to implement wired and wireless convergence and provide unified wired and wireless management and experience. Huawei APs integrate IoT modules to provide functions of IoT base stations, implementing converged Wi-Fi and IoT networks as well as simplified management. Huawei's solution provides unified authentication and access policy control for wired and wireless users by integrating the user authentication, user management, and policy association functions. Administrators can obtain consistent user management experience and simplify O&M of wired and wireless networks.

## Slide 9
Notes: All-scenario WLAN: ideal for differentiated access requirements of customers
  Huawei provides Wi-Fi 6 APs, high-density APs, and an agile distributed Wi-Fi solution tailored for a diverse of scenarios, such as common indoor deployments, high-density stadiums, outdoor environments, and dense rooms. These offerings provide pervasive high-density WLAN coverage and deliver assured user access experience. The resulting benefits include convenient deployment and reduced investment costs.
  Wi-Fi 6 is the sixth generation of Wi-Fi standards. It inherits a large number of key 5G technologies, such as orthogonal frequency division multiple access (OFDMA), multi-user multiple-input multiple-output (MU-MIMO), and 1024 Quadrature Amplitude Modulation (1024-QAM). Compared with Wi-Fi 5, Wi-Fi 6 offers a 4-fold increase in both the network bandwidth and concurrent user quantity, and shortens the network latency from 30 ms to 20 ms. All these merits enable Wi-Fi 6 to easily meet the ultra-large bandwidth, ultra-high density access, and ultra-low latency requirements in various application scenarios. Typical scenarios include, for example, 4K ultra-HD video conferencing (ultra-large bandwidth), high-density stadium (ultra-high concurrency), and VR (ultra-low latency). Based on the profound understanding and grasp of 5G technologies, Huawei becomes a major contributor to the Wi-Fi 6 standard. Huawei experts have served as the chairmen of five Wi-Fi standard working groups.
Hybrid optical-electrical switch & 200-m PoE++: higher bandwidth and more flexible network deployment
  With the advent of 802.11ac standards and products, the access rate of wireless terminals exceeds 1 Gbps. However, the access rate of GE interfaces fails to meet this trend. Huawei provides hybrid optical-electrical switches that provide PoE++ power for APs within 300 m through hybrid cables.

## Slide 10: CloudCampus — Simplified Campus Network Deployment
Physical network automation
VN automation
User policy automation
The following is achieved via iMaster NCE-Campus GUI:
Device plug-and-play and automatic deployment
Underlay network route orchestration
Interoperability configuration
Automatic deployment
The following is achieved via iMaster NCE-Campus GUI:
Unified fabric deployment and automated VXLAN tunnel setup via the BGP EVPN control plane
Fully automated VN construction
Centralized service configuration, automatic service provisioning
Automatic construction of virtual networks (VNs), implementing a multi-purpose network
OA VN
R&D VN
IoT VN
The following is achieved via iMaster NCE-Campus GUI:
Planning of user groups and inter-group policies
Automated policy delivery
Free mobility, which delivers unified policies and consistent service experience to users, regardless of their access locations
Student
Teacher
Teaching server

## Slide 11: CloudCampus — Intelligent Campus Network O&M
Huawei CloudCampus Solution introduces iMaster NCE-CampusInsight (campus network analyzer) to change the traditional monitoring mode that focuses on resource status. iMaster NCE-CampusInsight visualizes data by user, application, and time, identifies potential faults, and locates root causes, improving user experience.
Full-journey experience visibility for each user, at each moment
Automatic identification of network issues
Intelligent demarcation and root cause analysis of network issues
Uses the standard telemetry technology in the industry to dynamically obtain network KPI data in seconds, facilitating fault tracing.
Collects data from multiple dimensions, displays network profiles of all users in real time, and visualizes network experience (who, when, which AP to connect, experience, and problem) throughout the journey.
Uses big data and AI technologies to automatically identify connectivity, air interface performance, roaming, and device issues, improving the identification rate of potential issues by 85%.
Dynamically generates a baseline through historical data that is learned using machine learning, and compares the baseline with real-time data and analyzes it to predict potential faults.
Intelligently identifies the issue pattern and impact range based on the network O&M expert system and various AI algorithms, helping administrators locate faults.
Analyzes possible issue causes based on the big data platform and provides rectification suggestions.

## Slide 12: Network Architecture of the CloudCampus Solution — Large- and Medium-Sized VXLAN-based Virtualized Campus Networks
The following figure shows the typical network architecture of the CloudCampus Solution for a large- or medium-sized campus network. The network architecture consists of the network layer, management layer, and application layer.
Application layer
Network layer
Management layer
MDM
e-Schoolbag
Asset management
Health management
AAA
…
Intelligent OAM
VN 1
VN 3
VN 2
VN
Internet/
WAN
Native AC
AP
Switch
Switch
Switch
Switch
Switch
Firewall
Physical network
Open APIs
SNMP
NETCONF/
YANG
Telemetry
Notes: Network layer
  Virtualization technologies are introduced to divide the network layer into a physical network and a virtual network.
    Physical network: is also called the underlay network and provides basic connection services for campus networks. To meet access requirements of multiple types of terminals, the physical network provides a unified three-network access capability, and allows access of wired, wireless, and IoT terminals simultaneously.
    Virtual network: is also called the overlay network. Virtualization technology is used to construct one or more overlay networks over the underlay network. Service policies are deployed on the overlay networks and are separated from the underlay network, decoupling services from networks. Multiple overlay networks can serve different services or customer segments.

## Slide 13
Notes: Management layer
  The management layer provides network-level management capabilities, such as configuration management, service management, maintenance and fault detection, and security threat analysis. Traditional campus networks use a network management system (NMS) for network management. Although the NMS can display the network status, it lacks flexible and automatic management capability. Once service requirements change, the network administrator needs to re-plan services and manually modify configurations on network devices (including routers, switches, and firewalls), which is inefficient and error-prone. Therefore, to maintain network flexibility is critical in rapidly changing service environments, which requires the use of automation tools to assist in network and service management. Huawei's CloudCampus Solution uses iMaster NCE-Campus to implement automatic network and service provisioning.
  iMaster NCE-Campus abstracts network devices and applications, and rapidly develops and automatically deploys applications through orchestration and by invoking abstract models. iMaster NCE-Campus illustrates the entire network but not independent devices (such as switches, routers, and APs) or discrete configurations (such as access control, QoS, and routing policies) on devices.
Application layer
  The CloudCampus Solution provides standard APIs based on iMaster NCE-Campus. Through these APIs, the solution opens up various information, such as user identities, network resources, service quality, network location information, and network topology, to upper-layer services. Third parties can use these APIs to customize innovative service applications based on their service requirements, meeting service requirements in multiple fields, such as education, business, enterprise, and government.

## Slide 14: VXLAN-based Virtualized Campus Network Layers and Related Concepts
Overlay (virtual network layer)
Underlay (physical network layer)
Fabric
Border
Edge
Edge
Access
Access
VN 1
VN 2
VN 3
Sets up a physical network with physical devices
Provides interconnection and interoperability capabilities for all services in the campus
Serves as the basic network for service data forwarding
Uses virtualization technology to build a logical topology over any physical underlay topology
Creates service networks on the fabric to realize decoupling from the physical network
Creates multiple VNs based on service requirements to implement service isolation
Implements Layer 2 and Layer 3 communication via VXLAN
Notes: Physical network layer: also called underlay network. It is a physical topology consisting of physical network devices (such as switches, APs, firewalls, and routers) to provide interconnection and interoperability capabilities for all services on a campus network, building the basic network for campus service data forwarding.
Fabric: is a fully-connected logical topology built over a physical underlay topology using VXLAN technology. A service network is created on the fabric to decouple the service network from the physical network. When the service network needs to be adjusted, the physical network topology does not need to be changed.
Virtual network layer: also called overlay network. It is abstracted from the physical network layer through virtualization technologies to group physical network resources into a network resource pool that can be flexibly scheduled by the service layer. Multiple VNs can be created on a fabric based on service requirements to isolate services. On a traditional campus network, to isolate services, the OA network and security network are designed as two independent physical networks. On a virtualized network, physical network sharing is implemented through the overlay. That is, two VNs can be created and used as the OA network and security network for service isolation.

## Slide 15
VXLAN-based Virtualized Campus Network and Solution
Underlay Design
Fabric Design
Overlay Design
Admission Control and Free Mobility Design
WLAN Design
O&M Design

## Slide 16: Underlay Design Outline
1. Network architecture and topology design
Network architecture selection
Hierarchical model design
Hierarchical networking design
Network egress design
2. Basic service design
VLAN planning
IP address planning
DHCP service design
Route design
3. LAN automation design
Network deployment design
Automatic orchestration of underlay routes

## Slide 17: Overview of the Network Architecture
Egress zone: the border between the internal and external networks. This zone allows internal users to access the external network, and likewise, enables external users (including customers, partners, branch users, and remote users) to access the internal network. Network security and WAN access are the focuses during egress zone design.
DC zone: used to deploy servers and application systems. It provides data and application services for both internal and external users.
O&M zone: used to deploy network management servers, such as the NMS and authentication servers.
Core layer: the backbone of a campus network. It is the core for data switching and connects all parts on the campus network, such as the data center, O&M zone, and egress zone.
Aggregation layer: located at the intermediate layer of a campus network. It aggregates or switches data and provides key basic network functions, such as routing, QoS, and security.
Access layer: the first layer for terminals to access a campus network. It provides the campus network access function for end users.
Terminal layer: Various terminals connecting to a campus network are located at this layer.
Network Architecture and Topology Design
Basic Service Design
LAN Automation Design
iStack/CSS cables
Egress zone
Core layer
Aggregation layer
Access layer
Terminal layer
Internet
WAN
O&M zone
DC
Notes: Large- and medium-sized campus networks often use the tree topology with the core layer as the root. The topology in the figure is stable and easy to expand and maintain. A campus network can be divided into the following layers: access layer, aggregation layer, core layer, and multiple zones including the egress zone, DC zone, and O&M zone. Internal changes in a module do not affect other modules, facilitating fault location.
Terminal layer
  The terminal layer involves various terminals that access the campus network, such as PCs, printers, IP phones, mobile phones, and cameras.
Access layer
  The access layer provides various access modes for users and is the first network layer for terminals to access a campus network. The access layer is usually composed of access switches. There are a large number of access switches that are sparsely distributed in different places on the network. In most cases, an access switch is a simple Layer 2 switch. If the terminal layer has wireless terminals, the access layer has APs that access the network through access switches.
Aggregation layer
  The aggregation layer connects the access layer to the core layer. The aggregation layer forwards horizontal traffic between users and forwards vertical traffic to the core layer. It can also function as the switching core for a department or zone and connect the department or zone to the exclusive server zone. In addition, the aggregation layer can further extend a quantity of access terminals.

## Slide 18
Notes: Core layer
  The core layer is the core of data exchange on a campus network. It connects to various components of the campus network, such as the DC zone, aggregation layer, and egress zone. The core layer is responsible for high-speed interconnection of the entire campus network. High-performance core switches need to be deployed to meet network requirements for high bandwidth usage and fast convergence upon network faults. It is recommended that the core layer be deployed if a campus has more than three departments. For a wireless network, the core layer includes ACs. After a wireless terminal accesses the wireless network through an AP, the AP communicates with the AC by using a Control and Provisioning of Wireless Access Points (CAPWAP) tunnel.
Egress zone
  The campus egress is the edge that connects a campus network to an external network. Internal users of the campus network can access the external network through the campus egress zone, and external users can access the internal network through the campus egress zone. Routers and firewalls need to be deployed in the campus egress zone. The routers enable interconnection between internal and external networks, and the firewalls provide border security protection.
DC zone
  In the DC zone, service servers such as the file server and email server are managed, and services are provided for internal and external users.
O&M zone
  In the O&M zone, network servers such as the network management system and authentication server are managed. The standard NMS interacts with network devices through the Simple Network Management Protocol (SNMP) and provides configuration, management, and maintenance functions. For example, it provides network topology and port display management, network device configuration management, network fault diagnosis and alarm, and network performance and status analysis. Huawei CloudCampus solution provides intelligent O&M based on NETCONF and telemetry.
In addition to these, a campus may have a demilitarized zone (DMZ). It provides access services with strictly controlled security for external guests (personnel other than the enterprise employees). Public servers are usually deployed in the DMZ.

## Slide 19: Network Architecture Selection
In actual applications, you can choose the three-layer or two-layer architecture based on the network scale or service requirements.
Block 1
Block N
Three-layer architecture
Two-layer architecture
Core layer
Aggregation layer
Access layer
Core layer
Access layer
Scenario: large campus networks with a large number of users or involving multiple buildings, for example, high education campus networks
Scenario: small- and medium-sized campus networks involving one building
Hierarchical design
Modular design
Redundancy design
Symmetry design
Network Architecture and Topology Design
Basic Service Design
LAN Automation Design
Notes: Hierarchical design
  Each layer can be considered as a well-structured module with specific role and function. This layered structure is easy to expand and maintain, simplifying the design.
Modular design
  Each module corresponds to a department, function, or service zone. Modules can be expanded flexibly based on the network scale, and adjustment in a department or zone covers a small scope, which facilitates fault locating.
Redundancy design
  Dual-node redundancy design can ensure device-level reliability. Appropriate redundancy improves reliability, but excessive redundancy makes O&M difficult. If dual-node redundancy cannot be implemented, you may consider card-level redundancy, such as dual main control boards or switch fabric units (SFUs), for modular core switches or egress routers. In addition, Eth-Trunk can be deployed to ensure link-level reliability of important links.
Symmetry design
  The symmetric network structure makes the topology more clear and facilitates service deployment, and protocol design and analysis.

## Slide 20: Hierarchical Model Design
During network design, you can use the bottom-up method to determine the type of architecture required based on the network scale.
1. Determine the number of access ports
2. Select access switches
3. Calculate the number of access switches required
4. Select aggregation switches
5. Calculate the number of uplinks of access switches
6. Calculate the number of aggregation switches required
Three-layer architecture
Two-layer architecture
Single-layer architecture
If a single port corresponds to a single user or a specific number of users, the number of access ports required can be estimated based on the network scale.
Determine the appropriate access switches (including access capability, port density, and uplink mode) based on the port rates of terminals' NICs.
Quantity = Number of access ports/Number of downlink ports on a switch
Select the appropriate aggregation switches based on the uplink port rates of access switches.
Quantity = Required network bandwidth/Uplink port rate of an access switch
Quantity = (Number of access ports x Access port rate x Bandwidth oversubscription ratio)/Uplink port rate of an access switch
Quantity = Number of uplinks of access switches/Number of aggregation switch downstream ports
N
Y
Y
N
Network Architecture and Topology Design
Basic Service Design
LAN Automation Design
Quantity >1？
Quantity >1？
Notes: Design method of the hierarchical model for common network architectures:
  Determine the number of ports on access switches based on the network scale. Generally, one port corresponds to one terminal or one network access point (for example, AP).
  Select switches based on the port rates of terminals' NICs.
  Calculate the number of access switches.
    Number of access switches required = Number of access ports/Number of downlink ports on a switch
    If the calculation result is greater than 1, aggregation switches need to be deployed. Otherwise, use the single-layer architecture.
  Select aggregation switches based on the uplink port rates of access switches.
  Calculate the number of uplinks of an access switch using either of the following methods:
    Based on the network bandwidth: Number of uplinks = Network bandwidth/Uplink port rate of an access switch
    Based on the network scale: Number of uplinks = Number of access ports x Access port rate x Bandwidth oversubscription ratio/Uplink port rate of an access switch

## Slide 21
Notes:   Calculate the number of aggregation switches.
  Number of aggregation switches required = Number of uplinks of access switches/Number of aggregation switch downstream ports
  If the number is greater than 1, select the three-layer architecture. Otherwise, use the two-layer architecture.
Note:
  In the preceding calculations, the calculation results need to be rounded up.
  Bandwidth oversubscription ratio = Actual downstream bandwidth of a service/Maximum physical bandwidth provided by a single switch
    Traffic of the service may exhaust the maximum physical bandwidth. However, this probability is low in most cases. Generally, network planning focuses on service experience in common situations. That is, certain bandwidth redundancy is designed when actual possible bandwidth is met.
    Before designing a network traffic oversubscription ratio, we need to understand the service applications and features to be deployed on the network and to determine the network services and traffic models. Additionally, the volume and ratio of traffic must be thoroughly considered for the design of a suitable oversubscription ratio and selection of suitable devices.

## Slide 22: Hierarchical Networking Design
Stacking core networking
Dual-core networking
Core layer
Aggregation layer
Access layer
Stacking
Eth-trunk
Loop-free networking: There is no need to deploy complex ring network protocols or reliability protocols. This networking ensures device-level and link-level reliability, simplifies the network topology, and reduces deployment and maintenance workload.
Equal-cost load balancing and redundancy
Unlike the stacking core networking that has only one core from the service perspective, dual-core networking has two cores. The aggregation layer can have two equal-cost routes to the core switches at the same time. During the upgrade of core switches, services are not interrupted. To simplify O&M, stacking core networking is recommended. If the customer is sensitive to service interruption, the dual-core networking is recommended.
Equal-cost load balancing and redundancy
Network Architecture and Topology Design
Basic Service Design
LAN Automation Design
Notes: To simplify O&M, stacking core networking is recommended. If customers are sensitive to service interruption, dual-core networking is recommended.
Two-Layer networking on large- and medium-sized campus networks typically uses stacking core networking.

## Slide 23: Network Egress Design
As the boundary between the campus network and external network (including the Internet and WAN), the egress zone is responsible for communication and security protection between internal and external networks.
The requirements for the egress zone design are as follows:
  Network connectivity: Internal users can access the external network. If the campus network provides access for external users, external users must be allowed to access the campus network.
  Network security: To ensure that the campus network is secure and controllable, especially border security, firewalls and the Intrusion Prevention System (IPS) devices must be configured. Security components are selected based on security requirements and investment scales.
  Flexible access modes: Various access modes are provided, including wired or wireless access on the LAN side and access on the WAN side.
  Strong service control capability: Service deployment and isolation are easy, and various VPN access modes are provided, including IPsec VPN, SSL VPN, and MPLS VPN.
Core layer
Aggregation layer
Access layer
iStack/CSS link
O&M zone
DC
O&M zone
Internet
WAN
Egress zone
Network Architecture and Topology Design
Basic Service Design
LAN Automation Design

## Slide 24: Egress Network Service Scenarios
Internet
Egress zone
Security
NAT
Remote access
Multi-campus interconnection
Security
Multi-campus interconnection
WAN
Service Scenario | Sub-scenario | Description | Applicable Network
Security | Firewall | A firewall uses security zones to divide networks and identify packet forwarding paths. When a packet is transmitted between security zones, the firewall can perform a security check and enforce corresponding security policies. | Internet and leased line
 | URL filtering | URL filtering controls internal users’ access to external URLs. It allows or forbids users to access certain web page resources to standardize online behaviors. | Internet
NAT | Source NAT | Intranet users usually use private IP addresses to access the Internet. To ensure successful access to Internet services, private IP addresses must be translated into public IP addresses. | Internet
 | NAT server | Servers deployed on the campus network, such as the file server, can be mapped to the Internet using public IP addresses or public IP addresses and port numbers through the NAT server for Internet access. | Internet
Remote access | SSL VPN access | The SSL VPN gateway connects to the Internet and provides SSL VPN services for mobile office users (employees on business trips). After a mobile user uses a terminal (such as a laptop or smart phone) to establish an SSL VPN tunnel with an enterprise intranet gateway, the user can remotely access intranet resources such as the web server, file server, and mail server through the SSL VPN tunnel. | Internet
Multi-campus interconnection | Traditional MPLS VPN interconnection | CE switches can be connected to the private line MPLS VPN network. | Leased line
 | IPsec VPN interconnection | IPsec VPN tunnels are established between multiple campuses to ensure secure data transmission on a low-security bearer network. | Internet and leased line
Network Architecture and Topology Design
Basic Service Design
LAN Automation Design

## Slide 25: Network Egress Design: WAN-side Interconnection
Internet
WAN
Internet
Internet2
/WAN
Internet1
Optional
WAN
Internet
WAN
Internet
LTE
Single AR and single egress
Single AR and dual egresses
Dual ARs and single egress
Dual ARs and dual egresses
Dual ARs and multiple egresses
Optional
Optional
Optional
Optional
AR egress
Firewall egress
Internet
WAN
Internet
Internet2
/WAN
Internet1
Internet2
/WAN
Internet1
Single firewall and single egress
Single firewall and dual egresses
Dual firewalls and single egress
Dual firewalls and dual egresses
Hot standby heartbeat link
Interlink
The following factors need to be considered during WAN-side interconnection design
Egress link type
SD-WAN requirements
Protocol interconnection requirements
Network Architecture and Topology Design
Basic Service Design
LAN Automation Design
Notes: To ensure reliability, routers and firewalls are usually deployed in redundancy mode. It is recommended that devices be deployed in redundancy mode at the egress of a large- or medium-sized campus network.
WAN-side interconnection design:
  Egress link type
    Ethernet: Select the firewall as the egress.
    For non-Ethernet links, such as EI, CE1, and CPOS links, select the AR as the egress.
  SD-WAN requirements:
    If there are SD-WAN requirements, select the AR as the egress.
    If there is no SD-WAN requirement, select the firewall as the egress.
  Protocol interconnection requirements:
    If BGP runs between the egress device and the external network, it is recommended that the AR be used as the egress. This is because the routing table size and performance of the router are more powerful and many routing policies need to be deployed on the egress device.

## Slide 26: Network Egress Design: LAN-side Interconnection
CSS
A single firewall is connected to a single border node
Two firewalls are connected to a CSS composed of border nodes in square-looped mode
CSS
A single AR is connected to a single border node
Two ARs are connected to a CSS composed of border nodes in square-looped mode
CSS
Two firewalls are connected to a CSS composed of border nodes in dual-homed mode
CSS
Two ARs are connected to a CSS composed of border nodes in dual-homed mode
LAN-side interconnection design
On large- and medium-sized campus networks, border nodes are usually deployed in cluster or stack mode and virtualized into one logical switch to ensure reliability of core switches.
Egress gateways are usually deployed in a two-node cluster to meet reliability requirements. For different types of gateways, such as firewalls or ARs, the two-node cluster deployment capabilities are slightly different. For example, the hot standby link between the active and standby firewalls is used only for heartbeat and entry hot backup, but is not used as a traffic forwarding channel. The interlink between ARs (gateways) can be used as a service interconnection channel and can implement information synchronization and backup between them.
It is recommended that egress gateways and border nodes be connected in dual-homed mode and link aggregation be used to enhance the reliability and forwarding bandwidth of the link layer between devices.
Hot standby heartbeat link
Interlink
Stack
Link aggregation
Network Architecture and Topology Design
Basic Service Design
LAN Automation Design
Notes: Note: The interlink can be used as the interconnection link between two ARs (gateways) to forward different service (VPN) traffic between devices through sub-interfaces.

## Slide 27: Network Egress Design: Firewall Deployment in Off-path Mode
Deploying firewalls in off-path mode
In the egress zone, firewalls can be connected to border nodes in off-path mode. Generally, off-path deployment of firewalls is selected based on the following principles:
  Whether traffic passes through a firewall can be flexibly defined.
  Expansion is easy, including the reconstruction of the original network and the expansion and reconstruction of the new network.
  A firewall fault has little impact on services.
On a campus network:
  If a firewall is used as the egress gateway to connect to the carrier network, the firewall usually provides functions such as security policies, NAT, and VPN gateway. The north-south traffic must pass through the firewall. In this case, if scalability is not considered, in-path deployment is recommended.
  If the AR is used as the egress gateway to connect to the carrier network, the firewall is used only for high-level security functions, such as intrusion prevention, antivirus, and URL filtering. Off-path deployment can be used based on the preceding principles.
Hot standby heartbeat link
Stacking
Link aggregation
Two firewalls are connected to border nodes in off-path mode
WAN
Internet
OA PC1
OA PC2
R&D PC3
Traffic from PC1 to the Internet
Traffic from PC2 to PC3
Interlink
Network Architecture and Topology Design
Basic Service Design
LAN Automation Design

## Slide 28: VLAN Design
You are advised to assign consecutive VLAN IDs to ensure proper use of VLAN resources.
You are advised to reserve a certain number of VLANs for future expansion.
VLANs are classified into service VLANs, management VLANs, and interconnection VLANs.
Typically, VLANs are divided based on interfaces. According to different design principles, interfaces of access switches are added to different VLANs so that users of different service types can be isolated.
Service VLAN design
Management VLAN design
VLAN assignment based on geographical areas
VLAN assignment based on logical areas
VLAN assignment based on the personnel structure
VLAN assignment based on service types
Management VLAN 100
VLANIF 100
192.168.100.1
VLANIF 100
192.168.100.2
VLANIF 100
192.168.100.254
In most cases, a Layer 2 device uses the VLANIF interface's IP address as the management IP address. It is recommended that all Layer 2 switches use the same management VLAN and their management IP addresses be on the same network segment.
Network Architecture and Topology Design
Basic Service Design
LAN Automation Design
Notes: Service VLAN:
  Assign VLANs by logical area, geographical area, personnel structure, or service type.
    Assign VLANs by logical area. For example, VLANs 100 to 199 are used in the core network zone, VLANs 200 to 999 are used in the server zone, and VLANs 2000 to 3499 are used on the access network.
    Assign VLANs by geographical area. For example, VLANs 2000 to 2199 are used in area A, and VLANs 2200 to 2399 are used in area B.
    Assign VLANs by personnel structure. For example, department A uses VLANs 2000 to 2009, and department B uses VLANs 2010 to 2019.
    Assign VLANs by service type. For example, VLANs 200 to 299 are used in the web server zone, VLANs 300 to 399 are used in the app server zone, and VLANs 400 to 499 are used in the database server zone.
  If users are sensitive to the voice latency, the voice service must be preferentially guaranteed. It is recommended that the voice VLAN be planned for the voice service. Huawei switches can automatically identify voice data, transmit voice data in the voice VLAN, and perform QoS guarantee. When network congestion occurs, voice data can be preferentially transmitted.

## Slide 29
Notes:   If different users have the same multicast data service, you are advised to plan a multicast VLAN and bind the user VLANs to the multicast VLAN. By doing this, the uplink gateway does not copy multicast data in multiple user VLANs.
  VLAN 1 is not recommended as the service VLAN.
Management VLAN:
  It is recommended that the management VLAN be planned for a Layer 2 switch and the VLANIF interface of the management VLAN be used as the management interface. The NMS uses this interface to manage the switch. It is recommended that all Layer 2 switches use the same management VLAN.
  It is recommended that service interfaces be used as management interfaces on Layer 3 devices (gateways or higher-level devices), and no management VLAN needs to be planned.
Interconnection VLAN:
  An interconnection VLAN is usually configured between two Layer 3 switches or between a Layer 3 switch and a router. VLANIF interfaces are created for Layer 3 interconnection.

## Slide 30: IP Address Design
The IP addresses of the campus network are classified into service, management, and interconnection IP addresses.
Management IP address
A Layer 2 device uses the VLANIF interface's IP address as the management IP address. It is recommended that all Layer 2 switches connected to a gateway be on the same network segment.
Management VLAN 100
VLANIF 100
192.168.100.1
VLANIF 100
192.168.100.2
VLANIF 100
192.168.100.254
Service and interconnection IP addresses
Service IP addresses are the IP addresses of servers, hosts, and gateways.
You are advised to use the same last octet as the gateway IP address, for example, .254.
The IP address range of each service must be clearly distinguished. The IP addresses for each type of service terminals must be continuous and can be aggregated.
You are advised to use an IP address segment with a 24-bit mask.
It is recommended that the interconnection IP address use a 30-bit mask. The core device uses a smaller host IP address.
Employee
192.168.40.0/24
Partner
192.168.50.0/24
Guest
192.168.100.0/24
VLANIF 200: 192.168.200.1/30
VLANIF 200: 192.168.200.2/30
Interconnection VLAN 200
Service VLAN 40/50/100
VLANIF 40: 192.168.40.254
VLANIF 50: 192.168.50.254
VLANIF 100: 192.168.100.254
Network Architecture and Topology Design
Basic Service Design
LAN Automation Design
Notes: IP address planning complies with the following principles:
  Uniqueness: Each host on an IP network must have a unique IP address.
  Contiguousness: Node addresses of the same service must be contiguous to facilitate route planning and summarization. Contiguous addresses facilitate route summarization, reducing the size of the routing table and speeding up route calculation and convergence.
  Scalability: IP addresses need to be reserved at each layer. When the network is expanded, no address segments or routes need to be added.
  Easy maintenance: Device and service address segments need to be clearly distinguished from each other, facilitating subsequent statistics monitoring and security protection based on address segments. IP addresses can be planned based on VLANs.
Pay attention to the following points when designing the three types of IP addresses:
  Service IP address:
    Considering the scope of a broadcast domain and easy planning, it is recommended that an IP address segment with a 24-bit mask be reserved for each service. If the number of service terminals exceeds 200, another IP address segment with a 24-bit mask is reserved.

## Slide 31
Notes:   Management IP address:
    It is recommended that a Layer 3 device use a Layer 3 interface for management and deployment. The interface address is used as the management IP address for local login and interworking with the controller.
  Interconnection IP address:
    Interconnection addresses are usually aggregated before being advertised. Therefore, you need to use contiguous and aggregatable addresses during planning.
In addition, if devices at the aggregation and access layers are interconnected, you need to plan IP addresses for policy association in some cases. The IP addresses must be planned based on the entire CloudCampus network and cannot conflict with other service IP addresses.

## Slide 32: DHCP Service Design
DHCP service oriented to terminals:
  Plan an independent DHCP server to allocate IP addresses to terminals.
  You are advised to configure DHCP snooping on access devices to defend against attacks.
  Network administrators can use either of the two mechanisms to assign IP addresses to hosts based on network requirements:
    Dynamic IP address assignment: An IP address with a lease is assigned to a host. This mode applies to scenarios where hosts require temporary access or IP addresses are insufficient. For example, IP addresses are assigned to portable computers of traveling employees and mobile terminals in cafes.
    Static IP address assignment: Fixed IP addresses are assigned to specified hosts or servers such as DNS servers.
  In the address pool planning, static IP addresses must be filtered out.
  The lease needs to be planned based on the online duration of a client.
  In most cases, the DHCP server and hosts on a large or midsize campus network are not on the same network segment. Therefore, you are advised to enable the DHCP relay function on the gateway.
DHCP server
DHCP client
Network Architecture and Topology Design
Basic Service Design
LAN Automation Design
Notes: Note: It is recommended that core switches provide the DHCP service for network deployment. For details, see the network deployment section.

## Slide 33: Routing Design
Three-layer networking: scenario 1
Three-layer networking: scenario 2
OSPF area 0
OSPF area 1
OSPF area 2
Core (border)
Aggregation
Access (edge)
OSPF area 0
Core (border)
Aggregation
Access (edge)
Three-layer networking:
  Scenario 1 (multi-area): The interconnection links between core switches belong to OSPF area 0, and the interconnection link with each aggregation switch belongs to an independent OSPF area.
  Scenario 2 (single-area): Core, aggregation, and access switches all work in OSPF area 0. If the number of switches to be deployed in a network area is fewer than 100, scenario 2 is recommended.
  Two-layer networking:
  OSPF runs only between core switches and access switches. In this case, only OSPF area 0 needs to be planned on the entire network.
Network Architecture and Topology Design
Basic Service Design
LAN Automation Design
CSS/iStack link
Notes: The routing design includes internal and egress routing design of a campus network.
  Internal routing design:
    The routing design must support communication between devices, between terminals, and between devices and terminals on the campus network, as well as communication between these devices and the Internet and between terminals and the Internet.
    It is recommended that you design internal routes based on the gateway location.
      If gateways are deployed at the aggregation layer, routes need to be deployed at core and aggregation layers. Routing tables can be dynamically updated along with network topology changes, so an Interior Gateway Protocol (IGP), such as Open Shortest Path First (OSPF), is recommended.
      If gateways are deployed at the core layer, you only need to configure routes at the core layer. It is recommended that static routes be used preferentially.

## Slide 34
Notes:   Egress routing design:
    Egress routes must meet requirements of internal terminals for accessing the Internet and WAN.
    A large or medium-sized campus network usually has a large number of branches. The egress needs to support multiple links for Internet access and mutual communication between enterprise branches. For this purpose, a large number of routes need to be imported to the campus network. Therefore, you are advised to plan a dynamic routing protocol such as OSPF.
It is recommended that OSPF be planned for a campus network. The OSPF design precautions are as follows:
  You are advised to use the IP addresses of loopback interfaces as the router IDs.
  Areas are divided according to the core, aggregation, and access layers. It is recommended that egress routers and core switches be deployed in the backbone area. The design of non-backbone areas depends on the geographical location and device performance.
Note:
  This slide describes the routing design in the scenario of VXLAN to the access layer.
  In the scenario of VXLAN to the aggregation layer, the routing design (for example, OSPF area division design) is the same as that in the scenario of VXLAN to the access layer. The difference is that the aggregation device is the border of the routing domain.

## Slide 35: Network Deployment Design
CSS/iStack link
Native AC
Core
Aggregation
Access
Traditional deployment
Plug-and-play
Traditional deployment (via CLI or web system):
Egress router
Egress firewall
Core switch
Plug-and-play
Aggregation switch
Access switch
AP
Network Architecture and Topology Design
Basic Service Design
LAN Automation Design
Notes: Typically, egress and core devices on large- and medium-sized campus networks are centrally deployed in a core equipment room. Services transmitted on these devices are complex and their locations on the network are important. In most cases, network engineers need to commission devices onsite during the deployment. Therefore, you are advised to use web system or CLI to deploy devices at the core layer and upper layers (including core devices, standalone ACs in off-path mode, and egress devices).
A large number of devices (including aggregation devices, access devices, and APs) are deployed at lower layers of the core layer, and service configurations are similar. Therefore, plug-and-play deployment is recommended to simplify deployment.
  You are advised to use the DHCP option mode to achieve plug-and-play deployment.
  In DHCP option-based plug-and-play deployment, IP addresses and DHCP options (IP address of iMaster NCE-Campus configured using Option 148 and IP address of the AC configured using Option 43) required by devices are configured on the DHCP server. After a device goes online, it automatically obtains the management IP address and DHCP Option from the DHCP server, and then automatically registers with iMaster NCE-Campus. The switches at lower layers of the core layer register with iMaster NCE-Campus through DHCP Option 148, and APs register with the AC through DHCP Option 43.

## Slide 36: Recommended Deployment Modes
Location | Device | Recommended Deployment Mode | Remarks
Egress | Router | Local CLI or web system | -
 | Firewall | Local CLI or web system | -
Core layer | Core switch | Local CLI | -
 | Standalone AC | Web system | Alternative: DHCP Option 148
Aggregation layer | Aggregation switch | DHCP Option 148 | Alternative: CLI
Access layer | Access switch | DHCP Option 148 | Alternative: CLI
 | AP | DHCP Option 43 | Alternative: CLI
Network Architecture and Topology Design
Basic Service Design
LAN Automation Design
Notes: Note: Switches at the core layer obtain IP addresses through the local CLI to complete network deployment. After a management channel is established between the core switch and controller, services are automatically delivered by the controller.

## Slide 37: Network Deployment: DHCP-based, Plug-and-Play of Network Devices
The network administrator has deployed the DHCP service on the network in advance. (It is recommended that the DHCP service be deployed on the core switch.)
For devices to be deployed, the DHCP server not only delivers IP address to them, but also uses DHCP Option 148 to notify them of the IP address and port number of the cloud management platform.
Core switch
1
2
DHCP Request message
3
DHCP Reply message, which carries information such as the IP address, DNS and working mode, and Option 148 (IP address and port number of the controller)
4
Proactively initiate a registration with the cloud management platform
Device types supported: AR router, switch, and AP
Switch to be deployed
Network Architecture and Topology Design
Basic Service Design
LAN Automation Design
Notes: The network administrator first deploys the DHCP server and configures Option 148. The network administrator enters the mode type (cloud mode), controller domain name or address, and port number into Option 148. After obtaining such information through DHCP, network devices can automatically register with the controller.
  The core switch at a tenant's site can function as the DHCP server. You can configure the DHCP server function and Option 148 on the core switch. If possible, a third-party DHCP server can also be used.
  After a network device at a site starts, it obtains parameters such as the IP address through DHCP and obtains parameters such as the running mode, controller IP address, and port number through Option 148. The device automatically restarts, switches to the cloud mode, and applies for an IP address again. After the device in cloud mode obtains an IP address, it automatically sends a registration request to the controller.

## Slide 38: Network Deployment Process: Complete Device Onboarding and Planning in Sequence
Core
Aggregation
(device to be deployed)
Internet
Egress gateway
(DHCP server)
Preparation
An administrator deploys the DHCP server function on the egress gateway or deploys an independent DHCP server on the network, and then configures DHCP Option 148.
The administrator configures the core switch so that it can be managed by iMaster NCE-Campus.
Switch Onboarding
After an aggregation switch is powered on, it proactively sends Link Layer Discovery Protocol Data Units (LLDPDUs) to the core switch to negotiate with the core switch and obtain the PnP VLAN.
The aggregation switch uses the PnP VLAN to obtain an IP address and Option 148 from the DHCP server.
The aggregation registers with iMaster NCE-Campus based on iMaster NCE-Campus information obtained from the DHCP server.
After an access switch is powered on, it follows a similar process as the aggregation switch.
The administrator imports switch information (such as the ESN and device model) to iMaster NCE-Campus (batch import is supported).
Switches use LLDP to discover the network topology and report their topology information to iMaster NCE-Campus through NETCONF. iMaster NCE-Campus then discovers the network topology based on such topology information.
The administrator performs network planning and configuration provisioning on iMaster NCE-Campus.
Access
(device to be deployed)
Network Architecture and Topology Design
Basic Service Design
LAN Automation Design
Notes: In the Huawei's CloudCampus Solution, a DHCP server helps implement plug-and-play deployment of switches, removing the need to manually enable the Network Configuration Protocol (NETCONF) and configure iMaster NCE-Campus's address information.
  An unconfigured switch starts and sends a Request message containing VLAN 1 to the DHCP server.
  A user-defined VLAN can be used by the device to initiate a DHCP request. This VLAN is called plug and play (PnP) VLAN.
In this example, assume that another VLAN but not VLAN 1 is used as the PnP VLAN. You need to configure the PnP VLAN on the core switch or configure the PnP VLAN on iMaster NCE-Campus after the core switch registers and is managed by iMaster NCE-Campus.
During network deployment, the administrator uses the preceding methods to deploy and onboard devices.
  If there are aggregated links between the devices, redundant links will be blocked by STP because link aggregation has not been configured when the devices are installed and onboarded. After the devices are onboarded and register with the controller, the administrator checks the topology and deploys link aggregation and service configurations on the controller.
This deployment process applies to the scenario where the installation time is scattered.

## Slide 39: Network Deployment Process: Complete Planning and Device Onboarding in Sequence
Core
Aggregation
(device to be deployed)
Internet
Egress gateway
(DHCP server)
Preparation
An administrator deploys the DHCP server function on the egress gateway or deploys an independent DHCP server on the network, and then configures DHCP Option 148.
The administrator configures the core switch so that it can be managed by iMaster NCE-Campus.
The administrator plans the network topology using the template (an Excel file) provided by iMaster NCE-Campus and then imports the template with the planning data to iMaster NCE-Campus.
Switch Onboarding
After aggregation and access switches are powered on, they complete PnP VLAN negotiation and DHCP message exchange processes, and then register with iMaster NCE-Campus.
Aggregation and access switches are then managed by iMaster NCE-Campus and report LLDP neighbor information to iMaster NCE-Campus. Subsequently, iMaster NCE-Campus compares such LLDP information with that in the network topology planning document uploaded by the administrator. If any inconsistency is found, an error is reported. In this way, the administrator can correct the topology information error as prompted.
The administrator performs offline pre-configuration on iMaster NCE-Campus.
Switches automatically obtain the configuration after onboarding.
Access
(device to be deployed)
Network Architecture and Topology Design
Basic Service Design
LAN Automation Design
Notes: This deployment process is applicable to the scenario where the installation time is centralized. The administrator is advised to plan the network first and then onboard devices. If the network cannot be planned in advance, the administrator can onboard devices and then determine the network topology.
Plan the network first, and then onboard devices.
  During network deployment, the administrator enters device ESNs and specifies stack members and aggregated links on the controller to complete network topology planning.
  Alternatively, the administrator can import the preceding planning information in batches using a template. Using a template to import data in batches simplifies operations and is therefore recommended.
  Then, the administrator uses the preceding methods to deploy and onboard devices.
  After devices go online and register with the controller, the controller automatically checks whether the actual topology of the devices is the same as the planned one. If cables are incorrectly connected during installation, the controller immediately notifies the administrator.
Note: Parameters can be planned for an Eth-Trunk interface. After a device goes online, the corresponding Eth-Trunk configuration is automatically obtained.

## Slide 40: Automatic Orchestration of Underlay Routes on the LAN
Interconnection VLAN
Interconnection IP address
Interconnection VLAN
Interconnection IP address
IGP (OSPF)
Define VLAN IDs or IP addresses
Define a fabric
Edge
Edge
Border
Enable automatic orchestration of underlay routes
iMaster NCE-Campus automatically calculates the topology, partitions OSPF areas, and configures interconnection addresses and routes for communication between VTEPs.
The network administrator can select single-area orchestration or multi-area orchestration based on the network scale. When the number of devices in the network area where routes need to be deployed on the underlay network is fewer than 100, single-area orchestration is recommended. Otherwise, multi-area orchestration is recommended.
Define loopback interface address
2
3
4
1
5
Device Interconnection VLAN
Device interconnection IP address
Loopback interface IP
Network Architecture and Topology Design
Basic Service Design
LAN Automation Design
Notes: The following network resources need to be planned for underlay automation:
  Network scope for the fabric: Devices are connected through VLANIF interfaces at Layer 3. Each interconnection link is assigned a VLAN.
  IP addresses of the VLANIF interfaces for device interconnection: Devices are automatically assigned interconnection IP addresses with 30-bit masks.
  Device loopback addresses: Each device is automatically assigned the IP address of Loopback 0 with a 32-bit mask. This IP address serves as the OSPF route ID and VTEP address.

## Slide 41
VXLAN-based Virtualized Campus Network and Solution
Underlay Design
Fabric Design
Overlay Design
Admission Control and Free Mobility Design
WLAN Design
O&M Design

## Slide 42: Fabric Design Overview
Underlay (physical network layer)
Fabric
Fabric
External network
Network service resource
Wired access
Wireless access
Fabric design
The campus fabric is a resource pooling network abstracted from the underlay network. The fabric virtualizes underlay network resources into a resource pool to implement "one network for multiple purposes".
The fabric design involves the following:
Fabric networking and node design
Interconnection design between the fabric and external network
Fabric network service resource planning
Fabric access management
External network
IP/VLAN segment
Access point
VN
Network service resource
Notes: Fabric network service resource planning:
  In the resource model design for the fabric network, network service resources are created on the border node so that service terminals on the campus network can access service resources in the network management zone, such as the DHCP server and NAC server.
  Multiple network service resources can be created, and one network service resource model can contain access addresses of multiple service resources.
  If only a few network service resources need to be accessed by the network management zone, you are advised to plan these resources in the same network service resource model. This saves interconnection VLAN and IP address resources and simplifies route configuration on the network management zone side.
Fabric access management:
  Configuring access management for the fabric is to configure authentication control points and plan access point resources for VN creation.
  The wired access point resource refers to switch interfaces connected by terminals, and the wireless access point resource refers to SSIDs connected by terminals.

## Slide 43: Fabric Design — Two-Layer Networking
A fabric can use two-layer or three-layer networking. The selection of a two-layer or three-layer network architecture is similar to that of a common network architecture.
Selecting the fabric architecture depends on the physical network architecture. When the physical network uses a two-layer architecture, the following is designed for fabric architecture:
  The core switch functions as the border node.
  Access switches function as edge nodes.
VXLAN
Border
Edge
Core layer
Access layer
Notes: Application scenarios of the two-layer architecture:
  Small-scale networks with a small number of access users
  Scenarios where access users are densely distributed: For example, all access users are located on the same floor of the same building.

## Slide 44: Fabric Design — Three-Layer Networking
If the physical network uses a three-layer architecture, the fabric architecture can be deployed in either of the following modes.
VXLAN
Border
Edge
Core layer
Access layer
VXLAN to the access layer
VXLAN to the aggregation layer
Solution description: The core switch functions as the border node and aggregation switches as the edge nodes. Access switches function only as access nodes of wired users or APs. In this case, policy association is implemented between aggregation and access switches to control user admission on the access switches.
Application scenario: This solution applies to legacy network reconstruction scenarios. Low-end access switches can be reused.
Aggregation layer
Solution description: The core switch functions as the border node, access switches as the edge nodes, and aggregation switches as transparent nodes on the fabric.
Application scenario: This solution applies to new network deployment scenarios. The entire network is virtualized, facilitating service provisioning and network management.
Transparent Node
VXLAN
Border
Edge
Core layer
Access layer
Aggregation layer
Access
Notes: Application scenarios of the three-layer architecture:
  Large-scale networks with a large number of access users (a large number of access switches)
  This mode applies to scenarios where access users are sparsely distributed. For example, all access users are located in different buildings. Therefore, traffic of each building can be centralized through the aggregation switch, and traffic of different buildings can be centralized through the core switch in the core equipment room.

## Slide 45: Fabric Networking Scenario Summary
For a two-layer or three-layer network architecture, a border or edge node can be used as the gateway.
  Centralized gateway: When the border node functions as the gateway, it is easy to achieve centralized management and simplified O&M.
  Distributed gateway: When the edge node functions as the gateway, it is easy to expand the network scale.
Networking Type | Gateway Location | Edge Node Location | Number of Terminals Supported | Applicable Scenario
Centralized gateway, VXLAN to the access layer | Border | Access switch | ≤ 50,000 | Recommended when the number of terminals does not exceed 50,000
Centralized gateway, VXLAN to the aggregation layer | Border | Aggregation switch | ≤ 50,000 | The number of terminals does not exceed 50,000.
Distributed gateway | Edge | Aggregation switch | 50000–100000 | Recommended when the number of terminals exceeds 50,000

## Slide 46: Fabric Node Design
Border node (CSS/iStack or a single switch. CSS is recommended.)
  Large-capacity switches (such as S12700 or S12700E) are recommended.
  ENP cards are used for interconnection between the core layer and aggregation layer, and Eth-Trunk is deployed for interconnection links.
Edge node (CSS/iStack or a single switch. CSS/iStack is recommended.)
  Large-capacity switches (such as S7700, S6700, and S12700) are recommended.
  Eth-Trunk is used for interconnection between core and aggregation switches, and between aggregation and access switches.
Access node
  Wired access nodes: Each access node can be a switch stack (a maximum of four member switches are recommended) or a standalone switch. A maximum of two layers of access switches are supported.
  Wireless access nodes: refer to Fit APs, which are managed by the native AC on agile switches.
Fabric domain
(VXLAN)
Border
Edge
Edge
Edge
L2
L3
Core layer
Aggregation layer
Access layer
Egress zone
CSS/iStack
Access
AP
Access
Link aggregation
Notes: It is recommended that core switches be used as border nodes. Access or aggregation switches can be used as edge nodes, and you are advised to use access switches as edge nodes.
You are advised to configure BGP EVPN route reflectors (RRs) on the VXLAN network. After RRs are configured, BGP peer relationships only need to be established between edge and border nodes.
  If no RR is configured, BGP peer relationships need to be established between edge nodes, and between edge and border nodes. The configuration is complex and many BGP connections consume CPU resources.
Both border and edge nodes can function as RRs. It is recommended that border nodes be used as RRs because they have the strongest processing capability.
ENP: Ethernet Network Processor

## Slide 47: Designing Fabric Nodes — Policy Association
Policy association can be deployed between access and aggregation switches (gateways). The gateway manages user access policies in a unified manner, and the access switch enforces user access policies.
  Authentication control points and enforcement points are connected through CAPWAP tunnels (which are the management tunnels used by policy association).
  CAPWAP tunnels implement user association, message transmission, user authorization policy delivery, user information synchronization, and other functions.
  After policy association is configured, enforcement points can transparently transmit BPDUs, report user logout and user access locations in real time, and enforce user access policies upon request, thereby controlling user access to the network.
CSS/iStack
Authentication control point
Authentication enforcement point
CAPWAP tunnel
Fabric domain
(VXLAN)
Border
Edge
Edge
Edge
L2
L3
Core layer
Aggregation layer
Access layer
Egress zone
Access
AP
Access
Policy association
Policy association
Link aggregation

## Slide 48: Fabric Node Design — Multiple Border Nodes
Fabric domain
(VXLAN)
Border1
Border2
Edge1
Edge2
Internet
DC
When a fabric needs to connect to multiple external networks that are not in the same physical location, multi-border networking can be used. Border nodes are located in different areas, and devices in different areas are connected to different external networks.
Scenario
Multiple border nodes are deployed independently and connect to different networks. Different services can use different network egresses.
Requirements
A maximum of eight border nodes can be planned in a fabric.
Each border node can be a standalone device or CSS/iStack. The cluster or stack is recommended.
Only distributed VXLAN gateways are supported.
Solution

## Slide 49: Interconnection Between the Fabric and External Network
L3 shared egress mode
L3 exclusive egress mode
L2 shared egress mode
Application scenario:
Multiple VNs need to access external networks, and these VNs use the same security policies.
Application scenario:
Multiple VNs need to access external networks, and each VN uses differentiated security policies.
Application scenario:
Border nodes do not function as user gateways, and user gateways must be located outside the fabric.
VRF
VRF
VRF
Shared VRF
Green VRF
Red VRF
VRF
Green VRF
Border
Border
Edge1
Border
L2 shared port
Edge2
Trust zone
VRF
Red VRF
Trust zone
Red zone
Trust zone
User gateway
Notes: All terminal data inside a campus network is forwarded through VXLAN tunnels. When the campus network needs to communicate with an external network, the data must pass through the border node. For example, a campus network communicates with an external network such as the Internet, DC, or another branch through the border node.
Three modes are available for interconnection between the fabric network and egress: L3 shared egress mode, L3 exclusive egress mode, and L2 shared egress mode. The L3 shared egress mode is applicable to the scenario where firewalls do not need to perform security detection on VNs and traffic of all VNs is transmitted in the same security zone. The L3 exclusive egress mode is suitable for the scenario where firewalls need to perform security detection on VNs and traffic of all VNs is transmitted in multiple security zones. The L2 shared egress mode applies to the scenario where the user gateway must be located outside the fabric, and the border node and egress firewalls are connected at Layer 2.
  In L3 shared egress mode, the campus network shares the same VPN instance (VRF) to access an external network, and static routes or dynamic BGP routes can be used between the border node and egress firewalls.

## Slide 50
Notes:     Static route design
      A border node learns global internal routes. The default route points to an egress firewall.
      A VPN instance on the border node is configured with a static default route that points to the public interface connected to the egress firewall.
      If there are multiple egress firewalls, you can deploy association between Network Quality Analysis (NQA) or Bidirectional Forwarding Detection (BFD) and static routes for switching.
    BGP route design
      A border node establishes a BGP connection with a firewall, summarizes user routes in VPN instances, and imports the summarized routes to BGP.
  L3 exclusive egress mode: A firewall is partitioned into security zones with the same number as VPN instances and connects to the border node through a physical interface or sub-interface. On the border node, a VPN instance is configured with a static default route that points to the corresponding physical interface or sub-interface of security zones of the firewall.
  L2 shared egress mode: The border node connects to the egress device through a Layer 2 interface, and the egress device is used as the user gateway to access the external network.
Application scenario:
  Typically, there are only a few egress routes between the campus network and external network. Therefore, the L3 shared egress mode is recommended, and static routes are used for route advertisement between the border node and egress firewall.
  When egress firewalls need to perform security detection on each VN based on security zones, the L3 exclusive egress mode can be used.
  The L2 shared egress mode applies only to the scenario where the user gateway must be located outside the fabric. In higher education scenarios, if a BRAS is used as the user authentication point and PPPoE dialup is required on the network, the L2 shared egress mode can be used.

## Slide 51
VXLAN-based Virtualized Campus Network and Solution
Underlay Design
Fabric Design
Overlay Design
Admission Control and Free Mobility Design
WLAN Design
O&M Design

## Slide 52: VN Design Process
Fabric
VN1: OA network
VN2: R&D network
VN3: production network
VN design
Divide the physical network into multiple VNs.
Policy design
Group users and define inter-group policies (policy control matrix).
Define inter-VN access policies based on the policy control matrix.
VN access design
Plan the mapping between VLANs of physical networks and BDs of VNs.
Plan terminal user access modes.
VN1: OA network
VN2: R&D network
VN3: production network
VIP
Sales
Guest
Marketing
Testing
Code library
Server
Operations
…
…
Server
Programmer
VN1: OA network
VN2: R&D network
VN3: production network
5W1H
5W1H
5W1H
1
2
3
Notes: VN design:
  VNs are generally divided based on services on a campus network. An independent service is assigned a VN, and VNs are isolated from each other by default. For example, on a campus network, services such as guest, teaching, IoT, and video surveillance services, each is assigned to an independent VN. For example, on an enterprise campus network, services including office network services, production network services, and R&D services can be allocated to independent VNs.
Policy design:
  Some isolation requirements caused by different user roles can be met by deploying policy control technologies (such as free mobility).
  VNs are isolated by default. Additional VN interworking configuration is required to meet access requirements of user groups on a VN.
VN access design:
  Service data enters different VNs according to the VLAN to which the user belongs from a physical network through an edge node. Therefore, during network design, you need to plan the mappings between VLANs of physical networks and BDs of VNs, and configure VLANs for wired and wireless users.

## Slide 53
Notes: 5W1H:
  Who: identity of an access user, for example, a company leader, a common employee, or a visitor
  Where: user access location, for example, campus access or remote access
  What: type of the terminal used by the access user, for example, mobile phone access or PC/laptop access
  When: time when a user accesses the network, for example, whether the user accesses the network in the daytime or in the evening
  Whose: device owner, for example, whether the device is a company-issued or BYOD one
  How: access mode of a user, for example, wired or wireless access

## Slide 54: VN Design
Overlay (virtual network layer)
Underlay (physical network layer)
Fabric
VN 1
VN 2
VN 3
Fabric
External network
Network service resource
Wired access
Wireless access
VRF+VNI
VRF+VNI
VRF+VNI
1. Network service abstraction
Physical network resources are pooled through orchestration, and the network is abstracted into Fabric as a Service (FaaS). A VN is an FaaS instance and includes:
IP/VLAN segment
External network
Network service resource: The IP/VLAN segment is the capability provided by the VN for clients to use network resources.
Access point: Terminals access VNs through access points.
2. Network service orchestration
Deliver the mapping between VNIs and BDs.
Deliver the mapping between BDs and VLANs.
Deliver the IP address segments corresponding to VBDIF interfaces.
Deliver VRFs and binds them to VBDIF interfaces.
Deploy VNs
Deliver configurations
External network
IP/VLAN segment
Access point
VN
Network service resource

## Slide 55: VN Access Design
Service data enters different VNs according to the VLAN to which the user belongs from a physical network through an edge node.
Wired user traffic is directly transmitted to virtual networks based on VLANs. After wireless user traffic is forwarded to the native AC, the native AC decapsulates CAPWAP packets and forwards the packets to the corresponding BD based on the VLAN.
Static VLANs
VN1
VN2
A static VLAN is configured for wired users on an interface of an access switch.
A static service VLAN is configured for wireless users on an SSID.
Dynamically authorized VLANs
VN1
VN2
Authorized user VLANs of wired users are delivered to an access switch, and then the access switch sends user traffic to different VLANs.
A service VLAN for wireless users is configured in a VAP profile. After the user is authenticated successfully, an authorized VLAN is delivered to an access switch. For 802.1X authentication and MAC address authentication, dynamic authorized VLANs are supported. For Portal authentication, only the configured service VLAN takes effect.
Native AC
Configure a static VLAN
Deliver the static service VLAN
Native AC
Deliver the authorized user VLAN
Deliver the authorized user VLAN
Notes: Application scenarios:
  The static VLAN mode applies when terminals access the VLAN at fixed locations and do not need to be authenticated. This access mode is more secure but lacks flexibility. When the locations of terminals change, you need to perform the configuration again.
  The dynamically authorized VLAN mode applies when terminals access the VLAN anywhere and need to be authenticated based on the VLAN information delivered during user authentication. This access mode is flexible and the configuration does not need to be changed when the locations of terminals change. Dynamic access is more automated, easy to manage and use, and is recommended.
VN access design for wireless users:
  If distributed gateways are used and edge nodes have the native AC function deployed, traffic of wireless users is forwarded to the edge nodes through CAPWAP tunnels. After the edge nodes decapsulate CAPWAP packets, the decapsulated packets enter a given VXLAN network (VN) based on the VLAN to which the wireless users belong.
  If centralized gateways are used and border nodes have the native AC function deployed, it is recommended that traffic of wireless users be directly forwarded to the border nodes through CAPWAP tunnels. The border nodes then decapsulate CAPWAP packets and forward them to a given BD based on the associated VLAN. The administrator needs to configure different VLAN ranges for wired and wireless terminals. The VLANs of wired terminals are bound to BDs on the edge node, whereas the VLANs of wireless terminals are bound to BDs on the border nodes.

## Slide 56: Inter-VN Communication Design
Inter-VN communication through a border node
Inter-VN communication through an external gateway
Border
Host 1
10.1.1.1/24
Host 2
10.2.2.2/24
VTEP1
1.1.1.1
VTEP2
2.2.2.2
VBDIF 10.1.1.254
VBDIF 10.2.2.254
VNI 1000
VNI 1001
Traffic for inter-VN communication is forwarded through the border node. VRFs on the border node need to import routes from each other.
This mode applies to the scenario where two VNs belong to the same security zone and there are low security control requirements.
Traffic for inter-VN communication is forwarded to the border node and then diverted to the external gateway. Subsequently, the external gateway performs a security check or forwards the traffic to the border node and proceeds finally to the destination.
This mode applies to the scenario where two VNs belong to different security zones and there are high security control requirements.
VRF1 and VRF2 on the border node import each other's network segment routes.
Border
Host 1
10.1.1.1/24
Host 2
10.2.2.2/24
VTEP1
1.1.1.1
VTEP2
2.2.2.2
VBDIF 10.1.1.254
VBDIF 10.2.2.254
VNI 1000
VNI 1001
VRF1
(L3VNI 1000)
VRF2
(L3VNI 1001)
VRF1
(L3VNI 1000)
VRF2
(L3VNI 1001)
Firewall
Notes: Inter-VN communication can be implemented through a border node or an external gateway.
  Through a border node
    If two VNs belong to the same security zone and have low security control requirements, devices on the two VNs can directly communicate with each other through a border node. In addition, permission control can be implemented based on the free mobility policy. To implement communication between VNs, the border node needs to import the network segment routes that can be reachable between devices on the VNs.
  Through an external gateway
    If two VNs belong to different security zones and have high security control requirements, it is recommended that devices on the two VNs communicate through an external gateway (a firewall) and that a security zone policy be configured on the firewall for permission control.

## Slide 57
VXLAN-based Virtualized Campus Network and Solution
Underlay Design
Fabric Design
Overlay Design
Admission Control and Free Mobility Design
WLAN Design
O&M Design
Notes: The design objective of the network access control solution is to solve user authentication and policy control issues of user networks. This solution uses the user organization structure and account information to implement classified user authentication and policy control.

## Slide 58: User Management Solution Design
The user management solution is designed to confirm the user data source server. Typical user data source servers of enterprises include RADIUS, AD, and LDAP servers.
Confirm the user data source server
RADIUS server
AD server
LDAP server
If an enterprise has no data source server, it is recommended that Huawei iMaster NCE-Campus be used as the data source server.
If an enterprise has used the AD/LDAP server as the user data source server, the enterprise can continue to use the legacy AD/LDAP server. iMaster NCE-Campus can synchronize user data with such a server and finally perform network authorization.
Same principles as the AD server
User Management Solution Design
User Authentication and Policy Management Design
Terminal Identification and Policy Automation Design

## Slide 59: User Authentication Technology Selection
Common authentication technologies include 802.1X, MAC address, and Portal authentication. The following table compares these authentication modes.
On large- and medium-sized campus networks, 802.1X authentication is recommended for employees, Portal authentication for guests, and MAC address authentication for dumb terminals.
If a customer wants to use more than one authentication mode on the same access point, the hybrid authentication mode can be used. After the hybrid authentication mode is configured, terminals can access the network after passing any authentication mode. This mode is applicable to scenarios where one port is used for access of multiple types of users. For example, if a PC is connected upstream to an IP phone, you can configure hybrid authentication (MAC address authentication + 802.1X authentication). In this way, the IP phone uses MAC address authentication, and the PC uses 802.1X authentication.
Item | 802.1X Authentication | MAC Address Authentication | Portal Authentication
Client required or not | Required | Not required | Not required
Advantage | High security | No need to install a client | Flexible deployment
Disadvantage | Inflexible deployment | MAC addresses need to be registered, complicating management | Low security
Application scenario | Network authentication of office users with high security requirements | Access authentication of dumb terminals such as printers and fax machines | Network authentication of guests who move frequently and use different types of terminals
User Management Solution Design
User Authentication and Policy Management Design
Terminal Identification and Policy Automation Design
Notes: If 802.1X or MAC address authentication (Layer 2 authentication technologies) is used, the authentication point must be on the same network segment as the user host. It is recommended that the access device function as the authentication point.
  If a large number of access devices are deployed, the aggregation or core device needs to be deployed as the authentication point. You can also deploy policy association. The gateway functions as the authentication control point, and the access device functions as the authentication enforcement point to simplify policy deployment.
If Portal authentication is used, the authentication point can be deployed anywhere as long as it is routable to the user host. Layer 2 Portal authentication is recommended.

## Slide 60: Association Between Authenticated Users and VNs
The administrator creates VNs on iMaster NCE-Campus.
After authentication, users obtain the authorized VLANs and then are associated with VNs based on such VLANs.
The administrator creates VNs and specifies the IP network segments and VLANs of VNs.
The administrator configures user authentication rules, authorization rules, and authorization results, so that users can obtain corresponding VLANs after being authenticated. For example, the administrator configures user test to obtain the authorized VLAN 10 after passing 802.1X authentication.
OA VN
VLAN 10: 10.1.10.0/24
VLAN 20: 10.1.20.0/24
R&D VN
VLAN 30: 10.1.30.0/24
VLAN 40: 10.1.40.0/24
1
User test attempts to access the network.
Send an authentication request.
Issue the authorization result (VLAN 10 authorized) after successful user authentication.
2
3
4
User Test accesses the OA VN.
test
User Management Solution Design
User Authentication and Policy Management Design
Terminal Identification and Policy Automation Design

## Slide 61: Free Mobility Solution (1)
Scenario description
Centralized authentication point + centralized policy enforcement point
The authentication point and policy enforcement point are combined on the core device.
Devices do not support VXLAN.
Scenario characteristics
The core device functions as the centralized authentication point for both wired and wireless users on the entire network.
The core device also works as the centralized policy enforcement point for free mobility.
The core device stores authentication information about all users on the network. After traffic is forwarded to the core device, it enforces policies based on the policy control matrix defined by users.
The network does not need to support or deploy VXLAN.
Group Name | Group ID
Sales | 1
R&D | 2
Marketing | 3
… | …
 | Sales | R&D | Marketing | …
Sales | √ | × | √ | …
R&D | × | √ | √ | …
Marketing | √ | √ | √ | …
… | … | … | … | …
PC1 1.1.1.1
Sales user
PC3 3.3.3.3
Marketing user
Core
AGG1
AGG2
Access1
Access2
Security group
Security group-based policy control matrix
PC2 2.2.2.2
R&D user
Authentication point
Policy enforcement point
Security group and policy control matrix delivery
User Management Solution Design
User Authentication and Policy Management Design
Terminal Identification and Policy Automation Design

## Slide 62: Free Mobility Solution (2)
Group Name | Group ID
Sales | 1
R&D | 2
Marketing | 3
… | …
 | Sales | R&D | Marketing | …
Sales | √ | × | √ | …
R&D | × | √ | √ | …
Marketing | √ | √ | √ | …
… | … | … | … | …
Core
AGG1
AGG2
Access1
Access2
Security group
Security group-based policy control matrix
Scenario description
Distributed authentication points + centralized policy enforcement point
The authentication point is separated from the policy enforcement point.
Devices do not support VXLAN.
Scenario characteristics
Multiple authentication points exist on the entire network, for example, distributed on aggregation switches.
The core device functions as the centralized policy enforcement point for free mobility.
iMaster NCE-Campus proactively synchronizes IP-security group information to the core device. After traffic is forwarded to the core device, it enforces policies based on the policy control matrix defined by users.
The network does not need to support or deploy VXLAN.
Authentication point
Policy enforcement point
Security group and policy control matrix delivery
IP Address | Group ID
1.1.1.1 | 1
2.2.2.2 | 2
3.3.3.3 | 3
… | …
IP-security group mapping table
Actively synchronizing IP-security group information
PC1 1.1.1.1
Sales user
PC3 3.3.3.3
Marketing user
PC2 2.2.2.2
R&D user
User Management Solution Design
User Authentication and Policy Management Design
Terminal Identification and Policy Automation Design
Device enabled with IP-security group
entry synchronization

## Slide 63: Free Mobility Solution (3)
Core
AGG1
AGG2
Access1
Access2
Scenario description
VXLAN-based virtualized campus network, achieving automatic service provisioning
Distributed authentication points + policy enforcement points
Scenario characteristics
Multiple authentication points exist on the entire network, for example, distributed on aggregation switches.
Aggregation switches support VXLAN and function as policy enforcement points.
The policy for traffic exchanged between users on the same aggregation switch is enforced by the aggregation switch itself.
Traffic exchanged between users on different aggregation switches is encapsulated using VXLAN. The source security group ID is encapsulated into VXLAN-encapsulated traffic. Policies are enforced on the peer aggregation switch.
Authentication point
Policy enforcement point
Security group and policy control matrix delivery
Group Name | Group ID
Sales | 1
R&D | 2
Marketing | 3
… | …
 | Sales | R&D | Marketing | …
Sales | √ | × | √ | …
R&D | × | √ | √ | …
Marketing | √ | √ | √ | …
… | … | … | … | …
Security group
Security group-based policy control matrix
VXLAN
PC1 1.1.1.1
Sales user
PC3 3.3.3.3
Marketing user
PC2 2.2.2.2
R&D user
User Management Solution Design
User Authentication and Policy Management Design
Terminal Identification and Policy Automation Design

## Slide 64: Free Mobility Solution (4)
Host1
Sales
A-Agg
B-Agg
B-Access
1
2
3
4
5
AP
A terminal attempts to go online and initiates authentication.
Authenticate the user.
Generate an IP-security group entry.
Deliver the IP-security group entry.
Enforce the inter-group policy when the traffic arrives.
Device enabled with IP-security group
entry synchronization
A-Access
(third party)
Host4
Guest
Scenario description
VXLAN-based virtualized campus network
Distributed authentication points + policy enforcement point
The third-party device functions as the user authentication point.
Scenario characteristics
A third-party switch exists on the network and functions as the user authentication point.
Aggregation switches support VXLAN and function as policy enforcement points.
The policy for traffic exchanged between users on the same aggregation switch is enforced by the aggregation switch itself.
Traffic exchanged between users on different aggregation switches is encapsulated using VXLAN. The source security group ID is encapsulated into VXLAN-encapsulated traffic. Policies are enforced on the peer aggregation switch.
VXLAN
Authentication point
Policy enforcement point
Security group and policy control matrix delivery
Actively synchronizing IP-security group information
User Management Solution Design
User Authentication and Policy Management Design
Terminal Identification and Policy Automation Design

## Slide 65: Terminal Identification and Policy Automation
Difficult to locate bogus terminals
Example: an enterprise
10+ authentication faults reported every day
50+ types of smart terminals
Example: a high education institution
Data of smart terminals collected by level-2 departments
Difficult and error-prone MAC address collection
Terminal type-based
Automatic authorization
Recognized as a camera
Automatically added to a video surveillance group
Set as a VIP user
Terminal type-based
Automatic authentication
Recognized as a printer
Automatic MAC address authentication, without the need of manual MAC address input
Terminal type-based
Bogus terminal detection
Recognized as an IP phone first and then a PC
Report a bogus terminal alarm.
Requirements & challenges
Terminal identification and policy automation
Terminal fingerprint database
Information reporting
Proactive scanning
>>
User Management Solution Design
User Authentication and Policy Management Design
Terminal Identification and Policy Automation Design
Notes: On large- and medium-sized campus networks, access terminals include smart terminals (such as PCs and mobile phones) and dumb terminals (such as IP phones, printers, and IP cameras). Currently, terminal management on campus networks faces the following challenges:
  The network management system (NMS) can only display the IP and MAC addresses of access terminals, but cannot identify the specific terminal type. As a result, the NMS cannot provide refined management for network terminals.
  Network service configurations and policies vary according to the terminal type. Consequently, administrators need to manually configure different services and policies for each type of service terminals, complicating service deployment and operations.
To address these challenges, Huawei provides the automatic terminal identification and policy delivery solution, which delivers the following functions:
  iMaster NCE-Campus can display the network-wide terminal types and operating systems, for example, dumb terminals including printers, IP cameras, smart all-in-one card, and access control system. iMaster NCE-Campus can also collect statistics and display traffic by terminal type.
  Administrators do not need to manually configure different services and policies for different types of dumb terminals such as IP phones, printers, and IP cameras on the campus network. iMaster NCE-Campus can automatically identify terminals and deliver the corresponding access policies and service configurations to them.

## Slide 66: Terminal Identification
To deploy the terminal identification and automatic policy delivery solution, network administrators need to design terminal identification methods and terminal policies.
The terminal management function of iMaster NCE-Campus can help identify terminals and display the terminal type, operating system, and vendor.
The following table describes terminal identification methods.
Type | Identification Method | Description | Applicable Scenario
Information reporting | MAC OUI | The first three bytes of a MAC address indicate vendor information. This method is inaccurate in most cases. | Identify the device vendor only
 | HTTP UserAgent | A browser's UserAgent string contains the vendor, terminal type, operating system, browser type, and other information. | Mobile phones, tablets, PCs, workstations, intelligent audio/video terminals
 | DHCP Option | Some options of a terminal's DHCP packets can be used to classify terminals, for example, DHCP options 55, 60, and 12. | Mobile phones, tablets, PCs, workstations, IP cameras, IP phones, printers, etc.
 | LLDP | LLDPDUs carry device model information. | IP phones, IP cameras, network devices, etc.
 | mDNS | mDNS packets contain terminal model and service information. | Apple devices, printers, IP cameras, etc.
Proactive scanning | SNMP Query | Obtains identification information by querying device information-related SNMP MIB objects. | Network devices, printers, etc.
 | Nmap | Scans the OS and services of terminals to detect the terminal model and OS information. | PCs, workstations, printers, IP phones, IP cameras, etc.
User Management Solution Design
User Authentication and Policy Management Design
Terminal Identification and Policy Automation Design
Notes: When a terminal accesses the network, the network device connected to it can collect information about the terminal and report the information to iMaster NCE-Campus or iMaster NCE-Campus automatically scans terminal information. Then, iMaster NCE-Campus automatically identifies the type, operating system, and vendor of the terminal.

## Slide 67: Terminal Identification — Proactive and Passive Detection
Passive detection
Proactive detection
Terminal visibility: collects terminal type statistics (by vendor and OS), displays the relationship between terminals and access ports, queries access policies (covering VLAN, QoS, and authentication mode), and exports reports.
Terminal policy automation:
  Supports automatic terminal access based on terminal types, thereby achieving automatic MAC address authentication of dumb terminals.
  Authorizes policies (covering VLAN, security group, access permission, and QoS) on a per-terminal group basis.
  Supports IPv4/IPv6 dual-stack terminals.
Scan and detect
Provide feedback
1
2
4
Deliver configurations/policies
3
Display identification result
Administrator
5
Deliver configurations/policies
4
Display identification result
Administrator
1
Send traffic
Collect fingerprint
2
3
Report fingerprint
User Management Solution Design
User Authentication and Policy Management Design
Terminal Identification and Policy Automation Design
Notes: Passive fingerprint-based identification: Network devices collect fingerprints of terminal packets and report the fingerprints to iMaster NCE-Campus for terminal type identification.
Proactive scanning and identification: iMaster NCE-Campus proactively detects or scans terminals, and identifies terminal types based on feedback information from the terminals.

## Slide 68: Terminal Identification Methods (1)
To view terminal types and perform network management based on the terminal types through iMaster NCE-Campus, the network administrator needs to perform the following operations:
Collect the types of terminals on the network, such as PCs, mobile phones, printers, IP cameras, and access control devices.
Check whether to deploy Portal authentication or not.
Check whether the IP addresses of terminals are assigned in DHCP or static mode.
Analyze the network.
Method | Identifiable Terminal Type | Applicable Scenario
MAC OUI | All IP terminals (only device vendors can be identified) | General scenarios
HTTP UserAgent | Mobile phones, tablets, PCs, and workstations, as well as intelligent audio and video terminals | Portal authentication scenarios only
DHCP Option | Mobile phone, tablets, PCs, workstations, IP cameras, IP phones, printers, etc. | Dynamic IP address assignment scenarios only
LLDP | IP phones, IP cameras, network devices, etc. | General scenarios
mDNS | Apple devices, printers, IP cameras, etc. | General scenarios
SNMP Query | Network devices, printers | Local deployment
Nmap | PCs, workstations, printers, IP phones, IP cameras, etc. | Local deployment
Traverse items one by one according to the following table.
Based on the collected information, traverse the items listed in the following table one by one and select the required terminal identification methods. All the identification methods that meet requirements must be enabled.
1
2
User Management Solution Design
User Authentication and Policy Management Design
Terminal Identification and Policy Automation Design
Notes: In this slide, "general scenarios" refer to authentication, non-authentication, and dynamic/static IP address assignment scenarios.
In non-authentication scenarios, the controller can display information about wired terminals only after the ARP snooping function is enabled on access devices.

## Slide 69: Terminal Identification Methods (2)
If the network administrator cannot determine which terminal identification method is to be used, the following methods are recommended to be enabled: MAC OUI, HTTP UserAgent, DHCP Option, LLDP, and mDNS.
It is recommended that Nmap be disabled by default because its identification period is long. If the preceding methods for passive fingerprint-based identification cannot meet requirements, enable Nmap.
Enable the terminal identification function.
Method | Enabled On | Other Functions to Be Enabled
MAC OUI | Access switch and AP | -
HTTP UserAgent | Portal authentication device | -
DHCP Option | Access switch and AP | DHCP snooping must be enabled on access switches. By default, DHCP snooping is already enabled on APs.
LLDP | Access switch and AP | -
mDNS | Access switch and AP | mDNS snooping must be enabled on access switches and APs.
SNMP Query | Controller | -
Nmap | Controller | -
3
User Management Solution Design
User Authentication and Policy Management Design
Terminal Identification and Policy Automation Design

## Slide 70: Terminal Policy Design
The network administrator can use iMaster NCE-Campus to automatically deliver policies to terminals, without the need to manually configure different services and policies for each type of service terminals.
Terminal policies can be delivered based on the terminal type, operating system, or vendor.
Enable automatic policy delivery based on terminal types to authorize policies depending on access authentication.
Deploy admission authentication on access switches and APs.
Enable MAC address authentication on access switches and APs when dumb terminals are deployed.
Perform policy design.
Enable the terminal identification function on the network.
Sort out the types of terminals that require automatic policy delivery on the network, design corresponding authorization policies, and configure the policies on iMaster NCE-Campus.
Item | Access Policy | Authorization Policy
Operating system: Android | User access | Authorized ACL 1
Operating system: iOS | User access | Authorized ACL 2
Terminal type: printer | Automatic access | Authorized VLAN 10
Terminal type: IP camera | Automatic access | Authorized VLAN 20
Terminal type: IP phone | Automatic access | Authorized VLAN 30; DSCP 48
Terminal type: access control device | Automatic access | Authorized VLAN 40
Vendor: ABC | User access | Authorized ACL 100
1
2
3
User Management Solution Design
User Authentication and Policy Management Design
Terminal Identification and Policy Automation Design
Notes: It is recommended that admission and authorization policies be automatically delivered to dumb terminals (such as printers, IP phones, and IP cameras) based on terminal types. This helps implement automatic service provisioning and plug-and-play for dumb terminals.

## Slide 71
VXLAN-based Virtualized Campus Network and Solution
Underlay Design
Fabric Design
Overlay Design
Admission Control and Free Mobility Design
WLAN Design
O&M Design

## Slide 72: WLAN Service Solution
Native AC solution
Switches provide the native AC function.
Free mobility is supported. Policies for both wired and wireless users are centrally enforced on the switches.
Unified O&M for both wired and wireless users
Standalone AC solution
Standalone AC (connected to the core switch in off-path mode)
The solution supports free mobility for wireless users, which requires the collaboration with the IP-security group entry synchronization solution.
Separate O&M for wired and wireless users
Native AC
Standalone AC
Standalone AC
Native AC
Native AC
The native AC function can be applied to aggregation or core switches.
Notes: On a large- or medium-sized campus network, the WLAN typically uses the "AC + Fit AP" networking architecture. Depending on the location of the AC, two AC deployment modes are available: in-path and off-path. When a native AC (integrated on a switch) is used, only the in-path deployment mode can be adopted. When a standalone AC is used, the two deployment modes are both supported (off-path mode recommended).

## Slide 73: How to Select an AC
In Huawei's solution, ACs include native AC (built-in AC on agile switches to implement wired and wireless convergence) and standalone ACs.
Select appropriate ACs based on the AC performance specifications and actual project requirements by considering the following factors:
  Number of managed APs
  Number of concurrent terminals
  Forwarding capability, especially in centralized forwarding mode
  Concurrent access rate. In higher education scenarios, for example, this factor is a key factor to consider, especially in the teaching area where a large number of users may go online concurrently after class.
When the specifications meet the requirements, the native AC is preferred. If the wired and wireless networks are independently deployed or capacity expansion is needed in the future, the standalone AC is recommended.
In addition to the preceding specifications, key features must be considered. If the following features are required, only the native AC can be selected:
  Wired and wireless convergence to provide unified authentication and management
  Free mobility

## Slide 74: Native AC Solution Deployed on a VXLAN-based Virtualized Campus Network (1)
Distributed gateway scenario
Native AC
Scenario 1: The switch used as the edge node provides the native AC function to manage downstream APs.
When the number of wireless users on the entire network exceeds 50K, it is recommended that native AC be deployed on edge nodes. In this scenario, it is recommended that the AP should use the tunnel forwarding mode.
Border
Edge
Layer 3
gateway
Edge
Layer 3
gateway
Edge
Layer 3
gateway
Scenario 2: The switch used as the border node provides the native AC function to manage downstream APs.
When the number of wireless users on the entire network is fewer than 50K, it is recommended that native AC be deployed on the border node. In this scenario, the local forwarding mode is recommended for APs.
Border
Edge
Layer 3
gateway
Edge
Layer 3
gateway
Edge
Layer 3
gateway

## Slide 75: Native AC Solution Deployed on a VXLAN-based Virtualized Campus Network (2)
Centralized gateway scenario
Scenario: The switch used as the border node provides the native AC function to manage all APs.
It is recommended that native AC be deployed on edge nodes and APs use the tunnel forwarding mode.
Border
L3 gateway
Edge
Edge
Edge
Native AC

## Slide 76: WLAN Virtualization Deployment Solution Design
The following table describes the WLAN virtualization deployment solution for centralized and distributed gateway networking.
In new deployment scenarios or wired and wireless network reconstruction scenarios, the native AC is recommended and the tunnel forwarding mode is preferred for APs.
Networking Type | AC | Wireless Terminal Gateway | AP Forwarding Mode | Wireless Traffic Virtualization Location | Number of Terminals Supported | Applicable Scenario
Centralized gateway | Native AC on the border node | Border node | Tunnel forwarding | Border node | ≤ 50,000 | Recommended when the number of terminals does not exceed 50,000 and centralized forwarding is implemented for wireless terminals
 | Native AC on the border node | Border node | Local forwarding | Edge node | ≤ 50,000 | Applies when local forwarding is implemented for wireless terminals (this solution is not recommended)
 | Standalone AC connected to the border node in off-path mode | Border node | Tunnel forwarding | Border node | ≤ 50,000 | Recommended when the wired network is reconstructed first and centralized forwarding is implemented for wireless terminals
 | Standalone AC connected to the border node in off-path mode | Border node | Local forwarding | Edge node | ≤ 50,000 | Applies when the wired network is reconstructed first and local forwarding is implemented for wireless terminals (this solution is not recommended)
Distributed gateway | Edge node | Edge node | Tunnel forwarding | Edge node | 50,000–100,000 | Recommended when the number of terminals exceeds 50,000 and centralized forwarding is implemented for wireless terminals

## Slide 77
VXLAN-based Virtualized Campus Network and Solution
Underlay Design
Fabric Design
Overlay Design
Admission Control and Free Mobility Design
WLAN Design
O&M Design

## Slide 78: Intelligent O&M Panorama
Visualized management and monitoring
Device management
Log management
File/Configuration management
Alarm management
File/Configuration management
NE management
Service quality monitoring
Link management
Wireless network quality monitoring
Network management
Terminal management
Customer flow analysis
User management
Terminal management
Device dimension
User roaming dimension
User application dimension
User access dimension
User throughput dimension
Network health
Intelligent troubleshooting
Network diagnosis and test
SLA management
Packet header obtaining
Packet path tracing
Fault locating
Access analysis
Protocol tracing
Issue analysis
Performance analysis
Fault analysis
Access analysis
Protocol tracing
Radio calibration
Performance analysis
Network optimization
Controller
Analyzer
CloudCampus
APP

## Slide 79: Intelligent O&M Solution Deployment Design
Huawei iMaster NCE-CampusInsight disrupts the traditional monitoring mode that focuses on resource status. This platform applies AI to the O&M field and adopts Telemetry technology to collect performance indicators and log data of network devices. By using big data, AI algorithms, and more advanced analytics technologies as well as leveraging scenario-specific continuous learning and expert experience accumulation, iMaster NCE-CampusInsight frees O&M personnel from nerve-wracking alarms and noises, making user network experience visualized and O&M automated and intelligent.
The intelligent O&M solution integrates iMaster NCE-CampusInsight, iMaster NCE-Campus, and devices. Currently, iMaster NCE-CampusInsight can manage and perform intelligent analysis on Huawei cloud switches and cloud APs.
Devices need to periodically report data to iMaster NCE-CampusInsight. Therefore, the campus network needs to reserve bandwidth for data reporting. The average bandwidth consumed by each device is 3 kbit/s.
Network bandwidth design
iMaster NCE-CampusInsight and iMaster NCE-Campus can be deployed at different locations. They can collaborate with each other as long as network connectivity is available. To avoid the instability of the intermediate network, you are advised to deploy them in the same location, for example, in the same DC.
Deployment location design

## Slide 80: Precautions for Intelligent O&M Design
Ensure that there are reachable routes between network devices and the analyzer iMaster NCE-CampusInsight so that the network devices can send KPI performance data and log information to iMaster NCE-CampusInsight.
During network deployment, ensure that devices are clock-synchronized with iMaster NCE-CampusInsight. You are advised to deploy an NTP server to synchronize the system clock of the network.
Network deployment design
To identify DHCP-related connectivity issues and implement protocol trace, you need to use the AC as the DHCP server or enable DHCP snooping on the AC.
Protocol playback function design
The audio and video quality analysis function requires devices to send related log information to iMaster NCE-CampusInsight. You are advised to configure the same log sending interval for switches and WLAN devices. The maximum difference between the log sending intervals cannot exceed 20s.
Audio and video quality analysis function design
Intelligent radio calibration and traditional radio calibration cannot be deployed on APs in the same region simultaneously.
Intelligent radio calibration function design

## Slide 81
(Single-Choice) Which of the following networking modes is used for large-scale campus network architecture design? ( )
  Single-layer architecture
  Two-layer architecture
  Three-layer architecture
  Multi-layer architecture
Notes: Answer:
  C

## Slide 82
(Single-Choice)The recommended fabric networking mode is ( ) for a large-scale campus network with more than 50,000 terminals, the gateway is located on the ( ), and the edge is located on the ( ).
  Centralized gateway
  Distributed gateway
  Edge
  Border
  Access switch
  Aggregation switch
Notes: Answer
  BCF

## Slide 83
To meet requirements of digital transformation, campus networks need to be reconstructed systematically. Based on the IDN concept, Huawei CloudCampus Solution helps enterprises build intelligent, simplified, converged, open, and secure networks.
This course describes the solution architecture, technical solution comparison, engineering design suggestions, and O&M for large- and medium-sized campus networks, helping trainees understand Huawei CloudCampus Solution technologies and design the optimal campus network solution.