## Slide 1
2020.11.30
Zhang Linrui/wx570554
Optimized
Zhu Shigeng/00261992
2020.09.28
New
Lu Yueyue/wx445705

## Slide 2: VXLAN-based Virtualized Campus Network Deployment Guide

## Slide 3
Huawei CloudCampus Solution adopts a new philosophy of Intent-Driven Network (IDN), and introduces big data analytics and Artificial Intelligence (AI) technologies into cloud and software-defined networking (SDN). It helps enterprises build intelligent, simplified, converged, open, and secure networks.
Different from traditional campus networks that focus on standalone devices, a virtualized campus network focuses on the overall service experience of the entire network and uses iMaster NCE-Campus and virtual extensible local area network (VXLAN) technology to flexibly schedule network resources. Virtualization technologies group physical network resources into a network-wide resource pool that can be flexibly adjusted by the service layer and allocated by iMaster NCE-Campus. A physical network is virtualized into multiple logically independent virtual networks that carry various services and have independent network resources. This virtualization decouples services from networks and facilitates service management.
This course describes the deployment process and typical deployment cases of the VXLAN-based virtualized campus network solution.

## Slide 4
Upon completion of this course, you will be able to:
  Describe the deployment process of the CloudCampus VXLAN-based virtualized campus network solution.
  Deploy a typical CloudCampus VXLAN-based virtualized campus network solution.
  Configure iMaster NCE-Campus to manage and maintain the CloudCampus VXLAN-based virtualized campus network.

## Slide 5
VXLAN-based Virtualized Campus Network Deployment Plan
VXLAN-based Virtualized Campus Network Deployment Process and Guide
  Deployment Process
  Preparations for Deployment
  Deployment Guide

## Slide 6: Review: Virtualized Campus Network Architecture
Underlay (physical network layer)
Fabric
Core
Aggregation
Aggregation
Access
Access
Border
BGP EVPN
BGP EVPN
External networks
Network service resources
Edge
Edge
Wired access
Wireless access
Overlay (virtual network layer)
Virtual network 1
Virtual network N
VRF+VNI
VRF+VNI
Network egress
IP/VLAN
Access point
Network services
Fabric instantiation
Underlay: a physical topology consisting of physical network devices, such as switches, access points (APs), firewalls, and routers, to provide interconnection capabilities for all services on the campus network, building the basic bearer network for campus service data forwarding.
Fabric: a network with pooled resources abstracted from the underlay network. When creating an instantiated virtual network, you can select the pooled network resources on the fabric.
Virtual network: a logically isolated virtual network instance that is constructed by instantiating a fabric. One virtual network corresponds to one isolated network (service network), for example, research network.
OSPF
VXLAN

## Slide 7: Review: Network Nodes on a Virtualized Campus Network
Egress gateway: is an egress device of the campus network, which can be an AR router or a firewall.
Border node: implements communication between the fabric and external networks. It is typically a core switch.
Edge node: is a fabric edge device that connects user-side devices to the fabric. Data packets from wired users are encapsulated into VXLAN packets on edge nodes.
Transparent node: is a transparent device on the fabric, and does not need to support VXLAN.
Access node: is typically an access switch (wired access node) or an AP (wireless access node). Wired access nodes can be combined with edge nodes, that is, VXLAN is deployed to the access layer. If wired access nodes do not need to support VXLAN, aggregation nodes can be combined with edge nodes, that is, VXLAN is deployed to the aggregation layer, and policy association is deployed on wired access nodes and VXLAN edge nodes.
Fabric domain (VXLAN)
Access domain
Border node
Transparent node
Edge node
Access node
VXLAN-capable nodes
Egress gateway
Notes: On a fabric, VXLAN tunnel endpoints (VTEPs) are further divided into the following roles:
  Border: is a physical network device and provides data forwarding between the fabric and external networks. In most cases, VXLAN-capable core switches function as border nodes.
  Edge: is a physical network device. Access user traffic enters the fabric from an edge node. Generally, VXLAN-capable access or aggregation switches function as edge nodes.

## Slide 8: Lab: Requirements
HQ
AR1
CORE1
AGG1
ACC1
AGG2
AP
Host 1
Host 2
Host 3
GE0/0/1
ACC2
GE0/0/2
GE0/0/3
GE0/0/1
GE0/0/24
GE0/0/24
GE0/0/23
GE0/0/1
GE0/0/2
GE0/0/2
GE0/0/1
GE0/0/1
To implement multi-service convergence on a campus network, virtual networks are deployed and configured on the campus network through iMaster NCE-Campus. This enables different virtual networks on the same physical network to be divided based on services.
Using the VXLAN technology, virtual networks meet the following requirements:
Network devices support DHCP-based plug-and-play provisioning.
Multiple services on the campus network share the same physical network, but are logically isolated. Mutual access control can be implemented among these services.
Service configuration is automated, and virtual network configurations are delivered by iMaster NCE-Campus, removing the need to log in to devices to manually configure them.
Users can access virtual networks from anywhere on the campus network, implementing flexible user authentication, onboarding, and free mobility.

## Slide 9: Lab: Gateway Solution Selection
When designing the virtualization solution, first determine the gateway solution to be used. After the gateway solution is determined, you can perform end-to-end design on the entire campus network based on the selected gateway solution.
Item | Centralized Gateway | Distributed Gateway
User gateway location | Border | Edge
O&M deployment | A border node functions as the gateway of all users, and the native access controller (AC) function is typically enabled on the border node to configure wireless services, simplifying O&M deployment. | Multiple edge nodes function as user gateways, and the native AC function is typically enabled on these edge nodes. Wireless services may need to be configured on multiple edge nodes, complicating O&M deployment.
Terminal scale | ≤ 50,000 (This solution is recommended when the number of terminals does not exceed 50,000.) | 50,000 to 100,000 (This solution is recommended when the number of terminals exceeds 50,000.)

## Slide 10: Lab: Recommended Networking Plan for Gateway Solutions
Gateway Solution | Border Node Location | Edge Node Location | AC Type and Location | Wireless Data Forwarding Mode | Application Scenario
Centralized gateway | Core | Access | Native AC located on a core device | Tunnel forwarding | New network with no more than 50,000 terminals.
 |  | Aggregation |  |  | Reconstructed network with no more than 50,000 terminals. VXLAN-incapable access switches can be reused.
 |  | Access | Standalone AC connected to a core device in off-path mode. |  | Reconstructed network with no more than 50,000 terminals. Standalone ACs can be reused.
 |  | Aggregation |  |  | Reconstructed network with no more than 50,000 terminals. Standalone ACs and VXLAN-incapable access switches can be reused.
Distributed gateway | Core | Aggregation | Native AC located on an aggregation device | Tunnel forwarding | New or reconstructed network with more than 50,000 and less than or equal to 100,000 terminals. Access switches do not need to support VXLAN.

## Slide 11: Lab: Physical and VXLAN Networking
HQ
AR1
CORE1
(Border)
AGG1
ACC1
(Edge)
AGG2
AP
Host 1
Host 2
Host 3
GE0/0/1
GE0/0/0
VXLAN
ACC2
(Edge)
GE0/0/2
GE0/0/3
GE0/0/1
GE0/0/24
GE0/0/24
GE0/0/23
GE0/0/1
GE0/0/2
GE0/0/2
GE0/0/1
GE0/0/1
GE0/0/17
GE0/0/20
SW1
HQ: ACC1 and ACC2 function as access devices that connect to wired terminals and provide network services for wired users. An AP is connected to ACC2 to provide network services for wireless users. AGG1 and AGG2 serve as aggregation devices, and CORE1 is the core device. AR1 functions as both the campus egress and the DHCP server that allocates IP addresses to other devices and user terminals at the HQ. OSPF is used for underlay connectivity at the HQ.
Cloud: SW1 functions as the gateway of iMaster NCE-Campus and connects the HQ and iMaster NCE-Campus.
VXLAN network (fabric): The network topology for this lab uses a distributed gateway model, in which VXLAN is deployed to the access layer. ACC1 and ACC2 function as edge nodes, whereas CORE1 functions as the border node.

## Slide 12: Lab: Virtual Network
HQ
AR1
CORE1
(Border)
AGG1
ACC1
(Edge)
AGG2
AP
Host 1
Host 2
Host 3
GE0/0/1
VXLAN
ACC2
(Edge)
GE0/0/1
GE0/0/2
GE0/0/3
OA
Internet
RD
172.16.12.0/24
MKT
172.16.13.0/24
External networks
DHCP server
(User terminal)
Network service resources
OA_VN
RD_VN
MKT_VN
Virtual network: Three virtual networks are defined for access of different terminal users.
OA virtual network for access of guests (Guest_Group)
RD virtual network for access of R&D personnel (Research_Group)
MKT virtual network access of sales personnel (Sales_Group)
External network: Three external networks are defined for the three virtual networks to allow access of different terminal users to different external networks.
OA external network is provided for Internet access of guests through the OA virtual network.
RD and MKT external networks are provided for access of R&D personnel and sales personnel.
Network service resources: One DHCP server is deployed to allocate IP addresses to all terminal users on virtual networks.

## Slide 13: Lab: Security Group and Policy Control Matrix
Security group: Three security groups are defined to identify different terminal users.
Guest_Group is a security group to which guests are assigned after they pass Portal authentication.
Research_Group is a security group to which R&D personnel are assigned after they pass 802.1X authentication.
Sales_Group is a security group to which sales personnel are assigned after they pass 802.1X authentication.
RD_VN
MKT_VN
Fabric
Research
(802.1X)
Sales
(802.1X)
OA_VN
Guest
(802.1X)
Guest
(Portal)
Guest
security group
Research
security group
Sales
security group
Security group-based policy control matrix
 | Guest_Group | Research_Group | Sales_Group
Guest_Group |  | Status: Enable Default: Deny | Status: Enable Default: Deny
Research_Group | Status: Enable Default: Permit |  | Status: Enable Default: Permit
Sales_Group | Status: Enable Default: Permit | Status: Enable Default: Permit | 
unknown |  | Status: Enable Default: Deny | Status: Enable Default: Deny
Policy control matrix
Guests can access the Internet only through the OA virtual network (OA_VN).
R&D personnel and sales personnel can communicate with each other and access the Internet through the OA virtual network.
Other users are not allowed to access the RD and MKT virtual networks and external networks.
Destination Security Group
Source Security Group

## Slide 14
VXLAN-based Virtualized Campus Network Deployment Plan
VXLAN-based Virtualized Campus Network Deployment Process and Guide
  Deployment Process
  Preparations for Deployment
  Deployment Guide

## Slide 15: VXLAN-based Virtualized Campus Network Deployment Flowchart
Start
Server and software installation
Networking configuration in the NMS zone
License activation
Site creation
Basic network configurations
Network service configurations
End
Install servers.
Connect cables.
Power on servers.
Install iMaster NCE-Campus.
Configure the gateway in the NMS zone.
Obtain the ESN of iMaster NCE-Campus.
Obtain licenses of iMaster NCE-Campus.
Load licenses.
Create an administrator.
Create sites.
Add devices, stacks, or AC groups.
Configure device management.
Configure physical links.
Configure network resources.
Configure a fabric.
Configure virtual networks.
Configure the WLAN.
Configure the egress network.
Configure access control.
Configure security services.
Configure QoS.
Configure O&M management.
Network device installation
Install network devices.
Connect cables.
Power on devices.
Configure the underlay network.
Notes: VXLAN-based large- and medium-sized virtualized campus networks have complex services. Therefore, the deployment process is complex. The deployment process provided in this slide is the general process for you reference.
The following part of this course focuses on key operations in the deployment process.

## Slide 16
VXLAN-based Virtualized Campus Network Deployment Plan
VXLAN-based Virtualized Campus Network Deployment Process and Guide
  Deployment Process
  Preparations for Deployment
  Deployment Guide

## Slide 17: Installing Servers and Software (1)
Installing iMaster NCE-Campus
Installing iMaster NCE-CampusInsight
iMaster NCE-Campus can be deployed in the on-premises scenario, Huawei public cloud scenario, and MSP-owned cloud scenario.
Large- and medium-sized campuses typically adopt the on-premises deployment mode, in which enterprises install iMaster NCE-Campus by themselves.
For more information, see iMaster NCE-Campus Product Documentation.
iMaster NCE-CampusInsight can be deployed independently or integrated with iMaster NCE-Campus.
It is recommended that iMaster NCE-CampusInsight be integrated with iMaster NCE-Campus in the CloudCampus Solution.
For more information, see iMaster NCE-CampusInsight Product Documentation.
Notes: iMaster NCE-CampusInsight can be deployed independently or integrated with iMaster NCE-Campus.
  When iMaster NCE-CampusInsight is deployed independently, network device functions (such as data reporting) must be configured on each device using commands.
  When iMaster NCE-CampusInsight is integrated with iMaster NCE-Campus, network device configurations can be automatically delivered by iMaster NCE-Campus. In addition, iMaster NCE-Campus can work with iMaster NCE-CampusInsight to implement functions such as path tracing and fault demarcation.
  It is recommended that iMaster NCE-CampusInsight be integrated with iMaster NCE-Campus in the CloudCampus Solution. To prevent the instability of the network between iMaster NCE-CampusInsight and iMaster NCE-Campus, it is recommended that iMaster NCE-CampusInsight and iMaster NCE-Campus be deployed at the same location, for example, in the same data center or equipment room.

## Slide 18: Installing Servers and Software (2)
Installing the CloudCampus APP
When installing APs, upload information about their actual installation locations to iMaster NCE-Campus for efficient O&M and value-added services based on terminal locations. The CloudCampus APP can record and upload AP information.
In addition to the deployment function, the CloudCampus APP also provides the Wi-Fi experience testing, speed testing, and video testing.
The CloudCampus APP can be obtained in either of the following methods:
Android system: Search for CloudCampus on Huawei AppGallery and install the CloudCampus APP.
Scan the QR code to download the CloudCampus APP.
Huawei AppGallery

## Slide 19: Preconfiguring Devices
HQ
AR1
CORE1
(Border)
AGG1
ACC1
(Edge)
AGG2
AP
Host 1
Host 2
Host 3
GE0/0/1
GE0/0/0
VXLAN
ACC2
(Edge)
GE0/0/2
GE0/0/3
GE0/0/1
GE0/0/24
GE0/0/24
GE0/0/23
GE0/0/1
GE0/0/2
GE0/0/2
GE0/0/1
GE0/0/1
GE0/0/17
GE0/0/20
SW1
Task | Preconfiguration Plan
Preconfigure AR1. | Complete basic configurations such as assigning VLANs, creating VLANIF interfaces, and configuring IP routing. Configure the DHCP server for plug-and-play of devices at sites. Configure the DHCP server for terminal user access. Simulate external networks, including the Internet, RD external network, and MKT external network.

## Slide 20
VXLAN-based Virtualized Campus Network Deployment Plan
VXLAN-based Virtualized Campus Network Deployment Process and Guide
  Deployment Process
  Preparations for Deployment
  Deployment Guide

## Slide 21: Creating Sites and Adding Devices
To enable network devices within the same management scope to be centrally managed on iMaster NCE-Campus, you can create a site on iMaster NCE-Campus and add these network devices to the site.
You can add devices when creating a site or after a site is created.
Site Design
VN Management
Service Deployment
Fabric Management
Network Plan
Device Management
HQ
CORE1
(Border)
AGG1
ACC1
(Edge)
AP
Host 1
Host 2
Host 3
VXLAN
ACC2
(Edge)
GE0/0/1
Notes: Note: In most cases, one site corresponds to one fabric.

## Slide 22: How to Create Sites and Add Devices
Creating sites one by one
Creating sites in a batch
Add devices manually.
1
Download a template (an Excel file) from iMaster NCE-Campus.
2
Fill in the template with site and device information.
3
Import the template to iMaster NCE-Campus.
Site Name | Campus Device Type | Device role | Device Model | Device Type | Device ESN | Device Name
HQ | LSW, AC | CORE | S5731-H24P4XC | LSW | … | CORE1
HQ | LSW, AC | AGG | S5731-H24P4XC | LSW | .. | AGG1
… | … | … | … | … | … | …
… | … | … | … | … | … | …
Create sites and import devices in a batch.
Site Design
VN Management
Service Deployment
Fabric Management
Network Plan
Device Management
Create sites one by one.
Notes: When creating sites, pay attention to the following points:
  To facilitate device management and improve service deployment efficiency, add devices on the same network of a tenant to the same site.
  You can create sites on iMaster NCE-Campus for unified O&M management. Two methods are available to create sites:
    Create sites one by one: You can create sites one by one when a small number of sites need to be added.
    Create sites in a batch: You can create sites in a batch when a large number of sites need to be added.
When adding devices, pay attention to the following points:
  On a VXLAN-based virtualized campus network, managed devices are typically LSWs (switches) and ACs (wireless access controllers).
  To add devices manually, select By Model or By ESN.
  On large- and medium-sized virtualized campus networks, the WLAN typically adopts the architecture of "AC + Fit AP". In this architecture, Fit APs are centrally managed and configured by the AC. After the AC is managed by iMaster NCE-Campus, you can be redirected from iMaster NCE-Campus to the web platform of the AC to manage Fit APs.

## Slide 23: Adding an AC Group
If standalone ACs are used, have hot standby configured, and need to be managed by iMaster NCE-Campus, then:
  Add devices to be managed to a site.
  Preconfigure hot standby through the CLI.
  After the configuration is complete, add an AC group to the site on iMaster NCE-Campus.
VRRP
Virtual-IP
CoreSwitch
AC1
AC2
192.168.1.254
VLAN102
VLAN100
VLAN100
Campus
network
AP
Site Design
VN Management
Service Deployment
Fabric Management
Network Plan
Device Management

## Slide 24: Lab: Creating a Site, Adding Devices, and Configuring the Plug-and-Play Function
Site creation and device addition
On iMaster NCE-Campus, create a single site to create the HQ site.
Add devices (CORE1, AGG1, AGG2, ACC1, ACC2, and AP1) one by one based on the device model or ESN.
Device plug-and-play (onsite operation)
Connect and power on the switches and APs on the network.
The switches obtain IP addresses and iMaster NCE-Campus address/port through AR1, and initiate registration requests to iMaster NCE-Campus. They are managed by iMaster NCE-Campus once registered.
Device management (by iMaster NCE-Campus)
Check the device registration status.
Check the physical network topology.
HQ
AR1
(DHCP server)
CORE1
AGG1
ACC1
AP
ACC2
2
1
DHCP Offer
Devices proactively register with iMaster NCE-Campus.
1
2
Devices to be managed by iMaster NCE-Campus
Site Design
VN Management
Service Deployment
Fabric Management
Network Plan
Device Management
Notes: Device plug-and-play:
  Customer pain points: In traditional network deployment, engineers need to commission network devices one by one onsite, resulting in heavy configuration workload and low efficiency.
  Solution:
    This lab demonstrates the plug-and-play function of network devices in the CloudCampus Solution. The DHCP Option solution is used to implement plug-and-play of switches. In this example, the DHCP service and related parameters must be preconfigured on AR1.
    In this step, switches on the campus network can be directly deployed using factory settings and get managed by iMaster NCE-Campus, greatly reducing the configuration workload.

## Slide 25: Configuring Network Resources: Fabric Global Resource Pool
Before creating a fabric, plan a fabric global resource pool that contains bridge domains (BDs), VXLAN network identifiers (VNIs), VLANs, and loopback interface IP address resources.
Task | Resource Pool Plan
Configure a fabric global resource pool. | Configure VLAN resources, including service VLANs (terminal access VLANs), VLANs for connecting to external networks and network service resources, and CAPWAP management VLAN. Configure loopback interface IP addresses. As the VXLAN control plane adopts BGP Ethernet VPN (EVPN), loopback interface IP addresses are required to establish BGP EVPN peer relationships between border and edge nodes. Configure BDs and VNIs for Layer 2 broadcast domain isolation in virtual networks.
External network
Network service resources
CORE1
(Border)
AGG1
ACC1
(Edge)
ACC2
(Edge)
VLAN
VLAN
VNI
VXLAN tunnel
VLAN
VLAN
AGG2
HQ
Site Design
VN Management
Service Deployment
Fabric Management
Network Plan
Device Management

## Slide 26: Lab: Configuring a Fabric Global Resource Pool
Choose Fabric Network > Network Plan. On the resource pool configuration page that is displayed, click Fabric Global Resource Pool, set parameters, and click +.
Site Design
VN Management
Service Deployment
Fabric Management
Network Plan
Device Management
iMaster NCE-Campus provides the logical topology view to help users understand the meanings of parameters.
Notes: Parameters in the fabric global resource pool:
  VLAN: Configure a service VLAN pool when you need to configure VLANs for connecting to external networks, VLANs for connecting to network service resources, CAPWAP management VLAN, and terminal access VLANs.
  Loopback interface IP address: Configure a loopback interface IP address resource pool when the underlay routing domain is automatically configured. Loopback interface IP addresses are used as the VTEP IP addresses of a VXLAN tunnel.
  Bridge Domain (BD): On a VXLAN network, VNIs can be mapped to BDs in 1:1 mode so that a BD can function as a VXLAN network entity to transmit traffic. A BD is a Layer 2 broadcast domain used to forward data packets on a VXLAN network.
  VXLAN Network Identifier (VNI): A VNI is similar to a VLAN ID and identifies a VXLAN.

## Slide 27: Configuring Network Resources: Underlay Automation Resource Pool
The underlay automation resource pool contains the IP addresses and VLAN resources used for OSPF route orchestration on the underlay network.
CORE1
AGG1
ACC1
ACC2
AGG2
HQ
OSPF
Interconnection VLAN
Interconnection IP address
Interconnection VLAN
Interconnection IP address
Interconnection VLAN
Interconnection IP address
Interconnection VLAN
Interconnection IP address
Task | Resource Pool Plan
Configure an underlay automation resource pool. | Configure interconnection VLANs, which cannot conflict with the fabric global resource pool and service VLANs for terminal user access. Configure interconnection IP addresses, which cannot conflict with the fabric global resource pool and service IP addresses for user access. The preceding resources are used for automatic orchestration of routing domains on the underlay network.
Site Design
VN Management
Service Deployment
Fabric Management
Network Plan
Device Management

## Slide 28: Lab: Configuring an Underlay Automation Resource Pool
On iMaster NCE-Campus, choose Fabric Network > Network Plan. On the resource pool configuration page that is displayed, click Underlay Automation Resource Pool, set related parameters, and click +.
Site Design
VN Management
Service Deployment
Fabric Management
Network Plan
Device Management
iMaster NCE-Campus provides the logical topology view to help users understand the meanings of parameters.
Notes: Parameters in the underlay automation resource pool:
  Interconnection VLAN: Configure an interconnection VLAN resource pool for interconnection between devices that participate in automatic routing orchestration of the underlay network in a fabric.
  Interworking IP: Configure an interconnection IP address resource pool for interconnection between devices that participate in automatic routing orchestration of the underlay network in a fabric.

## Slide 29: Configuring Policy Template Resources: User Access Authentication
In the large- and medium-sized virtualized campus network solution, you need to specify the authentication templates to be bound to wired and wireless access points during fabric access management. The authentication templates need to be planned.
The policy template resources configured on iMaster NCE-Campus typically include the RADIUS server template, Portal server template, and user authentication template.
Research
(802.1X)
Sales
(802.1X)
Guest
(802.1X)
Guest
(Portal)
CORE1
AGG1
ACC1
ACC2
AGG2
HQ
Controller built-in server
RADIUS server & Portal server
Authentication point
AP
Site Design
VN Management
Service Deployment
Fabric Management
Network Plan
Device Management

## Slide 30: Lab: Configuring User Authentication Templates
On iMaster NCE-Campus, choose Design > Basic Network Design > Template Management > Policy Template, and create and configure a RADIUS server template, a Portal server template, and user authentication templates.
Task | Procedure
Create a RADIUS server template. | Select a RADIUS server type. The iMaster NCE-Campus built-in RADIUS server is recommended. Configure the RADIUS server IP address. If the iMaster NCE-Campus built-in RADIUS server is used, you do not need to configure the RADIUS server IP address.
Create a Portal server template. | Select a Portal server type. The iMaster NCE-Campus built-in Portal server is recommended. Configure the Portal server IP address. If the iMaster NCE-Campus built-in Portal server is used, you do not need to configure the Portal server IP address. Configure the Portal server URL. If the iMaster NCE-Campus built-in Portal server is used, you do not need to configure the Portal server URL.
Create user authentication templates. | Select a user authentication mode, which is typically 802.1X authentication, MAC address authentication, or Portal authentication. A template can contain multiple authentication modes. Select the RADIUS server template or Portal server template to be bound.
Site Design
VN Management
Service Deployment
Fabric Management
Network Plan
Device Management

## Slide 31: Configuring a Fabric
A fabric is a virtual network built on top of a physical network using the VXLAN technology, and has all resources pooled.
External network
Network service
resources
CORE1
(Border)
AGG1
ACC1
(Edge)
ACC2
(Edge)
Fabric
AGG2
HQ
Task | Procedure
Configure a fabric. | Create a fabric and complete automatic deployment of an underlay network. Create an external network, that is, configure the connectivity between the fabric and external networks (including the interconnection port, interconnection VLAN, interconnection IP address, peer address, and route). Configure network service resources, that is, configure the connectivity between the fabric and network service resources (DHCP server, RADIUS server, Portal server, and other servers). The connectivity configuration includes the device IP address, interconnection VLAN, interconnection IP address, peer IP address, and interconnection port. Configure access management, that is, configure an interface on an access device to invoke an authentication template.
AP1
Site Design
VN Management
Service Deployment
Fabric Management
Network Plan
Device Management

## Slide 32: Configuring a Fabric: Creating a Fabric
You need to create a fabric and then complete basic networking configurations for the fabric, including selecting border and edge nodes as well as configuring BGP EVPN on the VXLAN control plane.
In addition, you can enable automatic routing orchestration of the underlay network when creating a fabric.
Task | Procedure
Create a fabric. | Select a networking type: centralized or distributed. Select wireless authentication devices, including wireless authentication points on the aggregation switch, core switch, and standalone AC. Add devices to the fabric and specify the devices as border and edge nodes. If VXLAN is deployed to the aggregation layer on the fabric, access switches are usually used as extended nodes. (Optional) Configure storm suppression on the fabric. To mitigate the risks caused by network storms, you are advised to enable storm suppression. (Optional) Enable terminal identification information reporting. You need to enable this function when configuring the terminal identification function. Enable automatic routing domain orchestration of the underlay network. Configure BGP EVPN. You are advised to configure the core switch that functions as a border node as a route reflector (RR).
Site Design
VN Management
Service Deployment
Fabric Management
Network Plan
Device Management

## Slide 33: Lab: Creating a Fabric (1)
Create a fabric on the iMaster NCE-Campus GUI and set the networking type.
CORE1
(Border)
AGG1
ACC1
(Edge)
ACC2
(Edge)
Fabric
AGG2
HQ
AP1
Distributed gateway networking with VXLAN deployed to the access layer
Site Design
VN Management
Service Deployment
Fabric Management
Network Plan
Device Management
Define the networking type.
Specify wireless authentication devices.
Notes: A fabric consists of core, aggregation, and access devices. An access device supports access of different network services, reducing costs and improving network device efficiency.
A virtualized campus network uses the overlay virtualization technology (VXLAN) to support multiple virtual networks on the same fabric and support flexible service deployment.
The networking type specifies the fabric deployment mode:
  Centralized: The gateway in a fabric is a centralized gateway. Traffic accessing external networks and intranet passes through the centralized gateway. In this case, only the border node can function as the centralized gateway.
  Distributed: Gateways in a fabric are distributed gateways. Traffic accessing external networks and intranet passes through different distributed gateways. In this case, both border nodes and edge nodes can function as distributed gateways.

## Slide 34: Lab: Creating a Fabric (2)
Add devices to the fabric and specify device roles.
CORE1
(Border)
AGG1
ACC1
(Edge)
ACC2
(Edge)
Fabric
AGG2
HQ
AP1
Select a specific site and corresponding devices.
Specify the roles of the devices in the fabric.
Distributed gateway networking with VXLAN deployed to the access layer
Site Design
VN Management
Service Deployment
Fabric Management
Network Plan
Device Management
Notes: Role: Specify the roles of devices in the fabric, including the border node, edge node, and extended node. By default, the role of a device is an extended node.

## Slide 35: Lab: Creating a Fabric (3)
CORE1
(Border)
AGG1
ACC1
(Edge)
ACC2
(Edge)
AGG2
HQ
AP1
OSPF
Area 0
Complete automatic deployment of the underlay network on iMaster NCE-Campus.
Enable automatic routing domain configuration.
Define OSPF areas and packet authentication.
Configuring a single OSPF area
Site Design
VN Management
Service Deployment
Fabric Management
Network Plan
Device Management
Notes: Automatic routing domain configuration: After this function is enabled, the underlay network is automatically configured. You can specify sites for automatic routing domain configuration and specify OSPF route parameters. Currently, the following parameters are supported:
  Domain: In single-domain mode, all devices belong to area 0. In multi-domain mode, all edge nodes are located in their respective non-backbone areas, and border nodes are interconnected through the backbone area (area 0).
  Network type: You can specify the OSPF network type to broadcast, P2MP, or P2P.
  Encryption: You can set the encryption mode between adjacent devices to HMAC-SHA256, MD5, or None.
  Key: It refers to the authentication key ID used for ciphertext authentication on an interface, and must be consistent with that of the peer device. The value is an integer in the range from 1 to 255.
  Password: It specifies the ciphertext authentication key. The value is a string of 1 to 255 characters and cannot contain spaces.
  Confirm password: You need to enter the ciphertext authentication key again for confirmation.
  OSPF graceful: You can enable OSPF GR.

## Slide 36: Lab: Creating a Fabric (4)
After this step is complete, a fabric is successfully created based on the physical network, and the underlay network configuration (such as interconnection between network devices and OSPF configuration) is automatically completed on iMaster NCE-Campus, laying a foundation for creating virtual networks.
CORE1
(Border)
AGG1
ACC1
(Edge)
ACC2
(Edge)
AGG2
HQ
AP1
BGP EVPN
Configure BGP EVPN on iMaster NCE-Campus.
Define BGP EVPN parameters.
Site Design
VN Management
Service Deployment
Fabric Management
Network Plan
Device Management
Notes: AS number: You can specify the BGP AS number used on a fabric.
After a fabric is created, the underlay network can be automatically deployed, and configurations such as VLANIF interfaces, loopback interfaces, VTEP IP addresses, and routes required for establishing a BGP EVPN can be automatically provisioned. iMaster NCE-Campus allocates resources from the fabric global resource pool and underlay automation resource pool to devices.

## Slide 37: Configuring a Fabric: Creating an External Network
In the fabric resource model design, external networks are created on border nodes so that terminals on the campus network can access external networks such as the Internet.
Three types of external network resources are defined: Layer 3 shared egress, Layer 3 exclusive egress, and Layer 2 shared egress. If the user gateway is located in the fabric, the Layer 3 shared egress or Layer 3 exclusive egress is used.
  Layer 3 shared egress: Multiple virtual networks on the fabric share a Layer 3 egress to communicate with the egress device. The Layer 3 shared egress helps save interconnection VLAN and IP resources and applies to scenarios where there are low requirements on security control policies between virtual networks.
  Layer 3 exclusive egress: Each virtual network on the fabric exclusively uses a Layer 3 egress to communicate with the egress device. In this case, multiple security zones are typically configured on the firewall, each corresponding to one Layer 3 exclusive egress. The traffic of different virtual networks to the firewall is isolated from each other.
Task | Procedure
Create an external network. | Select the type of the connection with the external network. Select an external network resource type. Configure interconnection physical interfaces, VLANs, and IP addresses. Configure a routing protocol for interconnection.
Site Design
VN Management
Service Deployment
Fabric Management
Network Plan
Device Management

## Slide 38: Lab: Creating an External Network (1)
Create an external network for the fabric and select the egress connection mode.
External network
Network service
resources
CORE1
(Border)
AGG1
ACC1
(Edge)
ACC2
(Edge)
Fabric
AGG2
HQ
AP1
Site Design
VN Management
Service Deployment
Fabric Management
Network Plan
Device Management

## Slide 39: Lab: Creating an External Network (2)
Define the external route to the external network.
Complete basic configurations of the external network, including specifying the external network name, determining whether to connect the external network to the Internet (whether to use the default route as the external route), and configuring the external route.
External network
Network service
resources
CORE1
(Border)
AGG1
ACC1
(Edge)
ACC2
(Edge)
Fabric
AGG2
HQ
AP1
Site Design
VN Management
Service Deployment
Fabric Management
Network Plan
Device Management
Notes: Basic information:
  If Internet connection is enabled, iMaster NCE-Campus uses a default route to direct traffic to the corresponding external network. If Internet connection is disabled, you need to specify a route prefix.

## Slide 40: Lab: Creating an External Network (3)
External network
Network service
resources
CORE1
(Border)
AGG1
ACC1
(Edge)
ACC2
(Edge)
Fabric
AGG2
HQ
AP1
External route
Local port
Local IP address
Local VLAN
Peer IP address
Configure interconnection information for the external network.
Configure routing information for the external network.
Site Design
VN Management
Service Deployment
Fabric Management
Network Plan
Device Management
Notes: Interconnection information:
  Select the border device to be connected to an external network, and select the interconnection interface, interconnection IP address, and interconnection VLAN.
  Note: The configured interconnection IP address cannot conflict with the IP address in the underlay automation resource pool. The configured interconnection VLAN belongs to the fabric global resource pool.
Routing information:
  After Deliver static routes is enabled, iMaster NCE-Campus delivers static routes destined for the external network to the border device (only when the external network is invoked by the virtual network).

## Slide 41: Configuring a Fabric: Creating Network Service Resources
In the fabric resource model design, network service resources are created on a border node so that service terminals on the campus network can access service resources, such as the DHCP server and NAC server, in the network management zone.
You can create multiple network service resources or add IP addresses for accessing multiple network service resources to a network service resource model.
If only a few service resources in the network management zone need to be accessed, you are advised to plan these resources in the same network service resource model. This saves interconnection VLANs and IP addresses and simplifies routing configuration in the network management zone.
Task | Procedure
Create network service resources. | Select a server type, which can be DHCP server, third-party RADIUS server, and third-party Portal server. Configure the IP addresses for accessing network service resources, such as the DHCP service address and iMaster NCE-Campus southbound IP address. Select an interconnection scenario, which can be directly connected to a server or directly connected to a switch. Configure interconnection physical interfaces, VLANs, and IP addresses.
Site Design
VN Management
Service Deployment
Fabric Management
Network Plan
Device Management

## Slide 42: Lab: Creating Network Service Resources (1)
Create a network service resource for the fabric and configure the server, including defining the name, type, and IP address of the connected server.
Define the server type.
Define the server IP address.
Define the device IP address segment for interconnection with the server.
External network
Network service resources
CORE1
(Border)
AGG1
ACC1
(Edge)
ACC2
(Edge)
Fabric
AGG2
HQ
AP1
Site Design
VN Management
Service Deployment
Fabric Management
Network Plan
Device Management
Notes: Server configuration:
  Server type: server resource specified by the network service resource. In this example, the defined network service resource is a DHCP server.
  DHCP server: IPv4 and/or IPv6 address of a DHCP server.
  Server interconnection address pool: If an IPv6 address pool is configured for the DHCP server, this parameter is mandatory. If only an IPv4 address pool is configured for the DHCP server, this parameter is optional.

## Slide 43: Lab: Creating Network Service Resources (2)
Complete device configurations, including selecting the scenario and configuring interconnection information.
External network
Network service resources
CORE1
(Border)
AGG1
ACC1
(Edge)
ACC2
(Edge)
Fabric
AGG2
HQ
AP1
Local port
Local VLAN
Local IP address
Peer IP address
Select an interconnection scenario.
Configure interconnection information.
Site Design
VN Management
Service Deployment
Fabric Management
Network Plan
Device Management
Notes: Device configuration:
  If Directly connected to a switch is selected, the border node adds the interconnection port to the interconnection VLAN in tagged mode to connect to network resources. If Directly connected to a server is selected, the switch adds the interconnection port to the interconnection VLAN in untagged mode.
  Interconnection device: Select the border node (CORE1). The device functions as a border node that connects the fabric to the external network service resource.
  External port: Select the port used by the border node to connect to the network service resource.
  External VLAN: Select the VLAN used by the border node to connect to the network service resource.
  Interconnection IPv4/IPv6 address: Select the IP address of the port used by the border node to connect to the network service resource.
  Peer IPv4/IPv6 address: Select the IP address of the peer device.
  Mask: Select the network mask.
Note: The configured interconnection IP address cannot conflict with the IP address in the underlay automation resource pool. The configured interconnection VLAN belongs to the fabric global resource pool.

## Slide 44: Configuring a Fabric: Configuring Access Management
Access control needs to be deployed on the campus network to authenticate access users, including 802.1X authentication, MAC address authentication, and Portal authentication. The implementation of 802.1X authentication and MAC address authentication requires the use of the RADIUS server, whereas the implementation of Portal authentication requires the use of the RADIUS server and Portal server.
Configuring access management for the fabric is to configure authentication control points and plan access point resources, which will be used during virtual network creation.
Wired access point resources refer to switch interfaces connected to terminals, and wireless access point resources refer to SSIDs connected to terminals.
  During access management configuration for the fabric, three connection types are defined for access ports of switches:
    Extended AP: Huawei Fit APs, which can be managed by iMaster NCE-Campus.
    Extended access switch: Huawei switches, which can be managed by iMaster NCE-Campus.
    Terminal (PC, Phone, dumb terminal, non-fabric extended switch/AP): user terminals, switches and APs that cannot be managed by iMaster NCE-Campus, and switches that can be managed by iMaster NCE-Campus but do not support fabric extension.
Access management configuration for the fabric varies depending on the gateway solution.
Site Design
VN Management
Service Deployment
Fabric Management
Network Plan
Device Management

## Slide 45: Lab: Configuring Fabric Access Management (1)
CORE1
(Border)
AGG1
ACC1
(Edge)
ACC2
(Edge)
Fabric
AGG2
HQ
AP1
Configure access management for wired access terminals and activate authentication on a switch interface.
Site Design
VN Management
Service Deployment
Fabric Management
Network Plan
Device Management
Authentication point

## Slide 46: Lab: Configuring Fabric Access Management (2)
CORE1
(Border)
AGG1
ACC1
(Edge)
ACC2
(Edge)
Fabric
AGG2
HQ
AP1
Authentication point
To configure access management for wireless access terminals, configure the CAPWAP management VLAN and CAPWAP management IP address so that switches can establish CAPWAP tunnels with APs and APs can obtain IP addresses and get onboarded.
Configure an SSID and a wireless authentication template for terminal access.
Site Design
VN Management
Service Deployment
Fabric Management
Network Plan
Device Management
Notes: Configure the CAPWAP management VLAN and CAPWAP management IP address. That is, create the management VLAN and CAPWAP tunnel source interface in the WLAN service, and assign an IP address to the source interface. APs obtain IP addresses from the interface address pool.
Note: The configured management IP address cannot conflict with the IP address in the underlay automation resource pool. The configured management VLAN belongs to the fabric global resource pool.

## Slide 47: Virtual Network Management
After a fabric is created, you can select network resources in the fabric to create virtual networks.
To enable access users in different virtual networks to communicate with each other, you need to configure communication between virtual networks.
HQ
CORE1
(Border)
AGG1
ACC1
(Edge)
AGG2
AP
Host 1
Host 2
Host 3
VXLAN
ACC2
(Edge)
OA_VN
RD_VN
MKT_VN
Task | Procedure
VN management | Create virtual networks. Different virtual networks represent services of different users and can be used to isolate services of these users. Configure communication between virtual networks to ensure that there are reachable routes between users in different virtual networks on the underlay network.
External network
Network service
resources
Site Design
VN Management
Service Deployment
Fabric Management
Network Plan
Device Management

## Slide 48: Fabric Resource Pools and Resource Invoking During Virtual Network Creation
Fabric Resource Pool | How to Invoke Resources in the Resource Pool During Virtual Network Creation
VLAN resource pool, which is used in scenarios where terminals are connected to virtual networks and virtual networks communicate with external networks. The VLAN resource pool is planned during the configuration of the fabric global resource pool. | When creating a user gateway in a virtual network, select a resource from the fabric global resource pool to configure a user VLAN.
BD and VNI resource pools, which are used to divide Layer 2 broadcast domains in a virtual network and configure VBDIF interfaces as the gateway interfaces of user subnets. The BD and VNI resource pools are planned during the configuration of the fabric global resource pool. | When a user gateway is created in a virtual network, resources in the BD and VNI resource pools are automatically invoked to create a BD and the corresponding VBDIF interface.
User access point resource pool, which is planned during fabric access management configuration. This resource pool includes the authentication modes that can be configured on access points. | When configuring user access in a virtual network, you can select planned access point resources.
Egress pool, which contains the external resources that can be used by virtual networks. Two types of external resources are created during fabric configuration: External networks: used for virtual networks to communicate externally Network service resources: used for virtual networks to communicate with the authentication server and DHCP server, etc. | When creating a virtual network, you can select external networks and network service resources.
Site Design
VN Management
Service Deployment
Fabric Management
Network Plan
Device Management

## Slide 49: Virtual Network Management: Creating a Virtual Network
Creating a virtual network is to create a VPN instance to isolate different services.
Task | Procedure
Create a virtual network. | (Optional) Select an external network for communication between the virtual network and external network (this step is typically performed). (Optional) Select network service resources for communication between the virtual network and network service resources (this step is typically performed). Configure a user gateway, which can be manually specified or automatically allocated. Configure wired access: Select the access ports configured during fabric access management configuration, and add the ports to the service VLAN configured on the user gateway. Configure wireless access: Select the AC that connects to the wireless user subnet. Then the service VLAN configured on the user gateway will be delivered to the AC.
Site Design
VN Management
Service Deployment
Fabric Management
Network Plan
Device Management

## Slide 50: Lab: Creating a Virtual Network (1)
Create a virtual network, define the virtual network name and user gateway location, and configure the external network and network service resources to be connected to the virtual network.
HQ
CORE1
(Border)
AGG1
ACC1
(Edge)
AGG2
AP
Host 1
(Sales)
172.16.3.0/24
Host 2
(Research)
172.16.2.0/24
Host 3
(Guest)
172.16.1.0/24
VXLAN
ACC2
(Edge)
OA_VN
RD_VN
MKT_VN
External network
Network service
resources
Site Design
VN Management
Service Deployment
Fabric Management
Network Plan
Device Management

## Slide 51: Lab: Creating a Virtual Network (2)
Define user network segments for the virtual network. Network segments can be manually created one by one by the network administrator or created in a batch through automatic allocation.
HQ
CORE1
(Border)
AGG1
ACC1
(Edge)
AGG2
AP
Host 1
(Sales)
172.16.3.0/24
Host 2
(Research)
172.16.2.0/24
Host 3
(Guest)
172.16.1.0/24
VXLAN
ACC2
(Edge)
OA_VN
RD_VN
External network
Network service
resources
Site Design
VN Management
Service Deployment
Fabric Management
Network Plan
Device Management
MKT_VN

## Slide 52: Lab: Creating a Virtual Network (3)
Configure wired access.
Configure wireless access.
HQ
CORE1
(Border)
AGG1
ACC1
(Edge)
AGG2
AP
Host 1
(Sales)
172.16.3.0/24
Host 2
(Research)
172.16.2.0/24
Host 3
(Guest)
172.16.1.0/24
VXLAN
ACC2
(Edge)
OA_VN
RD_VN
MKT_VN
External network
Network service
resources
Site Design
VN Management
Service Deployment
Fabric Management
Network Plan
Device Management
Notes: User access is configured on the access points of the current virtual network.
  Wired access: Users on the OA virtual network need to access the network through ACC1 and ACC2 and need to be authenticated. Therefore, you need to configure wired access on the interfaces on which authentication has been enabled on the two switches.
  Wireless access: Configure wireless access on ACC2. ACC2 is a switch that provides the native AC function and manages APs through the AC to provide wireless access.
    In wireless access configuration, the AC needs to function as the authentication control point for fabric access management configuration. This is applicable to the distributed gateway scenario that requires the unified authentication control point for wired and wireless users.

## Slide 53: Virtual Network Management: Configuring Communication Between Virtual Networks
By default, virtual networks are isolated from each other. However, in some scenarios, they may need to communicate with each other, so reachable routes must be configured between them.
Configuring communication between virtual networks is to create static routes for VPN instances so that access users in different virtual networks can communicate with each other.
Task | Procedure
Configure communication between virtual networks. | Select interconnection devices. Select the interworking mode, including full interworking and partial interworking. Configure the source virtual network, source IPv4 prefix, destination virtual network, and destination IPv4 prefix.
Site Design
VN Management
Service Deployment
Fabric Management
Network Plan
Device Management

## Slide 54: Lab: Configuring Communication Between Virtual Networks
Access the VN Interwork page, and click Add to configure communication between virtual networks.
RD_VN
MKT_VN
Fabric
Reachable routes
Sales
172.16.3.0/24
Research
172.16.2.0/24
Site Design
VN Management
Service Deployment
Fabric Management
Network Plan
Device Management

## Slide 55: Service Deployment
On large-sized campus networks, users are usually allowed access from any location, any VLAN, and any IP network segment with controlled network access rights.
Task | Procedure
Service deployment | Configure free mobility, including creating security groups and a policy control matrix. Configure access authentication, including creating user authentication accounts, authentication rules, authorization results, authorization rules, and Portal page management. Deliver WLAN services.
RD_VN
MKT_VN
Fabric
Research
(802.1X)
Sales
(802.1X)
OA_VN
Guest
(802.1X)
Guest
(Portal)
Guest
security group
Research
security group
Sales
security group
Security group-based policy control matrix
Site Design
VN Management
Service Deployment
Fabric Management
Network Plan
Device Management

## Slide 56: Free Mobility: Creating Security Groups
A security group is an entity unit for permission control. Users or network service resources are allocated to different security groups. The access permissions between security groups are configured for user permission management on the network.
RD_VN
MKT_VN
Fabric
Research
(802.1X)
Sales
(802.1X)
OA_VN
Guest
(802.1X)
Guest
(Portal)
Guest
security group
Research
security group
Sales
security group
Site Design
VN Management
Service Deployment
Fabric Management
Network Plan
Device Management

## Slide 57: Free Mobility: Creating a Policy Control Matrix
Administrators can define network-wide control inter-group policies based on security groups. An inter-group control policy controls access between groups.
RD_VN
MKT_VN
Fabric
Research
(802.1X)
Sales
(802.1X)
OA_VN
Guest
(802.1X)
Guest
(Portal)
Guest
security group
Research
security group
Sales
security group
Security group-based policy control matrix
Select policy enforcement points.
The policy control matrix: implements visualized management of communication policies between different security groups on the campus network.
Site Design
VN Management
Service Deployment
Fabric Management
Network Plan
Device Management
Notes: When multiple policies are configured to control access between a source security group and multiple destination security groups, the sequence in which these policies are matched can be determined based on the policy priority. For example, if destination security groups are resource groups where the destination IP addresses of the resources may be the same, you need to manually adjust the priority of a specific policy to ensure that this policy is matched first.

## Slide 58: Access Authentication
Task | Procedure
Configure 802.1X authentication. | Create user authentication accounts. Configure authentication rules. Configure authorization results and authorization rules.
Task | Procedure
Configure Portal authentication. | Create user authentication accounts. Configure authentication rules. Configure authorization results and authorization rules.
(Optional) Configure a MAC authentication exemption policy. | To enable a user client to be exempt from authentication based on its MAC address within a period after the client passes Portal authentication for the first time, configure a MAC authentication exemption policy in the user control policy.
802.1X authentication
802.1X is a port-based network access control protocol. It verifies user identities and controls access permissions of users on ports of LAN access devices.
When iMaster NCE-Campus functions as a RADIUS server, 802.1X authentication configuration on the server is illustrated in the following table:
Portal authentication
Portal authentication is also known as web authentication, and websites for Portal authentication are referred to as web portals. When a user accesses the network, the user must be authenticated on the web portal. If the user fails the authentication, the user can access only specified network resources. The user can access other network resources only after being authenticated successfully.
When iMaster NCE-Campus functions as the Portal server and RADIUS server, Portal authentication configuration on the server is illustrated in the following table:
Site Design
VN Management
Service Deployment
Fabric Management
Network Plan
Device Management

## Slide 59: Lab: Adding an Account
In the enterprise employee access scenario, user name and password authentication can be used to implement user access.
During 802.1X authentication and Portal authentication, users need to enter account information for authentication.
  Account information includes a user name and password, which are preconfigured by an administrator on iMaster NCE-Campus.
Site Design
VN Management
Service Deployment
Fabric Management
Network Plan
Device Management

## Slide 60: Lab: Configuring Authentication Rules
You can configure authentication rules to authenticate clients and users who access the network, ensuring network security.
iMaster NCE-Campus has a default authentication rule named default. According to the rule, the local data source is used for authentication.
Site Design
VN Management
Service Deployment
Fabric Management
Network Plan
Device Management
Notes: Default authentication rule default: The default rule can be modified to allow the use of a third-party data source for authentication.

## Slide 61: Lab: Configuring Authorization Results
When configuring access authentication, you need to configure the rights obtained by users after they pass authentication.
In the authorization result, you can define the rights to be authorized to users, such as ACLs, security groups, URL filtering policies, and VLANs.
Site Design
VN Management
Service Deployment
Fabric Management
Network Plan
Device Management
Notes: After configuring authorization results, you need to bind the results to created sites.
iMaster NCE-Campus provides two default authorization results: permit access and deny access. Once selected, the default authorization result takes effect for all sites and cannot be modified or deleted.

## Slide 62: Lab: Configuring Authorization Rules
When authorizing a user who passes the authentication, the system matches the user against an authorization rule and grants specific permissions to the user based on the matching rule.
Configure the authorization rule name, authentication mode, and access mode.
Match users against account information and add user accounts.
Bind the authorization result to the authorization rule.
Site Design
VN Management
Service Deployment
Fabric Management
Network Plan
Device Management
Notes: An authorization rule defines authorization conditions. When a user matches the conditions, the user obtains the corresponding authorization result. That is, the authorization result specifies the rights of the user after the user is authenticated successfully.
iMaster NCE-Campus provides the default authorization rule named default with the authorization result of deny access. The default authorization result can be modified to allow the use of another authorization result.

## Slide 63: WLAN Service (Distributed Gateway)
In the distributed gateway solution, if VXLAN to the access layer is deployed on a fabric, an edge device provides the native AC function, and APs get onboarded on the edge device, then the APs need to be managed by the edge device.
WLAN service configuration: You need to configure an SSID on the AC for APs to provide Wi-Fi signals for guest access, and configure Portal authentication for guests who attempt to connect to the SSID.
Task | Procedure
WLAN service delivery (on an edge node's web UI) | Configure an SSID profile. Configure a VAP profile, and bind it to the SSID profile and authentication template. Bind the VAP profile to an AP group.
Site Design
VN Management
Service Deployment
Fabric Management
Network Plan
Device Management

## Slide 64
(Essay) Which site creation methods are supported by iMaster NCE-Campus?
(Multiple-choice) Which of the following parameters can be entered in the fabric global resource pool? ( )
  VLAN
  Loopback interface IP address
  BD
  VNI
Notes: Answer:
  Create sites one by one: You can create sites one by one when a small number of sites need to be added.
  Create sites in a batch: You can create sites in a batch when a large number of sites need to be added.
Answer: ABCD

## Slide 65
This course introduces the VXLAN-based virtualized campus network deployment process and helps trainees understand the functions of the VXLAN-based virtualized campus network solution and build network deployment skills through hands-on labs.
Upon completion of this course, you will be able to deploy the VXLAN-based virtualized campus network solution and perform network O&M and management.