## Slide 1
V100R019C10
Zhu Shigeng/00261992
2019-11-25
Wan Yunfei/00364921
New
Shi Miaomiao/swx791350
2020-11-16
Update

## Slide 2: Small- and Medium-Sized Campus Network Design Guide

## Slide 3
A campus network generally refers to the intranet of an enterprise or organization, which aims to ensure more efficient operation of main services.
In terms of network scale, campus networks can be classified into medium- and large-sized campus networks and small- and medium-sized campus networks.
With the development of technologies and digitalization of industries, services in small- and medium-scale scenarios, such as chain stores and branch offices, are gradually connected to the enterprise intranet through cloud-managed networks.
Cloud-managed networks have become the trend in constructing small- and medium-sized campus networks. Cloud-based solutions help enterprises improve management efficiency and build networks that can quickly support the development of new services.
This document mainly describes the design and planning methods of small- and medium-sized campus networks in terms of the solution architecture, technical solution comparison, engineering design suggestions, and O&M.

## Slide 4
Upon completion of this course, you will be able to:
  Describe service requirements, development trend, and challenges of small- and medium-sized campus networks.
  Describe the architecture of Huawei CloudCampus Solution for small- and medium-sized campus networks.
  Describe typical solutions for small- and medium-sized campus networks.
  Independently design the CloudCampus solution for small- and medium-sized campus networks based on user requirements, including networking design, physical network design, site deployment design, basic network service design, WLAN design, access control design, QoS design, and security design.

## Slide 5
Service Requirements and Challenges of Small- and Medium-Sized Campus Networks
Introduction to Huawei CloudCampus Solution
Huawei CloudCampus Solution Design for Small- and Medium-Sized Campus Networks
Typical Industry Application Scenarios

## Slide 6: Technology Development Trend
Network cloudification
IoT
Due to evolution to the cloud architecture, enterprises can focus on services without the need to pay too much attention to the IT architecture construction.
To support service cloudification, enterprises need to create a ubiquitous, intelligent, controllable, and on-demand network.
The network needs to become more a service than a solution.
Cloud security
The cloud security becomes increasingly important.
Facing cloudification, enterprises are subject to attacks that are different from traditional networks when providing various services.
Security has shifted from passive defense to proactive defense.
Detection and response have become as important as defense.
The use of IoT directly leads to a huge increase in the number and types of terminals that access the networks, and these terminals generate a large amount of data.
Diversified IoT sensing networks need to be smoothly connected to the existing campus network.
The types of terminals connected to the campus network become complex, and the network becomes a converged network with multiple types of terminals and media.
Notes: Network cloudification
  Cloud computing has completely changed the production mode of enterprises over the past decade. A large number of services are deployed and operate on the cloud, enabling enterprises to quickly launch new services. Due to evolution to the cloud architecture, enterprises can focus on services without the need to pay too much attention to the IT architecture construction.
  As the pipe, the most important part in the cloud-pipe-device architecture, the network plays a decisive role in user experience. To support service cloudification, enterprises need to create a ubiquitous, intelligent, controllable, and on-demand network. The traditional network architecture cannot adapt to cloud transformation. The network needs to be more a service than a solution, which is not only the business value brought by network cloudification to enterprises but also the trend of network cloudification.
  Network cloudification is an important method to build service-based networks. With IaaS, enterprises no longer need to repeatedly construct infrastructure. Similarly, with network cloudification, enterprises simply need to consider the functions a network needs to provide and no longer need to care about the architecture, location, or function implementation of networks. In this way, enterprises can fully focus on services.
Cloud security
  Security and ICT are closely related. Cloud services not only change the service mode, but also change security boundaries. As service systems and networks undergo a closed-to-open transition, the importance of cloud security continues to increase.
  In the trend of cloudification, enterprises are subject to attacks that are fundamentally different from traditional networks when providing various services. Attacks are no longer from only viruses but a combination of multiple attacking methods. Enterprises have to quickly identify the attack behavior and the time of the attack, so that they can take measures promptly to minimize the loss. Therefore, security investment has changed significantly in recent years, and security has shifted from passive defense to proactive defense.

## Slide 7
Notes: IoT
  In recent years, IoT applications have become increasingly mature and been widely used. Examples include the positioning of goods in large warehouses, campus asset management, and parking navigation.
  The use of IoT on a campus network directly leads to a huge increase in the number and types of terminals that access the network. Therefore, a large amount of data needs to be transmitted and stored.
  Currently, there are various types of IoT sensing technologies, for example, Bluetooth, ZigBee, and Radio Frequency Identification (RFID), all of which have their respective application scenarios. How to smoothly connect these diversified IoT sensing networks to the existing campus network is a pressing issue to address.
  With IoT applications deployed on the campus network, the types of terminals connected to the network become complex. The network is not just pure Ethernet any longer but a converged network with multiple types of terminals and media.

## Slide 8: Service Requirements and Challenges of Small- and Medium-Sized Campus Networks
Industry changes accelerate, bringing the following changes in campus network service requirements
Network cloudification brings rapid development in new ICT technologies, such as cloud computing, cloud security, big data, and IoT, leading to tremendous changes in all industries.
Traditional retail industry such as shopping malls and supermarkets often offer free Wi-Fi as a way to attract and retain customers, and they also use wireless positioning and customer flow analysis to carry out precision marketing.
In education sector, electronic classrooms are becoming more and more popular, and various multimedia teaching methods can stimulate students' interest.
Small- and medium-sized enterprises (SMEs) implement simplified service deployment and fast provisioning through cloud management network interconnection, remote access, and mobile office, as well as unified cloud data management and analysis.
However, an increasing number of network nodes bring complex requirements.
Traditional deployment and management solutions have the following problems
Low deployment efficiency slows down service provisioning
Site survey, planning, deployment, software commissioning, configuration, and optimization must be completed onsite by professional IT personnel.
Complex network management causes high OPEX
Local professional O&M results in low O&M efficiency and high labor costs. The network management system (NMS), policy control server, charging system, and data analysis platform are deployed independently, causing high management and maintenance costs.
Poor network openness
The open data provided by multiple management systems of the traditional network needs to be integrated. In addition, due to the incompatibility of APIs, the network and applications are connected at a far slower speed than application development.
Notes: OPEX: operating expense, such as the management, office, employee salary, and advertising expenses of an enterprise
API: Application Programming Interface

## Slide 9: Requirement Analysis for Small- and Medium-Sized Campus Networks
Plug-and-play network devices improve deployment efficiency
Centrally delivers configurations of multiple sites, reducing onsite configuration and commissioning workload and improving deployment efficiency.
Implements plug-and-play of network devices and on-demand expansion, requiring low costs for upgrades.
Network devices at a site
Unified management and centralized configuration
Plug-and-play and on-demand expansion
Cloud-based centralized and simplified O&M
Centrally manages scattered campus branches on the cloud through the Internet.
Integrates multiple automation tools for troubleshooting, monitoring, and other management operations, so as to implement remote automated O&M.
Centralized cloud management of multiple branches and automated remote O&M
Site network 1
Site network 2
Site network N
Open APIs accelerate business application integration
Interconnects with multiple management systems to achieve unified network management through open APIs and big data analytics capabilities.
Provides more value-added applications to help digital transformation of enterprises.
Site network
Cloud management platform
Site network
Site network
Open APIs and big data analytics capabilities
Digitalization leads to changes in network models, accelerating network transformation to cloud-based network management.

## Slide 10
Service Requirements and Challenges of Small- and Medium-Sized Campus Networks
Introduction to Huawei CloudCampus Solution
Huawei CloudCampus Solution Design for Small- and Medium-Sized Campus Networks
Typical Industry Application Scenarios

## Slide 11: Huawei Cloud Managed Network, Enabling Digital Operations with Ultimate Experience
Ultra-broadband connection, improving network and application quality
All-scenario WLAN, ensuring high bandwidth, high concurrency, and low latency
Secure and reliable platform and network in compliance with laws and regulations of the industry and related countries
Open APIs for industry-specific applications, accelerating digital transformation
Simplified management, reducing OPEX
WLAN Planner: customized network planning templates and automatic generation of network planning reports
Diversified scenario-based packages: topology + device models + parameters, implementing one-stop configuration
Various O&M methods based on GIS maps, logical topologies, and mobile apps
Online and centralized inspection of multiple branches and automatic report generation
AI-powered cloud-based Intelligent O&M
Intelligent network O&M: proactively predicts potential faults, ensuring user and application access experience
SD-WAN: intelligently ensures WAN interconnection of key services, bringing ultimate experience to branches
Multi-tenant network
iMaster NCE
Value-added SaaS
Industry applications
Notes: SaaS: Software as a Service
GIS: Geographic Information System

## Slide 12: Simplified Full-Lifecycle Management
Procurement
Manual order placement
Scenario-based package
Self-service order placement
Network planning
Manual 2D planning
3D
Online network planning
Acceptance
Mobile app
One-click acceptance
Manual inspection
O&M
Manual fault locating
Intelligent O&M
Fault self-diagnosis
Deployment
Onsite deployment
Deployment by scanning barcodes using a mobile app
Automatic delivery of scenario-based configurations
Cloud managed network
Traditional network

## Slide 13: Architecture of Huawei CloudCampus Solution for Small- and Medium-Sized Campus Networks
Hotel
Micro store
Supermarket/Shopping mall
Firewall
Switch
AP
AP
AP
Firewall
Switch
Central AP
RU
Firewall
AR
Shopping center, primary/secondary education
Firewall
Switch
DCN
AR
Multi-tenant network
iMaster NCE
Value-added SaaS
Internet
Internet
Internet
Internet
Big data analytics
Customer flow analysis
Third-party authentication and accounting
APP
...
RESTful API
WAC
Huawei public cloud scenario
MSP-owned cloud scenario
On-premises scenario
Cloud-based network planning
Cloud-based deployment
Cloud-based O&M
Cloud-based inspection
Notes: Huawei CloudCampus Solution for small- and medium-sized campus networks uses cloud computing technology to implement automatic and centralized network management, and provides data collection and analysis capabilities that are unavailable on traditional networks, so as to achieve network (LAN/WLAN) as a service (NaaS).

## Slide 14
Notes: There are three layers in the architecture of Huawei CloudCampus Solution for small- and medium-sized campus networks: multi-tenant network, iMaster NCE, and value-added SaaS platform.
  Multi-tenant network: It consists of hundreds of network devices, including APs, switches, firewalls, and ARs. It is deployed at the customer side to provide user access.
  Cloud management platform: iMaster NCE-Campus, an SDN controller, is the core component of the CloudCampus Solution. It is also a cloud-based network management, O&M, and control system. In addition to basic management and configuration for cloud-based devices, remote O&M and monitoring, and user admission control, iMaster NCE-Campus can implement various VASs based on the big data platform.
  iMaster NCE-CampusInsight: It is an intelligent network analysis engine that provides intelligent O&M services for user networks. iMaster NCE-CampusInsight integrates AI to the O&M. Based on data such as device performance indicators and terminal logs, iMaster NCE-CampusInsight digitizes user experience on the network through big data analytics, AI algorithms, and more advanced analysis technologies, helping customers detect network problems in a timely manner and improve user experience.
  Value-added SaaS platform: iMaster NCE-Campus provides open APIs to interconnect with other service systems (such as the big data platform) to offer tenants a variety of value-added application services, such as customer flow analysis, business Portal push, electronic shelf label (ESL), asset management, and medical IoT.
Huawei CloudCampus Solution applies to three deployment scenarios: Huawei public cloud, MSP-owned cloud, and on-premises. The on-premises scenario applies to large- and medium-sized campus networks. The Huawei public cloud and MSP-owned cloud scenarios apply to small- and medium-sized campus networks.

## Slide 15: Highlights of Huawei CloudCampus Solution for Small- and Medium-Sized Campus Networks
Automatic deployment: Devices can be easily and quickly deployed.
Cloud-based network planning and mobile O&M: WLAN design and device O&M are simplified.
Diversified product portfolios: Huawei provides different product portfolios, including full series of network devices (switches, firewalls, ARs, and APs), meeting diversified network requirements of tenants.
Dual-working-mode: All network devices used in this solution can work in either cloud-based or traditional management mode. Tenants can implement cloud-based network management after devices are upgraded.
VASs: Terminal behavior analysis is a value-added application of iMaster NCE-Campus. More VASs can be developed based on terminal behavior analysis.

## Slide 16
Service Requirements and Challenges of Small- and Medium-Sized Campus Networks
Introduction to Huawei CloudCampus Solution
Huawei CloudCampus Solution Design for Small- and Medium-Sized Campus Networks
  Networking Solution Design
  Network Design
  QoS and Security Design
Typical Industry Application Scenarios

## Slide 17: Solution Design for Small- and Medium-Sized Campus Networks
2.Network design
Administrator design
Physical network design
Network deployment design
Basic service design
WLAN design
Access control design
3.QoS design
Rate limiting
Wireless QoS
4.Security design
Egress security design
Intranet security (wired network)
Intranet security (wireless network)
1.Networking solution design
Single AP, AR, or firewall
AR + AP
Firewall + AP
AR + L2 switch + AP
Firewall + L2 switch + AP
AR + L2 switch + central AP + RU
Firewall + L2 switch + central AP + RU
Notes: The roadmap of designing the architecture of Huawei CloudCampus Solution for small- and medium-sized campus networks is as follows:
  Construct a cloud campus communication network that features unified bearing, on-demand definition, and elastic scaling. Then determine the networking scheme of the multi-tenant network based on user requirements and application scenarios, and conduct the network design according to the actual service requirements of users, including the physical network design, basic network service design, WLAN service design, and user access control design.
  After the network design is complete, use a centralized cloud management system to implement automatic management and intelligent analysis of the network with automated deployment and intelligent O&M features. In addition, to meet requirements of basic network attributes such as security, reliability, and openness, the design in network security and interconnection with other value-added platforms must also be considered.

## Slide 18: Design Principles of the Networking Solution (1)
Internet
or
AP
AP
…
Switch
AR
Firewall
Network scale
Site area, number of terminals, etc.
Network security requirements
Requirements for advanced security features and egress gateway security
Number of APs, etc.
Egress gateway device model and security feature requirements
Requirement
analysis
Notes: Before designing a networking solution, obtain the following information:
  Scale of the customer's network, including the area to be covered by the network and the number of terminals to be supported on the network. This information helps determine the number of APs to be deployed.
  Customer's security requirements, for example, whether advanced security features are required and whether the egress gateway devices need to work in dual-system hot standby mode. This information helps select egress device models.

## Slide 19: Design Principles of the Networking Solution (2)
Network Scale | Egress Security Requirement | Key Networking Requirement | Recommended Networking | Recommended Networking Device
Area < 50 m²; maximum number of concurrent online terminals < 50 | Low | Wireless user access only Single Internet egress | Singe-device networking | AP
 | Low | Wired and wireless user access Ethernet uplink or 3G/LTE uplink |  | AR
 | High | Wired and wireless user authentication and access Multiple Internet uplinks with an LTE backup uplink High security requirements (URL filtering/IPS/security protection/antivirus) |  | Firewall
Area < 300 m²; maximum number of concurrent online terminals < 200 | Low | Wireless access only Ethernet uplink or 3G/LTE uplink | Egress gateway + AP networking | AR + AP
 | High | Wired and wireless authentication and access Multiple Internet uplinks High security requirements (URL filtering/IPS/security protection/antivirus) |  | Firewall + AP

## Slide 20: Design Principles of the Networking Solution (3)
Network Scale | Egress Security Requirement | Key Networking Requirement | Recommended Networking | Recommended Networking Device
Area < 3000 m²; maximum number of concurrent online terminals < 2000 | Low | Wired and wireless access Multiple Internet uplinks | Egress gateway + L2 switch + AP networking | AR + L2 switch + AP
 | High | Wired and wireless access Multiple Internet uplinks High security requirements (URL filtering/IPS/security protection/antivirus) |  | Firewall + L2 switch + AP
Area < 3000 m²; maximum number of concurrent online terminals < 2000 | Low | Wired and wireless access Multiple Internet uplinks Densely-located room scenarios, such as hotels and dormitories | Egress gateway + L2 switch + distributed AP networking | AR + L2 switch + central AP + RU
 | High | Wired and wireless access Multiple Internet uplinks Hot standby for egress devices High security requirements (URL filtering/IPS/security protection/antivirus), applicable to densely-located room scenarios such as hotels and dormitories |  | AR + L2 switch + central AP + RU RU

## Slide 21: Networking Solution: Single AP
Solution description
  In single-AP networking, an AP functions as the gateway of end users and the egress device of the campus network.
Applicable scenarios
  This networking applies to small-sized stores (such as agent stores and gas stations) with an area of smaller than 50 m².
  A maximum of 50 concurrent online terminals are supported.
  Only wired user access is supported.
  Only one wired Internet egress link is required.
Internet
Carrier CPE
AP
Notes: CPE: Customer-Premises Equipment

## Slide 22: Networking Solution: Single AR
Solution description
  In single-AR networking, an AR functions as the gateway to provide access for wired and wireless terminals.
Applicable scenarios
  This networking applies to small convenience stores and clothing stores with an area of smaller than 50 m².
  A maximum of 50 concurrent online terminals are supported.
  Wired and wireless terminal access is supported, and wired uplinks or 3G/LTE wireless uplinks are required for Internet access.
Internet
Carrier CPE
AR
Carrier LTE
base station
Wired uplink

## Slide 23: Networking Solution: Single Firewall
Solution description
  In single-firewall networking, a firewall functions as the gateway to provide access for wired and wireless terminals.
Applicable scenarios
  This networking applies to high-security scenarios such as small stores for logistics, office, and finance with an area of smaller than 50 m².
  A maximum of 50 concurrent online terminals are supported.
  High security requirements (URL filtering/IPS/security protection/antivirus) need to be met and Internet access is provided through multiple uplinks. For example, in a scenario where an LTE backup link is required, only simple PSK or non-authentication wireless access is supported.
Internet
Carrier CPE
Firewall
Carrier LTE
base station
Wired uplink

## Slide 24: Networking Solution: AR + AP
Solution description
  In a scenario where multiple APs are required to meet wireless coverage requirements, an AR functions as the user gateway to provide egress features, such as WAN access, DHCP, and NAT.
Applicable scenarios
  This networking applies to small- and medium-sized clothing stores, shopping malls, and supermarkets with an area of smaller than 300 m².
  A maximum of 200 concurrent online terminals are supported.
  Multiple APs are required to provide coverage, and a wired uplink or a 3G/LTE wireless uplink is required for Internet access.
Internet
Carrier CPE
AR
Carrier LTE base station
Wired uplink
AP
AP

## Slide 25: Networking Solution: Firewall + AP
Solution description
  In a scenario where multiple APs are required to meet wireless coverage requirements, a firewall functions as the user gateway to provide egress features, such as WAN access, DHCP, and NAT.
Applicable scenarios
  This networking applies to small- and medium-sized experience stores and logistics/insurance service stores, with an area of smaller than 300 m² and fewer than 200 concurrent online terminals.
  Multiple APs are required, high security requirements (URL filtering/IPS/security protection/antivirus) must be met, and Internet access is provided through multiple uplinks.
Internet
Carrier CPE
Firewall
AP
AP

## Slide 26: Networking Solution: AR + L2 Switch + AP
Solution description
  An L2 PoE switch is used to increase the number of APs that can be connected.
  An AR functions as the egress gateway and user gateway to provide egress features, such as WAN access, DHCP, and NAT.
  An L2 switch provides extended PoE access and access for wired terminals, which connects to APs that provide access for wireless terminals.
Applicable scenarios
  This networking applies to small- and medium-sized clothing stores and retail stores with an area of smaller than 3000 m² and fewer than 2000 concurrent online terminals.
  Multiple APs need to be deployed to provide wireless access, a PoE LAN switch is used to increase the number of APs that can be connected, and multiple uplinks are required for Internet access.
Internet
Carrier CPE
AR
L2 switch
AP
AP

## Slide 27: Networking Solution: Firewall + L2 Switch + AP
Solution description
  An L2 PoE switch is used to increase the number of APs that can be connected. A firewall functions as the user gateway to provide egress features, such as WAN access, DHCP, and NAT. An L2 switch provides extended PoE access and access for wired terminals, which connects to APs that provide access for wireless terminals.
Applicable scenarios
  This networking applies to small- and medium-sized experience stores and logistics/insurance service stores, with an area of smaller than 3000 m² and fewer than 2000 concurrent online terminals.
  Multiple APs need to be deployed to provide wireless access, high security requirements (URL filtering/IPS/security protection/antivirus) need to be met, and multiple uplinks are required for Internet access.
Internet
Carrier CPE
Firewall
L2 switch
AP
AP

## Slide 28: Networking Solution: AR + L2 Switch + Central AP + RU
Solution description
  Network planning is automated and an RU is deployed in each room. An AR provides egress features, such as WAN access, DHCP, and NAT. An L2 switch provides access for wired terminals or serves as a Layer 2 aggregation switch. Central APs provide PoE access for RUs and manage these RUs, and RUs provide WLAN capabilities.
Applicable scenarios
  This networking applies to multi-room buildings such as dormitories and hotels with an area of less than 3000 m² and fewer than 2000 concurrent online terminals.
  Network planning is automated, each room transmits signals separately, and multiple uplinks are required for Internet access.
Internet
Carrier CPE
AR
L2 switch
AP
Central AP
Central AP
RU
RU
RU
RU

## Slide 29: Networking Solution: Firewall + L2 Switch + Central AP + RU
Solution description
  Network planning is automated and an RU is deployed in each room.
  A firewall provides egress features, such as WAN access, DHCP, and NAT.
  An L2 switch provides access for wired terminals or serves as a Layer 2 aggregation switch.
  Central APs provide PoE access for RUs and manage these RUs, and RUs provide WLAN capabilities.
Applicable scenarios
  This networking applies to multi-room buildings such as dormitories and hotels with an area of less than 3000 m² and fewer than 2000 concurrent online terminals.
  High security requirements (URL filtering/IPS/security protection/antivirus) need to be met, and multiple uplinks are required for Internet access.
Internet
Carrier CPE
Firewall
L2 switch

## Slide 30
Service Requirements and Challenges of Small- and Medium-Sized Campus Networks
Introduction to Huawei CloudCampus Solution
Huawei CloudCampus Solution Design for Small- and Medium-Sized Campus Networks
  Networking Solution Design
  Network Design
  QoS and Security Design
Typical Industry Application Scenarios

## Slide 31: CloudCampus Solution Account Role Design
Platform operator
MSP
MSP
Tenant
Tenant
Tenant
Tenant
In small- and medium-sized campus scenarios, tenant accounts are used by campus users to build and manage networks.
Administrator Design
Physical Network Design
WLAN Design
Network Deployment Design
Basic Service Design
Access Control Design

## Slide 32: Site Design
Internet
Store
Supermarket
School
A site is an abstract concept in the CloudCampus Solution. It can be defined as an independent network, such as a branch or an independent campus network.
Site in the CloudCampus Solution
An independent branch can be deployed as a site based on the physical location, for example, a financial branch of a bank or a campus of a university.
Each site can be assigned a tenant administrator for network O&M or an MSP administrator for O&M.
For a medium-sized campus network, do not allocate too many sites. Otherwise, the interconnection between sites and the management will be complicated.
Site design: considering simplified management and O&M
Administrator Design
Physical Network Design
WLAN Design
Network Deployment Design
Basic Service Design
Access Control Design

## Slide 33: Physical Network Design for a Site - Egress
Internet
L2 switch
Egress gateway
Use firewalls in high security scenarios.
Use ARs in family hotels, small retail outlets, and branches.
Use APs in small stores where only a single AP is deployed.
Egress networking design
For a large-scale network, it is recommended that firewalls or ARs be deployed in a two-node cluster at the egress and links of multiple carriers be used as egress links for backup.
For a small-scale network, it is recommended that a single device and links of a single carrier be used at the egress.
Function requirements for egress devices
Basic VPN function and WAN port/dial-up access function
Security firewall function for scenarios with security requirements.
Egress gateway
Gateway
Administrator Design
Physical Network Design
WLAN Design
Network Deployment Design
Basic Service Design
Access Control Design

## Slide 34: Physical Network Design for a Site - Core and Aggregation Layer
Internet
layer (combined with the core layer):
For a large-scale network, stack networking is recommended for the aggregation layer. If there are two layers of aggregation switches, they are interconnected through Eth-Trunks. It is recommended that the egress device be used as the user gateway.
For a small-scale network, it is recommended that a single device be deployed at the aggregation layer. Stack networking can also be deployed based on the network scale and reliability requirements. It is recommended that the egress device be used as the user gateway.
For smaller-scale networks such as small shopping malls and supermarkets, aggregation devices do not need to be deployed.
Aggregation layer
Administrator Design
Physical Network Design
WLAN Design
Network Deployment Design
Basic Service Design
Access Control Design

## Slide 35: Physical Network Design for a Site - Access Layer
Access device
Select PoE switches with enough ports to satisfy the number of connected APs.
Select a PoE switch according to the specific AP model.
Use agile distributed APs in multi-room building scenarios.
Networking design
For a large-scale network, stack networking is recommended for the access layer. If a single device can provide sufficient access capacity for downstream terminals, the single-device networking can be used at the access layer. When the upstream devices at the access layer are stacked, it is recommended that Eth-Trunks be used to connect to the upstream devices. If multiple APs need to be deployed, PoE LAN switches can be used to increase the number of APs that can be connected.
For a small-scale network, it is recommended that the single-device networking be used at the access layer and a single link be used to connect to the upstream device. If multiple APs need to be deployed, PoE LAN switches can be used to increase the number of APs that can be connected.
In small- and medium-sized stores, APs need to be deployed. APs can be directly connected to egress gateways without access switches.
Access layer
Access layer
Internet
Administrator Design
Physical Network Design
WLAN Design
Network Deployment Design
Basic Service Design
Access Control Design
Notes: Access device selection:
  Consider the number of APs to be connected and the power that can be provided by a PoE switch. An AP consumes about 10 W to 20 W, and a single PoE switch supplies more than 300 W. Therefore, select a PoE switch according to the specific AP model.
  In multi-room building scenarios such as hotels and dormitories, use central APs to provide PoE access and management for RUs that provide WLAN capabilities.

## Slide 36: Physical Network Design for a Site - Reliability
Network reliability
Internet
Network egress device
Wired uplink
(Primary)
3G/LTE
(Secondary)
Two egress gateways can be deployed for dual-system backup.
LAN switches at the core and aggregation layers can be stacked to implement physical device backup.
Egress link reliability
Device reliability
Cloud management platform reliability
  iMaster NCE-Campus can be deployed on the cloud platform in two modes: public cloud and local cloud. The public cloud platform ensures stable running of iMaster NCE-Campus. The local cloud platform generally uses cluster deployment to ensure stable running of iMaster NCE-Campus.
Management-side reliability
High redundancy
Authentication reliability
You can consider the bypass policy that is used if the authentication server is faulty. Currently, there are two types of policies that come into effect after a fault: those that require no authentication and those that prevent user access from being affected.
Network admission control device
Terminal
Authentication server
Administrator Design
Physical Network Design
WLAN Design
Network Deployment Design
Basic Service Design
Access Control Design
Notes: iMaster NCE-Campus provides management-side reliability. iMaster NCE-Campus is deployed in highly reliable data centers and the cloud management software provides high redundancy. Network reliability is the focus of network design.
Authentication reliability: When the device is connected to the authentication server, you can consider the escape policy that is used if the authentication server is faulty. Currently, there are two types of policies that come into effect after a fault: those that require no authentication and those that prevent user access from being affected.
Network reliability involves link and device reliability:
  Reliability of egress links: In most scenarios, there is only one egress link, and therefore no link redundancy needs to be considered. In scenarios where high reliability is required, more than one egress link needs to be deployed, so primary and secondary links must be configured.
  Reliability of internal links on a campus network: Typically, Eth-Trunk technology is adopted to ensure link reliability. It is recommended that inter-device Eth-Trunks be used to ensure link reliability of switch stacks.
  Device reliability: Two devices can be deployed as egress gateways in hot standby mode. LAN switches at the core and aggregation layers can be stacked for physical device redundancy.

## Slide 37: Network Deployment Design - Deployment Mode (1)
Through CloudCampus APP (barcode scanning)
Internet
Scan barcode.
Tenant: Tenant X
Site: Site Y
Device: AP (ESN...)
1
2
The APP obtains the ESN, MAC address, and management SSID of the AP.
Report AP information.
3
4
5
Register and get managed.
Through registration center
1.1.1.1:8080
Devices supported: AP
Devices supported: AR, firewall, switch, AP
Huawei registration center
1
Record device information.
2
Synchronize device information.
4
Automatically initiate a query request to Huawei registration center to obtain the IP address and port number of iMaster NCE-Campus.
Internet
6
Register and get managed.
Tenant: Tenant X
iMaster NCE-Campus: 1.1.1.1:8080
Device: AP (ESN...)
3
5
Switch to the cloud mode and initiate a registration request to iMaster NCE-Campus.
Administrator Design
Physical Network Design
WLAN Design
Network Deployment Design
Basic Service Design
Access Control Design
Notes: The registration center is a public cloud service provided by Huawei on the Internet and can therefore be considered a cloud platform. It is mainly used to implement plug-and-play of devices on the user network. During the deployment configuration of network devices, the core is to register the network devices with iMaster NCE-Campus and enable them to be managed by iMaster NCE-Campus. Huawei CloudCampus Solution supports the public cloud and MSP-owned cloud deployment modes. Therefore, multiple iMaster NCE-Campus instances may exist on the Internet. The problem is which iMaster NCE-Campus should a device register with after the device is powered on and connected to the network?
Huawei has set up a registration center. Users can implement plug-and-play of network devices through the registration center in the Huawei public cloud or MSP-owned cloud scenarios. Users need to record information about the network devices to be managed on iMaster NCE-Campus, including device SNs. iMaster NCE-Campus synchronizes the information to the Huawei registration center, which maintains the information. After a user connects a Huawei cloud device to the network with factory settings, the device obtains an IP address and then initiates a query request to the registration center. The domain name of the registration center has been preset on the device before delivery. The domain name is unique globally. The device initiates resolution requests through DNS servers in different regions and obtains the addresses of the registration centers in these regions. Then, the registration center returns information such as the IP address of the corresponding iMaster NCE-Campus to the device. In this way, the device can initiate a registration request to the address so it can get managed by iMaster NCE-Campus.
The registration center mode can be used only when iMaster NCE-Campus is interconnected with the registration center.

## Slide 38: Network Deployment Design - Deployment Mode (2)
Through web system
Devices supported: AR, firewall, switch, AP
Internet
2
Register and get managed.
1
In the web system, configure Internet access parameters, cloud management mode, and IP address/URL and port number of iMaster NCE-Campus.
Web
Through CLI
Devices supported: AR, firewall, switch, AP
Internet
2
Register and get managed.
1
On the CLI, configure Internet access parameters, cloud management mode, and IP address/URL and port number of iMaster NCE-Campus.
CLI
Administrator Design
Physical Network Design
WLAN Design
Network Deployment Design
Basic Service Design
Access Control Design
Notes: The switch does not need to be switched to the cloud-based management mode. The current switch version does not distinguish whether the cloud-based management mode is used.

## Slide 39: Network Deployment Design - Deployment Mode (3)
Through DHCP Option 148
Internet
AR
1
The network administrator has deployed the DHCP service on the network in advance (by deploying the DHCP service on the egress device or deploying an independent DHCP server.)
In addition to delivering IP addresses to the devices to be deployed, the DHCP server uses DHCP Option 148 to notify network devices of iMaster NCE-Campus's IP address and port number.
2
DHCP request
3
DHCP response carrying Option 148
4
Initiate a registration request to iMaster NCE-Campus.
Devices supported: AR, switch, AP
Switch to be deployed
Administrator Design
Physical Network Design
WLAN Design
Network Deployment Design
Basic Service Design
Access Control Design

## Slide 40: Network Deployment Design - Recommended Deployment Mode for Egress Gateways
Scenario | Recommended Deployment Mode |  | 
 | AR | Firewall | AP
In the Huawei public cloud or MSP-owned cloud scenario, egress gateways can obtain IP addresses only in static or PPPoE mode. | Web system | Web system | CloudCampus APP
In the on-premises scenario, egress gateways cannot obtain IP addresses of external network interfaces through DHCP. | Web system | Web system | CloudCampus APP
In the Huawei public cloud scenario, egress gateways can directly obtain IP addresses of external network interfaces through DHCP. | Registration center | Registration center | Registration center
In the on-premises scenario, egress gateways can directly obtain IP addresses of external network interfaces through DHCP, and Option 148 can be configured on the DHCP server. | DHCP Option 148 or web system | Web system | DHCP Option 148
Administrator Design
Physical Network Design
WLAN Design
Network Deployment Design
Basic Service Design
Access Control Design

## Slide 41: Basic Service Design
VLAN
IP addresses
IP address allocation
Routing
Basic service design
The VLAN design and IP address design are the same as those for large- and medium-sized campus networks. For details, see Large- and Medium-sized Campus Network Design Guide.
Administrator Design
Physical Network Design
WLAN Design
Network Deployment Design
Basic Service Design
Access Control Design

## Slide 42: Basic Service Design - IP Address Assignment Mode (1)
Egress gateway
Internet
Carrier CPE
Egress gateway
IP addresses of WAN interfaces: assigned in static, DHCP, or PPPoE mode
IP addresses of WAN interfaces on egress gateways are assigned by the carrier in static, DHCP, or PPPoE mode. The IP addresses of these interfaces need to be obtained from the carrier in advance.
Devices such as servers and printers
It is recommended that servers and special terminals (such as time attendance machines, printers, and IP video surveillance devices) use static IP addresses.
End user
Internet
AP
Egress gateway
It is recommended that end users be assigned IP addresses in DHCP mode and the gateway provide the DHCP service.
Administrator Design
Physical Network Design
WLAN Design
Network Deployment Design
Basic Service Design
Access Control Design
Notes: Dynamically allocated or statically bound IP addresses can be used. On a small- or medium-sized campus network, IP addresses are assigned based on the following principles:
  IP addresses of WAN interfaces on egress gateways are assigned by the carrier in static, DHCP, or PPPoE mode. The IP addresses of the egress gateways need to be obtained from the carrier in advance.
  It is recommended that servers and special terminals (such as time attendance machines, printers, and IP video surveillance devices) use static IP addresses.
  It is recommended that the DHCP server be deployed on the gateway to dynamically assign IP addresses to user terminals such as PCs and IP phones using DHCP.

## Slide 43: Basic Service Design - IP Address Assignment Mode (2)
LAN-side devices
When the egress gateway connects to an L3 switch, it is recommended that the interconnection IP addresses be manually configured in static mode.
Internet
L3 switch
Egress gateway
AP
Egress gateway
Layer 3 interconnection
Internet
It is recommended that the DHCP server be deployed on the gateway to dynamically allocate IP addresses to APs.
Administrator Design
Physical Network Design
WLAN Design
Network Deployment Design
Basic Service Design
Access Control Design

## Slide 44: Routing Design
Internal routing design of the campus network
  AP: After an IP address is assigned through DHCP, a default route is generated by default.
  Switch and gateway: Static routes can be used to meet requirements. No complex routing protocol needs to be deployed.
Egress routing design of the campus network
  You are advised to configure static routes on the egress device.
Internet
L2 switch
Egress gateway
AP
AP
Administrator Design
Physical Network Design
WLAN Design
Network Deployment Design
Basic Service Design
Access Control Design
Notes: The routing design of the small- or medium-sized campus network includes design of internal routes and the routes between the campus egress and the Internet or WAN devices.
The internal routing design of the campus network must meet the communication requirements of devices and terminals on the campus network and allow exchange of external routes. As the campus network is small in size, the network architecture is simple.
  AP: After an IP address is assigned through DHCP, a default route is generated by default.
  Switch and gateway: Static routes can be used to meet requirements. No complex routing protocol needs to be deployed.
The egress routing design meets requirements of intranet users for accessing the Internet and WAN. When the egress device is connected to the Internet or WAN, you are advised to configure static routes on the egress device.

## Slide 45: WLAN Design 1: WLAN Planner
2
4
Obtain the floor plan.
1
Log in to Huawei online WLAN Planner.
https://serviceturbo-cloud-cn.huawei.com/serviceturbocloud/dist/#/toolappmarket
1. Environment setting
2. Region setting
3. Device deployment
4. Signal simulation
5. Report export
With Huawei Cloud-based WLAN Planner, users can complete WLAN planning in five steps.
3
Use the network planning report to provide guidance for onsite construction.
The network planning result can be imported into iMaster NCE-Campus.
Administrator Design
Physical Network Design
WLAN Design
Network Deployment Design
Basic Service Design
Access Control Design
Notes: Network planning is important for WLAN project implementation. WLAN planning consists of the following parts:
  Network coverage design: Determine the requirements and principles for signal coverage.
  Network capacity design: Determine the bandwidth requirements of a single user based on the service model and STA behavior, and then determine the number of APs based on the AP capability.
  AP and switch deployment design: Determine AP deployment positions based on the deployment principles.
  AP channel design: Properly plan channels for APs in neighboring areas to reduce co-channel and adjacent-channel interference.
  AP power supply and cabling design
This document does not describe the WLAN design from the preceding dimensions. For details about the WLAN design, access https://e.huawei.com/en/material/networking/campus-network/699b63ddae1543f1b91dd014e799e3e0
Huawei provides online cloud-based WLAN Planner to guide users through WLAN network planning in simple steps.

## Slide 46: WLAN Design 2: Leader AP
Campus
AP
AP
Leader AP
AP
AP
A cloud AP is a Fat AP. When some WLAN services such as radio calibration need to be processed in a centralized manner, a global control role similar to the AC should be configured.
The leader AP is such a role.
Leader AP: In a group of APs, an AP with strong capabilities is elected as the leader AP. The leader AP is responsible for radio calibration, load balancing, and other services.
After the leader AP is elected, other APs set up CAPWAP links with the leader AP for sending radio calibration and load balancing messages.
Administrator Design
Physical Network Design
WLAN Design
Network Deployment Design
Basic Service Design
Access Control Design
Notes: The core algorithm logic of a cloud AP is the same as that of a traditional AC. APs detect and collect radio frequency and interference information about neighboring APs, and then report the information to the calibration compute engine. After the computing is complete, the compute engine delivers the allocated channel and power to each AP.
      When a traditional network and a traditional AC are deployed, the calibration compute engine resides on the AC. When a cloud network is deployed, the calibration compute engine resides on the leader AP.

## Slide 47: WLAN Design 3: Radio Calibration
iMaster NCE-Campus supports three radio calibration modes:
  Automatic mode: APs periodically perform global calibration based on the calibration time and interval.
  Manual mode: APs do not proactively perform radio calibration, and you need to manually perform global or local calibration for APs at the site on iMaster NCE-Campus.
  Scheduled mode: APs perform global calibration at a scheduled time every day.
APs perform calibration detection according to the configured mode and switch to other channels to scan neighboring APs. The scanning lasts for 15 minutes.
During the detection, the APs report the detected data to the leader AP every 10s.
The leader AP performs computing and calibration every 5 minutes and performs computing for three times to achieve algorithm convergence.
The leader AP delivers the calibration result to each AP in the group, including the calculated channel and power.
Campus
iMaster NCE-Campus delivers the calibration command.
1
2
All APs perform detection.
4
The leader AP performs computing and calibration.
5
The leader AP delivers the calibration result.
3
The APs report detection data.
Administrator Design
Physical Network Design
WLAN Design
Network Deployment Design
Basic Service Design
Access Control Design
Notes: During scheduled radio calibration, you can enable intelligent radio calibration and use the analyzer to analyze historical data of the WLAN and predict interference sources on the network. During network optimization, APs can avoid possible interference sources on the network in advance to improve the quality of the entire WLAN.
During deployment, you are advised to perform manual calibration to automatically plan the channels and power of APs after APs are deployed and go online.

## Slide 48: WLAN Design 4: AP Grouping Design
The number of APs that the leader AP can manage is limited.
If the number of APs exceeds the management capability of a leader AP, network planning is required. Management VLANs need to be planned for AP grouping. When there are a large number of APs in a management VLAN, the APs are automatically divided into multiple groups.
Radio calibration is performed on WLANs in a continuous area. Therefore, it is recommended that APs be grouped by geographic location such as by floor to ensure that APs in a group are in the same area. This maximizes the calibration effect.
Random grouping
F1
F2
F3
Grouping based on management VLANs
F1
F2
F3
VLAN 1000
VLAN 1001
VLAN 1002
If manual intervention is not performed when the number of APs exceeds the upper limit, APs are randomly grouped, affecting the calibration effect.
In a continuous area (such as adjacent APs or APs on the same floor), management VLANs are planned for AP grouping. A leader AP is elected in each group.
Administrator Design
Physical Network Design
WLAN Design
Network Deployment Design
Basic Service Design
Access Control Design

## Slide 49: WLAN Design 5: Channel and Frequency Bandwidth Selection
AP channel
2.4 GHz frequency band: Channel sets 1, 6, and 11 are recommended. If APs are densely deployed, channel sets 1, 5, 9, and 13 are recommended.
5 GHz frequency band: When an AP uses a single 5 GHz radio, it is recommended that high and low frequency channels of neighboring APs be staggered. When an AP uses dual 5 GHz radios, it is recommended that two 5 GHz radios be planned at low and high frequencies respectively.
Frequency bandwidth
2.4 GHz frequency band: Only the 20 MHz bandwidth can be selected.
5 GHz frequency band: The 40 MHz bandwidth is recommended.
Administrator Design
Physical Network Design
WLAN Design
Network Deployment Design
Basic Service Design
Access Control Design

## Slide 50: WLAN Design 6: Basic Concepts of Wireless Roaming
SSID guest (VLAN 100)
192.168.1.25
192.168.1.25
AP1
AP2
When a STA roams between APs on the same Layer 2 network, the service VLAN remains unchanged before and after the roaming.
Characteristics: Two APs at the same site have the same SSID and service VLAN.
Layer 2 roaming
APs before and after STA roaming belong to different service VLANs. The two APs belong to different Layer 2 service domains, and connect to different service gateways.
Characteristics: Two APs at the same site have the same SSID and authentication mode but different service VLANs.
Layer 3 roaming
192.168.1.25
192.168.1.25
SSID guest (VLAN 100)
Before roaming
After roaming
Before roaming
After roaming
AP1
AP2
SSID guest (VLAN 101)
Administrator Design
Physical Network Design
WLAN Design
Network Deployment Design
Basic Service Design
Access Control Design
Notes: When a WLAN is deployed for an enterprise or campus, the coverage area of a single AP is limited, and multiple APs are generally required to implement continuous wireless coverage of the entire space. To deliver good user experience and ensure service continuity when STAs move among APs, the APs must support roaming.

## Slide 51: WLAN Design 7: Wireless Roaming Design
A small- and medium-sized campus network has a small number of STAs. Therefore, Layer 2 roaming is recommended on such a network. (An SSID corresponds to one service VLAN, and all users share one user gateway.)
When more than 50 APs are deployed on a network or there are more than 1,000 STAs, Layer 3 roaming needs to be deployed. (An SSID corresponds to different service VLANs.)
802.11r fast roaming supports an enhanced roaming mechanism based on device-pipe synergy when working with Huawei terminals. This mechanism helps reduce the roaming handover delay and packet loss rate. Therefore, you are advised to enable the mechanism when enabling 802.11r fast roaming.
Note:
  Wireless roaming is supported only by APs at the same site.
  If the Layer 2 roaming domain is large, broadcast packets may be flooded. You are advised to rate limit broadcast packets on iMaster NCE-Campus. By default, the rate limit for broadcast packets is 256 pps.
  Each AP supports only 64 Layer 3 roaming STAs. If there are a larger number of Layer 3 roaming STAs, roaming fails and STAs need to go offline and then online again.
  When a STA roams at Layer 3, its traffic is detoured to the AP that the STA accesses for the first time or another AP in the same Layer 2 domain as the AP that the STA accesses for the first time. Therefore, it is recommended that a large Layer 2 domain be planned for APs at the network ingress to facilitate traffic detouring and load sharing after Layer 3 roaming.
Administrator Design
Physical Network Design
WLAN Design
Network Deployment Design
Basic Service Design
Access Control Design

## Slide 52: WLAN Design 8: VAS Design (Customer Flow Analysis)
Internet
AP
Leveraging WLANs, enterprises can obtain more customer flow information to facilitate their operation and management, including:
  Master the customer flow situation and distribution, and properly arrange market activities.
  Master the hotspot areas with high customer density, and use them as a basis for determining the rental, which improves the management efficiency and precision.
  Obtain highly loyal customers based on the visit frequency and launch promotions.
Customer
Passer-by
The AP periodically reports STA information (such as the MAC address, IP address, access AP, SSID, and signal strength) to the cloud management platform.
Collect statistics on customer flows at different time points and customer flow trends.
  Distinguish passers-by from customers and calculate the percentage of customers to all persons.
  Collect statistics on and analyze the customer dwell duration.
  Analyze the customer loyalty (repeated visit rate of regular customers).
Administrator Design
Physical Network Design
WLAN Design
Network Deployment Design
Basic Service Design
Access Control Design
Notes: Customer flow analysis requires APs to periodically report STA information to iMaster NCE-Campus. The STA information includes the MAC address, IP address, access AP, SSID, and signal strength. Therefore, enable STA location reporting in the settings of the site where the APs reside on iMaster NCE-Campus. If using STA information may pose data security threats, disable this function.
By default, customer flow analysis is performed by site. To check results of specific devices at the site, mark APs with tags. One AP can be marked with multiple tags to facilitate result check from different dimensions. For example, in shopping mall A, an AP at the entrance of store B can be marked with A/B/entrance. AP check and behavior analysis then can be performed based on tags.
Huawei CloudCampus Solution for small- and medium-sized campus networks can be interconnected with third-party terminal behavior management software to provide more detail-oriented services such as terminal profile and behavior analysis. This solution provides APIs for interconnection. Third-party software can adapt to the APIs to provide customer behavior analysis based on big data for commercial promotion.

## Slide 53: WLAN Design 9: VAS Design (Commercial Portal Page Push)
With this function, enterprises can conveniently customize their own Portal pages so as to launch VASs such as brand promotion and advertisement push.
Administrator Design
Physical Network Design
WLAN Design
Network Deployment Design
Basic Service Design
Access Control Design

## Slide 54: WLAN Design 10: VAS Design (Wi-Fi & IoT Convergence Solution)
Internet
Huawei IoT AP has an IoT card installed
Huawei IoT cloud APs provide pipe-layer capabilities, that is, standard Mini PCIe expansion slots and USB ports for access of IoT card modules, as well as uplink data channels.
Partners provide IoT card modules that comply with Huawei interface specifications and connect to Huawei IoT cloud APs through Mini PCIe ports or USB ports.
Partners provide terminal-layer capabilities, including tags and wristbands, to interact with IoT cards.
AP management channel
Card management channel
IoT management system
IoT card
IoT terminal (such as tag and wristband)
Wi-Fi & IoT convergence
Cost-saving
Simple site design and power supply solutions
Site locations and communication channels provided by APs
Simple deployment
Easy service provisioning
Mini PCIe expansion slots + USB ports
Scalability
Convenient installation of IoT cards
Administrator Design
Physical Network Design
WLAN Design
Network Deployment Design
Basic Service Design
Access Control Design
Notes: Huawei IoT cloud APs only forward uplink and downlink data of IoT card modules, but do not process data of specific IoT service protocols.
Compared with the traditional IoT solution, Huawei Wi-Fi & IoT Convergence Solution offers the following advantages:
  IoT base stations and APs are deployed on the same site, and Wi-Fi and IoT networks are converged, facilitating site planning and power supply while reducing deployment costs.
  APs provide uplink data channels for a unified entry and unified management, simplifying deployment.
  APs provide pipe-layer capabilities, enabling flexibility and scalability.

## Slide 55: Access Control Design - Typical Authentication Technology Comparison
Item | Portal Authentication | MAC Address Authentication | 802.1X Authentication
Client | Not required | Not required | Required
Advantage | Flexible deployment | No client required | High security
Disadvantage | Low security | MAC address registration required, complicating management | Inflexible deployment
Applicable scenario | Network authentication of guests who move frequently and use different types of terminals | Access authentication of dumb terminals such as printers and fax machines | Network authentication of office users with high security requirements
Administrator Design
Physical Network Design
WLAN Design
Network Deployment Design
Basic Service Design
Access Control Design

## Slide 56: Access Control Design - Portal Authentication Used in Multiple Application Scenarios (1)
Authentication Mode | Feature | Dependency | Application Scenario
User name and password authentication | A user can use the user name and password created by the tenant administrator or register an account for access authentication. | - | Authentication based on the user name and password created by an administrator is applicable to a fixed user group, for example, enterprise employees. Authentication based on accounts registered by users is applicable to scenarios where access permission of guests such as membership needs to be verified. The accounts registered by users need to be approved.
Anonymous authentication | Guests access the network without using any accounts. iMaster NCE-Campus automatically displays the login accounts of the guests as anonymous accounts. | - | This mode is applicable to open networks on which the Internet access service is provided for customers free of charge.
SMS authentication | A user enters a mobile number as the user name and clicks the button for obtaining a password. The SMS server then sends a password to the user. The system automatically registers and authenticates the user name and password after the user enters the password. | An SMS server has been configured. | This mode is applicable to guest authentication. SMS authentication improves the validity of guest identities and enables merchants to obtain customer information more conveniently so that they can interact with the customers.
Administrator Design
Physical Network Design
WLAN Design
Network Deployment Design
Basic Service Design
Access Control Design

## Slide 57: Access Control Design - Portal Authentication Used in Multiple Application Scenarios (2)
Authentication Mode | Feature | Dependency | Application Scenario
Social media authentication (Facebook authentication used as an example) | iMaster NCE-Campus interworks with the Facebook platform, so that users can use their social media accounts and passwords to perform authentication on the service manager page without registering any new account. After being authenticated, users can access the network. | For Facebook authentication, an enterprise has applied for and obtained an independent Facebook account from Facebook. | Facebook authentication is applicable to shopping malls that provide free Internet access services for guests.
Passcode authentication | Users enter the passcode on the pushed page for access authentication. | - | This mode is simple and applicable to guest access in stores.
Administrator Design
Physical Network Design
WLAN Design
Network Deployment Design
Basic Service Design
Access Control Design

## Slide 58: Access Control Design - Best Practices
Portal authentication is recommended for guests. Authentication points can be deployed on APs, ARs, or firewalls based on the networking requirements.
Portal or 802.1X authentication can be selected for enterprise employees. It is recommended that access devices be selected as authentication points.
Dumb terminals in enterprises are connected to the network in wired mode. MAC address authentication is recommended for these dumb terminals, and access switches can be selected as authentication points.
Internet
L2 switch
Egress gateway
Guest's terminal
Employee's terminal
Dumb terminal
AP
Administrator Design
Physical Network Design
WLAN Design
Network Deployment Design
Basic Service Design
Access Control Design
Notes: Based on the preceding authentication modes, access devices are recommended as authentication points.
The advantages of using access devices as authentication points are as follows:
  Multiple access devices perform user authentication to share the workload of centralized authentication.
  Authentication points are closer to terminals, improving security.
  The configuration is simple. If authentication points are deployed at the upper layer, the following factors must be considered: performance specifications of the devices acting as authentication points, Layer 2 isolation at the access layer, and transparent transmission of 802.1X protocol packets at the access layer.

## Slide 59
Service Requirements and Challenges of Small- and Medium-Sized Campus Networks
Introduction to Huawei CloudCampus Solution
Huawei CloudCampus Solution Design for Small- and Medium-Sized Campus Networks
  Networking Solution Design
  Network Design
  QoS and Security Design
Typical Industry Application Scenarios

## Slide 60: QoS Design - Rate Limiting
The CloudCampus Solution for small- and medium-sized campus networks supports the following rate limiting modes.
Per-user rate limiting
SSID-based rate limiting
ACL-based rate limiting
This mode is applicable to the scenario where an administrator wants to perform refined control over the traffic of each user. For example, the administrator assigns different bandwidths for VIP users, enterprise employees, and guests.
This mode is applicable to the scenario where an administrator performs comprehensive management and control over traffic of all users connected to a specific service. For example, the administrator limits the maximum bandwidth for all guests to 20 Mbit/s.
This mode is applicable to the scenario where an administrator manages and controls the traffic that meets specific characteristics. For example, the administrator rate-limits FTP traffic on the network.
Internet
Guest terminals
Employee terminals
Internet
Guest terminals
Employee terminals
SSID1
Unlimited bandwidth
SSID2
Bandwidth < 20 Mbit/s
Internet
FTP applications
Notes: The purpose of rate limiting is to prevent some users or applications from occupying a large amount of bandwidth resources. In this way, other users or applications can obtain sufficient bandwidth resources, ensuring user experience.

## Slide 61: QoS Design - Wireless QoS (Wireless Queue Mapping)
On a WLAN, user traffic of different services is mapped to different queues based on the priority configured for each service. This ensures that services that are sensitive to network parameters, such as voice and video services, can be preferentially scheduled.
Modifying DSCP priorities based on application types
Re-marking DSCP priorities of packets based on user groups
Internet
Example: Re-mark DSCP priorities after a device identifies the audio and video services.
Internet
Example: Re-mark the DSCP priority for users in a VIP group.
VIP

## Slide 62: Security Design - Basic Concepts (Security Policy)
Firewall
PC1
192.168.1.1/24
External network
Intranet
Internet
Control traffic forwarding
Control content security monitoring
The firewall can identify traffic attributes and match the attributes with security policy conditions.
If all the conditions are met, the traffic matches the security policy. The firewall then applies the action defined in the matching security policy to the traffic.
  If the action is permit, the firewall checks the traffic content, and determines whether to permit traffic based on content security detection results.
  If the action is deny, the firewall does not allow the traffic to pass through.
Integrated content security detection uses the intelligent awareness engine to detect and process the content of a flow, implementing content security functions including antivirus, intrusion prevention, URL filtering, DNS filtering, file filtering, content filtering, application behavior control, email filtering, and Advanced Persistent Threat (APT) defense. This ensures network security.
Notes: The security policy is the core function of firewalls. In normal cases, there is no need to divide many security zones for small- and medium-sized campus networks. To simplify configurations, you are advised to add WAN-side interfaces to the untrusted zone and LAN-side interfaces to the trusted zone, and allow inter-zone traffic. Traditional firewalls block or forward inter-zone traffic based on 5-tuple, including source IP address, destination IP address, source port, destination port, and protocol type. Security policies of Huawei NGFWs can replace the packet filtering function and implement traffic forwarding control based on users and applications. In addition, they can be used to detect and process traffic content. Security policies of NGFWs can better adapt to modern network characteristics and meet modern network requirements.

## Slide 63: Security Design - Intranet Security (Wired Network) (1)
L2 switch
Broadcast storm control
DHCP snooping
On downlink interfaces of the access layer, configure suppression of broadcast, unknown unicast, and multicast (BUM) packets to effectively reduce broadcast storms.
L2 switch
BUM traffic
Broadcast storm suppression
Valid DHCP response
Trusted interface
Untrusted interface
DHCP server
Invalid DHCP response
When DHCP snooping is enabled, the interface directly or indirectly connected to a trusted DHCP server needs to be configured as a trusted interface, and other interfaces are configured as untrusted interfaces. This ensures that DHCP clients can obtain IP addresses only from the authorized DHCP server.
Notes: BUM: broadcast, unknown, and multicast frames. By default, a switch floods BUM frames.

## Slide 64: Security Design - Intranet Security (Wired Network) (2)
L2 switch
IP source guard (IPSG) and dynamic ARP inspection (DAI)
Port isolation
IPSG prevents unauthorized hosts from accessing or attacking the network through IP addresses of authorized hosts or through specified IP addresses.
A DAI-enabled device matches the source IP address, source MAC address, interface, and VLAN ID in an ARP packet against a binding table, and then discards invalid ARP packets after detecting them.
L2 switch
Bogus traffic
Port isolation
You are advised to configure port isolation on the interfaces connecting the access switch to terminals. This configuration secures user communication and prevents invalid broadcast packets from affecting user services.
Guest 1
Guest 2
Forger
Authorized user
Notes: IPSG checks user entries to determine whether packets are sourced from authorized hosts. The entries can be manually configured or dynamically generated based on DHCP snooping binding entries.
After DAI is enabled, the device checks ARP packets based on DHCP snooping binding entries, including the mapping between IP addresses, MAC addresses, and interface numbers.

## Slide 65: Security Design - Intranet Security (Wireless Network): Wireless Air Interface Security
WIDS and WIPS
Attack detection
WIDS and WIPS can be enabled to prevent intrusion of unauthorized devices or interference devices, so as to detect and contain rogue devices on the network.
To prevent attacks on the WLAN, you are advised to enable the attack detection function in public areas and primary/secondary education scenarios with high security requirements to detect flood, weak-vector, and spoofing attacks, automatically add attackers to the dynamic blacklist, and send alarms to notify the administrator.
STA
AP
AC
AAA
Access authentication
Link encryption
Attack
detection and prevention
Rogue device
detection and containment
Policy control
WIDS & WIPS
Rogue device
Rogue STA
Rogue AP
Ad-hoc device
Rogue bridge
Notes: Wireless Intrusion Detection System (WIDS): WIDS can detect rogue APs, wireless bridges, STAs, ad-hoc devices, and interfering APs with overlapping channels.
Wireless Intrusion Prevention System (WIPS): WIPS can disconnect authorized users from rogue APs and disconnect unauthorized STAs and ad-hoc devices from the wireless network, defending against rogue devices.
WIDS is used to detect unauthorized terminals, malicious user attacks, and wireless network intrusions. WIDS is an extension to WIDS and further protects enterprise wireless networks. It prevents enterprise networks and users from authorized access and provides defense against attacks to network systems.
Concepts related to WIDS and WIPS:
  Rogue AP: an authorized or malicious AP. A rogue AP can be an AP that is connected to a network without permission, unconfigured AP, neighboring AP, or an AP manipulated by an attacker.
  Rogue client: an unauthorized or malicious client, similar to a rogue AP.
  Rogue wireless bridge: an unauthorized or malicious wireless bridge.
  Monitor AP: an AP that scans or listens on wireless channels and attempts to detect attacks to wireless networks.
  Ad-hoc mode: working mode of a wireless client. Ad-hoc devices can directly communicate with each other without the support of any device.

## Slide 66: Security Design - Intranet Security (Wireless Network): Terminal Access Security
Four WLAN security policies are available: Wired Equivalent Privacy (WEP), Wi-Fi Protected Access (WPA), WPA2, WLAN Authentication and Privacy Infrastructure (WAPI). Each security policy has a series of security mechanisms, including link authentication used to establish a wireless link, user authentication used when users attempt to connect to a wireless network, and data encryption used during data transmission.
Security Mechanism | Characteristics
WEP | The same static key needs to be preconfigured on the server and client. Both the encryption mechanism and the encryption algorithm are vulnerable to security threats. Therefore, this authentication mode is not recommended.
WPA/WPA2 | WPA and WPA2 provide almost the same level of security. WPA/WPA2 has two editions: enterprise edition and personal edition. WPA/WPA2 in enterprise edition requires an authentication server and is recommended for employee access on medium- and large-sized campus networks. WPA/WPA2 in personal edition does not require an authentication server and is recommended for guest access on medium- and large-sized campus networks. The WPA/WPA2-Private PSK (PPSK) enhances network security while ensuring the convenience.
WAPI | WAPI is a WLAN security standard proposed in China and provides higher security than WEP and WPA.
For example, in an enterprise, the following access authentication modes can be used:
  Enterprise employees: WPA/WPA2-802.1X authentication
  Guests: WPA/WPA2-PPSK or Portal authentication
  Dumb terminals: MAC address authentication
In addition, if users do not need to communicate with each other, it is recommended that user isolation be configured.

## Slide 67
Service Requirements and Challenges of Small- and Medium-Sized Campus Networks
Introduction to Huawei CloudCampus Solution
Huawei CloudCampus Solution Design for Small- and Medium-Sized Campus Networks
Typical Industry Application Scenarios

## Slide 68: Retail Industry Scenario 1 - Small Chain Stores
Customer requirements
Quick rollout of widely distributed new chain stores
No professional O&M personnel, difficult to locate faults in a short period of time
Manual replacement of paper shelf labels in stores, which is slow and error-prone
Solutions
Deployment by scanning barcodes enables wireless networks to go online in minutes, and iMaster NCE-Campus implements one-stop management from deployment to O&M. Customized advertisement push pages are configured for guests who connect to the network through Portal authentication.
IoT APs provide built-in IoT slots to implement IoT & Wi-Fi convergence and co-site deployment. ELSs interconnect with management and ERP systems of supermarkets to dynamically display prices and implement interactive functions such as real-time price change and out-of-stock warning.
Information about wireless terminals such as barcode scanners can be imported in batches, implementing access of massive terminals quickly.
Customer benefits
IoT & Wi-Fi convergence deployment and unified planning, saving investments
Real-time or periodic update of ESLs, ensuring fast response, eliminating errors, and reducing costs
Internet
Store 1
Store N
POS machine
Mobile phone
Barcode scanner
POS machine
Mobile phone
Barcode scanner
Advertisement push
ELS
Small chain supermarket

## Slide 69: Retail Industry Scenario 2 - Medium-Sized Stores
Customer requirements
Support various types of wireless terminals and diversified applications
Effectively support sales growth and bring business benefits
Save labor costs
Solutions
Firewalls function as egress gateways. Switches and APs provide wired and wireless network access, and the switches supply power to APs and terminals.
The wireless network reports information to iMaster NCE-CampusInsight in real time. iMaster NCE-CampusInsight then analyzes customers' preferences and habits, accurately pushes advertisements to customers, and assists in goods display.
The digital screen displays discount information in real time for customers and online price comparison and self-service checkout are supported.
Customer benefits
Access devices supply power to cameras, reducing cabling costs. Video surveillance ensures property security.
iMaster NCE-CampusInsight helps customers make operation decisions, improve sales performance, and enhance customer loyalty through precision pushing.
Internet
Store 1
Store N
POS machine
Mobile phone
Barcode scanner
POS machine
Mobile phone
Barcode scanner
Customer flow analysis
Medium-sized store
Digital
screen
Energy efficiency management
ELS
Video surveillance
Heat map analysis
Camera
Camera

## Slide 70: Retail Industry Scenario 3 - Large Shopping Malls
Customer requirements
Unified management of wired and wireless devices, meeting the access requirements of different types of terminals and simplifying O&M
Car seeking mechanism in large shopping malls, improving shopping experience
Solutions
Core switches, access switches, and APs are managed in a unified manner, meeting the bandwidth requirements even in scenarios of burst traffic.
Portal, SMS, social media, and MAC address authentication modes are supported to ensure access security of dumb terminals (including phones, printers, and cameras).
On a WLAN, APs collect and report RSSI information about terminals to the RTLS. The RTLS then uses the established fingerprint database to calculate locations of terminals and provide services such as car seeking and store navigation.
Customer benefits
Simplify management and require no O&M professionals.
Improve users' shopping experience, implement precision marketing, and ensure the security and control of important assets.
Internet
POS machine
Mobile phone
Barcode scanner
Asset management
Large shopping mall
Store navigation
Car seeking
Customer flow analysis
Camera
Shopping area
Parking lot
Office area
Notes: RSSI: Received Signal Strength Indicator (The RSSI value can be used to determine the signal strength between a STA and an AP.)
RTLS: Real-Time Locating Systems

## Slide 71: Hotel Industry Scenario - Chain Hotels
Customer requirements
Remote and unified management of multiple chain hotels and fast service provisioning, requiring no technical professionals
Cyber security compliance, complying with local laws and regulations
Quick response to network faults, ensuring good Internet access experience and improving customer experience
Value-added services for hotels, such as customer profiling and online behavior analysis
Solutions
In Huawei public cloud scenario, unified management is implemented. The CloudCampus APP is used to complete remote management of site survey, network planning, deployment, acceptance, and O&M, implementing quick service rollout.
Firewalls are used as egress gateways to implement cyber security compliance through online behavior management. The agile distributed AP solution is also supported.
iMaster NCE-CampusInsight provides network visualization, user journey, and root cause analysis for wireless air interfaces to quickly locate faults.
Network data is reported to the big data analytics platform in real time to implement value-added applications such as customer profiling.
Customer benefits
Devices are plug-and-play and networks are deployed remotely, reducing deployment costs. The network status is monitored in real time and faults are quickly rectified.
The cloud platform provides various northbound APIs to connect to multiple applications, improving hotel service experience and bringing profits to hotels through big data analytics.
Internet
RFID
Mobile phone
PC
Customer profiling
Chain hotel
Online behavior analysis
Camera
Central AP
RU
Property management system

## Slide 72: Primary/Secondary Education Campus
Customer requirements
Implement multi-level and multi-domain management and centralized management and O&M of schools in a region, requiring a visualized, easy-to-understand, and easy-to-operate management platform.
Meet wireless coverage requirements in multiple campus scenarios and implement flexible authentication and accounting based on roles.
Implement smart classrooms to improve teaching experience, and provide unified management of VASs such as student health monitoring, electronic attendance, and asset management.
Solutions
In Huawei public cloud scenario, unified management is implemented. The education bureau serves as the tenant to perform multi-level and multi-domain management for schools.
Various AP models are provided to meet wireless access requirements in multiple scenarios, such as classrooms, dormitories, auditoriums, and stadiums.
APs provide IoT slots for IoT & Wi-Fi convergence. In addition, network data is reported to the big data analytics platform in real time to implement various digital service applications.
Customer benefits
Devices are plug-and-play and networks are deployed remotely, reducing deployment costs. Servers such as the network management system (NMS) do not need to be deployed locally, reducing investment costs.
The cloud platform provides various northbound APIs to connect to multiple applications, facilitating on-demand subscription.
Education MAN
Attendance management
Primary and secondary school
Health monitoring
Asset management
Personnel tracking
School 1
School N
Wristband
Mobile phone
Camera
Wristband
Mobile phone
Camera
PC
PC

## Slide 73
(TorF) After obtaining the IP address of the controller through DHCP Option 148, a switch switches to the cloud-based management mode.( )
  True
  False
(Multiple-choice) In small- and medium-sized campus scenarios, which of the following methods can bring network devices online?( )
  Manually specifying the IP address of the controller using the CLI
  Query through the registration center
  Barcode scanning through an app
  DHCP Option 148
Notes: Answers:
  B
  ABCD

## Slide 74
This course describes the network design solution in small- and medium-sized campus scenarios, including networking solution design, network design, QoS and security design. It describes how to use iMaster NCE-Campus to manage cloud-based networks and build an efficient campus network in small- and medium-sized campus scenarios.