## Slide 1
Shi Miaomiao/swx791350
2019.11

## Slide 2: Small- and Medium-Sized Campus Networks Deployment Guide

## Slide 3
Upon completion of this course, you will be able to:
  Onboard ARs in DHCP mode.
  Onboard ARs through the CLI.
  Configure ARs through iMaster NCE-Campus.
  Configure wireless services through iMaster NCE-Campus.

## Slide 4
Networking Topology
Deployment Guide

## Slide 5: Networking Topology
In this demo, Site2 consists of AR2 and AP2. AR2 obtains an IP address and the IP address of iMaster NCE-Campus through DHCP, and completes LAN-side address allocation and is configured with NAT to enable AP2 to go online.
iMaster NCE-Campus is connected to SW1, and its gateway is set to VLANIF40 on SW1.
Site2
AP2
AR2
SW1
GE0/0/18
GE0/0/8
GE0/0/1

## Slide 6
Networking Topology
Deployment Guide

## Slide 7: Creating a Site (1)
Site
To enable network devices within the same management scope to be centrally managed on iMaster NCE-Campus, you can create a site on iMaster NCE-Campus and add these network devices to the site.
Creating a site consists of two parts:
  Create sites.
  Add devices.
Site Creation
Device Onboarding
AR2 Service Configuration
AP2 Service Configuration
O&M
Notes: A site usually corresponds to the headquarters or a branch. A site is a general term for networks and network users, and is also a basic unit for managing small- and medium-sized campus networks. Devices on the same network under the same tenant account can be added to one site. This facilitates device management for the tenant and improves the service deployment efficiency.

## Slide 8: Creating a Site (2)
Creating sites one by one.
Creating sites in a batch
Add devices manually.
1
Download a template (an Excel file) from iMaster NCE-Campus.
2
Fill in the template with site and device information.
3
Import the template to iMaster NCE-Campus.
Site Name | Device Type | Device Model | Device ESN | Device Name
Sitename | LSW,AP | S5730-36C-PWH-HI | *** | 
 |  | S5730-36C-PWH-HI | *** | 
 |  | S5731-H24P4XC | *** | 
… | … | … | … | …
Create sites and import devices in a batch.
Site Creation
Device Onboarding
AR2 Service Configuration
AP2 Service Configuration
O&M
Notes: A tenant administrator can create different organizations and configure a site to belong to an organization. Currently, a maximum of five levels of organizations can be created.
You can create sites on iMaster NCE-Campus for unified O&M. Two methods are available to create sites:
  Create sites one by one: You can create sites one by one when a small number of sites need to be added.
  Create sites in a batch: You can create sites in a batch when a large number of sites need to be added. Cloud sites cannot be created in batches.
On iMaster NCE-Campus, you can create a site by cloning an existing site to reduce repeated configurations.

## Slide 9: Creating a Site (3)
In this demo, a single site is created, and AR2 is manually added based on the ESN.
When creating a site, set the device type to AP or AR.
Site Creation
Device Onboarding
AR2 Service Configuration
AP2 Service Configuration
O&M

## Slide 10: Registration and Onboarding: Recommended Egress Gateway Deployment Mode
Scenario | Recommended Egress Gateway Deployment Mode |  | 
 | AR | Firewall | AP
In Huawei public cloud or MSP-owned cloud deployment scenarios, egress gateways can obtain IP addresses only in static mode or PPPoE mode. | Web system | Web system | CloudCampus APP
In the local deployment scenario, the egress gateway cannot obtain an IP address of an external network interface through DHCP. | Web system | Web system | CloudCampus APP
In Huawei public cloud deployment scenarios, the egress gateway can directly obtain an IP address of an external network interface through DHCP. | Registration center | Registration center | Registration center
In the local deployment scenario, the egress gateway can directly obtain an IP address of an external network interface through DHCP, and Option148 can be configured on the DHCP server. | DHCP Option148 or Web system | Web system | DHCP Option148
Site Creation
Device Onboarding
AR2 Service Configuration
AP2 Service Configuration
O&M

## Slide 11: Registration and Onboarding: LAN-side Device Deployment
LAN-side devices include LSWs and APs. These devices are deployed on the internal network.
In public cloud deployment scenarios, deployment through the registration center is recommended.
If an enterprise does not want to synchronize device information to the registration center, DHCP Option148 can be used for deployment.
Networking Scenario |  | LAN-side Device Deployment Mode | 
 |  | LSW | AP
Huawei public cloud scenario | DHCP Option148 cannot be configured on the network. | Registration center | 
 | DHCP Option148 can be configured on the network. | Registration center or DHCP Option148 | 
MSP-owned cloud scenario | DHCP Option148 cannot be configured on the network. | Web system | CloudCampus APP
 | DHCP Option148 can be configured on the network. | Registration center or DHCP Option148 | 
Site Creation
Device Onboarding
AR2 Service Configuration
AP2 Service Configuration
O&M

## Slide 12: Registration and Onboarding: AR Login
Site2
AP2
AR2
GE0/0/8
GE0/0/1
1
AR2 obtains its IP address through DHCP and the IP address of iMaster NCE-Campus through DHCP Option148.
2
AR2 is registered and goes online.
In this demo, the AR goes online in DHCP Option148 mode. When the AR starts, it automatically obtains an IP address from the WAN interface. If the AR obtains the IP address through DHCP Option148, it sends a registration request to the IP address and port number in DHCP Option148.
interface Vlanif67
dhcp select interface
dhcp server Option148 ascii agilemode=agile-cloud;agilemanage-mode=ip;agilemanage-domain=192.168.4.104;agilemanage-port=10020;
SW1
GE0/0/18
GE0/0/20
Site Creation
Device Onboarding
AR2 Service Configuration
AP2 Service Configuration
O&M
Notes: In addition to obtaining the IP address of iMaster NCE-Campus through DHCP, you can also manually specify the IP address of iMaster NCE-Campus through the web system or CLI. On the CLI, you can run the agile controller host controller-ip port control-port command to manually specify the IP address of iMaster NCE-Campus.

## Slide 13: Registration and Onboarding: AP Login
In this demo, the DHCP service and DHCP Option148 are configured to implement zero-touch deployment for the LAN-side device (AP2) connected to the AR.
To ensure the IP connectivity between AP2 and iMaster NCE-Campus, configure NAT on AR2.
Site2
AP2
AR2
GE0/0/8
GE0/0/1
DHCP
Option148
N
N
Source network address translation (SNAT)
Site Creation
Device Onboarding
AR2 Service Configuration
AP2 Service Configuration
O&M

## Slide 14: LAN Network Service
On the LAN tab page, configure a network configuration mode.
To set the same DHCP parameters for ARs at a site, select Local Internet access.
To set different DHCP parameters for ARs at a site, select Multi-branch interconnection.
Click Create and set LAN-side subnet parameters.
Internet
Site
Site Creation
Device Onboarding
AR2 Service Configuration
AP2 Service Configuration
O&M

## Slide 15: LAN Network Service
Create a DHCP address pool and set the VLAN ID, IP address, and mask.
Configure the cloud platform address in the DHCP option.
Site Creation
Device Onboarding
AR2 Service Configuration
AP2 Service Configuration
O&M
Notes: After a subnet for an AP to go online is created, a VLANIF interface corresponding to the VLAN is created on AR2, the DHCP server function is enabled on the VLANIF interface, and DHCP Option148 is configured.

## Slide 16: WAN Network Service
Site2
AP2
AR2
GE0/0/8
GE0/0/1
N
Configure SNAT to translate the source address range into a LAN subnet.
N
SNAT
Site Creation
Device Onboarding
AR2 Service Configuration
AP2 Service Configuration
O&M
Notes: To ensure that AP2 can communicate with iMaster NCE-Campus after obtaining an IP address, configure SNAT on AR2 and use an ACL to limit the source IP address range to the subnet created for AP2 to go online. The ACL to be invoked can be configured in the ACL template in advance.

## Slide 17: Interface Configuration
Site2
AP2
AR2
GE0/0/8
GE0/0/1
T
Configure the interface connected to AP2 to allow packets from VLAN 10 to pass through.
T
Trunk interface
Site Creation
Device Onboarding
AR2 Service Configuration
AP2 Service Configuration
O&M
Notes: AR2 connects to AP2 through a trunk interface. To ensure that AP2 can obtain an IP address, configure the trunk interface to allow packets from VLAN 10 to pass through.

## Slide 18: SSID Configuration Overview
On a WLAN, SSIDs are used to identify different wireless networks. In this demo, SSIDs are created.
  Employee: is used for employee access. The 802.1X authentication mode is used.
  iMaster_NCE_Demo: is used for guest access. The Portal authentication mode is used. The Portal authentication mode does not need the input password for connecting to the SSID, which facilitates business promotion.
AP2
SSID: iMaster_NCE_Demo
Portal authentication
SSID: Employee
802.1X authentication
Site Creation
Device Onboarding
AR2 Service Configuration
AP2 Service Configuration
O&M

## Slide 19: Basic Configuration for the Guest SSID
Configure basic WLAN parameters and the VLAN to which wireless users belong.
AP2
SSID: iMaster_NCE_Demo
Portal authentication
Site Creation
Device Onboarding
AR2 Service Configuration
AP2 Service Configuration
O&M

## Slide 20: Security Authentication Configuration for the Guest SSID
Configure security authentication (Portal authentication) and use iMaster NCE-Campus as the Portal or RADIUS server.
AP2
SSID: iMaster_NCE_Demo
Portal authentication
Site Creation
Device Onboarding
AR2 Service Configuration
AP2 Service Configuration
O&M
Notes: To ensure that wireless terminals can properly perform DNS resolution and successfully initiate HTTP access, you need to configure the ACL that permits DNS traffic in advance and invoke the ACL in the default permit rule.

## Slide 21: Policy Control Configuration for the Guest SSID
Configure policy control parameters, such as rate limiting.
AP2
SSID: iMaster_NCE_Demo
Portal authentication
Site Creation
Device Onboarding
AR2 Service Configuration
AP2 Service Configuration
O&M

## Slide 22: Basic Configuration for the Employee SSID
SSIDs and user VLANs are different.
AP2
SSID: Employee
802.1X authentication
Site Creation
Device Onboarding
AR2 Service Configuration
AP2 Service Configuration
O&M

## Slide 23: Security Authentication Configuration for the Employee SSID
AP2
SSID: Employee
802.1X authentication
Configure security authentication (802.1X authentication) and use iMaster NCE-Campus as the RADIUS server.
Site Creation
Device Onboarding
AR2 Service Configuration
AP2 Service Configuration
O&M

## Slide 24: Policy Control Configuration for the Employee SSID
Configure policy control parameters, such as rate limiting.
AP2
SSID: Employee
802.1X authentication
Site Creation
Device Onboarding
AR2 Service Configuration
AP2 Service Configuration
O&M

## Slide 25: Configuration for Wireless Users to Access the Network (1)
User VLANs of SSIDs Employee and iMaster_NCE_Demo on AP2 are VLAN 200 and VLAN 100, respectively. The AP uses direct forwarding (Layer 2 forwarding mode) in cloud management mode. To ensure that wireless terminals can obtain IP addresses and access the external network, perform the following configurations:
  Configure the LAN interface of AR2 to allow packets from the corresponding VLANs to pass through.
  Configure a DHCP address pool on AR2 to assign IP addresses to wireless terminals.
  Configure SNAT for wireless terminals connected to the AP to access the external network.
AP2
SSID: iMaster_NCE_Demo
Portal authentication
SSID: Employee
802.1X authentication
T
T
Trunk interface
T
N
N
NAT interface
Site Creation
Device Onboarding
AR2 Service Configuration
AP2 Service Configuration
O&M

## Slide 26: Network Access Configuration for Wireless Users (2)
Configure LAN resources for wireless users on AR2.
AP2
SSID: iMaster_NCE_Demo
Portal authentication
Site Creation
Device Onboarding
AR2 Service Configuration
AP2 Service Configuration
O&M

## Slide 27: Network Access Configuration for Wireless Users (3)
Configure the LAN interface of AR2 to allow packets from the VLANs to which wireless users belong to pass through.
AP2
SSID: iMaster_NCE_Demo
Portal authentication
Site Creation
Device Onboarding
AR2 Service Configuration
AP2 Service Configuration
O&M

## Slide 28: Network Access Configuration for Wireless Users (4)
Add a subnet for wireless users in the ACL referenced by SNAT.
AP2
SSID: iMaster_NCE_Demo
Portal authentication
Site Creation
Device Onboarding
AR2 Service Configuration
AP2 Service Configuration
O&M

## Slide 29: Service Verification
huawei
Portal_User
dot1x
802.1x_User
Create accounts for Portal and 802.1X authentication.
1
Connect to an SSID.
2
Enter the password of the Portal authentication account huawei.
3
Authentication is successful.
1
Connect to an SSID.
2
Enter the password of the 802.1X authentication account dot1x.
3
802.1X authentication is successful.
Site Creation
Device Onboarding
AR2 Service Configuration
AP2 Service Configuration
O&M

## Slide 30: Monitoring: Site
After network services are provisioned, an administrator can monitor statistics about device online status and network resource status at the site so that maintenance personnel can obtain device data status to prevent exceptions.
Choose Monitoring > Health > Site from the main menu of iMaster NCE-Campus.
Check the cloud-managed device health, network health, and terminal packet loss rate.
Check the device deployment status based on the outdoor map.
Check the status of all devices at a site in a list.
Check the site health, device management status, alarms, and cloud-managed device health statistics.
Monitor session statistics.
Site Creation
Device Onboarding
AR2 Service Configuration
AP2 Service Configuration
O&M
Notes: Check the cloud-managed device health, network health, and terminal packet loss rate.
  Cloud-managed device health score = (1 – Number of abnormal devices/Total number of devices) x 100
  Network health score (Wi-Fi)/Radio health score = (1 – Number of abnormal radios/Total number of radios) x 100
  Network health score (WAN) = Average quality of all links at a site (SLQM: site link quality monitor) x 10

## Slide 31: Monitoring: Device
Choose Monitoring > Health > Device 360. The device monitoring page is displayed. Click a device. The device management page is displayed.
Basic device information
Interface information and data
Device location
Device login and logout logs
Detect network connectivity
Device file management
CPU usage and memory usage
Alarm information generated by the device
Site Creation
Device Onboarding
AR2 Service Configuration
AP2 Service Configuration
O&M

## Slide 32: Alarm
You can set alarm or event rules to customize alarm or event monitoring policies as required, improving troubleshooting efficiency.
Alarm severity
Alarm source
Last occurrence time
Possible cause
...
Site Creation
Device Onboarding
AR2 Service Configuration
AP2 Service Configuration
O&M

## Slide 33: Configuration Management
Choose Maintenance > Configuration Maintenance > Configuration Save. The configuration saving page is displayed. You can save the configurations of all devices in batches.
Site Creation
Device Onboarding
AR2 Service Configuration
AP2 Service Configuration
O&M

## Slide 34
（TorF）For wireless SSIDs used by guests,802.1X authentication is recommended.
  True
  False
Notes: Answer:
  B

## Slide 35
This course describes the deployment process in typical small- and medium-sized campus scenarios, including site creation, device onboarding, LAN service, wireless service, and O&M.
After learning this course and practicing in the demo environment, trainees will be able to independently deploy the small- and medium-sized campus network solution and master network O&M and management capabilities through iMaster-NCE Campus.