## Slide 1
Zhang Linrui/wx570554)
2020-11
New

## Slide 2: WLAN Planning and Design in Campus Scenarios

## Slide 3
For large-scale enterprise WLANs, WLAN planning design is one of the key factors that determine the WLAN quality. The purpose of WLAN planning and design is to reduce the probability of coverage holes and WLAN signal interference through proper network planning and ensure that the number of STAs connected to each AP is proper.
A good WLAN planning solution can meet signal coverage and capacity requirements and reduce interference, ensuring good network experience for wireless users.

## Slide 4
Upon completion of this course, you will be able to:
  Describe the WLAN planning and delivery process.
  Collect WLAN requirements and perform a site survey.
  Describe the capacity, frequency, and coverage planning, and AP model selection.
  Describe the WLAN channel planning, AP deployment design, power supply and cabling design, and AP installation mode design.
  Describe WLAN project acceptance methods.

## Slide 5
Introduction to WLAN Planning and Design
WLAN Planning and Design Details
WLAN Planning Cases

## Slide 6: Why Is WLAN Planning and Design Required?
WLAN planning and design are performed based on user requirements and actual conditions to determine the AP model, quantity, and position, laying a solid foundation for improving user experience.
If professional WLAN planning and design are not performed, problems may occur frequently after the project is delivered.
Low STA's signal strength
The AP transmit power is not considered during AP coverage distance design. As a result, signal coverage holes occur.
Slow Internet access of STAs
More concurrent users result in more fierce channel competition and higher probability of collision.
Severe co-channel interference
Co-channel interference indicates that two APs working at the same frequency interfere with each other. As a result, the WLAN quality is poor, the network speed is slow, or even the network is unavailable.
Poor experience in VIP areas
VIP areas are key areas covered by WLANs. Therefore, service and experience of VIP users must be ensured during solution design.
Notes: A WLAN uses radio signals (high-frequency electromagnetic waves) to transmit data. The strength of radio signals becomes weaker as the transmission distance increases. In addition, adjacent radio signals cause interference overlapping. All these factors reduce the signal quality or even cause network unavailability. To improve the WLAN quality and meet customers' requirements on network construction, WLAN planning and design are required. During WLAN planning and design, the AP models and quantity, installation positions and modes, and cable deployment modes need to be planned to ensure pervasive WLAN coverage, fast Internet access, and optimal network experience. If WLAN planning and design are not performed in the early stage, rework may be required after APs are installed. This is because network optimization after APs are installed may require AP reinstallation and re-cabling.

## Slide 7: WLAN Planning and Delivery Process
Requirement clarification
Site survey
Solution design
Installation
Acceptance test
Acceptance passed?
Adjustment and optimization
Solution review passed?
Solution modification
No
End
Yes
No
Yes
Collect basic project information and requirements from the customer.
Perform site survey and collect information about interference sources and obstacles for subsequent network planning and solution design.
Network planning solution design: Based on the site survey result and user requirements, determine the WLAN coverage mode (indoor coverage, outdoor coverage, or high-density coverage), and then design the network planning solution in terms of network coverage, network capacity, and AP deployment.
Install devices based on the network planning and design.
After the construction is complete, perform the acceptance test. The test includes whether the expected network coverage and service usage requirements are met. You can use the network test tool to perform the acceptance test.
1
2
3
4
5
Notes: In the solution design and acceptance test phase, some professional tools can be used:
  Huawei WLAN Planner allows you to import drawings, add obstacle information, automatically deploy APs, simulate actual space through 3D simulation, and set walking routes to simulate the coverage effect of each point on the routes. In this way, you can determine whether the wireless area meets the coverage requirements.
  The CloudCampus APP can automatically test the coverage effect of each area and whether common services can be used properly.
For details about how to use the two professional tools, see the following sections.

## Slide 8
Introduction to WLAN Planning and Design
WLAN Planning and Design Details
  Project Preparation and Planning & Design
  Project Acceptance
WLAN Planning Cases

## Slide 9: Task Summary
1. Project preparation
Requirement collection
Site survey
3. WLAN deployment design
2. WLAN planning and design
Channel design
AP deployment design
Power supply and cabling design
Capacity design
Installation design
Device selection
Signal coverage analysis

## Slide 10: Requirement Collection (1)
Requirement | Description | Network Planning Tool Support
Regulatory restrictions | Check the effective isotropic radiated power (EIRP) limit and available channels. | -
Drawing information | Ensure that complete drawings with scale information are available. Computer-aided design (CAD) drawings of customer buildings can be obtained from the customer's capital construction management office. | -
Coverage | Determine the key coverage areas (such as office areas and meeting rooms) and common coverage areas (such as stairs and bathrooms) required by the customer. | Common projects' requirements for key and common coverage areas are pre-configured, and one-click setting is supported.
Field strength | The customer may impose specific requirements for the signal field strength in a coverage area, for example, –40 dBm to –65 dBm in key areas and greater than –75 dBm in common areas. | The field strength can be manually configured according to customers' specific requirements. If not required, the pre-configured empirical data can be used.
Number of access users | Determine the total number of access STAs in a coverage area and the number of concurrent users in this area. For example, in a wireless office scenario, each user has a mobile phone and a laptop. In this case, the number of access STAs is calculated as follows: Number of access STAs = Number of access users x 2. | Empirical data has been pre-configured and can be modified.
STA type | Type and number of STAs on the live network (Common STAs include mobile phones, tablets, and laptops, and special STAs such as scanners and cash registers.) (Optional, based on the customer's technical competence) Proportion of MIMO types supported by STAs, based on which the number and models of APs can be determined | -
Bandwidth | Major service types and bandwidth requirements for each user | Empirical data has been pre-configured and can be modified.
Project Preparation
WLAN Planning and Design
WLAN Deployment Design
WLAN Planner
Notes: Effective Isotropic Radiated Power (EIRP) indicates the signal strength when an antenna transmits signals.
Drawing information: The detailed drawing of the coverage area is the basic requirement.
Coverage: Signal coverage is not provided for areas with few wireless requirements, such as bathrooms, staircases, equipment rooms, and archive rooms.
Field strength: Generally, the signal strength of indoor dual-band APs should be greater than -65 dBm, and that of outdoor dual-band APs should be greater than -70 dBm.
Number of connected STAs: Consider the number of connected STAs.
STA type: Consider wireless features of different types of STAs and the requirements for the WLAN quality.
Bandwidth: Determine the bandwidth based on service requirements of STAs connected to an AP. Generally, common Internet access and email sending and receiving require a bandwidth of 512 kbit/s, and standard definition (SD) video requires a bandwidth of 2 Mbit/s.

## Slide 11: Requirement Collection (2)
Requirement | Description | Network Planning Tool Support
Coverage mode | Indoor settled, agile distributed, or outdoor coverage | Indoor, outdoor, and agile distributed scenarios are supported.
Power distribution mode | Customer's requirements on the power supply mode, and available power supply facilities and areas | PoE power supply can be drawn.
Switch location | Location of switches connected to the WLAN | A topology with switches and cables can be drawn.
To ensure that all possible requirements are collected, prepare a requirement collection checklist, and collect and record customer requirements based on the checklist.
Project Preparation
WLAN Planning and Design
WLAN Deployment Design
WLAN Planner
Notes: Coverage mode: Analyze the coverage mode based on customer requirements.
Power distribution mode: The power supply mode of APs must be considered.
Switch location: If PoE power supply is used, the length of the network cable cannot exceed 80 m. If PoE++ is supported, the length of the network cable can reach 200 m.

## Slide 12: Site Survey (1)
During site survey, obtain information such as the STA type, floor height, building material and signal attenuation, interference sources, new obstacles, and extra-low voltage (ELV) room. Based on the collected information, you can determine the AP model, AP installation mode and positions, and power supply and cabling design.
Site Survey Item | Information (Example) | Remarks
Floor height | 3 m for a common indoor floor | It is important to obtain the floor height information of areas such as atriums, halls, and lecture halls. You can use a rangefinder to measure the height.
Building materials and signal attenuation | 240 mm thick brick wall (attenuation: 15 dB @ 2.4 GHz, 25 dB @ 5 GHz) 80 mm thick colored glass (attenuation: 8 dB @ 2.4 GHz, 10 dB @ 5 GHz) | Obtain the building materials on the site and their thicknesses to determine signal attenuation values. If possible, test the signal attenuation on the site. Otherwise, query the table of "Signal attenuation caused by common obstacles."
Interference sources | Information about Wi-Fi interference sources detected on the site | Check whether there is interference caused by, for example, mobile hotspots, Wi-Fi devices of other vendors, and non-Wi-Fi devices (such as Bluetooth devices and microwave ovens). Tools such as the CloudCampus APP can be used to record interference source information.
New obstacles | New partitions on the site | Check whether obstacles on the site are consistent with those on the drawing. If not, mark the inconsistent areas and take photos.
Site photos | Global site photos | Take as many photos as possible to record the environment and transfer survey information.
Project Preparation
WLAN Planning and Design
WLAN Deployment Design
WLAN Planner
Notes: On a WLAN, obstacles cause strong attenuation on wireless signals, which affects user experience. Therefore, during site survey, master the methods of testing the attenuation of unknown obstacles.

## Slide 13: Site Survey (2)
Site Survey Item | Information (Example) | Remarks
AP type | Common settled AP | Select indoor settled, agile distributed, outdoor, or high-density APs based on scenarios.
AP installation mode and position | Ceiling or wall mounting | Check whether APs can be mounted against the ceiling. If not, mount APs against the wall or on junction boxes.
ELV room locations | ELV room locations | On the drawing, mark the locations of ELV rooms where switches are to be deployed.
Power supply cabling | Ethernet cables to be routed | Mark PoE power supply cables to be routed on the drawing. It is recommended that the length of a PoE power cable be less than or equal to 80 m.
Implementation feasibility | AP deployment feasibility, distance to switches, distance to power supply, and cabling feasibility | Check whether there is a fire door or whether the concrete bearing wall allows for easy hole-drilling.
Outdoor site | Main buildings on the site and their heights | Observe the heights of the tall buildings, street lamps, and towers in or near the coverage area, which can be used as the main buildings of the AP site.
Outdoor propagation environment | Signal propagation environment in the coverage area | Learn about the general outline of the coverage area and check whether there are obstacles such as tall buildings and trees around the coverage area. If possible, take photos of some areas for future use or archiving.
Special requirements | Roaming packet loss rate: < 1% Latency: < 20 ms | Collect special customer requirements, such as roaming packet loss rate and latency.
Project Preparation
WLAN Planning and Design
WLAN Deployment Design
WLAN Planner

## Slide 14: Signal Coverage Design - Overview
To improve user experience, consider signal strength requirements in WLAN coverage areas during network planning.
The signal strength is determined by factors such as the AP location, AP transmit power, signal attenuation caused by obstacles, AP antenna gain, and transmission distance.
Signal strength = AP transmit power + Antenna gain – Transmission attenuation – Signal attenuation caused by obstacles
Coverage Area | Field Strength | Typical Area in Common Projects
Major coverage areas | –40 dBm to –65 dBm | Dorm room, library, classroom, hotel room, lobby, meeting room, office, and hall
Common coverage areas | > –75 dBm | Corridor, kitchen, storeroom, dressing room, etc.
Special coverage areas | Depending on the actual situation | Areas where coverage or installation is limited or not allowed, for the sake of service security or property management
Field strength requirements in common coverage areas
Project Preparation
WLAN Planning and Design
WLAN Deployment Design
WLAN Planner
Notes: An AP transmits radio signals through an antenna and generates a WLAN coverage area around the antenna. The signal strength becomes weaker as radio signals are transmitted further. Generally, the area where the signal strength around an antenna is greater than the edge field strength is called WLAN coverage area.
The received signal strength indicator (RSSI) indicates the received signal strength at a location in the coverage area of a WLAN. The RSSI is the EIRP minus the transmission attenuation and attenuation caused by obstacles.
If signal attenuation caused by obstacles is not considered, the signal transmission distance is 15 m, and the signal strength is 5 GHz, the RSSI is as follows:
  RSSI = AP transmit power (20 dBm) + Antenna gain (4 dBi) – Transmission attenuation (88.3 dB) – Signal attenuation caused by obstacles (0 dB) = –64.3 dBm

## Slide 15: Signal Coverage Design - Antenna and Antenna Gain
An antenna is a passive component and concentrates energy in a specific direction for radiation by controlling the signal transmission direction, so as to enhance signal strength in the specified direction.
The antenna gain is the ratio of the power density in a given direction to the power density of a reference antenna (using an ideal radiation source) in the same direction. It is expressed in dBd and dBi.
Based on the characteristics of the horizontal antenna radiation pattern, antennas can be classified into three types.
Directional antenna
A directional antenna radiates energy more effectively in one direction than in others on the horizontal and vertical planes.
Omnidirectional antenna
An omnidirectional antenna radiates equal energy in all directions on the horizontal plane and radiates different energy in different directions on the vertical plane.
Smart antenna
A smart antenna has multiple directional radiation patterns and one omnidirectional radiation pattern on the horizontal plane.
Project Preparation
WLAN Planning and Design
WLAN Deployment Design
WLAN Planner
Notes: The antenna gain is the ratio of the power density in a given direction to the power density of a reference antenna (using an ideal radiation source) in the same direction. It is expressed in dBd and dBi.
Omnidirectional antenna: Omnidirectional antennas provide omnidirectional coverage. Therefore, the gains of omnidirectional antennas are small and the coverage distance is short. All antennas are single-polarized antennas with one port. Therefore, two or three omnidirectional antennas are required to implement the diversity and MIMO features.
Directional antenna: With the same radio energy, a directional antenna provides a longer coverage distance than an omnidirectional antenna in a particular direction. Directional antennas are classified into single-polarized and dual-polarized antennas. To implement the polarization and MIMO features, select two single-polarized antennas or only one dual-polarized antenna.
Smart antenna: An antenna receives signals transmitted by STAs in omnidirectional mode. The smart antenna algorithm is a directional radiation mode. It determines the location of a STA based on the received signals and controls the CPU to point to the location of the STA in the direction with the maximum radiation.
Single-polarized antenna: only transmits or receives radio waves. Radio waves received or transmitted by a single-polarized antenna are either horizontally or vertically polarized. Single-polarized antennas require a large installation space and heavy maintenance workload.
Dual-polarized antenna: transmits and receives radio waves simultaneously on both the horizontal and vertical planes.

## Slide 16: Signal Coverage Design - Antenna Angle
The antenna angles include azimuth and the downtilt angles, which are formed between an antenna and the elevation plane and between an antenna and the azimuth plane.
The antenna gain is related to the antenna radiation pattern. A narrower main lobe indicates a smaller minor lobe and higher gain. However, the antenna gain is not simply a "more is better" parameter. The key is to meet signal coverage requirements. The signal coverage range of an antenna can be controlled by adjusting the antenna azimuth and downtilt angles.
Antenna downtilt θ°
Vertical lobe angle 30°
Antenna height H
Near-point distance d
Far-point distance D
Project Preparation
WLAN Planning and Design
WLAN Deployment Design
WLAN Planner
Notes: There are two antenna types by directionality: omnidirectional and directional antennas. An omnidirectional antenna receives or transmits signals in all horizontal directions. Therefore, angles of antennas usually refer to azimuth and downtilt angles of directional antennas.

## Slide 17: Signal Coverage Design - Attenuation
According to the formula for calculating the signal strength, the signal strength can be enhanced by increasing the transmit power and transmit antenna gain as well as reducing the signal attenuation caused by obstacles.
However, the transmit power and transmit antenna gain are limited based on site requirements, and cannot be increased infinitely. Therefore, their values must be changed within a proper range based on different hardware devices and the laws and regulations of a country. When deploying APs, minimize the number of obstacles to reduce the signal attenuation caused by these obstacles. The path loss directly affects the coverage range of an AP.
Distance | 1 m | 2 m | 5 m | 10 m | 20 m | 40 m | 80 m | 100 m
2.4 GHz | 46 dB | 53.5 dB | 63.5 dB | 71 dB | 78.5 dB | 86 dB | 93.6 dB | 96 dB
5 GHz | 53 dB | 62 dB | 74 dB | 83 dB | 92 dB | 101 dB | 110.1 dB | 113 dB
Obstacle | Thickness (mm) | 2.4 GHz Signal Attenuation (dB) | 5 GHz Signal Attenuation (dB)
Synthetic material | 20 | 2 | 3
Asbestos | 8 | 3 | 4
Wooden door | 40 | 3 | 4
Glass window | 50 | 4 | 7
Heavy colored glass | 80 | 8 | 10
Brick wall | 120 | 10 | 20
Thick brick wall | 240 | 15 | 25
Armored glass | 120 | 25 | 35
Concrete | 240 | 25 | 30
Metal | 80 | 30 | 35
Relationship between the signal attenuation and transmission distance
Signal attenuation caused by common obstacles
Project Preparation
WLAN Planning and Design
WLAN Deployment Design
WLAN Planner

## Slide 18: Signal Coverage Design
Preliminarily calculate the number of APs and then design multiple APs to implement network coverage. The WLAN Planner is recommended for network coverage design. Based on the requirements collection list, set the coverage area and STA capacity on the WLAN Planner. The WLAN Planner can automatically design a WLAN planning solution, simulate the signal strength in the coverage area, and output a simulation diagram.
Project Preparation
WLAN Planning and Design
WLAN Deployment Design
WLAN Planner

## Slide 19: Capacity Design - Overview
The WLAN capacity is designed based on actual service requirements. The number of APs required to meet service bandwidth requirements is estimated based on the AP performance, bandwidth requirements, number of STAs, and concurrency rate.
  Bandwidth required by a single STA: Bandwidth requirements vary depending on STA types and services to be provided by STAs. For example, the bandwidth required by a STA used for watching HD videos is higher than that required by a STA used only for browsing web pages. Therefore, plan sufficient bandwidth based on STA services and types to avoid bandwidth insufficiency or waste.
  Number of STAs: You need to specify an accurate number of STAs to be supported on the WLAN according to the WLAN planning.
  Concurrency rate: The concurrency rate refers to the ratio of STAs using the network concurrently to the total number of STAs. The average number of STAs using the network concurrently is calculated based on the concurrency rate and the number of STAs.
  Performance of a single AP: The recommended number of concurrent access STAs varies according to AP models. For details, see the following slides.
Calculation formula: Number of APs = (Number of STAs x Bandwidth required by a single STA x Concurrency rate)/Performance of a single AP
Project Preparation
WLAN Planning and Design
WLAN Deployment Design
WLAN Planner

## Slide 20: Capacity Design - Bandwidth
Calculate the capacity based on service bandwidth and concurrency in specific scenarios. If required bandwidth is not specified in a specific scenario, you can evaluate the bandwidth based on the scenario-specific bandwidth requirements.
Service Type | Single-Service Baseline Rate (kbps) |  | Proportion of Services in Different Scenarios |  |  | 
 | Excellent | Good | Meeting Room | Canteen | Multimedia Classroom | Office Area…
Web page browsing | 8000 | 4000 | 50% | 60% | 20% | …
Streaming media (1080p) | 16000 | 12000 | 10% | 10% | 50% | …
Streaming media (4K) | 50000 | 22500 | 0% | 0% | 0% | …
VoIP (voice) | 256 | 128 | 10% | 0% | 0% | …
Electronic whiteboard | 32000 | 16000 | 10% | 0% | 0% | …
Email | 32000 | 16000 | 5% | 0% | 0% | …
File transfer | 32000 | 16000 | 0% | 0% | 0% | …
Desktop sharing | 2500 | 1200 | 0% | 0% | 20% | …
Gaming | 2000 | 1000 | 0% | 0% | 0% | …
Instant messaging | 512 | 256 | 15% | 30% | 10% | …
Project Preparation
WLAN Planning and Design
WLAN Deployment Design
WLAN Planner

## Slide 21: Capacity Design - MIMO
Transmit antenna (TX antenna)
Receive antenna (RX antenna)
Single-input single-output (SISO)
There is a unique path between the TX antenna and the RX antenna, along which one signal is transmitted. Each signal is defined as one spatial stream.
TX antenna
RX antenna
Multiple-input single-output (MISO)
There are two paths between the TX antennas and RX antenna. Only one RX antenna exists, and therefore the two TX antennas can send only the same data along the two paths. The effect is similar to that of SIMO.
TX antenna
RX antenna
Single-input multiple-output (SIMO)
There are two paths between the TX antenna and RX antennas. Data is sent from the same TX antenna, and therefore only one signal is transmitted, doubling transmission reliability.
Multiple-input multiple-output (MIMO)
There are four paths between TX and RX antennas, along which two signals are transmitted at the same time, thereby doubling the transmission rate.
Unique path
Path 1
Path 2
Path 1
Path 2
TX antenna
RX antenna
Path 1
Path 2
Path 3
Path 4
Project Preparation
WLAN Planning and Design
WLAN Deployment Design
WLAN Planner
Notes: SISO
  Apparently, SISO transmission is unreliable and rate limited because there is only one path between the TX antenna and RX antenna. To address this issue, we add more antennas on the receiver (STA) so that two or more signals can be received concurrently.
SIMO
  There are multiple paths between the TX antenna and RX antennas. Data is sent from the same TX antenna, and therefore only one signal is transmitted, doubling reliability. This mode is also known as receive diversity.
MISO
  There are multiple paths between TX antennas and the RX antenna. Only one RX antenna exists, and therefore the TX antennas can send only the same data along the two paths. The effect is similar to that of SIMO. This mode is also known as transmit diversity.

## Slide 22
Notes: MIMO
  MIMO technology allows multiple antennas to send and receive spatial streams (multiple signals) simultaneously and to differentiate the signals sent to or received from different places. By leveraging technologies such as spatial reuse (SR) and space diversity (SD), MIMO improves the system capacity, coverage, and SNR without increasing the occupied bandwidth.
Relationship between spatial streams and MIMO: A MIMO system is generally written as MxN MIMO, with M and N indicating the number of transmit and receive antennas, respectively. MTNR can also be used, with T and R indicating transmission and receiving, respectively. The number of spatial streams in MIMO is generally less than or equal to the smaller number of transmit or receive antennas. If the number of receive antennas is different from that of transmit antennas, the number of spatial streams is smaller than or equal to the minimum number of receive or transmit antennas. For example, 4x4 MIMO (4T4R) allows for transmitting four or fewer spatial streams, and 3x2 MIMO (3T2R) allows for transmitting two or one spatial stream.

## Slide 23: Capacity Design - MU-MIMO
According to the user quantity, MIMO systems can be classified into the single-user MIMO (SU-MIMO) and multi-user MIMO (MU-MIMO) systems.
MU-MIMO can be used to increase the MU rate. That is, multiple parallel spatial streams occupying the same radio resources can be sent to different users. The following example uses an antenna system that consists of a base station with four transmit antennas and four users with a single receive antenna.
Transmit antenna
Receive antenna
Receive antenna
Receive antenna
Receive antenna
Traffic 1
Traffic 2
Traffic 3
Traffic 4
Project Preparation
WLAN Planning and Design
WLAN Deployment Design
WLAN Planner
Notes: The core of MU-MIMO technology is the space division multiple access (SDMA) technology. SDMA uses the same timeslot and subcarrier but different antennas to transmit data of multiple STAs. SDMA differentiates users in terms of space to accommodate more STAs and increase the capacity.
802.11ac allows a maximum of four users to communicate simultaneously, and 802.11ax increases this number to eight.

## Slide 24: Capacity Design - AP Throughput
Throughput refers to the total amount of data that an AP can transmit per unit time. Throughput is calculated using the following formula:
Throughput = User access bandwidth x Maximum number of concurrent STAs
Throughput design example
  Assume that a customer wants to use Wi-Fi 6 and requires 8 Mbps access bandwidth per user. In this case, the required throughout of a single-radio AP is 120 Mbps (8 x 15) and that of a dual-radio AP is 192 Mbps (8 x 24).
Maximum Number of Concurrent STAs with Different Bandwidths Dual Spatial Streams, 802.11ax (Wi-Fi 6) Supported |  |  | 
No. | User Access Bandwidth (Per Capita) | Maximum Number of Concurrent Users (Single Radio) | Maximum Number of Concurrent Users (Dual Radios)
1 | 2 Mbps | 42 | 72
2 | 4 Mbps | 24 | 41
3 | 6 Mbps | 18 | 29
4 | 8 Mbps | 15 | 24
5 | 16 Mbps | 9 | 14
6 | 50 Mbps | 3 | 5
Project Preparation
WLAN Planning and Design
WLAN Deployment Design
WLAN Planner
Notes: For details about the throughput in more scenarios, see the attachment.

## Slide 25: Capacity Design
As for capacity design, the WLAN Planner is also recommended.
After you set the coverage area and STA capacity (including the STA type, quantity, and service parameters) on the WLAN Planner, the WLAN Planner automatically calculates a proper network planning solution, which greatly improves the design efficiency. You can adjust the solution based on the actual network planning environment, for example, adjust the AP position.
Project Preparation
WLAN Planning and Design
WLAN Deployment Design
WLAN Planner

## Slide 26: Device Model Selection Factors
Item | Description
MIMO | The number of spatial streams ranges from 4 to 16. An AP with more spatial streams supports higher throughput and larger access capacity. Therefore, select APs with a proper number of spatial streams based on the application scenario and access density.
Antenna | Indoor scenario: Smart antennas provide the best coverage effect. Therefore, APs with smart antennas are recommended. Directional antennas are suitable for high-position installation scenarios. Omnidirectional antennas are suitable for scenarios where the coverage area is small and the deployment is not dense. Outdoor scenario: Use directional antennas for long-distance coverage and wireless backhaul, and omnidirectional antennas for short-distance coverage. (In China, if the coverage distance is greater than 80 m, use directional antennas. If the coverage distance is less than 80 m, use omnidirectional antennas. The actual coverage distance depends on the local EIRP restrictions.) Antenna angle: Select an appropriate antenna angle based on the installation height and coverage area.
Maximum transmit power (combined power) | The Wi-Fi transmit power is controlled by the country code and varies depending on the local laws and regulations. When the transmit power gets closer to the specified upper limit, the transmitted signal is stronger and the coverage distance is longer. For details, see the Channel and Power Restrictions in the product documentation.
Power supply mode | The power supply mode is related to the deployment scenario. Currently, PoE (PoE+/PoE++) power supply is used in most scenarios. You can also use a single power supply or dual power supplies for backup.
Wi-Fi standard | The Wi-Fi standard has evolved to the sixth generation, and each generation of the standard is compatible with earlier ones. The latest Wi-Fi 6 standard greatly improves the Wi-Fi speed and capacity, and achieves a four-fold increase in the throughput and capacity. Therefore, Wi-Fi 6 APs are recommended.
Others | As the Internet of Things (IoT) comes into widespread use, deploying an IoT network independently will cause repeated cabling, separate management and O&M, and high hardware and O&M investment. Therefore, it is recommended that IoT scalability be considered when you select Wi-Fi APs.
… | …
Project Preparation
WLAN Planning and Design
WLAN Deployment Design
WLAN Planner

## Slide 27: Channel Design - Overview
Multiple APs are required to provide full network coverage, which inevitably causes overlapping coverage areas between neighboring APs. To prevent coverage holes and ensure roaming experience on the Wi-Fi network, 10% to 15% overlapping buffer areas need to be reserved.
To reduce co-channel interference in overlapping areas, you need to plan radio frequency bands that do not interfere with each other for neighboring APs.
Frequency bandwidth
20 MHz
1
2.412
2
2.417
3
2.422
4
2.427
5
2.432
6
2.437
7
2.442
8
2.447
9
2.452
10
2.457
11
2.462
12
2.467
13
2.472
14
2.484
The 2.4 GHz frequency band is divided into fourteen 20 MHz channels numbered from 1 to 14, with adjacent channels overlapped.
Compared with the 2.4 GHz frequency band, the 5 GHz frequency band has more 20 MHz channels. In addition, adjacent channels do not overlap.
802.11a/n
802.11ac/ax
Project Preparation
WLAN Planning and Design
WLAN Deployment Design
WLAN Planner
Notes: 2.4 GHz frequency band: According to the channel distribution, channel combinations such as channels 1, 6, and 11 with a minimum interval of four channels can avoid co-channel interference. Similarly, a combination of channels 2, 7, and 12 or channels 3, 8, and 13 can also avoid co-channel interference. In some countries or regions, only channels 1 to 11 are allowed.
5 GHz frequency band: In some regions, radar systems work on the 5 GHz frequency band, which may interfere with radio signals of APs working on the 5 GHz frequency band. Radar signals may interfere with channels 52, 56, 60, 64, 100, 104, 108, 112, 116, 120, 124, 128, 132, 136, 140, and 144 (120, 124, and 128 are weather radar channels). In manual channel configuration mode, do not specify a radar channel for a radio during channel planning; in dynamic channel adjustment mode, the system automatically switches the channel upon detecting interference.

## Slide 28: Channel Design
2.4 GHz cellular coverage
11
1
1
11
11
1
6
Determine available channels on the 2.4 GHz band.
Avoid overlapping channels of neighboring APs.
5 GHz cellular coverage
153
157
157
153
153
157
149
All 5 GHz channels do not overlap. Therefore, you only need to ensure that neighboring APs use different 5 GHz channels.
2.4 GHz coverage (3D)
Reduce cross-floor interference.
Avoid channel conflicts.
2.4 GHz & 5 GHz cellular coverage
11&153
1&161
1&157
11&157
11&161
1&153
6&149
11
1
6
6
11
1
Floor 1
Floor 2
Project Preparation
WLAN Planning and Design
WLAN Deployment Design
WLAN Planner
Notes: Confirm with customers about available channels allowed by the local laws and regulations.
  Available channels on the 5.8 GHz band for outdoor scenarios in China: 149, 153, 157, 161, and 165
  Some channels may be reserved in different countries or regions. Therefore, you need to confirm the reserved channels before the planning.
Avoid co-channel interference.
  In the case of multiple floors, avoid overlapping with channels of APs at the same or adjacent floors. If channel overlapping cannot be avoided, reduce AP power to minimize the overlapping areas.
  For the 2.4 GHz frequency band, a combination of channels 1, 5, 9, and 13 can also be used in high-density scenarios.

## Slide 29: AP Deployment Design - Overview
APs can be deployed indoors or outdoors. The basic deployment principles are as follows:
  Indoor scenario
    When installing an AP, try to reduce the number of obstacles that signals pass through.
    Ensure that the front side of an AP faces the target coverage area.
    Place APs away from interference sources: Place APs away from interference sources such as electronic devices. Do not deploy microwave ovens, wireless cameras, wireless phones, or other electronic devices in the coverage area.
    If PoE power supply is required, you need to consider the distances between APs and the ELV room where PDs are deployed. It is recommended that the power supply distance be less than 80 m. If PoE++ power supply is used, it is recommended that the distance be less than 200 m.
  Outdoor scenario:
    The path between a site and its coverage area must be visible and cannot be blocked by obstacles.
    Avoid heavy electromagnetic interference or other signal interference near the site.
    Reliable power sources must be available for a site.
Project Preparation
WLAN Planning and Design
WLAN Deployment Design
WLAN Planner

## Slide 30: AP Deployment Design - Indoor Scenario
Common indoor scenarios, such as classrooms, conference rooms, and offices, are characterized by simple building structure and a few obstacles. In most cases, common APs with omnidirectional antennas are deployed, which is simple. Based on the area of a single room, APs can be installed in the following three scenarios:
  < 50 ㎡: Deploy one AP.
  50 ㎡–100 ㎡: Deploy two APs.
  > 100 ㎡: Calculate the number of APs based on the actual situation and deploy them in triangle mode.
Area of a single room < 50 ㎡
Area of a single room < 50 ㎡
AP spacing with a solid wall between APs: 3 m
AP spacing with a non-solid wall between APs: 6 m
Area of a single room: 50 ㎡–100 ㎡
AP spacing with a solid wall between APs: 3 m
AP spacing with a non-solid wall between APs: 6 m
Area of a single room: 100 ㎡–200 ㎡
AP spacing with a solid wall between APs: 3 m
AP spacing with a non-solid wall between APs: 6 m
Project Preparation
WLAN Planning and Design
WLAN Deployment Design
WLAN Planner
Notes: In room-intensive scenarios such as hotel rooms, dormitories, and wards, the agile distributed Wi-Fi solution is used because the room area is small and the density is high. That is, an RU is deployed in each room.

## Slide 31: AP Deployment Design - High-Density Scenario
High-density scenarios, such as stadiums, large conference rooms, and ticket halls, are densely populated in a large area. The following deployment rules are available based on the AP installation height:
  4–6 m: Use triple-radio APs with omnidirectional antennas for coverage at a spacing of 10 m to 15 m.
  6–10 m: Use small-angle APs with built-in directional antennas (for example, 30° x 30°) for coverage at a spacing of 12 m to 16 m based on the user capacity planning.
  10–25 m: Use APs with external antennas and external small-angle directional antennas (for example, 18° x 18°) for coverage at a spacing of 12 m to 16 m based on the user capacity planning.
  > 25 m: Use the AP with external antennas and external small-angle directional antennas for coverage. Calculate the proper distance between APs based on the antenna type and user capacity.
Project Preparation
WLAN Planning and Design
WLAN Deployment Design
WLAN Planner
Notes: When APs are installed at a height of 10 m to 25 m and use external antennas and external small-angle directional antennas, the minimum distance between APs can reach 6 m to 8 m if some APs work in dual-5G mode for signal coverage.

## Slide 32: AP Deployment Design - Outdoor Scenario
Outdoor scenarios usually are open and have a few obstacles, such as parks, squares, and streets. They can be classified into the following:
  In Figure 1, omnidirectional antennas are used to provide coverage for parks. It is recommended that APs be installed at a height of 4 m to 6 m and the distance between APs be 50 m to 60 m.
  In Figure 2, large-angle directional antennas are used to provide coverage for squares. APs are installed against walls of buildings. It is recommended that APs be installed at a height of 4 m to 6 m at a spacing of 30 m to 40 m.
  In Figure 3, directional antennas are used for road coverage. It is recommended that APs be installed at a height of 6 m to 8 m and the distance between APs be 120 m to 150 m.
Figure 1
Figure 3
Figure 2
Project Preparation
WLAN Planning and Design
WLAN Deployment Design
WLAN Planner
Notes: Note: The distance between APs recommended in this slide does not consider the EIRP.

## Slide 33: Power Supply Design
PoE power supply (recommended): PoE switches are used for data transmission and power supply of APs (through Ethernet cables or hybrid cables).
Local power supply: Non-PoE switches forward data packets sent from APs, and APs use independent power supplies.
PoE module for power supply: PoE injectors are used for data transmission and power supply of APs.
PoE switch
Local AC power supply
Fiber mechanical splicer
Power connector
RJ45 power connector
Data port connecting to a switch
AC power supply
PoE port connecting to an AP
Power indicator
PoE module for power supply
Hybrid cable for PoE power supply
Project Preparation
WLAN Planning and Design
WLAN Deployment Design
WLAN Planner
Notes: PoE power supply mode facilitates construction and power supply. The power supply is stable and secure.
  Hybrid cable: Currently, optical data is transmitted over the network port, and the transmission distance can reach 300 m.
    Advantage: The cost of one-time cabling is low and the service life is long. Hybrid cables apply to long-distance power supply scenarios and reduce the PoE power supply distance.
    Disadvantage: Hybrid optical-electrical switches are required, resulting in high costs. Optical modules are expensive, and one cable occupies two physical ports (one optical port and one electrical port). This means that more switches are used.
Local power supply is inconvenient. Exposed power cables affect the appearance and bring security risks.
The PoE module mode does not require power supply. However, a potential fault point is added, which is inconvenient for maintenance.

## Slide 34
Notes: Select a power supply mode based on the AP power.
  PoE power supply protocols: 802.3af, 802.3at, and 802.3bt
    PoE technology complies with IEEE 802.3af. The maximum power of a PD is 12.95 W.
    PoE+ technology complies with IEEE 802.3at. The maximum power of a PD is 25.5 W.
    PoE++ technology complies with IEEE 802.3bt. The maximum power of a PD is 81.6 W. Some Wi-Fi 6 APs require 802.3bt power supply.
  Power supply by the local power module (pay attention to the power requirements of Wi-Fi 5 and Wi-Fi 6)
  Local AC power supply

## Slide 35: Cabling Design
Cabling design rules:
  The length of Ethernet cables between a switch and APs does not exceed 80 m.
  The length of hybrid cables between a switch and APs does not exceed 300 m.
  Reserve about 5 m of an Ethernet cable or hybrid cable at the AP side for future adjustment.
  Keep cables away from strong electromagnetic sources.
  Confirm with customers in advance so that customers will not stop engineering for property and appearance considerations.
Project Preparation
WLAN Planning and Design
WLAN Deployment Design
WLAN Planner

## Slide 36: Installation Modes and Rules of Indoor Settled APs
Support mounting
Wall mounting
Ceiling mounting
The installation modes are detailed as follows:
Ceiling mounting (recommended): If the installation height is smaller than 6 m, use APs with omnidirectional antennas. If the installation height is greater than 6 m, use APs with directional antennas.
Wall mounting: If APs cannot be installed against the ceiling, the wall mounting mode is recommended.
Support mounting: This is a temporary installation mode when ceiling or wall mounting is not supported. This installation mode typically used in temporary exhibition scenarios.
In addition to ceiling-mounted and wall-mounted installation modes, an indoor AP can also be installed on a panel.
Panel mounting
Project Preparation
WLAN Planning and Design
WLAN Deployment Design
WLAN Planner

## Slide 37: Installation Modes and Rules of Outdoor APs
Wall mounting
Schematic diagram
Installation diagram
Pole mounting
Schematic diagram
Installation diagram
Project Preparation
WLAN Planning and Design
WLAN Deployment Design
WLAN Planner
Notes: Installation rules of outdoor APs:
  The azimuth and downtilt of an antenna can be flexibly adjusted based on the auxiliary mounting kits.
  An AP can be installed on a wall without adjusting the antenna angle.
  Outdoor omnidirectional antennas are installed at a height of 4 m to 6 m, and directional antennas are installed at a height of 6 m to 8 m.

## Slide 38: Introduction to the WLAN Planner
The WLAN Planner is a web-based WLAN planning tool that provides functions such as environment drawing, AP deployment, signal simulation, and report generation. The WLAN Planner helps engineers effectively support WLAN planning tasks and improve network planning efficiency.
Project Preparation
WLAN Planning and Design
WLAN Deployment Design
WLAN Planner
Notes: Website of WLAN Planner (only the Chrome browser is supported currently): https://serviceturbo-cloud.huawei.com
The WLAN Planner is carried on the ServiceTurbo Cloud platform and can be available only after login.
  Login and permission application
    Enter the URL (https://serviceturbo-cloud.huawei.com) of the ServiceTurbo Cloud platform in the address box of a browser and press Enter.
    Click Log In in the upper right corner to log in using a Huawei account or Uniportal account. If you do not have a Uniportal account, click Register to register one.
  After successful login, search for WLAN Planner in the Tool Application Market to open the tool.
    By default, Huawei, ASP, and enterprise network CSP accounts have the permission to use the WLAN Planner.
    If you do not have the permission, click the lower right corner of WLAN Planner and fill in the application information as prompted. After the application is submitted, you can choose My Workspace > My Applications > Permission Application to view the approval progress.

## Slide 39: WLAN Planner — Six-Step Network Planning
Step 1 Create a project.
Indoor or outdoor projects can be created based on drawings or AutoNavi maps.
Step 2 Automatically identify obstacles.
Obstacles can be manually drawn or automatically identified.
Step 3 Configure areas.
Coverage areas can be drawn with different field strengths and capacity requirements.
Step 4 Automatically deploy APs in one-click mode.
APs can be automatically deployed in one-click mode and channels can be automatically calculated based on the drawn area.
Step 5 Check the simulation effect.
Field strength and signal-to-noise ratio (SNR) simulation drawings can be viewed.
Step 6 Export reports.
Reports in Word format and a bill of materials (BOM) in Excel format can be exported.
Project Preparation
WLAN Planning and Design
WLAN Deployment Design
WLAN Planner

## Slide 40: Six-Step Network Planning 1: Create a Project
Enter the project name, select the region and representative office, and then select the country/region.
Note: The country/region corresponds to the country code. The available channels are restricted based on the country code and EIRP requirements.
Project Preparation
WLAN Planning and Design
WLAN Deployment Design
WLAN Planner
Notes: Create a project, enter the project name, select a country (optional, you can quickly find the target country through search), and select the environment type. Address and overview are optional. After the project is created, you are able to see it on the project management page. Click Open to open the project.

## Slide 41: Six-Step Network Planning 2.1: Create Buildings and Floors
After entering the project, create a floor based on the created building and import the drawing. The following uses an indoor scenario as an example.
Add a building, enter the name, and select the corresponding scenario.
Add a floor, select a scenario, and import the drawing (CAD is supported).
Note: You can also right-click a building name to perform related operations.
Project Preparation
WLAN Planning and Design
WLAN Deployment Design
WLAN Planner

## Slide 42: Six-Step Network Planning 2.2: Import Drawings and Draw Obstacles (1)
Draw obstacles (CAD drawing) based on the drawing and onsite environment.
Click the check box to set the obstacle type.
Click the bulb to hide or display the layer.
Select one or more target areas. If no target area is selected, the complete drawing is submitted.
You can right-click the selected area to delete it.
One-click identification of obstacles with keywords, such as walls, doors, and windows
Adjust the definition parsed from the CAD drawing. A larger value indicates a higher definition.
Note:
Obstacles must be automatically drawn on the CAD drawing page. After the drawing is submitted, the obstacles can only be manually drawn.
The tool automatically obtains the scale of the CAD drawing. The scale can be modified after the drawing is submitted.
Note: This is a very important operation prompt.
Note: You are advised to zoom in on the layer. Right-click the layer to set the obstacle.
Project Preparation
WLAN Planning and Design
WLAN Deployment Design
WLAN Planner
Notes: A CAD drawing may contain multiple floors. You can select each floor and submit the drawing. The tool automatically creates multiple floors.

## Slide 43: Six-Step Network Planning 2.2: Import Drawings and Draw Obstacles (2)
Draw obstacles (in other formats) based on the drawing and onsite environment.
Tips:
Scroll the mouse wheel to zoom in or zoom out the drawing.
Press and hold the space bar and move the mouse to move the drawing.
During obstacle drawing, hold down Shift to draw a straight line.
You can press Ctrl+Z to roll back the operation.
Set the scale.
Select the wall shape
and type.
Draw an obstacle. Click to start drawing and right-click to end drawing.
1
2
3
Project Preparation
WLAN Planning and Design
WLAN Deployment Design
WLAN Planner
Notes: Draw a linear obstacle: Click on a drawing to set the start point. Click repeatedly to set intermediate nodes. Right-click to complete drawing of a linear obstacle. Press Esc, use other tools, or right-click the mouse to exit drawing.
Interference source: If rogue APs are found during the site survey, the WLAN Planner can plan AP channels to avoid channel interferences.
Obstacles: Construction materials and structures are considered. Common obstacle types in indoor scenarios are pre-configured in the WLAN Planner. You can add obstacles such as walls, windows, and doors to a drawing to simulate signal obstruction in rooms, offices, elevators, and warehouses. You can also customize materials.
Drawing a rectangle obstacle: Press and drag the mouse, and then loosen it to draw a rectangle obstacle (Press Esc, use other tools, or right-click in the drawing to exit drawing).

## Slide 44
Notes: Note:
  If obstacles preconfigured in the WLAN Planner do not comply with environmental requirements, you can add obstacles in pre-configuration.
  Buildings, floors, obstacles, and interference sources can be copied. Right-click an obstacle or interference source to view its menu, and double-click it to display the attribute page.
  Select an obstacle, right-click it, and select Properties , or double-click the obstacle to view configured Properties . Click and drag the obstacle to change its location. Use the white point that appears after you select an obstacle to change the obstacle size.
  All NEs on the drawing can be deleted by pressing the Delete key. You can select and delete one or more devices at a time. All NE devices can be selected and dragged.

## Slide 45: Six-Step Network Planning 3: Configure Areas
Before using the WLAN Planner to automatically deploy APs, you need to set parameters for the target area. Skip this step if APs are manually deployed.
Select the area shape or type.
Design the coverage or capacity.
1
2
Configure the coverage type.
3
Project Preparation
WLAN Planning and Design
WLAN Deployment Design
WLAN Planner
Notes: Draw an area.
  Drawing a rectangle area: Press and drag the mouse, and then loosen it to draw a rectangle area. Press Esc, use other tools, or right-click the mouse to exit drawing.
  Draw a polygon area: Click on a drawing to set the start point. Click repeatedly to set intermediate nodes. Right-click to complete drawing of a polygon area. Press Esc, use other tools, or right-click the mouse to exit drawing.
You can also set obstacle reference sources on the drawing to simulate the actual environment, making the simulation more nature.
Right-click an area and choose Properties, or double-click an area to display the coverage area property dialog box. You can set the AP type.
Areas of the same type cannot be covered, but areas of different types can be covered.
The AP type in the region attributes is the type of the AP to be automatically deployed.
After selecting an area, you can drag the area or adjust the area size by using white dots.

## Slide 46
Notes: The WLAN Planner has three built-in coverage types:
  VIP coverage (≥ 60 dBm)
  Common coverage (≥ 65 dBm)
  Simple coverage (≥ 70 dBm)
You can customize the coverage type and related parameters in the preset scenario.

## Slide 47: Six-Step Network Planning 4: Automatically Deploy APs (1)
Automatically deploy APs in one-click mode.
Select the automatic deployment function and perform operations according to the automatic deployment configuration procedure.
It is strongly recommended that the automatic deployment result be reviewed and adjusted.
Project Preparation
WLAN Planning and Design
WLAN Deployment Design
WLAN Planner
Notes: The WLAN Planner supports automatic deployment, channel calculation, and manual deployment of APs. Note that automatically deployed APs will override the original APs on the drawing.
If a country is selected, you need to select the channel calculation mode. If no country is selected, only channels 1, 6, and 11 can be selected. Channel calculation can prevent AP channel conflicts.
You can drag an AP and right-click the AP to view the shortcut menu, or double-click an AP to open the attribute panel.

## Slide 48: Six-Step Network Planning 4: Automatically Deploy APs (2)
The CAD uses multi-layer drawing, and the common drawing is single-layer.
1
2
Select an AP model.
3
4
Retain default settings.
Enabling the “Follow EIRP” function is recommended.
Enable Power Tuning to optimize APs.
Automatically deploy APs in one-click mode.
Project Preparation
WLAN Planning and Design
WLAN Deployment Design
WLAN Planner

## Slide 49: Six-Step Network Planning 4: Automatically Deploy APs (3)
Manually deploy APs.
Tip: Double-click an AP icon or right-click an AP icon and choose Property from the shortcut menu to open the AP property panel where you can edit AP properties, such as the model, icon color, antenna, power, and channel.
Select the AP model to be deployed.
1
Click on the drawing to deploy the AP. Right-click to finish the deployment.
2
After APs are deployed, perform channel calculation and power calibration.
3
Project Preparation
WLAN Planning and Design
WLAN Deployment Design
WLAN Planner
Notes: Based on the actual environments and AP deployment experience, you can manually deploy APs on a drawing to meet users' network signal coverage demands.
After adjusting the location or properties of APs, obstacles, and coverage areas, you can click Channel Calculation to recalculate the AP channels. This step is optional.
Available channels in each country or region are different. Some countries or regions may reserve some channels. Confirm the local available channels before performing network planning.

## Slide 50: Six-Step Network Planning 5: Check the Simulation Effect
After the AP deployment is complete, check the simulation result.
Note: You can select one or more APs and right-click to perform partial simulation.
Check simulation data
Open/Close or refresh the simulation diagram
Drag the slider to adjust the data range to be displayed in the simulation diagram.
Project Preparation
WLAN Planning and Design
WLAN Deployment Design
WLAN Planner
Notes: Enable the simulation function to view the coverage result. You can view the RSSI simulation diagram, SINR simulation diagram, physical layer throughput simulation diagram, and application layer throughput simulation diagram of both the 2.4 G and 5 G frequency bands.
In the lower left corner, you can modify the color scheme of the simulation diagram. In the legend of the simulation diagram, you can drag the slider to adjust the data range to be displayed in the simulation diagram.
To simulate one or more APs, right-click the APs and choose Simulation from the shortcut menu.
When the simulation diagram is opened, the coverage area is transparent except the dashed border to avoid color overlapping between the simulation diagram and the area.

## Slide 51: Six-Step Network Planning 6: Export Reports
Export the network planning report, including the simulation diagram and material list.
Export the network planning report and material list in one-click mode.
Select a building or floor to be exported.
1
3
Configure report parameters, such as the language, format, and whether HD simulation images are required.
2
Project Preparation
WLAN Planning and Design
WLAN Deployment Design
WLAN Planner
Notes: You can use the WLAN Planner to export a detailed network planning report to provide guidance for implementation engineers.

## Slide 52
Introduction to WLAN Planning and Design
WLAN Planning and Design Details
  Project Preparation and Planning & Design
  Project Acceptance
WLAN Planning Cases

## Slide 53: Project Acceptance (1)
Performing dotting through the CloudCampus App for project acceptance.
Step 1: Choose Tools > WLAN Tester.
Step 2: Log in using a Huawei technical support account.
Step 3: Touch the project to be edited.
Step 4: In the Acceptance view, select a floor and touch the settings icon in the upper right corner.
Step 5: Determine test items.
Step 6: Find the position on the drawing and touch the dotting.
Notes: Project acceptance can be performed in multiple modes. This document describes only the acceptance mode using the CloudCampus APP and WLAN Planner.
The CloudCampus APP is a mobile app that integrates functions such as field strength detection and interference test. It is used for actual test acceptance after network deployment. It greatly reduces the workload of wireless O&M personnel and simplifies O&M.

## Slide 54: Project Acceptance (2)
Step 7: After the test point is complete, continue the test at the next point (the distance between test points cannot exceed 5 m). After each point is tested, the test data is uploaded to the WLAN Planner in real time.
Step 8: Touch the view icon on the right. Select RSSI to view the actual coverage effect of the heat map drawn by the WLAN Planner based on the test result.

## Slide 55: Project Acceptance (3)
Acceptance view
Select the path to be viewed. (Use the CloudCampus APP for dotting to generate one or more paths.)
Move the cursor to a point to view the uploaded RSSI information.
1
2
Verify the collected dotting data using the WLAN Planner.

## Slide 56: Project Acceptance (4)
Switch the view to view the actual coverage simulation. The following filtering conditions are supported: frequency band, channel, and SSID.
3

## Slide 57: Project Acceptance (5)
Export acceptance reports in Word format. The following information can be filtered: test area, test path, test item, frequency band, SSID, BSSID, and channel.
4

## Slide 58
Introduction to WLAN Planning and Design
WLAN Planning and Design Details
WLAN Planning Cases

## Slide 59: WLAN Coverage Project in the Office Area (1)
Office building drawing:

## Slide 60: WLAN Coverage Project in the Office Area (2)
Customer requirement collection:
Requirement | Obtained Result
Coverage | The target coverage areas are located on the third floor of an office building, with an area of 130 m x 80 m. The key coverage areas include office desks and meeting rooms, and the common coverage areas include corridors and tea rooms.
Field strength | No specific requirement Ensure that the office area can receive signals.
Number of access users | About 100 users For details about user distribution, see the drawing.
Bandwidth | At least 1 Mbps for each user
Coverage mode | Indoor settled AP
Power distribution mode | PoE power supply
Switch location | Switches are deployed in the room next to the stair in the upper right corner of the office area.
Notes: In the onsite environment, most obstacles are concrete walls, glass walls, and wooden doors, and there is no third-party or non-Wi-Fi interference source. Confirm with the customer about cabling on the ceiling.
Device model selection:
  In indoor settled Wi-Fi scenarios, AirEngine Wi-Fi 6 indoor APs can be used. Compared with the Wi-Fi 5 APs, AirEngine Wi-Fi 6 indoor APs have higher performance, support access of STAs complying with multiple protocols, and use industry-leading smart antennas. Therefore, radio signals can move with users and are more stable.
Coverage design:
  Obstacles with high signal attenuation, such as load-bearing walls, divide a large coverage area into multiple small coverage areas. In this project, eight areas are divided including the office area and conference room. A single AP can meet the requirements of each area. Therefore, a total of eight APs are required.
Deployment design:
  Each AP is deployed against the ceiling in the middle of a small coverage area. The channel of an AP is staggered with that of other APs (such as 1/149, 6/153, and 11/157).
Bandwidth design:
  There are a total of 100 employees. A maximum of 30 employees are in each small area, meeting access requirements of dual-band APs. The maximum total bandwidth in each small area is 30 Mbit/s. According to the bandwidth design principle, when 30 users are connected to an 802.11ax dual-band AP, the bandwidth is greater than 80 Mbit/s, which meets the requirements.
Power supply and cabling design:
  The distances between the PoE switch and APs are 70 m at most, which meets the requirement.

## Slide 61: WLAN Coverage Project in the Office Area (3)
The following figure shows the overall process of network planning and design using tools.
Deploy APs manually
Set environment parameters
Import drawing
Deploy APs automatically
Route cables and determine the power supply mode
Simulate signals
Create a project
Start
End
Export the network planning reports

## Slide 62
(Single-Choice) Which of the following obstacles will cause the highest attenuation of 2.4 GHz signals if they have the same thickness? ( )
  Metal
  Concrete
  Wooden door
  Tinted glass
Notes: Answer:
  A

## Slide 63
WLAN network planning and design is the basis of building high-quality WLANs.
During the WLAN planning and design, consider the actual environment factors based on the customer's requirements and WLAN knowledge, and use the corresponding auxiliary tools.

## Slide 64
WLAN tool usage guide: https://support.huawei.com/enterprise/en/doc/EDOC1100154882