## Slide 1
Lu Yueyue/WX445705
2020.12
Optimize

## Slide 2: CampusInsight Intelligent O&M

## Slide 3
In the Big Data era, traditional O&M based on specified rules cannot meet network O&M requirements, and the lack of automatic O&M becomes increasingly prominent. It is becoming an emergency to use a large amount of data generated on the network to perform intelligent O&M and improve the O&M efficiency.
Huawei iMaster NCE-CampusInsight, an intelligent network O&M platform, overrides traditional resource monitoring methods and applies AI to the O&M domain. Based on existing O&M data (such as device metrics and client logs), big data, AI algorithms, and more advanced analysis technologies, CampusInsight digitizes user experience on the network to help customers detect network access issues in a timely manner, improving user experience.
iMaster NCE-CampusInsight uses the Telemetry technology to collect metrics and logs of network devices and detects network exceptions based on real service traffic. The big data platform supports centralized data collection, storage, and analysis to process big data efficiently.
Notes: iMaster NCE-CampusInsight will be referred to as CampusInsight in the subsequent content of this course.

## Slide 4
On completion of this course, you will be able to：
  Describe the pain points and requirements of intelligent O&M of campus networks.
  Describe the logical architecture and external interfaces of CampusInsight.
  Describe the application scenarios and deployment modes of CampusInsight.
  Describe the main functions and applications of CampusInsight.
  Complete major operations on CampusInsight.

## Slide 5
CampusInsight Overview
CampusInsight Functions and Demonstration
  Telemetry
  Visibility
  Analysis
  Optimization

## Slide 6: Challenges Facing Campus Network O&M
Precise detection
Issue identification
Experience detection
During traditional O&M, network faults can be detected only after receiving clients' complaints. As a result, faults cannot be effectively and proactively identified and analyzed.
Traditional O&M is based on SNMP and data is collected in minutes. Once a fault occurs, data at the fault occurrence time cannot be obtained in real time and no convenient backtracking method is available.
During traditional O&M, only device metrics are monitored. However, user experience may be poor when the metrics are normal. Traditional O&M lacks means of correlatively analyzing the client and network.
Difficult to proactively identify problems
Difficult user experience measurement
Difficult fault locating and analysis

## Slide 7: Campus Network O&M Requirements: AI-Powered Intelligent O&M
Device-Centric Network Management
User Experience-Centric AI-Powered Intelligent O&M
Device-centric management: User experience cannot be perceived.
Passive response: Potential faults cannot be identified.
Professional engineers locate faults on site.
SNMP
Network data collection within minutes
Topology management
Performance management
Alarm management
Configuration management
Experience visibility: Telemetry-based data collection within seconds, enabling visible experience for each client, in each application, and at each moment.
Identification of potential faults and location of root causes:
  Identification of potential faults based on the dynamic baseline and big data correlation.
  KPI correlation analysis and protocol tracing, helping accurately locate root causes of faults.
Network optimization and self-healing: Continuous learning and predictive analysis through AI algorithms, implementing predictive optimization of wireless networks.
Traditional NMS
Telemetry
Network data collection within seconds
Visible experience management
Client journey tracing
Identification of potential faults
Location of root causes
Intelligent network optimization
To-BE
Notes: Customer benefits: The transformation is to improve efficiency by using algorithms. With scenario-based continuous learning and expert experience, intelligent O&M frees O&M personnel from complex alarms and noises, making O&M more automatic and intelligent.

## Slide 8: CampusInsight: Improving User and Service Experience Based on Prediction and AI
Intelligent Network Optimization
Real-time Experience Visibility
Fault Locating Within Minutes
Proactive issue identification: Proactively identify 85% of potential network issues through the AI algorithms that are continuously trained via Huawei's 200,000+ terminals.
Fault locating within minutes: Locate issues within minutes, identify the root causes of issues, and provide effective fault rectification suggestions based on the fault reasoning engine.
Intelligent fault prediction: Learn historical data through AI to dynamically generate a baseline, and compare and analyze the baseline with real-time data to predict possible faults.
Real-time simulation feedback: Evaluate channel conflicts on wireless networks in real time and provide optimization suggestions based on the neighbor relationship and radio information of devices on each floor.
Predictive optimization: Identify edge APs, predict the load trend of APs, perform predictive optimization on wireless networks, and compare the gains before and after the optimization based on historical data analysis. This practice improves the network-wide performance by 50%+ (Tolly-verified).
Each region: Intuitively display the network status and user experience on the entire network or in each region through multi-dimensional evaluation of wired and wireless network health.
Each client: Display network experience (who, when, which AP to connect, experience, and issue) of all clients in real time throughout the journey.
Each application: Perceive experience of audio and video applications in real time, demarcate faulty devices quickly and intelligently, and analyze the root cause of poor quality.

## Slide 9: CampusInsight: Logical Architecture
Campus
Insight
Campus
Service
Issue analysis
Connection analysis
Performance experience
APIs
Information Reporting
Client
Analysis: Big data platform common services
Syslog data
Performance
counter data
Spark
Druid
Kafka
HDFS
Data collection: multi-dimensional data related to client, radios, APs, and client logs.
Intelligent analysis system
Issue identification: intelligent identification of connection, air interface performance, roaming, and device issues.
Access analysis & performance experience: analysis of connection and performance experience issues.
User and network profiles: client journey retrospection and AP details analysis.
Application analysis: audio and video quality detection.
Data storage: real-time preprocessing flow, offline distributed processing flow, and data storage service.
Data analysis: mode identification, AI engine, and data aggregation and query.
Business Services: Data analysis service based on scenarios
Data Analysis: Big data platform and data analysis service
Data Collection: Second-level performance counter and log collection
Application
AI engine
Machine learning algorithm library
Machine learning framework

## Slide 10: CampusInsight: External Interfaces
The CampusInsight southbound interface implements interconnection between CampusInsight and devices, enabling CampusInsight to manage devices. CampusInsight supports the following southbound interface types: SNMP, HTTP2+ProtoBuf, Syslog.
Supports standard SNMPv2c and SNMPv3.
SNMP can be used to connect CampusInsight to network devices.
SNMP is an application-layer network management protocol based on TCP/IP. It uses UDP as the transport-layer protocol to manage network devices that support proxy processes.
SNMP
CampusInsight uses HTTP2+ProtoBuf interfaces to collect device metric packets.
The security layer of the HTTP2 protocol uses SSL and TLS to authenticate and encrypt communication channels.
ProtoBuf is a data serialization protocol developed by Google (similar to XML, JSON, and hessian). ProtoBuf can serialize data and is widely used in data storage and communication protocols.
HTTP2+ProtoBuf
The Syslog protocol is a standard for forwarding system logs on an IP network.
Industry standard protocol used to record device logs.
CampusInsight receives log data reported by devices through the Syslog protocol.
Syslog

## Slide 11: CampusInsight: Data Processing Flowchart
User log
Device/User performance counters
Data receiving
Raw data
Aggregated data
Analyzed data
Kafka
Syslog
Telemetry
Collection service
Device management
SNMP
Data distribution/buffering
Streaming
Spark
Device
Analyzer
Real-time data processing
Offline data processing
AI
algorithm
Subscription
Collection
Distribution/
Buffering
Analysis/
AI computing
Storage
After data subscription, the collection service collects data in seconds. After the data is buffered and distributed by a high-throughput distributed message system, each application service completes data analysis and computing based on AI algorithms and expert experience, and saves processed data to a fast and column-based distributed data storage system. Then pages can access the data to display related functions.
Spark
Druid/HDFS

## Slide 12: CampusInsight Deployment Scenario: Independent Deployment (Local Deployment)
AC
SW
AP
AP
Internet
Scenario Description
CampusInsight is deployed independently on the network.
Supports intelligent analysis of wireless and wired network devices in campus enterprises.
Network Description
The following networking modes are supported:
All ACs (including standalone ACs, native ACs, and ACUs) + Fit AP
All ACs (including standalone ACs, native ACs, and ACUs) + central AP + RU
Hybrid networking of switches and WLAN devices

## Slide 13: CampusInsight Deployment Scenario: CloudCampus Deployment (Local Deployment)
Scenario Description
CampusInsight is co-deployed with iMaster NCE-Campus.
An enterprise purchases the Huawei cloud management platform (iMaster NCE-Campus and CampusInsight) and deploys the platform in the enterprise data center. O&M personnel of the enterprise maintains the cloud management platform and enterprise network. The platform is used within the enterprise. The enterprise purchases related licenses from the Huawei service team.
Network Description
Management and intelligent analysis are supported for Huawei cloud switches, cloud ACs, and cloud APs. For details about supported device models, see the iMaster NCE-CampusInsight Specifications List.
An enterprise deploys CampusInsight and iMaster NCE-Campus in the enterprise data center, and manages devices through iMaster NCE-Campus. CampusInsight synchronizes device management information from iMaster NCE-Campus.
Internet
AC
SW
AP
AP

## Slide 14: CampusInsight Deployment Scenario: CloudCampus Deployment (Huawei Public Cloud Scenario)
AC
SW
AP
AP
Internet
Scenario Description
In the Huawei public cloud scenario, the cloud management platform (iMaster NCE-Campus and CampusInsight) is uniformly managed by the cloud management and operations team of Huawei and provides the SaaS service for end users.
Tenant network devices are connected to the Huawei cloud management platform through the carrier network.
Network Description
Management and intelligent analysis are supported for Huawei cloud switches, cloud ACs, and cloud APs. For details about supported device models, see the iMaster NCE-CampusInsight Specifications List (CloudCampus).
Huawei cloud management and operations team deploys CampusInsight and iMaster NCE-Campus on Huawei data public cloud, and manages devices through the iMaster NCE-Campus. CampusInsight synchronizes device management information from iMaster NCE-Campus.
AC
SW
AP
AP
Tenant 1
Tenant N
Huawei
Notes: SaaS, software as a service

## Slide 15: CampusInsight Deployment Scenario: CloudCampus Deployment (MSP Self-built Cloud Scenario)
Scenario Description
MSPs purchase the controller (iMaster NCE-Campus) and analyzer (iMaster NCE-CampusInsight) for operational purposes. Software can be deployed in their data centers or on the public cloud IaaS.
MSPs develop their tenants and provide SaaS services for tenants.
Tenant network devices connect to the MSP data center or public cloud IaaS through the carrier network.
Network Description
Management and intelligent analysis are supported for Huawei cloud switches, cloud ACs, and cloud APs. For details about supported device models, see the iMaster NCE-CampusInsight Specifications List (CloudCampus).
AC
SW
AP
AP
Internet
AC
SW
AP
AP
Tenant 1
Tenant N
MSP
Notes: IaaS, infrastructure as a service

## Slide 16
CampusInsight Overview
CampusInsight Functions and Demonstration
  Telemetry
  Visibility
  Analysis
  Optimization

## Slide 17: Meeting Real-Time Analysis Requirements Based on the Telemetry Technology
SNMP
Telemetry
SNMP
Traditional NMS
Protocol development stagnation --- SNMP is designed for limited processing capabilities.
Polling technology --- The minute-level polling cycle cannot meet the service requirements of real-time management.
Rigid data structure --- Fixed data structures are defined, and multiple data requests are required to complete each effective data collection.
Telemetry
Based on HTTP2 and ProtoBuf
Subscription-based release and on-demand use
Efficient encoding and decoding technology to obtain multiple data records at a time, implementing second-level data acquisition
The quasi-real-time data acquisition capability is the key dependency for the analyzer to mine data.

## Slide 18: Monitoring Telemetry Metrics on Wireless Networks
Measured Object | Measurement Metric | Supported Device Type | Default Collection Period
AP | CPU usage, memory usage, and number of online clients | AP | 1 minute
Radio | Number of online clients, channel utilization, noise, traffic, backpressure queue, interference rate, and power | AP | 1 minute
Client | RSSI, negotiated rate, packet loss rate, and latency | AP | 1 minute
Monitor key metrics on wireless networks based on the telemetry technology, display the wireless network quality from the AP, radio, and client dimensions, and proactively identify air interface performance issues, such as weak-signal coverage, high interference, and high channel utilization.
Real-time data display
Automatic issue identification
Display key metrics on wireless networks and single out abnormal metric status.
Automatically identify air interface performance issues based on AI algorithms, correlative analysis, and exception modes.
Telemetry metric collection on wireless networks
Automatically identify air interface performance issues based on telemetry metrics, AI algorithms, correlative analysis, and exception modes.
Display AP's key metrics on wireless networks and single out abnormal metric status.
Notes: RSSI: Received Signal Strength Indicator

## Slide 19: Monitoring Telemetry Metrics on Wired Networks
Analyze telemetry metric data of devices, interfaces, and optical links collected through Telemetry on wired networks, and proactively monitor and predict network issues
Measured Object | Measurement Metric | Supported Device Type | Default Collection Period
Device/ Card | CPU usage | Switch and AC | 1 minute
 | Memory usage | Switch and AC | 1 minute
Interface | Number of received/sent packets, number of received/sent broadcast packets, number of received/sent multicast packets, number of received/sent unicast packets, number of received/sent packets that are discarded, and number of received/sent error packets | Switch and AC | 1 minute
Display key metrics on wired networks in real time, including top N devices and historical trend.
Use AI algorithms to predict the baselines of key metrics, such as the CPU/memory usage. Identify network metric deterioration before service interruptions through comparison with dynamic baselines.
Telemetry metric collection on wired networks
Multiple metric display methods
Identify the device with abnormal metrics
Real-time display of
key metrics
Exception detection based on dynamic baselines

## Slide 20
CampusInsight Overview
CampusInsight Functions and Demonstration
  Telemetry
  Visibility
  Analysis
  Optimization

## Slide 21: Campus Health: Intuitive Insights into the Network Quality
Wireless
Continuously guides network optimization based on KQIs/KPIs
Wired
Detect and handle faults in a timely manner based on accurate issue reporting
Wired Network Health
Major Portal for Routine O&M
Centralized wired/wireless network monitoring
Intuitive, clear, and efficient display of buildings
Device capacity
Network status
Network performance
Device environment
Wireless Network Health
Access success rate, access duration
Roaming success rate, roaming duration
Signal and interference
Air interface capacity
Air interface throughput
Campus Health
Health
Quality Evaluation Reports
Radio Heat Map
Notes: Intuitive insights into campus network health based on multi-faceted wired and wireless network health monitoring, implementing intelligent, simplified campus network O&M.
Network health topology as a uniform portal for rapidly handling network and device problems in local buildings, simplifying network O&M.
Note:
  KQI: key quality indicator

## Slide 22: Building Topology: Displaying Key KPI and Network Issues Based on Buildings
Intuitive, clear problem display from the building perspective
Your network is abnormal.
Device off-boarding, intermittent port disconnection, AP off-boarding.
An Access fault occurs on your network.
Users fail to be authenticated in a batch.
Traffic congestion occurs on your network.
Port or queue congestion.
Packet error occurs on your network.
The number of error packets on a network port exceeds the threshold, or the number of error packets keeps increasing.
Health
Quality Evaluation Reports
Radio Heat Map

## Slide 23: Multi-Dimensional Network Health Evaluation Model, Comprehensively Evaluating Network Experience
Wireless network health evaluation model
Displays wireless network quality from 3 dimensions and 6 sub-categories.
Access Experience
Roaming Experience
Throughput Experience
Check whether users can access the network properly.
Check whether network experience is smooth without frame freezing when users move.
Check whether interference exists on the wireless network and whether capacity expansion is required.
Wired network health evaluation model
Device Environment
Device Capacity
Network Status
Check whether the status of physical components is abnormal.
Check whether device resources or capacities are sufficient.
Check whether the status of network ports is abnormal.
Network Performance
Data transmission is abnormal, affecting the throughput.
Analyzes 10+ types of monitored objects and 30+ indicators to intuitively display the wired network quality.
Health
Quality Evaluation Reports
Radio Heat Map
Notes: Wireless Network Health Evaluation Model:
  Access Experience
    Access success rate: Association/Authentication/DHCP success rate.
    Access duration: Association/Authentication/DHCP duration.
  Roaming Experience
    Roaming fulfillment rate: Roaming success rate/Roaming duration.
  Throughput Experience
    Signal and interference: STA signal strength and interference rate.
    Capacity fulfillment rate: Channel utilization/Number of users.
    Throughput fulfillment rate: Interference rate/Non-5G-prior access/Air interface congestion fulfillment rate.
Wired Network Health Evaluation Model:
  Device Environment: Fault of a device, board, fan, power supply, or file system
  Device Capacity: ARP/MAC/FIB entry capacity, ACL resources, storage capacity
  Network status: Intermittent port disconnection, port suspension, optical module exception
  Network performance: Port congestion, queue congestion, port error packets

## Slide 24: Case 1: Wireless Network Health
Case: Using the wireless health of CampusInsight, O&M personnel at a site find that the network quality of Shenzhen campus is much lower than that of other campuses. The access success rate, coverage, and throughput fulfillment rate of Shenzhen campus are below the industry benchmark. By drilling down data, O&M personnel successfully locate the cause and rectify the fault.
2. In fulfillment rate rankings, the fulfillment rate of Shenzhen campus is lower than that of other campuses. Click Shenzhen. The quality evaluation data of Shenzhen campus is displayed.
3. Check data of the multiple dimensions. It is found that the quality evaluation result of the coverage is Good, which is below the industry benchmark. Click the RSSI fulfillment rate metric to drill down data for analysis.
4. On the RSSI fulfillment rate analysis page, two weak-signal coverage issues are detected. Click the link in the Issue Name column to go to the issue details page and check the specific issue.
1. Choose Health > Wireless Health.
Health
Quality Evaluation Reports
Radio Heat Map

## Slide 25: Case 2: Wired Network Health
Case: The O&M personnel at a site use CampusInsight to check the wired network health and find that the network performance is abnormal. The O&M personnel view the anomaly details, find the abnormal monitoring item, go to the corresponding issue analysis page to view the root cause, and rectify the anomaly.
1. Choose Health > Wired Health.
2. If Network Performance is abnormal, click View Details.
3. View the abnormal monitoring item. Click Issues to go to the issue analysis page, view the root cause and rectification suggestions, and resolve the anomaly.
Health
Quality Evaluation Reports
Radio Heat Map

## Slide 26: Real-Time or Periodic Quality Evaluation Reports, Facilitating Optimization
Professional evaluation report services are provided. Specifically, network quality evaluation reports on the network overview, indicator details, and rectification suggestions are generated in real time or periodically. These deliver measurable network experience.
Network Overview
Get a full picture of network-wide information, including resources, users, and quality statistics.
Indicator Details
Rank sites by multiple metrics of the network health, presenting the site quality trend.
Rectification Suggestions
Identify root causes of top network problems and provide rectification suggestions for continuously improving network quality.
Health
Quality Evaluation Reports
Radio Heat Map

## Slide 27: Case 3: Quality Evaluation Reports
1. Choose Health. On the Wireless Health page that is displayed, click Report Export in the upper right corner.
2. Scheduled Sending: Set Send Time and Notify User Group for the report. The report then is sent to the specified email boxes at the specified interval.
3. Immediate Sending: Set Report Start and End Time and Receiving Mode for the report. The report then is generated immediately. (Download immediately: The report can be directly downloaded from the browser. Send by email: The report is immediately sent to the specified email boxes.)
Health
Quality Evaluation Reports
Radio Heat Map

## Slide 28: Radio Heat Map: Visualizing Network Coverage Simulation
Impact: Is there any impact on the network if an isolation wall needs to be added?
Simulate the impact on wireless coverage by adding faulty objects.
Less interference: Do device configurations need to be modified to interfere with other devices?
After device configurations such as power and channel are modified, simulate whether interference occurs between devices in real time.
Comparison with planning: Is the coverage of the deployed wireless network consistent with the planning?
Simulate the coverage based on the actual radio power and power after the network is deployed.
Simulation of signal strength, rate, and channel distribution wireless signal coverage in a floor
Reflect signal coverage and strength variation based on floors, check coverage holes, and display the network coverage status of enterprise buildings.
Set obstacles to enhance environment simulation.
Detect and rectify weak signal coverage areas in a timely manner due to obstacles.
Ability | Description
By RSSI | Wi-Fi signal strength at each location of the simulation floor
By rate | Indicates the attainable Wi-Fi access rate at each location of the simulation floor.
By Channel | Simulate the signal strength and conflict of each floor on the specified channel.
Health
Quality Evaluation Reports
Radio Heat Map
Notes: The service topology collects statistics on the status, access, congestion, and error packet issues, displays the number of clients and traffic volume based on sites, regions, buildings, and floors. This allows administrators to quickly search for and view the buildings that users pass by, helping administrators quickly identify campus network issues.
In the Service Topology of CampusInsight, you can access WLAN Topology to view the radio heat map of the network.

## Slide 29: Case 4: Radio Heat Map (1)
Case: A company has insufficient conference room resources and need to partition the office area to form some conference rooms. The construction design personnel consult the company's IT department about whether this practice affects the office Wi-Fi. The IT personnel edit the coverage obstacles such as conference room walls and glass doors based on the radio heat map, and fill coverage holes or adjust APs based on the simulation result.
2. Select Shenzhen > N10 > N10-1F from the left navigation tree.
3. Switch to editing state, right-click and select Add Obstacle.
Switch to the editing modes
1. Choose Service Topology > WLAN Topology.
Health
Quality Evaluation Reports
Radio Heat Map

## Slide 30: Case 4: Radio Heat Map (2)
Use Case Benefits
Using radio heat map, CampusInsight can simulate Wi-Fi coverage based on the radio signal transmission model upon changes of the radio environment or signal configuration. In this manner, CampusInsight can proactively identify coverage holes and areas affected by conflicts, and provide references for filling coverage holes and adjusting network configurations
4. Set Shape to PolyLine and Type to Brick wall 1 or Wooden door.
5. Draw a conference room on the topology (as shown by the quadrate in the figure), double-click the left button of the mouse to exit the obstacle drawing view, and click Save.
6. Enter the monitoring state, select By RSSI, and click Refresh to check whether there are coverage holes. Perform operations according to the simulation result.
Switch to the monitor modes
Health
Quality Evaluation Reports
Radio Heat Map

## Slide 31
CampusInsight Overview
CampusInsight Functions and Demonstration
  Telemetry
  Visibility
  Analysis
  Optimization

## Slide 32: CampusInsight: Individual and Group Issue Analysis
During campus network O&M, administrators encounter the following types of issues:
1. Individual issues: for example, access failures caused by incorrect client configurations.
2. Group issues: for example, group authentication failures caused by authentication server faults and group weak-signal coverage issues caused by insufficient AP coverage.
Solution to Individual Issues
1. Each metric: Collect data within seconds and detect issues.
2. Each client: Analyze the protocol-level access process, trace the client journey and analyze experience, and detect audio and video application quality.
Solution to Group Issues
Issue identification: Intelligently identify connection, air interface performance, roaming issues, and device issues.

## Slide 33: CampusInsight: Fault Reasoning
Rule 1
Rule 2
Rule 3
Rule 4
Fault knowledge base
Fault analysis
Accurate matching of fault scenarios
Automatic identification of root causes
Optimal rectification suggestions
120+ fault reasoning rules
Long-lasting expert-level O&M expertise of Huawei engineers
Continuous inputs from fault troubleshooting at real sites
Symptom: Client access fails at the authentication phase.
The authentication mode is 802.1x authentication.
The last packet for protocol interaction is EAP-Failure.
The packet before the EAP-Failure packet is sent from the client to the AP.
The interval between the EAP-Failure packet and the previous packet is less than 2 seconds.
Failure cause: The user name or password is incorrect or the certificate is installed incorrectly, causing the rejection by the authentication server.
Rectification suggestion: Check whether the user name and password of the client are correct and whether the certificate is installed correctly.
Fault occurring
Telemetry
Syslog
Data collection
Rule matching
Precise root cause analysis

## Slide 34: CampusInsight: Intelligently Analyze Individual Issues from Four Aspects
CampusInsight analyzes individual issues encountered during network O&M from the access network, client journey, experience, and application detection dimensions, and implements protocol process analysis, visible client journey tracing, correlative analysis of poor experience, and audio and video application quality detection, helping administrators maintain networks and ensure the experience of VIP clients.
Unable to analyze the phase where access failures occur
Unable to analyze client locations and experience
Unable to effectively detect application quality
Journey Analysis
    Protocol tracing
    (wireless + wired networks)
Experience Analysis
    Correlative analysis of poor-experience clients
    (wireless networks)
Access Analysis
    Client journey
    (wireless + wired networks)
Application Analysis
    Audio and video application quality detection
    (wireless + wired networks)
Challenges
Identify network experience issues of individual clients in E2E mode and analyze the root causes of the issues.
Requirements
Solution and Customer Benefits
Individual Issue
Group Issue

## Slide 35: Client Journey: Real-Time Experience Visibility for Each Client at Each Moment
Step1 Experience Overview
Step2 Experience Trend
Step3 Client Journey
Check APs that connect to the network at each moment, their experience, and issues that occur.
Check the overall experience metrics.
Check for experience trend changes or deterioration.
High packet loss rate, poor signal quality, and weak-signal coverage issue
Individual Issue
Journey Analysis
Application Analysis
Access Analysis
Experience Analysis

## Slide 36: Case 5: Wi-Fi User Experience Visibility (1)
Case: A VIP user reports that the Wi-Fi experience is poor. O&M personnel use the client journey function and find that the packet loss rate is high and the signal quality is poor in the cafe. In addition, the weak-signal coverage issue occurs.
1. Click Clients.
2. Enter l00419514 in the search box, and click Search.
3. Click the MAC address to go to the client journey page. (For detailed operations, see the next slide.)
Individual Issue
Journey Analysis
Application Analysis
Access Analysis
Experience Analysis
Notes: Note: The process of viewing wired user experience visibility is the same as that of viewing wireless user experience visibility.

## Slide 37: Case 5: Wi-Fi User Experience Visibility (2)
1. Check the experience overview and find that the average packet loss rate is high (15%) among Wi-Fi experience metrics.
2. Check the experience metric trend. The client experience deteriorates significantly after a period of connecting to the Wi-Fi, with poor signal quality (< -65 dBm) and a high packet loss rate (> 5%).
3. When the client accesses the AP N10-2F-3, the weak-signal coverage issue occurs. In this case, the signal quality is poor and the packet loss rate is high.
Use Case Benefits
Using client journey, CampusInsight focuses on the real Wi-Fi experience of clients and accurately traces the entire Wi-Fi access process of each client (regarded as a sensor). The traced information includes: client, time, location, connected AP, experience, and issue.
Individual Issue
Journey Analysis
Application Analysis
Access Analysis
Experience Analysis

## Slide 38: Protocol Tracing: Locating the Root Cause of Access Faults Within Minutes
3 simple steps to resolve connection issues
Interaction: Check protocol interaction
Check the association, authentication, and DHCP phases to determine the abnormal phase.
Root Cause: Check root causes
Check possible causes and rectification suggestions.
Status: Check terminal connections
Check the session access result to determine whether access issues occur.
1
2
3
Step 1 Identify the access status by session.
Step 2 Display protocol interaction details between the terminals, authentication points, and authentication server.
Step 3 Analyze the root causes of issues based on the characteristics of protocol packets.
Intuitive display of abnormal phases
Individual Issue
Journey Analysis
Application Analysis
Access Analysis
Experience Analysis

## Slide 39: Case 6: Locating Wireless Access Issues (1)
Case: Clients at a site report that the Wi-Fi cannot be connected. Using protocol tracing on CampusInsight, O&M personnel detect that the DHCP address pool is full, causing the failure to assign IP addresses to mobile phones. After the available IP address range is expanded for the DHCP address pool, the fault is rectified.
1. Click Protocol Trace.
2. Click the Switch Client icon.
3. Enter l00419514 in the search box, and click Select.
4. Related data is displayed. (For detailed operations, see the next slide.)
Individual Issue
Journey Analysis
Application Analysis
Access Analysis
Experience Analysis
Notes: Note: The procedure for locating wired access problems is the same as that for locating wireless access problems.

## Slide 40: Case 6: Locating Wireless Access Issues (2)
1. Confirm that access failures occur.
Click a session that encounters an access failure in the session list.
2. Check the client access process. It is found that the association and authentication phases are successful, but the DHCP phase is abnormal. Click DHCP to check the DHCP interaction process.
3. During the DHCP interaction, the client sends a DHCP request to the DHCP server, but the DHCP server sends back a NAK packet.
4. The most possible root cause of the fault is that the DHCP address pool does not have available IP addresses. It is recommended that the range of available IP addresses in the address pool be expanded.
Use Case Benefits
Using protocol tracing, CampusInsight can analyze the protocol interaction details in the three phases (association, authentication, and DHCP) for a client to access the wireless network in a fine-grained manner, and provide root causes and rectification suggestions. This facilitates the resolution of connection issues.
Individual Issue
Journey Analysis
Application Analysis
Access Analysis
Experience Analysis

## Slide 41: Correlation Analysis for Wi-Fi Experience Deterioration
Step2 AI Analysis
Use the correlation analysis algorithm to analyze the network metric with the highest relevance and locate the root cause.
Step1 AI Identification
Use the AI algorithm to detect outliers and identify clients with deteriorated Wi-Fi experience.
Step3 AI Closed-loop Management
Provide the most reasonable rectification suggestions based on Huawei's accumulated O&M expertise.
Individual Issue
Journey Analysis
Application Analysis
Access Analysis
Experience Analysis

## Slide 42: Audio and Video Quality Detection
Proactive detection of the audio and video quality: Through the SIP Snooping technology, the analyzer proactively senses SIP+RTP audio and video streams, detects the setup and teardown of audio and video sessions in real time, and automatically uses the eMDI technology to monitor the audio and video stream quality during the session period and identify poor-quality audio and video streams.
Analysis on the root cause for poor audio and video quality: Analyze the correlation between the MOS value and air interface metrics (signal strength, interference rate, channel utilization, negotiation rate, number of backpressure queues, etc.), wired interface metrics (packet loss rate, buffer usage, etc.), and device metrics (CPU and memory usage), identifying the root cause of poor quality.
Analysis on the root cause for unexpected session disconnections: Automatically analyze the root causes for unexpected audio and video session disconnections, including roaming exceptions, Wi-Fi disassociation, network-side metric deterioration, and signaling interaction exceptions.
Key Technology
Audio and video session statistics
Audio and video session list
Audio and video session path
Audio and video session quality analysis
Analysis on the root cause for unexpected session disconnections
Individual Issue
Journey Analysis
Application Analysis
Access Analysis
Experience Analysis
Notes: Case:
  The O&M personnel check the audio and video session list in the office area and find that the session quality is poor for a client. After checking the poor-quality session details, the O&M personnel find that a large number of packets are lost on the access switch of the client. The correlative analysis result of access switch port KPIs shows that the port is congested. After the traffic rate limit is adjusted and the port congestion issue is solved, the quality of the audio and video session becomes normal.
Constraints:
  This feature is supported only for audio and video applications that use non-encrypted SIP signaling and are carried by the RTP in the IPv4 scenario. Huawei IP phones, such as HUAWEI Video Phone 8950, can function as hard terminals.
  Switches of specific models support audio and video service analysis, while APs of specific models support only audio service analysis. For details, see HUAWEI Device Support SPEC List in the CampusInsight specification list.
  Switches of V200R013C00 or a later version and APs of V200R010C00 or a later version are supported.
  Path analysis is supported only on cloud devices.

## Slide 43: CampusInsight: Intelligent Identification of Four Types of Group Issues
In the digital era, passive O&M performed after events occur cannot ensure service experience.
More intelligent methods are required to automatically identify potential faults and accurately locate root causes to reduce the fault response time.
Scenario and Requirements
Identify potential faults: The fault response time is reduced from hours to minutes.
Roaming
    Repeated roaming
    Roaming exception
Device
    Weak-signal coverage
    High channel utilization
    High interference
    Dual band capable clients prefer 2.4 GHz
    Client capacity
    Air interface congestion
    AP offline
    Device offline
    High CPU/Memory usage
    PoE power supply failure
    Forwarding entry exceeds the threshold
    CPCAR packet loss
    Layer 2 loop
Connection
Air Interface Performance
    Association failure
    Slow association
    Authentication failure
    Authentication timeout
    Slow authentication
    DHCP connection failure
    Slow DHCP connection
    Client Gateway Unreachable
Wireless
Wired
Individual Issue
Group Issue

## Slide 44: CampusInsight: Intelligent Identification of Four Typical Issues (1)
Type | Description | Issue
Connection Issues | CampusInsight quickly identifies a variety of network access issues such as mass authentication failure and slow authentication that occur at the association, authentication, and DHCP phases. CampusInsight quickly and accurately identifies the root causes of each issue based on the fault knowledge base and provides troubleshooting suggestions accordingly. | Authentication failure (wireless + wired networks)
 |  | Authentication timeout (wireless + wired networks)
 |  | Slow authentication (wireless + wired networks)
 |  | Association failure (wireless networks)
 |  | Slow association (wireless networks)
 |  | DHCP failure (wireless + wired networks)
 |  | Slow DHCP (wireless + wired networks)
 |  | Unreachable user gateway (wireless networks)
Performance Issues | CampusInsight monitors air interface performance data in real time. On the basis of real-time performance monitoring and Huawei's expertise in WLAN field, CampusInsight intelligently identifies six classes of air interface issues that affect network access experience after users get connected to the wireless network and provides troubleshooting suggestions accordingly. | Weak-signal coverage (wireless networks)
 |  | High interference (wireless networks)
 |  | High channel utilization (wireless networks)
 |  | Air interface congestion (wireless networks)
 |  | Dual band capable client prefers 2.4G (wireless networks)
 |  | Client capacity (wireless networks)
Individual Issue
Group Issue

## Slide 45: CampusInsight: Intelligent Identification of Four Typical Issues (2)
Type | Description | Issue
Roaming Issues | CampusInsight analyzes the process when a user roams between APs to intelligently identify network access experience issues when the user moves and provides troubleshooting suggestions accordingly. | Repeated roaming (wireless networks)
 |  | Roaming exception (wireless networks)
Device Issues | Intelligently identifies device status, physical performance, and protocol performance issues and provides rectification suggestions. | AP offline (wireless networks)
 |  | Device offline (wireless + wired networks)
 |  | PoE power supply failure (wired networks)
 |  | Forwarding entry exceeds the threshold (wired networks)
 |  | High CPU usage (wireless + wired networks)
 |  | High Memory usage (wireless + wired networks)
 |  | CPCAR packet loss (wired networks)
 |  | Layer 2 loop (wired networks)
Individual Issue
Group Issue

## Slide 46: Connection Issue Analysis
Exception detection: Detection of network access exceptions.
  Normal connection failure (no fault, as shown by section A in the right figure): The wireless network access failure persists, but the failure is not caused by a network fault.
  Noise reduction for abnormal terminals (as shown by section B in the right figure): Exclude impacts of individual terminal factors. The access failure rate increases due to faulty terminals. Although the access failure rate already exceeds the threshold, but it does not indicate that a network fault occurs.
  Intelligent fault identification (as shown by section C in the right figure): Intelligently identify group issues with large impact scopes (issues with a large number of failed clients and a large failure rate).
Pattern identification: Causes may be different for issues with the same symptom. Through identifying patterns, CampusInsight can locate possible causes. In addition, CampusInsight abstracts features of clients with access failures and performs group analysis using aggregation algorithms.
Root cause analysis: Analyze possible root causes based on client online logs and provide rectification suggestions, helping O&M personnel resolve issues.
Key Technologies
Time axis
Access failure rate
Number of clients
Section C
A large number of access failures
Section B
Exclude impacts of individual terminal factors
Section A
The wireless network access failure persists
Green curve: number of users Blue curve: access failure rate Gray shadow: failure rate baseline
Fault mode
Root cause analysis and rectification suggestions
Group Issue
Connection Issues
Device Issues
Performance Issues

## Slide 47: Case 7: Connection Issue Analysis (1)
Case: At noon of a day, O&M personnel at a site received a complaint from the customer that mobile phones failed to access the network during working hours in the morning and did not recover until about 10:00. The IT personnel found that the RADIUS server had poor performance and could not process a large number of authentication requests in peak hours. As a result, the authentication failed. The fault was rectified after the legacy RADIUS server was replaced with a server with higher performance.
1. Click Issue Analysis.
2. Click the connection issue tab and click Timed Out Authentication. The page of authentication failure issues is displayed.
3. Click Statistics and view the statistical analysis chart "Number of Clients & Authentication Failure Ratio". (For the analysis details, see the next slide.)
1
Group Issue
Connection Issues
Device Issues
Performance Issues

## Slide 48: Case 7: Connection Issue Analysis (2)
3. (Following step 3 in the previous slide) Click Statistics and view the statistical chart "Number of Clients & Authentication Failure Ratio".
4. Under Original Issue List, click the issue-specific hyperlink to navigate to the issue details page.
5. View the failure event and possible cause.
Failure cause: The response from the RADIUS server times out.
Possible cause provided by the analyzer: The server is abnormal or the connection between the access controller and server is abnormal. You are advised to log in to the authentication server for further check.
2
1
3
Use Case Benefits
Due to factors such as signal coverage, obstacles in physical environments, and radio interference, user access failures persist on the wireless network. CampusInsight analyzes client access data to identify abnormal clients and eliminate invalid failure events. In addition, CampusInsight uses the machine learning algorithm to intelligently identify issues with a large number of failed clients and a large failure rate, accurately identify group connection faults on the network in a timely manner, and provide proper rectification suggestions based on expert experience.
Group Issue
Connection Issues
Device Issues
Performance Issues
Notes: The statistics of the "Number of Clients & Authentication Failure Ratio”:
  Noise reduction for abnormal terminals: The authentication failure rate increases sharply in some time periods. The analysis result shows that the abnormal terminals initiate a large number of authentication requests, and the failure rate is 100%. This issue is not caused by network faults, and noise data needs to be removed. (The client revisit shows that these clients are new employees and the terminals are not installed with Huawei Wi-Fi certificate. In this manner, frequent re-authentication causes a large number of failure events.)
  Intelligent identification of issues with a large number of failed clients and a large failure rate: When the number of wireless access users increases sharply at 8:00 a.m., the authentication failure rate reaches 70%. (The RADIUS server cannot respond to authentication requests in a timely manner due to its limited performance.) This is a typical issue with a large number of failed clients and a large failure rate, indicating that a group fault occurs.
  Connection failure but not a fault: Due to the instability of wireless client access (for example, when a client moves or passes through a coverage hole), the user authentication failure persists in each time segment, but does not affect user experience. The fault is rectified after the user automatically accesses the network again.

## Slide 49: Weak-Signal Coverage Issue Analysis
Step2 Issue Analysis
Extensive information for issue analysis
Step1 Issue Identification
Intelligent identification of weak-signal coverage issues
Intelligently identify and remotely cope with weak-signal coverage issues
Step3 Cause Locating
Troubleshooting based on suggestions
Remote clients are associated with high-power radio.
Group Issue
Connection Issues
Device Issues
Performance Issues

## Slide 50: Case 8: Weak-Signal Coverage Issue Analysis (1)
Case: On CampusInsight, O&M personnel at a site detect multiple weak-signal coverage issues. The issue details show that many remote clients are associated with this high-power radio and therefore most clients have a low RSSI. O&M personnel perform troubleshooting based on the rectification suggestions. The fault is rectified.
1. Click Issue Analysis.
2. Click the air interface issue tab and click Weak-Signal Coverage. The page of weak-signal coverage issues is displayed.
3. Click Original Issue List. In the issue list, click the first issue. The issue details page is displayed. (For detailed operations, see the next slide.)
Group Issue
Connection Issues
Device Issues
Performance Issues

## Slide 51: Case 8: Weak-Signal Coverage Issue Analysis (2)
1. The N10-2F-3 AP encounters the weak-signal coverage issue. Check the RSSI distribution of clients under the AP. It is found that the RSSI of more than 80% clients is abnormal (< –65 dBm) during the period of the issue. (According to Huawei's accumulated IT O&M expertise, user experience will be affected if the RSSI is lower than –65 dBm.)
2. Check the radio power of the AP. It is found that the 5G radio power of the AP is set to 30 during the period of the issue. (According to Huawei's accumulated IT O&M expertise, the 5G radio power is generally set to 13.) If the power is too high, remote clients will be associated with the AP, causing the weak-signal coverage issue.
3. CampusInsight provides the possible cause of the issue (high radio power of the AP) and suggestions (reducing the radio power).
Use Case Benefits
Weak-signal coverage issues easily occur on Wi-Fi networks due to improper network planning and configuration. Such issues lead to poor RSSI of clients and deteriorate Wi-Fi experience. Using weak-signal coverage issue analysis, CampusInsight can automatically identify weak-signal coverage issues, analyze data such as the RSSI and radio power, and provide possible causes and rectification suggestions.
Group Issue
Connection Issues
Device Issues
Performance Issues

## Slide 52: High Interference Issue Analysis
Step2 Correlation Analysis
Correlation analysis on metrics related to high interference issues.
Step1 Intelligent Identification
Proactively identify high interference issues on the network.
Passive O&M is changed to proactive O&M.
Step3 Fault Diagnosis
Locate the root cause and rectify the fault based on possible causes and rectification suggestions
Find the neighboring AP with the highest relevance based on the correlation algorithm.
Co-channel interference caused by the neighboring AP
Group Issue
Connection Issues
Device Issues
Performance Issues

## Slide 53: Case 9: High Interference Issue Analysis (1)
Case: On CampusInsight, O&M personnel at a site detect a co-channel interference issue caused by the neighboring AP through correlation analysis. Then they perform troubleshooting based on the rectification suggestions. The fault is rectified.
2. Click the air interface issue tab and click High Interference. The page of high interference issues is displayed.
3. Click Original Issue List. In the issue list, click the first issue. The issue details page is displayed.
(For detailed operations, see the next slide.)
1. Click Issue Analysis.
Group Issue
Connection Issues
Device Issues
Performance Issues

## Slide 54: Case 9: High Interference Issue Analysis (2)
1. The N5-2F-1 AP encounters the high interference issue. The interference rate of an AP is closely related to the channel utilization and RSSI of the neighboring AP that causes interference to the AP. CampusInsight uses the correlation analysis algorithm to automatically identify the neighboring AP (N5-2F-3) that causes interference to the AP.
2. According to the analysis of the interference rate, the neighboring AP N5-2F-3 is configured with the same channel (channel 1), causing interference to N5-2F-1.
3. CampusInsight provides the possible cause (co-channel interference by neighboring AP N5-2F-3) and suggestions (radio calibration).
Use Case Benefits
High interference issues easily occur on Wi-Fi networks. These issues affect user experience and cause problems such as long network delay and congested network access. As a result, user experience on the Wi-Fi network deteriorates. Using correlation analysis and big data analytics, CampusInsight can detect high interference issues on the network, find the most possible causes, and provide rectification suggestions.
Group Issue
Connection Issues
Device Issues
Performance Issues

## Slide 55: Layer 2 Loop Issue
To improve network reliability, redundant devices and links are usually used on an Ethernet switching network. However, due to network adjustment, configuration modification, upgrade, and cutover, data or protocol packets are often forwarded in a ring, which inevitably leads to loops.
Topology-based loop path display: Restores the loop path of a Layer 2 loop based on the switch neighbor relationship.
Key Technologies
Monitors KPIs and exception logs of all ports based on the Telemetry + Syslog mechanism, identifies Layer 2 loop ports, and quickly locates them.
Displays the list and locations of loop ports.
Works together with the controller to eradicate loops.
Group Issue
Connection Issues
Device Issues
Performance Issues

## Slide 56: Case 10: Layer 2 Loop Issue Analysis
Case: On a campus network, the traffic on a device port surged, causing the port load to increase rapidly. As a result, the services on the port were interrupted, and therefore the fault needed to be located and rectified as soon as possible.
An O&M engineer used CampusInsight to rapidly locate the fault, and found that a Layer 2 loop occurred on the port. Services were quickly restored after the port was isolated.
Issue details: Displayed the ports where the loop occurred, loop occurrence time, and issue status.
Topology restoration: Displayed information about the ports where the loop occurred, and restored the devices and ports affected by the loop based on the topology.
Impact analysis: Detected a broadcast packet surge caused by the loop, which severely affected services.
This displays existing issues. From this list, we can see that a Layer 2 loop occurred. Expand the list to view further details.
1. Choose Health > Pending Issues.
Group Issue
Connection Issues
Device Issues
Performance Issues
Notes: Use Case Benefits: The Layer 2 loop issue function of CampusInsight proactively detects Layer 2 loops on the network, restores the loop topology based on switch link information, and locates the loop location.

## Slide 57: Port Packet Error Issue
Service impact: Service packets will be directly discarded on a port with error packets, leading to slow file downloads, multicast artifacts, or voice blurring.
Issue Identification:
  Outlier detection algorithm: Compares with other ports to identify exceptions in the space dimension.
  Typical scenario: The negotiated rate supported by a terminal is different from that supported by the switch port connected to the terminal. As a result, the bit error rate of the port is significantly higher than that of other switch ports.
  Time series anomaly detection algorithm: Compares with the port itself to identify exceptions in the time dimension.
  Typical scenario: Aged physical components such as Ethernet cables and RJ45 connectors can cause the bit error rate to gradually and continuously increase over a long period of time.
Key Technologies
Outlier detection
Time series anomaly detection algorithm
Group Issue
Connection Issues
Device Issues
Performance Issues
Notes: Root cause analysis
  Check whether error packets are caused by inconsistent configurations (such as the negotiated rate) at both ends of a link.
  Guide customers to test port cables in order to figure out whether error packets are caused by cable aging or internal crosstalk.

## Slide 58: Cass 11: Port Packet Error Issue Analysis (1)
Case: Jack is an O&M engineer in a company. Just this morning he viewed the health topology for building N7 of Nanjing Area on CampusInsight and discovered that error packets were detected on the network. Jack visited his colleague Sam who accessed the network through the faulty port. According to Sam's feedback, frame freezing occurred during video playback, and this affected routine office work.
By using CampusInsight, Jack was able to rapidly locate the fault and pinpoint that continuous error packets occurred on the faulty port. This was because the Ethernet cable connected to the port aged out. The fault was rectified and services were restored after the Ethernet cable was replaced.
1. Choose Service Topology.
2. Error packets are detected on the network of building N7. Directly click the issue to bring up further details.
Group Issue
Connection Issues
Device Issues
Performance Issues

## Slide 59: Cass 11: Port Packet Error Issue Analysis (2)
Skewness analysis: According to the historical big data analysis and the skewness algorithm, the number of error packets on the faulty port is significantly greater than that on other ports. This indicates that the port is faulty.
3. Click Issue Analysis and then expand the displayed page to view details about Port error packets exceeding threshold.
Exception identification: Check the number of error packets on the port and discover that error packets on the port are persistent in each period.
Root cause analysis: Troubleshooting suggests that the virtual-cable-test command is run on the device to test the Ethernet cable. Crosstalk is discovered on the network and is rectified after the Ethernet cable is replaced.
Use Case Benefits
CampusInsight continuously monitors the number of error packets on ports, detects any substantial increase in error packets based on the dynamic baseline, and automatically generates corresponding issues. This approach accurately identifies error packet issues on the network in a timely manner, and provides expert suggestions.
Group Issue
Connection Issues
Device Issues
Performance Issues

## Slide 60: Frequent Port Up/Down Issue
Service impact: A device port frequently alternates between Up and Down states. As a result, the port is physically disconnected, interrupting services.
Issue identification: Monitor the Up and Down events of each port. If a port frequently alternates between Up and Down states in a short period of time, an exception occurs.
Root cause analysis
  Correlation analysis: Check whether the port status changes after/upon port negotiation to determine whether the port frequently alternates between Up and Down states due to inconsistent duplex modes and speeds negotiated between the local and peer ports.
  Port cable test: Guide customers to test port cables in order to figure out whether the port repeatedly negotiates with the peer port due to damaged internal wires of the cable's RJ45 connector.
Key Technologies
Time-based correlation analysis
Port cable test
Group Issue
Connection Issues
Device Issues
Performance Issues

## Slide 61: Case 12: Frequent Port Up/Down Issue (1)
Case: George is a company employee. He turned on his laptop to work and found that the laptop frequently disconnected from the network.
He contacted an O&M engineer who used CampusInsight to rapidly locate the fault, and discovered that the wired port that was connecting George to the network frequently alternated between Up and Down states. A further check indicated that the internal wires of the Ethernet cable's RJ45 connector were damaged, and this was rectified after the Ethernet cable was replaced.
1. Choose Health > Pending Issues.
2. On the Pending Issues page, the port of Edge-1 device frequently alternates between Up and Down states.
Group Issue
Connection Issues
Device Issues
Performance Issues

## Slide 62: Case 12: Frequent Port Up/Down Issue (2)
Issue analysis: According to the statistics on port Down events, the port frequently alternates between Up and Down states and this symptom persists for a long period of time.
3. Click the Port alternates between Up and Down states issue to expand the issue details.
Root cause analysis：
When the port alternates between Up and Down states, the negotiated rate of the port changes multiple times. As a result, the port repeatedly performs rate negotiation, causing intermittent disconnection.
2. Troubleshooting suggests that the virtual-cable-test command is run to check the Ethernet cable connected to the port. The command output indicates that the Ethernet cable has only 4 wires in 2 pairs. (A typical Ethernet cable has 8 wires in 4 pairs.) As a result, the port rate changes, causing intermittent disconnection. A further check indicates that the RJ45 connector of the Ethernet cable is faulty. The fault is rectified after the RJ45 connector is remade.
Test output of the faulty Ethernet cable
Group Issue
Connection Issues
Device Issues
Performance Issues
Notes: Use Case Benefits: CampusInsight continuously monitors the Down event of each port and can accurately detect any intermittent port disconnection on the network in a timely manner, providing expert suggestions.

## Slide 63
CampusInsight Overview
CampusInsight Functions and Demonstration
  Telemetry
  Visibility
  Analysis
  Optimization

## Slide 64: AI-powered Intelligent Radio Calibration Improves Network-wide Performance
Scenario 1: manual calibration
Real-time Simulation Feedback
Provide prediction and simulation tools based on real-time feedback of environment changes to drive network optimization.
Predictive Calibration
Provide the service weight balancing and optimization capability based on big data analytics and AI.
About 20% of customers choose to manually plan channels. However, they may face the following challenges:
Real-time network awareness is not supported.
The network environment is complex and interference changes rapidly.
Channels planned in manual mode are not the optimal ones.
Load balancing is not considered during load sharing calibration
Scenario 2: automatic calibration
About 80% of customers choose automatic calibration. However, they may face the following challenges:
Only the current network status can be detected.
Unable to detect historical loads and interference

## Slide 65: Scenario 1: Providing Optimal Channel Planning Suggestions Based on Neural Network Simulation Feedback (1)
An IT engineer optimizes the network in the area where a fault is reported. However, faults are reported in surrounding areas after the optimization. The optimization is performed multiple times in several days, but the optimization result is not satisfactory, and the network stability becomes worse.
Problem
Expert experience-based optimization, high professional requirements; heavy analysis workload; wireless network not planned from the entire network perspective in manual mode.
Challenge

## Slide 66: Scenario 1: Providing Optimal Channel Planning Suggestions Based on Neural Network Simulation Feedback (2)
11
11
6
6
6
6
11
11
11
6
1
1
11
6
6
11
11
6
6
11
11
6
1
1
Interference between APs caused by improper channel planning
Two APs using channel 1 are too close to each other. As a result, the two APs interfere with each other.
Technical Root Cause
Technical root cause: The impact of inter-AP interference, surrounding interference, and distance must be fully considered during AP configuration. In most cases, optimization can only ensure that the local network is at its optimal state, and comprehensive network-wide evaluation cannot be provided.
Wireless Network Simulation Feedback Solution
Expected result: network-wide optimal reasoning to properly allocate air interface resources; simulation capability (customers evaluate the simulation result based on network scores and determine whether to deliver the simulation result)
Reinforcement learning
Optimal iteration benefits
Optimized benefit forecast
Quality scoring
Neural network reasoning
Configuration recommendation by probability
AI
Real time data
Configuration and neighbor information
Signal Configuration
Channel
Output
Input

## Slide 67: Scenario 2: AI-Powered Predictive Calibration
On a wireless network, APs are busy to different extents. How to accurately predict the load trend of each AP and perform differentiated predictive calibration on the entire network?
Challenge: How to efficiently use spectrum resources based on AP load data?
Solution: Integrates multiple prediction models to accurately predict AP loads and implement differentiated radio calibration.
Load Trend
Data
Yesterday
Today
“Tomorrow”
Optimization Time
Traditional calibration: based on historical data
AI-powered predictive calibration:
based on predicted values
Differentiated radio calibration: APs with heavy loads preferentially select clean channels.
Historical data in the past 7 days
Baseline training
AI-powered intelligent algorithm
Device
Load prediction
Report data
Guide device optimization

## Slide 68: Case 13: AI-Powered Predictive Calibration (1)
Case: The wireless network office area of a company was upgraded and reconstructed. Employees were temporarily moved to building C4 for centralized office. As a result, the number of employees in building C4 increased, and the network load also increased. Employees complained that the wireless network response was getting slower. Using the intelligent radio calibration, CampusInsight automatically identified high-load areas in building C4 and accordingly adjusted APs' frequency bandwidth, thereby improving client bandwidth and network experience.
1. Choose Intelligent Radio Calibration and Big Data Calibration.
2. Enable intelligent radio calibration. You are advised to enable this function in advance to improve the data training accuracy.
Enable intelligent radio calibration
3. Click Next. On the Load Optimization page, many high-load APs are identified by 4C-3F.

## Slide 69: Case 13: AI-Powered Predictive Calibration (2)
4. On the second day after big data calibration is enabled, the bandwidth of the APs on the third floor of building C4 is increased to 252 Mbps (by 50%) and the average channel utilization is reduced to 4% (by 50%).
5. Check the calibration details. The 5 GHz frequency band of the high-load APs on the third floor of building 4C is changed from 20 MHz to 40 MHz. The Internet access experience is improved and no frame freezing occurs.
Note: If the frequency band of APs increases, the client bandwidth will also increase.
Use Case Benefits
Using intelligent radio calibration, CampusInsight continuously collects massive data of real clients, identifies high-load APs and edge APs through AI algorithms, and provides decision-making data for differentiated system optimization, enabling the network to follow clients.

## Slide 70
(Multiple-choice) Which of the following functions can CampusInsight provide?( )
  Network Health Evaluation
  Wired-user Experience Visualization
  Protocol Tracing for Locating Wireless Access Issues
  Minute-level Fault Locating
Notes: Answer: ABCD

## Slide 71
CampusInsight is a campus network analyzer launched by Huawei. It uses big data analytics technologies and machine learning algorithms to provide excellent network service assurance experience by analyzing data of each user at any time.
CampusInsight can implement real-time experience visualization, minute-level fault locating, and intelligent network optimization. This course describes the main functions and application cases of CampusInsight, including wired and wireless network health, individual and massive fault analysis, and intelligent optimization.